VIRGINIA BOARD FOR ASBESTOS, LEAD, AND HOME INSPECTORS

Title of Regulation: 18 VAC 15-20-10 et seq.  Virginia Asbestos Licensing Regulations (amending 18 VAC 15-20-10 through 18 VAC 15-20-90, 18 VAC 15-20-110, 18 VAC 15-20-150, 18 VAC 15-20-250, 18 VAC 15-20-270, 18 VAC 15-20-290, 18 VAC 15-20-330, 18 VAC 15-20-400 through 18 VAC 15-20-500, 18 VAC 15-20-520 through 18 VAC 15-20-610, and 18 VAC 15-20-700 through 18 VAC 15-20-880; adding 18 VAC 15-20-21, 18 VAC 15-20-101, 18 VAC 15-20-251, 18 VAC 15-20-271, 18 VAC 15-20-291, 18 VAC 15-20-331, 18 VAC 15-20-332, 18 VAC 15-20-361, 18 VAC 15-20-451 through 18 VAC 15-20-455, [ 18 VAC 15-20-455.1, ] 18 VAC 15-20-456 through 18 VAC 15-20-459, 18 VAC 15-20-459.1 through 18 VAC 15-20-459.15, and 18 VAC 15-20-511; repealing 18 VAC 15-20-100, 18 VAC 15-20-120 through 18 VAC 15-20-140, 18 VAC 15-20-160 through 18 VAC 15-20-240, 18 VAC 15-20-260, 18 VAC 15-20-280, 18 VAC 15-20-300 through 18 VAC 15-20-320, 18 VAC 15-20-340 through 18 VAC 15-20-360, 18 VAC 15-20-370 through 18 VAC 15-20-390, 18 VAC 15-20-510, 18 VAC 15-20-620 through 18 VAC 15-20-690, and 18 VAC 15-20-890 through 18 VAC 15-20-960).

Statutory Authority: § 54.1-501 of the Code of Virginia.

Effective Date: January 2, 2002.

Summary:

The amendments revise definitions; delete the roofing, flooring and siding provisions (abolished by House Bill 951, effective July 1, 1996); clarify fees for initial approval of accredited asbestos training programs; and create a biennial renewal requirement and fee for accredited asbestos training programs. Project monitors who also hold a valid supervisor or project designer license may renew their project monitor license by completing the supervisor or project designer refresher training. Language has been added to make clear that a refresher training certificate may be used only once to renew a license. The entry standards for inspectors, management planners and project designers have been changed to allow applicants to present evidence of minimal competence. Project monitors will be required on projects involving more than 260 linear feet or 160 square feet of asbestos-containing materials. An additional option to qualify for an asbestos and analytical laboratory license has been added and performance standards for laboratory operation have been added.

In addition, the regulation has been revised to enhance clarity, delete a proposed change in the expiration date for individual licenses, and add a new section (18 VAC 15-20-455.1) to clarify which asbestos abatement projects require a project monitor.

Summary of Public Comment and Agency's Response:  A summary of comments made by the public and the agency's response may be obtained from the promulgating agency or viewed at the office of the Registrar of Regulations.

Agency Contact:  Tabatha Williams, Department of Professional and Occupational Regulation, 3600 West Broad Street, Richmond, VA 23230, telephone (804) 367-2648.

18 VAC 15-20-10. Scope.

The purpose of this section is to identify those in the asbestos industry individuals and firms who need a specific Virginia asbestos license to be licensed. The following lists the types of asbestos license and those required to be licensed.

Asbestos Contractors Contractor's License: Required for companies firms that contract with another person, for compensation, to carry out an asbestos abatement project that exceeds 10 linear or 10 square feet.

Asbestos RFS Contractors License: Required for companies that contract with another person, for compensation, to remove nonfriable asbestos-containing roofing, flooring, or siding. This material must remain nonfriable during the entire removal process. Employees of RFS contractors are not required to be licensed, however, they must have RFS training specific to the type of nonfriable asbestos-containing material they remove (roofing, flooring, or siding).

Asbestos Worker Worker's License: Required for those individuals who remove or otherwise engage in an asbestos project.*

Asbestos Supervisor Supervisor's License: Required for those individuals who supervise an asbestos abatement project. The Commonwealth of Virginia National Emission Standards for Hazardous Air Pollutants (NESHAP) Program recognizes the "competent person" as an individual licensed under this classification.*

Asbestos Building Inspector Inspector's License: Required for those individuals who inspect buildings to identify, classify, record, sample, test and prioritize by exposure potential asbestos-containing material.*

RFS Inspector License: Required for those who identify the presence of asbestos-containing roofing, flooring or siding material through sampling and interpretation of testing reports prepared by a licensed asbestos analytical laboratory.

Asbestos Management Planners Planner's License: Required for those individuals who prepare or update an asbestos management plan.*

Asbestos Project Monitors Monitor's License: Required for those individuals who act as a project monitor on asbestos abatement sites. Project monitors who analyze Phase Contrast Microscopy (PCM) asbestos air samples on an asbestos abatement project must shall be employed by a firm that holds a valid Virginia Asbestos Analytical Laboratory license, and shall have National Institute of Occupational Safety and Health (NIOSH) 582 training, or equivalent [ , as approved by the American Industrial Hygiene Association (AIHA) ].

Asbestos Analytical Laboratory License: Required for laboratories who that analyze air or bulk samples for the presence of asbestos by Polarized Light Microscopy (PLM), PCM, or Transmission Electron Microscopy (TEM).

Asbestos Project Designers Designer's License: Required for those individuals who prepare or update an asbestos abatement project design, specifications for asbestos abatement projects, and addenda to the specifications.*

Accredited Asbestos Training Program: Required for those who offer asbestos training programs to individuals seeking licensure as an asbestos worker, supervisor, inspector, management planner, project monitor or project designer.

* Employees who conduct asbestos response actions, inspections, prepare management plans or project designs for their employer, on property owned or leased by the employer, are exempt from Virginia asbestos licensure,; however, they are required to meet all [ OSHA and ] EPA training requirements.

PART II.
DEFINITIONS AND GENERAL.

18 VAC 15-20-20. Definitions.

The following words and terms, when used in this chapter, shall have the following meanings, unless the context clearly indicates otherwise:

"AAR" means Asbestos Analyst Registry.

"AAT" means Asbestos Analyst Testing.

"Accredited asbestos training program" means a training program that has been approved by the board to provide training for individuals to engage in asbestos abatement, conduct asbestos inspections, prepare management plans, prepare project designs or act as a project monitor.

"Accredited asbestos training provider" means a firm or individual who has been approved by the board to offer an accredited asbestos training program.

"ACM" means asbestos-containing material.

"AHERA" means Asbestos Hazard Emergency Response Act. 40 CFR Part 763, Subpart E.

"AIHA" means American Industrial Hygiene Association.

"Approval letter" means a written notice confirming the firm or individual applicant’s licensure or accreditation by the board.

"Asbestos" means any material containing more than 1.0% asbestos by area as determined by microscopy.* the asbestiform varieties of actinolite, amosite, anthophyllite, chrysotile, crocidolite, and tremolite.

"Asbestos Analytical Laboratory License" means an authorization issued by the department board to perform phase contrast, polarized light, or transmission electron microscopy on material known or suspected to contain asbestos.*

"Asbestos contractor" means any person who has met the board’s requirements and has been issued an asbestos contractor’s license by the board to enter into contracts to perform asbestos projects.

"Asbestos Contractor's License" means an authorization issued by the department board permitting a person to enter into contracts to perform an asbestos abatement project.*

"Asbestos-containing material" or "ACM" means any material or product which contains more than 1.0% asbestos by area as determined by microscopy or such percentage as established by EPA final rule.

"Asbestos inspector" means any person who performs an on-site investigation to identify, classify, record, sample, test and prioritize by exposure potential asbestos-containing materials inspection as defined in this chapter.

"Asbestos Inspector's License" means an authorization issued by the department board permitting a person to perform on-site investigations to identify, classify, record, sample, test and prioritize by exposure potential asbestos-containing materials.*

"Asbestos Management Plan" means a program designed to control or abate any potential risk to human health from asbestos.*

"Asbestos management planner" means any person preparing or updating a management plan.

"Asbestos Management Planner's License" means an authorization issued by the department board permitting a person to develop or alter prepare or update an asbestos management plan.*

"Asbestos project" or "asbestos abatement project" means an activity involving job set-up for containment, removal, encapsulation, enclosure, encasement, renovation, repair, construction or alteration of asbestos-containing materials. An asbestos project or asbestos abatement project shall not include nonfriable asbestos-containing roofing, flooring and siding material which when installed, encapsulated or removed does not become friable.*

"Asbestos project design" means any descriptive form written as instructions or drafted as a plan describing the construction of an asbestos abatement area or site, response action or work practices to be utilized on the asbestos abatement project.

"Asbestos project designer" means any person providing an asbestos project design or specifications for an asbestos abatement project.

"Asbestos Project Designer's License" means an authorization issued by the department board permitting a person to design an asbestos abatement project.*

"Asbestos project monitor" means any person hired by a building owner, lessee or his agent to monitor, inspect, provide visual clearance or clearance monitoring of an asbestos abatement project.

"Asbestos Project Monitor Monitor's License" means an authorization issued by the department board permitting a person to monitor an asbestos project, subject to department board regulations.*

"Asbestos supervisor" means any person so designated by an asbestos contractor who provides on-site supervision and direction to the workers engaged in asbestos projects.*

"Asbestos Supervisor's License" means an authorization issued by the department board permitting an individual to supervise and work on an asbestos project.

"Asbestos worker" means any person who engages in an asbestos abatement activity project.

"Asbestos Worker's License" means an authorization issued by the department board permitting an individual to work on an asbestos project.*

"ASHARA" means Asbestos School Hazard Abatement Reauthorization Act, 40 CFR Part 763, Subpart E.

"Board" means the Virginia Asbestos Licensing Board for Asbestos [ and , ] Lead [ , and Home Inspectors ].

"Department" means the Department of Professional and Occupational Regulation.*

"Demolition" means the wrecking or taking out of any load-supporting structural member of a structure or solid barrier which is known to contain or be enclosing an asbestos-containing material.

"Director" means the Director of the Department of Professional and Occupational Regulation.*

"Direct supervision" means a licensed or accredited inspector, management planner, project monitor or project designer, who undertakes to supervise the activities of an unlicensed inspector, management planner, project monitor or project designer, shall be physically present on the premises at all times while any unlicensed inspector, management planner, project monitor or project designer under his supervision is engaged in the activities of an inspector, management planner, project monitor or project designer.

"Employee" means all persons in the service of another under any contract of hire, express or implied, oral or written.

"Encapsulation" means the treatment of asbestos-containing material (ACM) with a material that surrounds or embeds asbestos fibers in an adhesive matrix to prevent the release of fibers, as the encapsulant creates a membrane over the surface (bridging encapsulant) or penetrates the material and binds its components together (penetrating encapsulant).

"Encasement" means any process by which an asbestos-containing material (ACM) is sprayed with an insulating sealer which is then mechanically fastened to the asbestos covered substrate. The insulating sealer is then covered with a sealer to give structural strength and durability.

"Enclosure" means the construction or installation over or around the asbestos-containing material (ACM) of any leak tight solid or flexible coverings, which will not deteriorate or decompose for an extended period of time, so as to conceal the ACM, contain ACM fibers, and render the ACM inaccessible.

"Environmental remediation activity" means any activity planned or carried out for the purpose of reducing or eliminating any environmental hazard, including activities necessary to train individuals in the proper or lawful conduct of such activities, which are regulated by federal or state law or regulation.

"EPA" means United States Environmental Protection Agency.

"Financial interest" means financial benefit accruing to an officer or an employee individual or to a member of his immediate family. Such interest shall exist by reason of (i) ownership in a business if the ownership exceeds 3.0% of the total equity of the business; (ii) annual gross income that exceeds, or may be reasonably anticipated to exceed, $1,000 from ownership in real or personal property or a business,; (iii) salary, other compensation, fringe benefits, or benefits from the use of property, or any combination of it, paid or provided by a business that exceeds or may be reasonably expected to exceed $1,000 annually,; (iv) ownership of real or personal property if the interest exceeds $1,000 in value and excluding ownership in business, income, salary, other compensation, fringe benefits or benefits from the use of property.

"Friable" means that the material when dry, may be crumbled, pulverized or reduced to powder by hand pressure and includes previously nonfriable material after such previously nonfriable material becomes damaged to the extent that when dry it may be crumbled, pulverized, or reduced to powder by hand pressure.*

"Full approval" means approval given to a training provider for a course that has met the requirements of this chapter.

"Guest instructor" means an instructor who is invited to instruct a specific topic or topics in an accredited asbestos training program and whose instruction is limited to two hours per day.

"Hands-on experience" means the physical participation of students in an asbestos training class program. The physical participation includes mock sampling and inspection techniques, report preparation, writing project specifications, glovebag demonstrations and containment construction.

"Immediate family" means (i) a spouse, (ii) a sibling or step sibling, (iii) a parent or step parent, (iv) children or step children, and or (v) any other person residing in the same household as the officer or employee individual.

"Inspection" means an activity undertaken to determine the presence or location, or to access the condition of, friable or nonfriable asbestos-containing material (ACM) or suspected ACM, whether by visual or physical examination, or by collecting samples of such material. This term includes reinspections of friable and nonfriable known or assumed ACM that has been previously identified. The term does not include the following:

1. Periodic surveillance of the type described in 40 CFR 763.92(b) solely for the purpose of recording or reporting a change in the condition of known or assumed ACM;

2. Inspections performed by employees or agents of federal, state, or local [ government governments ] solely for the purpose of determining compliance with applicable statutes or regulations; or

3. Visual inspections solely for the purpose of determining completion of response actions.

"Instructor" means a person who instructs one or more accredited asbestos training programs, to include the principal instructor, but excluding guest instructors.

"Local education agency" or "LEA" shall have the meaning provided in the USEPA AHERA regulations set forth in 40 CFR 763.*

"NIOSH" means National Institute of Occupational Safety and Health.

"NIST" means National Institute of Standards and Technology.

"NVLAP" means National Voluntary Laboratory Accreditation Program.

"Occupied" means any area of any building designed or intended for human habitation occupancy for any purpose.

"Officer" means any person appointed, elected or hired by any company, whether or not he receives compensation or any other emolument of office.

"OSHA" means the U.S. Department of Labor Occupational Safety and Health Administration.

[ "OSHA Class III Work" means repair and maintenance operations where asbestos-containing material (ACM), including thermal system insulation and surfacing material, is likely to be disturbed. ]

"PAT" means Proficiency Analytical Testing.

"Person" means a corporation, partnership, sole proprietorship, firm, enterprise, franchise, association or any other individual or entity.*

"Preliminary review" means a review conducted by the board department following the submission of training materials to ascertain if the proposed [ asbestos ] training course program meets the standards established by this chapter.

"Primary Principal instructor" means an instructor whose main responsibility is to instruct courses accredited asbestos training programs, supervise other instructors and manage the overall [ asbestos ] training [ course program ] curriculum.*

"PCM" means phase contrast microscopy.

"PLM" means polarized light microscopy.

"RFS Contractor's License" means an authorization issued by the department permitting a person to enter into contracts to install, remove or encapsulate nonfriable asbestos-containing roofing, flooring and siding materials.

"RFS inspector" means any person performing on-site investigations to identify, classify, record or sample suspect asbestos-containing roofing, flooring or siding materials.

"RFS Inspector's License" an authorization issued by the department authorizing a person to identify the presence of asbestos-containing roofing, flooring or siding material through sampling and interpretation of testing reports prepared by a licensed asbestos analytical laboratory.*

"Removal" means the physical removal of asbestos-containing material (ACM) and disposal of it in accordance with all applicable regulations.

"Renovation" means altering in any way, one or more facility components.

"Repair" means returning damaged asbestos-containing material (ACM) to an undamaged condition or to an intact state so as to prevent fiber release.

"Residential buildings" means site-built homes, modular homes, condominium units, mobile homes, manufactured housing, and duplexes, or other multi-unit dwellings consisting of four units or less which fewer that are currently in use or intended for use only for residential purposes.

"Response action" means any method, including removal, encapsulation, enclosure or, encasement, or operation and maintenance, that remediates an protects human health and the environment from friable asbestos-containing material.

"Site" means an area established by the employer or contractor to demarcate areas where the airborne concentration of asbestos exceeds or can reasonably be expected to exceed the permissible exposure limit. The area may take the form of a temporary enclosure as defined by 29 CFR 1926.58(e)(6) or be demarcated in any manner which restricts employees from entering the area.

[ "Small-scale, short-duration" (SSSD) means activities involving the removal of three linear or three square feet or less of friable asbestos-containing material (ACM) if required in the performance of another maintenance activity, replacement of asbestos-containing gaskets, installation, repair or other maintenance work through or proximate to ACM. ]

"Structure" means any building or load supporting framework whether fixed or portable utilized for occupancy, storage, or conveyance of public utilities or industrial materials.

"Substantial change" means a change in overall course curriculum [ asbestos ] training program, materials, [ primary principal ] instructors, [ training managers, ] directors, ownership, facilities, equipment, examinations, and certificates of completion. The addition of updated regulations, exam questions or news articles shall not be considered a substantial change.

"TEM" means transmission electron microscopy.

[ "Training manager" means the individual responsible for administering a training program and monitoring the performance of the instructors. ]

"USEPA" means United States Environmental Protection Agency.

"Visual inspection" means a process of looking for conditions, which if not corrected during the asbestos abatement project, will lead to residual asbestos-containing dust or debris. Visual inspection includes examination of an asbestos abatement project area prior to clearance air monitoring for evidence that the project has been successfully completed as indicated by the absence of residue, dust and debris.

* Cited from § 54.1-500 of the Code of Virginia

18 VAC 15-20-21. [ No change from proposed. ]

PART III.
GENERAL ENTRY AND RENEWAL REQUIREMENTS.

18 VAC 15-20-30. License application.

A. Individual and business applicants are responsible for obtaining a current application. All requests for applications should be directed to: Application for asbestos licensure shall be made on forms provided by the department.

Assistant Director

Virginia Board for Asbestos and Lead

Virginia Department of Professional and Occupational Regulation

3600 West Broad Street

Richmond, Virginia 23230

B. Each individual applicant shall be at least 18 years of age.

B. Individuals C. Each individual applying for initial licensure as a supervisor, inspector, management planner, project designer or project monitor shall provide proof evidence of successful completion of an EPA/AHERA or board-approved initial [ accredited ] asbestos training course program and all subsequent EPA/AHERA or board-approved [ accredited asbestos ] refresher [ courses training programs ], relevant to the applicants applicant's discipline. If, at any time, there has been a lapse of AHERA accreditation of more than 24 months, the applicant must show successful completion within the past 12 months of an EPA/AHERA or board approved initial asbestos training course, relevant to the applicants discipline. [ The date of training completion shall be no later than 12 months before the date the department receives the application. The training certificate must indicate that the training was taken within 12 months preceding the date the department receives the application. ]

D. Each individual applying for initial licensure as a worker shall provide proof of successful completion of (i) an EPA/AHERA or board-approved initial  [ accredited ] asbestos worker training program and all subsequent EPA/AHERA or board-approved [ accredited ] asbestos worker refresher training [ program programs ] or (ii) [ proof of successful completion of ] an EPA/AHERA or board-approved initial [ accredited ] supervisor [ course asbestos training program ] and all subsequent EPA/AHERA or board-approved [ accredited asbestos ] supervisor refresher training [ program programs ]. [ The date of training completion shall be no later than 12 months before the date the department receives the application. The training certificate must indicate that the training was taken within 12 months preceding the date the department receives the application. ]

E. Each applicant for licensure as an asbestos contractor shall submit a completed asbestos [ contractors contractor ] application to the department.

F. Each applicant for licensure as an asbestos analytical laboratory shall submit a completed asbestos analytical laboratory application and all documents required by this chapter to the department.

G. Each applicant for approval as an accredited asbestos training program shall submit to the board a completed accredited asbestos training program application and all documents required by this chapter.

C. H. Each application for a license shall be signed by the applicant and shall include a certification, by the applicant, that [ within three years prior to the application date, ] the applicant's license or other authorization to perform asbestos related work has not been suspended or revoked by any jurisdiction and that no enforcement action by any jurisdiction is pending against the applicant.

D. I. In the event disciplinary actions have been taken against the applicant, in any jurisdiction, the applicant shall submit the following information, as the board may deny an applicant's request for a license based on prior disciplinary actions which indicate that the asbestos related work may not be performed in a manner that would protect the public health, safety and welfare:

1. A complete list of all prior disciplinary actions, including any sanctions imposed on the applicant by any jurisdiction or any state or federal court.

2. A description of any asbestos abatement or inspection activities, or both, conducted by the applicant that were terminated prior to completion, including the circumstances of the termination.

3. A copy of all reports compiled by the enforcement agency or a copy of a final report.

E. All applications J. Each application shall be completed according to the instructions provided by the department with the application. Incomplete applications will be returned to the applicant; fees received will shall not be refunded.

Applicants who submit checks which are dishonored by the institution on which they are drawn shall pay a $25 service fee in addition to the application fee required by this chapter.

18 VAC 15-20-40. Experience and [ Educational Education ] Verification Form (Form A) Forms.

Each application for inspector, management planner, project monitor and project designer shall include an Experience and Education Verification Form (Form A) completed by the applicant and signed by a supervisor verifying the job description of the applicant during the term of employment. The form A shall contain the name and address of the employer, a complete and concise job description, a job title, the dates of employment or dates of work performed and the signature, typewritten or printed name, address and phone number of the supervisor verifying the experience. In lieu of a verifying signature for experience, an applicant who is self employed may submit a copy of three completed inspections, management plans, project designs or project monitor reports, whichever is applicable. [ A letter from a supervisor verifying the experience may be submitted in lieu of the Experience Verification Form. ] If verification of a degree is required, the [ Degree Education ] Verification Form must shall be sent directly from the school to the department. An incomplete Form A will be returned to the applicant with an explanation for the return, and will constitute an incomplete application for licensure. Form A may be resubmitted following completion by the applicant [ A letter from a supervisor verifying the experience may be submitted in lieu of the Experience Verification Form. ]

18 VAC 15-20-50. Fees.

A. The fee for an initial application for or a renewal of an asbestos worker, supervisor, inspector, RFS inspector, management planner, project designer, or project monitor license shall be $25.

B. The renewal fee for [ individual licenses an asbestos worker, supervisor, inspector, management planner, project designer, or project monitor license ] not renewed within 30 days after the noted its expiration date shall be $50.

C. The fee for an initial application for or a renewal of an asbestos analytical laboratory license shall be $40.

D. The renewal fee for asbestos analytical laboratory licenses not renewed within 30 days after the noted its expiration date shall be $65.

E. The fee for an initial application for or a renewal of an asbestos Contractor License and RFS Asbestos Contractor contractor's license shall be $40.

F. The renewal fee for asbestos contractor licenses or RFS Contractors Licenses not renewed within 30 days after the noted its expiration date shall be $65.

G. The fee for an initial application for approval of an accredited asbestos training program shall be $400 per day of training.

H. The renewal fee for an accredited asbestos training program shall be $50 [ per training provider ].

I. The renewal fee for accredited asbestos training programs not renewed within 30 days after its expiration date shall be $75 [ per training provider ].

G. J. A license not renewed within six months after the expiration date printed on the license shall not be renewed and the licensee person shall apply for a new license.

K. All checks or money orders shall be made payable to the Treasurer of Virginia.

H. Applicants [ L. Persons who submit a dishonored check will be charged a $25 service fee in addition to the required application fee. ]

[ M. L. ] Fees received shall not be refunded.

18 VAC 15-20-60. Expiration.

All A. Each individual asbestos licenses license issued under this chapter shall expire one year from the last day of the month in which they are issued as indicated on the license [ wherein the applicant’s initial training or most recent refresher training required by 18 VAC 15-20-30 was completed in which it was issued ].

B. Each asbestos contractor and each asbestos analytical laboratory license issued under this chapter shall expire one year from the last day of the month in which it was issued.

C. Each accredited asbestos training program approved prior to [ the effective date of these regulations January 2, 2002 ] shall expire [ 24 months from the last day of the month in which it was approved on January 31, 2004, ] and may be renewed for 24 months at a time thereafter. Each accredited asbestos training program approved after [ the effective date of these regulations January 2, 2002, ] shall expire 24 months from the last day of the month in which it was approved.

18 VAC 15-20-70. Renewal application.

A. The department will shall mail a renewal notice to the each licensee and to each approved accredited asbestos training program at the last known address. The notice shall outline the procedures for renewal and the renewal fee amount. Failure to receive the notice shall not relieve the licensee or the approved accredited asbestos training program of the obligation to renew in a timely fashion.

B. Prior to the expiration date shown on the license or approval letter, each licensee licensed asbestos contractor, licensed asbestos analytical laboratory and approved accredited asbestos training program desiring to renew the license or approval shall return to the board the renewal notice and appropriate fee to the department. Should the licensee fail to receive the renewal notice, a copy of the current license may be submitted with the required fee. Should an approved accredited asbestos training program fail to receive the renewal notice, a letter indicating the desire to renew and the applicable fee may be submitted.

C. For individual licenses, only asbestos refresher training courses approved by the board shall meet the Prior to the expiration date shown on the individual’s current license, the individual desiring to renew that license shall provide evidence of meeting the annual refresher training requirement for license renewal and the appropriate fee. [ Asbestos refresher ] courses [ training programs approved by the ] US [ EPA under AHERA Regulations will not fulfill the renewal requirements unless the ] course [ training program is also a ] Virginia [ board-approved asbestos refresher training ] course [ program. The board will accept any asbestos training programs that are approved by EPA/AHERA or the board. ] All refresher courses must be discipline specific. Applicants for renewal shall forward proof that the annual retraining requirements and an examination has been successfully completed. A copy of the training certificate meeting the requirements outlined in 18 VAC 15-20-490 of this chapter shall accompany the renewal card notice and fee.

D. If the renewal fee is not received by the department within 30 days after the expiration date noted on the license, a late renewal fee shall be required in addition to the renewal fee as stated in 18 VAC 15-20-50.

E. Licensees failing to renew their licenses within six months after the expiration date noted on the license shall not be permitted to renew their licenses and shall apply as new applicants. Applicants shall reapply in accordance with Part III of this chapter.

D. Project monitors who also hold a valid Virginia asbestos supervisor or project designer license may meet the renewal training requirements by completing the supervisor refresher or project designer refresher, whichever is applicable.  Project monitors who hold only a project monitor license shall complete an accredited asbestos project monitor refresher training program to meet the renewal training requirements.

E. Annual refresher training certificates shall only be used once to renew an individual license.

F. Each license and each accredited asbestos training program approval that is not renewed within 30 days of the expiration date on the license or [ accreditation approval ] shall be subject to late fees as established in 18 VAC 15-20-50.

G. Each license and each approved accredited asbestos training program not renewed within six months after the expiration date shall not be renewed and the licensee or approved accredited asbestos training program shall apply for a new license or new approval.

18 VAC 15-20-80. [ No change from proposed. ]

PART IV.
ASBESTOS WORKER AND SUPERVISOR LICENSING REQUIREMENTS.

18 VAC 15-20-90. [ No change from proposed. ]

18 VAC 15-20-100. [ No change from proposed. ]

PART V.
ASBESTOS SUPERVISOR LICENSING REQUIREMENTS.

18 VAC 15-20-101. [ No change from proposed. ]

PART V VI.
ASBESTOS CONTRACTOR LICENSING REQUIREMENTS.

18 VAC 15-20-110 through 18 VAC 15-20-240. [ No change from proposed. ]

[ PART VI.
RFS CONTRACTOR LICENSING REUQIREMENTS.

PART VII.
RFS INSPECTOR LICENSING REQUIREMENTS. ]

PART VIII VII.
ASBESTOS INSPECTOR LICENSING REQUIREMENTS.

18 VAC 15-20-250. Qualifications for licensure.

A. Each individual applying to the board for licensure as an asbestos inspector shall have the following qualifications: submit a completed application, all training documents as required by 18 VAC 15-20-30 C, the appropriate fee as established in 18 VAC 15-20-50, and evidence of meeting the experience requirements as established in subsection B of this section. Evidence of experience and education shall comply with 18 VAC 15-20-40.

1. Applicants shall be at least 18 years of age;

2. The applicant must have successfully completed an asbestos inspector training course and examination approved by the board or an USEPA accredited AHERA inspector training course and examination. Applicants shall submit all training documents in accordance with 18 VAC 15-20-30 B;

3. B. The applicant shall be required to provide proof evidence of experience in performing asbestos inspections in buildings or industrial facilities, including collecting bulk samples, categorizing ACM, assessing ACM and preparing inspection reports. Experience may be gained by acting as an inspector, being in responsible charge of inspectors, or being under the direct supervision of an inspector The amount of experience required is dependent on the applicant’s formal education and is as follows:

a. Acting as an inspector accredited (after December 17, 1987) according to AHERA or the Virginia Asbestos Licensing Program;

b. Being in responsible charge of persons accredited as inspectors according to AHERA or the Virginia Asbestos Licensing Program; or

c. Being under the direct supervision of an inspector accredited according to AHERA or the Virginia Asbestos Licensing Program. All reports prepared by the unlicensed individual must be signed by the licensed or accredited individual in charge. The licensed or accredited individual in charge assumes responsibility for all reports prepared by the unlicensed individual.

4. 1. An applicant with a bachelor's degree in engineering, architecture, industrial hygiene, [ physical ] science or a related field must shall have at least six months experience as described above or have completed a minimum of five inspections. The applicant must submit the Experience and Educational Form (Form A) as noted in 18 VAC 15-20-40.

5. 2. An applicant with a two-year associate's degree in engineering, architecture, industrial hygiene, [ physical ] science or a related field must shall have at least 12 months experience as described above or have completed a minimum of 10 inspections. The applicant must submit the Experience and Educational Form (Form A) as noted in 18 VAC 15-20-40.

6. 3. An applicant with a high school diploma must shall have at least 24 months experience as described above or have completed a minimum of 15 inspections. The applicant must submit the Experience Verification Form (Form A) as noted in 18 VAC 15-20-40.

18 VAC 15-20-251. [ No change from proposed. ]

PART IX VIII.
ASBESTOS MANAGEMENT PLANNER LICENSING REQUIREMENTS.

18 VAC 15-20-260. [ No change from proposed. ]

18 VAC 15-20-270. Qualifications for licensure.

A. Each individual applying to the board for licensure as an asbestos management planner shall have the following qualifications: submit a completed application, all training documents as required by 18 VAC 15-20-30 C, the appropriate fee as required by 18 VAC 15-20-50, and evidence of meeting the experience requirements established by 18 VAC 15-20-250 B and subsection B of this section.  The applicant shall also meet all qualifications to be licensed as an asbestos inspector, whether or not the license is held.  Evidence of experience and education shall comply with 18 VAC 15-20-40.

1. Applicants shall be at least 18 years of age.

2. The applicant must have successfully completed an asbestos management planner training course and examination approved by the board or a USEPA accredited AHERA management planner training course and examination. Applicants shall submit all training documents in accordance with 18 VAC 15-20-30 B.

3. The applicant must meet all of the qualifications to be licensed as an asbestos inspector, whether or not the asbestos inspector license is held.

4. B. The applicant is required to shall provide proof evidence of experience evaluating inspection reports, selecting response actions, analyzing the cost of response actions, ranking response actions, preparing operations and maintenance plans and preparing management plans. The amount of experience required is dependent on the applicant’s formal education and is as follows:

B. Experience may be gained by acting as a management planner, being in responsible charge of management planners or being under the direct supervision of a management planner as follows:

1. Any experience gained after December 17, 1987, must be gained acting as a management planner accredited according to AHERA, or the Virginia Asbestos Licensing Program, being in responsible charge of persons accredited as management planners according to AHERA or being under the direct supervision of a management planner accredited according to AHERA or the Virginia Asbestos Licensing Program. All reports prepared by the unlicensed individual must be signed by the licensed or accredited person in charge, who assumes responsibility; or

2. Experience gained as an inspector as outlined in 18 VAC 15-20-250 may be substituted for the management planner experience requirements.

C. 1. An applicant with a bachelor's degree in engineering, architecture, industrial hygiene, [ physical ] science or a related field must shall have at least six months experience as described above or shall have completed a minimum of five management plans. The applicant must submit the Experience and Educational Verification Form (Form A) as noted in 18 VAC 15-20-40.

D. 2. An applicant with a two-year associate's degree in engineering, architecture, industrial hygiene, [ physical ] science or a related field must shall have at least 12 months experience as described above or shall have completed a minimum of 10 management plans. The applicant must submit the Experience and Educational Form (Form A) as noted in 18 VAC 15-20-40.

E. 3. An applicant with a high school diploma must shall have at least 24 months experience as described above or shall have completed a minimum of 15 management plans. The applicant must submit the Experience Verification Form (Form A) as noted in 18 VAC 15-20-40.

18 VAC 15-20-271. [ No change from proposed. ]

PART X IX.
ASBESTOS PROJECT DESIGNER LICENSING REQUIREMENTS.

18 VAC 15-20-280. [ No change from proposed. ]

18 VAC 15-20-290. [ No change from proposed. ]

18 VAC 15-20-291. [ No change from proposed. ]

PART XI X.
ASBESTOS PROJECT MONITOR LICENSING REQUIREMENTS.

18 VAC 15-20-300 through 18 VAC 15-20-332. [ No change from proposed. ]

PART XII XI.
ASBESTOS ANALYTICAL LABORATORY LICENSE LICENSING REQUIREMENTS.

18 VAC 15-20-340 through 18 VAC 15-20-360. [ No change from proposed. ]

18 VAC 15-20-361. Qualifications for licensure.

A. Each applicant for an asbestos analytical laboratory license shall submit a completed application, the appropriate fee as required by 18 VAC 15-20-50, and evidence of meeting the standards to perform one or more of the analyses described in subsections B, C and D of this section. Each license issued shall indicate which kind of analysis the asbestos analytical laboratory is seeking authorization to perform.

B. For authorization to analyze bulk materials using PLM, the applicant shall provide evidence that the asbestos analytical laboratory is currently NVLAP accredited for bulk asbestos fiber analysis or evidence that the asbestos analytical laboratory is AIHA accredited and proficient in the AIHA bulk asbestos program. A copy of the NVLAP Certificate of Accreditation, Scope of Accreditation and documentation of NVLAP proficiency or a copy of an AIHA accreditation certificate and proof of proficiency in the AIHA bulk program shall be submitted with the application for licensure.

C. For authorization to analyze airborne fibers using PCM:

1. For fixed laboratory sites, the applicant shall provide evidence that each facility is accredited by AIHA or that each facility has been rated "proficient" in the PAT Program’s most recent round of asbestos evaluations, or the applicant shall provide evidence that each analyst is listed or has applied for listing in the Asbestos Analyst Registry (AAR) and has a performance rating of "acceptable" for the most recent Asbestos Analyst Testing (AAT) round. The applicant shall also provide evidence that each analyst has completed the NIOSH 582 training program or equivalent [ as approved by the AIHA ].

2. For laboratories that will be conducting on-site analysis, the applicant shall provide evidence that each on-site analyst is listed [ or the applicant shall provide evidence that each analyst is listed ] or has applied for listing in the AAR and has a performance rating of "acceptable" for the most recent AAT round within six months after [ the implementation date of this chapter January 2, 2002, or is accredited by AIHA or has been rated "proficient" in the PAT Program's most recent round of asbestos evaluations.  The applicant shall also provide evidence that each analyst has completed the NIOSH 582 training program or equivalent ].

D. For licensure to analyze asbestos airborne fibers using TEM, the applicant shall provide evidence that the asbestos analytical laboratory is currently NVLAP accredited to analyze asbestos airborne fibers using TEM. A copy of the NVLAP Certificate of Accreditation, Scope of Accreditation and documentation of NVLAP proficiency shall be submitted with the application.

18 VAC 15-20-370 through 18 VAC 15-20-390. [ No change from proposed. ]

PART XIII XII.
GENERAL STANDARDS OF PRACTICE AND CONDUCT.

18 VAC 15-20-400. [ No change from proposed. ]

18 VAC 15-20-410. [ No change from proposed. ]

18 VAC 15-20-420. [ No change from proposed. ]

18 VAC 15-20-430. [ No change from proposed. ]

18 VAC 15-20-440. [ No change from proposed. ]

18 VAC 15-20-450. Prohibited acts Grounds for disciplinary action.

A. The following may be grounds for disciplinary action by the board shall have the authority to fine any licensee or [ accredited asbestos training program, ] accredited asbestos training provider or instructor, and to deny renewal, suspend, revoke or deny application for any license or approval as an [ accredited asbestos training program, ] accredited asbestos training provider or instructor provided for under Chapter 5 (§ 54.1-500 et seq.) [ or of ] Title 54.1 of the Code of Virginia for:

1. The licensee, training provider, or primary instructor has violated Violating or induced inducing another person to violate any of the provisions of Chapters Chapter 1, 2, 3, or 5 of Title 54.1 of the Code of Virginia, or any of the provisions of this chapter.

2. The licensee has obtained his Obtaining a license, [ approval as an accredited asbestos training program, ] approval as an accredited asbestos training provider or approval as an instructor through fraudulent means.

3. The licensee has altered Altering [ a , falsifying or issuing a fraudulent ] Virginia Asbestos License [ issued by the ] Commonwealth [ board ] or a training certificate issued by a an accredited asbestos training provider program.

4. The licensee, training provider or primary instructor violates Violating any provision of AHERA or ASHARA, or any federal or state regulation pertinent to asbestos activity.

5. The licensee has Having been found guilty by the board, an administrative body, or by a court of any material misrepresentation in the course of performing his asbestos-related operating duties.

6. The licensee has Subject to the provisions of § 54.1-204 of the Code of Virginia, having been convicted or found guilty, regardless of adjudication in any jurisdiction of the United States, of any felony or of any misdemeanor involving lying, cheating, or stealing, or of any violation while engaged in environmental remediation activity, which resulted in the significant harm or the imminent and substantial threat of significant harm to human health or the environment there being no appeal pending therefrom or the time for appeal having elasped. Any plea of nolo contendere shall be considered a conviction for the purposes of this chapter. The record of a conviction authenticated in such form as to be admissible in evidence under the laws of the jurisdiction where convicted, A certified copy of the final order, decree or case decision by a court or regulatory agency with lawful authority to issue such order, decree or case decision shall be admissible as prima facie evidence of such conviction or discipline.

7. Failing to notify the board in writing within 30 days of pleading guilty or nolo contendere or being convicted or found guilty of any felony or of any misdemeanor involving lying, cheating, or stealing or of any violation while engaged in environmental remediation activity which resulted in the significant harm or the imminent and substantial threat of significant harm to human health or the environment.

8. Negligence, or a continued pattern of incompetence, in the practice of the discipline in which the asbestos license is held.

9. Failing or neglecting to send any information or documentation that was requested by the board or its representatives.

10. Refusing to allow state or federal representatives access to any area of an abatement site for the purpose of lawful compliance inspections.

[ Any unlawful act or violation of any provision of Chapter 5 (§ 54.1-500 et seq.) of Title 54.1 of the Code of Virginia or of the regulations of the board by any asbestos supervisor or asbestos worker may be cause for disciplinary action against the asbestos contractor for whom he works if it appears to the satisfaction of the board that the asbestos contractor knew or should have known of the unlawful act or violation. ]

B. Any individual or firm whose license [ , approval as an accredited asbestos training program, ] or approval as an accredited asbestos training provider is revoked under this section shall not be eligible to reapply for a period of one year from the effective date of the final order of revocation. The individual or firm shall meet all education, experience and training requirements, complete the application and submit the required fee for consideration as a new applicant.

PART XIII.
STANDARDS OF PRACTICE AND CONDUCT FOR LICENSED ASBESTOS CONTRACTORS.

18 VAC 15-20-451. Asbestos contractor responsibilities.

A. Licensed asbestos contractors shall comply with all requirements, procedures, standards and regulations covering any part of an asbestos project established by the U.S. Environmental Protection Agency, the U.S. Occupational Safety and Health Administration, the Virginia Department of Labor and Industry [ , ] and [ the ] Divisions of Air Pollution and Waste Management of the Department of Environmental Quality (§ 54.1-517 [ of the ] Code of Virginia).

B. Licensed asbestos contractors shall comply with the requirements found in § 54.1-1100 of the Code of Virginia governing the regulation of general contractors.

C. A licensed asbestos contractor shall employ only licensed asbestos supervisors and workers to perform work on any asbestos project.

D. A licensed asbestos contractor shall ensure that a licensed asbestos supervisor is present at each job site while an asbestos project is in progress.

18 VAC 15-20-452. [ No change from proposed. ]

18 VAC 15-20-453. [ No change from proposed. ]

18 VAC 15-20-454. [ No change from proposed. ]

PART XIV.
STANDARDS OF PRACTICE AND CONDUCT FOR ASBESTOS PROJECT MONITORS.

18 VAC 15-20-455. [ No change from proposed. ]

[ 18 VAC 15-20-455.1.  Abatement projects that require a project monitor.

A project monitor is required on:

1. Asbestos projects performed in buildings that are occupied or intended to be occupied upon completion of the asbestos project exceeding 260 linear feet or 160 square feet or 35 cubic feet of asbestos-containing material; or

2. Whenever the building or property owner deems it necessary to monitor asbestos projects. ]

18 VAC 15-20-456. Responsibilities.

A. Asbestos project monitors shall conduct inspections of the contractor’s work practices and inspections of the containment [ each day abatement is performed when the project monitor is present ].

B. Asbestos project monitors shall maintain a daily log of all work performed. The daily log shall include, but not be limited to, inspection reports, air sampling data, type of work performed by the contractor, problems encountered and corrective action taken.

C. Asbestos project monitors shall take final air samples on all abatement projects, except for abatement projects in residential buildings.

D. Project monitors who analyze PCM air samples on site shall be employed by a licensed analytical laboratory and shall be listed or have applied for listing in the AAR [ and rated "acceptable" or is accredited by AIHA or has been rated "proficient" in the PAT Program's most recent round of asbestos evaluations ].

PART XV.
STANDARDS OF PRACTICE AND CONDUCT FOR ASBESTOS PROJECT DESIGNERS.

18 VAC 15-20-457. [ No change from proposed. ]

18 VAC 15-20-458. Responsibilities.

[ A. Licensed asbestos project designers shall prepare a written project design for each asbestos abatement project, except projects conducted in residential buildings.

B. ] The project design shall include, but is not limited to:

1. Scope of work.

2. Order of work.

3. Work methods and practices to be used.

4. Number and type of final air samples to be taken.

PART XVI.
STANDARDS OF PRACTICE AND CONDUCT FOR ASBESTOS INSPECTORS AND MANAGEMENT PLANNERS.

18 VAC 15-20-459. [ No change from proposed. ]

18 VAC 15-20-459.1. [ No change from proposed. ]

PART XVII.
STANDARDS OF PRACTICE AND CONDUCT FOR ASBESTOS ANALYTICAL LABORATORIES.

18 VAC 15-20-459.2. [ No change from proposed. ]

18 VAC 15-20-459.3. Responsibilities.

A. Each asbestos analytical laboratory using PLM to analyze bulk suspect material for the presence of asbestos shall analyze the material in accordance with [ "Interim Method for the Determination of Asbestos in Bulk Insulation Samples" found in Appendix A to Subpart F of 40 CFR Part 763 EPA 600/R-93/116 Method of Determination of Bulk Asbestos ] or the NIOSH method 9002.

B. Each asbestos analytical laboratory using PCM to analyze air samples for the presence of airborne fibers shall use the method outlined in Appendix A of OSHA’s 1926.1101 regulation or shall use the most recent version of NIOSH’s 7400 method.

C. Each asbestos analytical laboratory using TEM to analyze air samples for the presence of airborne asbestos fibers shall use the method outlined in Appendix A to Subpart E of 40 CFR Part 763 or shall use the most recent version of NIOSH’s 7402 method.

18 VAC 15-20-459.4. [ No change from proposed. ]

18 VAC 15-20-459.5. License [ certificate ].

A. The transfer of an asbestos analytical laboratory license is prohibited. Whenever there is any change in the controlling interest of the legal entity licensed, a new license is required.

B. A copy of the current asbestos analytical laboratory license will be on site at all times where analysis is performed, including project sites. The license shall be available for review by the department.

C. The board shall require asbestos analytical laboratories that wish to become or to remain licensed in the Commonwealth to conform to any future additional standards or regulations set forth by the EPA or accrediting entity.

D. The licensee shall permit the board to conduct periodic on-site inspections and evaluations of licensed asbestos analytical laboratory facilities. The inspections shall include, but not be limited to, equipment, procedure and protocol records, training and accreditation documentation and any other program evaluation results on file. Prior notice of such inspections is not required.

PART XVIII.
ACCREDITED ASBESTOS TRAINING PROGRAM APPROVAL.

18 VAC 15-20-459.6. [ No change from proposed. ]

18 VAC 15-20-459.7. [ No change from proposed. ]

18 VAC 15-20-459.8. [ No change from proposed. ]

18 VAC 15-20-459.9. [ No change from proposed. ]

18 VAC 15-20-459.10. Refresher approval.

A. Refresher training programs shall be one day (8 hours) for supervisors, workers, project designers and project monitors, and one-half day (4 hours) for inspectors and management planners. The refresher training program shall review federal and state regulations; discuss changes to the regulations, if applicable, and developments in state-of-the-art procedures; and review key aspects of the initial training program.

B. Persons wishing to [ sponsor conduct ] refresher training programs shall submit a training program review and audit application as established in 18 VAC 15-20-459.6.

18 VAC 15-20-459.11. Renewal of accredited asbestos training programs.

Providers of accredited asbestos training programs desiring to renew their approval shall submit the renewal notice to the department along with the following:

1. Appropriate fee.

2. [ List Name ] of [ the ] training [ programs program ] for which they are renewing.

3. Any changes made to the training [ program(s) program ].

4. Dates on which the training material was last updated.

[ 5.  Statement indicating that the training program continues to meet the regulation requirements established in this chapter. ]

18 VAC 15-20-459.12. Changes to an approved accredited asbestos training program.

Once an accredited asbestos training program has been approved, prior to the continuation of the accredited asbestos training program, substantial changes in the information required by subdivisions 1 through 5 of this section shall be submitted to the board for review and approval. The board will state its approval or disapproval of the changes by mail.

1. Training program curriculum.

2. Training program examination.

3. Training program materials.

4. [ Primary Principal ] instructors [ and work practice instructors ].

5. Certificate of completion.

18 VAC 15-20-459.13. Transfer of approval of an accredited asbestos training program.

The transfer of the approval of an accredited asbestos training program will require a review by the following procedure:

1. The applicant for transfer shall submit an application to the department and materials for review to determine if substantial changes have been made to the program. All submissions shall be in accordance with 18 VAC 15-20-459.6.

2. Receipt of applications and deposit of fees submitted does not indicate approval of the transfer.

3. A review of the submitted materials shall be performed to determine if substantial changes have been made. A substantial change is defined as a change in training program materials, curriculum, [ primary principal ] instructors or facilities at the time of transfer of the accredited asbestos training program. A complete field audit may be conducted of any applicant believed to have made a substantial change.

18 VAC 15-20-459.14. Access by the department.

Accredited asbestos training [ program ] providers shall permit department representatives to attend, evaluate, and monitor any accredited asbestos training program. Prior notice of attendance by agency representatives is not required.

18 VAC 15-20-459.15. Suspension or revocation of approval of an accredited asbestos training program.

A. The board may withdraw approval of any accredited asbestos training program for the following reasons:

1. The school, instructors, or training programs no longer meet the standards established in this chapter.

2. The board determines that the provider is not conducting the training in a manner that meets the requirements as set forth in this chapter.

3. Suspension or revocation of training approval in another state or by the EPA.

B. Decisions regarding withdrawal of approval shall be made by the board under the provisions of the Virginia Administrative Process Act [ (§ 9-6.14:1 § 2.2-4000 ] et seq. of the Code of Virginia).

PART XIV XIX.
TRAINING PROVIDER REQUIREMENTS ACCREDITED ASBESTOS TRAINING PROGRAM PERFORMANCE STANDARDS.

18 VAC 15-20-460. General.

This part outlines the recordkeeping responsibilities for an individual, a business, an agency, an institution or a sponsor [ a provider an accredited asbestos training provider (training provider) ] performing asbestos training under Virginia law. All records are required to be available for review by representatives of the board. Records required to be maintained by the training provider must shall be maintained at the address on the Certificate of Approval of the asbestos training course. All training requirements are in accordance with ASHARA (40 CFR 763 Appendix C to Subpart E ), the EPA April 1990 memorandum, or recommended EPA policy physical location of the accredited asbestos training provider.

18 VAC 15-20-470. Recordkeeping.

A. For all accredited asbestos training courses programs approved by the board, the training providers provider shall keep a list of all course training program participants attending the accredited asbestos training course program. The list shall contain the following minimum information:

1. Training provider;

2. Date of training;

3. Location of training course program presentation;

4. Type and length of training;

5. Course Training program [ director manager ] and [ primary principal ] instructor;

6. Course participants Training program participant's name as it will appear on the Certificate of Completion to be issued by the training provider;

7. Participants Participant's employer, if applicable;

8. Participants Participant's name, address, and social security number;

9. Participants Participant's Virginia asbestos license number, if applicable;

10. The resulting certificate number assigned to a participant who successfully completes the course accredited asbestos training program when applicable and expiration date; and

11. The participant's examination score, when applicable.

B. The course training program participant list shall be completed by the training provider and course training program participants daily.

C. The course training program participant [ listing list ] shall be retained by the training provider for three years following the date of completion of the training course program.

[ D. ] The course participant list shall be submitted to the board within five working days, after the last day of the course. [ The training provider shall provide to the board the training program participant list as described in subsection A of this section within 24 hours of training program completion. ]

[ E. D. ] The training provider shall retain all examinations completed by course training program participants for a period of three years.

[ E. F. ] Training providers shall notify the department no less than 48 hours prior to conducting an accredited asbestos training program. [ The department will not recognize training certificates from approved training providers that fail to notify. ]

[ G. The department will not recognize training certificates from approved training providers that fail to notify or fail to provide a training program participant list. ]

18 VAC 15-20-480. Course Accredited asbestos training program outline and syllabus.

A. Prior to the start of the accredited asbestos training course program, the training provider shall prepare a course outline or syllabus. The outline shall contain the following minimum information:

1. Course Training program title and length of training;

2. Starting time of each day of training;

3. Course Training program section, inclusive length of training time for each section and instructor for each course program section;

4. Scheduled breaks and inclusive length of breaks;

5. Scheduled lunch break and inclusive length of break;

6. Scheduled hands-on training, a description of the training to be performed, length of training and name of the instructor or instructors; and

7. Examination and inclusive length of examination time.

B. The training provider shall disseminate the course training program outline or syllabus to all course training program participants. A copy of the [ course training program ] outline shall be retained by the training provider for a period of three years following the completion of the training course program.

18 VAC 15-20-490. Certificates of completion.

A. Following attendance of the accredited asbestos training course program and successful completion of an examination by the course training program participant, the training provider shall issue a Certificate of Completion to the course training program participant. The certificate shall contain the following minimum information:

1. Training provider's business name;

2. Training provider's business address and phone number;

3. Location of training;

4. Typewritten or printed name of course training program participant;

5. Course Training program title and length of training in hours;

6. Certificate number;

7. Inclusive course training program dates;

8. Examination date;

9. An expiration date one year subsequent to after the date of completion of the accredited asbestos training course program;

10. For courses training programs covered under 40 CFR Part 763, Subpart E, Appendix C, a statement that the person receiving the certificate has completed the requisite training for asbestos accreditation under TSCA Title II;

11. Statement of attendance and successful completion of an examination by the course training program participant; and

12. Signature and typewritten or printed name of course the accredited asbestos training program [ director manager ] or administrator and [ primary principal ] instructor. The signature may be a printed facsimile.

B. Changes to the Certificate of Completion shall be submitted to the board for review and approval prior to issuance to course training program participants.

18 VAC 15-20-500. Course Training program materials: course training program manuals; video instruction; training equipment.

A. All training course program participants shall be issued a course training program manual for the asbestos training course program.

All materials will be legible and, in the case of Virginia approved training courses, submitted for review and approval by the board at least 45 days prior to being used by a course participant in an asbestos training course.

The training provider shall retain a copy on file for a period of three years following any amendments to the manual.

B. Use of video instruction is permitted as a method of instruction in a Virginia approved an accredited asbestos training course program, provided that videos are not the sole and primary source of instruction unless [ they the videos ] are interactive [ videos ].

Videos shall not be the primary source of instruction unless it is an interactive video.

All videos utilized in a Virginia approved asbestos training course shall have undergone the review and approval process required in Part XIV of this chapter.

Videos shall be made available to the board, if requested, during an on-site audit or inspection.

C. In no case will equipment utilized for display or part of hands-on training have been utilized on an asbestos abatement project site.

Equipment will be dedicated for training use only.

The training provider shall keep a listing of all equipment utilized for training on file.

The equipment list will contain the following minimum information:

1. Equipment brand name;

2. Equipment description; and

3. A statement of how the equipment is to be utilized in the accredited asbestos training course program.

The dated equipment list will be updated as new equipment is added as part of an accredited asbestos training program and retained each list must be maintained for a period of three years.

18 VAC 15-20-510. [ No change from proposed. ]

18 VAC 15-20-511. Instructor qualifications.

A. An approved accredited asbestos training program shall employ a training manager who:

1. Has a minimum of two years experience in teaching adults; or

2. Has a minimum of three years experience in the asbestos abatement industry.

B. An approved accredited asbestos training program shall use principal instructors who:

1. Have a minimum of 24 hours of asbestos specific training; and

2. Have a minimum of two years experience in the asbestos abatement industry, or have a minimum of two years' [ experience ] in teaching adults.

C. Documentation of all instructor qualifications shall be reviewed and approved by the board prior to the instructor teaching in an accredited asbestos training program.

D. Guest instructors are exempt from instructor qualifications and are limited to no more than two hours of training per day.

18 VAC 15-20-520. Number of instructors required to provide training.

A. The board strongly recommends a minimum of two instructors to teach a Virginia approved an accredited asbestos initial worker course training program.

B. The board requires At least two instructors shall be used for each Virginia approved supervisor, inspector, management planner, project designer and project monitor initial course accredited asbestos training program.

C. One instructor is adequate per [ accredited asbestos ] refresher course training program.

D. At least one instructor shall be in the class classroom and available to the students at all times during the course [ accredited asbestos ] training program.

18 VAC 15-20-530. [ No change from proposed. ]

18 VAC 15-20-540. [ No change from proposed. ]

18 VAC 15-20-550. [ No change from proposed. ]

18 VAC 15-20-560. [ No change from proposed. ]

18 VAC 15-20-570. Non-English speaking accredited asbestos training courses programs.

All Virginia approved [ accredited ] asbestos training courses programs shall be taught in English. Accredited asbestos worker training courses programs are exempt from this section.

18 VAC 15-20-580. Examinations.

A. All accredited asbestos training courses approved by the board and utilized for licensure by the board programs shall contain an examination following the instructional portion of the accredited asbestos training course program. This requirement shall apply to all Virginia approved courses accredited asbestos training programs regardless of course training program location.

B. Oral examinations, except for workers, are not permitted in a Virginia approved an accredited asbestos training course program. Trainers who provide worker oral examinations shall issue an answer sheet to be marked by the student. The student shall sign the answer sheet and it shall become a part of the trainers training provider’s required recordkeeping under 18 VAC 15-20-470 E.

C. Examinations in languages other than English are [ only ] permitted in accredited asbestos worker courses training programs [ only ].

D. Examinations shall be given in the language of the [ accredited asbestos ] training program’s [ course ] instruction.

E. Reexamination following unsuccessful completion of the examination is permitted in a Virginia approved asbestos training course. The reexamination shall be limited to one attempt to pass following the initial examination. If the participant fails to achieve a 70% passing score after the second attempt, the participant must shall retake the accredited asbestos training course program before he is permitted to take a retest. The training provider shall retain [ all ] the examinations completed by the course [ accredited asbestos ] training program participant in compliance with 18 VAC 15-20-470 E the recordkeeping requirements of this chapter.

18 VAC 15-20-590. Change of address, phone number or contact person.

Training providers approved by the board Providers of accredited asbestos training programs are required to notify the board in writing of changes of address, phone number or [ primary principal ] instructor within 30 business days of after changes to any of these items.

18 VAC 15-20-600. Termination of training.

When a board-approved training provider ceases to conduct any of its training [ courses programs ], the training provider it shall notify the board in writing and give the board the opportunity to take possession of the provider's asbestos training records relating to such [ courses programs ].

18 VAC 15-20-610. [ No change from proposed. ]

PART XV.
TRAINING COURSE APPROVAL PROCESS.

18 VAC 15-20-620 through 18 VAC 15-20-690. [ No change from proposed. ]

PART XVI XX.
accredited asbestos TRAINING COURSE REQUIREMENTS program STANDARDS.

18 VAC 15-20-700. General.

In all of the following accredited asbestos training course program [ (training program) ] requirements, one day shall be equal to eight hours, inclusive of lunch and breaks. In all refresher training course requirements one day shall be equal to eight hours. All training courses, except project monitor, shall meet the minimum requirements set forth in ASHARA (40 CFR 763).

18 VAC 15-20-710. [ No change from proposed. ]

18 VAC 15-20-720. [ No change from proposed. ]

18 VAC 15-20-730. [ No change from proposed. ]

18 VAC 15-20-740. [ No change from proposed. ]

18 VAC 15-20-750. [ No change from proposed. ]

18 VAC 15-20-760. [ No change from proposed. ]

18 VAC 15-20-770. Inspector training.

A. Asbestos inspectors shall complete a three-day (24 hours) [ accredited asbestos ] training course program as outlined below. The course training program shall include lectures, demonstrations, four hours of hands-on training, course training program review and a written examination. The accredited asbestos inspector training course program shall address the following topics:

1. Course Training program overview.

a. The role of the inspector in the asbestos abatement industry.

b. A discussion of inspection requirements and criteria for AHERA, NESHAPs and state agencies.

2. Background information on asbestos.

a. Identification of asbestos, and examples and discussion of the uses and locations of asbestos in buildings.

b. Physical appearance of asbestos.

3. Potential health effects related to asbestos exposure.

a. The nature of asbestos-related diseases.

b. Routes of exposure, dose-response relationships and the lack of a safe exposure level.

c. The synergism between cigarette smoking and asbestos exposure.

d. Latency period for asbestos-related diseases, a discussion of the relationship of asbestos exposure to asbestosis, lung cancer, mesothelioma and cancer of other organs.

4. Functions/qualifications for inspectors.

a. Discussions of prior experience and qualifications for inspectors and management planners.

b. Discussions of the functions of an accredited inspector as compared to those of an accredited management planner.

c. Discussion of the inspection process including inventory of ACM and physical assessment.

5. Legal liabilities and defenses.

a. Responsibilities of the inspector, a discussion of comprehensive general liability policies, claims made and occurrence policies, environment and pollution liability policy clauses; state liability insurance requirements.

b. Bonding and relationship of insurance availability to bond availability.

6. Understanding building systems.

a. The relationship between building systems, including: an overview of common building physical plan layout; heat, ventilation and air conditioning (HVAC) system types; physical organization; and where asbestos is found on HVAC components.

b. Building mechanical systems, their types and organization and where to look for asbestos on such systems.

c. Inspecting electrical systems, including appropriate safety precautions.

d. Reading building plans and as-built drawings.

7. Public/employee/building occupant relations.

a. Notification of employee organizations about the inspection.

b. Signs to warn building occupants.

c. Tactics in dealing with occupants and the press.

d. Scheduling inspections to minimize disruptions.

e. Education of building occupants about actions being taken.

8. Preinspection planning and review of previous inspection records.

a. Scheduling the inspection and obtaining access.

b. Building record review; identification of probable homogeneous areas from building plans or as-built drawings.

c. Consultation with maintenance or building personnel.

d. Review of previous inspection, sampling, and abatement records of a building.

e. The role of the inspector in exclusions for previously performed inspections.

9. Inspection for friable and nonfriable asbestos-containing material (ACM) and assessment of the condition of friable ACM.

a. Procedures to follow in conducting visual inspections for friable and nonfriable ACM.

b. Types of building materials that may contain asbestos.

c. Touching materials to determine friability.

d. Open return air plenums and their importance in HVAC systems.

e. Assessing damage, significant damage, potential damage, and potential significant damage.

f. Amount of suspected ACM, both in total quantity and as a percentage of the total area.

g. Type of damage.

h. Accessibility.

i. Material's potential for disturbance.

j. Known or suspected causes of damage or significant damage, and deterioration as assessment factors.

10. Bulk sampling/documentation of asbestos in schools.

a. Detailed discussion of the "Simplified Sampling Scheme for Friable Surfacing Materials" (USEPA 560/5-85-030a October 1985).

b. Techniques to ensure sampling in a randomly distributed manner for other than friable surfacing materials.

c. Techniques for bulk sampling.

d. Sampling equipment the inspector should use.

e. Patching or repair of damage done in sampling; an inspector's repair kit.

f. Discussion of polarized light microscopy.

g. Choosing an accredited laboratory to analyze bulk samples.

h. Quality control and quality assurance procedures.

11. Inspector respiratory protection and equipment.

a. Classes and characteristics of respirator types.

b. Limitations of respirators.

c. Selection, inspection, donning, use, maintenance, and storage procedures for respirators.

d. Methods for field testing of the facepiece-to-face seal (positive and negative pressure fitting tests); qualitative and quantitative fit testing procedures.

e. Variability between field and laboratory protection factors.

f. Factors that alter respirator fit (e.g., facial hair, dental work, weight loss or gain).

g. The components of a proper respiratory protection program.

h. Selection and use of personal protective clothing.

i. Use, storage, and handling of nondisposable clothing.

12. Recordkeeping and writing the inspection report.

a. Labeling of samples and keying sample identification to sampling location.

b. Recommendations on sample labeling.

c. Detailing of ACM inventory.

d. Photographs of selected sampling areas and examples of ACM condition.

e. Information required for inclusion in the management plan by TSCA Title II section 203 (i)(1).

13. Regulatory review.

a. USEPA EPA Worker Protection Rule found at 40 CFR Part 763, Subpart G.

b. TSCA Title II.

c. OSHA Asbestos Construction Standard (29 CFR 1926.58 1926.1101).

d. OSHA respirator requirements (29 CFR 1910.134).

e. The friable ACM in Schools Rule found at 40 CFR Part 763, Subpart F.

f. Applicable state and local regulations.

g. Differences in federal and state requirements where they apply and the effects, if any, on public and nonpublic schools, and commercial and public buildings.

14. Field trip.

a. [ Including a ] Field exercise with a walk-through inspection.

b. On-site discussion of information gathering and determination of sampling locations.

c. On-site practice in physical assessment.

d. Classroom discussion of field exercise.

15. Course Training program review. A review of key aspects of the accredited asbestos training course program.

18 VAC 15-20-780. [ No change from proposed. ]

18 VAC 15-20-790. [ No change from proposed. ]

18 VAC 15-20-800. Asbestos management planner training.

Asbestos management planners seeking accreditation must shall complete an accredited asbestos inspector training course program as outlined above provided in 18 VAC 15-20-770 and a two-day [ accredited asbestos ] management planner training course program. The two-day (16 hours) accredited asbestos training program shall include lectures, demonstrations, course program review, and a written examination. The accredited asbestos management planner training course program shall address the following topics:

1. Course Training program overview.

a. The role of the management planner.

b. Operations and maintenance programs.

c. Setting work priorities; protection of building occupants.

2. Evaluation/interpretation of survey results.

a. Review of TSCA Title II requirements for inspection and management plans as given in section 203(i)(1) of TSCA Title II.

b. Summarized field data and laboratory results; comparison between field inspector's data sheet with laboratory results and site survey.

3. Hazard assessment.

a. Amplification of the difference between physical assessment and hazard assessment.

b. The role of the management planner in hazard assessment.

c. Explanation of significant damage, damage, potential damage, and potential significant damage and use of a description (or decision tree) code for assessment of ACM; assessment of friable ACM.

d. Relationship of accessibility, vibration sources, use of adjoining space, air plenums and other factors to hazard assessment.

4. Legal implications.

a. Liability; insurance issues specific to management planners.

b. Liabilities associated with interim control measures, in-house maintenance, repair, and removal.

c. Use of results from previous inspections.

5. Evaluation and selection of control options.

a. Overview of encapsulation, enclosure, interim operations and maintenance, and removal; advantages and disadvantages of each method.

b. Response actions described via a decision tree or other appropriate method; work practices for each response action.

c. Staging and prioritizing of work in both vacant and occupied buildings.

d. The need for containment barriers and decontamination in response actions.

6. Role of other professionals.

a. Use of industrial hygienists, engineers and architects in developing technical specifications for response actions.

b. Any requirements that may exist for an architect to sign-off on plans.

c. Team approach to designing of high-quality job specifications.

7. Developing an operations and maintenance (O&M) plan.

a. Purpose of the plan.

b. Discussion of applicable USEPA guidance documents.

c. What actions should be taken by custodial staff: proper cleaning procedures; steam cleaning and high efficiency particulate aerosol air (HEPA) vacuuming.

d. Reducing disturbance of ACM.

e. Scheduling O&M for off-hours; rescheduling or canceling renovation in areas with ACM.

f. Boiler room maintenance.

g. Disposal of ACM.

h. In-house procedures for ACM: bridging and penetrating encapsulants, pipe fittings, metal sleeves, poly vinyl chloride (PVC), canvas, and wet wraps; muslin with straps; fiber mesh cloth; mineral wool, and insulating cement.

i. Discussion of employee protection programs and staff training.

j. Case study in developing an O&M plan (development, implementation process, and problems that have been experienced).

8. Regulatory review.

a. Focusing on the OSHA Asbestos Construction Standard found in 29 CFR 1926.58.

b. The National Emission Standard for Hazardous Air Pollutants (NESHAPS) found at 40 CFR 61, Subparts A (General Provisions) and M (National Emission Standard for Asbestos).

c. USEPA Worker Protection Rule found in 40 CFR 763, Subpart G; TSCA Title II.

d. Applicable state regulations.

9. 8. Recordkeeping for the management planner.

a. Use of field inspector's data sheet along with laboratory results.

b. On-going recordkeeping as a means to track asbestos disturbance.

c. Procedures for recordkeeping.

10. 9. Assembling and submitting the management plan.

a. Plan requirements in TSCA Title II section 203(I)(1).

b. The management plan as a planning tool.

11. 10. Financing abatement actions.

a. Economic analysis and cost estimates.

b. Development of cost estimates.

c. Present costs of abatement versus future operations and maintenance costs.

d. Asbestos School Hazard Abatement Act grants and loans.

12. 11. A review of key aspects of the accredited asbestos training course program.

18 VAC 15-20-810. [ No change from proposed. ]

18 VAC 15-20-820. Refresher training course program.

A. Management planners shall attend [ both the management planner refresher training program of one-half day (four hours) and ] the inspector refresher course training program of 1/2 one-half day (four hours) [ plus an additional 1/2 one-half day (four hours) on management planning ]. The course [ management planner refresher ] training program shall review federal and state regulations, discuss changes, if applicable, and review developments in state-of-the-art procedures. A review of the following topics from the initial accredited asbestos management planner training course program shall be included in the asbestos management planner refresher training course program:

1. Evaluation and interpretation of survey results;

2. Hazard assessment;

3. Evaluation and selection of control options; and

4. Developing an Operations and Maintenance plan.

B. The use of exercises to encourage interactive learning and participation is suggested. These exercises may take the form of reviewing inspection reports, a video or photo walk-through of a building to have a management plan prepared for and a review of reinspection or abatement reports to update or prepare a management plan to draw upon items covered in the accredited asbestos inspector course training program and the initial accredited asbestos management planner course training program.

C. A written closed-book examination will be administered covering the topics included in the asbestos inspector management planner refresher course training program. The examination will consist of no fewer than 50 questions. The passing score will be 70% correct. Persons who pass the asbestos management planner refresher training course program examination will receive a Certificate of Completion as specified in 18 VAC 15-20-490 this chapter.

18 VAC 15-20-830. Asbestos project designer training.

Asbestos project designers shall complete a three-day (24 hours) [ accredited asbestos project designer ] training course program as outlined below. The three-day asbestos project designer training program shall include lectures, demonstrations, a field trip, course training program review, and a written examination. The three-day asbestos project designer training course program shall address the following topics:

1. Course Training program overview.

a. The role of the project designer in the asbestos abatement industry.

b. Discussion of what a project design is.

2. Background information on asbestos.

a. Identification of asbestos; examples and discussion of the uses and locations of asbestos in buildings.

b. Physical appearance of asbestos.

3. Potential health effects related to asbestos exposure.

a. Nature of asbestos-related diseases.

b. Routes of exposure, dose-response relationships and the lack of a safe exposure level.

c. The synergistic effect between cigarette smoking and asbestos exposure.

d. The latency period of asbestos-related diseases; a discussion of the relationship between asbestos exposure and asbestosis, lung cancer, mesothelioma, and cancer of other organs.

4. Overview of abatement construction projects.

a. Abatement as a portion of a renovation project.

b. OSHA requirements for notification of other contractors on a multi-employer site (29 CFR 1926.58 1926.1101).

5. Safety system design specifications.

a. Construction and maintenance of containment barriers and decontamination enclosure systems.

b. Positioning of warning signs.

c. Electrical and ventilation system lock-out.

d. Proper working techniques for minimizing fiber release.

e. Entry and exit procedures for the work area, use of wet methods, use of negative pressure exhaust ventilation equipment, use of high efficiency particulate aerosol air (HEPA) vacuums, proper clean-up and disposal of asbestos, work practices as they apply to encapsulation, enclosure, and repair, use of glove bags and a demonstration of glove bag use.

6. Field trip.

a. Visit an a proposed abatement site or other suitable building site, including on-site discussions of abatement design.

b. Building walk-through inspection, and discussion following the walk-through.

7. Employee personal protective equipment.

a. Classes and characteristics of respirator types.

b. Limitations of respirators, proper selection, inspection, donning, use, maintenance, and storage procedures.

c. Methods for field testing of the face-to-facepiece facepiece-to-face seal (positive and negative pressure fitting tests).

d. Qualitative and quantitative fit testing procedures.

e. Variability between field and laboratory protection factors, factors that alter respirator fit (e.g., facial hair, dental work and weight loss or gain).

f. Components of a proper respiratory protection program.

g. Selection and use of personal protective clothing, use, storage and handling of nondisposable clothing.

h. Regulations covering personal protective equipment.

8. Additional safety hazards.

a. Hazards encountered during abatement activities and how to deal with them.

b. Electrical hazards, heat stress, air contaminants other than asbestos, fire and explosion hazards.

9. Fiber aerodynamics and control.

a. Aerodynamic characteristics of asbestos fibers.

b. Importance of proper containment barriers.

c. Settling time for asbestos fibers.

d. Wet methods in abatement.

e. Aggressive air monitoring following abatement.

f. Aggressive air movement and negative pressure exhaust ventilation as a clean-up method.

10. Designing abatement solutions.

a. Discussions of removal, enclosure, and encapsulation methods.

b. Asbestos waste disposal.

11. Budgeting/cost estimation.

a. Development of cost estimates.

b. Present costs of abatement versus future operations and maintenance costs.

c. Setting priorities for abatement jobs to reduce cost.

12. Writing abatement specifications.

a. Means and methods specifications versus performance specifications.

b. Design of abatement in occupied buildings.

c. Modification of guide specifications to a particular building.

d. Worker and building occupant health/medical considerations.

e. Replacement of ACM with non-asbestos substitutes.

f. Clearance of work area after abatement.

g. Air monitoring for clearance.

13. Preparing abatement drawings.

a. Use of as-built drawings.

b. Use of inspection photographs and on-site reports.

c. Particular problems in abatement drawings.

14. Contract preparation and administration.

15. Legal/liabilities/defenses.

a. Insurance considerations, bonding, hold harmless clauses, and use of abatement contractor's liability insurance.

b. Claims-made versus occurrence policies.

16. Replacement of asbestos with asbestos-free substitutes.

17. Role of other consultants.

a. Development of technical specification sections by industrial hygienists or engineers.

b. The multi-disciplinary team approach to abatement design.

c. The use and responsibilities of a project monitor on the abatement site.

18. Occupied buildings.

a. Special design procedures required in occupied buildings.

b. Education of occupants.

c. Extra monitoring recommendations.

d. Staging of work to minimize occupant exposure.

e. Scheduling of renovation to minimize exposure.

19. Relevant federal, state and local regulatory requirements. Procedures and standards including:

a. Requirements of TSCA Title II;

b. 40 CFR Part 61, National Emission Standards for Hazardous Air Pollutants, Subparts A (General Provisions) and M (National Emission Standard for Asbestos);

c. OSHA standards for permissible exposure to airborne concentrations of asbestos fibers and respiratory protection (29 CFR 1910.134);

d. USEPA Worker Protection Rule, found at 40 CFR Part 763, Subpart G;

e. OSHA Asbestos Construction Standard found at 29 CFR 1926.58 1926.1101; and

f. OSHA Hazard Communication Standard found in 29 CFR 1926.59.

20. A review of key aspects of the accredited asbestos training course program.

18 VAC 15-20-840. [ No change from proposed. ]

18 VAC 15-20-850. [ No change from proposed. ]

18 VAC 15-20-860. Project monitor training.

A. Asbestos abatement project monitors shall complete a five-day (40 hours) [ accredited asbestos ] training course program as outlined below. All training courses programs shall be approved by the department board. The accredited asbestos training course program shall include lecture lectures, demonstrations, course training program review, examination, and at least six hours of hands-on training which allows project monitors the experience of performing actual tasks associated with asbestos project monitoring. Those applicants who hold current [ supervisors supervisor ] or project [ designers designer ] certification accreditation need not complete the entire 40-hour accredited asbestos training course program, but may complete the 16-hour portion of the course beginning at topic number 11 training program described in subdivision B 1 of this section and take the examination. The comprehensive 40-hour accredited asbestos project monitor training course program shall address the following topics:

1. The physical characteristics of asbestos and asbestos-containing materials.

a. Identification of asbestos.

b. Typical uses and locations in buildings, physical appearance.

c. A review of hazard assessment control options.

d. A summary of abatement control options.

2. Potential health effects related to asbestos exposure.

a. The nature of asbestos-related diseases.

b. Routes of exposure, dose-response relationships and the lack of a safe exposure level.

c. Synergism between cigarette smoking and asbestos exposure.

d. Latency period for disease; a discussion of the relationship between asbestos exposure and asbestosis, lung cancer, mesothelioma, and cancer of the other organs.

3. Employee personal protective equipment.

a. Classes and characteristics of respirator types.

b. Limitations of respirators and their proper selection, inspection, donning, use, maintenance and storage procedures.

c. Methods for field testing of the facepiece-to-face seal (positive and negative pressure fitting tests).

d. Qualitative and quantitative fit testing procedures.

e. Variability between field and laboratory protection factors.

f. Factors that alter respirator fit (e.g., facial hair, dental work, weight loss or gain).

g. The components of a proper respiratory protection program.

h. Selection and uses of personal protective clothing; use, storage, and handling of nondisposable clothing.

i. Regulations covering personal protection equipment.

4. State of the art work practices.

a. Work practices for asbestos abatement activities including description of proper construction and maintenance barriers and decontamination enclosure systems.

b. Positioning of warning signs.

c. Electrical and ventilation system lock-out.

d. Working techniques for minimizing fiber release, use of wet methods, use of negative pressure ventilation equipment, use of high efficiency particulate air (HEPA) vacuums. Entry and exit procedures for work area.

e. Clean-up and disposal procedures.

f. Work practices for removal, encapsulation, enclosure and repair. Use of glove bags and a demonstration of glove bag use.

g. Emergency procedures for sudden release.

h. Potential exposure situations.

i. Transport and disposal procedures.

j. Recommended and prohibited work practices.

k. Discussion of new abatement related techniques and methodologies.

5. Personal hygiene.

a. Entry and exit procedures for the work area; use of showers; avoidance of eating, drinking, smoking, and chewing (gum or tobacco) in the work area.

b. Potential exposures, such as family exposure, shall also be included.

6. Additional safety hazards as covered in OSHA CFR Parts 1926 and 1910 to include:

a. Hazards encountered during the abatement activities and how to deal with them, including electrical hazards, heat stress, air contaminants other than asbestos, fire, and explosion hazards;

b. Scaffold and ladder hazards;

c. Slips, trips and falls; and

d. Confined spaces.

7. Medical monitoring. OSHA requirements for a pulmonary function test, chest x-rays and a medical history for each employee.

8. Respiratory protection programs and medical surveillance programs.

9. Insurance and liability issues:

a. Contractor issues, worker's compensation coverage, and exclusions.

b. Third-party liabilities and defenses.

c. Insurance coverage and exclusions.

10. Relevant federal, state and local regulatory requirements, procedures and standards including:

a. Requirements of TSCA Title II;

b. 40 CFR Part 61 National Emission Standards for Hazardous Air Pollutants, Subparts A (General Provisions) and M (National Emission Standards for Asbestos);

c. OSHA Standards for permissible exposure to airborne concentrations of asbestos fibers and respiratory protection (29 CFR 1910.134);

d. OSHA Asbestos Construction Standard (29 CFR 1926.58 1926.1101);

e. OSHA Hazard Communication Standard (29 CFR 1926.59);

f. USEPA Worker Protection Rule, 40 CFR Part 763, Subpart G;

g. Requirements of Asbestos-Containing Waste Materials, 9 VAC 20-80-640;

h. DOT 49 CFR Parts 171 and 172 Subpart H; and

i. Virginia asbestos licensing regulations.

B. The material outlined below encompasses the 16-hour accredited asbestos project monitor training course program. Those applicants who are currently accredited as supervisors or project designers need only to complete this the 16-hour project monitors course monitor training program and examination. The comprehensive 40-hour project monitor training program includes the preceding topics and continues below.

1. Air monitoring.

a. NIOSH Asbestos Monitoring Procedure. Procedures to determine airborne concentration of asbestos fibers, including a description of aggressive sampling, sampling equipment and methods.

(1) Explanation of analytical methods, measures of precision, control of errors, collecting measurement samples, fiber counts, sampling and calibration equipment, statistics, quality control techniques in sampling.

(2) Review of OSHA Asbestos Regulations 29 CFR Part 1926, Subpart F, 1-6.

b. Sampling strategy.

(1) Why samples are taken.

(2) Sampling inside and outside of containment area.

(3) Placement of pumps.

c. Reasons for air monitoring.

d. Types of samples and interpretation of results, specifically from analysis performed by polarized light, phase-contrast, and electron microscopy analyses.

e. Final clearance.

2. Overview of supervisory techniques for asbestos abatement activities to include the information covered in the accredited asbestos supervisor's supervisor training course program. A review of the required work practices and safety considerations.

3. Field Trip.

a. Visit a proposed abatement site or other suitable building site, including on-site discussions of abatement design.

b. Building walk-through inspection and discussion following the walk through.

4. Fiber aerodynamics and control.

a. Aerodynamic characteristics of asbestos fibers.

b. Importance of proper containment barriers.

c. Settling time for asbestos fibers.

d. Wet methods in abatement.

e. Aggressive air monitoring following abatement.

f. Aggressive air movement and negative pressure exhaust ventilation as a clean-up method.

5. Project specifications. Discussion of key elements that are included in contract specifications.

a. Means and methods specifications versus performance specifications.

b. Considerations for design of abatement in occupied buildings.

c. Worker and building occupant health/medical considerations.

d. Replacement of ACM with nonasbestos substitutes.

e. Clearance of work area after abatement.

f. Use of as-built drawings.

g. Use of inspection photographs and on-site reports.

h. Particular problems in abatement drawings.

6. Conducting inspections.

a. Inspection prior to containment to assure condition of items and proper precleaning.

b. Inspection of containment prior to commencement of abatement to assure that containment is complete and proper.

c. Daily work and containment inspections.

d. Final visual inspection and a discussion of the ASTM E1368 method.

7. Recordkeeping and documentation.

a. Project logs.

b. Inspection reports.

c. Waste shipment record requirements (WSR).

d. Recordkeeping required by federal, state or local regulations.

e. Recordkeeping required for insurance purposes.

8. Role of project monitor in relation to:

a. Building owner,

b. Building occupants,

c. Abatement contractor, and

d. Other consultants.

9. Occupied buildings.

a. Special procedures recommended in occupied buildings.

b. Extra monitoring recommendations.

10. A review of NESHAP Guidance Documents.

a. Common Questions on the Asbestos NESHAP.

b. Asbestos NESHAP: Regulated Asbestos-containing Materials Guidance (EPA 340/1-90-018).

c. Asbestos NESHAP: Adequately Wet Guidance (EPA 340/1-90-019).

11. A review of key aspects of the accredited asbestos training course program.

12. Examination.

18 VAC 15-20-870. [ No change from proposed. ]

18 VAC 15-20-880. Refresher training course program.

A. [ The ] accredited asbestos project monitor refresher training program shall be one day (eight hours) [ in length ] . The course training program shall review federal and state regulations, discuss changes to the regulations, if applicable, and review developments in state-of-the-art procedures. A review of the following topics from the initial accredited asbestos project monitor training course program shall be included in the asbestos project monitor refresher training course program:

1. State-of-the-art work practices;

2. Occupied buildings;

3. Employee personal protective equipment;

4. Fiber aerodynamics and control; and

5. Recordkeeping and documentation.

B. The use of exercises to encourage interactive learning and participation is suggested. These exercises may take the form of reviewing inspection reports, a video or photo walk-through of a building to determine a sampling strategy, a review of a mock-up abatement area to determine that containment is adequate, or review of a mock-up abatement area where a visual inspection may be performed.

C. A written closed-book examination will be administered covering the topics included in the asbestos project monitor refresher courses training program. The examination will consist of no fewer than 50 questions. The passing score will be 70% correct. Persons who pass the asbestos project monitor refresher training course program examination will receive a Certificate of Completion as specified in 18 VAC 15-20-490 this chapter.

18 VAC 15-20-890 through 18 VAC 15-20-960. [ No change from proposed. ]

NOTICE: The forms used in administering 18 VAC 15-20, Virginia Asbestos Licensing Regulations, are not being published due to the large number; however, the name of each form is listed below. The forms are available for public inspection at the Department of Professional and Occupational Regulation, 3600 West Broad Street, Richmond, Virginia, or at the office of the Registrar of Regulations, General Assembly Building, 2nd Floor, Richmond, Virginia.

PART XVII.

FEE SCHEDULE.

FORMS

[ Application for Asbestos Contractor License (Revised 1/97).

Application for Asbestos Licensing.

Application for Training Course Approval.

Asbestos Licensing Application, Form A.

Verification of Degree Granted.

Instruction Sheets.

Asbestos License Application Instructions, 33AINS (eff. 10/30/01).

Asbestos License Application, 33ALIC (eff. 10/30/01).

Experience Verification, 33AEXPED (eff. 10/30/01).

Education Verification, 33AEXPED (eff. 10/30/01).

Virginia Asbestos Licensing Consumer Information Sheet, 33ACIS (eff. 10/30/01).

Inspector/Project Designer Contractor Disclosure Form, 33ADIS (eff. 10/30/01).

Asbestos Contractor License Application, 33ACON (eff. 10/30/01).

Asbestos Analytical Laboratory License Application, 33ALAB (eff. 10/30/01).

Asbestos Training Program Review and Audit Application, 33ACRS (eff. 10/30/01); w/instructions, 33ACRSRQ (eff. 10/30/01). ]

VA.R. Doc. No. R00-185; Filed November 8, 2001, 9:20 a.m.