STATE AIR POLLUTION CONTROL BOARD

Title of Regulation: Regulations for the Control and Abatement of Air Pollution (Rev. D00). 9 VAC 5-80. Permits for Stationary Sources (amending 9 VAC 5-80-2000 through 9 VAC 5-80-2090, 9 VAC 5-80-2110, 9 VAC 5-80-2120, 9 VAC 5-80-2150, 9 VAC 5-80-2180, and 9 VAC 5-80-2190; adding 9 VAC 5-80-2200, 9 VAC 5-80-2210, 9 VAC 5-80-2220, 9 VAC 5-80-2230, and 9 VAC 5-80-2240; repealing 9 VAC 5-80-2100 and 9 VAC 5-80-2160).

Statutory Authority: § 10.1-1308 of the Code of Virginia.

Effective Date: May 1, 2002.

Summary:

The amendments (i) revise the emission reduction offset ratio; (ii) provide for state-only permit terms and conditions; (iii) clarify the regulation’s applicability; and (iv) make the regulation consistent with the other new source review regulations.

Since the proposed amendments were published, the following substantive changes were made:

1.  The definition of "fugitive emissions" has been amended to remove the language that would leave the impression that a functionally equivalent opening must already exist (9 VAC 5-80-2010 C).

2.  Provisions that would allow the designation of state-only conditions have been amended to limit the designated conditions to those relating to state toxics or odor control programs (9 VAC 5-80-2020 E 1 (ii) and E 2).

Since the proposed amendments were published, the following substantive changes were made:

1. The definition of “fugitive emissions” has been amended to remove language that would leave the impression that a functionally equivalent opening must already exist.  (9 VAC 5-80-2010 C)

2. Provisions that would allow the designation of state-only conditions have been amended to limit the designated conditions to those relating to state toxics or odor control programs. (9 VAC 5-80-2020 E 1 (ii) and E 2)

Summary of Public Comment and Agency's Response:  A summary of comments made by the public may be obtained from the promulgating agency or viewed at the office of the Registrar of Regulations.

Agency Contact: Alma Jenkins, Office of Air Regulatory Development, Department of Environmental Quality, P.O. Box 10009, Richmond, VA 23240, telephone (804) 698-4070.

REGISTRAR'S NOTICE: The proposed regulation was adopted as published in 18:3 VA.R. 282-300 October 22, 2001, with the changes identified below. Pursuant to § 2.2-4031 of the Code of Virginia, the adopted regulation is not published at length; however, the sections that have changed since publication of the proposed are set out.

9 VAC 5-80-2000. Applicability.

A. The provisions of this article apply to the construction or reconstruction of any person seeking to construct or reconstruct any new major stationary source or to make a major modification to a major stationary source, if the source or modification is or would be major for the pollutant for which the area is designated as nonattainment.

B. The provisions of this article apply in nonattainment areas [ designated in 9 VAC 5-20-204 ].

C. At such time that a particular source or modification becomes a major stationary source or major modification solely by virtue of a relaxation in any enforceable limitation which was established after August 7, 1980, on the capacity of the source or modification otherwise to emit a pollutant, such as a restriction on hours of operation, then the requirements of this article shall apply to the source or modification as though construction had not commenced on the source or modification.

D. Where a source is constructed or modified in contemporaneous increments which individually are not subject to approval under this article and which are not part of a program of construction or modification in planned incremental phases approved by the board, all such increments shall be added together for determining the applicability of this article. An incremental change is contemporaneous with the particular change only if it occurs between the date five years before construction on the particular change commences and the date that the increase from the particular change occurs.

E. Unless specified otherwise, the provisions of this article are applicable to various sources apply as follows:

1. Provisions referring to "sources," "new and/or modified sources" or "stationary sources" are applicable apply to the construction, reconstruction or modification of all major stationary sources and major modifications.

2. Any emissions units or pollutants not subject to the provisions of this article may be subject to the provisions of 9 VAC 5-80-10 Article 6 (9 VAC 5-80-1100 et seq.), Article 7 (9 VAC 5-80-1400 et seq.), or Article 8 (9 VAC 5-80-1700 et seq.) of this part.

3. Provisions referring to "state and federally enforceable" and "federally and state enforceable" or similar wording shall mean "state-only enforceable" for terms and conditions of a permit designated state-only enforceable under 9 VAC 5-80-2020 E.

F. Regardless of the exemptions provided in this article, no owner or other person shall circumvent the requirements of this article by causing or allowing a pattern of ownership or development over a geographic area of a source which, except for the pattern of ownership or development, would otherwise require a permit.

9 VAC 5-80-2010. Definitions.

A. As used in this article, all words or terms not defined here shall have the meanings given them in 9 VAC 5 Chapter 10 (9 VAC 5-10-10 et seq.), unless otherwise required by context.

B. For the purpose of this article, 9 VAC 5-50-270 and any related use, the words or terms shall have the meanings given them in subsection C of this section.

C. Terms defined.

"Actual emissions" means the actual rate of emissions of a pollutant from an emissions unit, as determined in accordance with subdivisions a through c of this definition.

a. In general, actual emissions as of a particular date shall equal the average rate, in tons per year, at which the unit actually emitted the pollutant during a two-year period which precedes the particular date and which is representative of normal source operation. The board shall allow the use of a different time period upon a determination that it is more representative of normal source operation. Actual emissions shall be calculated using the unit's actual operating hours, production rates, and types of materials processed, stored, or combusted during the selected time period.

b. The board may presume that the source-specific allowable emissions for the unit are equivalent to the actual emissions of the unit.

c. For any emissions unit which has not begun normal operations on the particular date, actual emissions shall equal the potential to emit of the unit on that date.

"Administrator" means the Administrator of the U.S. Environmental Protection Agency (EPA) or his an authorized representative.

"Allowable emissions" means the emissions rate of a stationary source calculated using the maximum rated capacity of the source (unless the source is subject to federally and state enforceable limits which restrict the operating rate, or hours of operation, or both) and the most stringent of the following:

a. The applicable standards set forth in 40 CFR Parts 60 and 61;

b. Any applicable State Implementation Plan emissions limitation including those with a future compliance date; or

c. The emissions rate limit specified as a federally and state enforceable permit condition, including those with a future compliance date.

"Applicable federal requirement" means all of the following as they apply to emissions units in a source subject to this article (including requirements that have been promulgated or approved by the administrator through rulemaking at the time of permit issuance but have future-effective compliance dates):

a. Any standard or other requirement provided for in an implementation plan established pursuant to § 110 or § 111(d) of the federal Clean Air Act, including any source-specific provisions such as consent agreements or orders.

b. Any limit or condition in any construction permit issued under the new source review program or in any operating permit issued pursuant to the state operating permit program.

c. Any emission standard, alternative emission standard, alternative emission limitation, equivalent emission limitation or other requirement established pursuant to § 112 or § 129 of the federal Clean Air Act as amended in 1990.

d. Any new source performance standard or other requirement established pursuant to § 111 of the federal Clean Air Act, and any emission standard or other requirement established pursuant to § 112 of the federal Clean Air Act before it was amended in 1990.

e. Any limitations and conditions or other requirement in a Virginia regulation or program that has been approved by EPA under subpart E of 40 CFR Part 63 for the purposes of implementing and enforcing § 112 of the federal Clean Air Act.

f. Any requirement concerning accident prevention under § 112(r)(7) of the federal Clean Air Act.

g. Any compliance monitoring requirements established pursuant to either § 504(b) or § 114(a)(3) of the federal Clean Air Act.

h. Any standard or other requirement for consumer and commercial products under § 183(e) of the federal Clean Air Act.

i. Any standard or other requirement for tank vessels under § 183(f) of the federal Clean Air Act.

j. Any standard or other requirement in 40 CFR Part 55 to control air pollution from outer continental shelf sources.

k. Any standard or other requirement of the regulations promulgated to protect stratospheric ozone under Title VI of the federal Clean Air Act, unless the administrator has determined that such requirements need not be contained in a permit issued under this article.

l. With regard to temporary sources subject to 9 VAC 5-80-130, (i) any ambient air quality standard, except applicable state requirements, and (ii) requirements regarding increments or visibility as provided in Article 8 (9 VAC 5-80-1700 et seq.) of this part.

"Begin actual construction" means, in general, initiation of physical on-site construction activities on an emissions unit which are of a permanent nature. Such activities include, but are not limited to, installation of building supports and foundations, laying of underground pipework, and construction of permanent storage structures. With respect to a change in method of operation, this term refers to those on-site activities other than preparatory activities which mark the initiation of the change.

"Building, structure, facility, or installation" means all of the pollutant-emitting activities which belong to the same industrial grouping, are located on one or more contiguous or adjacent properties, and are under the control of the same person (or persons under common control) except the activities of any vessel. Pollutant-emitting activities shall be considered as part of the same industrial grouping if they belong to the same "major group" (i.e., which have the same two-digit code) as described in the "Standard Industrial Classification Manual," as amended by the supplement (see 9 VAC 5-20-21).

"Commence," as applied to construction of a major stationary source or major modification, means that the owner has all necessary preconstruction approvals or permits and either has:

a. Begun, or caused to begin, a continuous program of actual on-site construction of the source, to be completed within a reasonable time; or

b. Entered into binding agreements or contractual obligations, which cannot be canceled or modified without substantial loss to the owner, to undertake a program of actual construction of the source, to be completed within a reasonable time.

"Complete application" means that the application contains all the information necessary for processing the application and the provisions of § 10.1-1321.1 of the Virginia Air Pollution Control Law have been met. Designating an application complete for purposes of permit processing does not preclude the board from requesting or accepting additional information.

"Construction" means any physical change or change in the method of operation (including fabrication, erection, installation, demolition, or modification of an emissions unit) which would result in a change in actual emissions.

"Emissions cap" means any limitation on the rate of emissions of any regulated air pollutant from one or more emissions units established and identified as an emissions cap in any permit issued pursuant to the new source review program or operating permit program.

"Emissions unit" means any part of a stationary source which emits or would have the potential to emit any pollutant subject to regulation under the federal Clean Air Act.

"Enforceable as a practical matter" means that the permit contains emission limitations that are enforceable by the board or the department and meet the following criteria:

a. Are permanent;

b. Contain a legal obligation for the owner to adhere to the terms and conditions;

c. Do not allow a relaxation of a requirement of the Implementation Plan;

d. Are technically accurate and quantifiable;

e. Include averaging times or other provisions that allow at least monthly (or a shorter period if necessary to be consistent with the Implementation Plan) checks on compliance. This may include, but not be limited to, the following: compliance with annual limits in a rolling basis, monthly or shorter limits, and other provisions consistent with 9 VAC 5-80-2050 and other regulations of the board; and

f. Require a level of recordkeeping, reporting and monitoring sufficient to demonstrate compliance.

"Federally enforceable" means all limitations and conditions which are enforceable by the administrator, including those requirements developed pursuant to 40 CFR Parts 60 and 61, requirements within the State Implementation Plan, and any permit requirements established pursuant to 40 CFR 52.21 or this chapter, including operating permits issued under an EPA-approved program that is incorporated into the State Implementation Plan and expressly requires adherence to any permit issued under such program. and citizens under the federal Clean Air Act or that are enforceable under other statutes administered by the administrator. Federally enforceable limitations and conditions include, but are not limited to the following:

a. Emission standards, alternative emission standards, alternative emission limitations, and equivalent emission limitations established pursuant to § 112 of the federal Clean Air Act as amended in 1990.

b. New source performance standards established pursuant to § 111 of the federal Clean Air Act, and emission standards established pursuant to § 112 of the federal Clean Air Act before it was amended in 1990.

c. All terms and conditions in a federal operating permit, including any provisions that limit a source's potential to emit, unless expressly designated as not federally enforceable.

d. Limitations and conditions that are part of an implementation plan established pursuant to § 110 or § 111(d) of the federal Clean Air Act.

e. Limitations and conditions that are part of a federal construction permit issued under 40 CFR 52.21 or any construction permit issued under regulations approved by EPA in accordance with 40 CFR Part 51.

f. Limitations and conditions that are part of an operating permit issued pursuant to a program approved by EPA into a SIP as meeting EPA's minimum criteria for federal enforceability, including adequate notice and opportunity for EPA and public comment prior to issuance of the final permit and practicable enforceability.

g. Limitations and conditions in a Virginia regulation or program that has been approved by EPA under subpart E of 40 CFR Part 63 for the purposes of implementing and enforcing § 112 of the federal Clean Air Act.

h. Individual consent agreements that EPA has legal authority to create.

"Fixed capital cost" means the capital needed to provide all the depreciable components.

"Fugitive emissions" means those emissions which that could not reasonably pass through a stack, chimney, vent, or other functionally equivalent opening [ designed for eliminating emissions from the structure ].

"Lowest achievable emissions rate" means for any source, the more stringent rate of emissions based on the following:

a. The most stringent emissions limitation which is contained in the implementation plan of any state for such class or category of stationary source, unless the owner of the proposed stationary source demonstrates that such limitations are not achievable; or

b. The most stringent emissions limitation which is achieved in practice by such class or category of stationary sources. This limitation, when applied to a modification, means the lowest achievable emissions rate for the new or modified emissions units within the stationary source. In no event shall the application of this term permit a proposed new or modified stationary source to emit any pollutant in excess of the amount allowable under an applicable new source standard of performance.

"Major modification"

a. Means any physical change in or change in the method of operation of a major stationary source that would result in a significant net emissions increase of any qualifying nonattainment pollutant subject to regulation under the federal Clean Air Act.

b. Any net emissions increase that is considered significant for volatile organic compounds shall be considered significant for ozone.

c. A physical change or change in the method of operation shall not include:

(1) Routine maintenance, repair and replacement;

(2) Use of an alternative fuel or raw material by a stationary source which:

(a) The source was capable of accommodating before December 21, 1976, unless such change would be prohibited under any federally and state enforceable permit condition which was established after December 21, 1976, pursuant to 40 CFR 52.21 or this chapter; or

(b) The source is approved to use under any permit issued under 40 CFR 52.21 or this chapter;

(3) An increase in the hours of operation or in the production rate, unless such change is prohibited under any federally and state enforceable permit condition which was established after December 21, 1976, pursuant to 40 CFR 52.21 or this chapter.

"Major new source review (major NSR)" means a program for the preconstruction review of changes that are subject to review as new major stationary sources or major modifications under Article 7 (9 VAC 5-80-1400 et seq.), Article 8 (9 VAC 5-80-1700 et seq.) or Article 9 (9 VAC 5-80-2000 et seq.) of this part.

"Major stationary source"

a. Means:

(1) Any stationary source of air pollutants which emits, or has the potential to emit, (i) 100 tons per year or more of any nonattainment pollutant subject to regulation under the federal Clean Air Act, (ii) 50 tons per year or more of volatile organic compounds or nitrogen oxides in ozone nonattainment areas classified as serious in 9 VAC 5-20-204, or (iii) 25 tons per year or more of volatile organic compounds or nitrogen oxides in ozone nonattainment areas classified as severe in 9 VAC 5-20-204; or

(2) Any physical change that would occur at a stationary source not qualifying under subdivision a (1) of this definition as a major stationary source, if the change would constitute a major stationary source by itself.

b. A major stationary source that is major for volatile organic compounds shall be considered major for ozone.

c. The fugitive emissions of a stationary source shall not be included in determining for any of the purposes of this article whether it is a major stationary source, unless the source belongs to one of the following categories of stationary sources:

(1) Coal cleaning plants (with thermal dryers).

(2) Kraft pulp mills.

(3) Portland cement plants.

(4) Primary zinc smelters.

(5) Iron and steel mills.

(6) Primary aluminum ore reduction plants.

(7) Primary copper smelters.

(8) Municipal incinerators (or combinations of them) capable of charging more than 250 tons of refuse per day.

(9) Hydrofluoric acid plants.

(10) Sulfuric acid plants.

(11) Nitric acid plants.

(12) Petroleum refineries.

(13) Lime plants.

(14) Phosphate rock processing plants.

(15) Coke oven batteries.

(16) Sulfur recovery plants.

(17) Carbon black plants (furnace process).

(18) Primary lead smelters.

(19) Fuel conversion plants.

(20) Sintering plants.

(21) Secondary metal production plants.

(22) Chemical process plants.

(23) Fossil-fuel boilers (or combination of them) totaling more than 250 million British thermal units per hour heat input.

(24) Petroleum storage and transfer units with a total storage capacity exceeding 300,000 barrels.

(25) Taconite ore processing plants.

(26) Glass fiber manufacturing plants.

(27) Charcoal production plants.

(28) Fossil fuel steam electric plants of more than 250 million British thermal units per hour heat input.

(29) Any other stationary source category which, as of August 7, 1980, is being regulated under § 111 or § 112 of the federal Clean Air Act.

"Minor new source review (minor NSR)" means a program for the preconstruction review of changes that are subject to review as new or modified sources and that do not qualify as new major stationary sources or major modifications under Article 7 (9 VAC 5-80-1400 et seq.), Article 8 (9 VAC 5-80-1700 et seq.) or Article 9 (9 VAC 5-80-2000 et seq.) of this part.

"Necessary preconstruction approvals or permits" means those permits or approvals required under federal air quality control laws and regulations, and those air quality control laws and regulations which are part of the applicable State Implementation Plan.

"Net emissions increase"

a. Means the amount by which the sum of the following exceeds zero:

(1) Any increase in actual emissions from a particular physical change or change in the method of operation at a stationary source; and

(2) Any other increases and decreases in actual emissions at the source that are contemporaneous with the particular change and are otherwise creditable.

b. An increase or decrease in actual emissions is contemporaneous with the increase from the particular change only if it occurs before the date that the increase from the particular change occurs. For sources located in ozone nonattainment areas classified as serious or severe in 9 VAC 5-20-204, an increase or decrease in actual emissions of volatile organic compounds or nitrogen oxides is contemporaneous with the increase from the particular change only if it occurs during a period of five consecutive calendar years which includes the calendar year in which the increase from the particular change occurs.

c. An increase or decrease in actual emissions is creditable only if:

(1) It occurs between the date five years before construction on the change specified in subdivision a (1) of this definition commences and the date that the increase specified in subdivision a (1) of this definition occurs; and

(2) The board has not relied on it in issuing a permit for the source pursuant to this chapter which permit is in effect when the increase in actual emissions from the particular change occurs.

d. An increase in actual emissions is creditable only to the extent that the new level of actual emissions exceeds the old level.

e. A decrease in actual emissions is creditable only to the extent that:

(1) The old level of actual emissions or the old level of allowable emissions, whichever is lower, exceeds the new level of actual emissions;

(2) It is federally and state enforceable at and after the time that actual construction on the particular change begins;

(3) The board has not relied on it in issuing any permit pursuant to this chapter or the board has not relied on it in demonstrating attainment or reasonable further progress in the State Implementation Plan; and

(4) It has approximately the same qualitative significance for public health and welfare as that attributed to the increase from the particular change.

f. An increase that results from a physical change at a source occurs when the emissions unit on which construction occurred becomes operational and begins to emit a particular pollutant. Any replacement unit that requires shakedown becomes operational only after a reasonable shakedown period, not to exceed 180 days.

"New source review program" means a program for the preconstruction review and permitting of new stationary sources or expansions to existing ones in accordance with regulations promulgated to implement the requirements of §§ 110 (a)(2)(C), 165 (relating to permits in prevention of significant deterioration areas), 173 (relating to permits in nonattainment areas), and 112 (relating to permits for hazardous air pollutants) of the federal Clean Air Act.

"Nonattainment pollutant" means, within [ an a ] nonattainment area, the pollutant for which such area is designated nonattainment. For ozone nonattainment areas, the nonattainment pollutants shall be volatile organic compounds (including hydrocarbons) and nitrogen oxides.

"Potential to emit" means the maximum capacity of a stationary source to emit a pollutant under its physical and operational design. Any physical or operational limitation on the capacity of the source to emit a pollutant, including air pollution control equipment, and restrictions on hours of operation or on the type or amount of material combusted, stored, or processed, shall be treated as part of its design only if the limitation or the effect it would have on emissions is federally and state enforceable. Secondary emissions do not count in determining the potential to emit of a stationary source.

"Public comment period" means a time during which the public shall have the opportunity to comment on the new or modified source permit application information (exclusive of confidential information), the preliminary review and analysis of the effect of the source upon the ambient air quality, and the preliminary decision of the board regarding the permit application.

"Qualifying pollutant" means, with regard to a major stationary source, any pollutant emitted in such quantities or at such rate as to qualify the source as a major stationary source.

"Reasonable further progress" means the annual incremental reductions in emissions of a given air pollutant (including substantial reductions in the early years following approval or promulgation of a state an implementation plan and regular reductions thereafter) which are sufficient in the judgment of the board to provide for attainment of the applicable ambient air quality standard within a specified nonattainment area by the attainment date prescribed in the State Implementation Plan for such area.

"Reconstruction" means when the fixed capital cost of the new components exceeds 50% of the fixed capital cost of a comparable entirely new stationary source. Any final decision as to whether reconstruction has occurred shall be made in accordance with the provisions of subdivisions a through c of this definition. A reconstructed stationary source will be treated as a new stationary source for purposes of this article.

a. The fixed capital cost of the replacements in comparison to the fixed capital cost that would be required to construct a comparable entirely new facility.

b. The estimated life of the facility after the replacements compared to the life of a comparable entirely new facility.

c. The extent to which the components being replaced cause or contribute to the emissions from the facility.

"Regulated air pollutant" means any of the following:

a. Nitrogen oxides or any volatile organic compound;

b. Any pollutant for which an ambient air quality standard has been promulgated;

c. Any pollutant subject to any standard promulgated under § 111 of the federal Clean Air Act;

d. Any pollutant subject to a standard promulgated under or other requirements established under § 112 of the federal Clean Air Act concerning hazardous air pollutants and any pollutant regulated under 40 CFR Part 63; or

e. Any pollutant subject to a regulation adopted by the board.

"Secondary emissions" means emissions which would occur as a result of the construction or operation of a major stationary source or major modification, but do not come from the major stationary source or major modification itself. For the purpose of this article, secondary emissions must be specific, well defined, quantifiable, and impact affect the same general area as the stationary source or modification which causes the secondary emissions. Secondary emissions include emissions from any off-site support facility which would not be constructed or increase its emissions except as a result of the construction or operation of the major stationary source or major modification. Secondary emissions do not include any emissions which come directly from a mobile source, such as emissions from the tailpipe of a motor vehicle, from a train, or from a vessel.

"Significant" means, in reference to a net emissions increase or the potential of a source to emit any of the following pollutants, a rate of emissions that would equal or exceed any of the following rates:

a. Ozone nonattainment areas classified as serious or severe in 9 VAC 5-20-204.

Pollutant	Emissions Rate

Carbon Monoxide	100 tons per year (tpy)

Nitrogen Oxides	25 tpy

Sulfur Dioxide	40 tpy

Particulate Matter	25 tpy

Ozone	25 tpy of volatile organic compounds

Lead	0.6 tpy

b. Other nonattainment areas.

Pollutant	Emissions Rate

Carbon Monoxide	100 tons per year (tpy)

Nitrogen Oxides	40 tpy

Sulfur Dioxide	40 tpy

Particulate Matter	25 tpy

Ozone	40 tpy of volatile organic compounds

Lead	0.6 tpy

"State enforceable" means all limitations and conditions that are enforceable as a practical matter, including any regulation of the board, those requirements developed pursuant to 9 VAC 5-170-160, requirements within any applicable order or variance, and any permit requirements established pursuant to this chapter.

"State operating permit program" means a program for issuing limitations and conditions for stationary sources in accordance with Article 5 (9 VAC 5-80-800 et seq.) of this part, promulgated to meet EPA's minimum criteria for federal enforceability, including adequate notice and opportunity for EPA and public comment prior to issuance of the final permit and practicable enforceability.

"Stationary source" means any building, structure, facility, or installation which emits or may emit any air pollutant subject to regulation under the federal Clean Air Act.

"Synthetic minor" means a stationary source whose potential to emit is constrained by state-enforceable and federally enforceable limits, so as to place that stationary source below the threshold at which it would be subject to permit or other requirements governing major stationary sources in regulations of the board or in the federal Clean Air Act.

9 VAC 5-80-2020. General.

A. No owner or other person shall begin actual construction, reconstruction or modification of any major stationary source or major modification without first obtaining from the board a permit to construct and operate such source.

B. No owner or other person shall relocate any emissions unit subject to the provisions of 9 VAC 5-20-160 from one stationary source to another without first obtaining from the board a permit to relocate the unit.

C. The board may combine the requirements of and the permits for emissions units within a stationary source subject to 9 VAC 5-80-10, Article 8 (9 VAC 5-80-1700 et seq.) of this part, and this article the new source review program into one permit. Likewise the board may require that applications for permits for emissions units within a stationary source required by 9 VAC 5-80-10, Article 8 of this part, and this article any provision of the new source review program be combined into one application.

D. The board may incorporate the terms and conditions of a state operating permit into a permit issued pursuant to this article. The permit issued pursuant to this article may supersede the state operating permit provided the public participation provisions of the state operating permit program are followed.

E. All terms and conditions of any permit issued under this article shall be federally enforceable except those that are designated state-only enforceable under subdivision 1 of this subsection. Any term or condition that is not federally enforceable shall be designated as state-only enforceable as provided in subdivision 2 of this subsection.

1. A term or condition of any permit issued under this article shall not be federally enforceable if [ (i) ] it is derived from or is designed to implement Article 2 (9 VAC 5-40-130 et seq.) or Article 3 (9 VAC 5-40-160 et seq.) of 9 VAC 5 Chapter 40 or Article 2 (9 VAC 5-50-130 et seq.) or Article 3 (9 VAC 5-50-160 et seq.) of 9 VAC 5 Chapter 50 [ or (ii) it is designated in the proposed permit as provided in subdivision 2 of this subsection and public review of the designation takes place under 9 VAC 5-80-2070 ].

2. Any term or condition of any permit issued under this article that is not federally enforceable shall be marked in the permit as state-only enforceable and shall only be enforceable by the board. [ Failure to mark a term or condition as state-only enforceable shall not render it federally enforceable. ] Incorrectly designating a term or condition as state-only enforceable shall not provide a shield from federal enforcement of a term or condition that is legally federally enforceable.

F. Nothing in the regulations of the board shall be construed to prevent the board from granting permits for programs of construction or modification in planned incremental phases. In such cases, all net emissions increases from all emissions units covered by the program shall be added together for determining the applicability of this article.

9 VAC 5-80-2030. [ No change from proposed. ]

9 VAC 5-80-2040. [ No change from proposed. ]

9 VAC 5-80-2050. Standards/conditions Standards and conditions for granting permits.

A. No permit will be granted pursuant to this article unless it is shown to the satisfaction of the board that [ the source will ] be designed, built and equipped to operate without causing a violation of the applicable provisions of these regulations and that [ comply with ] the following standards [ and conditions have been met ]:

1. The source shall be designed, built and equipped to comply with standards of performance prescribed under 9 VAC 5 Chapter 50 (9 VAC 5-50-10 et seq.) and with emission standards prescribed under 9 VAC 5 Chapter 60 (9 VAC 5-60-10 et seq.).

2. The source shall be designed, built and equipped to operate without preventing or interfering with the attainment or maintenance of any applicable ambient air quality standard and without causing or exacerbating a violation of any the applicable ambient air quality standard provisions of regulations of the board or the applicable control strategy portion of the implementation plan.

3. The board determines that the following occurs:

a. By the time the source is to commence operation, sufficient offsetting emissions reductions shall have been obtained in accordance with 9 VAC 5-80-2120 such that total allowable emissions of qualifying nonattainment pollutants from existing sources in the region, from new or modified sources which are not major emitting facilities, and from the proposed source will be sufficiently less than total emissions from existing sources, as determined in accordance with the requirements of this article, prior to the application for such permit to construct or modify so as to represent (when considered together with any applicable control measures in the State Implementation Plan) reasonable further progress; or

b. In the case of a new or modified major stationary source which is located in a zone, within the nonattainment area, identified by the administrator, in consultation with the Secretary of Housing and Urban Development, as a zone to which economic development should be targeted, that emissions of such pollutant resulting from the proposed new or modified major stationary source shall not cause or contribute to emissions levels which exceed the allowance permitted for such pollutant for such area from new or modified major stationary sources in the State Implementation Plan [ . ; and

c. ] Any emission reductions required as a precondition of the issuance of a permit under subdivision 3 a or 3 b of this section subsection shall be state and federally enforceable before such permit may be issued.

4. The applicant shall demonstrate that all major stationary sources owned or operated by such applicant (or by any entity controlling, controlled by, or under common control with such applicant) in the Commonwealth are subject to emission limitations and are in compliance, or on a schedule for compliance, with all applicable emission limitations and standards under these regulations.

5. The administrator has not determined that the applicable implementation plan is not being adequately implemented for the nonattainment area in which the proposed source is to be constructed or modified in accordance with the requirements of this article.

6. The applicant shall demonstrate, through an analysis of alternative sites, sizes, production processes, and environmental control techniques for such proposed source, that benefits of the proposed source significantly outweigh the environmental and social costs imposed as a result of its location, construction, or modification.

B. Permits may be granted to stationary sources or emissions units that contain emission caps provided the limits or caps are made enforceable as a practical matter using the elements set forth in subsection D of this section.

C. Permits granted pursuant to this article may contain emissions standards as necessary to implement the provisions of this article and 9 VAC 5-50-270. The following criteria shall be met in establishing emission standards to the extent necessary to assure that emissions levels are enforceable as a practical matter:

1. Standards may include the level, quantity, rate, or concentration or any combination of them for each affected pollutant.

2. In no case shall a standard result in emissions that would exceed the emissions rate based on the potential to emit of the emissions unit.

3. The standard may prescribe, as an alternative to or a supplement to an emission limitation, an equipment, work practice, fuels specification, process materials, maintenance, or operational standard, or any combination of them.

D. Permits issued under this article shall contain, but not be limited to, any of the following elements as necessary to ensure that the permits are enforceable as a practical matter:

1. Emission standards.

2. Conditions necessary to enforce emission standards. Conditions may include, but not be limited to, any of the following:

a. Limit on fuel sulfur content.

b. Limit on production rates with time frames as appropriate to support the emission standards.

c. Limit on raw material usage rate.

d. Limits on the minimum required capture, removal and overall control efficiency for any air pollution control equipment.

3. Specifications for permitted equipment, identified as thoroughly as possible. The identification shall include, but not be limited to, type, rated capacity, and size. Specifications included in the permit under this subdivision are for informational purposes only and do not form enforceable terms or conditions of the permit unless the specifications are needed to form the basis for one or more of the other terms or conditions in the permit.

4. Specifications for air pollution control equipment installed or to be installed. Specifications included in the permit under this subdivision are for informational purposes only and do not form enforceable terms or conditions of the permit unless the specifications are needed to form the basis for one or more of the other terms or conditions in the permit.

5. Specifications for air pollution control equipment operating parameters and the circumstances under which such equipment shall be operated, where necessary to ensure that the required overall control efficiency is achieved. The operating parameters may include, but not be limited to, any of the following:

a. Pressure indicators and required pressure drop.

b. Temperature indicators and required temperature.

c. pH indicators and required pH.

d. Flow indicators and required flow.

6. Requirements for proper operation and maintenance of any pollution control equipment, and appropriate spare parts inventory.

7. Stack test requirements.

8. Reporting or recordkeeping requirements, or both.

9. Continuous emission or air quality monitoring requirements, or both.

10. Other requirements as may be necessary to ensure compliance with the applicable regulations.

9 VAC 5-80-2060 through 9 VAC 5-80-2110. [ No change from proposed. ]

9 VAC 5-80-2120. Offsets.

A. Owners shall comply with the offset requirements of this article by obtaining emission reductions from the same source or other sources in the same nonattainment area, except that for ozone precursor pollutants the board may allow the owner to obtain such emission reductions in another nonattainment area if (i) the other area has an equal or higher nonattainment classification than the area in which the source is located and (ii) emissions from such other area contribute to a violation of the ambient air quality standard in the nonattainment area in which the source is located. By the time a new or modified source begins operation, such emission reductions shall (i) be in effect, (ii) be state and federally enforceable and (iii) assure that the total tonnage of increased emissions of the air pollutant from the new or modified source shall be offset by an equal or greater reduction, as applicable, in the actual emissions of such air pollutant from the same or other sources in the nonattainment area.

B. The (i) ratio of total emission reductions of volatile organic compounds to total increased emissions of volatile organic compounds or (ii) the ratio of total emission reductions of nitrogen oxides to total increased emissions of nitrogen oxides in ozone nonattainment areas designated in 9 VAC 5-20-204 shall be at least the following:

1. Ozone Nonattainment areas classified as marginal --1.1 to one.

2. Ozone Nonattainment areas classified as moderate --1.15 to one.

3. Ozone Nonattainment areas classified as serious --1.2 to one.

4. Ozone Nonattainment areas classified as severe --1.3 to one.

5. Nonattainment areas [ not classified with any other classification or no classification ] --1 to one.

The ratio of total emissions reductions of the nonattainment pollutant to total increased emissions of the nonattainment pollutant in nonattainment areas (other than ozone nonattainment areas) designated in 9 VAC 5-20-204 shall be at least 1 to one.

C. Emission reductions otherwise required by these regulations shall not be creditable as emissions reductions for purposes of any such offset requirement. Incidental emission reductions which are not otherwise required by these regulations shall be creditable as emission reductions for such purposes if such emission reductions meet the requirements of subsection A of this section.

D. The board shall allow an owner to offset by alternative or innovative means emission increases from rocket engine and motor firing, and cleaning related to such firing, at an existing or modified major source that tests rocket engines or motors under the following conditions:

1. Any modification proposed is solely for the purpose of expanding the testing of rocket engines or motors at an existing source that is permitted to test such engines on November 15, 1990.

2. The source demonstrates to the satisfaction of the board that it has used all reasonable means to obtain and utilize offsets, as determined on an annual basis, for the emissions increases beyond allowable levels, that all available offsets are being used, and that sufficient offsets are not available to the source.

3. The source has obtained a written finding from the U.S. Department of Defense, U.S. Department of Transportation, National Aeronautics and Space Administration or other appropriate federal agency, that the testing of rocket motors or engines at the facility is required for a program essential to the national security.

4. The owner will comply with an alternative measure, imposed by the board, designed to offset any emission increases beyond permitted levels not directly offset by the source. In lieu of imposing any alternative offset measures, the board may impose an emissions fee to be paid to the board which shall be an amount no greater than 1.5 times the average cost of stationary source control measures adopted in that nonattainment area during the previous three years. The board shall utilize the fees in a manner that maximizes the emissions reductions in that nonattainment area.

E. For sources subject to the provisions of this article, the baseline for determining credit for emissions reduction is the emissions limit under the applicable State Implementation Plan in effect at the time the application to construct is filed, except that the offset baseline shall be the actual emissions of the source from which offset credit is obtained where:

1. The demonstration of reasonable further progress and attainment of ambient air quality standards is based upon the actual emissions of sources located within a designated nonattainment area; or

2. The applicable State Implementation Plan does not contain an emissions limitation for that source or source category.

F. Where the emissions limit under the applicable State Implementation Plan allows greater emissions than the potential to emit of the source, emissions offset credit will be allowed only for control below this potential.

G. For an existing fuel combustion source, credit shall be based on the allowable emissions under the applicable State Implementation Plan for the type of fuel being burned at the time the application to construct is filed. If the owner of the existing source commits to switch to a cleaner fuel at some future date, emissions offset credit based on the allowable (or actual) emissions for the fuels involved is not acceptable, unless the permit is conditioned to require the use of a specified alternative control measure which would achieve the same degree of emissions reduction should the source switch back to a dirtier fuel at some later date. The board will ensure that adequate long-term supplies of the new fuel are available before granting emissions offset credit for fuel switches.

H. Emissions reductions achieved by shutting down an existing source or curtailing production or operating hours below baseline levels may be generally credited if such reductions are permanent, quantifiable, and federally and state enforceable. In addition, the shutdown or curtailment is creditable only if it occurred on or after January 1, 1991.

I. No emissions credit may be allowed for replacing one hydrocarbon volatile organic compound with another of lesser reactivity, except for those compounds listed in Table 1 of EPA's "Recommended Policy on Control of Volatile Organic Compounds" (42 FR 35314, July 8, 1977).

J. Where these regulations do this article does not adequately address a particular issue, the provisions of Appendix S to 40 CFR Part 51 shall be followed to the extent that they do not conflict with this section article.

K. Credit for an emissions reduction can be claimed to the extent that the board has not relied on it in issuing any permit under this chapter or has not relied on it in demonstrating attainment or reasonable further progress.

9 VAC 5-80-2150 through 9 VAC 5-80-2200. [ No change from proposed. ]

9 VAC 5-80-2210. Administrative permit amendments.

A. Administrative permit amendments shall be required for and limited to the following:

1. Correction of typographical or any other error, defect or irregularity that does not substantially affect the permit.

2. Identification of a change in the name, address, or phone number of any person identified in the permit, or of a similar minor administrative change at the source.

3. Change in ownership or operational control of a source where the board determines that no other change in the permit is necessary, provided that a written agreement containing a specific date for transfer of permit responsibility, coverage, and liability between the current and new permittee has been submitted to the board and the requirements of [ 9 VAC 5-80-2180 9 VAC 5-80-2170 ] have been fulfilled.

4. The combining of permits under the new source review program as provided in 9 VAC 5-80-2020 C.

B. The administrative permit amendment procedures are as follows:

1. The board will normally take final action on a request for an administrative permit amendment no more than 60 days from receipt of the request.

2. The board shall incorporate the changes without providing notice to the public under 9 VAC 5-80-2070. However, any such permit revisions shall be designated in the permit amendment as having been made pursuant to this section.

3. The owner may implement the changes addressed in the request for an administrative amendment immediately upon submittal of the request.

9 VAC 5-80-2220, 9 VAC 5-80-2230 and 9 VAC 5-80-2240. [ No change from proposed. ]

VA.R. Doc. No. R01-14; Filed March 5, 2002, 2:34 p.m.