STATE WATER CONTROL BOARD

REGISTRAR'S NOTICE: The following regulation (9 VAC 25-196) filed by the State Water Control Board is exempt from the Administrative Process Act in accordance with § 2.2-4006 A 9 of the Code of Virginia, which exempts general permits issued by the State Water Control Board pursuant to the State Water Control Law (§ 62.1-44.2 et seq.), Chapter 24 (§ 62.1-242 et seq.) of Title 62.1 and Chapter 25 (§ 62.1-254 et seq.) of Title 62.1 of the Code of Virginia if the board (i) provides a Notice of Intended Regulatory Action in conformance with the provisions of § 2.2-4007 B, (ii) following the passage of 30 days from the publication of the Notice of Intended Regulatory Action forms a technical advisory committee composed of relevant stakeholders, including potentially affected citizens groups, to assist in the development of the general permit, (iii) provides notice and receives oral and written comment as provided in § 2.2-4007 F, and (iv) conducts at least one public hearing on the proposed general permit.

Title of Regulation: 9 VAC 25-196. General Virginia Pollutant Discharge Elimination System (VPDES) Permit for Cooling Water Discharges (amending 9 VAC 25-196-40 through 9 VAC 25-196-70; repealing 9 VAC 25-196-80).

Statutory Authority: § 62.1-44.15 of the Code of Virginia.

Public Hearing Date: September 27, 2002 - 10 a.m.

Public comments may be submitted until 4 p.m. on October 31, 2002.

(See Calendar of Events section

for additional information)

Agency Contact: Jon van Soestbergen, P.E., Environmental Manager II, Department of Environmental Quality, P.O. Box 10009, Richmond, VA 23240, telephone (804) 698-4117, FAX (804) 698-4032 or e-mail jvsoest@deq.state.va.us.

Summary:

This proposed regulatory action sets forth guidelines for the permitting of the point source discharge of cooling water to surface waters. The State Water Control Board proposes to reissue the general permit subject to certain conditions and has prepared a draft permit. The proposed general permit consists of limitations and monitoring requirements on point source discharges of cooling water to surface water for the following parameters; flow, 50,000 gallons per day maximum; temperature, maximum 32°C for discharges to nontidal coastal and piedmont waters, or 31°C for discharges to upper piedmont waters; pH, 6.0 minimum, 9.0 maximum; total residual chlorine, nondetectable. Monitoring only is also required for Ammonia, Hardness, Total Dissolved Copper, Total Dissolved Zinc, Total Dissolved Silver, Total Phosphorous. Monitoring frequency is once every three months. The regulation also sets forth the minimum information requirements for all requests for coverage under the general permit.

9 VAC 25-196-40. Effective date of the permit.

This general permit will become effective on March 1, 1998 2003. This general permit will expire five years from the effective date. This general permit is effective as to any covered owner upon compliance with all the provisions of 9 VAC 25-196-50 and the receipt of this general permit.

9 VAC 25-196-50. Authorization to discharge.

A. Any owner governed by this general permit is hereby authorized to discharge to surface waters of the Commonwealth of Virginia provided that the owner files and receives acceptance by the board of the registration statement of 9 VAC 25-196-60, files the required permit fee, complies with the effluent limitations and other requirements of 9 VAC 25-196-70, and provided that:

1. The owner shall not have has not been required to obtain an individual permit as may be required in the VPDES Permit Regulation according to 9 VAC 25-31-170 B 3.

2. The owner shall not discharge to Class V stockable trout waters, Class VI natural trout waters, or any state waters specifically named in other board regulations or policies which prohibit such discharges. Chlorine or any other halogen compounds shall not be used for disinfection or other treatment purposes, including biocide applications, for any discharges to waters containing endangered or threatened species as identified in 9 VAC 25-260-110 C of the Water Quality Standards.

3. The owner shall neither use tributyltin and any chemical additives containing tributyltin, nor use any hexavalent chromium-based water treatment chemicals in the cooling water systems.

4. The owner shall not use groundwater remediation wells as the source of cooling water.

B. Receipt of this general permit does not relieve any owner of the responsibility to comply with any other federal, state or local statute, ordinance or regulation.

9 VAC 25-196-60. Registration statement.

The owner shall file a complete general VPDES permit registration statement for cooling water discharges. Any owner proposing a new discharge shall file a complete registration statement at least 30 days prior to the date planned for commencing operation of the new discharge. Any owner of an existing discharge covered by an individual VPDES permit who is proposing to be covered by this general permit shall file the registration statement at least 180 days prior to the expiration date of the individual VPDES permit. Any owner of an existing discharge not currently covered by a VPDES permit who is proposing to be covered by this general permit shall file a complete registration statement. The required registration statement shall contain the following information:

VIRGINIA POLLUTANT DISCHARGE ELIMINATION SYSTEM

GENERAL PERMIT REGISTRATION STATEMENT FOR COOLING WATER DISCHARGES

1. APPLICANT INFORMATION

A. Name of Facility: _______________________________

B. Facility Owner: ________________________________

C. Owner's Mailing Address

a. Street or P.O. Box ____________________________

b. City or Town ______________ c. State __ d. Zip Code _______

e. Phone Number _____________________

D. Facility Location: _______________________________

Street No., Route No., or Other Identifier

_____________________________________________

County

E. Is the operator of the facility also the owner?

Yes ___ No ___ If No, complete F. & G.

F. Name of Operator: _______________________________

G. Operator's Mailing Address

a. Street or P.O. Box ____________________________

b. City or Town _____________ c. State __ d. Zip Code _______

e. Phone Number ____________________

2. FACILITY INFORMATION

A. Does this facility currently have a VPDES permit?

Yes ___ No ___ If yes, give permit number. ____________________

B. List any point source discharges that are not composed entirely of cooling water ____________________________

C. List type and size (tons) of cooling equipment or noncontact cooling water process:

Type Size (tons)

_____________________________________________

_____________________________________________

D. Complete the following if any chemical and/or nonchemical treatment is employed in each of the cooling water systems:

a. Describe the chemical and/or nonchemical treatment to be employed and its purpose;

_____________________________________________

If chemical additives other than chlorine are used, complete b, c, d and e below.

b. Provide name and manufacturer of each additive used;

_____________________________________________

c. Provide list of active ingredients and percent composition;

_____________________________________________

d. Give the proposed schedule and quantity of chemical usage, and estimate the concentration in the discharge; and

_____________________________________________

e. Attach available aquatic toxicity information for each additive proposed for use.

E. Describe any type of treatment or retention being provided to the wastewater before discharge (i.e., retention ponds, settling ponds, etc.):

_____________________________________________

3. FACILITY SCHEMATIC DRAWING

Attach a schematic drawing of the cooling water equipment which shows the source of the cooling water, its flow through the facility, and each cooling water discharge point.

4. MAP

For cooling water systems with a direct discharge to surface waters, attach a topographic map extending to at least one mile beyond property boundary. The map must show the outline of the facility, and the location of each of its existing and proposed intake and discharge points. Include all springs, rivers and other surface water bodies.

5. DISCHARGE INFORMATION

A. List all cooling water discharges by a number that is the same as on the map required in Question 4, if applicable. Identify the source of cooling water. Estimate the maximum daily discharge flow in gallons per day (gpd). Give the name of the waterbody receiving direct discharge or discharge through the municipal separate storm sewer system.

Outfall No. Source Max. Daily Flow (gpd) Receiving Stream

_____________________________________________

_____________________________________________

_____________________________________________

B. Identify the duration and frequency of the discharge for each separate discharge point:

a. Continuous: _________________________________

b. Intermittent: (please describe) ___________________

c. Seasonal: ___________________________________

C. Give the name of the owner of the municipal separate storm sewer system that receives the discharge (if applicable):

_____________________________________________

6. CERTIFICATION

I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to assure that qualified personnel properly gather and evaluate the information submitted. Based on my inquiry of the person or persons who manage the system or those persons directly responsible for gathering the information, the information submitted is to the best of my knowledge and belief true, accurate, and complete. I am aware that there are significant penalties for submitting false information including the possibility of fine and imprisonment for knowing violations.

Signature ________________________ Date: ___________

Name of person(s) signing above: _____________________

(printed or typed)

Title(s): _________________________________________________

REQUIRED ATTACHMENTS

Aquatic Toxicity Information For Chemical Additives (if applicable)

Facility Schematic Drawing

Topographic Map (if applicable)

For Department Use Only:

Accepted/Not Accepted by: _______________________ Date: _______________

Basin _______ Stream Class _______ Section ________________________________

Special Standards ______________________________

1. Facility name and address, owner name and mailing address and telephone number;

2. Operator name, mailing address, and telephone number if different from owner;

3. Does the facility currently have a VPDES permit? Permit Number if yes;

4. Listing of point source discharges that are not composed entirely of cooling water;

5. Listing of type and size (tons) of cooling equipment or noncontact cooling water processes;

6. The following information if any chemical or nonchemical treatment, or both, is employed in each of the cooling water systems:

a. Description of the chemical or nonchemical treatment, or both, to be employed and its purpose;

For chemical additives other than chlorine, b, c, and d below;

b. Name and manufacturer of each additive used;

c. List of active ingredients and percent composition;

d. Proposed schedule and quantity of chemical usage, and estimate of the concentration in the discharge;

e. Available aquatic toxicity information for each proposed additive used; and

f. Any other information such as product or constituent degradation, fate, transport, synergies, bioavailability, etc., that will aid the board with the toxicity evaluation of the discharge.

7. Description of any type of treatment or retention being provided to the wastewater before discharge (i.e. retention ponds, settling ponds, etc.)

8. A schematic drawing of the cooling water equipment that shows the source of the cooling water, its flow through the facility, and each cooling water discharge point.

9. For cooling waters with a direct discharge to surface waters, a topographic map extending to at least one mile beyond the property boundary. The map must show the outline of the facility and the location of each of its existing and proposed intake and discharge points, and must include all springs, rivers and other surface water bodies.

10. The following discharge information:

a. A listing of all cooling water discharges by a unique number;

b. The source of cooling water for each discharge;

c. An estimate of the maximum daily flow in gallons per day for each discharge;

d. The name of the waterbody receiving direct discharge or discharge through the municipal separate storm sewer system;

e. The duration and frequency of the discharge for each separate discharge point; continuous, intermittent, or seasonal;

f. The name and contact information of the owner of the municipal separate storm sewer system that receives the discharge, if applicable.

11. The following certification:

I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to assure that qualified personnel properly gather and evaluate the information submitted. Based on my inquiry of the person or persons who manage the system or those persons directly responsible for gathering the information, the information submitted is to the best of my knowledge and belief true, accurate, and complete. I am aware that there are significant penalties for submitting false information including the possibility of fine and imprisonment for knowing violations.

The registration statement shall be signed in accordance with 9 VAC 25-31-110.

9 VAC 25-196-70. General permit.

Any owner whose registration statement is accepted by the board will receive the following permit and shall comply with the requirements therein and be subject to all requirements of the VPDES Permit Regulation 9 VAC 25-31.

General Permit No: VAG25

Effective Date:

Expiration Date:

GENERAL PERMIT FOR COOLING WATER DISCHARGES

AUTHORIZATION TO DISCHARGE UNDER THE VIRGINIA POLLUTANT DISCHARGE ELIMINATION SYSTEM AND THE VIRGINIA STATE WATER CONTROL LAW

In compliance with the provisions of the Clean Water Act, as amended, and pursuant to the State Water Control Law and regulations adopted pursuant thereto, owners of cooling water discharges are authorized to discharge to surface waters within the boundaries of the Commonwealth of Virginia, except Class V stockable trout waters, Class VI natural trout waters, and those specifically named in board regulations or policies which prohibit such discharges. Chlorine or any other halogen compounds shall not be used for disinfection or other treatment purposes, including biocide applications, for any discharges to waters containing endangered or threatened species as identified in 9 VAC 25-260-110 C of the Water Quality Standards.

The authorized discharge shall be in accordance with this cover page, Part I--Effluent Limitations and Monitoring Requirements, and Part II--Conditions Applicable to all VPDES Permits, as set forth herein.

PART I

A. EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS.

During the period beginning on the permit's effective date and lasting until the permit's expiration date, the permittee is authorized to discharge cooling water. Samples taken in compliance with the monitoring requirements specified below shall be taken at the following location(s): outfall(s) serial number: _______________.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS | DISCHARGE LIMITATIONS | MONITORING REQUIREMENTS |
| --- | --- | --- |
|  | Maximum | Minimum | Frequency | Sample Type |
| Flow (MGD) | 0.05 | NA | 1/3 Months | Estimate |
| Temperature (°C) | (1) | NA | 1/3 Months | Immersion Stabilization |
| pH (SU) | 9(2) | 6(2) | 1/3 Months | Grab |
| Ammonia-N(3) (mg/l) | NL | NA | 1/3 Months | Grab |
| Total Residual Chlorine(3) (mg/l) | Nondetectable | NA | 1/3 Months | Grab |
| Hardness (mg/l CaCO3) | NL | NA | 1/3 Months | Grab |
| Total Dissolved Copper(4) (μg/l) | NL | NA | 1/3 Months | Grab |
| Total Dissolved Zinc(4) (μg/l) | NL | NA | 1/3 Months | Grab |
| Total Dissolved Silver(4), (5) (μg/l) | NL | NA | 1/3 Months | Grab |
| Total Phosphorus(6) (mg/l) | NL | NA | 1/3 Months | Grab |

NL = No limitation, monitoring required

NA = Not applicable

(1) The effluent temperature shall not exceed a maximum 32°C for discharges to nontidal coastal and piedmont waters, or 31°C for mountain and upper piedmont waters. No maximum temperature limit, only monitoring, applies to discharges to estuarine waters.

The effluent shall not cause an increase in temperature of the receiving stream of more than 3° C above the natural water temperature. The effluent shall not cause the temperature in the receiving stream to change more than 2°C per hour. Natural temperature is defined as that temperature of a body of water (measured as the arithmetic average over one hour) due solely to natural conditions without the influence of any point-source discharge.

(2) Where the Water Quality Standards (9 VAC 25-260-5 et seq.) establish alternate standards for pH in the waters receiving the discharge, those standards shall be the maximum and minimum effluent limitations.

(3) Chlorine limitation of nondetectable (<0.1 mg/l) and chlorine and ammonia monitoring only apply to outfalls directly discharging to surface waters and are required where the source or of cooling water is chlorinated or contains chloramines.

(4) A specific analysis is not specified for these materials. An appropriate analysis shall be selected from the following list of EPA methods to achieve a quantification level that is less than the target level for the material under consideration:

| Material | EPA Method | Target Level (μg/l) |
| --- | --- | --- |
| Copper | 220.1, 220.2, 200.7, 200.8, 200.9, 1638, 1640 | 9.2 |
| Zinc | 289.1, 289.2, 200.7, 200.8, 1638, 1639 | 65.0 |
| Silver | 272.1, 272.2, 200.7, 200.8, 200.9, 1638 | 1.2 |

Quality control/assurance information shall be submitted to document that the required quantification level has been attained.

(5) Silver monitoring is only required where Cu/Ag anode is used.

(6) Phosphorous monitoring is only required where additive containing phosphorous is used.

| Material | EPA Method | Target Level (μg/l) |
| --- | --- | --- |
| Copper | 220.1, 220.2, 200.7, 200.8, 200.9, 1638, 1640 | 9.2 |
| Zinc | 289.1, 289.2, 200.7, 200.8, 1638, 1639 | 65.0 |
| Silver | 272.1, 272.2, 200.7, 200.8, 200.9, 1638 | 1.2 |

Quality control/assurance information shall be submitted to document that the required quantification level has been attained.

B. Special conditions.

1. There shall be no discharge of floating solids or visible foam in other than trace amounts.

2. No discharges other than cooling water, as defined, are permitted under this general permit.

3. The use of any chemical additives not identified in the registration statement, except chlorine, without prior approval is prohibited under this general permit. Prior approval shall be obtained from the DEQ before any changes are made to the chemical and/or nonchemical treatment technology employed in the cooling water system. Requests for approval of the change shall be made in writing and shall include the following information:

a. Describe the chemical and/or nonchemical treatment to be employed and its purpose; if chemical additives are used, provide the information prescribed in subdivisions 3 b, c, d and e;

b. Provide name and manufacturer of each additive used;

c. Provide list of active ingredients and percentage of composition;

d. Give the proposed schedule and quantity of chemical usage, and estimate the concentration in the discharge; and

e. Attach available aquatic toxicity information for each additive proposed for use.

f. Attach any other information such as product or constituent degradation, fate, transport, synergies, bioavailability, etc., that will aid the board with the toxicity evaluation for the discharge.

4. Where cooling water is discharged through a municipal storm sewer system to surface waters, the permittee shall, within 30 days of coverage under this general permit, notify the owner of the municipal separate storm sewer system of the existence of the discharge and provide the following information: the name of the facility, a contact person and phone number, nature of the discharge, number of the outfalls, and the location of the discharge. A copy of such notification shall be provided to the department.

5. The permittee shall at all times properly operate and maintain all cooling water systems. Inspection shall be conducted for each cooling water unit by the plant personnel at least once per year with reports maintained on site.

6. The permittee shall notify the department as soon as they know or have reason to believe:

a. That any activity has occurred or will occur which would result in the discharge, on a routine or frequent basis, of any toxic pollutant which is not limited in this permit, if that discharge will exceed the highest of the following notification levels:

(1) One hundred micrograms per liter (100 μg/l);

(2) Two hundred micrograms per liter (200 μg/l) for acrolein and acrylonitrile; 500 micrograms per liter (500 μg/l) for 2,4-dinitrophenol and for 2-methyl-4,6-dinitrophenol; and one milligram per liter (1 mg/l) for antimony;

(3) Five times the maximum concentration value reported for that pollutant in the permit application; or

(4) The level established by the board in accordance with 9 VAC 25-31-220 F.

b. That any activity has occurred or will occur which would result in any discharge, on a nonroutine or infrequent basis, of a toxic pollutant which is not limited in this permit, if that discharge will exceed the highest of the following notification levels:

(1) Five hundred micrograms per liter (500 μg/l);

(2) One milligram per liter (1 mg/l) for antimony;

(3) Ten times the maximum concentration value reported for that pollutant in the permit application; or

(4) The level established by the board in accordance with 9 VAC 25-31-220 F.

PART II

CONDITIONS APPLICABLE TO ALL VPDES PERMITS

A. Monitoring.

1. Samples and measurements taken as required by this permit shall be representative of the monitored activity.

2. Monitoring shall be conducted according to procedures approved under 40 CFR Part 136 or alternative methods approved by the U.S. Environmental Protection Agency, unless other procedures have been specified in this permit.

3. The permittee shall periodically calibrate and perform maintenance procedures on all monitoring and analytical instrumentation at intervals that will ensure accuracy of measurements.

B. Records.

1. Records of monitoring information shall include:

a. The date, exact place and time of sampling or measurements;

b. The individual(s) who performed the sampling or measurements;

c. The date(s) and time(s) analyses were performed;

d. The individual(s) who performed the analyses;

e. The analytical techniques or methods used; and

f. The results of such analyses.

2. Except for records of monitoring information required by this permit related to the permittee's sewage sludge use and disposal activities, which shall be retained for a period of at least five years, the permittee shall retain records of all monitoring information, including all calibration and maintenance records and all original strip chart recordings for continuous monitoring instrumentation, copies of all reports required by this permit, and records of all data used to complete the registration statement for this permit, for a period of at least three years from the date of the sample, measurement, report or request for coverage. This period of retention shall be extended automatically during the course of any unresolved litigation regarding the regulated activity or regarding control standards applicable to the permittee or as requested by the board.

C. Reporting monitoring results.

1. The permittee shall submit the results of the monitoring required by this permit not later than the 10th day of the month after monitoring takes place, unless another reporting schedule is specified elsewhere in this permit. Monitoring results shall be submitted to the department's regional office.

2. Monitoring results shall be reported on a Discharge Monitoring Report (DMR) or on forms provided, approved or specified by the department.

3. If the permittee monitors any pollutant specifically addressed by this permit more frequently than required by this permit using test procedures approved under 40 CFR Part 136 or using other test procedures approved by the U.S. Environmental Protection Agency or using procedures specified in this permit, the results of this monitoring shall be included in the calculation and reporting of the data submitted in the DMR or reporting form specified by the department.

4. Calculations for all limitations which require averaging of measurements shall utilize an arithmetic mean unless otherwise specified in this permit.

D. Duty to provide information. The permittee shall furnish to the department, within a reasonable time, any information which the board may request to determine whether cause exists for modifying, revoking and reissuing, or terminating this permit or to determine compliance with this permit. The board may require the permittee to furnish, upon request, such plans, specifications, and other pertinent information as may be necessary to determine the effect of the wastes from his discharge on the quality of state waters, or such other information as may be necessary to accomplish the purposes of the State Water Control Law. The permittee shall also furnish to the department upon request copies of records required to be kept by this permit.

E. Compliance schedule reports. Reports of compliance or noncompliance with, or any progress reports on, interim and final requirements contained in any compliance schedule of this permit shall be submitted no later than 14 days following each schedule date.

F. Unauthorized discharges. Except in compliance with this permit or another permit issued by the board, it shall be unlawful for any person to:

1. Discharge into state waters sewage, industrial wastes, other wastes, or any noxious or deleterious substances; or

2. Otherwise alter the physical, chemical or biological properties of such state waters and make them detrimental to the public health, to animal or aquatic life, to the use of such waters for domestic or industrial consumption, for recreation, or for other uses.

G. Reports of unauthorized discharges. Any permittee who discharges or causes or allows a discharge of sewage, industrial waste, other wastes or any noxious or deleterious substance into or upon state waters in violation of Part II F, or who discharges or causes or allows a discharge that may reasonably be expected to enter state waters in violation of Part II F, shall notify the department of the discharge immediately upon discovery of the discharge, but in no case later than 24 hours after said discovery. A written report of the unauthorized discharge shall be submitted to the department within five days of discovery of the discharge. The written report shall contain:

1. A description of the nature and location of the discharge;

2. The cause of the discharge;

3. The date on which the discharge occurred;

4. The length of time that the discharge continued;

5. The volume of the discharge;

6. If the discharge is continuing, how long it is expected to continue;

7. If the discharge is continuing, what the expected total volume of the discharge will be; and

8. Any steps planned or taken to reduce, eliminate and prevent a recurrence of the present discharge or any future discharges not authorized by this permit.

Discharges reportable to the department under the immediate reporting requirements of other regulations are exempted from this requirement.

H. Reports of unusual or extraordinary discharges. If any unusual or extraordinary discharge including a bypass or upset should occur from a treatment works and the discharge enters or could be expected to enter state waters, the permittee shall promptly notify, in no case later than 24 hours, the department by telephone after the discovery of the discharge. This notification shall provide all available details of the incident, including any adverse affects on aquatic life and the known number of fish killed. The permittee shall reduce the report to writing and shall submit it to the department within five days of discovery of the discharge in accordance with Part II I 2. Unusual and extraordinary discharges include but are not limited to any discharge resulting from:

1. Unusual spillage of materials resulting directly or indirectly from processing operations;

2. Breakdown of processing or accessory equipment;

3. Failure or taking out of service some or all of the treatment works; and

4. Flooding or other acts of nature.

I. Reports of noncompliance. The permittee shall report any noncompliance which may adversely affect state waters or may endanger public health.

1. An oral report shall be provided within 24 hours from the time the permittee becomes aware of the circumstances. The following shall be included as information which shall be reported within 24 hours under this subsection:

a. Any unanticipated bypass; and

b. Any upset which causes a discharge to surface waters.

2. A written report shall be submitted within five days and shall contain:

a. A description of the noncompliance and its cause;

b. The period of noncompliance, including exact dates and times, and if the noncompliance has not been corrected, the anticipated time it is expected to continue; and

c. Steps taken or planned to reduce, eliminate, and prevent reoccurrence of the noncompliance.

The board may waive the written report on a case-by-case basis for reports of noncompliance under Part II I if the oral report has been received within 24 hours and no adverse impact on state waters has been reported.

3. The permittee shall report all instances of noncompliance not reported under Part II I 1 or 2, in writing, at the time the next monitoring reports are submitted. The reports shall contain the information listed in Part II I 2.

NOTE: The immediate (within 24 hours) reports required in Parts II G, H and I may be made to the department's regional office by telephone or by fax. For reports outside normal working hours, leave a message and this shall fulfill the immediate reporting requirement. For emergencies, the Virginia Department of Emergency Services maintains a 24-hour telephone service at 1-800-468-8892.

J. Notice of planned changes.

1. The permittee shall give notice to the department as soon as possible of any planned physical alterations or additions to the permitted facility. Notice is required only when:

a. The permittee plans alteration or addition to any building, structure, facility, or installation from which there is or may be a discharge of pollutants, the construction of which commenced:

(1) After promulgation of standards of performance under § 306 of Clean Water Act which are applicable to such source; or

(2) After proposal of standards of performance in accordance with § 306 of Clean Water Act which are applicable to such source, but only if the standards are promulgated in accordance with § 306 within 120 days of their proposal;

b. The alteration or addition could significantly change the nature or increase the quantity of pollutants discharged. This notification applies to pollutants which are subject neither to effluent limitations nor to notification requirements specified elsewhere in this permit; or

c. The alteration or addition results in a significant change in the permittee's sludge use or disposal practices, and such alteration, addition, or change may justify the application of permit conditions that are different from or absent in the existing permit, including notification of additional use or disposal sites not reported during the permit application process or not reported pursuant to an approved land application plan.

2. The permittee shall give advance notice to the department of any planned changes in the permitted facility or activity which may result in noncompliance with permit requirements.

K. Signatory requirements.

1. Registration statements. All registration statements shall be signed as follows:

a. For a corporation: by a responsible corporate officer. For the purpose of this section, a responsible corporate officer means: (i) a president, secretary, treasurer, or vice-president of the corporation in charge of a principal business function, or any other person who performs similar policy-making or decision-making functions for the corporation, or (ii) the manager of one or more manufacturing, production, or operating facilities employing more than 250 persons or having gross annual sales or expenditures exceeding $25 million (in second-quarter 1980 dollars) if, provided the manager is authorized to make management decisions that govern the operation of the regulated facility including having the explicit or implicit duty of making major capital investment recommendations, and initiating and directing other comprehensive measures to assure long-term environmental compliance with environmental laws and regulations; the manager can ensure that the necessary systems are established or actions taken to gather complete and accurate information for permit application requirements; and where authority to sign documents has been assigned or delegated to the manager in accordance with corporate procedures;

b. For a partnership or sole proprietorship: by a general partner or the proprietor, respectively; or

c. For a municipality, state, federal, or other public agency: by either a principal executive officer or ranking elected official. For purposes of this section, a principal executive officer of a public agency includes: (i) the chief executive officer of the agency, or (ii) a senior executive officer having responsibility for the overall operations of a principal geographic unit of the agency.

2. Reports, etc. All reports required by permits, and other information requested by the board shall be signed by a person described in Part II K 1, or by a duly authorized representative of that person. A person is a duly authorized representative only if:

a. The authorization is made in writing by a person described in Part II K 1;

b. The authorization specifies either an individual or a position having responsibility for the overall operation of the regulated facility or activity such as the position of plant manager, operator of a well or a well field, superintendent, position of equivalent responsibility, or an individual or position having overall responsibility for environmental matters for the company (a duly authorized representative may thus be either a named individual or any individual occupying a named position); and

c. The written authorization is submitted to the department.

3. Changes to authorization. If an authorization under Part II K 2 is no longer accurate because a different individual or position has responsibility for the overall operation of the facility, a new authorization satisfying the requirements of Part II K 2 shall be submitted to the department prior to or together with any reports or information to be signed by an authorized representative.

4. Certification. Any person signing a document under Part II K 1 or 2 shall make the following certification:

"I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to assure that qualified personnel properly gather and evaluate the information submitted. Based on my inquiry of the person or persons who manage the system, or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete. I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations."

L. Duty to comply. The permittee shall comply with all conditions of this permit. Any permit noncompliance constitutes a violation of the State Water Control Law and the Clean Water Act, except that noncompliance with certain provisions of this permit may constitute a violation of the State Water Control Law but not the Clean Water Act. Permit noncompliance is grounds for enforcement action; for permit termination, revocation and reissuance, or modification; or denial of a permit renewal application.

The permittee shall comply with effluent standards or prohibitions established under § 307(a) of the Clean Water Act for toxic pollutants and with standards for sewage sludge use or disposal established under § 405(d) of the Clean Water Act within the time provided in the regulations that establish these standards or prohibitions or standards for sewage sludge use or disposal, even if this permit has not yet been modified to incorporate the requirement.

M. Duty to reapply. If the permittee wishes to continue an activity regulated by this permit after the expiration date of this permit, the permittee shall apply for and obtain a new permit. All permittees with a currently effective permit shall submit a new registration statement at least 180 days before the expiration date of the existing permit, unless permission for a later date has been granted by the board. The board shall not grant permission for registration statements to be submitted later than the expiration date of the existing permit.

N. Effect of a permit. This permit does not convey any property rights in either real or personal property or any exclusive privileges, nor does it authorize any injury to private property or invasion of personal rights, or any infringement of federal, state or local law or regulations.

O. State law. Nothing in this permit shall be construed to preclude the institution of any legal action under, or relieve the permittee from any responsibilities, liabilities, or penalties established pursuant to any other state law or regulation or under authority preserved by § 510 of the Clean Water Act. Except as provided in permit conditions on bypass (Part II U) and upset (Part II V), nothing in this permit shall be construed to relieve the permittee from civil and criminal penalties for noncompliance.

P. Oil and hazardous substance liability. Nothing in this permit shall be construed to preclude the institution of any legal action or relieve the permittee from any responsibilities, liabilities, or penalties to which the permittee is or may be subject under §§ 62.1-44.34:14 through 62.1-44.34:23 of the State Water Control Law.

Q. Proper operation and maintenance. The permittee shall at all times properly operate and maintain all facilities and systems of treatment and control (and related appurtenances) which are installed or used by the permittee to achieve compliance with the conditions of this permit. Proper operation and maintenance also includes effective plant performance, adequate funding, adequate staffing, and adequate laboratory and process controls, including appropriate quality assurance procedures. This provision requires the operation of back-up or auxiliary facilities or similar systems which are installed by the permittee only when the operation is necessary to achieve compliance with the conditions of this permit.

R. Disposal of solids or sludges. Solids, sludges or other pollutants removed in the course of treatment or management of pollutants shall be disposed of in a manner so as to prevent any pollutant from such materials from entering state waters.

S. Duty to mitigate. The permittee shall take all reasonable steps to minimize or prevent any discharge or sludge use or disposal in violation of this permit which has a reasonable likelihood of adversely affecting human health or the environment.

T. Need to halt or reduce activity not a defense. It shall not be a defense for a permittee in an enforcement action that it would have been necessary to halt or reduce the permitted activity in order to maintain compliance with the conditions of this permit.

U. Bypass.

1. "Bypass" means the intentional diversion of waste streams from any portion of a treatment facility. The permittee may allow any bypass to occur which does not cause effluent limitations to be exceeded, but only if it also is for essential maintenance to ensure efficient operation. These bypasses are not subject to the provisions of Part II U 2 and U 3.

2. Notice.

a. Anticipated bypass. If the permittee knows in advance of the need for a bypass, prior notice shall be submitted, if possible at least 10 days before the date of the bypass.

b. Unanticipated bypass. The permittee shall submit notice of an unanticipated bypass as required in Part II I.

3. Prohibition of bypass.

a. Bypass is prohibited, and the board may take enforcement action against a permittee for bypass, unless:

(1) Bypass was unavoidable to prevent loss of life, personal injury, or severe property damage;

(2) There were no feasible alternatives to the bypass, such as the use of auxiliary treatment facilities, retention of untreated wastes, or maintenance during normal periods of equipment downtime. This condition is not satisfied if adequate back-up equipment should have been installed in the exercise of reasonable engineering judgment to prevent a bypass which occurred during normal periods of equipment downtime or preventive maintenance; and

(3) The permittee submitted notices as required under Part II U 2.

b. The board may approve an anticipated bypass, after considering its adverse effects, if the board determines that it will meet the three conditions listed in Part II U 3 a.

V. Upset.

1. An upset constitutes an affirmative defense to an action brought for noncompliance with technology based permit effluent limitations if the requirements of Part II V 2 are met. A determination made during administrative review of claims that noncompliance was caused by upset, and before an action for noncompliance, is not a final administrative action subject to judicial review.

2. A permittee who wishes to establish the affirmative defense of upset shall demonstrate, through properly signed, contemporaneous operating logs, or other relevant evidence that:

a. An upset occurred and that the permittee can identify the cause(s) of the upset;

b. The permitted facility was at the time being properly operated;

c. The permittee submitted notice of the upset as required in Part II I; and

d. The permittee complied with any remedial measures required under Part II S.

3. In any enforcement proceeding the permittee seeking to establish the occurrence of an upset has the burden of proof.

W. Inspection and entry. The permittee shall allow the director, or an authorized representative, upon presentation of credentials and other documents as may be required by law, to:

1. Enter upon the permittee's premises where a regulated facility or activity is located or conducted, or where records must be kept under the conditions of this permit;

2. Have access to and copy, at reasonable times, any records that must be kept under the conditions of this permit;

3. Inspect at reasonable times any facilities, equipment (including monitoring and control equipment), practices, or operations regulated or required under this permit; and

4. Sample or monitor at reasonable times, for the purposes of assuring permit compliance or as otherwise authorized by the Clean Water Act and the State Water Control Law, any substances or parameters at any location.

For purposes of this subsection, the time for inspection shall be deemed reasonable during regular business hours, and whenever the facility is discharging. Nothing contained herein shall make an inspection unreasonable during an emergency.

X. Permit actions. Permits may be modified, revoked and reissued, or terminated for cause. The filing of a request by the permittee for a permit modification, revocation and reissuance, or termination, or a notification of planned changes or anticipated noncompliance does not stay any permit condition.

Y. Transfer of permits.

1. Permits are not transferable to any person except after notice to the department. Except as provided in Part II Y 2, a permit may be transferred by the permittee to a new owner or operator only if the permit has been modified or revoked and reissued, or a minor modification made, to identify the new permittee and incorporate such other requirements as may be necessary under the State Water Control Law and the Clean Water Act.

2. As an alternative to transfers under Part II Y 1, this permit may be automatically transferred to a new permittee if:

a. The current permittee notifies the department at least 30 days in advance of the proposed transfer of the title to the facility or property;

b. The notice includes a written agreement between the existing and new permittees containing a specific date for transfer of permit responsibility, coverage, and liability between them; and

c. The board does not notify the existing permittee and the proposed new permittee of its intent to modify or revoke and reissue the permit. If this notice is not received, the transfer is effective on the date specified in the agreement mentioned in Part II Y 2 b.

Z. Severability. The provisions of this permit are severable. If any provision of this permit or the application of any provision of this permit to any circumstance is held invalid, the application of such provision to other circumstances and the remainder of this permit shall not be affected thereby.

9 VAC 25-196-80. Evaluation of chapter and petitions for reconsideration or revision. (Repealed.)

A. Within three years after March 1, 1998, the department shall perform an analysis on this chapter and provide the board with a report on the results. The analysis shall include (i) the purpose and need for the chapter, (ii) alternatives which would achieve the stated purpose of this chapter in a less burdensome and less intrusive manner, (iii) an assessment of the effectiveness of this chapter, (iv) the results of a review of current state and federal statutory and regulatory requirements, including identification and justification of requirements of this chapter which are more stringent than federal requirements, and (v) the results of a review as to whether this chapter is clearly written and easily understandable by affected entities. Upon review of the department's analysis, the board shall confirm the need to (i) continue this chapter without amendment, (ii) repeal this chapter or (iii) amend this chapter. If the board's decision is to repeal or amend this chapter, the board shall authorize the department to initiate the applicable regulatory process to carry out the decision of the board.

B. The board shall receive, consider and respond to petitions by any interested person at any time with respect to reconsideration or revision of this chapter.

DOCUMENTS INCORPORATED BY REFERENCE

Method	Cite

| 200.7 | EPA 600/R-94-111; 40 CFR 136, App D, 1996 |
| --- | --- |
| 200.8 | EPA 600/R-94-111 |
| 200.9 | EPA 600/R-94-111 |
| 220.1 | EPA 600/4-79-020; 40 CFR 136, App D, 1996 |
| 220.2 | EPA 600/4-79-020; 40 CFR 136, App D, 1996 |
| 272.1 | EPA 600/4-79-020 |
| 272.2 | EPA 600/4-79-020; 40 CFR 136, App D, 1996 |
| 289.1 | EPA 600/4-79-020; 40 CFR 136, App D, 1996 |
| 289.2 | EPA 600/4-79-020 |
| 1638 | EPA 821/R-95-031 |
| 1639 | EPA 821/R-95-032 |
| 1640 | EPA 821/R-95-033 |

VA.R. Doc. No. R01-273; Filed August 5, 2002, 9:54 a.m.