TITLE 9. ENVIRONMENT

STATE WATER CONTROL BOARD

REGISTRAR'S NOTICE: The State Water Control Board adopted revisions to the Regulation for Nutrient Enriched Waters and Dischargers within the Chesapeake Bay Watershed (9 VAC 25-40) and the Water Quality Management Planning Regulation (9 VAC 25-720), which were published in final version in 21:23 VA.R. 3236-3249 July 25, 2005, and at the same time the amendments to the regulations were suspended by the board pursuant to § 2.2-4015 A 4 of the Administrative Process Act. The changes made since the 21:23 VA.R. publication are shown in brackets.

The board deferred action on 9 VAC 25-720-60 (James River Basin) and 9 VAC 25-720-120 (York River), therefore, these sections have been removed and are not being printed at this time. The board is expected to take final action on these sections at a future meeting.

Titles of Regulations:  9 VAC 25-40. Regulation for Nutrient Enriched Waters and Dischargers within the Chesapeake Bay Watershed (amending 9 VAC 25-40-10, 9 VAC 25-40-30, 9 VAC 25-40-40, and 9 VAC 25-40-50; adding 9 VAC 25-40-25, 9 VAC 25-40-70; and repealing 9 VAC 25-40-20).

9 VAC 25-720. Water Quality Management Planning Regulation (amending 9 VAC 25-720-10, 9 VAC 25-720-30, 9 VAC 25-720-40, 9 VAC 25-720-50, 9 VAC 25-720-70, 9 VAC 25-720-110.

Statutory Authority:  § 62.1-44.15 of the Code of Virginia; § 303 of the federal Clean Water Act.

Effective Date:  November 16, 2005.

Agency Contact:  John Kennedy, Department of Environmental Quality, P.O. Box 10009, Richmond, VA 23240, telephone (804) 698-4312, FAX (804) 698-4116, or 
e-mail jmkennedy@deq.virginia.gov.

Summary:

The amendments (i) revise the existing point source policy for nutrient enriched waters to establish technology-based, annual average total nitrogen and total phosphorus concentration requirements for certain dischargers located in Virginia's Chesapeake Bay watershed, and (ii) revise the Water Quality Management Planning Regulation to establish total nitrogen and total phosphorus annual waste load allocations for certain dischargers within Virginia's portion of the Chesapeake Bay Watershed, and authorize a trading and offsets program to assist in the achievement and maintenance of the waste load allocations.

The State Water Control Board deferred making a decision on 9 VAC 25-720-60 and 9 VAC 25-720-120, which included nitrogen and phosphorus waste load allocations to restore the Chesapeake Bay and its tidal rivers.   The amendments to these sections will be considered at a future meeting of the  State Water Control Board.

Summary of Public Comment and Agency Response:  A summary of comments made by the public and the agency's response may be obtained from the promulgating agency or viewed at the Office of the Registrar of Regulations.

CHAPTER 40.

POLICY REGULATION FOR NUTRIENT ENRICHED WATERS AND DISCHARGERS WITHIN THE CHESAPEAKE BAY WATERSHED.

9 VAC 25-40-10. Purpose.

This policy regulation provides for the control of discharges of nutrients from point sources affecting state waters that have been are designated "nutrient enriched waters" in 9 VAC 25-260-350 or are located within the Chesapeake Bay watershed, which consists of the following Virginia river basins: Potomac River Basin (9 VAC 25-260-390 and 9 VAC 25-260-400), James River Basin (9 VAC 25-260-410, 9 VAC 25-260-415, 9 VAC 25-260-420, and 9 VAC 25-260-430), Rappahannock River Basin (9 VAC 25-260-440), Chesapeake Bay and small coastal basins (9 VAC 25-260-520, Sections 2 through 3g), and the York River Basin (9 VAC 25-260-530).

The provisions of this regulation and the Water Quality Management Planning Regulation (9 VAC 25-720) constitute the nutrient reduction requirements for point source discharges in the Chesapeake Bay Watershed to protect the Chesapeake Bay and its tidal rivers.

9 VAC 25-40-20. Authority. (Repealed.)

The board has adopted this policy under the authority of §§ 62.1-44.15(3), 62.1-44.15(10) and 62.1-44.15(14) of the Code of Virginia.

9 VAC 25-40-25. Definitions.

The following words and terms when used in this chapter shall have the following meanings unless the context clearly indicates otherwise:

“Equivalent load” means 2,300 pounds per year of total nitrogen and 300 pounds per year of total phosphorus at a flow volume of 40,000 gallons per day; 5,700 pounds per year of total nitrogen and 760 pounds per year of total phosphorus at a flow volume of 100,000 gallons per day; and 28,500 pounds per year of total nitrogen and 3,800 pounds per year of total phosphorus at a flow volume of 500,000 gallons per day.

“Expansion” or “expands” means initiating construction [ of a at an existing ] facility after July 1, 2005, to increase treatment capacity, except that the term does not apply in those cases where a Certificate to Construct was issued on or before July 1, 2005.

“Point source dischargers” or “dischargers” do not include permitted discharges of noncontact cooling water or storm water.

9 VAC 25-40-30. Strategy for "nutrient enriched waters." outside of Chesapeake Bay Watershed.

As specified here, the board shall reopen the NPDES permits of certain point source dischargers to "nutrient enriched waters" and shall impose effluent limitations on nutrients in the discharges authorized by those permits and certain new permits.

A. All dischargers authorized by NPDES VPDES permits issued on or before July 1, 1988, to discharge 1 1.0 MGD or more to "nutrient enriched waters" shall be required to meet a monthly average total phosphorus effluent limitation of 2 mg/1 as quickly as possible and in any event within three years following modification of the NPDES permit 2.0 mg/l.

At the time of modification of the NPDES permit, any discharger who voluntarily accepts a permit to require installation and operation of nitrogen removal facilities to meet a monthly average total nitrogen effluent limitation of 10 mg/1 for the months of April through October shall be allowed an additional year to meet the phosphorus effluent limitation in 9 VAC 25-40-30 A.

B. All New source dischargers as defined in 9 VAC 25-30-10 with a permit issued that commence discharging 9 VAC 25-21 9 VAC 25-31 with a permit issued after July 1, 1988, and a design flow greater than or equal to 0.05 are authorized by VPDES permits to discharge 0.050 MGD who propose to discharge or more to "nutrient enriched waters" shall be required to meet a monthly average total phosphorus effluent limitation of 2 mg/1 2.0 mg/l.

C. This policy regulation shall not be construed to relax any effluent limitation concerning a nutrient that is imposed under any other requirement of state or federal law. No time extensions outlined in 9 VAC 25-40-30 A for installation and operation of nitrogen removal facilities shall be granted to a discharger if such an effluent limitation or a time extension is already imposed under any other requirement of state or federal law or regulation.

D. Any discharger to "nutrient enriched waters" that is located within the Chesapeake Bay Watershed is not subject to the requirements of this section.

9 VAC 25-40-40. Permit amendments.

Whenever the board determines that a permittee has the potential for discharging monthly average total phosphorus concentrations greater than or equal to 2 mg/1 2.0 mg/l or monthly average total nitrogen concentrations greater than or equal to 10 mg/1 1.0 x 101  10 mg/l to "nutrient enriched waters," the board may reopen the NPDES VPDES permit to impose monitoring requirements for nutrients in the discharge.

9 VAC 25-40-50. Possibility of further limitations.

The board anticipates that, following implementation of the foregoing requirements and evaluation of effects of this policy regulation and of the results of the nonpoint source control programs, further limitations on discharges of phosphorus or of other nutrients may be necessary to control undesirable growths of aquatic plants.

9 VAC 25-40-70. Strategy for Chesapeake Bay Watershed.

[ A. In recognition that nutrient reductions from point source discharges have a significant role in the restoration of the Chesapeake Bay and its tidal rivers since they provide a more immediate benefit to water quality and are more reliable than reductions from nonpoint sources, it shall be the policy of the board that point source dischargers within the Chesapeake Bay Watershed utilize biological nutrient removal technology or its equivalent whenever feasible, as provided by subsection B of this section.  For the purposes of this chapter and the related sections of 9 VAC 25-720, the terms "point source dischargers" or "dischargers" do not include permitted discharges of noncontact cooling water or storm water operate installed nutrient removal technologies at the treatment efficiency levels for which they were designed.

B. A. ] As specified herein, the board shall issue and reissue the VPDES permits of certain point source dischargers within the Chesapeake Bay Watershed and shall impose effluent concentration limitations on nutrients in the discharges authorized by those permits include technology-based effluent concentration limitations in the individual permit for any facility that has installed technology for the control of nitrogen and phosphorus whether by new construction, expansion, or upgrade. Such limitations shall be based upon the technology installed by the facility and shall be expressed as annual average concentrations.

1. Except as provided under subdivision 4 of this subsection,  all significant dischargers, as defined in 9 VAC 25-720, authorized by VPDES permits issued on or before [the effective date of this chapter] shall achieve an annual average total nitrogen effluent limitation of not more than 8.0 mg/l and an annual average total phosphorus effluent limitation of not more than 1.0 mg/l; provided, however, these dischargers must achieve an annual total nitrogen waste load allocation and an annual total phosphorus waste load allocation as required by the Water Quality Management Planning Regulation (9 VAC 25-720).  The applicable limitations shall be achieved within four years following reissuance or major modification of the VPDES permit, but in no case later than December 31, 2010 an owner or operator of a facility authorized by a Virginia Pollutant Discharge Elimination System permit first issued before July 1, 2005, that expands his facility to discharge 100,000 gallons or more per day, or an equivalent load directly into tidal waters, or 500,000 gallons or more per day, or an equivalent load, directly into nontidal waters shall install state-of-the-art nutrient removal technology at the time of the expansion and achieve an annual average total nitrogen effluent concentration of 3.0 milligrams per liter and an annual average total phosphorus effluent concentration of 0.3 milligrams per liter.

2. Except as provided under subdivision 4 of this subsection,  all dischargers that do not meet the definition of a significant discharger and are authorized by VPDES permits issued on or before July 1, 2004, to discharge 0.040 MGD or more shall be required to achieve an annual average total nitrogen effluent limitation of 8.0 mg/l and an annual average total phosphorus effluent limitation of 1.0 mg/l.  These limitations shall be included in reissued or modified permits after December 31, 2010, and shall be achieved within four years following reissuance or major modification of the VPDES permits an owner or operator of a facility authorized by a Virginia Pollutant Discharge Elimination System permit first issued before July 1, 2005, that expands his facility to discharge 100,000 gallons or more per day up to and including 499,999 gallons per day, or an equivalent load, directly into nontidal waters shall install, at a minimum, biological nutrient removal technology at the time of the expansion and achieve an annual average total nitrogen effluent concentration of 8.0 milligrams per liter and an annual average total phosphorus effluent concentration of 1.0 milligrams per liter.

3. Except as provided under subdivision 4 of this subsection,  all new dischargers or expanded discharges of nitrogen or phosphorus authorized by VPDES permits issued after [the effective date of this chapter] to discharge 0.040 MGD or more shall achieve an annual average total nitrogen effluent limitation of 3.0 mg/l and an annual average total phosphorus effluent limitation of 0.30 mg/l an owner or operator of a facility authorized by a Virginia Pollutant Discharge Elimination System permit first issued on or after July 1, 2005, to discharge 40,000 gallons or more per day, or an equivalent load, shall install:

a. At a minimum, biological nutrient removal technology at any facility authorized to discharge up to and including 99,999 gallons per day, or an equivalent load, directly into tidal and nontidal waters or up to and including 499,999 gallons per day, or an equivalent load, to nontidal waters and achieve an annual average total nitrogen effluent concentration of 8.0 milligrams per liter and an annual average total phosphorus effluent concentration of 1.0 milligrams per liter; and

b. State-of-the-art nutrient removal technology at any facility authorized to discharge 100,000 gallons or more per day, or an equivalent load, directly into tidal waters or 500,000 gallons or more per day, or an equivalent load, directly into nontidal waters and achieve an annual average total nitrogen effluent concentration of 3.0 milligrams per liter and an annual average total phosphorus effluent concentration of 0.3 milligrams per liter.

4. On a case-by-case basis, a discharger may demonstrate to the satisfaction of the board through treatability, engineering, or other studies that biological nutrient removal technology or its equivalent at a point source discharge cannot achieve the effluent limitations of subdivision 1, 2 or 3 of this subsection, as applicable.  In these cases, the board shall require alternative effluent limitations the board deems appropriate for that discharger; the board may establish a technology-based standard and associated concentration limitation less stringent than the applicable standard specified in subdivision 1, 2 or 3 of this subsection, as applicable, based on a demonstration by an owner or operator that the specified standard is not technically or economically feasible for the affected facility or that the technology-based standard and associated concentration limitation would [ degrade receiving waters or ] require the owner or operator to construct treatment facilities not otherwise necessary to comply with his waste load allocation without reliance on nutrient credit exchanges pursuant to § 62.1-44.19:18 of the Code of Virginia, provided, however, the discharger must achieve an annual total nitrogen waste load allocation and an annual total phosphorus waste load allocation as required by the Water Quality Management Planning Regulation (9 VAC 25-720).

5. Any effluent limitation concerning a nutrient that is imposed under any other requirement of state or federal law or regulation that is more stringent than those established herein shall not be affected by this regulation.

[ C. B. ] In accordance with Article 1.1 (§ 10.1-1187.1 et seq.) of Chapter 11.1 of Title 10.1 of the Code of Virginia, the board may approve an alternate compliance method to the technology-based effluent concentration limitations as required by subsection [ B A ] of this section. Such alternate compliance method shall be incorporated into the permit of an Exemplary Environmental Enterprise (E3) facility or an Extraordinary Environmental Enterprise (E4) facility to allow the suspension of applicable technology-based effluent concentration limitations during the period the E3 or E4 facility has a fully implemented environmental management system that includes operation of installed nutrient removal technologies at the treatment efficiency levels for which they were designed.

C. [ D. C. ] Notwithstanding [ subsections A and B subsection A ] of this section, point source dischargers within the Chesapeake Bay Watershed are also governed by the Water Quality Management Planning Regulation (9 VAC 25-720).

9 VAC 25-720-10. Definitions.

The following words and terms when used in this chapter shall have the following meanings unless the context clearly indicates otherwise:

"Assimilative capacity" means the greatest amount of loading that a water can receive without violating water quality standards, significantly degrading waters of existing high quality, or interfering with the beneficial use of state waters.

"Best management practices (BMP)" means a schedule of activities, prohibition of practices, maintenance procedures and other management practices to prevent or reduce the pollution of state waters.  BMPs include treatment requirements, operating and maintenance procedures, schedule of activities, prohibition of activities, and other management practices to control plant site runoff, spillage, leaks, sludge or waste disposal, or drainage from raw material storage.

"Best practicable control technology currently available (BPT)" means control measures required of point source discharges (other than POTWs) as determined by the EPA pursuant to § 304(b)(1) of the CWA (33 USC § 1251 et seq.) as of 1987.

"Board" means the State Water Control Board (SWCB).

"Chesapeake Bay Watershed" means the following Virginia river basins: Potomac River Basin (9 VAC 25-260-390 and 9 VAC 25-260-400), James River Basin (9 VAC 25-260-410, 9 VAC 25-260-415, 9 VAC 25-260-420, and 9 VAC 25-260-430), Rappahannock River Basin (9 VAC 25-260-440), Chesapeake Bay and small coastal basins (9 VAC 25-260-520, Sections 2 through 3g), and the York River Basin (9 VAC 25-260-530).

"Clean Water Act or Act (CWA)" means 33 USC § 1251 et seq. as amended, as of 1987.

"Delivered waste load" means the discharged load from a point source in a river basin that is adjusted by a delivery factor for any alteration of that load occurring from biological, chemical, and physical processes during riverine transport to tidal waters. Delivery factors are calculated using the Chesapeake Bay Program watershed model.

“Delivery factor” means an estimate of the number of pounds of total nitrogen or total phosphorus delivered to tidal waters for every pound discharged from a permitted facility, as determined by the specific geographic location of the permitted facility, to account for attenuation that occurs during riverine transport between the permitted facility and tidal waters. Delivery factors shall be calculated using the Chesapeake Bay Program watershed model.

"Discharge" means when used without qualification, a discharge of a pollutant or any addition of any pollutant or combination of pollutants to state waters or waters of the contiguous zone or ocean or other floating craft when being used for transportation.

"Effluent limitation" means any restriction imposed by the board on quantities, discharge rates or concentrations of pollutants that are discharged from joint point sources into state waters.

"Effluent limitation guidelines" means a regulation published by EPA under the Act and adopted by the board.

"Effluent limited segment (EL)" means a stream segment where the water quality does and probably will continue to meet state water quality standards after the application of technology-based effluent limitations required by §§ 301(b) and 306 of the CWA (33 USC § 1251 et seq.) as of 1987.

"Environmental Protection Agency (EPA)" means the United States Environmental Protection Agency.

”Equivalent load” means 2,300 pounds per year of total nitrogen and 300 pounds per year of total phosphorus at a flow volume of 40,000 gallons per day; 5,700 pounds per year of total nitrogen and 760 pounds per year of total phosphorus at a flow volume of 100,000 gallons per day; and 28,500 pounds per year of total nitrogen and 3,800 pounds per year of total phosphorus at a flow volume of 500,000 gallons per day.

"Load or loading" means the introduction of an amount of matter or thermal energy into a receiving water.  Loading may be either man-caused (pollutant loading) or natural (background loading).

"Load allocation (LA)" means the portion of a receiving water's loading capacity attributable either to one of its existing or future nonpoint sources of pollution or to natural background sources.  Load allocations are best estimates of the loading, which may range from accurate estimates to gross allotments, depending on the availability of data and appropriate techniques for predicting the loading.  Wherever possible, natural and nonpoint source loads should be distinguished.

"Nonpoint source" means a source of pollution, such as a farm or forest land runoff, urban storm water runoff, mine runoff, or salt water intrusion that is not collected or discharged as a point source.

"Point source" means any discernible, defined and discrete conveyance, including but not limited to any pipe, ditch, channel, tunnel, conduit, well, discrete fissure, container, rolling stock vessel or other floating craft, from which pollutants are or may be discharged.  This term does not include return flows from irrigated agricultural land.

"Pollutant" means any substance, radioactive material, or heat that causes or contributes to, or may cause or contribute to, pollution.  It does not mean:

1. Sewage from vessels; or

2. Water, gas, or other material that is injected into a well to facilitate production of oil, dry gas, or water derived in association with oil or gas production and disposed of in a well, if the well is used either to facilitate production or for disposal purposes if approved by the Department of Mines, Minerals and Energy unless the board determines that such injection or disposal will result in the degradation of ground or surface water resources.

"Pollution" means such alteration of the physical, chemical or biological properties of any state waters as will or is likely to create a nuisance or render such waters (i) harmful or detrimental or injurious to the public health, safety or welfare, or to the health of animals, fish or aquatic life;  (ii) unsuitable with reasonable treatment for use as present or possible future sources of public water supply;  or (iii) unsuitable for recreational, commercial, industrial, agricultural, or other reasonable uses;  provided that:  (a) an alteration of the physical, chemical, or biological property of state waters, or a discharge or deposit of sewage, industrial wastes or other wastes to state waters by any owner, which by itself is not sufficient to cause pollution, but which, in combination with such alteration of or discharge or deposit to state waters by other owners is sufficient to cause pollution;  (b) the discharge of untreated sewage by any owner into state waters;  and (c) contributing to the contravention of standards of water quality duly established by the board, are "pollution" for the terms and purposes of this water quality management plan.

"Publicly owned treatment works (POTW)" means any sewage treatment works that is owned by a state or municipality.  Sewers, pipes, or other conveyances are included in this definition only if they convey wastewater to a POTW providing treatment.

"Significant discharges discharger" means a point source discharger within the Chesapeake Bay Watershed that is listed in any of the following subsections: 9 VAC 25-720-50 C, 9 VAC 25-720-60 C, 9 VAC 25-720-70 C, 9 VAC 25-720-110 C, or 9 VAC 25-720-120 C; or a new or expanded point source discharger authorized by a VPDES permit issued after July 1, 2004, to discharge 2,300 pounds per year or more of total nitrogen or 300 pounds per year or more of total phosphorus (i) a point source discharger to the Chesapeake Bay watershed with a design capacity of 0.5 million gallons per day or greater, or an equivalent load; (ii) a point source discharger to the Chesapeake Bay watershed [ east downstream ] of the fall line with a design capacity of 0.1 million gallons per day or greater, or an equivalent load; (iii) a planned or newly expanding point source discharger to the Chesapeake Bay watershed that is expected to be in operation by 2010 with a permitted design of 0.5 million gallons per day or greater, or an equivalent load; or (iv) a planned or newly expanding point source discharger to the Chesapeake Bay watershed [ east downstream ] of the fall line with a design capacity of 0.1 million gallons per day or greater, or an equivalent load, that is expected to be in operation by 2010.

"State waters" means all waters, on the surface and under the ground and wholly or partially within or bordering the Commonwealth or within its jurisdiction, including wetlands.

"Surface water" means all waters in the Commonwealth except ground waters as defined in § 62.1-255 of the Code of Virginia.

"Total maximum daily load (TMDL)" means the sum of the individual waste load allocations (WLAs) for point sources, load allocations (LAs) for nonpoint sources, natural background loading and usually a safety factor.  TMDLs can be expressed in terms of either mass per time, toxicity, or other appropriate measure.  The TMDL process provides for point versus nonpoint source trade-offs.

"Toxic pollutant" means any agent or material including, but not limited to, those listed under § 307(a) of the CWA (33 USC § 1251 et seq. as of 1987), which after discharge will, on the basis of available information, cause toxicity.

"Toxicity" means the inherent potential or capacity of a material to cause adverse effects in a living organism, including acute or chronic effects to aquatic life, detrimental effects on human health or other adverse environmental effects.

[ "Trading" means the transfer of assigned waste load allocations or credits for total nitrogen or total phosphorus among point source dischargers.  It does not include the transfer of total nitrogen for total phosphorus, or the reverse. ]

"Virginia Pollution Discharge Elimination System (VPDES) permit" means a document issued by the board, pursuant to 9 VAC 25-30 9 VAC 25-31, authorizing, under prescribed conditions, the potential or actual discharge of pollutants from a point source to surface waters.

"Waste load allocation (WLA)" means the portion of a receiving water's loading or assimilative capacity allocated to one of its existing or future point sources of pollution.  WLAs are a type of water quality-based effluent limitation.

"Water quality limited segment (WQL)" means any stream segment where the water quality does not or will not meet applicable water quality standards, even after the application of technology-based effluent limitations required by §§ 301(b) and 306 of the CWA (33 USC § 1251 et seq. as of 1987).

"Water quality management plan (WQMP)" means a state- or area-wide waste treatment management plan developed and updated in accordance with the provisions of §§ 205(j), 208 and 303 of the CWA (33 USC § 1251 et seq. as of 1987).

"Water quality standards (WQS)" means narrative statements that describe water quality requirements in general terms, and of numeric limits for specific physical, chemical, biological or radiological characteristics of water.  These narrative statements and numeric limits describe water quality necessary to meet and maintain reasonable and beneficial uses such as swimming and, other water based recreation, public water supply and the propagation and growth of aquatic life.  The adoption of water quality standards under the State Water Control Law is one of the board's methods of accomplishing the law's purpose.

9 VAC 25-720-30. Reserved. Relationship to 9 VAC 25-40, Regulation for Nutrient Enriched Waters and Dischargers within the Chesapeake Bay Watershed.

The provisions of this chapter and 9 VAC 25-40, Regulation for Nutrient Enriched Waters and Dischargers within the Chesapeake Bay Watershed, constitute the nutrient reduction requirements for point source discharges in the Chesapeake Bay Watershed to protect the Chesapeake Bay and its tidal rivers.

9 VAC 25-720-40. Reserved Trading and offsets Implementing Nitrogen and Phosphorus Waste Load Allocations in the Chesapeake Bay Watershed.

A. Nitrogen and phosphorus waste load allocations assigned to individual significant dischargers in 9 VAC 25-720-50 C, 9 VAC 25-720-60 C, 9 VAC 25-720-70 C, 9 VAC 25-720-110 C, and 9 VAC 25-720-120 C may be [ traded exchanged ] among significant dischargers within the same river basin to assist in the achievement and maintenance of the total basin delivered waste load allocations in accordance with the Chesapeake Bay Watershed Nutrient Credit Exchange Program established under Article 4.02 (§ 62.1-44.19:12 et seq.) of Chapter 3.1 of Title 62.1 of the Code of Virginia. [ Trades Exchanges ] must account for the delivery factor applicable to each discharge based upon its location within the river basin and calculated by the Chesapeake Bay Program watershed model.

B. Any proposed trade shall not result in degradation or adverse impacts to local water quality or violations of water quality standards.

C. Any trade of nitrogen or phosphorus waste load allocation among individual significant dischargers shall not result in the exceedence of the total basin delivered waste load allocation within which the significant dischargers are located.

D. The board may authorize trading only through VPDES permits.  Trades conducted in accordance with this chapter through VPDES permits shall not require any amendments to this chapter.

E. Any discharge of nitrogen or phosphorus load from a new significant discharger or any increase in the discharge of nitrogen or phosphorus load from an expansion of an existing significant discharger that would exceed the waste load allocation for that significant discharger shall be accompanied by one of the following actions within the same river basin: (i) a trade for an equivalent or greater load reduction of the same pollutant from one or more existing dischargers; (ii) in accordance with the criteria listed below, the installation, monitoring and maintenance of best management practices that achieve an offsetting reduction of nonpoint source delivered load of nitrogen or phosphorus that the board determines is at least twice the reduction in delivered load compared to the new or increased delivered load from the significant discharger; or (iii) both actions in combination.

The board may approve use of the second option (clause (ii)) in the previous paragraph in accordance with the following:

1. The VPDES permit for the new or expanded significant discharger includes an annual average total nitrogen effluent limitation of 3.0 mg/l or an annual average total phosphorus effluent limitation of 0.30 mg/l, as appropriate, or alternative limits as required by 9 VAC 245-40-70 B 4;

2. Best management practices are installed within the locality or localities served by the new or expanded discharger, unless the board determines that installation of the needed best management practices in another locality provides greater water quality benefits;

3. Credit may be given for improvements to best management practices beyond that already required under other federal or state law to the extent that additional reduction in delivered nitrogen or phosphorus load is provided;

4. Credit may not be given for portions of best management practices financed by government programs; and

5. The installation, monitoring and maintenance of the best management practices are required by the VPDES permit of the new or expanded significant discharger and the best management practices are installed subsequent to the issuance of the VPDES permit.

F. Any trade or offset involving a new significant discharger must account for the delivery factor that is assigned to the discharger based on its location within the river basin and must recognize that new significant dischargers have no assigned waste load allocations.

To ensure the total basin delivered loads of nitrogen and phosphorus are not exceeded, any trading or offsets conducted in accordance with this section shall use delivered loads.  The following table contains the delivery factors for both nitrogen and phosphorus assigned to the identified Chesapeake Bay Program watershed model segments within each river basin.  A delivered load equals the discharged load multiplied by the delivery factor.

| River Basin | CBP Watershed Model Segment | Nitrogen Delivery Factor | Phosphorus Delivery Factor |
| --- | --- | --- | --- |
| Shenandoah-Potomac | 170 | 0.55 | 0.75 |
| Shenandoah-Potomac | 180 | 0.82 | 0.75 |
| Shenandoah-Potomac | 190 | 0.42 | 0.74 |
| Shenandoah-Potomac | 200 | 0.65 | 0.74 |
| Shenandoah-Potomac | 220 | 0.83 | 0.75 |
| Shenandoah-Potomac | 550 | 0.58 or 1.00* | 0.44 or 1.00* |
| Shenandoah-Potomac | 740 | 0.74 | 0.75 |
| Shenandoah-Potomac | 900 | 1.00 | 1.00 |
| Shenandoah-Potomac | 910 | 1.00 | 1.00 |
| Shenandoah-Potomac | 970 | 1.00 | 1.00 |
| Shenandoah-Potomac | 980 | 1.00 | 1.00 |
| Rappahannock | 230 | 0.61 | 1.03 |
| Rappahannock | 560 | 1.00 | 1.00 |
| Rappahannock | 580 | 1.00 | 1.00 |
| Rappahannock | 930 | 1.00 | 1.00 |
| York | 235 | 0.27 | 0.43 |
| York | 240 | 0.42 | 0.43 |
| York | 250 | 0.02 | 0.58 |
| York | 260 | 0.51 | 0.58 |
| York | 590 | 1.00 | 1.00 |
| York | 940 | 1.00 | 1.00 |
| James | 265 | 0.02 | 1.10 |
| James | 270 | 0.30 | 1.10 |
| James | 280 | 0.61 | 1.10 |
| James | 290 | 0.81 | 1.00 |
| James | 300 | 0.37 | 0.42 |
| James | 310 | 0.54 | 0.39 |
| James | 600 | 1.00 | 1.00 |
| James | 610 | 1.00 | 1.00 |
| James | 620 | 1.00 | 1.00 |
| James | 630 | 1.00 | 1.00 |
| James | 950 | 1.00 | 1.00 |
| James | 955 | 1.00 | 1.00 |
| James | 960 | 1.00 | 1.00 |
| James | 965 | 1.00 | 1.00 |
| C. Bay-Eastern Shore | 430 | 1.00 | 1.00 |
| C. Bay-Eastern Shore | 440 | 1.00 | 1.00 |

NOTE: *Drainage to Occoquan Reservoir - delivery factors = 0.58 for nitrogen; 0.44 for phosphorus.  Drainage outside Occoquan Reservoir - delivery factors = 1.00 for both nitrogen and phosphorus.

B. The nitrogen and phosphorus waste load allocations assigned to individual significant dischargers in 9 VAC 25-720-50 C, 9 VAC 25-720-60 C, 9 VAC 25-720-70 C, 9 VAC 25-720-110 C, and 9 VAC 25-720-120 C are considered to be bioavailable to aquatic life. On a case-by-case basis, a discharger may demonstrate to the satisfaction of the board that a significant portion of the nutrients discharged by the facility is not bioavailable to aquatic life. In these cases, the board may limit the permitted discharge to reflect only that portion of the assigned waste load allocation that is bioavailable. [ Such limits shall be consistent with the assumptions and methods used to derive the allocations through the Chesapeake Bay watershed and water quality models. ]

C. Unless otherwise noted, the nitrogen and phosphorus waste load allocations assigned to individual significant dischargers in 9 VAC 25-720-50 C, 9 VAC 25-720-60 C, 9 VAC 25-720-70 C, 9 VAC 25-720-110 C, and 9 VAC 25-720-120 C are considered total loads including nutrients present in the intake water from the river, as applicable. On a case-by-case basis, an industrial discharger may demonstrate to the satisfaction of the board that a significant portion of the nutrient load originates in its intake water. In these cases, the board may limit the permitted discharge to reflect only the net nutrient load portion of the assigned waste load allocation. [ Such limits shall be consistent with the assumptions and methods used to derive the allocations through the Chesapeake Bay watershed and water quality models.

D. The board may amend this regulation to adjust individual nitrogen and phosphorus waste load allocations.  Reasons for considering such an adjustment include, but are not limited to:

1. A discharger completes or does not complete a plant expansion as evidenced by issuance of a Certificate To Operate by December 31, 2010; or

2. A river basin nutrient load allocation is not achieved.

Any adjustment to an individual waste load allocation must ensure water quality standards are maintained. ]

9 VAC 25-720-50. Potomac, Shenandoah River Basin.

REGISTRAR'S NOTICE:  Subsections A and B are not amended; therefore, the text of those subsections is not set out.

C. Nitrogen and phosphorus waste load allocations to restore the Chesapeake Bay and its tidal rivers.

The following table presents nitrogen and phosphorus waste load allocations for the identified significant dischargers , the associated delivery factors used for trading or offset purposes, and the total nitrogen and total phosphorus delivered waste load allocation allocations for the [ basin listed facilities ].  These individual significant discharger waste load allocations may be revised through the watershed trading program contained in 9 VAC 25-720-30.  The waste load allocation listed below for a discharger, or the waste load allocation revised in accordance with 9 VAC 25-720-30, shall be achieved within four years following reissuance or modification of the discharger's VPDES permit, but in no case later than December 31, 2010.

| CBP Watershed Model Segment | Virginia Waterbody ID | Discharger Name | VPDES Permit No. | Total Nitrogen (TN) Waste Load Allocation (lbs/yr) | TN Delivery Factor | TN Waste Load Delivered Allocation (lbs/yr) | Total Phosphorus (TP) Waste Load Allocation (lbs/yr) | TP Delivery Factor | TP Waste Load Delivered Allocation (lbs/yr) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 190 | B37R | Coors Brewing Company | VA0073245 | 55,000 54,820 | 0.42 | 23,000 | 4,100 4,112 | 0.74 | 3,000 |
| 190 | B14R | Fishersville Regional STP | VA0025291 | 24,000 48,729 | 0.42 | 10,000 | 1,800 3,655 | 0.74 | 1,400 |
| 190 | B32R | INVISTA - Waynesboro (Outfall 101) | VA0002160 | 29,000 78,941 | 0.42 | 12,000 | 1,300 1,009 | 0.74 | 940 |
| 190 | B39R | Luray STP | VA0062642 | 19,000 19,492 | 0.42 | 8,200 | 1,500 1,462 | 0.74 | 1,100 |
| 190 | B35R | Massanutten PSA STP | VA0024732 | 18,000 18,273 | 0.42 | 7,700 | 1,400 1,371 | 0.74 | 1,000 |
| 190 | B37R | Merck - Stonewall WWTP [ (Outfall 101) ] | VA0002178 | 96,000 [ 96,184 14,619 ] | 0.42 | 40,000 | 15,000 [ 15,365 1,096 ] | 0.74 | 11,000 |
| 190 | B12R | Middle River Regional STP | VA0064793 | 83,000 82,839 | 0.42 | 35,000 | 6,200 6,213 | 0.74 | 4,600 |
| 190 | B23R | North River WWTF [ (2) ] | VA0060640 | 190,000 [ 194,916 253,391 ] | 0.42 | 82,000 | 15,000 [ 14,619 19,004 ] | 0.74 | 11,000 |
| 190 | B22R | Pilgrims Pride - VA Poultry Growers -Hinton | VA0002313 | 27,000 27,410 | 0.42 | 12,000 | 1,400 1,371 | 0.74 | 1,000 |
|  | B38R | Pilgrims Pride - Alma | VA0001961 | 18,273 |  |  | 914 |  |  |
| 190 | B31R | Stuarts Draft WWTP | VA0066877 | 29,000 48,729 | 0.42 | 12,000 | 2,200 3,655 | 0.74 | 1,600 |
| 190 | B32R | Waynesboro STP | VA0025151 | 49,000 48,729 | 0.42 | 20,000 | 3,600 3,655 | 0.74 | 2,700 |
| 190 | B23R | Weyers Cave STP | VA0022349 | 6,100 6,091 | 0.42 | 2,600 | 460 457 | 0.74 | 340 |
| 200 | B58R | Berryville STP | VA0020532 | 5,500 8,528 | 0.65 | 3,600 | 410 640 | 0.74 | 300 |
| 200 | B55R | Front Royal STP | VA0062812 | 49,000 48,729 | 0.65 | 32,000 | 3,600 3,655 | 0.74 | 2,700 |
| 200 | B49R | Georges Chicken LLC | VA0077402 | 31,000 31,065 | 0.65 | 20,000 | 1,600 1,553 | 0.74 | 1,100 |
| 200 | B48R | Mt. Jackson STP [ (3) ] | VA0026441 | 7,300 [ 7,309 8,528 ] | 0.65 | 4,800 | 550 [ 548 640 ] | 0.74 | 410 |
| 200 | B45R | New Market STP | VA0022853 | 6,100 6,091 | 0.65 | 4,000 | 460 457 | 0.74 | 340 |
| 200 | B45R | North Fork (SIL) WWTF | VA0090263 | 23,000 23,390 | 0.65 | 15,000 | 1,800 1,754 | 0.74 | 1,300 |
| 200 | B49R | Stoney Creek SD STP | VA0028380 | 7,300 7,309 | 0.65 | 4,800 | 550 548 | 0.74 | 410 |
|  | B50R | North Fork Regional WWTP (1) | VA0090328 | 9,137 |  |  | 685 |  |  |
| 200 | B51R | Strasburg STP | VA0020311 | 12,000 11,939 | 0.65 | 7,800 | 900 895 | 0.74 | 660 |
| 200 | B50R | Woodstock STP | VA0026468 | 9,700 24,364 | 0.65 | 6,300 | 730 1,827 | 0.74 | 540 |
| 220 | A06R | Basham Simms WWTF [ (4) ] | VA0022802 | 12,000 [ 12,182 18,273 ] | 0.83 | 10,000 | 910 [ 914 1,371 ] | 0.75 | 690 |
| 220 | A09R | Broad Run WRF [ (5) ] | VA0091383 | 120,000 [ 121,822 134,005 ] | 0.83 | 100,000 | 3,000 [ 3,046 3,350 ] | 0.75 | 2,300 |
| 220 | A08R | Leesburg WPCF | MD0066184 | 120,000 121,822 | 0.83 | 100,000 | 9,100 9,137 | 0.75 | 6,800 |
| 220 | A06R | Round Hill Town WWTF | VA0026212 | 6,100 9,137 | 0.83 | 5,000 | 460 685 | 0.75 | 340 |
| 550 | A25R | DSC - Section 1 WWTF [ (6) ] | VA0024724 | 36,000 [ 36,547 42,029 ] | 1.00 | 36,000 | 2,200 [ 2,193 2,522 ] | 1.00 | 2,200 |
| 550 | A25R | DSC - Section 8 WWTF [ (7) ] | VA0024678 | 36,000 [ 36,547 42,029 ] | 1.00 | 36,000 | 2,200 [ 2,193 2,522 ] | 1.00 | 2,200 |
| 550 | A25E | H L Mooney WWTF | VA0025101 | 220,000 219,280 | 1.00 | 220,000 | 13,000 13,157 | 1.00 | 13,000 |
| 550 | A22R | UOSA - Centreville | VA0024988 | 1,300,000 1,315,682 | 0.58 | 760,000 | 16,000 16,446 | 0.44 | 7,200 |
| 550 | A19R | Vint Hill WWTF [ (8) ] | VA0020460 | 5,500 [ 5,482 8,680 ] | 0.58 | 3,200 | 550 [ 548 868 ] | 0.44 | 240 |
| 740 | B08R | Opequon WRF | VA0065552 | 100,000 102,336 | 0.74 | 76,000 | 7,700 7,675 | 0.75 | 5,700 |
| 740 | B08R | Parkins Mills STP [ (9) ] | VA0075191 | 26,000 [ 36,547 60,911 ] | 0.74 | 19,000 | 1,900 [ 2,741 4,568 ] | 0.75 | 1,400 |
| 900 | A13E | Alexandria SA WWTF | VA0025160 | 490,000 493,381 | 1.00 | 490,000 | 30,000 29,603 | 1.00 | 30,000 |
| 900 | A12E | Arlington County Water PCF | VA0025143 | 360,000 365,467 | 1.00 | 360,000 | 22,000 21,928 | 1.00 | 22,000 |
| 900 | A16R | Noman M Cole Jr PCF | VA0025364 | 610,000 612,158 | 1.00 | 610,000 | 37,000 36,729 | 1.00 | 37,000 |
| 910 | A12R | Blue Plains (VA Share) | DC0021199 | 580,000 581,458 | 1.00 | 580,000 | 26,000 26,166 | 1.00 | 26,000 |
| 970 | A26R | Quantico WWTF | VA0028363 | 20,000 20,101 | 1.00 | 20,000 | 1,200 1,206 | 1.00 | 1,200 |
| 980 | A28R | Aquia WWTF | VA0060968 | 59,000 73,093 | 1.00 | 59,000 | 3,600 4,386 | 1.00 | 3,600 |
| 980 | A31E | Colonial Beach STP | VA0026409 | 18,000 18,273 | 1.00 | 18,000 | 1,800 1,827 | 1.00 | 1,800 |
| 980 | A30E | Dahlgren WWTF | VA0026514 | 9,100 9,137 | 1.00 | 9,100 | 910 914 | 1.00 | 910 |
| 980 | A29E | Fairview Beach | MD0056464 | 1,800 1,827 | 1.00 | 1,800 | 180 183 | 1.00 | 180 |
| 980 | A30E | US NSWC-Dahlgren WWTF | VA0021067 | 6,600 6,578 | 1.00 | 6,600 | 660 658 | 1.00 | 660 |
|  | A31R | Purkins Corner STP | VA0070106 | 1,096 |  |  | 110 |  |  |
| 980 | A26R | Widewater WWTF | VA0090387 | 4,600 | 1.00 | 4,600 | 270 | 1.00 | 270 |
|  |  | TOTALS: |  | 4,916,700 [ 5,121,242 5,156,169 ] |  | 3,887,100 | 245,200 [ 252,860 246,635 ] |  | 213,130 |

NOTE: (1) Shenandoah Co. - North Fork Regional WWTP waste load allocations (WLAs) based on a design flow capacity of 0.75 million gallons per day (MGD). If plant is not certified to operate at 0.75 MGD design flow capacity by December 31, 2010, the WLAs will be deleted and facility removed from Significant Discharger List.

[ (2) Harrisonburg-Rockingham Regional S.A.-North River STP: waste load allocations (WLAs) based on a design flow capacity of 20.8 million gallons per day (MGD). If plant is not certified to operate at 20.8 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 194,916 lbs/yr; TP = 14,619 lbs/yr, based on a design flow capacity of 16.0 MGD.

(3) Mount Jackson STP: waste load allocations (WLAs) based on a design flow capacity of 0.7 million gallons per day (MGD). If plant is not certified to operate at 0.7 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 7,309 lbs/yr; TP = 548 lbs/yr, based on a design flow capacity of 0.6 MGD.

(4) Purcellville-Basham Simms STP: waste load allocations (WLAs) based on a design flow capacity of 1.5 million gallons per day (MGD). If plant is not certified to operate at 1.5 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 12,182 lbs/yr; TP = 914lbs/yr, based on a design flow capacity of 1.0 MGD.

(5) Loudoun Co. S.A.-Broad Run WRF: waste load allocations (WLAs) based on a design flow capacity of 11.0 million gallons per day (MGD). If plant is not certified to operate at 11.0 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 121,822 lbs/yr; TP = 3,046 lbs/yr, based on a design flow capacity of 10.0 MGD.

(6) Dale Service Corp.-Section 1 WWTF: waste load allocations (WLAs) based on a design flow capacity of 4.6 million gallons per day (MGD). If plant is not certified to operate at 4.6 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 36,547 lbs/yr; TP = 2,193 lbs/yr, based on a design flow capacity of 4.0 MGD.

(7) Dale Service Corp.-Section 8 WWTF: waste load allocations (WLAs) based on a design flow capacity of 4.6 million gallons per day (MGD). If plant is not certified to operate at 4.6 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 36,547 lbs/yr; TP = 2,193 lbs/yr, based on a design flow capacity of 4.0 MGD.

(8) Fauquier Co. W&SA-Vint Hill STP: waste load allocations (WLAs) based on a design flow capacity of 0.95 million gallons per day (MGD). If plant is not certified to operate at 0.95 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 5,482 lbs/yr; TP = 548 lbs/yr, based on a design flow capacity of 0.6 MGD.

(9) Parkins Mill STP: waste load allocations (WLAs) based on a design flow capacity of 5.0 million gallons per day (MGD). If plant is not certified to operate at 5.0 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 36,547 lbs/yr; TP = 2,741 lbs/yr, based on a design flow capacity of 3.0 MGD. ]

9 VAC 25-720-70. Rappahannock River Basin.

REGISTRAR'S NOTICE:  Subsections A and B are not amended; therefore, the text of those subsections is not set out.

C. Nitrogen and phosphorus waste load allocations to restore the Chesapeake Bay and its tidal rivers.

The following table presents nitrogen and phosphorus waste load allocations for the identified significant dischargers , the associated delivery factors used for trading or offset purposes, and the total nitrogen and total phosphorus delivered waste load allocation allocations for the [ basin listed facilities ].  These individual significant discharger waste load allocations may be revised through the watershed trading program contained in 9 VAC 25-720-30.  The waste load allocation listed below for a discharger, or the waste load allocation revised in accordance with 9 VAC 25-720-30, shall be achieved within four years following reissuance or modification of the discharger's VPDES permit, but in no case later than December 31, 2010.

| CBP Watershed Model Segment | Virginia Waterbody ID | Discharger Name | VPDES Permit No. | Total Nitrogen (TN) Waste Load Allocation (lbs/yr) | TN Delivery Factor | TN Waste Load Delivered Allocation (lbs/yr) | Total Phosphorus (TP) Waste Load Allocation (lbs/yr) | TP Delivery Factor | TP Waste Load Delivered Allocation (lbs/yr) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 230 | E09R | Culpeper WWTP (1) | VA0061590 | 55,000 54,820 | 0.61 | 33,000 | 4,100 4,112 | 1.03 | 4,200 |
| 230 | E02R | Marshall WWTP | VA0031763 | 7,800 7,797 | 0.61 | 4,800 | 580 585 | 1.03 | 600 |
|  | E09R | Mountain Run STP [ (2) ] | VA0090212 | [ 18,273 30,456 ] |  |  | [ 1,371 2,284 ] |  |  |
| 230 | E13R | Orange STP | VA0021385 | 18,000 36,547 | 0.61 | 11,000 | 1,400 2,741 | 1.03 | 1,400 |
| 230 | E11R | Rapidan STP | VA0090948 | 7,300 7,309 | 0.61 | 4,400 | 550 548 | 1.03 | 560 |
| 230 | E02R | Remington WWTP [ (3) ] | VA0076805 | 24,000 [ 24,364 30,456 ] | 0.61 | 15,000 | 1,800 [ 1,827 2,284 ] | 1.03 | 1,900 |
| 230 | E02R | South Wales Utility Clevengers Corner STP [ (4) ] | VA0080527 | 11,000 [ 7,309 10,964 ] | 0.61 | 6,700 | 820 [ 548 822 ] | 1.03 | 850 |
| 230 | E02R | Warrenton Town STP | VA0021172 | 30,000 30,456 | 0.61 | 18,000 | 2,300 2,284 | 1.03 | 2,400 |
| 230 | E18R | Wilderness WWTP | VA0083411 | 9,100 15,228 | 0.61 | 5,600 | 680 1,142 | 1.03 | 710 |
| 560 | E20E | FMC WWTF | VA0068110 | 66,000 65,784 | 1.00 | 66,000 | 4,900 4,934 | 1.00 | 4,900 |
| 560 | E20E | Fredericksburg WWTF | VA0025127 | 43,000 42,638 | 1.00 | 43,000 | 3,200 3,198 | 1.00 | 3,200 |
| 560 | E21E | Haymount WWTF [ (5) ] | VA0089125 | 12,000 [ 7,066 11,695 ] | 1.00 | 12,000 | 870 [ 530 877 ] | 1.00 | 870 |
| 560 | E24E | Haynesville CC WWTP | VA0023469 | 2,800 2,802 | 1.00 | 2,800 | 210 | 1.00 | 210 |
|  | E21E | Hopyard Farms STP | VA0089338 | 6,091 |  |  | 457 |  |  |
| 560 | E20E | Little Falls Run WWTF | VA0076392 | 97,000 97,458 | 1.00 | 97,000 | 7,300 7,309 | 1.00 | 7,300 |
| 560 | E20E | Massaponax WWTF | VA0025658 | 97,000 97,458 | 1.00 | 97,000 | 7,300 7,309 | 1.00 | 7,300 |
| 560 | E23R | Montross Westmoreland WWTP | VA0072729 | 1,200 [ 1,218 1,584 ] | 1.00 | 1,200 | [ 91 119 ] | 1.00 | 91 |
|  | E21E | Oakland Park STP | VA0086789 | 1,706 |  |  | 128 |  |  |
| 560 | E23E | Tappahannock WWTP | VA0071471 | 9,700 9,746 | 1.00 | 9,700 | 730 731 | 1.00 | 730 |
| 560 | E26E | Urbanna WWTP | VA0026263 | 1,200 1,218 | 1.00 | 1,200 | 91 | 1.00 | 91 |
| 560 | E21R | US Army - Ft. A P Hill WWTP | VA0032034 | 6,400 6,457 | 1.00 | 6,400 | 480 484 | 1.00 | 480 |
| 560 | E23E | Warsaw Aerated Lagoons | VA0026891 | 3,600 3,655 | 1.00 | 3,600 | 270 274 | 1.00 | 270 |
| 580 | C01E | Omega Protein - Reedville | VA0003867 | 16,000 21,213 | 1.00 | 16,000 | 1,200 1,591 | 1.00 | 1,200 |
| 580 | C01E | Reedville Sanitary District | VA0060712 | 2,400 2,436 | 1.00 | 2,400 | 180 183 | 1.00 | 180 |
| 930 | C01E | Kilmarnock WTP | VA0020788 | 6,100 6,091 | 1.00 | 6,100 | 460 457 | 1.00 | 460 |
|  |  | TOTALS: |  | 526,600 [ 575,140 602,062 ] |  | 462,900 | 39,512 [ 43,135 45,155 ] |  | 39,902 |

NOTE: (1) Town of Culpeper WWTP waste load allocations (WLAs) based on a design flow capacity of 4.5 million gallons per day (MGD). If plant is not certified to operate at 4.5 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 36,547 lbs/yr; TP = 2,741 lbs/yr, based on a design flow capacity of 3.0 MGD.

[ (2) Mountain Run STP: waste load allocations (WLAs) based on a design flow capacity of 2.5 million gallons per day (MGD). If plant is not certified to operate at 2.5 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 18,273 lbs/yr; TP = 1,371 lbs/yr, based on a design flow capacity of 1.5 MGD.

(3) Fauquier Co. W&SA-Remington STP: waste load allocations (WLAs) based on a design flow capacity of 2.5 million gallons per day (MGD). If plant is not certified to operate at 2.5 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 24,364 lbs/yr; TP = 1,827 lbs/yr, based on a design flow capacity of 2.0 MGD.

(4) Clevengers Corner STP: waste load allocations (WLAs) based on a design flow capacity of 0.9 million gallons per day (MGD). If plant is not certified to operate at 0.9 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 7,309 lbs/yr; TP = 548 lbs/yr, based on a design flow capacity of 0.6 MGD.

(5) Haymount STP: waste load allocations (WLAs) based on a design flow capacity of 0.96 million gallons per day (MGD). If plant is not certified to operate at 0.96 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 7,066 lbs/yr; TP = 530 lbs/yr, based on a design flow capacity of 0.58 MGD. ]

9 VAC 25-720-110. Chesapeake Bay - Small Coastal - Eastern Shore River Basin.

REGISTRAR'S NOTICE:  Subsections A and B are not amended; therefore, the text of those subsections is not set out.

C. Nitrogen and phosphorus waste load allocations to restore the Chesapeake Bay and its tidal rivers.

The following table presents nitrogen and phosphorus waste load allocations for the identified significant dischargers , the associated delivery factors used for trading or offset purposes, and the total nitrogen and total phosphorus delivered waste load allocation allocations for the [ basin listed facilities ].  These individual significant discharger waste load allocations may be revised through the watershed trading program contained in 9 VAC 25-720-30.  The waste load allocation listed below for a discharger, or the waste load allocation revised in accordance with 9 VAC 25-720-30, shall be achieved within four years following reissuance or modification of the discharger's VPDES permit, but in no case later than December 31, 2010.

| CBP Watershed Model Segment | Virginia Waterbody ID | Discharger Name | VPDES Permit No. | Total Nitrogen (TN) Waste Load Allocation (lbs/yr) | TN Delivery Factor | TN Waste Load Delivered Allocation (lbs/yr) | Total Phosphorus (TP) Waste Load Allocation (lbs/yr) | TP Delivery Factor | TP Waste Load Delivered Allocation (lbs/yr) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 440 | C16E | Cape Charles Town WWTP [ (1) ] | VA0021288 | 6,100 6,091 | 1.00 | 6,100 | 460 457 | 1.00 | 460 |
| 440 | C11E | Onancock WWTP [ (2) ] | VA0021253 | 3,000 [ 3,046 9,137 ] | 1.00 | 3,000 | [ 230 685 ] | 1.00 | 230 |
| 440 | C13E | Shore Memorial Hospital | VA0027537 | 1,200 1,218 | 1.00 | 1,200 | 91 | 1.00 | 91 |
| 440 | C10E | Tangier WWTP | VA0067423 | 1,200 1,218 | 1.00 | 1,200 | 91 | 1.00 | 91 |
| 440 | C10R | Tyson Foods - Temperanceville | VA0004049 | 20,000 22,842 | 1.00 | 20,000 | 980 | 1.00 | 980 |
|  |  | TOTALS: |  | 31,500 [ 34,415 40,506 ] |  | 31,500 | 1,852 [ 2,010 2,467 ] |  | 1,852 |

[ NOTE: (1) Cape Charles STP: waste load allocations (WLAs) based on a design flow capacity of 0.5 million gallons per day (MGD). If plant is not certified to operate at 0.5 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 3,046 lbs/yr; TP = 228 lbs/yr, based on a design flow capacity of 0.25 MGD.

(2) Onancock STP: waste load allocations (WLAs) based on a design flow capacity of 0.75 million gallons per day (MGD). If plant is not certified to operate at 0.75 MGD design flow capacity by December 31, 2010, the WLAs will decrease to TN = 3,046 lbs/yr; TP = 228 lbs/yr, based on a design flow capacity of 0.25 MGD. ]

VA.R. Doc. No. R04-78; Filed September 28, 2005, 8:11 a.m.