TITLE 12. HEALTH

STATE BOARD OF HEALTH

REGISTRAR'S NOTICE: The following regulatory action is exempt from the Administrative Process Act in accordance with § 2.2-4006 A 4 c of the Code of Virginia, which excludes regulations that are necessary to meet the requirements of federal law or regulations provided such regulations do not differ materially from those required by federal law or regulation. The State Board of Health will receive, consider and respond to petitions by any interested person at any time with respect to reconsideration or revision.

Title of Regulation: 12 VAC 5-590. Waterworks Regulations (amending 12 VAC 5-590-530).

Statutory Authority: §§ 32.1-12 and 32.1-170 of the Code of Virginia.

Effective Date: July 26, 2006.

Agency Contact: Tamara Metzfield, Regulatory Compliance Paralegal, Department of Health, 109 Governor Street, Room 632, Richmond, VA 23219, telephone (804) 864-7499, FAX (804) 864-7520 or e-mail tamara.metzfield@vdh.virginia.gov.

Summary:

The amendment corrects a technical error made by the Virginia Department of Health during the promulgation of the Long Term Enhanced Surface Water Treatment Rule. Stage 1 requires a waterworks to provide the dates that self-assessment was triggered and completed, while the current Waterworks Regulations, as amended (effective April 6, 2005), state that the self-assessment be submitted only.

12 VAC 5-590-530. Reporting.

A. The results of any required monitoring activity shall be reported by the waterworks owner to the appropriate field office no later than the 10th day of the month following the month during which the tests were taken.

1. Waterworks required to sample quarterly must report to the appropriate field office within 10 days after the end of each quarter in which samples were collected.

2. Waterworks required to sample less frequently than quarterly must report to the appropriate field office within 10 days after the end of each monitoring period in which samples were collected.

B. It shall be the duty and responsibility of an owner to report to the appropriate field office in the most expeditious manner (usually by telephone) under the following circumstances.  If it is done by telephone a confirming report shall be mailed as soon as practical.

1. When a bacteriological examination shows a repeat sample is required (see 12 VAC 5-590-380 D), a report shall be made within 48 hours.  A waterworks owner must report a total coliform PMCL violation to the appropriate field office no later than the end of the next business day.

2. When the daily average of turbidity testing exceeds 5 NTU a report shall be made within 48 hours.

3. When a Primary Maximum Contaminant Level of an inorganic or organic chemical is exceeded for a single sample the owner shall report same within seven days.  If any one sample result would cause the compliance average to be exceeded the owner shall report same in 48 hours.

4. When the average value of samples collected pursuant to 12 VAC 5-590-410 exceeds the Primary Maximum Contaminant Level of any organic or inorganic chemical the owner shall report same within 48 hours.

5. When the maximum contaminant level for radionuclides has been exceeded as determined by Table 2.5 the results shall be reported within 48 hours.

6. The waterworks owner shall report to the appropriate field office within 48 hours the failure to comply with the monitoring and sanitary survey requirements of this chapter.

7. The waterworks owner shall report to the appropriate field office within 48 hours the failure to comply with the requirements of any schedule prescribed pursuant to a variance or exemption.

8. The waterworks owner shall report a Tier 1 violation or situation, as described in 12 VAC 5-590-540 A 1, to the appropriate field office as soon as practical, but no later than 24 hours after the waterworks learns of the Tier 1 violation or situation.  At the same time the report is made, the owner shall consult with the field office to determine the need for any additional actions to address the violation or situation.

9. The waterworks owner shall report a violation of treatment technique requirement resulting from a single exceedance of the maximum allowable turbidity limit, as described in 12 VAC 5-590-420 B 2 a (2), B 2 a (3) (b), B 2 b (2), B 2 c (2), and B 2 d, to the appropriate field office as soon as practical, but no later than 24 hours after the waterworks learns of the violation.  At the same time the report is made, the owner shall consult with the field office to determine the need for any additional actions to address the violation or situation.

C. Reporting requirements for filtration treatment and disinfection treatment.

1. The owner of a waterworks that provides filtration treatment shall report monthly to the division the following specified information beginning June 29, 1993, or when filtration is installed, whichever is later.

a. Turbidity measurements as required by 12 VAC 5-590-370 B 7 a shall be reported within 10 days after the end of each month the waterworks serves water to the public.  Information that shall be reported includes:

(1) The total number of filtered water turbidity measurements taken during the month.

(2) The number and percentage of filtered water turbidity measurements taken during the month which are less than or equal to the turbidity limits specified in 12 VAC 5-590-420 B 2 for the filtration technology being used.

(3) The date and value of any turbidity measurements taken during the month which exceed 5 NTU.

b. A waterworks using surface water or groundwater under the direct influence of surface water that provides conventional filtration treatment or direct filtration must report monthly to the commissioner the information specified in subdivisions C 1 a (1) and (2) of this section beginning January 1, 2002, for waterworks serving at least 10,000 people or January 1, 2005, for waterworks serving less than 10,000 people.  Also, a waterworks that provides filtration approved under 12 VAC 5-590-420 B 2 d must report monthly to the commissioner the information specified in subdivision C 1 a (1) of this section beginning January 1, 2002, for waterworks serving at least 10,000 people or January 1, 2005, for waterworks serving less than 10,000 people.

(1) Turbidity measurements as required by 12 VAC 5-590-420 B 2 a (3) must be reported within 10 days after the end of each month the system serves water to the public.  Information that must be reported includes:

(a) The total number of filtered water turbidity measurements taken during the month.

(b) The number and percentage of filtered water turbidity measurements taken during the month that are less than or equal to the turbidity limits specified in 12 VAC 5-590-420 B 2 a (3) or 12 VAC 5-590-420 B 2 d.

(c) The date and value of any turbidity measurements taken during the month that exceed 1 NTU for systems using conventional filtration treatment or direct filtration, or that exceed the maximum level set by the commissioner under 12 VAC 590-420 B 2 d.

(2) Waterworks must maintain the results of individual filter monitoring taken under 12 VAC 5-590-370 B 7 b (1) for at least three years.  Waterworks must report that they have conducted individual filter turbidity monitoring under 12 VAC 5-590-370 B 7 b (1) within 10 days after the end of each month the waterworks system serves water to the public.  Waterworks must report individual filter turbidity measurement results taken under 12 VAC 5-590-370 B 7 b (1) within 10 days after the end of each month the waterworks serves water to the public only if measurements demonstrate one or more of the conditions in subdivisions C 1 b (2) (a) or (b) of this section.  Waterworks that use lime softening may apply to the commissioner for alternative exceedance levels for the levels specified in subdivisions C 1 b (2) (a) or (b) of this section if they can demonstrate that higher turbidity levels in individual filters are due to lime carryover only and not due to degraded filter performance.

(a) For waterworks serving 10,000 or more people:

(i) For any individual filter that has a measured turbidity level of greater than 1.0 NTU in two consecutive measurements taken 15 minutes apart, the waterworks must report the filter number, the turbidity measurement, and the date, or dates, on which the exceedance occurred.  In addition, the waterworks must either produce a filter profile for the filter within seven days of the exceedance (if the waterworks is not able to identify an obvious reason for the abnormal filter performance) and report that the profile has been produced or report the obvious reason for the exceedance.

(ii) For any individual filter that has a measured turbidity level of greater than 0.5 NTU in two consecutive measurements taken 15 minutes apart at the end of the first four hours of continuous filter operation after the filter has been backwashed or otherwise taken offline, the waterworks must report the filter number, the turbidity, and the date, or dates, on which the exceedance occurred.  In addition, the waterworks must either produce a filter profile for the filter within seven days of the exceedance (if the waterworks is not able to identify an obvious reason for the abnormal filter performance) and report that the profile has been produced or report the obvious reason for the exceedance.

(iii) For any individual filter that has a measured turbidity level of greater than 1.0 NTU in two consecutive measurements taken 15 minutes apart at any time in each of three consecutive months, the waterworks must report the filter number, the turbidity measurement, and the date, or dates, on which the exceedance occurred.  In addition, the waterworks must conduct a self-assessment of the filter within 14 days of the exceedance and report that the self-assessment was conducted.  The self-assessment must consist of at least the following components: assessment of filter performance; development of a filter profile; identification and prioritization of factors limiting filter performance;  assessment of the applicability of corrections; and preparation of a filter self-assessment report.

(iv) For any individual filter that has a measured turbidity level of greater than 2.0 NTU in two consecutive measurements taken 15 minutes apart at any time in each of two consecutive months, the waterworks must report the filter number, the turbidity measurement, and the date, or dates, on which the exceedance occurred.  In addition, the waterworks must arrange for the conduct of a comprehensive performance evaluation by the commissioner or a third party approved by the commissioner no later than 30 days following the exceedance and have the evaluation completed and submitted to the commissioner no later than 90 days following the exceedance.

(b) For waterworks serving less than 10,000 people:

(i) For any individual filter (or the turbidity of combined filter effluent for systems with two filters that monitor combined filter effluent in lieu of individual filters) that has a measured turbidity level of greater than 1.0 NTU in two consecutive measurements taken 15 minutes apart, the waterworks must report the filter number(s), the turbidity measurement(s), and the date, or dates, on which the exceedance occurred and the cause (if known) for the exceedance(s).

(ii) For any individual filter (or the turbidity of combined filter effluent for systems with two filters that monitor combined filter effluent in lieu of individual filters) that has a measured turbidity level of greater than 1.0 NTU in two consecutive measurements taken 15 minutes apart at any time in each of three consecutive months, the waterworks must conduct a self-assessment of the filter(s) within 14 days of the day the filter exceeded 1.0 NTU unless a comprehensive performance evaluation as specified in paragraph (iii) of this section was required.  Waterworks with two filters that monitor the combined filter effluent in lieu of individual filters must conduct a self assessment on both filters.  The self-assessment must be reported to the commissioner and consist of at least the following components: date self-assessment was triggered, date the self-assessment was completed, assessment of filter performance;  development of a filter profile; identification and prioritization of factors limiting filter performance; assessment of the applicability of corrections;  and preparation of a filter self-assessment report.  The self assessment must be submitted within 10 days after the end of the month or 14 days after the self assessment was triggered only if it was triggered during the last four days of the month.

(iii) For any individual filter (or the turbidity of combined filter effluent for systems with two filters that monitor combined filter effluent in lieu of individual filters) that has a measured turbidity level of greater than 2.0 NTU in two consecutive measurements taken 15 minutes apart at any time in each of two consecutive months, the waterworks must arrange for a comprehensive performance evaluation by the commissioner or a third party approved by the commissioner no later than 60 days following the day the filter exceeded 2.0 NTU in two consecutive months.  The waterworks must report within 10 days after the end of the month that a comprehensive performance evaluation is required and the date that it was triggered.  If a comprehensive performance evaluation has been completed by the commissioner or a third party approved by the commissioner within the 12 prior months or the waterworks and the commissioner are jointly participating in an ongoing Comprehensive Technical Assistance project at the waterworks, a new comprehensive performance evaluation is not required.  If conducted, a comprehensive performance evaluation must be completed and submitted to the commissioner no later than 120 days following the day the filter exceeded 2.0 NTU in two consecutive measurements for the second straight month.

2. Disinfection information specified below shall be reported to the division within 10 days after the end of each month the waterworks serves water to the public.  Information that shall be reported includes:

a. For each day, the lowest measurement of residual disinfectant concentration in mg/l in water entering the distribution system.

b. The date and duration of each period when the residual disinfectant concentration in water entering the distribution system fell below 0.2 mg/l and when the division was notified of the occurrence.

c. The following information on the samples taken in the distribution system in conjunction with total coliform monitoring pursuant to 12 VAC 5-590-420 B.

(1) Number of instances where the residual disinfectant concentration is measured;

(2) Number of instances where the residual disinfectant concentration is not measured but HPC is measured;

(3) Number of instances where the residual disinfectant concentration is measured but not detected and no HPC is measured;

(4) Number of instances where no residual disinfectant concentration is detected and where HPC is greater than 500/mL;

(5) Number of instances where the residual disinfectant concentration is not measured and HPC is greater than 500/mL;

(6) For the current and previous month the system serves water to the public, the value of "V" in percent in the following formula:

V =       c + d + e        x 100

--------------------

a + b

a = the value in subdivision C 2 c (1) of this section

b = the value in subdivision C 2 c (2) of this section

c = the value in subdivision C 2 c (3) of this section

d = the value in subdivision C 2 c (4) of this section

e = the value in subdivision C 2 c (5) of this section

(7) If the division determines, based on site specific considerations, that a waterworks owner has no means for having a sample transported and analyzed for HPC by a certified laboratory within the requisite time and temperature conditions and that the waterworks is providing adequate disinfection in the distribution system, the requirements of subdivision C 2 c (1) through (6) of this section do not apply.

d. A waterworks owner need not report the data listed in subdivision C 2 a of this section if all data listed in subdivisions C 2 a through c of this section remain on file at the waterworks and the division determines that the waterworks owner has submitted all of the information required by subdivisions C 2 a through c of this section for the last 12 months.

3. If at any time the chlorine residual falls below 0.2 mg/l in the water entering the distribution system, the waterworks owner shall notify the division as soon as possible, but no later than by the end of the next business day.  The waterworks owner also shall notify the division by the end of the next business day whether or not the residual was restored to at least 0.2 mg/l within four hours.

D. Reporting requirements for lead and copper.  All waterworks owners shall report all of the following information to the appropriate field office in accordance with this section.

1. Reporting requirements for tap water monitoring for lead and copper and for water quality parameter monitoring.

a. A waterworks owner shall report the information specified below for all tap water samples within the first 10 days following the end of each applicable monitoring period specified in 12 VAC 5-590-370 B 6 a, b and c (i.e., every six months, annually, or every three years).

(1) The results of all tap samples for lead and copper including location or a location site code and the criteria under 12 VAC 5-590-370 B 6 a (1) (c), (d), (e), (f) and/or (g) under which the site was selected for the waterworks' sampling pool;

(2) A certification that each first draw sample collected by the waterworks is one-liter in volume and, to the best of their knowledge, has stood motionless in the service line, or in the interior plumbing of a sampling site, for at least six hours;

(3) Where residents collected samples, a certification that each tap sample collected by the residents was taken after the waterworks owner informed them of proper sampling procedures specified in 12 VAC 5-590-370 B 6 a (2) (b);

(4) The 90th percentile lead and copper concentrations measured from among all lead and copper tap water samples collected during each monitoring period (calculated in accordance with 12 VAC 5-590-410 E 3);

(5) With the exception of initial tap sampling conducted pursuant to 12 VAC 5-590-370 B 6 a (4) (a), the waterworks owner shall designate any site which was not sampled during previous monitoring periods, and include an explanation of why sampling sites have changed;

(6) The results of all tap samples for pH, and where applicable, alkalinity, calcium, conductivity, temperature, and orthophosphate or silica collected under 12 VAC 5-590-370 B 6 b (2) through (5);

(7) The results of all samples collected at the entry point(s) to the distribution system for applicable water quality parameters under 12 VAC 5-590-370 B 6 b (2) through (5).

b. By the applicable date in 12 VAC 5-590-370 B 6 a (4) (a) for commencement of monitoring, the owner of each community waterworks which does not complete the targeted sampling pool with tier 1 sampling sites meeting the criteria in 12 VAC 5-590-370 B 6 a (1) (c) shall send a letter to the appropriate field office justifying the selection of tier 2 and/or tier 3 sampling sites under 12 VAC 5-590-370 B 6 a (1) (d) and/or (e).

c. By the applicable date in 12 VAC 5-590-370 B 6 a (4) (a) for commencement of monitoring, the owner of each nontransient, noncommunity waterworks which does not complete the sampling pool with tier 1 sampling sites meeting the criteria in 12 VAC 5-590-370 B 6 a (1) (f) shall send a letter to the appropriate field office justifying the selection of sampling sites under 12 VAC 5-590-370 B 6 a (1) (g).

d. By the applicable date in 12 VAC 5-590-370 B 6 a (4) (a) for commencement of monitoring, the owner of each waterworks with lead service lines that is not able to locate the number of sites served by such lines required under 12 VAC 5-590-370 B 6 a (1) (b) (i) shall send a letter to the appropriate field office demonstrating why the owner was unable to locate a sufficient number of such sites based upon the information listed in 12 VAC 5-590-370 B 6 a (1) (b).

e. Each waterworks owner who requests that the commissioner reduce the number and frequency of sampling shall provide the information required under 12 VAC 5-590-370 B 6 a (4) (d).

2. Water supply (source water) monitoring reporting requirements.

a. A waterworks owner shall report the sampling results for all source water samples collected in accordance with 12 VAC 5-590-370 B 6 c within the first 10 days following the end of each source water monitoring period (i.e., annually, per compliance period, per compliance cycle) specified in 12 VAC 5-590-370 B 6 c.

b. With the exception of the first round of source water sampling conducted pursuant to 12 VAC 5-590-370 B 6 c (2), the waterworks owner shall specify any site which was not sampled during previous monitoring periods, and include an explanation of why the sampling point has changed.

3. Corrosion control treatment reporting requirements.  By the applicable dates under 12 VAC 5-590-420 C 2, waterworks owners shall report the following information:

a. For waterworks demonstrating that they have already optimized corrosion control, information required in 12 VAC 5-590-420 C 2 b (2) or (3).

b. For waterworks required to optimize corrosion control, the owner's recommendation regarding optimal corrosion control treatment under 12 VAC 5-590-420 C 1 a.

c. For waterworks required to evaluate the effectiveness of corrosion control treatments under 12 VAC 5-590-420 C 1 c, the information required by that subdivision.

d. For waterworks required to install optimal corrosion control designated by the commissioner under 12 VAC 5-590-420 C 1 d (1), a letter certifying that the owner has completed installing that treatment.

4. Water supply source water treatment reporting requirements.  By the applicable dates in 12 VAC 5-590-420 D, waterworks owners shall provide the following information to the appropriate field office:

a. If required under 12 VAC 5-590-420 D 2 a, the owner's recommendation regarding source water treatment;

b. For waterworks required to install source water treatment under 12 VAC 5-590-420 D 2 b, a letter certifying that the waterworks has completed installing the treatment designated by the commissioner within 24 months after the commissioner designated the treatment.

5. Lead service line replacement reporting requirements.  Waterworks owners shall report the following information to the appropriate field office to demonstrate compliance with the requirements of 12 VAC 5-590-420 E:

a. Within 12 months after a waterworks exceeds the lead action level in sampling referred to in 12 VAC 5-590-420 E 1, the owner shall demonstrate in writing to the appropriate field office that the owner has conducted a materials evaluation, including the evaluation in 12 VAC 5-590-370 B 6 a (1), to identify the initial number of lead service lines in the distribution system, and shall provide the appropriate field office with the waterworks' schedule for replacing annually at least 7.0% of the initial number of lead service lines in its distribution system.

b. Within 12 months after a waterworks exceeds the lead action level in sampling referred to in 12 VAC 5-590-420 E 1, and every 12 months thereafter, the waterworks owner shall demonstrate to the appropriate field office in writing that the waterworks owner has either:

(1) Replaced in the previous 12 months at least 7.0% of the initial lead service lines (or a greater number of lines specified by the commissioner under 12 VAC 5-590-420 E 6) in the distribution system, or

(2) Conducted sampling which demonstrates that the lead concentration in all service line samples from an individual line(s), taken pursuant to 12 VAC 5-590-370 B 6 a (7) (c), is less than or equal to 0.015 mg/l.  In such cases, the total number of lines replaced and/or which meet the criteria in 12 VAC 5-590-420 E 3 shall equal at least 7.0% of the initial number of lead lines identified under subdivision D 5 a of this section (or the percentage specified by the commissioner under 12 VAC 5-590-420 E 6).

c. The annual letter submitted to the appropriate field office under subdivision D 5 b of this section shall contain the following information:

(1) The number of lead service lines scheduled to be replaced during the previous year of the waterworks' replacement schedule;

(2) The number and location of each lead service line replaced during the previous year of the waterworks' replacement schedule;

(3) If measured, the water lead concentration and location of each lead service line sampled, the sampling method, and the date of sampling.

d. As soon as practicable, but in no case later than three months after a waterworks exceeds the lead action level in sampling referred to in 12 VAC 5-590-420 E 1, any waterworks owner seeking to rebut the presumption that it has control over the entire lead service line pursuant to 12 VAC 5-590-420 E 4 shall submit a letter to the appropriate field office describing the legal authority (e.g., state statutes, municipal ordinances, public service contracts or other applicable legal authority) which limits the waterworks owner's control over the service lines and the extent of the waterworks owner's control.

6. Public education program reporting requirements.  By December 31st of each year, the owner of any waterworks that is subject to the public education requirements in 12 VAC 5-590-420 F shall submit a letter to the appropriate field office demonstrating that the waterworks owner has delivered the public education materials that meet the content requirements in 12 VAC 5-590-420 F 1 and 2 and the delivery requirements in 12 VAC 5-590-420 F 3.  This information shall include a list of all the newspapers, radio stations, television stations, facilities and organizations to which the owner delivered public education materials during the previous year.  The owner shall submit the letter required by this subdivision annually for as long as it exceeds the lead action level.

7. Reporting of additional monitoring data.  The owner of any waterworks which collects sampling data in addition to that required by this subpart shall report the results to the appropriate field office within the first 10 days following the end of the applicable monitoring period under 12 VAC 5-590-370 B 6 a, b and c during which the samples are collected.

E. Reporting requirements for disinfection byproducts.  Waterworks must report the following information in accordance with subsection A of this section.  (The field office may choose to perform calculations and determine whether the PMCL was violated, in lieu of having the waterworks report that information):

1. A waterworks monitoring for TTHM and HAA5 under the requirements of 12 VAC 5-590-370 B 3 a on a quarterly or more frequent basis must report:

a. The number of samples taken during the last quarter.

b. The location, date, and result of each sample taken during the last quarter.

c. The arithmetic average of all samples taken in the last quarter.

d. The annual arithmetic average of the quarterly arithmetic averages of this section for the last four quarters.

e. Whether, based on 12 VAC 5-590-410 C 2 b, the PMCL was violated.

2. A waterworks monitoring for TTHMs and HAA5 under the requirements of 12 VAC 5-590-370 B 3 a less frequently than quarterly (but at least annually) must report:

a. The number of samples taken during the last year.

b. The location, date, and result of each sample taken during the last monitoring period.

c. The arithmetic average of all samples taken over the last year.

d. Whether, based on 12 VAC 5-590-410 C 2 b the PMCL was violated.

3. A waterworks monitoring for TTHMs and HAA5 under the requirements of 12 VAC 5-590-370 B 3 a less frequently than annually must report:

a. The location, date, and result of the last sample taken.

b. Whether, based on 12 VAC 5-590-410 C 2 b, the PMCL was violated.

4. A waterworks monitoring for chlorite under the requirements of 12 VAC 5-590-370 B 3 f must report:

a. The number of entry point samples taken each month for the last three months.

b. The location, date, and result of each sample (both entry point and distribution system) taken during the last quarter.

c. For each month in the reporting period, the arithmetic average of all samples taken in each three sample set taken in the distribution system.

d. Whether, based on 12 VAC 5-590-410 C 2 b, the PMCL was violated, in which month and how many times it was violated each month.

5. A waterworks monitoring for bromate under the requirements of 12 VAC 5-590-370 B 3 g must report:

a. The number of samples taken during the last quarter.

b. The location, date, and result of each sample taken during the last quarter.

c. The arithmetic average of the monthly arithmetic averages of all samples taken in the last year.

d. Whether, based on 12 VAC 5-590-410 C 2 b, the PMCL was violated.

F. Reporting requirements for disinfectants.  Waterworks must report the information specified below in accordance with subsection A of this section.  (The field office may choose to perform calculations and determine whether the MRDL was violated, in lieu of having the waterworks report that information):

1. A waterworks monitoring for chlorine or chloramines under the requirements of 12 VAC 5-590-370 B 3 h must report:

a. The number of samples taken during each month of the last quarter.

b. The monthly arithmetic average of all samples taken in each month for the last 12 months.

c. The arithmetic average of all monthly averages for the last 12 months.

d. Whether, based on 12 VAC 5-590-410 C 2 c, the MRDL was violated.

2. A waterworks monitoring for chlorine dioxide under the requirements of 12 VAC 5-590-370 B 3 h must report:

a. The dates, results, and locations of samples taken during the last quarter.

b. Whether, based on 12 VAC 5-590-410 C 2 c, the MRDL was violated.

c. Whether the MRDL was exceeded in any two consecutive daily samples and whether the resulting violation was acute or nonacute.

G. Reporting requirements for disinfection byproduct precursors and enhanced coagulation or enhanced softening.  Waterworks must report the following information in accordance with subsection A of this section.  (The field office may choose to perform calculations and determine whether the treatment technique was met, in lieu of having the waterworks report that information):

1. A waterworks monitoring monthly or quarterly for TOC under the requirements of 12 VAC 5-590-370 B 3 i and required to meet the enhanced coagulation or enhanced softening requirements in 12 VAC 5-590-420 H 2 b or c must report:

a. The number of paired (source water and treated water) samples taken during the last quarter.

b. The location, date, and results of each paired sample and associated alkalinity taken during the last quarter.

c. For each month in the reporting period that paired samples were taken, the arithmetic average of the percent reduction of TOC for each paired sample and the required TOC percent removal.

d. Calculations for determining compliance with the TOC percent removal requirements, as provided in 12 VAC 5-590-420 H 3 a.

e. Whether the system is in compliance with the enhanced coagulation or enhanced softening percent removal requirements in 12 VAC 5-590-420 H 2 a for the last four quarters.

2. A waterworks monitoring monthly or quarterly for TOC under the requirements of 12 VAC 5-590-370 B 3 i and meeting one or more of the alternative compliance criteria in 12 VAC 5-590-420 H 1 b or c must report:

a. The alternative compliance criterion that the system is using.

b. The number of paired samples taken during the last quarter.

c. The location, date, and result of each paired sample and associated alkalinity taken during the last quarter.

d. The running annual arithmetic average based on monthly averages (or quarterly samples) of source water TOC for systems meeting a criterion in 12 VAC 5-590-420 H 1 b (1) or (3) or of treated water TOC for systems meeting the criterion in 12 VAC 5-590-420 H 1 b (2).

e. The running annual arithmetic average based on monthly averages (or quarterly samples) of source water SUVA for systems meeting the criterion in 12 VAC 5-590-420 H 1 b (5) or of treated water SUVA for systems meeting the criterion in 12 VAC 5-590-420 H 1 b (6).

f. The running annual average of source water alkalinity for systems meeting the criterion in 12 VAC 5-590-420 H 1 b (3) and of treated water alkalinity for systems meeting the criterion in 12 VAC 5-590-420 H 1 c (1).

g. The running annual average for both TTHM and HAA5 for systems meeting the criterion in 12 VAC 5-590-420 H 1 b (3) or (4).

h. The running annual average of the amount of magnesium hardness removal (as CaCO sub3, in mg/l) for systems meeting the criterion in 12 VAC 5-590-420 H 1 c (2).

i. Whether the system is in compliance with the particular alternative compliance criterion in 12 VAC 5-590-420 H 1 b or c.

H. Reporting of analytical results to the appropriate field office will not be required in instances where the state laboratory performs the analysis and reports same to that office.

I. Recycle flow reporting requirements.  Any waterworks supplied by a surface water source and waterworks supplied by a groundwater source under the direct influence of surface water that employ conventional filtration or direct filtration treatment must notify the state in writing by December 8, 2003, if the system recycles spent filter backwash water, thickener supernatant, or liquids from dewatering processes.  This notification must include, as a minimum:

1. A plant schematic showing the origin of all flows that are recycled, including but not limited to spent filter backwash water, thickener supernatant, and liquids from dewatering processes.  The schematic shall also specify the hydraulic conveyance used to transport all recycle flows and the location where recycle flows are reintroduced back into the treatment plant.

2. Typical recycle flow in gallons per minute (gpm), the highest observed plant flow experienced in the previous year (gpm), design flow for the treatment plant (gpm), and state-approved operating capacity for the plant.

J. Information to be included on the operation monthly report shall be determined by the division for each waterworks on an individual basis.  Appendix G contains suggested monthly operation report requirements.

VA.R. Doc. No. R06-255; Filed June 5, 2006, 2:27 p.m.