TITLE 12. HEALTH

STATE BOARD OF HEALTH

REGISTRAR'S NOTICE: The following regulatory action is exempt from the Administrative Process Act in accordance with § 2.2-4006 A 4 c of the Code of Virginia, which excludes regulations that are necessary to meet the requirements of federal law or regulations provided such regulations do not differ materially from those required by federal law or regulation. The State Board of Health will receive, consider and respond to petitions by any interested person at any time with respect to reconsideration or revision.

Title of Regulation: 12 VAC 5-590. Waterworks Regulations (amending 12 VAC 5-590-10, 12 VAC 5-590-370, 12 VAC 5-590-410, 12 VAC 5-590-440, 12 VAC 5-590-545, and 12 VAC 5-590-820, and Appendix N).

Statutory Authority: §§ 32.1-12 and 32.1-170 of the Code of Virginia.

Effective Date: September 6, 2006.

Agency Contact: Tamara Metzfield, Regulatory Compliance Paralegal, Department of Health, 109 Governor Street, Room 632, Richmond, VA 23219, telephone (804) 864-7499, FAX (804) 864-7521 or e-mail tamara.metzfield@vdh.virginia.gov.

Summary:

The amendments conform the regulation to 40 CFR Parts 9, 141 and 142 – found in the National Primary Drinking Water Regulations; Arsenic and Clarifications to Compliance and New Source Contaminants Monitoring; Final Rule dated January 22, 2001.

The amendments (i) add new definitions and clarify existing definitions; (ii) add new requirements and clarify existing requirements for monitoring and testing; (iii) update and clarify existing requirements for determining compliance; (iv) update and clarify existing requirements and add new requirements for analytical methods; (v) update and clarify consumer confidence report requirements; (vi) add data on the best available technologies/treatment techniques for arsenic; and (vii) clarify consumer confidence report and public notification requirements.

12 VAC 5-590-10. Definitions.

As used in this chapter, the following words and terms shall have meanings respectively set forth unless the context clearly requires a different meaning:

"Action level" means the concentration of lead or copper in water specified in 12 VAC 5-590-410 E, which determines, in some cases, the treatment requirements contained in 12 VAC 5-590-420 C, D, E and F that a waterworks is required to complete.

"Air gap separation" means the unobstructed vertical distance through the free atmosphere between the lowest opening from any pipe or faucet supplying pure water to a tank, plumbing fixture, or other device and the rim of the receptacle.

"Annual daily water demand" means the average rate of daily water usage over at least the most recent three-year period.

"Applied water" means water that is ready for filtration.

"Approved" means material, equipment, workmanship, process or method that has been accepted by the division as suitable for the proposed use.

"Auxiliary water system" means any water system on or available to the premises other than the waterworks.  These auxiliary waters may include water from a source such as wells, lakes, or streams; or process fluids; or used water.  They may be polluted or contaminated or objectionable, or constitute an unapproved water source or system over which the water purveyor does not have control.

"Backflow" means the flow of water or other liquids, mixtures, or substances into the distribution piping of a waterworks from any source or sources other than its intended source.

"Backflow prevention device" means any approved device, method, or type of construction intended to prevent backflow into a waterworks.

"Best available technology (BAT)" means the best technology, treatment techniques, or other means which the commissioner finds, after examination for efficacy under field conditions and not solely under laboratory conditions and in conformance with applicable EPA regulations, are available (taking cost into consideration).

"Board" means the State Board of Health.

"Breakpoint chlorination" means the addition of chlorine to water until the chlorine demand has been satisfied and further additions result in a residual that is directly proportional to the amount added.

"Chlorine" means dry chlorine.

"Chlorine gas" means dry chlorine in the gaseous state.

"Chlorine solution (chlorine water)" means a solution of chlorine in water.  Note:  the term chlorine solution is sometimes used to describe hypochlorite solutions.  This use of the term is incorrect.

"Coagulation" means a process using coagulant chemicals and mixing by which colloidal and suspended materials are destabilized and agglomerated into flocs.

"Coliform bacteria group" means a group of bacteria predominantly inhabiting the intestines of man or animal but also occasionally found elsewhere.  It includes all aerobic and facultative anaerobic, gram-negative, non-sporeforming bacilli that ferment lactose with production of gas.  Also included are all bacteria that produce a dark, purplish-green colony with metallic sheen by the membrane filter technique used for coliform identification.

"Commissioner" means the State Health Commissioner.

"Community water system waterworks" means a waterworks which serves at least 15 service connections used by year-round residents or regularly serves at least 25 year-round residents.

"Compliance cycle" means the nine-year calendar year cycle during which a waterworks must monitor.  Each compliance cycle consists of three three-year compliance periods.  The first calendar year cycle begins January 1, 1993, and ends December 31, 2001; the second begins January 1, 2002, and ends December 31, 2010; the third begins January 1, 2011, and ends December 31, 2019.

"Compliance period" means a three-year calendar year period within a compliance cycle.  Each compliance cycle has three three-year compliance periods.  Within the first compliance cycle, the first compliance period runs from January 1, 1993, to December 31, 1995; the second from January 1, 1996, to December 31, 1998; the third from January 1, 1999, to December 31, 2001.

"Comprehensive performance evaluation" (CPE) is a thorough review and analysis of a treatment plant's performance-based capabilities and associated administrative, operational and maintenance practices.  It is conducted to identify factors that may be adversely impacting a plant's capability to achieve compliance and emphasizes approaches that can be implemented without significant capital improvements.  For purposes of compliance with 12 VAC 5-590-530 C 1 b (2), the comprehensive performance evaluation must consist of at least the following components:  assessment of plant performance; evaluation of major unit processes; identification and prioritization of performance limiting factors; assessment of the applicability of comprehensive technical assistance; and preparation of a CPE report.

"Confluent growth" means a continuous bacterial growth covering the entire filtration area of a membrane filter, or a portion thereof, in which bacterial colonies are not discrete.

"Consecutive waterworks" means a waterworks which has no water production or source facility of its own and which obtains all of its water from another permitted waterworks.

"Consumer" means any person who drinks water from a waterworks.

"Consumer's water system" means any water system located on the consumer's premises, supplied by or in any manner connected to a waterworks.

"Contaminant" means any objectionable or hazardous physical, chemical, biological, or radiological substance or matter in water.

"Conventional filtration treatment" means a series of processes including coagulation, flocculation, sedimentation, and filtration resulting in substantial particulate removal.

"Corrosion inhibitor" means a substance capable of reducing the corrosivity of water toward metal plumbing materials, especially lead and copper, by forming a protective film on the interior surface of those materials.

"Cross connection" means any connection or structural arrangement, direct or indirect, to the waterworks whereby backflow can occur.

"CT" or "CTcalc " means the product of "residual disinfectant concentration" (C) in mg/L determined before or at the first customer, and the corresponding "disinfectant contact time" (T) in minutes, i.e., "C" x "T."

"Daily fluid intake" means the daily intake of water for drinking and culinary use and is defined as two liters.

"Dechlorination" means the partial or complete reduction of residual chlorine in water by any chemical or physical process at a waterworks with a treatment facility.

"Degree of hazard" means the level of health hazard, as derived from an evaluation of the potential risk to health and the adverse effect upon the waterworks.

"Diatomaceous earth filtration" means a process resulting in substantial particulate removal in which (i) a precoat cake of diatomaceous earth filter media is deposited on a support membrane (septum), and (ii) while the water is filtered by passing through the cake on the septum, additional filter media known as body feed is continuously added to the feed water to maintain the permeability of the filter cake.

"Direct filtration" means a series of processes including coagulation and filtration but excluding sedimentation resulting in substantial particulate removal.

"Disinfectant" means any oxidant (including chlorine) that is added to water in any part of the treatment or distribution process for the purpose of killing or deactivating pathogenic organisms.

"Disinfectant contact time ("T" in CT calculations)" means the time in minutes that it takes for water to move from the point of disinfectant application to the point where residual disinfectant concentration ("C") is measured.

"Disinfection" means a process which inactivates pathogenic organisms in water by chemical oxidants or equivalent agents.

"Disinfection profile" means a summary of Giardia lamblia or virus inactivation through the treatment plant.

"Distribution main" means a water main whose primary purpose is to provide treated water to service connections.

"Domestic or other nondistribution system plumbing problem" means a coliform contamination problem in a waterworks with more than one service connection that is limited to the specific service connection from which the coliform positive sample was taken.

"Domestic use or usage" means normal family or household use, including drinking, laundering, bathing, cooking, heating, cleaning and flushing toilets (see Article 2 (§ 32.1-167 et seq.) of Chapter 6 of Title 32.1 of the Code of Virginia).

"Double gate-double check valve assembly" means an approved assembly composed of two single independently acting check valves including tightly closing shutoff valves located at each end of the assembly and petcocks and test gauges for testing the watertightness of each check valve.

"Effective corrosion inhibitor residual," for the purpose of 12 VAC 5-590-420 C 1 only, means a concentration sufficient to form a passivating film on the interior walls of a pipe.

"Enhanced coagulation" means the addition of sufficient coagulant for improved removal of disinfection byproduct precursors by conventional filtration treatment.

"Enhanced softening" means the improved removal of disinfection byproduct precursors by precipitative softening.

"Entry point" means the place where water from the source after application of any treatment is delivered to the distribution system.

"Equivalent residential connection" means a volume of water used equal to a residential connection which is 400 gallons per day unless supportive data indicates otherwise.

"Exception" means an approved deviation from a "shall" criteria contained in Part III (12 VAC 5-590-640 et seq.) of this chapter.

"Exemption" means a conditional waiver of a specific PMCL or treatment technique requirement which is granted to a specific waterworks for a limited period of time.

"Filter profile" means a graphical representation of individual filter performance, based on continuous turbidity measurements or total particle counts versus time for an entire filter run, from startup to backwash inclusively, that includes an assessment of filter performance while another filter is being backwashed.

"Filtration" means a process for removing particulate matter from water by passage through porous media.

"First draw sample" means a one-liter sample of tap water, collected in accordance with 12 VAC 5-590-370 B 6 a (2), that has been standing in plumbing pipes at least six hours and is collected without flushing the tap.

"Flocculation" means a process to enhance agglomeration or collection of smaller floc particles into larger, more easily settleable particles through gentle stirring by hydraulic or mechanical means.

"Free available chlorine" means that portion of the total residual chlorine remaining in water at the end of a specified contact period which will react chemically and biologically as hypochlorous acid or hypochlorite ion.

"GAC10" means granular activated carbon filter beds with an empty-bed contact time of 10 minutes based on average daily flow and a carbon reactivation frequency of every 180 days.

"Governmental entity" means the Commonwealth, a town, city, county, service authority, sanitary district or any other governmental body established under the Code of Virginia, including departments, divisions, boards or commissions.

"Gross alpha particle activity" means the total radioactivity due to alpha particle emission as inferred from measurements on a dry sample.

"Gross beta particle activity" means the total radioactivity due to beta particle emission as inferred from measurements on a dry sample.

"Groundwater" means all water obtained from sources not classified as surface water (or surface water sources).

"Groundwater under the direct influence of surface water" means any water beneath the surface of the ground with significant occurrence of insects or other macroorganisms, algae, or large-diameter pathogens such as Giardia lamblia, or Cryptosporidium.  It also means significant and relatively rapid shifts in water characteristics such as turbidity, temperature, conductivity, or pH that closely correlate to climatological or surface water conditions.  The office in accordance with 12 VAC 5-590-430 will determine direct influence of surface water.

"Haloacetic acids (five)" or "(HAA5)" means the sum of the concentrations in milligrams per liter of the haloacetic acid compounds (monochloroacetic acid, dichloroacetic acid, trichloroacetic acid, monobromoacetic acid, and dibromoacetic acid), rounded to two significant figures after addition.

"Halogen" means one of the chemical elements chlorine, bromine, fluorine, astatine or iodine.

"Health hazard" means any condition, device, or practice in a waterworks or its operation that creates, or may create, a danger to the health and well-being of the water consumer.

"Health regulations" means regulations which include all primary maximum contaminant levels, treatment technique requirements, and all operational regulations, the violation of which would jeopardize the public health.

"Hypochlorite" means a solution of water and some form of chlorine, usually sodium hypochlorite.

"Initial compliance period" means for all regulated contaminants, the initial compliance period is the first full three-year compliance period beginning at least 18 months after promulgation with the exception of waterworks with 150 or more service connections for contaminants listed at Table 2.3, VOC 19-21; Table 2.3, SOC 19-33; and antimony, beryllium, cyanide (as free cyanide), nickel, and thallium which shall begin January 1993.

"Interchangeable connection" means an arrangement or device that will allow alternate but not simultaneous use of two sources of water.

"Karstian geology" means an area predominantly underlain by limestone, dolomite, or gypsum and characterized by rapid underground drainage.  Such areas often feature sinkholes, caverns, and sinking or disappearing creeks.  In Virginia, this generally includes all that area west of the Blue Ridge and, in Southwest Virginia, east of the Cumberland Plateau.

"Large waterworks," for the purposes of 12 VAC 5-590-370 B 6, 12 VAC 5-590-420 C through F, 12 VAC 5-590-530 D, and 12 VAC 5-590-550 D only, means a waterworks that serves more than 50,000 persons.

"Lead free" when used with respect to solders and flux refers to solders and flux containing not more than 0.2% lead; when used with respect to pipes and pipe fittings refers to pipes and pipe fittings containing not more than 8.0% lead; and, when used with respect to plumbing fittings and fixtures intended by the plumbing manufacture to dispense water for human ingestion refers to fittings and fixtures that are in compliance with standards established in accordance with 42 USC § 300g-6(e).

"Lead service line" means a service line made of lead which connects the water main to the building inlet and any lead pigtail, gooseneck or other fitting which is connected to such lead line.

"Legionella" means a genus of bacteria, some species of which have caused a type of pneumonia called Legionnaires Disease.

"Liquid chlorine" means a liquefied, compressed gas as shipped in commerce.  Note:  The term liquid chlorine is sometimes used to describe a hypochlorite solution often employed for swimming pool sanitation.  This use of the term is incorrect.

"Log inactivation (log removal)" means that a 99% reduction is a 2-log inactivation; a 99.9% reduction is a 3-log inactivation; a 99.99% reduction is a 4-log inactivation.

"Man-made beta particle and photon emitters" means all radionuclides emitting beta particles and/or photons listed in the most current edition of "Maximum Permissible Body Burdens and Maximum Permissible Concentration of Radionuclides in Air or Water for Occupational Exposure," National Bureau of Standards Handbook 69, except the daughter products of thorium-232, uranium-235 and uranium-238.

"Maximum daily water demand" means the rate of water usage during the day of maximum water use.

"Maximum contaminant level (MCL)" means the maximum permissible level of a contaminant in water which is delivered to any user of a waterworks, except in the cases of turbidity and VOCs, where the maximum permissible level is measured at each entry point to the distribution system.  Contaminants added to the water under circumstances controlled by the user, except those resulting from corrosion of piping and plumbing caused by water quality, are excluded from this definition. MCLs are set as close to the MCLGs as feasible using the best available treatment technology. Maximum contaminant levels may be either "primary" (PMCL), meaning based on health considerations or "secondary" (SMCL) meaning based on aesthetic considerations.

"Maximum residual disinfectant level (MRDL)" means a level of a disinfectant added for water treatment that may not be exceeded at the consumer's tap without an unacceptable possibility of adverse health effects.  For chlorine and chloramines, a waterworks is in compliance with the MRDL when the running annual average of monthly averages of samples taken in the distribution system, computed quarterly, is less than or equal to the MRDL. For chlorine dioxide, a waterworks is in compliance with the MRDL when daily samples are taken at the entrance to the distribution system and no two consecutive daily samples exceed the MRDL. MRDLs are enforceable in the same manner as maximum contaminant levels.  There is convincing evidence that addition of a disinfectant is necessary for control of waterborne microbial contaminants.  Notwithstanding the MRDLs listed in Table 2.12, operators may increase residual disinfectant levels of chlorine or chloramines (but not chlorine dioxide) in the distribution system to a level and for a time necessary to protect public health to address specific microbiological contamination problems caused by circumstances such as distribution line breaks, storm runoff events, source water contamination, or cross-connections.

"Maximum residual disinfectant level goal (MRDLG)" means the maximum level of a disinfectant added for water treatment at which no known or anticipated adverse effect on the health of persons would occur, and which allows an adequate margin of safety.  MRDLGs are nonenforceable health goals and do not reflect the benefit of the addition of the chemical for control of waterborne microbial contaminants.

"Maximum total trihalomethane potential (MTP)" means the maximum concentration of total trihalomethanes produced in a given water containing a disinfectant residual after seven days at a temperature of 25°C or above.

"Medium-size waterworks," for the purpose of 12 VAC 5-590-370 B 6, 12 VAC 5-590-420 C through F, 12 VAC 5-590-530, and 12 VAC 5-590-550 D only, means a waterworks that serves greater than 3,300 and less than or equal to 50,000 persons.

“Method detection limit” means the minimum concentration of a substance that can be measured and reported with 99% confidence that the analyte concentration is greater than zero and is determined from analysis of a sample in a given matrix containing the analyte.

"Most probable number (MPN)" means that number of organisms per unit volume that, in accordance with statistical theory, would be more likely than any other number to yield the observed test result or that would yield the observed test result with the greatest frequency, expressed as density of organisms per 100 milliliters.  Results are computed from the number of positive findings of coliform-group organisms resulting from multiple-portion decimal-dilution plantings.

"Noncommunity water system waterworks" means a waterworks that is not a community waterworks, but operates at least 60 days out of the year.

"Nonpotable water" means water not classified as pure water.

"Nontransient noncommunity water system waterworks (NTNC)" means a waterworks that is not a community waterworks and that regularly serves at least 25 of the same persons over six months out of the year.

"Office" means the Commonwealth of Virginia, Department of Health, Office of Drinking Water.

"One hundred year flood level" means the flood elevation which will, over a long period of time, be equaled or exceeded on the average once every 100 years.

"Operator" means any individual employed or appointed by any owner, and who is designated by such owner to be the person in responsible charge, such as a supervisor, a shift operator, or a substitute in charge, and whose duties include testing or evaluation to control waterworks operations.  Not included in this definition are superintendents or directors of public works, city engineers, or other municipal or industrial officials whose duties do not include the actual operation or direct supervision of waterworks.

"Optimal corrosion control treatment" means the corrosion control treatment that minimizes the lead and copper concentrations at users' taps while ensuring that the treatment does not cause the waterworks to violate any other section of this chapter.

"Owner" or "water purveyor" means an individual, group of individuals, partnership, firm, association, institution, corporation, governmental entity, or the federal government which supplies or proposes to supply water to any person within this state from or by means of any waterworks (see Article 2 (§ 32.1-167 et seq.) of Chapter 6 of Title 32.1 of the Code of Virginia).

"Picocurie (pCi)" means that quantity of radioactive material producing 2.22 nuclear transformations per minute.

"Point of disinfectant application" means the point where the disinfectant is applied and water downstream of that point is not subject to recontamination by surface water runoff.

"Point-of-entry treatment device (POE)" means a treatment device applied to the water entering a house or building for the purpose of reducing contaminants in the water distributed throughout the house or building.

"Point-of-use treatment device (POU)" means a treatment device applied to a single tap for the purpose of reducing contaminants in the water at that one tap.

"Pollution" means the presence of any foreign substance (chemical, physical, radiological, or biological) in water that tends to degrade its quality so as to constitute an unnecessary risk or impair the usefulness of the water.

"Pollution hazard" means a condition through which an aesthetically objectionable or degrading material may enter the waterworks or a consumer's water system.

"Post-chlorination" means the application of chlorine to water subsequent to treatment.

"Practical quantitation level (PQL)" means the lowest level achievable by good laboratories within specified limits during routine laboratory operating conditions.

"Prechlorination" means the application of chlorine to water prior to filtration.

"Process fluids" means any fluid or solution which may be chemically, biologically, or otherwise contaminated or polluted which would constitute a health, pollutional, or system hazard if introduced into the waterworks.  This includes, but is not limited to:

1. Polluted or contaminated water;

2. Process waters;

3. Used waters, originating from the waterworks which may have deteriorated in sanitary quality;

4. Cooling waters;

5. Contaminated natural waters taken from wells, lakes, streams, or irrigation systems;

6. Chemicals in solution or suspension; and

7. Oils, gases, acids, alkalis, and other liquid and gaseous fluid used in industrial or other processes, or for fire fighting purposes.

"Pure water" or "potable water" means water fit for human consumption and domestic use which is sanitary and normally free of minerals, organic substances, and toxic agents in excess of reasonable amounts for domestic usage in the area served and normally adequate in quantity and quality for the minimum health requirements of the persons served (see Article 2 (§ 32.1-167 et seq.) of Chapter 6 of Title 32.1 of the Code of Virginia).

"Raw water main" means a water main which conveys untreated water from a source to a treatment facility.

"Reduced pressure principle backflow prevention device (RPZ device)" means a device containing a minimum of two independently acting check valves together with an automatically operated pressure differential relief valve located between the two check valves.  During normal flow and at the cessation of normal flow, the pressure between these two checks shall be less than the supply pressure.  In case of leakage of either check valve, the differential relief valve, by discharging to the atmosphere, shall operate to maintain the pressure between the check valves at less than the supply pressure.  The unit must include tightly closing shut-off valves located at each end of the device, and each device shall be fitted with properly located test cocks.  These devices must be of the approved type.

"REM" means the unit of dose equivalent from ionizing radiation to the total body or any internal organ or organ system.  A "millirem" (MREM) is 1/1000 of a REM.

"Repeat compliance period" means any subsequent compliance period after the initial compliance period.

"Residual disinfectant concentration ("C" in CT Calculations)" means the concentration of disinfectant measured in mg/L in a representative sample of water.

"Responsible charge" means designation by the owner of any individual to have duty and authority to operate or modify the operation of waterworks processes.

"Sanitary facilities" means piping and fixtures, such as sinks, lavatories, showers, and toilets, supplied with potable water and drained by wastewater piping.

"Sanitary survey" means an investigation of any condition that may affect public health.

"Secondary water source" means any approved water source, other than a waterworks' primary source, connected to or available to that waterworks for emergency or other nonregular use.

"Sedimentation" means a process for removal of solids before filtration by gravity or separation.

"Service connection" means the point of delivery of water to a customer's building service line as follows:

1. If a meter is installed, the service connection is the downstream side of the meter;

2. If a meter is not installed, the service connection is the point of connection to the waterworks;

3. When the water purveyor is also the building owner, the service connection is the entry point to the building.

"Service line sample" means a one-liter sample of water, collected in accordance with 12 VAC 5-590-370 B 6 a (2) (c), that has been standing for at least six hours in a service line.

"Sewer" means any pipe or conduit used to convey sewage or industrial waste streams.

"Single family structure," for the purpose of 12 VAC 5-590-370 B 6 (a) only, means a building constructed as a single-family residence that is currently used as either a residence or a place of business.

"Slow sand filtration" means a process involving passage of raw water through a bed of sand at low velocity (generally less than 0.4 m/h) resulting in substantial particulate removal by physical and biological mechanisms.

"Small waterworks," for the purpose of 12 VAC 5-590-370 B 6, 12 VAC 5-590-420 C through F, 12 VAC 5-590-530 D and 12 VAC 5-590-550 D only, means a waterworks that serves 3,300 persons or fewer.

"Standard sample" means that portion of finished drinking water that is examined for the presence of coliform bacteria.

"Surface water" means all water open to the atmosphere and subject to surface runoff.

"SUVA" means specific ultraviolet absorption at 254 nanometers (nm), an indicator of the humic content of water.  It is a calculated parameter obtained by dividing a sample's ultraviolet absorption at a wavelength of 254 nm (UV sub254 ) (in m-1) by its concentration of dissolved organic carbon (DOC) (in mg/L).

"Synthetic organic chemicals (SOC)" means one of the family of organic man-made compounds generally utilized for agriculture or industrial purposes.

"System hazard" means a condition posing an actual, or threat of, damage to the physical properties of the waterworks or a consumer's water system.

"Terminal reservoir" means an impoundment providing end storage of water prior to treatment.

"Too numerous to count" means that the total number of bacterial colonies exceeds 200 on a 47-mm diameter membrane filter used for coliform detection.

"Total effective storage volume" means the volume available to store water in distribution reservoirs measured as the difference between the reservoir's overflow elevation and the minimum storage elevation.  The minimum storage elevation is that elevation of water in the reservoir that can provide a minimum pressure of 20 psi at a flow as determined in 12 VAC 5-590-690 C to the highest elevation served within that reservoir's service area under systemwide maximum daily water demand.

"Total organic carbon" (TOC) means total organic carbon in mg/L measured using heat, oxygen, ultraviolet irradiation, chemical oxidants, or combinations of these oxidants that convert organic carbon to carbon dioxide, rounded to two significant figures.

"Total trihalomethanes (TTHM)" means the sum of the concentrations of the trihalomethanes expressed in milligrams per liter (mg/L) and rounded to two significant figures.  For the purpose of these regulations, the TTHM's shall mean trichloromethane (chloroform), dibromochloromethane, bromodichloromethane, and tribromomethane (bromoform).

"Transmission main" means a water main whose primary purpose is to move significant quantities of treated water among service areas.

"Treatment technique requirement" means a requirement which specifies for a contaminant a specific treatment technique(s) demonstrated to the satisfaction of the division to lead to a reduction in the level of such contaminant sufficient to comply with these regulations.

"Trihalomethane (THM)" means one of the family of organic compounds, named as derivatives of methane, wherein three of the four hydrogen atoms in methane are each substituted by a halogen atom in the molecular structure.

"Uncovered finished water storage facility" is a tank, reservoir, or other facility used to store water that will undergo no further treatment (except residual disinfection) and is open to the atmosphere.

"Unregulated contaminant (UC)" means a contaminant for which a monitoring requirement has been established, but for which no MCL or treatment technique requirement has been established.

"Used water" means any water supplied by a water purveyor from the waterworks to a consumer's water system after it has passed through the service connection.

"Virus" means a virus of fecal origin which is infectious to humans by waterborne transmission.

"Variance" means a conditional waiver of a specific regulation which is granted to a specific waterworks.  A PMCL Variance is a variance to a Primary Maximum Contaminant Level, or a treatment technique requirement.  An Operational Variance is a variance to an operational regulation or a Secondary Maximum Contaminant Level.  Variances for monitoring, reporting and public notification requirements will not be granted.

"Volatile synthetic organic chemical (VOC)" means one of the family of manmade organic compounds generally characterized by low molecular weight and rapid vaporization at relatively low temperatures or pressures.

"Waterborne disease outbreak" means the significant occurrence of acute infectious illness, epidemiologically associated with the ingestion of water from a waterworks which is deficient in treatment, as determined by the commissioner or the State Epidemiologist.

"Water purveyor" (same as owner).

"Water supply" means water that shall have been taken into a waterworks from all wells, streams, springs, lakes, and other bodies of surface waters (natural or impounded), and the tributaries thereto, and all impounded groundwater, but the term "water supply" shall not include any waters above the point of intake of such waterworks (see Article 2 (§ 32.1-167 et seq.) of Chapter 6 of Title 32.1 of the Code of Virginia).

"Water supply main" or "main" means any water supply pipeline that is part of a waterworks distribution system.

"Water Well Completion Report" means a report form published by the State Water Control Board entitled "Water Well Completion Report" which requests specific information pertaining to the ownership, driller, location, geological formations penetrated, water quantity and quality encountered as well as construction of water wells.  The form is to be completed by the well driller.

"Waterworks" means a system that serves piped water for drinking or domestic use to (i) the public, (ii) at least 15 connections, or (iii) an average of 25 individuals for at least 60 days out of the year.  The term "waterworks" shall include all structures, equipment and appurtenances used in the storage, collection, purification, treatment and distribution of pure water except the piping and fixtures inside the building where such water is delivered (see Article 2 (§ 32.1-167 et seq.) of Chapter 6 of Title 32.1 of the Code of Virginia).

"Waterworks with a single service connection" means a waterworks which supplies drinking water to consumers via a single service line.

12 VAC 5-590-370. Sampling frequency.

The commissioner may exempt consecutive waterworks that obtain potable water from another water system for distribution from all monitoring requirements in this section except for bacteriological (subsection A of this section), disinfectant residuals, byproducts and disinfection byproduct precursors (subdivision B 3 of this section), and lead and copper (subdivision B 6 of this section). The required sampling frequencies are as follows:

A. Bacteriological.

1. The waterworks owner shall collect total coliform samples at sites which are representative of water throughout the distribution system according to a written sample siting report. The report shall be established or approved by the division after investigation of the source, method of treatment and storage, and protection of the water concerned. The report must include, but is not limited to, the following:

a. The frequency of sampling distributed evenly throughout the month/quarter.

b. Distribution map showing the generalized location where specific sampling sites will be selected.

c. Supporting statement explaining how specific individual sites are selected, how sampling will be rotated among the sites, how repeat samples will be collected and other information demonstrating that sampling will be conducted in a manner to comply with this chapter.

d. Adequate sampling points to provide sampling representative of all the conditions in the system.

e. For small systems (less than 3,301 population), sample sites must also be identified by address and code number location.

f. Minimum of three sample locations for each sample required monthly so repeat sample locations are previously ascertained as being adequate in number and five customer service connections upstream and downstream. (See Appendix J for an example.)

g. The sampling point required to be repeat sampled shall not be eliminated from future collections based on a history of questionable water quality unless the sampling point is unacceptable as determined by the division.

2. The minimum number of bacteriological samples for total coliform evaluation to be collected and analyzed monthly from the distribution system of a community or nontransient noncommunity waterworks shall be in accordance with Table 2.1. All noncommunity waterworks that use a surface water source or a groundwater source under the direct influence of surface water, and all large noncommunity (serving 1,000 or more persons per day) waterworks, shall collect and submit samples monthly for analysis in accordance with Table 2.1. All other noncommunity waterworks shall submit samples for analysis each calendar quarter in accordance with Table 2.1.

3. The samples shall be taken at reasonably evenly spaced time intervals throughout the month or quarter.

If the results of a sanitary survey or other factors determine that some other frequency is more appropriate than that stated above, a modified sampling program report may be required. The altered frequency shall be confirmed or changed on the basis of subsequent surveys.

TABLE 2.1.

| POPULATION SERVED PER DAY | MINIMUM NUMBER OF SAMPLES (See 12 VAC 5-590-370 A 2) |
| --- | --- |
| 25 to 1,000 | 1 |
| 1,001 to 2,500 | 2 |
| 2,501 to 3,300 | 3 |
| 3,301 to 4,100 | 4 |
| 4,101 to 4,900 | 5 |
| 4,901 to 5,800 | 6 |
| 5,801 to 6,700 | 7 |
| 6,701 to 7,600 | 8 |
| 7,601 to 8,500 | 9 |
| 8,501 to 12,900 | 10 |
| 12,901 to 17,200 | 15 |
| 17,201 to 21,500 | 20 |
| 21,501 to 25,000 | 25 |
| 25,001 to 33,000 | 30 |
| 33,001 to 41,000 | 40 |
| 41,001 to 50,000 | 50 |
| 50,001 to 59,000 | 60 |
| 59,001 to 70,000 | 70 |
| 70,001 to 83,000 | 80 |
| 83,001 to 96,000 | 90 |
| 96,001 to 130,000 | 100 |
| 130,001 to 220,000 | 120 |
| 220,001 to 320,000 | 150 |
| 320,001 to 450,000 | 180 |
| 450,001 to 600,000 | 210 |
| 600,001 to 780,000 | 240 |
| 780,001 to 970,000 | 270 |
| 970,001 to 1,230,000 | 300 |
| 1,230,001 to 1,520,000 | 330 |
| 1,520,001 to 1,850,000 | 360 |
| 1,850,001 to 2,270,000 | 390 |

4. All bacteriological analyses shall be performed in accordance with 12 VAC 5-590-440 by the DCLS or by a laboratory certified by DCLS for drinking water samples.

B. Chemical. The location of sampling points, the chemicals measured, the frequency, and the timing of sampling within each compliance period shall be established or approved by the commissioner at the time of issuance of a waterworks operation permit. The commissioner may increase required monitoring where necessary to detect variations within the waterworks. Analysis of field composite samples shall not be allowed. Samples for contaminants that may exhibit seasonal variations shall be collected during the period of the year when contamination is most likely to occur. Failure to comply with the sampling schedules in this section will require public notification pursuant to 12 VAC 5-590-540.

Any other dates contained in this chapter notwithstanding, all waterworks shall comply with all applicable PMCLs listed in Tables 2.2 and 2.3.

Design criteria for new or modified waterworks or waterworks developing new sources of supply are found in 12 VAC 5-590-820, 12 VAC 5-590-830 and 12 VAC 5-590-840.

1. Inorganic chemical. Community and nontransient noncommunity waterworks owners shall conduct monitoring to determine compliance with the MCLs in Table 2.2 in accordance with this section. All other noncommunity waterworks owners shall conduct monitoring to determine compliance with the nitrate and nitrite PMCLs in Table 2.2 (as appropriate) in accordance with this section. Monitoring shall be conducted as follows:

a. The owner of any groundwater source waterworks with 150 or more service connections shall take a minimum of one sample at each entry point to the distribution system which is representative of each source, after treatment, unless a change in condition makes another sampling point more representative of each source or treatment plant (hereafter called a sampling point) starting in the compliance period beginning January 1, 1993. The owner of any groundwater source waterworks with fewer than 150 service connections shall take a minimum of one sample at each sampling point for asbestos, barium, cadmium, chromium, fluoride, mercury, nitrate, nitrite, and selenium in the compliance period beginning January 1, 1993, and for antimony, beryllium, cyanide (as free cyanide), nickel, and thallium in the compliance period beginning January 1, 1996, and for arsenic (for community and nontransient noncommunity waterworks) in compliance with 12 VAC 5-590-370 B 1 d (6) (b).

b. The owner of any waterworks which uses a surface water source in whole or in part with 150 or more service connections shall take a minimum of one sample at each entry point to the distribution system after any application of treatment or in the distribution system at a point which is representative of each source, after treatment, unless a change in conditions makes another sampling point more representative of each source or treatment plant (hereafter called a sampling point) beginning January 1, 1993. The owner of any waterworks which use a surface water source in whole or in part with fewer than 150 service connections shall take a minimum of one sample at each sampling point for asbestos, barium, cadmium, chromium, fluoride, mercury, nitrate, nitrite, and selenium beginning January 1, 1993, and for antimony, beryllium, cyanide (as free cyanide), nickel, and thallium beginning January 1, 1996 , and for arsenic (for community and nontransient noncommunity waterworks) in compliance with 12 VAC 5-590-370 B 1 d (6) (a).

c. If a waterworks draws water from more than one source and the sources are combined before distribution, the waterworks owner shall sample at an entry point to the distribution system during periods of normal operating conditions (i.e., when water is representative of all sources being used).

d. The frequency of monitoring for asbestos shall be in accordance with subdivision B 1 d (1) of this section; the frequency of monitoring for barium, cadmium, chromium, fluoride, mercury, and selenium shall be in accordance with subdivision B 1 d (2) of this section; the frequency of monitoring for antimony, beryllium, cyanide (as free cyanide), nickel, and thallium shall be in accordance with subdivision B 1 d (3) of this section; the frequency of monitoring for nitrate shall be in accordance with subdivision B 1 d (4) of this section; the frequency of monitoring for nitrite shall be in accordance with subdivision B 1 d (5) of this section; and the frequency of monitoring for arsenic shall be in accordance with subdivision B 1 d (6) of this section.

(1) The frequency of monitoring conducted to determine compliance with the PMCL for asbestos specified in Table 2.2 shall be conducted as follows:

(a) The owner of each community and nontransient noncommunity waterworks is required to monitor for asbestos during the first three-year compliance period of each nine-year compliance cycle beginning in the compliance period starting January 1, 1993.

(b) If the waterworks owner believes the waterworks is not vulnerable to either asbestos contamination in its source water or due to corrosion of asbestos-cement pipe, or both, the owner may apply to the commissioner for a waiver of the monitoring requirement in subdivision B 1 d (1) (a) of this section. If the commissioner grants the waiver, the waterworks owner is not required to monitor.

(c) The commissioner may grant a waiver based on a consideration of the following factors:

(i) Potential asbestos contamination of the water source; and

(ii) The use of asbestos-cement pipe for finished water distribution and the corrosive nature of the water.

(d) A waiver remains in effect until the completion of the three-year compliance period. Waterworks not receiving a waiver shall monitor in accordance with the provisions of subdivision B 1 d (1) (a) of this section.

(e) The owner of a waterworks vulnerable to asbestos contamination due solely to corrosion of asbestos-cement pipe shall take one sample at a tap served by asbestos-cement pipe and under conditions where asbestos contamination is most likely to occur.

(f) The owner of a waterworks vulnerable to asbestos contamination due solely to source water shall monitor sampling points in accordance with subdivision B 1 of this section.

(g) The owner of a waterworks vulnerable to asbestos contamination due both to its source water supply and corrosion of asbestos-cement pipe shall take one sample at a tap served by asbestos-cement pipe and under conditions where asbestos contamination is most likely to occur.

(h) The owner of a waterworks which exceeds the PMCL as determined in 12 VAC 5-590-410 B 1 shall monitor quarterly beginning in the next quarter after the violation exceedance occurred.

(i) The commissioner may decrease the quarterly monitoring requirement to the frequency specified in subdivision B 1 d (1) (a) of this section provided the commissioner has determined that the waterworks is reliably and consistently below the PMCL. In no case can the commissioner make this determination unless the owner of a groundwater source waterworks takes a minimum of two quarterly samples or the owner of a waterworks which uses a surface water source in whole or in part takes a minimum of four quarterly samples.

(j) If monitoring data collected after January 1, 1990, are generally consistent with the requirements of subdivision B 1 d (1) of this section, then the commissioner may allow waterworks owner to use that data to satisfy the monitoring requirement for the initial compliance period beginning January 1, 1993.

(2) The frequency of monitoring conducted to determine compliance with the MCLs in Table 2.2 for barium, cadmium, chromium, fluoride, mercury, and selenium shall be as follows:

(a) The owner of a groundwater source waterworks shall take one sample at each sampling point during each compliance period beginning in the compliance period starting January 1, 1993.

(b) The owner of a waterworks which uses a surface water source in whole or in part shall take one sample annually at each sampling point beginning January 1, 1993.

(c) A waterworks owner may apply to the commissioner for a waiver from the monitoring frequencies specified in subdivision B 1 d (2) (a) or (b) of this section.

(d) A condition of the waiver shall require that the waterworks owner shall take a minimum of one sample while the waiver is effective. The term during which the waiver is effective shall not exceed one compliance cycle (i.e., nine years).

(e) The commissioner may grant a waiver provided the owner of a waterworks which uses a surface water source in whole or in part has monitored annually for at least three years and groundwater waterworks have conducted a minimum of three rounds of monitoring. (At least one sample shall have been taken since January 1, 1990.) The owner of any waterworks which uses a surface water source in whole or in part or a groundwater source waterworks shall demonstrate that all previous analytical results were less than the PMCL. Waterworks that use a new water source are not eligible for a waiver until three rounds of monitoring from the new source have been completed.

(f) In determining the appropriate reduced monitoring frequency, the commissioner shall consider:

(i) Reported concentrations from all previous monitoring;

(ii) The degree of variation in reported concentrations; and

(iii) Other factors which may affect contaminant concentrations such as changes in groundwater pumping rates, changes in the waterworks configuration, changes in the waterworks operating procedures, or changes in stream flows or characteristics.

(g) A decision by the commissioner to grant a waiver shall be made in writing and shall set forth the basis for the determination. The request for a waiver may be initiated by the commissioner or upon an application by the waterworks owner. The owner shall specify the basis for the request. The commissioner shall review and, where appropriate, revise the determination of the appropriate monitoring frequency when the waterworks owner submits new monitoring data or when other data relevant to the waterworks appropriate monitoring frequency become available.

(h) Owners of waterworks which exceed the PMCLs as calculated in 12 VAC 5-590-410 shall monitor quarterly beginning in the next quarter after the violation exceedance occurred.

(i) The commissioner may decrease the quarterly monitoring requirement to the frequencies specified in subdivision B 2 d (2) (a), (b) or (c) of this section provided a determination has been made that the waterworks is reliably and consistently below the PMCL. In no case can the commissioner make this determination unless the owner of a groundwater source waterworks takes a minimum of two quarterly samples or the owner of a waterworks which uses a surface water source in whole or in part takes a minimum of four quarterly samples.

(3) The frequency of monitoring conducted to determine compliance with the PMCLs in Table 2.2 for antimony, beryllium, cyanide (as free cyanide), nickel, and thallium shall be as follows:

(a) The owner of a groundwater source waterworks with 150 or more service connections shall take one sample at each sampling point during each compliance period beginning in the compliance period starting January 1, 1993. The owner of a groundwater source waterworks with fewer than 150 service connections shall take one sample at each sampling point during each compliance period beginning in the compliance period starting January 1, 1996.

(b) The owner of a waterworks which uses a surface water source in whole or in part with 150 or more service connections shall take one sample annually at each sampling point beginning January 1, 1993. The owner of a waterworks which uses a surface water source in whole or in part with fewer than 150 service connections shall take one sample annually at each sampling point beginning January 1, 1996.

(c) A waterworks owner may apply to the commissioner for a waiver from the monitoring frequencies specified in subdivision B 2 d (3) (a) or (b) of this section.

(d) A condition of the waiver shall require that the waterworks owner shall take a minimum of one sample while the waiver is effective. The term during which the waiver is effective shall not exceed one compliance cycle (i.e., nine years).

(e) The commissioner may grant a waiver provided the owner of a waterworks which uses a surface water source in whole or in part has monitored annually for at least three years and groundwater waterworks have conducted a minimum of three rounds of monitoring. (At least one sample shall have been taken since January 1, 1990.) The owner of any waterworks which uses a surface water source in whole or in part or a groundwater source waterworks shall demonstrate that all previous analytical results were less than the PMCL. Waterworks that use a new water source are not eligible for a waiver until three rounds of monitoring from the new source have been completed.

(f) In determining the appropriate reduced monitoring frequency, the commissioner shall consider:

(i) Reported concentrations from all previous monitoring;

(ii) The degree of variation in reported concentrations; and

(iii) Other factors which may affect contaminant concentrations such as changes in groundwater pumping rates, changes in the waterworks configuration, changes in the waterworks operating procedures, or changes in stream flows or characteristics.

(g) A decision by the commissioner to grant a waiver shall be made in writing and shall set forth the basis for the determination. The request for a waiver may be initiated by the commissioner or upon an application by the waterworks owner. The owner shall specify the basis for the request. The commissioner shall review and, where appropriate, revise the determination of the appropriate monitoring frequency when the waterworks owner submits new monitoring data or when other data relevant to the waterworks appropriate monitoring frequency become available.

(h) Owners of waterworks which exceed the PMCLs as calculated in 12 VAC 5-590-410 shall monitor quarterly beginning in the next quarter after the violation exceedance occurred.

(i) The commissioner may decrease the quarterly monitoring requirement to the frequencies specified in subdivision B 2 d (3) (a), (b) or (c) of this section provided a determination has been made that the waterworks is reliably and consistently below the PMCL. In no case can the commissioner make this determination unless the owner of a groundwater source waterworks takes a minimum of two quarterly samples or the owner of a waterworks which uses a surface water source in whole or in part takes a minimum of four quarterly samples.

(4) All community, nontransient noncommunity and noncommunity waterworks owners shall monitor to determine compliance with the PMCL for nitrate in Table 2.2.

(a) Owners of community and nontransient noncommunity waterworks which use a groundwater source shall monitor annually beginning January 1, 1993.

(b) Owners of community and nontransient noncommunity waterworks which use a surface water source in whole or in part shall monitor quarterly beginning January 1, 1993.

(c) For community and nontransient noncommunity waterworks which use groundwater, the repeat monitoring frequency shall be quarterly for at least one year following any one sample in which the concentration is ≥50% of the PMCL. The commissioner may allow the owner of a waterworks, which uses groundwater, to reduce the sampling frequency to annually after four consecutive quarterly samples are reliably and consistently less than the PMCL.

(d) For community and nontransient noncommunity waterworks, the commissioner may allow the owner of a waterworks which uses a surface water source in whole or in part, to reduce the sampling frequency to annually if all analytical results from four consecutive quarters are <50% of the PMCL. Such waterworks shall return to quarterly monitoring if any one sample is ≥50% of the PMCL.

(e) The owners of all other noncommunity waterworks shall monitor annually beginning January 1, 1993.

(f) After the initial round of quarterly sampling is completed, the owner of each community and nontransient noncommunity waterworks which is monitoring annually shall take subsequent samples during the quarter(s) which previously resulted in the highest analytical result.

(5) All community, nontransient noncommunity and noncommunity waterworks owners shall monitor to determine compliance with the PMCL for nitrite in Table 2.2.

(a) All waterworks owners shall take one sample at each sampling point in the compliance period beginning January 1, 1993.

(b) After the initial sample, the owner of any waterworks where an analytical result for nitrite is <50% of the PMCL shall monitor at the frequency specified by the commissioner.

(c) The repeat monitoring frequency for any waterworks owner shall be quarterly for at least one year following any one sample in which the concentration is ≥50% of the PMCL. The commissioner may allow a waterworks owner to reduce the sampling frequency to annually after determining the analysis results are reliably and consistently less than the PMCL.

(d) Owners of waterworks which are monitoring annually shall take each subsequent sample during the quarter(s) which previously resulted in the highest analytical result.

(6) The frequency of monitoring conducted to determine compliance with the PMCLs in Table 2.2 for arsenic shall be as follows:

(a) The owner of each community and nontransient noncommunity waterworks which that use a surface water source in whole or in part shall take one sample annually at each sampling point beginning June 1, 1978 January 23, 2006.

(b) The owner of each community and nontransient noncommunity groundwater source waterworks shall take one sample at each sampling entry point within a three year during each compliance period starting June 1, 1979 January 23, 2006.

(c) Owners of waterworks which exceed the PMCL listed in Table 2.2 shall report to the commissioner within seven days and initiate three additional samples at the same sampling point within one month.

(d) For initial analyses required by subdivision B 1 d (6) (a) or (b) of this section, data for waterworks which use surface water source in whole or in part acquired within one year prior to the effective date for arsenic monitoring and data for groundwater waterworks acquired within three years prior to the effective date for arsenic monitoring may be substituted at the discretion of the commissioner.

(c) Owners of waterworks that exceed the PMCL, as calculated in 12 VAC 5-590-410, shall monitor quarterly beginning in the next quarter after the exceedance has occurred.

(d) The commissioner may decrease the quarterly monitoring requirement to the frequencies specified in subdivision B 2 d (6) (a) or (b) of this section provided a determination has been made that the waterworks is reliably and consistently below the PMCL. In no case can the commissioner make this determination unless the owner of a groundwater source waterworks takes a minimum of two quarterly samples or the owner of a waterworks that uses a surface water source in whole or in part takes a minimum of four quarterly samples.

(e)  No waivers shall be granted by the commissioner for arsenic.

2. Organic chemicals. Owners of all community and nontransient noncommunity waterworks shall sample for organic chemicals in accordance with their water source. Where two or more sources are combined before distribution, the waterworks owner shall sample at the entry point for the combined sources during periods of normal operating conditions.

a. Owners of waterworks which that use groundwater shall take a minimum of one sample at each entry point to the distribution system which is representative of each source, after treatment (hereafter called a sampling point).

b. Owners of waterworks which that use a surface water source in whole or in part shall take a minimum of one sample at points in the distribution system that are representative of each source or at each entry point to the distribution system, after treatment (hereafter called a sampling point).

c. The owner of each community and nontransient noncommunity waterworks shall take four consecutive quarterly samples for each contaminant listed in Table 2.3-VOC 2 through 21 and SOC during each compliance period, beginning in the compliance period starting January 1, 1993.

d. Reduced monitoring.

(1) VOC.

(a) If the initial monitoring for contaminants listed in Table 2.3-VOC 1 through 8 and the monitoring for the contaminants listed in Table 2.3-VOC 9 through 21 as allowed in subdivision B 2 d (1) (c) of this section has been completed by December 31, 1992, and the waterworks did not detect any contaminant listed in Table 2.3-VOC 1 through 21, then the owner of each groundwater waterworks and waterworks which use a surface water source in whole or in part shall take one sample annually beginning January 1, 1993.

(b) After a minimum of three years of annual sampling, the commissioner may allow the owner of a groundwater waterworks with no previous detection of any contaminant listed in Table 2.3-VOC 2 through 21 to take one sample during each compliance period.

(c) The commissioner may allow the use of monitoring data collected after January 1, 1988, for purposes of initial monitoring compliance. If the data are generally consistent with the other requirements in this section, the commissioner may use these data (i.e., a single sample rather than four quarterly samples) to satisfy the initial monitoring requirement of subdivision B 2 c of this section. Waterworks which use grandfathered samples and did not detect any contaminants listed in Table 2.3-VOC, 2 through 21, shall begin monitoring annually in accordance with subdivision B 2 d (1) (a) of this section beginning January 1, 1993.

(2) SOC.

(a) Waterworks serving more than 3,300 persons which do not detect a contaminant listed in Table 2.3-SOC in the initial compliance period, may reduce the sampling frequency to a minimum of two quarterly samples in one year during each repeat compliance period.

(b) Waterworks serving less than or equal to 3,300 persons which do not detect a contaminant listed in Table 2.3-SOC in the initial compliance period may reduce the sampling frequency to a minimum of one sample during each repeat compliance period.

e. Waiver application.

(1) For VOCs. The owner of any community and nontransient noncommunity groundwater waterworks which does not detect a contaminant listed in Table 2.3-VOC may apply to the commissioner for a waiver from the requirements of subdivisions B 2 d (1) (a) and (b) of this section after completing the initial monitoring. A waiver shall be effective for no more than six years (two compliance periods). The commissioner may also issue waivers to small systems for the initial round of monitoring for 1,2,4-trichlorobenzene.

(2) For SOCs. The owner of any community and nontransient noncommunity waterworks may apply to the commissioner for a waiver from the requirement of subdivisions B 2 c and d (2) of this section. The waterworks owner shall reapply for a waiver for each compliance period.

f. The commissioner may grant a waiver after evaluating the following factors: Knowledge of previous use (including transport, storage, or disposal) of the contaminant within the watershed or zone of influence of the source. If a determination by the commissioner reveals no previous use of the contaminant within the watershed or zone of influence, a waiver may be granted. If previous use of the contaminant is unknown or it has been used previously, then the following factors shall be used to determine whether a waiver is granted.

(1) Previous analytical results.

(2) The proximity of the waterworks to a potential point or nonpoint source of contamination. Point sources include spills and leaks of chemicals at or near a waterworks or at manufacturing, distribution, or storage facilities, or from hazardous and municipal waste landfills and other waste handling or treatment facilities. Nonpoint sources for SOCs include the use of pesticides to control insect and weed pests on agricultural areas, forest lands, home and gardens, and other land application uses.

(3) The environmental persistence and transport of the contaminants listed in Table 2.3 VOC and SOC.

(4) How well the water source is protected against contamination, such as whether it is a waterworks which uses a surface water source in whole or in part or whether it is a groundwater source waterworks. Groundwater source waterworks shall consider factors such as depth of the well, the type of soil, wellhead protection, and well structure integrity. Waterworks which use surface water in whole or in part shall consider watershed protection.

(5) Special factors.

(a) For VOCs. The number of persons served by the waterworks and the proximity of a smaller waterworks to a larger waterworks.

(b) For SOCs. Elevated nitrate levels at the waterworks supply source.

(c) For SOCs. Use of PCBs in equipment used in the production, storage, or distribution of water (i.e., PCBs used in pumps, transformers, etc.).

g. Condition for waivers.

(1) As a condition of the VOC waiver the owner of a groundwater waterworks shall take one sample at each sampling point during the time the waiver is effective (i.e., one sample during two compliance periods or six years) and update its vulnerability assessment considering the factors listed in subdivision B 2 f of this section. Based on this vulnerability assessment the commissioner shall reconfirm that the waterworks owner is nonvulnerable. If the commissioner does not make this reconfirmation within three years of the initial determination, then the waiver is invalidated and the waterworks is required to sample annually as specified in subdivision B 2 d (1) (a) of this section.

(2) The owner of any community and nontransient noncommunity waterworks which use surface water in whole or in part which does not detect a contaminant listed in Table 2.3-VOC may apply to the commissioner for a waiver from the requirements of subdivision B 2 d (1) (a) of this section after completing the initial monitoring. Waterworks meeting this criteria shall be determined by the commissioner to be nonvulnerable based on a vulnerability assessment during each compliance period. Each waterworks receiving a waiver shall sample at the frequency specified by the commissioner (if any).

(3) There are no conditions to SOC waivers.

h. If a contaminant listed in Table 2.3-VOC 2 through 21 or SOC 1 through 33 is detected then (NOTE: Detection occurs when a contaminant level exceeds the current detection limit as defined by EPA.):

(1) Each waterworks owner shall monitor quarterly at each sampling point which resulted in a detection.

(2) The commissioner may decrease the quarterly monitoring requirement specified in subdivision B 2 h (1) of this section provided it has determined that the waterworks is reliably and consistently below the PMCL. In no case shall the commissioner make this determination unless a groundwater waterworks takes a minimum of two quarterly samples and a waterworks which use surface water in whole or in part takes a minimum of four quarterly samples.

(3) If the commissioner determines that the waterworks is reliably and consistently below the PMCL, the commissioner may allow the waterworks to monitor annually. Waterworks which monitor annually shall monitor during the quarter(s) which previously yielded the highest analytical result.

(4) Waterworks which have three consecutive annual samples with no detection of a contaminant may apply to the commissioner for a waiver for VOC as specified in subdivision B 2 e (1) or to SOC as specified in subdivision B 2 e (2) of this section.

(5) Subsequent monitoring due to contaminant detection.

(a) Groundwater waterworks which have detected one or more of the following two-carbon organic compounds: trichloroethylene, tetrachloroethylene, 1,2-dichloroethane, 1,1,1-trichloroethane, cis-1,2-dichloroethylene, trans-1,2-dichloroethylene, or 1,1-dichloroethylene shall monitor quarterly for vinyl chloride. A vinyl chloride sample shall be taken at each sampling point at which one or more of the two-carbon organic compounds was detected. If the results of the first analysis do not detect vinyl chloride, the commissioner may reduce the quarterly monitoring frequency of vinyl chloride monitoring to one sample during each compliance period. Waterworks which use surface water in whole or in part are required to monitor for vinyl chloride as specified by the commissioner.

(b) If monitoring results in detection of one or more of certain related contaminants (heptachlor and heptachlor epoxide), then subsequent monitoring shall analyze for all related contaminants.

i. Waterworks which violate the requirements of Table 2.3 for VOCs or SOCs, as determined by 12 VAC 5-590-410 C, shall monitor quarterly. After a minimum of four consecutive quarterly samples which show the waterworks is in compliance as specified in 12 VAC 5-590-410 C and the commissioner determines that the waterworks is reliably and consistently below the PMCL, the waterworks may monitor at the frequency and time specified in subdivision B 2 h (3) of this section.

3. Disinfectant residuals, disinfection byproducts and disinfection byproduct precursors.

a. Unless otherwise noted, all waterworks that use a chemical disinfectant must comply with the requirements of this section as follows:

(1) Community or nontransient noncommunity waterworks that use surface water or groundwater under the direct influence of surface water and serving 10,000 or more persons, must comply with this section beginning January 1, 2002.

(2) Community or nontransient noncommunity waterworks that use surface water or groundwater under the direct influence of surface water serving fewer than 10,000 persons and waterworks using only groundwater not under the direct influence of surface water must comply with this section beginning January 1, 2004.

(3) Transient noncommunity waterworks which use surface water or groundwater under the direct influence of surface water and serving 10,000 or more persons and using chlorine dioxide as a disinfectant or oxidant must comply with any requirements for chlorine dioxide in this section beginning January 1, 2002.

(4) Transient noncommunity waterworks which use surface water or groundwater under the direct influence of surface water serving fewer than 10,000 persons and using chlorine dioxide as a disinfectant or oxidant and waterworks using only groundwater not under the direct influence of surface water and using chlorine dioxide as a disinfectant or oxidant must comply with any requirements for chlorine dioxide in this section beginning January 1, 2004.

b. Waterworks must take all samples during normal operating conditions.

(1) Analysis under this section for disinfection byproducts (TTHM, HAA5, chlorite and bromate) must be conducted by a laboratory that has received certification by EPA or the state except as noted in subdivision B 3 b (2) of this section.

(2) Measurement under this section of daily chlorite samples at the entry point to the distribution system, disinfection residuals (free chlorine, combined chlorine, total chlorine and chlorine dioxide), alkalinity, bromide, TOC, SUVA (DOC and UV sub254), and pH must be made by a party approved by the commissioner.

(3) DPD colorimetric test kits may be used to measure residual disinfectant concentrations for chlorine, chloramines and chlorine dioxide.

c. Failure to monitor in accordance with the monitoring plan required under subdivision B 3 j of this section is a monitoring violation. Failure to monitor will be treated as a violation for the entire period covered by the annual average where compliance is based on a running annual average of monthly or quarterly samples or averages and the waterworks' failure to monitor makes it impossible to determine compliance with PMCLs or MRDLs.

d. Waterworks may use only data collected under the provisions of this section or the US EPA Information Collection Rule, 40 CFR Part 141 Subpart M, Information Collection Requirements (ICR) for Public Water Systems, to qualify for reduced monitoring.

e. TTHM/HAA5 monitoring. Community or nontransient noncommunity waterworks must monitor TTHM and HAA5 at the frequency indicated below:

(1) Routine monitoring requirements.

(a) Waterworks using surface water or groundwater under the direct influence of surface water and serving at least 10,000 persons must collect four water samples per quarter per treatment plant. At least 25% of all samples collected each quarter must be at locations representing maximum residence time in the distribution system. The remaining samples must be taken at locations representative of at least average residence time in the distribution system and representative of the entire distribution system. When setting the sample locations the waterworks must take into account number of persons served, different sources of water, and different treatment methods.

(b) Waterworks using surface water or groundwater under the direct influence of surface water and serving from 500 to 9,999 persons must collect one sample per quarter per treatment plant. The sample location must represent maximum residence time in the distribution system.

(c) Waterworks using surface water or groundwater under the direct influence of surface water and serving fewer than 500 persons must collect one sample per year per treatment plant during the month of warmest water temperature. The sample location must represent maximum residence time in the distribution system. If the sample (or average of annual samples, if more than one sample is taken) exceeds PMCL in Table 2.13, the waterworks must increase monitoring to one sample per treatment plant per quarter, taken at a point reflecting the maximum residence time in the distribution system, until waterworks meets reduced monitoring criteria.

(d) Waterworks using only groundwater not under direct influence of surface water using chemical disinfectant and serving at least 10,000 persons must collect one sample per quarter per treatment plant. The sample location must represent maximum residence time in the distribution system.

(e) Waterworks using only groundwater not under direct influence of surface water using chemical disinfectant and serving fewer than 10,000 persons must collect one sample per year per treatment plant during the month of warmest water temperature. The sample location must represent maximum residence time in the distribution system. If the sample (or average of annual samples, if more than one sample is taken) exceeds PMCL in Table 2.13, the waterworks must increase monitoring to one sample per treatment plant per quarter, taken at a point reflecting the maximum residence time in the distribution system, until the waterworks meets the criteria for reduced monitoring found in subdivision B 3 e (4) of this section.

(f) If a waterworks elects to sample more frequently than the minimum required, at least 25% of all samples collected each quarter (including those taken in excess of the required frequency) must be taken at locations that represent the maximum residence time of the water in the distribution system. The remaining samples must be taken at locations representative of at least average residence time in the distribution system.

(g) With prior approval of the commissioner, waterworks that utilize multiple wells from a common aquifer may consider these multiple sources as one treatment plant for determining the minimum number of samples to be collected for TTHM and HAA5 analysis.

(2) After one year of routine monitoring a waterworks may reduce monitoring, except as otherwise provided, as follows:

(a) Waterworks using surface water or groundwater under the direct influence of surface water and serving at least 10,000 persons that has a source water annual average TOC level, before any treatment, of equal to or less than 4.0 mg/L and a TTHM annual average equal to or less than 0.040 mg/L and HAA5 annual average equal to or less than 0.030 mg/L may reduce its monitoring to one sample per treatment plant per quarter at a distribution system location reflecting maximum residence time.

(b) Waterworks using surface water or groundwater under the direct influence of surface water serving from 500 to 9,999 persons that has a source water annual average TOC level, before any treatment, equal to or less than 4.0 mg/L and a TTHM annual average equal to or less than 0.040 mg/L and HAA5 annual average equal to or less than 0.030 mg/L may reduce its monitoring to one sample per treatment plant per year at a distribution system location reflecting maximum residence time during the month of warmest water temperature.

(c) Waterworks using only groundwater not under the direct influence of surface water, using chemical disinfectant and serving at least 10,000 persons that has a TTHM annual average of equal to or less than 0.040 mg/L and HAA5 annual average of equal to or less than 0.030 mg/L may reduce its monitoring to one sample per treatment plant per year at a distribution system location reflecting maximum residence time during the month of warmest water temperature.

(d) Waterworks using only groundwater not under the direct influence of surface water, using chemical disinfectant and serving fewer than 10,000 persons that has a TTHM annual average equal to or less than 0.040 mg/L and HAA5 annual average equal to or less than 0.030 mg/L for two consecutive years or TTHM annual average equal to or less than 0.020 mg/L and HAA5 annual average of equal to or less than 0.015 mg/L for one year may reduce its monitoring to one sample per treatment plant per three-year monitoring cycle at a distribution system location reflecting maximum residence time during the month of warmest water temperature, with the three-year cycle beginning on January 1 following the quarter in which the system qualifies for reduced monitoring.

(e) Waterworks using surface water or groundwater under the direct influence of surface water serving fewer than 500 persons may not reduce its monitoring to less than one sample per treatment plant per year.

(3) Waterworks on a reduced monitoring schedule may remain on that reduced schedule as long as the average of all samples taken in the year (for waterworks that must monitor quarterly) or the result of the sample (for waterworks that must monitor no more frequently than annually) is no more than 0.060 mg/L and 0.045 mg/L for TTHMs and HAA5, respectively. Waterworks that do not meet these levels must resume monitoring at the frequency identified in subdivision B 3 e (1) of this section in the quarter immediately following the quarter in which the waterworks exceeds 0.060 mg/L or 0.045 mg/L for TTHMs or HAA5, respectively. For waterworks using only groundwater not under the direct influence of surface water and serving fewer than 10,000 persons, if either the TTHMs annual average is greater than 0.080 mg/L or the HAA5 annual average is greater than 0.060 mg/L, the waterworks must go to increased monitoring identified in subdivision B 3 e (1) of this section in the quarter immediately following the monitoring period in which the system exceeds 0.080 mg/L or 0.060 mg/L for TTHM or HAA5 respectively.

(4) Waterworks on increased monitoring may return to routine monitoring if, after at least one year of monitoring, their TTHM annual average is equal to or less than 0.060 mg/L and their HAA5 annual average is equal to or less than 0.045 mg/L.

(5) The commissioner may return a waterworks to routine monitoring at the commissioner's discretion.

f. Chlorite. Community and nontransient noncommunity waterworks using chlorine dioxide, for disinfection or oxidation, must conduct monitoring for chlorite.

(1) Routine monitoring.

(a) Daily monitoring. Waterworks must take daily samples at the entrance to the distribution system. For any daily sample that exceeds the chlorite PMCL in Table 2.13, the waterworks must take additional samples in the distribution system the following day at the locations required by subdivision B 3 f (1) (c) of this section, in addition to the sample required at the entrance to the distribution system.

(b) Monthly monitoring. Waterworks must take a three-sample set each month in the distribution system. The waterworks must take one sample at each of the following locations: near the first customer, at a location representative of average residence time, and at a location reflecting maximum residence time in the distribution system. Any additional routine sampling must be conducted in the same manner (as three-sample sets, at the specified locations). The waterworks may use the results of additional monitoring conducted under subdivision B 3 f (1) (c) of this section to meet the requirement for monitoring in this paragraph.

(c) Additional monitoring requirements. On each day following a routine sample monitoring result that exceeds the chlorite PMCL in Table 2.13 at the entrance to the distribution system, the waterworks is required to take three chlorite distribution system samples at the following locations: as close to the first customer as possible, in a location representative of average residence time, and as close to the end of the distribution system as possible (reflecting maximum residence time in the distribution system).

(2) Reduced monitoring.

(a) Chlorite monitoring at the entrance to the distribution system required by subdivision B 3 f (1) (a) of this section may not be reduced.

(b) Chlorite monitoring in the distribution system required by subdivision B 3 f (1) (b) of this section may be reduced to one three-sample set per quarter after one year of monitoring where no individual chlorite sample taken in the distribution system under subdivision B 3 f (1) (b) of this section has exceeded the chlorite PMCL in Table 2.13 and the waterworks has not been required to conduct monitoring under subdivision B 3 f (1) (c) of this section. The waterworks may remain on the reduced monitoring schedule until either any of the three individual chlorite samples taken quarterly in the distribution system under subdivision B 3 f (1) (b) of this section exceeds the chlorite PMCL or the waterworks is required to conduct monitoring under subdivision B 3 f (1) (c) of this section, at which time the waterworks must revert to routine monitoring.

g. Bromate.

(1) Each community and nontransient noncommunity waterworks treatment plant using ozone, for disinfection or oxidation, must take one sample per month and analyze it for bromate. Waterworks must take samples monthly at the entrance to the distribution system while the ozonation system is operating under normal conditions.

(2) Waterworks required to analyze for bromate may reduce monitoring from monthly to once per quarter, if the waterworks demonstrates that the average source water bromide concentration is less than 0.05 mg/L based upon representative monthly bromide measurements for one year. The waterworks may remain on reduced bromate monitoring until the running annual average source water bromide concentration, computed quarterly, is equal to or greater than 0.05 mg/L based upon representative monthly measurements. If the running annual average source water bromide concentration is equal to or greater than 0.05 mg/L, the waterworks must resume routine monitoring required by subdivision B 3 g (1) of this section.

(3) Bromide. Waterworks required to analyze for bromate may reduce bromate monitoring from monthly to once per quarter, if the waterworks demonstrates that the average source water bromide concentration is less than 0.05 mg/L based upon representative monthly measurements for one year. The waterworks must continue bromide monitoring to remain on reduced bromate monitoring.

h. Monitoring requirements for disinfectant residuals.

(1) Chlorine and chloramines.

(a) Waterworks that use chlorine or chloramines must measure the residual disinfectant level in the distribution system at the same point in the distribution system and at the same time as total coliforms are sampled, as specified in subsection A of this section. Waterworks that use surface water or groundwater under the direct influence of surface water may use the results of residual disinfectant concentration sampling found in subdivision B 7 c (1) of this section in lieu of taking separate samples.

(b) Residual disinfectant level monitoring may not be reduced.

(2) Chlorine dioxide.

(a) Waterworks that use chlorine dioxide for disinfection or oxidation must take daily samples at the entrance to the distribution system. For any daily sample that exceeds the MRDL in Table 2.12, the waterworks must take samples in the distribution system the following day at the locations required by subdivision B 3 h (2) (b) of this section, in addition to the sample required at the entrance to the distribution system.

(b) On each day following a routine sample monitoring result that exceeds the MRDL in Table 2.12, the waterworks is required to take three chlorine dioxide distribution system samples. If chlorine dioxide or chloramines are used to maintain a disinfectant residual in the distribution system, or if chlorine is used to maintain a disinfectant residual in the distribution system and there are no disinfection addition points after the entrance to the distribution system (i.e., no booster chlorination), the waterworks must take three samples as close to the first customer as possible, at intervals of at least six hours. If chlorine is used to maintain a disinfectant residual in the distribution system and there are one or more disinfection addition points after the entrance to the distribution system (i.e., booster chlorination), the waterworks must take one sample at each of the following locations: as close to the first customer as possible, in a location representative of average residence time, and as close to the end of the distribution system as possible (reflecting maximum residence time in the distribution system).

(c) Chlorine dioxide monitoring may not be reduced.

i. Monitoring requirements for disinfection byproduct precursors (DBPP).

(1) Community or nontransient noncommunity waterworks using surface water or groundwater under the direct influence of surface water and using conventional filtration treatment (as defined in 12 VAC 5-590-10) must monitor each treatment plant for TOC no later than the point of combined filter effluent turbidity monitoring and representative of the treated water. All waterworks required to monitor under this subdivision (B 3 i (1)) must also monitor for TOC in the source water prior to any treatment at the same time as monitoring for TOC in the treated water. These samples (source water and treated water) are referred to as paired samples. At the same time as the source water sample is taken, all waterworks must monitor for alkalinity in the source water prior to any treatment. Waterworks must take one paired sample and one source water alkalinity sample per month per plant at a time representative of normal operating conditions and influent water quality.

(2) Community or nontransient noncommunity waterworks that use surface water or groundwater under the direct influence of surface water with an average treated water TOC of less than 2.0 mg/L for two consecutive years, or less than 1.0 mg/L for one year, may reduce monitoring for both TOC and alkalinity to one paired sample and one source water alkalinity sample per plant per quarter. The waterworks must revert to routine monitoring in the month following the quarter when the annual average treated water TOC equal to or greater than 2.0 mg/L.

j. Each waterworks required to monitor under subdivision B 3 of this section must develop and implement a monitoring plan. The waterworks must maintain the plan and make it available for inspection by the commissioner and the general public no later than 30 days following the applicable compliance dates in subdivision B 3 a of this section. All community or nontransient noncommunity waterworks that use surface water or groundwater under the direct influence of surface water serving more than 3,300 people must submit a copy of the monitoring plan to the commissioner no later than the date of the first report required under 12 VAC 5-590-530 A. The commissioner may also require the plan to be submitted by any other waterworks. After review, the commissioner may require changes in any plan elements. The plan must include at least the following elements:

(1) Specific locations and schedules for collecting samples for any parameters included in subdivision B 3 of this section.

(2) How the waterworks will calculate compliance with PMCLs, MRDLs, and treatment techniques.

(3) The sampling plan for a consecutive waterworks must reflect the entire consecutive distribution system.

4. Unregulated contaminants (UCs). All community and nontransient noncommunity waterworks shall sample for the contaminants listed in Table 2.6 and Table 2.7 as follows:

a. Table 2.6--Group A

(1) Owners of waterworks which use a surface water source in whole or in part shall sample at the entry points to the distribution system which is representative of each source, after treatment (hereafter called a sampling point). The minimum number of samples is one year of consecutive quarterly samples per sampling point beginning in accordance with Table 2.8.

(2) Owners of waterworks which use groundwater shall sample at points of entry to the distribution system which is representative of each source (hereafter called a sampling point). The minimum number of samples is one sample per sampling point beginning in accordance with Table 2.8.

(3) The commissioner may require a confirmation sample for positive or negative results.

(4) Waterworks serving less than 150 connections may inform the commissioner, in writing, that their waterworks is available for sampling instead of performing the required sampling.

(5) All waterworks required to sample under this section shall repeat the sampling at least every five years.

b. Table 2.6--Group B and Table 2.7

(1) The owner of each community and nontransient noncommunity waterworks owner shall take four consecutive quarterly samples at the entry points to the distribution system which is representative of each source (hereafter called a sampling point) for each contaminant listed in Table 2.6 Group B and report the results to the commissioner. Monitoring shall be completed by December 31, 1995.

(2) The owner of each community and nontransient noncommunity waterworks shall take one sample at each sampling point for each contaminant listed in Table 2.7 and report the results to the commissioner. Monitoring shall be completed by December 31, 1995.

(3) The owner of each community and nontransient noncommunity waterworks may apply to the commissioner for a waiver from the monitoring requirements of subdivisions B 4 b (1) and (2) of this section for the contaminants listed in Table 2.6 Group B and Table 2.7.

(4) The commissioner may grant a waiver for the requirement of subdivision B 4 b (1) of this section based on the criteria specified in subdivision B 2 f of this section. The commissioner may grant a waiver from the requirement of subdivision B 4 b (2) of this section if previous analytical results indicate contamination would not occur, provided this data was collected after January 1, 1990.

(5) If the waterworks utilizes more than one source and the sources are combined before distribution, the waterworks shall sample at an entry point to the distribution system during periods of normal operating conditions (i.e., when water is representative of all sources being used).

(6) The commissioner may require a confirmation sample for positive or negative results.

(7) Instead of performing the monitoring required by this section, the owner of a community waterworks or nontransient noncommunity waterworks serving fewer than 150 service connections may send a letter to the commissioner stating that the waterworks is available for sampling. This letter shall be sent to the commissioner by January 1, 1994. The waterworks shall not send such samples to the commissioner unless requested to do so by the commissioner.

(8) All waterworks required to sample under this section shall repeat the sampling at least every five years.

5. Repealed.

6. Monitoring requirements for lead and copper. The owners of all community and nontransient noncommunity waterworks shall monitor for lead and copper in tap water (subdivision B 6 a of this section), water quality (corrosion) parameters in the distribution system and at entry points (subdivision B 6 b of this section), and lead and copper in water supplies (subdivision B 6 c of this section). The monitoring requirements contained in this section are summarized in Appendix M.

a. Monitoring requirements for lead and copper in tap water.

(1) Sample site location.

(a) By the applicable date for commencement of monitoring under subdivision B 6 a (4) (a), each waterworks owner shall complete a materials evaluation of the distribution system in order to identify a pool of targeted sampling sites that meets the requirements of this section, and which is sufficiently large to ensure that the owner can collect the number of lead and copper tap samples required in subdivision B 6 a (3). All sites from which first draw samples are collected shall be selected from this pool of targeted sampling sites. Sampling sites may not include faucets that have point-of-use or point-of-entry treatment devices designed to remove inorganic contaminants.

(b) A waterworks owner shall use the information on lead, copper, and galvanized steel that the owner is required to collect when conducting a materials evaluation (reference Appendix B Corrosion). When this evaluation is insufficient to locate the requisite number of lead and copper sampling sites that meet the targeting criteria of this section, the owner shall review the sources of information listed below in order to identify a sufficient number of sampling sites. In addition, the owner shall seek to collect such information where possible in the course of its normal operations (e.g., checking service line materials when reading water meters or performing maintenance activities):

(i) All plumbing codes, permits, and records in the files of the building department(s) which indicate the plumbing materials that are installed within publicly and privately owned structures connected to the distribution system;

(ii) All inspections and records of the distribution system that indicate the material composition of the service connections that connect a structure to the distribution system; and

(iii) All existing water quality information, which includes the results of all prior analyses of the waterworks or individual structures connected to the waterworks, indicating locations that may be particularly susceptible to high lead or copper concentrations.

(c) The sampling sites selected for a community waterworks' sampling pool ("tier 1 sampling sites") shall consist of single family structures that:

(i) Contain copper pipes with lead solder installed between January 1983 and April 1986 or contain lead pipes; and/or

(ii) Are served by a lead service line.

NOTE: When multiple-family residences comprise at least 20% of the structures served by a waterworks, the waterworks may include these types of structures in its sampling pool.

(d) The owner of any community waterworks with insufficient tier 1 sampling sites shall complete the sampling pool with "tier 2 sampling sites," consisting of buildings, including multiple-family residences that:

(i) Contain copper pipes with lead solder installed between January 1983 and April 1986 or contain lead pipes; and/or

(ii) Are served by a lead service line.

(e) The owner of any community waterworks with insufficient tier 1 and tier 2 sampling sites shall complete the sampling pool with "tier 3 sampling sites," consisting of single family structures that contain copper pipes with lead solder installed before 1983. The owner of a community waterworks with insufficient tier 1, tier 2, and tier 3 sampling sites shall complete the sampling pool with representative sites throughout the distribution system. For the purpose of this paragraph, a representative site is a site in which the plumbing materials used at that site would be commonly found at other sites served by the waterworks.

(f) The sampling sites selected for a nontransient noncommunity waterworks ("tier 1 sampling sites") shall consist of buildings that:

(i) Contain copper pipes with lead solder installed between January 1983 and April 1986 or contain lead pipes; and/or

(ii) Are served by a lead service line.

(g) The owner of a nontransient noncommunity waterworks with insufficient tier 1 sites that meet the targeting criteria in subdivision B 6 a (1) (f) of this section shall complete the sampling pool with sampling sites that contain copper pipes with lead solder installed before 1983. If additional sites are needed to complete the sampling pool, the owner of a nontransient noncommunity waterworks shall use representative sites throughout the distribution system. For the purpose of this paragraph, a representative site is a site in which the plumbing materials used at that site would be commonly found at other sites served by the waterworks.

(h) The owner of any waterworks whose distribution system contains lead service lines shall draw 50% of the samples the owner collects during each monitoring period from sites that contain lead pipes, or copper pipes with lead solder, and 50% of the samples the owner collects from sites served by a lead service line. Any owner who cannot identify a sufficient number of sampling sites served by a lead service line shall collect first draw tap samples from all of the sites identified as being served by such lines.

(2) Sample collection methods.

(a) All tap samples for lead and copper, with the exception of lead service line samples collected under 12 VAC 5-590-420 E 3 and samples collected under subdivision B 6 a (2) (e) of this section, shall be first draw samples.

(b) Each first-draw tap sample for lead and copper shall be one liter in volume and have stood motionless in the plumbing system of each sampling site for at least six hours. First draw samples from residential housing shall be collected from the cold-water kitchen tap or bathroom sink tap. First-draw samples from a nonresidential building shall be one liter in volume and shall be collected at an interior tap from which water is typically drawn for consumption. Non-first-draw samples collected in lieu of first-draw samples pursuant to subdivision B 6 a (2) (e) of this section shall be one liter in volume and shall be collected at an interior tap from which water is typically drawn for consumption. First draw samples may be collected by the waterworks owner or the owner may allow residents to collect first draw samples after instructing the residents of the sampling procedures specified in this paragraph. To avoid problems of residents handling nitric acid, acidification of first draw samples may be done up to 14 days after the sample is collected. After acidification to resolubilize the metals, the sample must stand in the original container for the time specified in the approved EPA method before the sample can be analyzed. If an owner allows residents to perform sampling, the owner may not challenge, based on alleged errors in sample collection, the accuracy of sampling results.

(c) Each lead service line sample collected pursuant to 12 VAC 5-590-420 E 3 for the purpose of avoiding replacement shall be one liter in volume and have stood motionless in the lead service line for at least six hours. Lead service line samples shall be collected in one of the following three ways:

(i) At the tap after flushing the volume of water between the tap and the lead service line. The volume of water shall be calculated based on the interior diameter and length of the pipe between the tap and the lead service line;

(ii) Tapping directly into the lead service line; or

(iii) If the sampling site is a building constructed as a single-family residence, allowing the water to run until there is a significant change in temperature which would be indicative of water that has been standing in the lead service line.

(d) A waterworks owner shall collect each first draw tap sample from the same sampling site from which the owner collected a previous sample. If, for any reason, the owner cannot gain entry to a sampling site in order to collect a follow-up tap sample, the owner may collect the follow-up tap sample from another sampling site in the sampling pool as long as the new site meets the same targeting criteria, and is within reasonable proximity of the original site.

(e) The owner of a nontransient noncommunity waterworks, or a community waterworks that meets the criteria of 12 VAC 5-590-420 F 3 g (1) and (2) that does not have enough taps that can supply first-draw samples, as defined in subdivision B 6 a (2) (b) of this section, may apply to the district engineer in writing to substitute non-first-draw samples. If approved by the commissioner, such owners must collect as many first-draw samples from appropriate taps as possible and identify sampling times and locations that would likely result in the longest standing time for the remaining sites.

(3) Number of samples. Waterworks owners shall collect at least one sample during each monitoring period specified in subdivision B 6 a (4) of this section from the number of sites listed in the first column ("standard monitoring") of the table in this paragraph. The owner of a waterworks conducting reduced monitoring under subdivision B 6 a (4) (d) of this section shall collect at least one sample from the number of sites specified in the second column ("reduced monitoring") of the table in this paragraph during each monitoring period specified in subdivision B 6 a (4) (d) of this section. Such reduced monitoring sites shall be representative of the sites required for standard monitoring. The commissioner may specify sampling locations when a waterworks owner is conducting reduced monitoring. The table is as follows:

| System Size (Number of People Served) | Number of sites (Standard Monitoring) | Number of sites (Reduced Monitoring) |
| --- | --- | --- |
| >100,000 | 100 | 50 |
| 10,001-100,000 | 60 | 30 |
| 3,301 to 10,000 | 40 | 20 |
| 501 to 3,300 | 20 | 10 |
| 101 to 500 | 10 | 5 |
| ≤100 | 5 | 5 |

(4) Timing of monitoring.

(a) Initial tap sampling. The first six-month monitoring period for small (serving ≤3,300 population), medium-size (serving 3,301 to 50,000 population) and large waterworks (serving >50,000 population) shall be established by the commissioner.

(i) All large waterworks shall monitor during two consecutive six-month periods.

(ii) All small and medium-size waterworks shall monitor during each six-month monitoring period until: the waterworks exceeds the lead or copper action level and is therefore required to implement the corrosion control treatment requirements under 12 VAC 5-590-420 C, in which case the owner shall continue monitoring in accordance with subdivision B 6 a (4) (b) of this section, or the waterworks meets the lead and copper action levels during two consecutive six-month monitoring periods, in which case the owner may reduce monitoring in accordance with subdivision B 6 a (4) (d) of this section.

(b) Monitoring after installation of corrosion control and water supply (source water) treatment.

(i) The owner of any large waterworks which installs optimal corrosion control treatment pursuant to 12 VAC 5-590-420 C 2 d (4) shall monitor during two consecutive six-month monitoring periods by the date specified in 12 VAC 5-590-420 C 2 d (5).

(ii) The owner of any small or medium-size waterworks which installs optimal corrosion control treatment pursuant to 12 VAC 5-590-420 C 2 e (5) shall monitor during two consecutive six-month monitoring periods by the date specified in 12 VAC 5-590-420 C 2 e (6).

(iii) The owner of any waterworks which installs source water treatment pursuant to 12 VAC 5-590-420 D 1 c shall monitor during two consecutive six-month monitoring periods by the date specified in 12 VAC 5-590-420 D 1 d.

(c) Monitoring after the commissioner specifies water quality parameter values for optimal corrosion control. After the commissioner specifies the values for water quality control parameters under 12 VAC 5-590-420 C 1 f, the waterworks owner shall monitor during each subsequent six-month monitoring period, with the first monitoring period to begin on the date the commissioner specifies the optimal values under 12 VAC 5-590-420 C 1 f.

(d) Reduced monitoring.

(i) The owner of a small or medium-size waterworks that meets the lead and copper action levels during each of two consecutive six-month monitoring periods may reduce the number of samples in accordance with subdivision B 6 a (3) of this section, and reduce the frequency of sampling to once per year.

(ii) The owner of any waterworks that maintains the range of values for the water quality control parameters reflecting optimal corrosion control treatment specified by the commissioner under 12 VAC 5-590-420 C 1 f during each of two consecutive six-month monitoring periods may reduce the frequency of monitoring to once per year and to reduce the number of lead and copper samples in accordance with subdivision B 6 a (3) of this section if the owner receives written approval from the commissioner. The commissioner shall review monitoring, treatment, and other relevant information submitted by the waterworks owner in accordance with 12 VAC 5-590-530 D, and shall notify the waterworks owner in writing when a determination is made that the owner is eligible to commence reduced monitoring pursuant to this paragraph. The commissioner shall review, and where appropriate, revise its determination when the owner submits new monitoring or treatment data, or when other data relevant to the number and frequency of tap sampling becomes available.

(iii) The owner of a small or medium-size waterworks that meets the lead and copper action levels during three consecutive years of monitoring may reduce the frequency of monitoring for lead and copper from annually to once every three years. Any waterworks that maintains the range of values for the water quality control parameters reflecting optimal corrosion control treatment specified by the commissioner under 12 VAC 5-590-420 C 1 f during three consecutive years of monitoring may reduce the frequency of monitoring from annually to once every three years if the owner receives written approval from the commissioner. The commissioner shall review monitoring, treatment, and other relevant information submitted by the owner in accordance with 12 VAC 5-590-530 D and shall notify the waterworks owner in writing when a determination is made that the owner is eligible to commence reduced monitoring pursuant to this paragraph. The commissioner shall review, and where appropriate, revise its determination when the owner submits new monitoring or treatment data, or when other data relevant to the number and frequency of tap sampling becomes available.

(iv) The owner of a waterworks that reduces the number and frequency of sampling shall collect these samples from representative sites included in the pool of targeted sampling sites identified in subdivision B 6 a (1) of this section. Waterworks owners sampling annually or less frequently shall conduct the lead and copper tap sampling during the months of June, July, August or September. For a nontransient noncommunity waterworks that does not operate during the months of June through September, the commissioner shall designate an alternate monitoring period that represents a time of normal operation for the waterworks.

(v) The owner of any waterworks that demonstrates for two consecutive six-month monitoring periods that the tap water lead level computed under 12 VAC 5-590-410 E 3 is less than or equal to 0.005 mg/L and the tap water copper level computed under 12 VAC 5-590-410 E 3 is less than or equal to 0.65 mg/L may reduce the number of samples in accordance with subdivision B 6 a (3) of this section and reduce the frequency of sampling to once every three calendar years.

(vi) The owner of a small or medium-size waterworks subject to reduced monitoring that exceeds the lead or copper action level shall resume sampling in accordance with subdivision B 6 a (4) (c) of this section and collect the number of samples specified for standard monitoring under subdivision B 6 a (3) of this section. Such waterworks owner shall also conduct water quality parameter monitoring in accordance with subdivision B 6 b (2), (3), or (4) of this section (as appropriate) during the monitoring period in which the action level is exceeded. The owner of any such waterworks may resume annual monitoring for lead and copper at the tap at the reduced number of sites specified in subdivision B 6 a (3) of this section after it has completed two subsequent consecutive six-month rounds of monitoring that meet the criteria of subdivision B 6 a (4) (d) (i) of this section and/or may resume triennial monitoring for lead and copper at the reduced number of sites after it demonstrates through subsequent rounds of monitoring that it meets the criteria of either subdivision B 6 a (4) (d) (iii) or (v) of this section.

(vii) The owner of any waterworks subject to the reduced monitoring frequency that fails to operate at or above the minimum value or within the range of values for the water quality parameters specified by the commissioner under 12 VAC 5-590-420 C 1 f for more than nine days in any six-month period specified in subdivision B 6 b (4) of this section shall conduct tap water sampling for lead and copper at the frequency specified in subdivision B 6 a (4) (c) of this section, collect the number of samples specified for standard monitoring under subdivision B 6 a (3) of this section, and shall resume monitoring for water quality parameters within the distribution system in accordance with subdivision B 6 b (4) of this section. The owner of such a waterworks may resume reduced monitoring for lead and copper at the tap and for water quality parameters within the distribution system under the following conditions:

((a)) The waterworks owner may resume annual monitoring for lead and copper at the tap at the reduced number of sites specified in subdivision B 6 a (3) of this section after completion of two subsequent six-month rounds of monitoring that meet the criteria of subdivision B 6 a (4) (d) (ii) of this section and the owner has received written approval from the commissioner that it is appropriate to resume reduced monitoring on an annual frequency.

((b)) The waterworks owner may resume triennial monitoring for lead and copper at the tap at the reduced number of sites after demonstration through subsequent rounds of monitoring that it meets the criteria of either subdivision B 6 a (4) (d) (iii) or (v) of this section and the owner has received written approval from the commissioner that it is appropriate to resume triennial monitoring.

((c)) The waterworks owner may reduce the number of water quality parameter tap water samples required in accordance with subdivision B 6 b (5) (a) of this section and the frequency with which it collects such samples in accordance with subdivision B 6 b (5) (b) of this section. The owner of such a waterworks may not resume triennial monitoring for water quality parameters at the tap until it demonstrates, in accordance with the requirements of subdivision B 6 b (5) (b) of this section, that it has requalified for triennial monitoring.

(viii) The owner of any waterworks subject to a reduced monitoring frequency under subdivision B 6 a (4) (d) of this section that either adds a new source of water or changes any water treatment shall inform the district engineer in writing in accordance with 12 VAC 5-590-530 D 1 c. The commissioner may require the waterworks owner to resume sampling in accordance with subdivision B 6 a (4) (c) of this section and collect the number of samples specified for standard monitoring under subdivision B 6 a (3) of this section or take other appropriate steps such as increased water quality parameter monitoring or re-evaluation of its corrosion control treatment given the potentially different water quality considerations.

(5) Additional monitoring by waterworks owner. The results of any monitoring conducted in addition to the minimum requirements of this section shall be considered by the waterworks owner and the commissioner in making any determinations (i.e., calculating the 90th percentile lead or copper level) under this subpart.

(6) Invalidation of lead or copper tap water samples. A sample invalidated under this paragraph does not count toward determining lead or copper 90th percentile levels under 12 VAC 5-590-410 E or toward meeting the minimum monitoring requirements of subdivision B 6 a (3) of this section.

(a) The commissioner may invalidate a lead or copper tap water sample if at least one of the following conditions is met.

(i) The laboratory establishes that improper sample analysis caused erroneous results.

(ii) The commissioner determines that the sample was taken from a site that did not meet the site selection criteria of this section.

(iii) The sample container was damaged in transit.

(iv) There is substantial reason to believe that the sample was subject to tampering.

(b) The waterworks owner must report the results of all samples to the district engineer and all supporting documentation for samples the owner believes should be invalidated.

(c) To invalidate a sample under subdivision B 6 a (6) (a) of this section, the decision and the rationale for the decision must be documented in writing. The commissioner may not invalidate a sample solely on the grounds that a follow-up sample result is higher or lower than that of the original sample.

(d) The waterworks owner must collect replacement samples for any samples invalidated under this section if, after the invalidation of one or more samples, the owner has too few samples to meet the minimum requirements of subdivision B 6 a (3) of this section. Any such replacement samples must be taken as soon as possible, but no later than 20 days after the date the commissioner invalidates the sample or by the end of the applicable monitoring period, whichever occurs later. Replacement samples taken after the end of the applicable monitoring period shall not also be used to meet the monitoring requirements of a subsequent monitoring period. The replacement samples shall be taken at the same locations as the invalidated samples or, if that is not possible, at locations other than those already used for sampling during the monitoring period.

(7) Monitoring waivers for small systems. The owner of any small waterworks that meets the criteria of this section may apply to the commissioner to reduce the frequency of monitoring for lead and copper to once every nine years (i.e., a "full waiver") if the owner meets all of the materials criteria specified in subdivision B 6 a (7) (a) of this section and all of the monitoring criteria specified in subdivision B 6 a (7) (b) of this section. The owner of any small system that meets the criteria in subdivisions B 6 a (7) (a) and (b) of this section only for lead, or only for copper, may apply to the commissioner for a waiver to reduce the frequency of tap water monitoring to once every nine years for that contaminant only (i.e., a "partial waiver").

(a) Materials criteria. The waterworks owner must demonstrate that the distribution system and service lines and all drinking water supply plumbing, including plumbing conveying drinking water within all residences and buildings connected to the waterworks, are free of lead-containing materials and/or copper-containing materials, as those terms are defined in this paragraph, as follows:

(i) Lead. To qualify for a full waiver, or a waiver of the tap water monitoring requirements for lead (i.e., a "lead waiver"), the waterworks owner must provide certification and supporting documentation to the commissioner that the waterworks is free of all lead-containing materials, as follows:

((a)) It contains no plastic pipes that contain lead plasticizers, or plastic service lines that contain lead plasticizers; and

((b)) It is free of lead service lines, lead pipes, lead soldered pipe joints, and leaded brass or bronze alloy fittings and fixtures, unless such fittings and fixtures meet the specifications of any standard established pursuant to 42 USC § 300g-6(e) (SDWA § 1417(e)).

(ii) Copper. To qualify for a full waiver, or a waiver of the tap water monitoring requirements for copper (i.e., a "copper waiver"), the waterworks owner must provide certification and supporting documentation to the commissioner that the waterworks contains no copper pipes or copper service lines.

(b) Monitoring criteria for waiver issuance. The waterworks owner must have completed at least one six-month round of standard tap water monitoring for lead and copper at sites approved by the commissioner and from the number of sites required by subdivision B 6 a (3) of this section and demonstrate that the 90th percentile levels for any and all rounds of monitoring conducted since the owner became free of all lead-containing and/or copper-containing materials, as appropriate, meet the following criteria.

(i) Lead levels. To qualify for a full waiver, or a lead waiver, the waterworks owner must demonstrate that the 90th percentile lead level does not exceed 0.005 mg/L.

(ii) Copper levels. To qualify for a full waiver, or a copper waiver, the waterworks owner must demonstrate that the 90th percentile copper level does not exceed 0.65 mg/L.

(c) Commissioner approval of waiver application. The commissioner shall notify the waterworks owner of its waiver determination, in writing, setting forth the basis of its decision and any condition of the waiver. As a condition of the waiver, the commissioner may require the owner to perform specific activities (e.g., limited monitoring, periodic outreach to customers to remind them to avoid installation of materials that might void the waiver) to avoid the risk of lead or copper concentration of concern in tap water. The owner of a small waterworks must continue monitoring for lead and copper at the tap as required by subdivisions B 6 a (4) (a) through (d) of this section, as appropriate, until it receives written notification from the commissioner that the waiver has been approved.

(d) Monitoring frequency for waterworks owners with waivers.

(i) A waterworks owner with a full waiver must conduct tap water monitoring for lead and copper in accordance with subdivision B 6 a (4) (d) (iv) of this section at the reduced number of sampling sites identified in subdivision B 6 a (3) of this section at least once every nine years and provide the materials certification specified in subdivision B 6 a (7) (a) of this section for both lead and copper to the commissioner along with the monitoring results.

(ii) A waterworks owner with a partial waiver must conduct tap water monitoring for the waived contaminant in accordance with subdivision B 6 a (4) (d) (iv) of this section at the reduced number of sampling sites specified in subdivision B 6 a (3) of this section at least once every nine years and provide the materials certification specified in subdivision B 6 a (7) (a) of this section pertaining to the waived contaminant along with the monitoring results. Such a waterworks owner also must continue to monitor for the nonwaived contaminant in accordance with requirements of subdivisions B 6 a (4) (a) through (d) of this section, as appropriate.

(iii) If a waterworks owner with a full or partial waiver adds a new source of water or changes any water treatment, the owner must notify the commissioner in writing in accordance with 12 VAC 5-590-530 D 1 c. The commissioner has the authority to require the owner to add or modify waiver conditions (e.g., require recertification that the waterworks is free of lead-containing and/or copper-containing materials, require additional round(s) of monitoring), if it deems such modifications are necessary to address treatment or source water changes at the waterworks.

(iv) If a waterworks owner with a full or partial waiver becomes aware that it is no longer free of lead-containing or copper-containing materials, as appropriate, (e.g., as a result of new construction or repairs), the owner shall notify the commissioner in writing no later than 60 days after becoming aware of such a change.

(e) Continued eligibility. If the waterworks owner continues to satisfy the requirements of subdivision B 6 a (7) (d) of this section, the waiver will be renewed automatically, unless any of the conditions listed in subdivisions (i), (ii), or (iii) of this subdivision (e) occurs. A waterworks owner whose waiver has been revoked may reapply for a waiver at such time as it again meets the appropriate materials and monitoring criteria of subdivisions B 6 a (7) (a) and (b) of this section.

(i) A waterworks owner with a full waiver or a lead waiver no longer satisfies the materials criteria of subdivision B 6 a (7) (a) (i) of this section or has a 90th percentile lead level greater than 0.005 mg/L.

(ii) A waterworks owner with a full waiver or a copper waiver no longer satisfies the materials criteria of subdivision B 6 a (7) (a) (ii) of this section or has a 90th percentile copper level greater than 0.65 mg/L.

(iii) The commissioner notifies the waterworks owner, in writing, that the waiver has been revoked, setting forth the basis of the decision.

(f) Requirements following waiver revocation. A waterworks owner whose full or partial waiver has been revoked by the commissioner is subject to the corrosion control treatment and lead and copper tap water monitoring requirements, as follows:

(i) If the waterworks owner exceeds the lead and/or copper action level, the owner must implement corrosion control treatment in accordance with the deadlines specified in 12 VAC 5-590-420 C 2 e and any other applicable requirements of this subpart.

(ii) If the waterworks owner meets both the lead and the copper action level, the owner must monitor for lead and copper at the tap no less frequently than once every three years using the reduced number of sample sites specified in subdivision B 6 a (3) of this section.

(g) Pre-existing waivers. Waivers for small waterworks approved by the commissioner in writing prior to April 11, 2000, shall remain in effect under the following conditions:

(i) If the waterworks owner has demonstrated that it is both free of lead-containing and copper-containing materials, as required by subdivision B 6 a (7) (a) of this section and that its 90th percentile lead levels and 90th percentile copper levels meet the criteria of subdivision B 6 a (7) (b) of this section, the waiver remains in effect so long as the owner continues to meet the waiver eligibility criteria of subdivision B 6 a (7) (e) of this section. The first round of tap water monitoring conducted pursuant to subdivision B 6 a (7) (d) of this section shall be completed no later than nine years after the last time the owner has monitored for lead and copper at the tap.

(ii) If the waterworks owner has met the materials criteria of subdivision B 6 a (7) (a) of this section but has not met the monitoring criteria of subdivision B 6 a (7) (b) of this section, the owner shall conduct a round of monitoring for lead and copper at the tap demonstrating that it meets the criteria of subdivision B 6 a (7) (b) of this section no later than September 30, 2000. Thereafter, the waiver shall remain in effect as long as the owner meets the continued eligibility criteria of subdivision B 6 a (7) (e) of this section. The first round of tap water monitoring conducted pursuant to subdivision B 6 a (7) (d) of this section shall be completed no later than nine years after the round of monitoring conducted pursuant to subdivision B 6 a (7) (b) of this section.

b. Monitoring requirements for water quality parameters. The owners of all large waterworks, and all small and medium-size waterworks that exceed the lead or copper action level shall monitor water quality parameters in addition to lead and copper in accordance with this section. The requirements of this section are summarized in Appendix M.

(1) General requirements.

(a) Sample collection methods.

(i) Tap samples shall be representative of water quality throughout the distribution system taking into account the number of persons served, the different sources of water, the different treatment methods employed by the waterworks, and seasonal variability. Tap sampling under this section is not required to be conducted at taps targeted for lead and copper sampling under subdivision B 6 (a) (1) of this section. Waterworks owners may find it convenient to conduct tap sampling for water quality parameters at sites approved for coliform sampling.

(ii) Samples collected at the entry point(s) to the distribution system shall be from locations representative of each source after treatment. If a waterworks draws water from more than one source and the sources are combined before distribution, the waterworks owner must sample at an entry point to the distribution system during periods of normal operating conditions (i.e., when water is representative of all sources being used).

(b) Number of samples.

(i) Waterworks owners shall collect two tap samples for applicable water quality parameters during each monitoring period specified under subdivision B 6 b (2) through (5) of this section from the following number of sites.

| System Size (Number of People Served) | Number of Sites for Water Quality Parameters |
| --- | --- |
| >100,000 | 25 |
| 10,001-100,000 | 10 |
| 3,301 to 10,000 | 3 |
| 501 to 3,300 | 2 |
| 101 to 500 | 1 |
| ≤100 | 1 |

(ii) Except as provided in subdivision B 6 b (3) (c) of this section, waterworks owners shall collect two samples for each applicable water quality parameter at each entry point to the distribution system during each monitoring period specified in subdivision B 6 b (2) of this section. During each monitoring period specified in subdivision B 6 b (3) through (5) of this section, waterworks owners shall collect one sample for each applicable water quality parameter at each entry point to the distribution system.

(2) Initial sampling. The owners of all large waterworks shall measure the applicable water quality parameters as specified below at taps and at each entry point to the distribution system during each six-month monitoring period specified in subdivision B 6 a (4) (a) of this section. The owners of all small and medium-size waterworks shall measure the applicable water quality parameters at the locations specified below during each six-month monitoring period specified in subdivision B 6 a (4) (a) of this section during which the waterworks exceeds the lead or copper action level.

(a) At taps:

(i) pH;

(ii) alkalinity;

(iii) orthophosphate, when an inhibitor containing a phosphate compound is used;

(iv) silica, when an inhibitor containing a silicate compound is used;

(v) calcium;

(vi) conductivity; and

(vii) water temperature.

(b) At each entry point to the distribution system: all of the applicable parameters listed in subdivision B 6 b (2) (a) of this section.

(3) Monitoring after installation of corrosion control. The owner of any large waterworks which installs optimal corrosion control treatment pursuant to 12 VAC 5-590-420 C 2 d (4) shall measure the water quality parameters at the locations and frequencies specified below during each six-month monitoring period specified in subdivision B 6 a (4) (b) (i) of this section. The owner of any small or medium-size waterworks which installs optimal corrosion control treatment shall conduct such monitoring during each six-month monitoring period specified in subdivision B 6 a (4) (b) (ii) in which the waterworks exceeds the lead or copper action level.

(a) At taps, two samples for:

(i) pH;

(ii) alkalinity;

(iii) orthophosphate, when an inhibitor containing a phosphate compound is used;

(iv) silica, when an inhibitor containing a silicate compound is used;

(v) calcium, when calcium carbonate stabilization is used as part of corrosion control.

(b) Except as provided in subdivision B 6 b (3) (c) of this section, at each entry point to the distribution system, at least one sample no less frequently than every two weeks (bi-weekly) for:

(i) pH;

(ii) when alkalinity is adjusted as part of optimal corrosion control, a reading of the dosage rate of the chemical used to adjust alkalinity, and the alkalinity concentration; and

(iii) when a corrosion inhibitor is used as part of optimal corrosion control, a reading of the dosage rate of the inhibitor used, and the concentration of orthophosphate or silica (whichever is applicable).

(c) The owner of any ground water waterworks can limit entry point sampling described in subdivision B 6 b (3) (b) of this section to those entry points that are representative of water quality and treatment conditions throughout the waterworks. If water from untreated ground water sources mixes with water from treated ground water sources, the owner must monitor for water quality parameters both at representative entry points receiving treatment and representative entry points receiving no treatment. Prior to the start of any monitoring under this paragraph, the owner shall provide to the commissioner written information identifying the selected entry points and documentation, including information on seasonal variability, sufficient to demonstrate that the sites are representative of water quality and treatment conditions throughout the waterworks.

(4) Monitoring after the commissioner specifies water quality parameter values for optimal corrosion control. After the commissioner specifies the values for applicable water quality control parameters reflecting optimal corrosion control treatment under 12 VAC 5-590-420 C 1 f, the owners of all large waterworks shall measure the applicable water quality parameters in accordance with subdivision B 6 b (3) of this section and determine compliance with the requirements of 12 VAC 5-590-420 C 1 g every six months with the first six-month period to begin on the date the commissioner specifies the optimal values under 12 VAC 5-590-420 C 1 f. The owner of any small or medium-size waterworks shall conduct such monitoring during each six-month monitoring period specified in this subdivision in which the waterworks exceeds the lead or copper action level. For the owner of any such small and medium-size waterworks that is subject to a reduced monitoring frequency pursuant to subdivision B 6 a (4) (d) of this section at the time of the action level exceedance, the end of the applicable six-month period under this paragraph shall coincide with the end of the applicable monitoring period under subdivision B 6 a (4) (d) of this section. Compliance with the commissioner-designated optimal water quality parameter values shall be determined as specified under 12 VAC 5-590-420 C 1 g.

(5) Reduced monitoring.

(a) The owner of any waterworks that maintains the range of values for the water quality parameters reflecting optimal corrosion control treatment during each of two consecutive six-month monitoring periods under subdivision B 6 b (4) of this section shall continue monitoring at the entry point(s) to the distribution system as specified in subdivision B 6 b (3) (b) of this section. The owner of such waterworks may collect two tap samples for applicable water quality parameters from the following reduced number of sites during each six-month monitoring period.

| Size of Water System (Number of People Served) | Reduced Number of WQP Monitoring Sites |
| --- | --- |
| >100,000 | 10 |
| 10,001 to 100,000 | 7 |
| 3,301 to 10,000 | 3 |
| 501 to 3,300 | 2 |
| 101 to 500 | 1 |
| ≤100 | 1 |

(b) The owner of any waterworks that maintains the range of values for the water quality parameters reflecting optimal corrosion control treatment specified by the commissioner under 12 VAC 5-590-420 C 1f during three consecutive years of monitoring may reduce the frequency with which the owner collects the number of tap samples for applicable water quality parameters specified in subdivision B 6 b (5) (a) of this section from every six months to annually. The owner of any waterworks that maintains the range of values for the water quality parameters reflecting optimal corrosion control treatment specified by the commissioner under 12 VAC 5-590-420 C 1 f during three consecutive years of annual monitoring under this paragraph may reduce the frequency with which it collects the number of tap samples for applicable water quality parameters specified in subdivision B 6 a (5) (a) of this section from annually to every three years.

(c) The owner of a waterworks may reduce the frequency with which tap samples are collected for applicable water quality parameters specified in subdivision B 6 b (5) (a) of this section to every three years if the owner demonstrates during two consecutive monitoring periods that the tap water lead level at the 90th percentile is less than or equal to the PQL for lead (0.005 mg/L), that the tap water copper level at the 90th percentile is less than or equal to 0.65 mg/L for copper, and that the owner also has maintained the range of values for water quality parameters reflecting optimal corrosion control treatment specified by the commissioner under 12 VAC 5-590-420 C 1 f.

(d) The owner of a waterworks that conducts sampling annually shall collect these samples evenly throughout the year so as to reflect seasonal variability.

(e) The owner of any waterworks subject to the reduced monitoring frequency that fails to operate at or above the minimum value or within the range of values for the water quality parameters specified by the commissioner under 12 VAC 5-590-420 C 1 f for more than nine days in any six-month period specified in 12 VAC 5-590-420 C 1 g shall resume distribution system tap water sampling in accordance with the number and frequency requirements in subdivision B 6 b (4) of this section. Such a waterworks owner may resume annual monitoring for water quality parameters at the tap at the reduced number of sites specified in subdivision B 6 b (5) of this section after completion of two subsequent consecutive six-month rounds of monitoring that meet the criteria of that subdivision and/or may resume triennial monitoring for water quality parameters at the tap at the reduced number of sites after demonstration through subsequent rounds of monitoring that the criteria of either subdivision B 6 b (5) (b) or (c) of this section has been met.

(6) Additional monitoring by waterworks owners. The results of any monitoring conducted in addition to the minimum requirements of this section shall be considered by the waterworks owner and the commissioner in making any determinations under this section or 12 VAC 5-590-420 C 1.

c. Monitoring requirements for lead and copper in water supplies (source water).

(1) Sample location, collection methods, and number of samples.

(a) The owner of a waterworks that fails to meet the lead or copper action level on the basis of tap samples collected in accordance with subdivision B 6 a of this section shall collect lead and copper water supply samples in accordance with the following requirements regarding sample location, number of samples, and collection methods:

(i) The owner of a waterworks served by groundwater sources shall take a minimum of one sample at every entry point to the distribution system which is representative of each well after treatment (hereafter called a sampling point). The waterworks owner shall take one sample at the same sampling point unless conditions make another sampling point more representative of each source or treatment plant.

(ii) The owner of a waterworks served by surface water sources shall take a minimum of one sample at every entry point to the distribution system after any application of treatment or in the distribution system at a point which is representative of each source after treatment (hereafter called a sampling point). The waterworks owner shall take each sample at the same sampling point unless conditions make another sampling point more representative of each source or treatment plant. Note that for the purpose of this paragraph, a waterworks served by a surface water source includes waterworks served by a combination of surface and ground sources.

(iii) If a waterworks draws water from more than one source and the sources are combined before distribution, the waterworks owner must collect samples at an entry point to the distribution system during periods of normal operating conditions (i.e., when water is representative of all sources being used).

(iv) The commissioner may reduce the total number of samples that must be analyzed by allowing the use of compositing. Compositing of samples must be done by certified laboratory personnel. Composite samples from a maximum of five samples are allowed, provided that if the lead concentration in the composite sample is greater than or equal to 0.001 mg/L or the copper concentration is greater than or equal to 0.160 mg/L, then either a follow-up sample shall be collected and analyzed within 14 days at each sampling point included in the composite or if duplicates of or sufficient quantities from the original samples from each sampling point used in the composite are available, the waterworks owner may use these instead of resampling.

(b) Where the results of sampling indicate an exceedance of maximum permissible water supply levels established under 12 VAC 5-590-420 D 4, the commissioner may require that one additional sample be collected as soon as possible after the initial sample was taken (but not to exceed two weeks) at the same sampling point. If a commissioner required confirmation sample is taken for lead or copper, then the results of the initial and confirmation sample shall be averaged in determining compliance with the commissioner-specified maximum permissible levels. Any sample value below the method detection limit shall be considered to be zero. Any value above the method detection limit but below the PQL shall either be considered as the measured value or be considered one-half the PQL. The PQL for Lead is equal to 0.005 mg/l and the PQL for Copper is equal to 0.050 mg/l.

(2) Monitoring frequency after waterworks exceeds tap action level. The owner of any waterworks which exceeds the lead or copper action level at the tap shall collect one water supply sample from each entry point to the distribution system within six months after the exceedance.

(3) Monitoring frequency after installation of water supply treatment. The owner of any waterworks which installs water supply treatment pursuant to 12 VAC 5-590-420 D 1 c shall collect an additional water supply sample from each entry point to the distribution system during two consecutive six-month monitoring periods by the deadline specified in 12 VAC 5-590-420 D 1 d.

(4) Monitoring frequency after the commissioner specifies maximum permissible water supply lead and copper levels or determines that water supply treatment is not needed.

(a) A waterworks owner shall monitor at the frequency specified below in cases where the commissioner specifies maximum permissible water supply lead and copper levels under 12 VAC 5-590-420 D 4 or determines that the owner is not required to install water supply treatment under 12 VAC 5-590-420 D 2 (b).

(i) The owner of a waterworks using only groundwater shall collect samples once during the three-year compliance period in effect when the applicable commissioner determination under subdivision B 6 c (4) (a) of this section is made. Owners of such waterworks shall collect samples once during each subsequent compliance period.

(ii) The owner of a waterworks using surface water (or a combination of surface and groundwater) shall collect samples once during each year, the first annual monitoring period to begin on the date on which the applicable commissioner determination is made under subdivision B 6 c (4) (a) of this section.

(b) A waterworks owner is not required to conduct water supply sampling for lead and/or copper if the waterworks meets the action level for the specific contaminant in tap water samples during the entire water supply sampling period applicable to the waterworks under subdivision B 6 c (4) (a) (i) or (ii) of this section.

(5) Reduced monitoring frequency.

(a) The owner of a waterworks using only groundwater may reduce the monitoring frequency for lead and copper in water supplies to once during each nine-year compliance cycle if the waterworks owner meets one of the following criteria:

(i) The waterworks owner demonstrates that finished drinking water entering the distribution system has been maintained below the maximum permissible lead and copper concentrations specified by the commissioner under 12 VAC 5-590-420 D 4 during at least three consecutive compliance periods under subdivision B 6 c (4) (a) of this section; or

(ii) The commissioner has determined that water supply treatment is not needed and the waterworks owner demonstrates that, during the last three consecutive compliance periods in which sampling was conducted under subdivision B 6 c (4) (a) of this section, the concentration of lead in the water supply was less than or equal to 0.005 mg/L and the concentration of copper in the water supply was less than or equal to 0.65 mg/L.

(b) The owner of a waterworks using surface water (or a combination of surface and ground waters) may reduce the monitoring frequency for lead and copper in water supplies to once during each nine-year compliance cycle if the waterworks owner meets one of the following criteria:

(i) The waterworks owner demonstrates that finished drinking water entering the distribution system has been maintained below the maximum permissible lead and copper concentrations specified by the commissioner under 12 VAC 5-590-420 D 4 for at least three consecutive years; or

(ii) The commissioner has determined that water supply treatment is not needed and the waterworks owner demonstrates that, during the last three consecutive years, the concentration of lead in the water supply was less than or equal to 0.005 mg/L and the concentration of copper in the water supply was less than or equal to 0.65 mg/L.

(c) A waterworks that uses a new water supply is not eligible for reduced monitoring for lead and/or copper until concentrations in samples collected from the new supply during three consecutive monitoring periods are below the maximum permissible lead and copper concentrations specified by the commissioner in 12 VAC 5-590-420 D 1 e.

7. Monitoring filtration and disinfection.

a. The owner of a waterworks that uses a surface water source or a groundwater source under the direct influence of surface water and provides filtration treatment must monitor in accordance with this section beginning June 29, 1993, or when filtration is installed, whichever is later.

b. Turbidity measurements as required by 12 VAC 5-590-410 F shall be performed on representative samples of the filtered water every four hours (or more frequently) that the waterworks serves water to the public. A waterworks owner may substitute continuous turbidity monitoring for grab sample monitoring if it validates the continuous measurement for accuracy on a regular basis using a protocol approved by the Office. For any waterworks using slow sand filtration or filtration treatment other than conventional treatment, direct filtration, or diatomaceous earth filtration, the office may reduce the sampling frequency to once per day if it determines that less frequent monitoring is sufficient to indicate effective filtration performance. For waterworks serving 500 or fewer persons, the office may reduce the turbidity sampling frequency to once per day, regardless of the type of filtration treatment used, if the office determines that less frequent monitoring is sufficient to indicate effective filtration performance.

(1) In addition to the above, as of January 1, 2001, waterworks serving at least 10,000 people and as of January 1, 2005, waterworks serving less than 10,000 people supplied by surface water or groundwater under the direct influence of surface water using conventional filtration treatment or direct filtration must conduct continuous monitoring of turbidity for each individual filter, using an approved method in 12 VAC 5-590-440. The turbidimeter must be calibrated using the procedure specified by the manufacturer. Waterworks must record the results of individual filter turbidity monitoring every 15 minutes.

(2) If there is a failure in the continuous turbidity monitoring equipment, the waterworks must conduct grab sampling every four hours in lieu of continuous monitoring but for no more than five working days (for waterworks serving at least 10,000 people) or 14 days (for waterworks serving less than 10,000 people) following the failure of the equipment.

(3) If a waterworks serving less than 10,000 people consists of two or fewer filters, continuous monitoring of the combined filter effluent may be used in lieu of individual filter monitoring.

c. The residual disinfectant concentration of the water entering the distribution system shall be monitored continuously, and the lowest value shall be recorded each day, except that if there is a failure in the continuous monitoring equipment, grab sampling every four hours may be conducted in lieu of continuous monitoring, but for no more than five working days following the failure of the equipment, and owners of waterworks serving 3,300 or fewer persons may take grab samples in lieu of continuous monitoring on an ongoing basis at the frequencies each day prescribed below:

| Waterworks Size By Population | Samples/Day1 |
| --- | --- |
| 500 or less | 1 |
| 501 to 1,000 | 2 |
| 1,000 to 2,500 | 3 |
| 2,501 to 3,300 | 4 |

1The day's samples cannot be taken at the same time. The sampling intervals are subject to commissioner's review and approval.

If at any time the residual disinfectant concentration falls below 0.2 mg/L in a waterworks using grab sampling in lieu of continuous monitoring, the waterworks owner shall take a grab sample every four hours until the residual disinfectant concentration is equal to or greater than 0.2 mg/L.

(1) The residual disinfectant concentration must be measured at least at the same points in the distribution system and at the same time as total coliforms are sampled, as specified in subsection A of this section, except that the division may allow a waterworks owner which uses both a surface water source or a groundwater source under direct influence of surface water, and a groundwater source to take disinfectant residual samples at points other than the total coliform sampling points if the division determines that such points are more representative of treated (disinfected) water quality within the distribution system. Heterotrophic bacteria, measured as heterotrophic plate count (HPC) as specified in 12 VAC 5-590-420 B may be measured in lieu of residual disinfectant concentration.

(2) If the office determines, based on site-specific considerations, that a waterworks has no means for having a sample transported and analyzed for HPC by a certified laboratory under the requisite time and temperature conditions and that the waterworks is providing adequate disinfection in the distribution system, the requirements of subdivision B 7 (1) of this section do not apply to that waterworks.

d. The following information on the samples taken in the distribution system in conjunction with total coliform monitoring pursuant to 12 VAC 5-590-420 B shall be reported monthly to the division by the waterworks owner:

(1) Number of instances where the residual disinfectant concentration is measured;

(2) Number of instances where the residual disinfectant concentration is not measured but HPC is measured;

(3) Number of instances where the residual disinfectant concentration is measured but not detected and no HPC is measured;

(4) Number of instances where no residual disinfectant concentration is detected and where the HPC is greater than 500/mL;

(5) Number of instances where the residual disinfectant concentration is not measured and HPC is greater than 500/mL.

(6) For the current and previous month the waterworks serves water to the public, the value of "V" in percent in the following formula:

V = (c + d + e) / (a + b) X 100

where

a = the value in subdivision B 7 d (1) of this section,

b = the value in subdivision B 7 d (2) of this section,

c = the value in subdivision B 7 d (3) of this section,

d = the value in subdivision B 7 d (4) of this section,

e = the value in subdivision B 7 d (5) of this section,

(7) If the division determines, based on site-specific considerations, that a waterworks owner has no means for having a sample transported and analyzed for HPC by a certified laboratory within the requisite time and temperature conditions and that the waterworks is providing adequate disinfection in the distribution system, the requirements of subdivision B 7 c (1) of this section do not apply.

e. A waterworks owner need not report the data listed in 12 VAC 5-590-530 C 2 a if all data listed in 12 VAC 5-590-530 C 2 a through c remain on file at the waterworks and the division determines that the waterworks owner has submitted all the information required by 12 VAC 5-590-530 C 2 a through c for at least 12 months.

8. Operational. Waterworks owners may be required by the division to collect additional samples to provide quality control for any treatment processes that are employed.

C. Physical. All samples for turbidity analysis shall be taken at a representative entry point or points to the water distribution system unless otherwise specified. Turbidity samples shall be analyzed, at least once per day at all waterworks that use surface water sources or groundwater sources under the direct influence of surface water.

D. Radiological. The location of sampling points, the radionuclides measured in community waterworks, the frequency, and the timing of sampling within each compliance period shall be established or approved by the commissioner. The commissioner may increase required monitoring where necessary to detect variations within the waterworks. Failure to comply with the sampling schedules in this section will require public notification pursuant to 12 VAC 5-590-540.

Community waterworks owners shall conduct monitoring to determine compliance with the PMCLs in Table 2.5 and 12 VAC 5-590-400 in accordance with this section.

1. Monitoring and compliance requirements for gross alpha particle activity, radium-226, radium-228, and uranium.

a. Community waterworks owners must conduct initial monitoring to determine compliance with 12 VAC 5-590-400 B 2, 12 VAC 5-590-400 B 3 and 12 VAC 5-590-400 B 4 by December 31, 2007. For the purposes of monitoring for gross alpha particle activity, radium-226, radium-228, uranium, and beta particle and photon radioactivity in drinking water, "detection limit" is defined as in Appendix B of this chapter.

(1) Applicability and sampling location for existing community waterworks or sources. The owners of all existing community waterworks using ground water, surface water or waterworks using both ground and surface water must sample at every entry point to the distribution system that is representative of all sources being used under normal operating conditions. The community waterworks owner must take each sample at the same entry point unless conditions make another sampling point more representative of each source.

(2) Applicability and sampling location for new community waterworks or sources. All new community waterworks or community waterworks that use a new source of water must begin to conduct initial monitoring for the new source within the first quarter after initiating use of the source. Community waterworks owners must conduct more frequent monitoring when directed by the commissioner in the event of possible contamination or when changes in the distribution system or treatment processes occur which may increase the concentration of radioactivity in finished water.

b. Initial monitoring: Community waterworks owners must conduct initial monitoring for gross alpha particle activity, radium-226, radium-228, and uranium as follows:

(1) Community waterworks without acceptable historical data, as defined below, must collect four consecutive quarterly samples at all entry points before December 31, 2007.

(2) Grandfathering of data: The commissioner may allow historical monitoring data collected at an entry point to satisfy the initial monitoring requirements for that entry point, for the following situations:

(a) To satisfy initial monitoring requirements, a community waterworks owner having only one entry point to the distribution system may use the monitoring data from the last compliance monitoring period that began between June 2000 and December 8, 2003.

(b) To satisfy initial monitoring requirements, a community waterworks owner with multiple entry points and having appropriate historical monitoring data for each entry point to the distribution system may use the monitoring data from the last compliance monitoring period that began between June 2000 and December 8, 2003.

(3) For gross alpha particle activity, uranium, radium-226, and radium-228 monitoring, the commissioner may waive the final two quarters of initial monitoring for an entry point if the results of the samples from the previous two quarters are below the method detection limit specified in Appendix B.

(4) If the average of the initial monitoring results for an entry point is above the PMCL, the community waterworks owner must collect and analyze quarterly samples at that entry point until the waterworks owner has results from four consecutive quarters that are at or below the PMCL, unless the community waterworks owner enters into another schedule as part of a formal compliance agreement with the commissioner.

c. Reduced monitoring: The commissioner may allow community waterworks owners to reduce the future frequency of monitoring from once every three years to once every six or nine years at each entry point, based on the following criteria:

(1) If the average of the initial monitoring results for each contaminant (i.e., gross alpha particle activity, uranium, radium-226, or radium-228) is below the method detection limit specified in Appendix B, the waterworks owner must collect and analyze for that contaminant using at least one sample at that entry point every nine years.

(2) For gross alpha particle activity and uranium, if the average of the initial monitoring results for each contaminant is at or above the method detection limit specified in Appendix B but at or below 1/2 of the PMCL, the community waterworks owner must collect and analyze for that contaminant using at least one sample at that entry point every six years. For combined radium-226 and radium-228, the analytical results must be combined. If the average of the combined initial monitoring results for radium-226 and radium-228 is at or above the method detection limit specified in Appendix B but at or below 1/2 the PMCL, the community waterworks owner must collect and analyze for that contaminant using at least one sample at that entry point every six years.

(3) For gross alpha particle activity and uranium, if the average of the initial monitoring results for each contaminant is above 1/2 the PMCL but at or below the PMCL, the community waterworks owner must collect and analyze at least one sample at that entry point every three years. For combined radium-226 and radium-228, the analytical results must be combined. If the average of the combined initial monitoring results for radium-226 and radium-228 is above 1/2 the PMCL but at or below the MPCL, the community waterworks owner must collect and analyze at least one sample at that entry point every three years.

(4) Community waterworks owners must use the samples collected during the reduced monitoring period to determine the monitoring frequency for subsequent monitoring periods (e.g., if a community waterworks' entry point is on a nine-year monitoring period, and the sample result is above 1/2 the PMCL, then the next monitoring period for that entry point is three years).

(5) If a community waterworks owner has a monitoring result that exceeds the PMCL while on reduced monitoring, the community waterworks owner must collect and analyze quarterly samples at that entry point until the community waterworks owner has results from four consecutive quarters that are below the PMCL, unless the community waterworks enters into another schedule as part of a formal compliance agreement with the commissioner.

d. Compositing. To fulfill quarterly monitoring requirements for gross alpha particle activity, radium-226, radium-228, or uranium, a community waterworks owner may composite up to four consecutive quarterly samples from a single entry point if analysis is done within a year of the first sample. The commissioner will treat analytical results from the composited sample as the average analytical result to determine compliance with the PMCLs and the future monitoring frequency. If the analytical result from the composited sample is greater than 1/2 the PMCL, the commissioner may direct the community waterworks owner to take additional quarterly samples before allowing the community waterworks owner to sample under a reduced monitoring schedule.

e. A gross alpha particle activity measurement may be substituted for the required radium-226 measurement provided that the measured gross alpha particle activity does not exceed 5 pCi/L. A gross alpha particle activity measurement may be substituted for the required uranium measurement provided that the measured gross alpha particle activity does not exceed 15 pCi/L.

The gross alpha measurement shall have a confidence interval of 95% (1.65, where is the standard deviation of the net counting rate of the sample) for radium-226 and uranium. When a community waterworks owner uses a gross alpha particle activity measurement in lieu of a radium-226 and/or uranium measurement, the gross alpha particle activity analytical result will be used to determine the future monitoring frequency for radium-226 and/or uranium. If the gross alpha particle activity result is less than the method detection limit as specified in Appendix B, 1/2 the method detection limit will be used to determine compliance and the future monitoring frequency.

2. Monitoring and compliance requirements for beta particle and photon radioactivity. To determine compliance with the maximum contaminant levels in 12 VAC 5-590-400 B 5 for beta particle and photon radioactivity, a community waterworks owner must monitor at a frequency as follows:

a. Community waterworks owners (using surface or groundwater) designated by the commissioner as vulnerable must sample for beta particle and photon radioactivity. Community waterworks owners must collect quarterly samples for beta emitters and annual samples for tritium and strontium-90 at each entry point to the distribution system, beginning within one quarter after being notified by the commissioner. Community waterworks already designated by the commissioner must continue to sample until the commissioner reviews and either reaffirms or removes the designation.

(1) If the gross beta particle activity minus the naturally occurring potassium-40 beta particle activity at an entry point has a running annual average (computed quarterly) less than or equal to 50 pCi/L (screening level), the commissioner may reduce the frequency of monitoring at that entry point to once every three years. Community waterworks owners must collect all samples required in subdivision 2 a of this subsection during the reduced monitoring period.

(2) For community waterworks in the vicinity of a nuclear facility, the commissioner may allow the community waterworks owners to utilize environmental surveillance data collected by the nuclear facility in lieu of monitoring at the community waterworks' entry point(s), where the commissioner determines if such data is applicable to a particular community waterworks. In the event that there is a release from a nuclear facility, community waterworks owners which are using surveillance data must begin monitoring at the community waterworks' entry point(s) in accordance with subdivision 2 a of this subsection.

b. Community waterworks owners (using surface or groundwater) designated by the commissioner as utilizing waters contaminated by effluents from nuclear facilities must sample for beta particle and photon radioactivity. Community waterworks owners must collect quarterly samples for beta emitters and iodine-131 and annual samples for tritium and strontium-90 at each entry point to the distribution system, beginning within one quarter after being notified by the commissioner. Owners of community waterworks already designated by the commissioner as using waters contaminated by effluents from nuclear facilities must continue to sample until the commissioner reviews and either reaffirms or removes the designation.

(1) Quarterly monitoring for gross beta particle activity shall be based on the analysis of monthly samples or the analysis of a composite of three monthly samples. The former is recommended.

(2) For iodine-131, a composite of five consecutive daily samples shall be analyzed once each quarter. As directed by the commission, more frequent monitoring shall be conducted when iodine-131 is identified in the finished water.

(3) Annual monitoring for strontium-90 and tritium shall be conducted by means of the analysis of a composite of four consecutive quarterly samples or analysis of four quarterly samples. The latter procedure is recommended.

(4) If the gross beta particle activity minus the naturally occurring potassium-40 beta particle activity at a sampling point has a running annual average (computed quarterly) less than or equal to 15 pCi/L (screening level), the commissioner may reduce the frequency of monitoring at that sampling point to every three years. Community waterworks owners must collect all samples required in subdivision 2 b of this subsection during the reduced monitoring period.

(5) For community waterworks in the vicinity of a nuclear facility, the commissioner may allow the community waterworks owner to utilize environmental surveillance data collected by the nuclear facility in lieu of the monitoring at the community waterworks' entry point(s), where the commissioner determines such data is applicable to a particular waterworks. In the event that there is a release from a nuclear facility, community waterworks owners which are using surveillance data must begin monitoring at the community waterworks' entry point(s) in accordance with subdivision 2 b of this subsection.

c. Owners of community waterworks designated by the commissioner to monitor for beta particle and photon radioactivity can not apply to the commissioner for a waiver from the monitoring frequencies specified in subdivision 2 a or b of this subsection.

d. Community waterworks owners may analyze for naturally occurring potassium-40 beta particle activity from the same or equivalent sample used for the gross beta particle activity analysis. Community waterworks owners are allowed to subtract the potassium-40 beta particle activity value from the total gross beta particle activity value to determine if the screening level is exceeded. The potassium-40 beta particle activity must be calculated by multiplying elemental potassium concentrations (in mg/l) by a factor of 0.82.

e. If the gross beta particle activity minus the naturally occurring potassium-40 beta particle activity exceeds the appropriate screening level, an analysis of the sample must be performed to identify the major radioactive constituents present in the sample and the appropriate doses must be calculated and summed to determine compliance with 12 VAC 5-590-400 B 5 a, using the formula in 12 VAC 590-400 B 5 b. Doses must also be calculated and combined for measured levels of tritium and strontium to determine compliance.

f. Community waterworks owners must monitor monthly at the entry point(s) which exceed the maximum contaminant level in 12 VAC 5-590-400 B 5 beginning the month after the exceedance occurs. Community waterworks owners must continue monthly monitoring until the community waterworks has established, by a rolling average of three monthly samples, that the PMCL is being met. Community waterworks owners who establish that the PMCL is being met must return to quarterly monitoring until they meet the requirements set forth in subdivision 2 a (1) or 2 b (4) of this subsection.

3. General monitoring and compliance requirements for radionuclides.

a. The commissioner may require more frequent monitoring than specified in subdivisions 1 and 2 of this subsection, or may require confirmation samples at his discretion. The results of the initial and confirmation samples will be averaged for use in compliance determinations.

b. Each community waterworks owner shall monitor at the time designated by the commissioner during each compliance period.

c. Compliance: Compliance with 12 VAC 5-590-400 B 2 through 12 VAC 5-590-400 B 5 will be determined based on the analytical results(s) obtained at each entry point. If one entry point is in violation of a PMCL, the community waterworks is in violation of the PMCL.

(1) For community waterworks monitoring more than once per year, compliance with the PMCL is determined by a running annual average at each entry point. If the average of any entry point is greater than the PMCL, then the community waterworks is out of compliance with the PMCL.

(2) For community waterworks monitoring more than once per year, if any sample result will cause the running average to exceed the PMCL at any entry point, the community waterworks is out of compliance with the PMCL immediately.

(3) Community waterworks owners must include all samples taken and analyzed under the provisions of this section in determining compliance, even if that number is greater than the minimum required.

(4) If a community waterworks owner does not collect all required samples when compliance is based on a running annual average of quarterly samples, compliance will be based on the running average of the samples collected.

(5) If a sample result is less than the method detection limit as specified in Appendix B, zero will be used to calculate the annual average, unless a gross alpha particle activity is being used in lieu of radium-226 and/or uranium. If the gross alpha particle activity result is less than the method detection limit as specified in Appendix B, 1/2 the method detection limit will be used to calculate the annual average.

d. The commissioner has the discretion to delete results of obvious sampling or analytic errors.

e. If the PMCL for radioactivity set forth in 12 VAC 5-590-400 B through 12 VAC 5-590-400 B 5 is exceeded, the owner of a community waterworks must give notice to the commissioner pursuant to 12 VAC 5-590-530 and to the public as required by 12 VAC 5-590-540.

12 VAC 5-590-410. Determination of compliance.

For the purposes of determining compliance with a PMCL or action level, the following criteria shall be used:

A. Bacteriological results. Compliance with the PMCL for coliform bacteria shall be determined as specified in 12 VAC 5-590-380 C. Repeat samples shall be used as a basis for determining compliance with these regulations.

B. Inorganic chemicals.

1. Antimony, arsenic, asbestos, barium, beryllium, cadmium, cyanide (as free cyanide), chromium, fluoride, mercury, nickel, selenium, and thallium. Where the results of sampling for antimony, arsenic, asbestos, barium, beryllium, cadmium, cyanide (as free cyanide), chromium, fluoride, mercury, nickel, selenium, or thallium exceed the PMCL, the waterworks shall take a confirmation sample, at the same sampling point, within two weeks of notification of the analytical results of the first sample.

a. The results of the initial and confirmation samples shall be averaged to determine compliance with subdivision 1 c of this subsection. The commissioner has the discretion to delete results of obvious sampling errors.

b. The commissioner may require more frequent monitoring.

c. Compliance with antimony, arsenic, asbestos, barium, beryllium, cadmium, cyanide (as free cyanide), chromium, fluoride, mercury, nickel, selenium, and thallium in Table 2.2 of 12 VAC 5-590-440 shall be determined based on the analytical result(s) obtained at each sampling point.

(1) For waterworks which are conducting monitoring more frequently than annually, compliance with the PMCL for antimony, arsenic, asbestos, barium, beryllium, cadmium, cyanide (as free cyanide), chromium, fluoride, mercury, nickel, selenium, and thallium is determined by a running annual average at each sampling point. If the average at any sampling point is greater than the PMCL, then the waterworks is out of compliance. If any one sample would cause the annual average to be exceeded, then the waterworks is out of compliance immediately. Any sample below the method detection limit shall be calculated at zero for the purpose of determining the annual average. (NOTE: Refer to detection definition at 12 VAC 5-590-370 B 2 h.) If a waterworks owner fails to collect the required number of samples, compliance (average concentration) shall be based on the total number of samples collected.

(2) For waterworks which are monitoring annually, or less frequently, the waterworks is out of compliance with the PMCL for antimony, arsenic, asbestos, barium, beryllium, cadmium, cyanide (as free cyanide), chromium, fluoride, mercury, nickel, selenium, and thallium if the average of the original sample and a confirmation sample of a contaminant at any sampling point is greater than the PMCL. Waterworks monitoring annually or less frequently whose sample result exceeds the PMCL must begin quarterly sampling.  The waterworks shall not be considered in violation of the PMCL until it has completed one year of quarterly sampling. However, if the confirmation sample is not collected, the waterworks is in violation of the PMCL for antimony, arsenic, asbestos, barium, beryllium, cadmium, cyanide (as free cyanide), chromium, fluoride, mercury, nickel, selenium, or thallium. If a waterworks owner fails to collect the required number of samples, compliance (average concentration) shall be based on the total number of samples collected.

2. Nitrate and nitrite. Compliance with the PMCL is determined based on one sample from each sampling point if the levels of these contaminants are below the PMCLs. Where nitrate or nitrite sample results exceed the PMCL, the waterworks owner shall take a confirmation sample from the same sampling point that exceeded the PMCL within 24 hours of the waterworks' receipt of the analytical results of the first sample. The results of the initial and confirmation sample shall be averaged to determine compliance with this subdivision. Waterworks owners unable to comply with the 24-hour sampling requirement must immediately notify the consumers in the area served by the waterworks in accordance with 12 VAC 5-590-540. Waterworks exercising this option must take and analyze a confirmation sample within two weeks of notification of the analytical results of the first sample. The commissioner may require more frequent monitoring. The commissioner has the discretion to delete results of obvious sampling errors.

3. Compliance with the PMCL for arsenic is determined by the average of four analyses made pursuant to 12 VAC 5-590-370 B 1 d (6). When the average is rounded off to the same number of significant figures as the PMCL and exceeds the PMCL the owner shall notify the commissioner and give notice to the public pursuant to 12 VAC 5-590-540. Monitoring after public notification shall be at a frequency designated by the commissioner and shall continue until the PMCL has not been exceeded in two successive samples or until a monitoring schedule as a condition to a variance, exemption or enforcement action shall become effective.

C. Organic chemicals.

1. VOCs and SOCs. A confirmation sample shall be required for positive results for contaminants listed in Table 2.3. The commissioner has the discretion to delete results of obvious sampling errors from this calculation.

a. The results of the initial and confirmation sample shall be averaged to determine the waterworks' compliance in accordance with subdivision 1 b of this subsection.

b. Compliance with Table 2.3 shall be determined based on the analytical results obtained at each sampling point. Any samples below the detection limit shall be calculated as zero for the purposes of determining the annual average.  (Note: Refer to detection definition at 12 VAC 5-590-370 B 2 h.)  If a waterworks fails to collect the required number of samples, compliance (average concentration) will be based on the total number of samples collected.

(1) For waterworks which are conducting monitoring more frequently than annually, compliance is determined by a running annual average of all samples taken at each sampling point. If the annual average of any sampling point is greater than the PMCL, then the waterworks is out of compliance. If the initial sample or a subsequent sample would cause the annual average to be exceeded, then the waterworks is out of compliance immediately. Any samples below the detection limit shall be calculated as zero for purposes of determining the annual average. (Note: Refer to detection definition at 12 VAC 5-590-370 B 2 h.)

(2) If monitoring is conducted annually, or less frequently, the waterworks is out of compliance not in violation if the level of a contaminant at any sampling point is greater than the PMCL. The determination of compliance will be based on the average of the initial and confirmation sample sample is greater than the PMCL for that contaminant; however, the waterworks must begin quarterly sampling. The  waterworks will not be considered in violation of the PMCL until it has completed one year of quarterly sampling.  If any sample will cause the running annual average to exceed the PMCL at any sampling point, the waterworks is immediately out of compliance with the PMCL.

2. Disinfectant residuals, disinfection byproducts and disinfection byproduct precursors. Compliance with 12 VAC 5-590-370 B 3 a through B 3 k is as follows:

a. General requirements.

(1) Where compliance is based on a running annual average of monthly or quarterly samples or averages and the waterworks fails to monitor for TTHM, HAA5, or bromate, this failure to monitor will be treated as a monitoring violation for the entire period covered by the annual average. Where compliance is based on a running annual average of monthly or quarterly samples or averages and the waterworks' failure to monitor makes it impossible to determine compliance with MRDLs for chlorine and chloramines, this failure to monitor will be treated as a monitoring violation for the entire period covered by the annual average.

(2) All samples taken and analyzed under the provisions of this subpart must be included in determining compliance, even if that number is greater than the minimum required.

(3) If during the first year of monitoring under 12 VAC 5-590-370 B 3 b, any individual quarter's average will cause the running annual average of that waterworks to exceed the PMCL in Table 2.12 and Table 2.13, the waterworks is out of compliance at the end of that quarter.

b. Disinfection byproducts.

(1) TTHMs and HAA5.

(a) For waterworks monitoring quarterly, compliance with PMCLs in Table 2.13 must be based on a running annual arithmetic average, computed quarterly, of quarterly arithmetic averages of all samples collected by the waterworks as prescribed by 12 VAC 5-590-370 B 3 e (1).

(b) For waterworks monitoring less frequently than quarterly, the waterworks demonstrate PMCL compliance if the average of samples taken that year under the provisions of 12 VAC 5-590-370 B 3 e (1) does not exceed the PMCLs in Table 2.13. If the average of these samples exceeds the PMCL, the waterworks must increase monitoring to once per quarter per treatment plant and such a waterworks is not in violation of the PMCL until it has completed one year of quarterly monitoring, unless the result of fewer then four quarter of monitoring will cause the running annual average to exceed the PMCL, in which case the waterworks is in violation at the end of that quarter. Waterworks required to increase monitoring frequency to quarterly monitoring must calculate compliance by including the sample that triggered the increase monitoring plus the following three quarter of monitoring.

(c) If the running annual arithmetic average of quarterly averages covering any consecutive four-quarter period exceeds the PMCL in Table 2.12 and Table 2.13, the waterworks is in violation of the PMCL and must notify the public pursuant to 12 VAC 5-590-540 in addition to reporting to the commissioner pursuant to 12 VAC 5-590-530.

(d) If a waterworks fails to complete four consecutive quarters of monitoring, compliance with the PMCL in Table 2.13 for the last four-quarter compliance period must be based on an average of the available data.

(2) Bromate. Compliance must be based on a running annual arithmetic average, computed quarterly, of monthly samples (or, for months in which the waterworks takes more than one sample, the average of all samples taken during the month) collected by the waterworks as prescribed by 12 VAC 5-590-370 B 3 g. If the average of samples covering any consecutive four-quarter period exceeds the PMCL in Table 2.13, the waterworks is in violation of the PMCL and must notify the public pursuant to 12 VAC 5-590-540, in addition to reporting to the commissioner pursuant to 12 VAC 5-590-530. If a waterworks fails to complete 12 consecutive months' monitoring, compliance with the PMCL for the last four-quarter compliance period must be based on an average of the available data.

(3) Chlorite. Compliance must be based on an arithmetic average of each three sample set taken in the distribution system as prescribed by 12 VAC 5-590-370 B 3 f (1) (a), (b) and (c). If the arithmetic average of any three sample set exceeds the PMCL in Table 2.13, the waterworks is in violation of the PMCL and must notify the public pursuant to 12 VAC 5-590-540, in addition to reporting to the commissioner pursuant to 12 VAC 5-590-530.

c. Disinfectant residuals.

(1) Chlorine and chloramines.

(a) Compliance must be based on a running annual arithmetic average, computed quarterly, of monthly averages of all samples collected by the waterworks under 12 VAC 5-590-370 B 3 h (1) (a). If the average covering any consecutive four-quarter period exceeds the MRDL in Table 2.12, the waterworks is in violation of the MRDL and must notify the public pursuant to 12 VAC 5-590-540, in addition to reporting to the commissioner pursuant to 12 VAC 5-590-530.

(b) In cases where waterworks switch between the use of chlorine and chloramines for residual disinfection during the year, compliance must be determined by including together all monitoring results of both chlorine and chloramines in calculating compliance. Reports submitted pursuant to 12 VAC 5-590-530 must clearly indicate which residual disinfectant was analyzed for each sample.

(2) Chlorine dioxide.

(a) Acute violations. Compliance must be based on consecutive daily samples collected by the waterworks under 12 VAC 5-590-370 B 3 h (2) (a). If any daily sample taken at the entrance to the distribution system exceeds the MRDL in Table 2.12, and on the following day one (or more) of the three samples taken in the distribution system exceed the MRDL, the waterworks is in violation of the MRDL and must take immediate corrective action to lower the level of chlorine dioxide below the MRDL and must notify the public pursuant to the procedures for Tier 1 conditions in 12 VAC 5-590-540 in addition to reporting to the commissioner in pursuant to 12 VAC 5-590-530. Failure to take samples in the distribution system the day following an exceedance of the chlorine dioxide MRDL at the entrance to the distribution system will also be considered an MRDL violation and the waterworks must notify the public of the violation in accordance with the provisions for Tier 1 conditions in 12 VAC 5-590-540 in addition to reporting to the commissioner in pursuant to 12 VAC 5-590-530.

(b) Nonacute violations. Compliance must be based on consecutive daily samples collected by the waterworks under 12 VAC 5-590-370 B 3 h (2) (a). If any two consecutive daily samples taken at the entrance to the distribution system exceed the MRDL in Table 2.12 and all distribution system samples taken are below the MRDL, the waterworks is in violation of the MRDL and must take corrective action to lower the level of chlorine dioxide below the MRDL at the point of sampling and shall notify the public pursuant to the procedures for Tier 2 conditions in 12 VAC 5-590-540 in addition to reporting to the commissioner in pursuant to 12 VAC 5-590-530. Failure to monitor at the entrance to the distribution system the day following an exceedance of the chlorine dioxide MRDL at the entrance to the distribution system is also an MRDL violation and the waterworks must notify the public of the violation in accordance with the provisions for Tier 2 conditions in 12 VAC 5-590-540 in addition to reporting to the commissioner in pursuant to 12 VAC 5-590-530.

d. Disinfection byproduct precursors (DBPP). Compliance must be determined as specified by 12 VAC 5-590-420 H 3. Waterworks may begin monitoring to determine whether Step 1 TOC removals can be met 12 months prior to the compliance date for the waterworks. This monitoring is not required and failure to monitor during this period is not a violation. However, any waterworks that does not monitor during this period, and then determines in the first 12 months after the compliance date that it is not able to meet the Step 1 requirements in 12 VAC 5-590-420 H 2 b and must therefore apply for alternate minimum TOC removal (Step 2) requirements, is not eligible for retroactive approval of alternate minimum TOC removal (Step 2) requirements as allowed pursuant to 12 VAC 5-590-420 H 2 c and is in violation. Waterworks may apply for alternate minimum TOC removal (Step 2) requirements any time after the compliance date. For waterworks required to meet Step 1 TOC removals, if the value calculated under 12 VAC 5-590-420 H 3 a (4) is less than 1.00, the waterworks is in violation of the treatment technique requirements and must notify the public pursuant to 12 VAC 5-590-540 in addition to reporting to the commissioner pursuant to 12 VAC 5-90-530.

D. Radiological results (gross alpha, combined radium-226 and radium-228, uranium and man-made radioactivity). Compliance with the radiological Primary Maximum Contaminant Levels shall be in accordance with 12 VAC 5-590-370 D 3 c. Primary Maximum Contaminant Levels are indicated in subsection B of Table 2.5. Sampling for radiological analysis shall be in compliance with 12 VAC 5-590-370 D 1 and D 2. Furthermore, compliance shall be determined by rounding off results to the same number of significant figures as the Primary Maximum Contaminant Level PMCL for the substance in question.

E. Lead and copper action levels.

1. The lead action level is exceeded if the concentration of lead in more than 10% of tap water samples collected during any monitoring period conducted in accordance with 12 VAC 5-590-370 B 6 a is greater than 0.015 mg/l (i.e., if the "90th percentile" lead level is greater than 0.015 mg/l).

2. The copper action level is exceeded if the concentration of copper in more than 10% of tap water samples collected during any monitoring period conducted in accordance with 12 VAC 5-590-370 B 6 a is greater than 1.3 mg/l (i.e., if the "90th percentile" copper level is greater than 1.3 mg/l).

3. The 90th percentile lead and copper levels shall be computed as follows:

a. The results of all lead or copper samples taken during a monitoring period shall be placed in ascending order from the sample with the lowest concentration to the sample with the highest concentration. Each sampling result shall be assigned a number, ascending by single integers beginning with the number 1 for the sample with the lowest contaminant level. The number assigned to the sample with the highest contaminant level shall be equal to the total number of samples taken.

b. The number of samples taken during the monitoring period shall be multiplied by 0.9.

c. The contaminant concentration in the numbered sample yielded by the calculation in subdivision 3 b of this subsection is the 90th percentile contaminant level.

d. For waterworks serving fewer than 100 people that collect five samples per monitoring period, the 90th percentile is computed by taking the average of the highest and second highest concentrations.

F. Turbidity. The requirements in this subsection apply to filtered waterworks until June 29, 1993. The requirements in this section apply to unfiltered waterworks with surface water sources or groundwater sources under the direct influence of surface water that are required to install filtration equipment until June 29, 1993, or until filtration is installed, whichever is later. When a sample exceeds the PMCL for turbidity a confirmation sample shall be collected for analysis as soon as possible. In cases where a turbidimeter is required at the waterworks, the preferable resampling time is within one hour of the initial sampling. The repeat sample shall be the sample used for the purpose of calculating the monthly average. Compliance for public notification purposes shall be based on the monthly averages of the daily samples. However, public notification is also required if the average of samples taken on two consecutive days exceeds five NTU.

G. All analyses for PMCL and action level compliance determinations shall be consistent with current Environmental Protection Agency Regulations found at 40 CFR Part 141.

12 VAC 5-590-440. Analytical methods.

Analytical methods to determine compliance with the requirements of this chapter shall be those specified in the applicable edition of "Standard Methods for the Examination of Water and Wastewater," published by the American Public Health Association, the American Water Works Association, and the Water Pollution Control Federation; "Methods for Chemical Analysis of Water and Wastes," Environmental Protection Agency, Office of Technology Transfer, Washington, D.C. 20460, 1974; and "Methods for the Determination of Organic Compounds in Finished Drinking Water and Raw Source Water" (Sept 1986), EPA, Environmental Monitoring and Support Laboratory, Cincinnati, OH 45268 or in the case of primary maximum contaminant levels and lead and copper action levels, those methods shall be followed by the Division of Consolidated Laboratory Services and consistent with current U.S. Environmental Protection Agency regulations found at 40 CFR Part 141. All laboratories seeking certification to perform drinking water analyses must comply with 1 VAC 30-40 all appropriate regulations promulgated by the Department of General Services, Division of Consolidated Laboratory Services.

Table 2.2
Inorganic Chemicals.

| Substance | Primary Maximum Contaminant Level (mg/L) |
| --- | --- |
| Antimony | 0.006 |
| Arsenic (As) | 0.05 0.010*** |
| Asbestos | 7 Million Fibers/Liter (longer than 10 um) |
| Barium (Ba) | 2 |
| Beryllium | 0.004 |
| Cadium (Cd) | 0.005 |
| Chromium (Cr) | 0.1 |
| Cyanide (as free Cyanide) | 0.2 |
| Fluoride (F) | 4.0 # |
| Mercury (Hg) | 0.002 |
| Nickel | 0.1 |
| Nitrate (as N) | 10 ** |
| Nitrite (as N) | 1 |
| Total Nitrate and Nitrite (as N) | 10 |
| Selenium (Se) | 0.05 |
| Thallium | 0.002 |
| Substance | Secondary Maximum Contaminant Level (mg/L) |
| Chloride (Cl) | 250.0 |
| Corrosivity | Noncorrosive, See Appendix B |
| Fluoride | 2.0 |
| Foaming Agents | 0.5 * |
| Iron (Fe) | 0.3 |
| Manganese (Mn) | 0.05 |
| Sodium (Na) | No Limits Designated |
| Sulfate (SO4) | 250.0 |
| Zinc (Zn) | 5.0 |
| Substance | Action Level (mg/L) |
| Lead (Pb) | 0.015 |
| Copper (Cu) | 1.3 |

# Note. For artificially fluoridated waterworks the minimum concentration of fluoride should be 0.8 mg/L and the maximum should be 1.0 mg/L. The optimum control limit is 0.9 mg/L. (See Appendix B)

* Note. Concentration reported in terms of Methylene Blue Active Substances.

** Note. See Appendix B for Exception Regarding Noncommunity Waterworks.

*** Note. The PMCL for arsenic is 0.010 mg/L for community and nontransient noncommunity waterworks effective January 23, 2006.  Arsenic sampling results shall be reported to the nearest 0.001 mg/L.

EDITOR'S NOTE: Tables 2.3 through 2.13 are not amended and are intentionally omitted from this publication.

12 VAC 5-590-545. Consumer confidence reports.

A. Purpose and applicability.

1. Each community waterworks owner shall deliver to his customers an annual report that contains information on the quality of the water delivered by the waterworks and characterizes the risks, if any, from exposure to contaminants detected in the drinking water.

2. For the purpose of this section, customers are defined as billing units or service connections to which water is delivered by a community waterworks.

3. For the purpose of this section, a contaminant is detected when the laboratory reports the contaminant level as a measured level and not as nondetected (ND) or less than (<) a certain level.  The laboratory's analytical and reporting procedures shall have been in accordance with 12 VAC 5-590-440; laboratory certification requirements of the Commonwealth of Virginia, Department of General Services, Division of Consolidated Laboratory Services; and consistent with current U. S. Environmental Protection Agency regulations found at 40 CFR Part 141.

B. Effective dates.

1. Each existing community waterworks owner shall deliver his report by July 1 annually.

2. The owner of a new community waterworks shall deliver his first report by July 1 of the year after its first full calendar year in operation and annually thereafter.

3. The owner of a community waterworks that sells water to a consecutive waterworks shall deliver the applicable information necessary to comply with the requirements contained in this section to the consecutive waterworks by April 1 annually, or on a date mutually agreed upon by the seller and the purchaser and specifically included in a contract between the parties.

C. Content.

1. Each community waterworks owner shall provide his customers an annual report that contains the information on the source of the water delivered as follows:

a. Each report shall identify the source or sources of the water delivered by the community waterworks by providing information on:

(1) The type of the water (e.g., surface water, ground water); and

(2) The commonly used name, if any, and location of the body or bodies of water.

b. Where a source water assessment has been completed, the report shall:

(1) Notify consumers of the availability of the assessment;

(2) Describe the means to obtain the assessment; and

(3) Include a brief summary of the waterworks' susceptibility to potential sources of contamination.

c. The waterworks owner should highlight in the report significant sources of contamination in the source water area if such information is readily available.

2. For the purpose of compliance with this section, each report shall include the following definitions:

a. "Maximum contaminant level goal" or "MCLG" means the level of a contaminant in drinking water below which there is no known or expected risk to health.  MCLGs allow for a margin of safety (See 12 VAC 5-590-10).

b. "Maximum contaminant level" or "MCL" means the highest level of a contaminant that is allowed in drinking water.  MCLs are set as close to the MCLGs as feasible using the best available treatment technology (See 12 VAC 5-590-10).

c. A report for a community water system operating under a variance or an exemption issued by the commissioner under 12 VAC 5-590-140 and 12 VAC 5-590-150 shall include the following definition:  "Variances and exemptions" means state or EPA permission not to meet an MCL or a treatment technique under certain conditions.

d. A report that contains data on contaminants that EPA regulates using any of the following terms shall include the applicable definitions:

(1) "Treatment technique" means a required process intended to reduce the level of a contaminant in drinking water.

(2) "Action level" means the concentration of a contaminant that, if exceeded, triggers treatment or other requirements that a water system must follow.

(3) "Maximum residual disinfectant level goal" or "MRDLG" means the level of a drinking water disinfectant below which there is no known or expected risk to health.  MRDLGs do not reflect the benefits of the use of disinfectants to control microbial contaminants.

(4) "Maximum residual disinfectant level" or "MRDL" means the highest level of a disinfectant allowed in drinking water.  There is convincing evidence that addition of a disinfectant is necessary for control of microbial contaminants.

3. Information on detected contaminants.

a. This section specifies the requirements for information to be included in each report for the following contaminants:

(1) Contaminants subject to a PMCL, action level, maximum residual disinfectant level, or treatment technique as specified in 12 VAC 5-590-370;

(2) Unregulated contaminants subject to monitoring as specified in 12 VAC 5-590-370; and

(3) Disinfection byproducts or microbial contaminants, except Cryptosporidium, for which monitoring is required by Information Collection Rule (40 CFR 141.142 and 141.143 (7-1-97 Edition)), except as provided under subdivision 5 a of this subsection, and which are detected in the finished water.

b. The data relating to these contaminants shall be displayed in one table or in several adjacent tables.  Any additional monitoring results that a community waterworks owner chooses to include in the report shall be displayed separately.

c. The data shall be derived from data collected to comply with EPA and state monitoring and analytical requirements during the calendar year preceding the year the report is due, except that:

(1) Where a waterworks owner is allowed to monitor for contaminants specified in subdivision 3 a (1) and (3) of this subsection less often than once a year, the table or tables shall include the date and results of the most recent sampling, and the report shall include a brief statement indicating that the data presented in the report are from the most recent testing done in accordance with the regulations.  No data older than five years need be included.

(2) Results of monitoring in compliance with the Information Collection Rule (40 CFR 141.142 and 141.143 (7-1-97 Edition)) need only be included for five years from the date of last sample or until any of the detected contaminants becomes regulated and subject to routine monitoring requirements, whichever comes first.

d. For detected contaminants subject to a PMCL, action level, or treatment technique as specified in 12 VAC 5-590-370 and listed in Tables 2.1, 2.2 (Primary Maximum Contaminant Levels only), 2.3, 2.4 (Primary Maximum Contaminant Levels only), and 2.5, the table or tables must contain:

(1) The PMCL for that contaminant expressed as a number equal to or greater than 1.0 as provided in Appendix O, with an exception for beta/photon emitters.  When the detected level of beta/photon emitters has been reported in the units of pCi/L and does not exceed 50 pCi/L, the report may list the PMCL as 50 pCi/L. In this case, the waterworks owner shall include in the report the following footnote:  The PMCL for beta particles is 4 mrem/year.  EPA considers 50 pCi/L to be the level of concern for beta particles;

(2) The MCLG for that contaminant expressed in the same units as the PMCL as provided in Appendix O;

(3) If there is no PMCL for a detected contaminant, the table must indicate that there is a treatment technique, or specify the action level, applicable to that contaminant, and the report shall include the definitions for treatment technique and/or action level, as appropriate, specified in subdivision 3 d of this subsection;

(4) For contaminants subject to a PMCL, except turbidity and total coliforms, the highest contaminant level used to determine compliance and the range of detected levels as follows:

(a) When compliance with the PMCL is determined annually or less frequently, the highest detected level at any sampling point and the range of detected levels expressed in the same units as the PMCL.

(b) When compliance with the PMCL is determined by calculating a running annual average of all samples taken at a sampling point, the highest average of any of the sampling points and the range of all sampling points expressed in the same units as the PMCL.

(c) When compliance with the PMCL is determined on a systemwide basis by calculating a running annual average of all samples at all sampling points, the average and range of detection expressed in the same units as the PMCL.

(5) For turbidity, the highest single measurement and the lowest monthly percentage of samples meeting the turbidity limits specified in 12 VAC 5-590-420 for the filtration technology being used.  The report should include an explanation of the reasons for measuring turbidity;

(6) For lead and copper, the 90th percentile value of the most recent round of sampling and the number of sampling sites exceeding the action level;

(7) For total coliform:

(a) The highest monthly number of positive samples for waterworks collecting fewer than 40 samples per month;

(b) The highest monthly percentage of positive samples for systems collecting at least 40 samples per month;

(8) For fecal coliform, the total number of positive samples;

(9) The likely source or sources of detected contaminants.  Specific information regarding contaminants may be available in sanitary surveys and source water assessments, and should be used when available to the waterworks owner.  If the waterworks owner lacks specific information on the likely source, the report shall include one or more of the typical sources for that contaminant listed in Appendix O that are most applicable to the system.

e. If a community waterworks owner distributes water to his customers from multiple hydraulically independent distribution systems that are fed by different raw water sources:

(1) The table shall contain a separate column for each service area and the report shall identify each separate distribution system; or

(2) Waterworks owner shall produce a separate report tailored to include data for each service area.

f. The table or tables shall clearly identify any data indicating violations of PMCLs, MRDLs, or treatment techniques and the report shall contain a clear and readily understandable explanation of the violation including:

(1) The length of the violation;

(2) The potential adverse health effects using the relevant language of Appendix O; and

(3) Actions taken by the waterworks owner to address the violation.

g. For detected unregulated contaminants subject to monitoring as specified in 12 VAC 5-590-370 and listed in Tables 2.6 and 2.7, for which monitoring is required, the table or tables shall contain the average and range at which the contaminant was detected.  The report may include a brief explanation of the reasons for monitoring for unregulated contaminants.

4. Information on Cryptosporidium, radon, and other contaminants:

a. If the waterworks has performed any monitoring for Cryptosporidium, including monitoring performed to satisfy the requirements of the Informational Collection Rule (40 CFR 141.143 (7-1-97 Edition)), which indicates that Cryptosporidium may be present in the source water or the finished water, the report shall include:

(1) A summary of the results of the monitoring; and

(2) An explanation of the significance of the results.

b. If the waterworks has performed any monitoring for radon which indicates that radon may be present in the finished water, the report shall include:

(1) The results of the monitoring; and

(2) An explanation of the significance of the results.

c. If the waterworks owner has performed additional monitoring that indicates the presence of other contaminants in the finished water, the report should include any results that may indicate a health concern, as determined by the commissioner.  Detections above a proposed MCL or health advisory level may indicate possible health concerns.  For such contaminants, the report should include:

(1) The results of the monitoring; and

(2) An explanation of the significance of the results noting the existence of a health advisory or a proposed regulation.

5. Compliance with other regulations.

a. In addition to the requirements of subdivision 3 f of this subsection the report shall note any violation that occurred during the year covered by the report of a requirement listed below.

(1) Monitoring and reporting of compliance data;

(2) Filtration and disinfection prescribed by 12 VAC 5-590-420.  For waterworks owners who have failed to install adequate filtration or disinfection equipment or processes, or have had a failure of such equipment or processes which constitutes a violation, the report shall include the following language as part of the explanation of potential adverse health effects:  Inadequately treated water may contain disease-causing organisms.  These organisms include bacteria, viruses, and parasites, which can cause symptoms such as nausea, cramps, diarrhea, and associated headaches;

(3) Lead and copper control requirements prescribed by 12 VAC 5-590-370.  For waterworks owners who fail to take one or more of the prescribed actions, the report shall include the applicable language of Appendix O for lead, copper, or both;

(4) Treatment techniques for Acrylamide and Epichlorohydrin prescribed by 12 VAC 5-590-420 G. For waterworks owners who violate the requirements of that section, the report shall include the relevant language from Appendix O;

(5) Recordkeeping of compliance data;

(6) Special monitoring requirements for unregulated contaminants prescribed by 12 VAC 5-590-370 B 4 and for sodium;

(7) Violation of the terms of a variance, an exemption, or an administrative or judicial order.

b. The report shall contain:

(1) A clear and readily understandable explanation of the violation;

(2) Any potential adverse health effects; and

(3) The steps the waterworks owner has taken to correct the violation.

6. Variances and exemptions.  If a system is operating under the terms of a variance or an exemption issued by the commissioner under 12 VAC 5-590-140 and 12 VAC 5-590-150, the report shall contain:

a. An explanation of the reasons for the variance or exemption;

b. The date on which the variance or exemption was issued;

c. A brief status report on the steps the waterworks owner is taking to install treatment, find alternative sources of water, or otherwise comply with the terms and schedules of the variance or exemption; and

d. A notice of any opportunity for public input in the review or renewal of the variance or exemption.

7. Additional information.

a. The report shall contain a brief explanation regarding contaminants, which may reasonably be expected to be found in drinking water including bottled water.  This explanation shall include the exact language of subdivisions 8 a (1), (2) and (3) of this subsection or the waterworks owner shall use his own comparable language following approval by the commissioner.  The report also shall include the exact language of subdivision 8 a (4) of this subsection.

(1) The sources of drinking water (both tap water and bottled water) include rivers, lakes, streams, ponds, reservoirs, springs, and wells.  As water travels over the surface of the land or through the ground, it dissolves naturally occurring minerals and, in some cases, radioactive material, and can pick up substances resulting from the presence of animals or from human activity.

(2) Contaminants that may be present in source water include:  (i) microbial contaminants, such as viruses and bacteria, which may come from sewage treatment plants, septic systems, agricultural livestock operations, and wildlife; (ii) inorganic contaminants, such as salts and metals, which can be naturally occurring or result from urban stormwater runoff, industrial or domestic wastewater discharges, oil and gas production, mining, or farming; (iii) pesticides and herbicides, which may come from a variety of sources such as agriculture, urban stormwater runoff, and residential uses; (iv) organic chemical contaminants, including synthetic and volatile organic chemicals, which are byproducts of industrial processes and petroleum production, and can also come from gas stations, urban stormwater runoff, and septic systems; (v) radioactive contaminants, which can be naturally occurring or be the result of oil and gas production and mining activities.

(3) In order to ensure that tap water is safe to drink, EPA prescribes regulations that limit the amount of certain contaminants in water provided by public water systems.  FDA regulations establish limits for contaminants in bottled water which must provide the same protection for public health.

(4) Drinking water, including bottled water, may reasonably be expected to contain at least small amounts of some contaminants.  The presence of contaminants does not necessarily indicate that water poses a health risk.  More information about contaminants and potential health effects can be obtained by calling the Environmental Protection Agency's Safe Drinking Water Hotline (800-426-4791).

b. The report shall include the telephone number of the waterworks owner, operator, or designee of the community waterworks as a source of additional information concerning the report.

c. In communities with a large proportion of non-English speaking residents, as determined by the commissioner, the report shall contain information in the appropriate language or languages regarding the importance of the report or contain a telephone number or address where such residents may contact the system to obtain a translated copy of the report or assistance in the appropriate language.

d. The report shall include the following information about opportunities for public participation in decisions that may affect the quality of the water.  The waterworks owner should consider including the following additional relevant information:

(1) The time and place of regularly scheduled board meetings of the governing body which has authority over the waterworks.

(2) If regularly scheduled board meetings are not held, the name and telephone number of a waterworks representative who has operational or managerial authority over the waterworks.

e. The waterworks owner may include such additional information as he deems necessary for public education consistent with, and not detracting from, the purpose of the report.

D. Additional health information.

1. All reports shall prominently display the following language:  Some people may be more vulnerable to contaminants in drinking water than the general population.  Immuno-compromised persons such as persons with cancer who are undergoing chemotherapy, persons who have undergone organ transplants, people with HIV/AIDS or other immune system disorders, some elderly, and infants can be particularly at risk from infections.  These people should seek advice about drinking water from their health care providers.  EPA/CDC guidelines on appropriate means to lessen the risk of infection by Cryptosporidium and other microbial contaminants are available from the Safe Drinking Water Hotline (800-426-4791).

2. Starting February 22, 2002, a waterworks owner who detects arsenic at levels above 25 ug/l 0.005 mg/l, but equal to or below the PMCL of 0.010 mg/l, shall include in his report the following informational statement about arsenic:  EPA is reviewing the drinking water standard for arsenic because of special concerns that it may not be stringent enough.  Arsenic is a naturally occurring mineral known to cause cancer in humans at high concentrations. While your drinking water meets EPA’s standard for arsenic, it does contain low levels of arsenic. EPA’s standard balances the current understanding of arsenic’s possible health effects against the cost of removing arsenic from drinking water. EPA continues to research the health effects of low levels of arsenic, which is a mineral known to cause cancer in humans at high concentrations and is linked to other health effects such as skin damage and circulatory problems.

In lieu of the statement required in this subdivision, the waterworks owner may include his own educational statement after receiving approval from the commissioner.

A waterworks owner who detects arsenic levels above 0.010 mg/l must include the health effects language contained in Appendix O.

3. A waterworks owner who detects nitrate at levels above 5 mg/l, but below the PMCL, shall include in his report the following informational statement about the impacts of nitrate on children:  Nitrate in drinking water at levels above 10 ppm is a health risk for infants of less than six months of age.  High nitrate levels in drinking water can cause blue baby syndrome.  Nitrate levels may rise quickly for short periods of time because of rainfall or agricultural activity.  If you are caring for an infant you should ask advice from your health care provider.

In lieu of the statement required in this subdivision, the waterworks owner may include his own educational statement after receiving approval from the commissioner.

4. A waterworks owner who detects lead above the action level in more than 5.0%, and up to and including 10%, of homes sampled shall include the following informational statement about the special impact of lead on children:  Infants and young children are typically more vulnerable to lead in drinking water than the general population.  It is possible that lead levels at your home may be higher than at other homes in the community as a result of materials used in your home's plumbing.  If you are concerned about elevated lead levels in your home's water, you may wish to have your water tested and flush your tap for 30 seconds to two minutes before using tap water.  Additional information is available from the Safe Drinking Water Hotline (800-426-4791).

In lieu of the statement required in this subdivision, the waterworks owner may include his own educational statement after receiving approval from the commissioner.

5. Community waterworks owners who detect TTHM above 0.080 mg/l, but below the PMCL, as an annual average shall include health effects language prescribed by paragraph 73 of Appendix O.

E. Report delivery and recordkeeping.

1. Each community waterworks owner shall mail or otherwise directly deliver one copy of the report to each customer.

2. The waterworks owner shall make a good faith effort that shall be tailored to the consumers who are served by the system but are not bill paying customers, such as renters and workers.  This good faith effort shall include at least one, and preferably two or more, of the following methods appropriate to the particular waterworks:

a. Posting the reports on the Internet;

b. Mailing to postal patrons in metropolitan areas;

c. Advertising the availability of the report in the news media;

d. Publication in a local newspaper;

e. Posting in public places such as libraries, community centers, and public buildings;

f. Delivery of multiple copies for distribution by single-biller customers such as apartment buildings or large private employers;

g. Delivery to community organizations.

h. Other methods as approved by the commissioner.

3. No later than July 1 of each year the waterworks owner shall deliver a copy of the report to the appropriate Virginia Department of Health, Environmental Engineering Field Office, followed within three months by a certification that the report has been distributed to customers and that the information in the report is correct and consistent with the compliance monitoring data previously submitted to the commissioner.

4. No later than July 1 of each year the waterworks owner shall deliver the report to any other agency or clearinghouse specified by the commissioner.

5. Each community waterworks owner shall make the report available to the public upon request.

6. The owner of each community waterworks serving 100,000 or more persons shall post the current year's report to a publicly accessible site on the Internet.

7. Each community waterworks owner shall retain copies of the report for no less than three years.

12 VAC 5-590-820. General.

Preference shall be given to the best available sources of supply which present minimal risks of contamination from wastewaters and which contain a minimum of impurities that may be hazardous to health. In all cases, sources shall be selected and maintained on a basis which will assure that the water is continuously amenable to available treatment processes. In selecting the source of water to be developed, the designing engineer must prove to the satisfaction of the division commissioner that the water which is to be delivered to the consumers will meet the current requirements shall comply with all applicable PMCLs of the board with respect to bacteriological, physical, chemical and radiological qualities. All water samples for chemical, physical and radiological analyses must be submitted to the Commonwealth of Virginia, Department of General Services, Division of Consolidated Laboratory Services or to a testing laboratory certified by the Division of Consolidated Laboratory Services. All bacteriological analyses must be performed at laboratories in accordance with analysis 12 VAC 5-590-370 A and 12 VAC 5-590-480 B 2.

APPENDIX N. INORGANIC COMPOUNDS AND ORGANIC CHEMICALS

TABLE I

INORGANIC COMPOUNDS

| Contaminant | BAT(s) |
| --- | --- |
| Arsenicd | 1, 2, 5, 6, 7, 9, 12e |
| Antimony | 2, 7 |
| Asbestos | 2, 3, 8 |
| Barium | 5, 6, 7, 9 |
| Beryllium | 1, 2, 5, 6, 7 |
| Cadmium | 2, 5, 6, 7 |
| Chromium | 2, 5, 6b, 7 |
| Cyanide | 5, 7, 13 |
| Fluoride | 1, 7, 9 |
| Mercury | 2a, 4, 6a, 7a |
| Nickel | 5, 6, 7 |
| Nitrate | 5, 7, 9 |
| Nitrite | 5, 7 |
| Selenium | 1, 2c, 6, 7, 9 |
| Thallium | 1,5 |

Key to Best Available Technologies/Treatment Techniques

1. Activated Alumina

2. Coagulation/Filtration (except for waterworks serving less than 500 service connections)

3. Direct or Diatomite Filtration

4. Granular Activated Carbon

5. Ion Exchange

6. Lime Softening (except for waterworks serving less than 500 service connections)

7. Reverse Osmosis

8. Corrosion Control

9. Electrodialysis/Electrodialysis Reversing

10. Chlorine

11. Ultraviolet

12. Oxidation/Filtration

13. Alkaline Chlorination pH ≥ 8.5

NOTES ON BAT DESIGNATIONS

a. BAT only if influent mercury concentrations are less than or equal to 10 µg/l

b. BAT for Chromium III only

c. BAT for Selenium IV only

d. BATs for Arsenic V.  Preoxidation may be required to convert Arsenic III to Arsenic V.

e. To obtain high removals, iron to arsenic ratio must be at least  20:1.

TABLE II
ORGANIC CHEMICALS

| Contaminant | BAT(s) |
| --- | --- |
| Acrylamide | 3 |
| Alachlor | 1 |
| Aldicarb | 1 |
| Aldicarb sulfoxide | 1 |
| Aldicarb sulfone | 1 |
| Atrazine | 1 |
| Benzene | 1, 2 |
| Carbofuran | 1 |
| Carbon tetrachloride | 1, 2 |
| Chlordane | 1 |
| 2,4-D | 1 |
| Dibromochloropropane (DBCP) | 1, 2 |
| o-Dichlorobenzene | 1, 2 |
| p-Dichlorobenzene | 1, 2 |
| 1,2-Dichloroethane | 1, 2 |
| 1,1-Dichloroethylene | 1, 2 |
| cis-1,2-Dichloroethylene | 1, 2 |
| trans-1,2-Dichloroethylene | 1, 2 |
| 1,2-Dichloropropane | 1, 2 |
| Epichlorohydrin | 3 |
| Ethylene dibromide (EDB) | 1, 2 |
| Ethylbenzene | 1, 2 |
| Heptachlor | 1 |
| Heptachlor epoxide | 1 |
| Lindane | 1 |
| Methoxychlor | 1 |
| Monochlorobenzene | 1, 2 |
| PCBs | 1 |
| Pentachlorophenol | 1 |
| Styrene | 1, 2 |
| 2,4,5-TP (Silvex) | 1 |
| Tetrachloroethylene | 1, 2 |
| 1,1,1-Trichloroethane | 1, 2 |
| Trichloroethylene | 1, 2 |
| Toluene | 1, 2 |
| Toxaphene | 1 |
| Vinyl chloride | 2 |
| Xylenes (total) | 1, 2 |
| Benzo(a)pyrene | 1 |
| Dalapon | 1 |
| Dichloromethane | 2 |
| Di(2-ethylhexyl)adipate | 1, 2 |
| Di(2-ethylhexyl)phthalate | 1 |
| Dinoseb | 1 |
| Diquat | 1 |
| Endothall | 1 |
| Endrin | 1 |
| Glyphosate | 4 |
| Hexachlorobenzene | 1 |
| Hexachloropentadiene | 1, 2 |
| Oxamyl (Vydate) | 1 |
| Picloram | 1 |
| Simazine | 1 |
| 1,2,4-Trichlorobenzene | 1, 2 |
| 1,1,2-Trichloroethane | 1, 2 |
| 2,3,7,8-TCDD (Dioxin) | 1 |

Key to Best Available Technologies/Treatment Techniques

1. Granular Activated Carbon

2. Packed Tower Aeration

3. Polymer Addition Practices

4. Oxidation (chlorination, with the exception of water having cyanide (as free cyanide) exceeding 0.2 mg/l, or ozonation)

VA.R. Doc. No. R06-291; Filed July 6, 2006, 2:24 p.m.