TITLE 12. HEALTH

STATE BOARD OF HEALTH

Final Regulation

Title of Regulation:  12 VAC 5-590. Waterworks Regulations (adding 12 VAC 5-590-505).

Statutory Authority:  § 32.1-170 of the Code of Virginia.

Effective Date:  October 18, 2006.

Agency Contact:  Robert A. K. Payne, JD, Director of Regulatory Compliance, Department of Health, 109 Governor Street, Richmond, VA 23219, telephone (804) 864-7498, FAX (804) 864-7520, or email rob.payne@vdh.virginia.gov.

Summary:

The amendment requires community waterworks to develop and maintain an emergency management plan (EMP) to provide pure water during extended power outages of no less than five days. The plan will address procedures for obtaining and distributing potable water; notification procedures to public officials, customers and the media; emergency disinfection procedures; and telephone numbers for state regulatory personnel, waterworks personnel, and energy suppliers to the waterworks.

Summary of Public Comments and Agency's Response: A summary of comments made by the public and the agency's response may be obtained from the promulgating agency or viewed at the office of the Registrar of Regulations.

12 VAC 5-590-505. Emergency management plan for extended power outages.

A. Each community waterworks (including consecutive waterworks) shall develop and maintain an emergency management plan for extended power outages.

B. Each plan shall be kept current and shall be kept at a location that is readily accessible in the event of an extended power outage.

C. Each community waterworks shall certify in writing to the appropriate field office of the Office of Drinking Water in the Department of Health that the waterworks has completed such plan.

D. Each plan shall address the following where applicable:

1. Identification of the criteria (events, duration of power outage, etc.) that will initiate activation of the plan.

2. How the community waterworks will respond to an extended power outage for a minimum of five days.

3. Procedures for obtaining and distributing potable water in the event that primary source(s) becomes unavailable.

4. Notification procedures and example notices to the public and media (local radio stations, television stations, local newspapers, etc.) including conservation and boil water advisories.

5. Emergency disinfection procedures for distribution system(s) and storage tank(s).

6. The telephone number of the appropriate field office of the Office of Drinking Water in the Virginia Department of Health.

7. The names and telephone numbers of the waterworks personnel who should be notified.

8. The name and telephone number of the Local Emergency Coordinator designated by the Virginia Department of Emergency Management.

9. The names and telephone numbers of the electric power, natural gas, and propane distributors, or other energy supplier to the waterworks.

VA.R. Doc. No. R05-96; Filed August 21, 2006, 3:24 p.m.