TITLE 9. ENVIRONMENT

STATE WATER CONTROL BOARD

Final Regulation

Title of Regulation:  9 VAC 25-260. Water Quality Standards (amending 9 VAC 25-260-5, 9 VAC 25-260-50, 9 VAC 25-260-310, [ 9 VAC 25-260-350, 9 VAC 25-260-415, 9 VAC 25-260-420, 9 VAC 25-260-450, ] 9 VAC 25-260-480 [ , 9 VAC 25-260-540 ] ; adding 9 VAC 25-260-187).

Statutory Authority:  § 62.1-44.15 of the Code of Virginia; Clean Water Act (33 USC § 1251 et seq.); 40 CFR Part 131.

Effective Date:  Upon filing the notice of EPA approval with the Registrar of Regulation.

Agency Contact: Jean W. Gregory, Department of Environmental Quality, P.O. Box 10009, Richmond, VA 23240, telephone (804) 698-4113, FAX (804) 698-4116, or email jwgregory@deq.virginia.gov.

Summary:

Amendments to the state’s Water Quality Standards regulation add new numerical and narrative criteria to protect designated uses of man-made lakes and reservoirs as well as the two natural lakes in the state from the impacts of nutrients. The rulemaking also clarifies that the existing dissolved oxygen criteria during times of thermal stratification should only apply to the upper layer (epilimnion) in man-made lakes and reservoirs where nutrient enrichment is controlled by applicable nutrient criteria in 9 VAC 25-260-187.

Since publication of the proposal, the following changes have been made: reassignment of Lake Whitehurst from a cool to a warm water fishery and Burke Lake from a warm water to a fertilized fishery with the appropriate changes in the numeric criteria; clarification that water quality assessment of nutrient criteria (chlorophyll a and total phosphorus) will be based on the two most recent monitoring years with available data; addition of a process for confirmation of use impairments when the criteria are exceeded; and retention of the nutrient enriched waters designations in 9 VAC 25-260-350 for Smith Mountain Lake, Lake Chesdin, South Fork Rivanna Reservoir, and Claytor Lake.

In addition, as a result of the retention of the nutrient enriched waters designations in 9 VAC 25-260-350, proposed deletion of references to the designations in 9 VAC 25-260-415, 9 VAC 25-260-420, 9 VAC 25-260-450 and 9 VAC 25-260-540 were reinstated in the final regulation.

Summary of Public Comment and Agency Response: A summary of comments made by the public and the agency's response may be obtained from the promulgating agency or viewed at the Office of the Registrar of Regulations.

PART I.

SURFACE WATER STANDARDS WITH GENERAL, STATEWIDE APPLICATION.

9 VAC 25-260-5. Definitions.

The following words and terms when used in this chapter shall have the following meanings unless the context clearly indicates otherwise:

"Algicides" means chemical substances, most commonly copper-based, used as a treatment method to control algae growths.

"Board" means State Water Control Board.

"Chesapeake Bay and its tidal tributaries" means all tidally influenced waters of the Chesapeake Bay; western and eastern coastal embayments and tributaries; James, York, Rappahannock and Potomac Rivers and all their tidal tributaries to the end of tidal waters in each tributary (in larger rivers this is the fall line); and includes subdivisions 1, 2, 3, 4, 5, and 6 of 9 VAC 25-260-390, subdivisions 1, 1b, 1d, 1f and 1o of 9 VAC 25-260-410, subdivisions 5 and 5a of 9 VAC 25-260-415, subdivisions 1 and 1a of 9 VAC 25-260-440, subdivisions 2, 3, 3a, 3b and 3e of 9 VAC 25-260-520, and subdivision 1 of 9 VAC 25-260-530. This definition does not include free flowing sections of these waters.

"Criteria" means elements of the board's water quality standards, expressed as constituent concentrations, levels, or narrative statements, representing a quality of water that supports a particular use.  When criteria are met, water quality will generally protect the designated use.

"Designated uses" means those uses specified in water quality standards for each water body or segment whether or not they are being attained.

"Drifting organisms" means planktonic organisms that are dependent on the current of the water for movement.

"Epilimnion" means the upper layer of nearly uniform temperature in a thermally stratified man-made lake or reservoir listed in 9 VAC 25-260-187 B.

"Existing uses" means those uses actually attained in the water body on or after November 28, 1975, whether or not they are included in the water quality standards.

"Lacustrine" means the zone within a lake or reservoir that corresponds to nonflowing lake-like conditions such as those near the dam. The other two zones within a reservoir are riverine (flowing, river-like conditions) and transitional (transition from river to lake conditions).

"Man-made lake or reservoir" means a constructed impoundment.

"Mixing zone" means a limited area or volume of water where initial dilution of a discharge takes place and where numeric water quality criteria can be exceeded but designated uses in the water body on the whole are maintained and lethality is prevented.

"Natural lake" means an impoundment that is natural in origin. There are two natural lakes in Virginia: Mountain Lake in Giles County and Lake Drummond located within the boundaries of Chesapeake and Suffolk in the Great Dismal Swamp.

"Passing organisms" means free swimming organisms that move with a mean velocity at least equal to the ambient current in any direction.

"Primary contact recreation" means any water-based form of recreation, the practice of which has a high probability for total body immersion or ingestion of water (examples include but are not limited to swimming, water skiing, canoeing and kayaking).

"Pycnocline" means the portion of the water column where density changes rapidly because of salinity and/or temperature.  In an estuary the pycnocline is the zone separating deep, cooler more saline waters from the less saline, warmer surface waters. The upper and lower boundaries of a pycnocline are measured as a change in density per unit of depth that is greater than twice the change of the overall average for the total water column.

"Secondary contact recreation" means a water-based form of recreation, the practice of which has a low probability for total body immersion or ingestion of waters (examples include but are not limited to wading, boating and fishing).

"Swamp waters" means waters with naturally occurring low pH and low dissolved oxygen caused by: (i) low flow velocity that prevents mixing and reaeration of stagnant, shallow waters and (ii) decomposition of vegetation that lowers dissolved oxygen concentrations and causes tannic acids to color the water and lower the pH.

"Use attainability analysis" means a structured scientific assessment of the factors affecting the attainment of the use which may include physical, chemical, biological, and economic factors as described in 9 VAC 25-260-10 H.

"Water quality standards" means provisions of state or federal law which consist of a designated use or uses for the waters of the Commonwealth and water quality criteria for such waters based upon such uses. Water quality standards are to protect the public health or welfare, enhance the quality of water and serve the purposes of the State Water Control Law (§ 62.1-44.2 et seq. of the Code of Virginia) and the federal Clean Water Act (33 USC § 1251 et seq.).

# 9 VAC 25-260-50. Numerical criteria for dissolved oxygen, pH, and maximum temperature.***

| CLASS***** | DESCRIPTION OF WATERS | DISSOLVED OXYGEN (mg/l)**** | pH | Max. Temp. (°C) |
| --- | --- | --- | --- | --- |
|  |  | Min. | Daily Avg. |  |  |
| I | Open Ocean | 5.0 | -- | 6.0-9.0 | -- |
| II | Estuarine Waters (Tidal Water-Coastal Zone to Fall Line) | 4.0 | 5.0 | 6.0-9.0 | -- |
| III | Nontidal Waters (Coastal and Piedmont Zones) | 4.0 | 5.0 | 6.0-9.0 | 32 |
| IV | Mountainous Zones Waters | 4.0 | 5.0 | 6.0-9.0 | 31 |
| V | Stockable Trout Waters | 5.0 | 6.0 | 6.0-9.0 | 21 |
| VI | Natural Trout Waters | 6.0 | 7.0 | 6.0-9.0 | 20 |
| VII | Swamp Waters | * | * | 4.3-9.0* | ** |

*This classification recognizes that the natural quality of these waters may fall outside of the ranges for D.O. and pH set forth above as water quality criteria; therefore, on a case-by-case basis, criteria for specific Class VII waters can be developed that reflect the natural quality of the waterbody. Virginia Pollutant Discharge Elimination System limitations in Class VII waters shall meet pH of 6.0 - 9.0.

**Maximum temperature will be the same as that for Classes I through VI waters as appropriate.

***The water quality criteria in this section do not apply below the lowest flow averaged (arithmetic mean) over a period of seven consecutive days that can be statistically expected to occur once every 10 climatic years (a climatic year begins April 1 and ends March 31).

****See 9 VAC 25-260-55 for implementation of these criteria in waters naturally low in dissolved oxygen.

*****For a thermally stratified man-made lake or reservoir in Class III, IV, V or VI  waters that are listed in 9 VAC 25-260-187, these dissolved oxygen criteria apply only to the epilimnion in the lacustrine portion of the water body. When these waters are not stratified, the dissolved oxygen criteria apply throughout the water column.

PART II.

STANDARDS WITH MORE SPECIFIC APPLICATION.

9 VAC 25-260-187. Criteria for man-made lakes and reservoirs to protect aquatic life and recreational designated uses from the impacts of nutrients.

A. [ The list of man-made lakes and reservoirs in subsection B of this section are those waters previously monitored or planned for monitoring by the department The criteria in subsection B of this section apply to the man-made lakes and reservoirs listed in this section ]. Additional man-made lakes and reservoirs [ will may ] be added as new reservoirs are constructed or monitoring data become available from outside groups or future agency monitoring.

B. Whether or not algicide treatments are used, the chlorophyll a criteria apply to all waters on the list. The total phosphorus criteria apply only if a specific man-made lake or reservoir received algicide treatment during the monitoring and assessment period of April 1 through October 31.

The 90th percentile of the chlorophyll a data collected at one meter or less within the lacustrine portion of the man-made lake or reservoir between April 1 and October 31 [ in any given year ] shall not exceed the chlorophyll a criterion for that water body [ for two consecutive assessments. The in each of the two most recent monitoring years that chlorophyll a data are available. For a water body that received algicide treatment, the ] median of the total phosphorus data collected at one meter or less within the lacustrine portion of the man-made lake or reservoir between April 1 and October 31 [ in any given year ] shall not exceed the total phosphorus criterion [ for two consecutive assessments for a water body that received algicide treatment in each of the two most recent monitoring years that total phosphorus data are available ].

Monitoring data used for assessment shall be from sampling location(s) within the lacustrine portion where observations are evenly distributed over the seven months from April 1 through October 31 and are in locations that are representative, either individually or collectively, of the condition of the man-made lake or reservoir.

| Man-made Lake or Reservoir Name | Location | Chlorophyll a (µg/L) | Total Phosphorus (µg/L) |
| --- | --- | --- | --- |
| Able Lake | Stafford County | 35 | 40 |
| Airfield Pond | Sussex County | 35 | 40 |
| Amelia Lake | Amelia County | 35 | 40 |
| Aquia Reservoir (Smith Lake) | Stafford County | 35 | 40 |
| Bark Camp Lake (Corder Bottom Lake, Lee/Scott/Wise Lake) | Scott County | 35 | 40 |
| Beaver Creek Reservoir | Albemarle County | 35 | 40 |
| Beaverdam Creek Reservoir (Beaverdam Reservoir) | Bedford County | 35 | 40 |
| Beaverdam Reservoir | Loudoun County | 35 | 40 |
| Bedford Reservoir (Stony Creek Reservoir) | Bedford County | 35 | 40 |
| Big Cherry Lake | Wise County | 35 | 40 |
| Breckenridge Reservoir | Prince William County | 35 | 40 |
| Briery Creek Lake | Prince Edward County | 35 | 40 |
| Brunswick Lake (County Pond) | Brunswick County | 35 | 40 |
| Burke Lake | Fairfax County | [ 35 60 ] | 40 |
| Carvin Cove Reservoir | Botetourt County | 35 | 40 |
| Cherrystone Reservoir | Pittsylvania County | 35 | 40 |
| Chickahominy Lake | Charles City County | 35 | 40 |
| Claytor Lake | Pulaski County | 25 | 20 |
| Clifton Forge Reservoir (Smith Creek Reservoir) | Alleghany County | 35 | 20 |
| Coles Run Reservoir | Augusta County | 10 | 10 |
| Curtis Lake | Stafford County | 60 | 40 |
| Diascund Creek Reservoir | New Kent County | 35 | 40 |
| Douthat Lake | Bath County | 25 | 20 |
| Elkhorn Lake | Augusta County | 10 | 10 |
| Emporia Lake (Meherrin Reservoir) | Greensville County | 35 | 40 |
| Fairystone Lake | Henry County | 35 | 40 |
| Falling Creek Reservoir | Chesterfield County | 35 | 40 |
| Fort Pickett Reservoir | Nottoway/ Brunswick County | 35 | 40 |
| Gatewood Reservoir | Pulaski County | 35 | 40 |
| Georges Creek Reservoir | Pittsylvania County | 35 | 40 |
| Goose Creek Reservoir | Loudoun County | 35 | 40 |
| Graham Creek Reservoir | Amherst County | 35 | 40 |
| Great Creek Reservoir | Lawrenceville | 35 | 40 |
| Harrison Lake | Charles City County | 35 | 40 |
| Harwood Mills Reservoir | York County | 60 | 40 |
| Hidden Valley Lake | Washington County | 35 | 40 |
| Hogan Lake | Pulaski County | 35 | 40 |
| Holiday Lake | Appomattox County | 35 | 40 |
| Hungry Mother Lake | Smyth County | 35 | 40 |
| Hunting Run Reservoir | Spotsylvania County | 35 | 40 |
| J. W. Flannagan Reservoir | Dickenson County | 25 | 20 |
| Kerr Reservoir, Virginia portion (Buggs Island Lake) | Halifax County | 25 | 30 |
| Keysville Reservoir | Charlotte County | 35 | 40 |
| Lake Albemarle | Albemarle County | 35 | 40 |
| Lake Anna | Louisa County | 25 | 30 |
| Lake Burnt Mills | Isle of Wight County | 60 | 40 |
| Lake Chesdin | Chesterfield County | 35 | 40 |
| Lake Cohoon | Suffolk City | 60 | 40 |
| Lake Conner | Halifax County | 35 | 40 |
| Lake Frederick | Frederick County | 35 | 40 |
| Lake Gaston, (Virginia portion) | Brunswick County | 25 | 30 |
| Lake Gordon | Mecklenburg County | 35 | 40 |
| Lake Keokee | Lee County | 35 | 40 |
| Lake Kilby | Suffolk City | 60 | 40 |
| Lake Lawson | Virginia Beach City | 60 | 40 |
| Lake Manassas | Prince William County | 35 | 40 |
| Lake Meade | Suffolk City | 60 | 40 |
| Lake Moomaw | Bath County | 10 | 10 |
| Lake Nelson | Nelson County | 35 | 40 |
| Lake Nottoway (Lee Lake, Nottoway Lake) | Nottoway County | 35 | 40 |
| Lake Pelham | Culpeper County | 35 | 40 |
| Lake Prince | Suffolk City | 35 | 40 |
| Lake Robertson | Rockbridge County | 35 | 40 |
| Lake Smith | Virginia Beach City | 60 | 40 |
| Lake Whitehurst | Norfolk City | [ 25 60 ] | [ 20 40 ] |
| Lake Wright | Norfolk City | 60 | 40 |
| Laurel Bed Lake | Russell County | 35 | 40 |
| Lee Hall Reservoir (Newport News Reservoir) | Newport News City | 60 | 40 |
| Leesville Reservoir | Bedford County | 25 | 30 |
| Little Creek Reservoir | Virginia Beach City | 60 | 40 |
| Little Creek Reservoir | James City County | 25 | 30 |
| Little River Reservoir | Montgomery County | 35 | 40 |
| Lone Star Lake F (Crystal Lake) | Suffolk City | 60 | 40 |
| Lone Star Lake G (Crane Lake) | Suffolk City | 60 | 40 |
| Lone Star Lake I (Butler Lake) | Suffolk City | 60 | 40 |
| Lunga Reservoir | Prince William County | 35 | 40 |
| Lunenburg Beach Lake (Victoria Lake) | Town of Victoria | 35 | 40 |
| Martinsville Reservoir (Beaver Creek Reservoir) | Henry County | 35 | 40 |
| Mill Creek Reservoir | Amherst County | 35 | 40 |
| Modest Creek Reservoir | Town of Victoria | 35 | 40 |
| Motts Run Reservoir | Spotsylvania County | 25 | 30 |
| Mount Jackson Reservoir | Shenandoah County | 35 | 40 |
| Mountain Run Lake | Culpeper County | 35 | 40 |
| Ni Reservoir | Spotsylvania County | 35 | 40 |
| North Fork Pound Reservoir | Wise County | 35 | 40 |
| Northeast Creek Reservoir | Louisa County | 35 | 40 |
| Occoquan Reservoir | Fairfax County | 35 | 40 |
| Pedlar Lake | Amherst County | 25 | 20 |
| Philpott Reservoir | Henry County | 25 | 30 |
| Phelps Creek Reservoir (Brookneal Reservoir) | Campbell County | 35 | 40 |
| Ragged Mountain Reservoir | Albemarle County | 35 | 40 |
| Rivanna Reservoir (South Fork Rivanna Reservoir) | Albemarle County | 35 | 40 |
| Roaring Fork | Pittsylvania County | 35 | 40 |
| Rural Retreat Lake | Wythe County | 35 | 40 |
| Sandy River Reservoir | Prince Edward County | 35 | 40 |
| Shenandoah Lake | Rockingham County | 35 | 40 |
| Silver Lake | Rockingham County | 35 | 40 |
| Smith Mountain Lake | Bedford County | 25 | 30 |
| South Holston Reservoir | Washington County | 25 | 20 |
| Speights Run Lake | Suffolk City | 60 | 40 |
| Spring Hollow Reservoir | Roanoke County | 25 | 20 |
| Staunton Dam Lake | Augusta County | 35 | 40 |
| Stonehouse Creek Reservoir | Amherst County | 60 | 40 |
| Strasburg Reservoir | Shenandoah County | 35 | 40 |
| Stumpy Lake | Virginia Beach | 60 | 40 |
| Sugar Hollow Reservoir | Albemarle County | 25 | 20 |
| Swift Creek Reservoir | Chesterfield County | 35 | 40 |
| Switzer Lake | Rockingham County | 10 | 10 |
| Talbott Reservoir | Patrick County | 35 | 40 |
| Thrashers Creek Reservoir | Amherst County | 35 | 40 |
| Totier Creek Reservoir | Albemarle County | 35 | 40 |
| Townes Reservoir | Patrick County | 25 | 20 |
| Troublesome Creek Reservoir | Bucking-ham County | 35 | 40 |
| Waller Mill Reservoir | York County | 25 | 30 |
| Western Branch Reservoir | Suffolk City | 25 | 20 |
| Wise Reservoir | Wise County | 25 | 20 |

[ C. When the board determines that the applicable criteria in subsection B of this section for a specific man-made lake or reservoir are exceeded, the board shall consult with the Department of Game and Inland Fisheries regarding the status of the fishery in determining whether or not the designated use for that water body is being attained. If the designated use of the subject water body is not being attained, the board shall assess the water body as impaired in accordance with § 62.1-44.19:5 of the Code of Virginia. If the designated use is being attained, the board shall assess the water body as impaired in accordance with § 62.1-44.19:5 of the Code of Virginia until site-specific criteria are adopted and become effective for that water body. ]

[ C. D. ] If the nutrient criteria specified for a man-made lake or reservoir in subsection B of this section do not provide for the attainment and maintenance of the water quality standards of downstream waters as required in 9 VAC 25-260-10 C, the nutrient criteria herein may be modified on a site-specific basis to protect the water quality standards of downstream waters.

9 VAC 25-260-310. Special standards and requirements.

The special standards are shown in small letters to correspond to lettering in the basin tables. The special standards are as follows:

a. Shellfish waters. In all open ocean or estuarine waters capable of propagating shellfish or in specific areas where public or leased private shellfish beds are present,

including those waters on which condemnation or restriction classifications are established by the State Department of Health, the following criteria for fecal coliform bacteria will apply:

The geometric mean fecal coliform value for a sampling station shall not exceed an MPN (most probable number) of 14 per 100 ml of sample and the 90th percentile shall not exceed 43 for a 5-tube, 3-dilution test or 49 for a 3-tube, 3-dilution test.

The shellfish area is not to be so contaminated by radionuclides, pesticides, herbicides, or fecal material that the consumption of shellfish might be hazardous.

b. Policy for the Potomac Embayments. At its meeting on September 12, 1996, the board adopted a policy (9 VAC 25-415, Policy for the Potomac Embayments) to control point source discharges of conventional pollutants into the Virginia embayment waters of the Potomac River, and their tributaries, from the fall line at Chain Bridge in Arlington County to the Route 301 bridge in King George County. The policy sets effluent limits for BOD5, total suspended solids, phosphorus, and ammonia, to protect the water quality of these high profile waterbodies.

c. Cancelled.

d. Cancelled.

e. Cancelled.

f. Cancelled.

g. Occoquan watershed policy. At its meeting on July 26, 1971 (Minute 10), the board adopted a comprehensive pollution abatement and water quality management policy for the Occoquan watershed. The policy set stringent treatment and discharge requirements in order to improve and protect water quality, particularly since the waters are an important water supply for Northern Virginia. Following a public hearing on November 20, 1980, the board, at its December 10-12, 1980 meeting, adopted as of February 1, 1981, revisions to this policy (Minute 20). These revisions became effective March 4, 1981. Additional amendments were made following a public hearing on August 22, 1990, and adopted by the board at its September 24, 1990, meeting (Minute 24) and became effective on December 5, 1990. Copies are available upon request from the Department of Environmental Quality.

h. Cancelled.

i. Cancelled.

j. Cancelled.

k. Cancelled.

l. Cancelled.

m. The following effluent limitations apply to wastewater treatment facilities in the entire Chickahominy watershed above Walker's Dam (this excludes effluents consisting solely of stormwater):

| CONSTITUENT | CONCENTRATION |
| --- | --- |
| 1. Biochemical Oxygen demand 5-day at 20 | 6.0 mg/l monthly average, with not more than 5% of individual samples to exceed 8.0 mg/l |
| 2. Settleable Solids | Not to exceed 0.1 ml/l |
| 3. Suspended Solids | 5.0 mg/l monthly average, with not more than 5% of individual samples to exceed 7.5 mg/l |
| 4. Ammonia Nitrogen | Not to exceed 2.0 mg/l as N |
| 5. Total Phosphorus | Not to exceed 0.1 mg/l monthly average for all discharges with the exception of Tyson Foods, Inc. which shall meet 0.3 mg/l monthly average and 0.5 mg/l daily maximum. |
| 6. Other Physical and Chemical Constituents | Other physical or chemical constituents not specifically mentioned will be covered by additional specifications as conditions detrimental to the stream arise. The specific mention of items 1 through 5 does not necessarily mean that the addition of other physical or chemical constituents will be condoned. |

n. No sewage discharges, regardless of degree of treatment, should be allowed into the James River between Bosher and Williams Island Dams.

o. The concentration and total amount of impurities in Tuckahoe Creek and its tributaries of sewage origin shall be limited to those amounts from sewage, industrial wastes, and other wastes which are now present in the stream from natural sources and from existing discharges in the watershed.

p. Cancelled.

q. Cancelled.

r. Cancelled.

s. Chlorides not to exceed 40 mg/l at any time.

t. Cancelled.

u. Maximum temperature for the New River Basin from West Virginia state line upstream to the Giles-Montgomery County line:

The maximum temperature shall be 27°C (81°F) unless caused by natural conditions; the maximum rise above natural temperatures shall not exceed 2.8°C (5°F).

This maximum temperature limit of 81°F was established in the 1970 water quality standards amendments so that Virginia temperature criteria for the New River would be consistent with those of West Virginia, since the stream flows into that state.

v. The maximum temperature of the New River and its tributaries (except trout waters) from the Montgomery-Giles County line upstream to the Virginia-North Carolina state line shall be 29°C (84°F).

w. Cancelled.

x. Clinch River from the confluence of Dumps Creek at river mile 268 at Carbo downstream to river mile 255.4. The special water quality criteria for copper (measured as total recoverable) in this section of the Clinch River are 12.4 μg/l for protection from chronic effects and 19.5 μg/l for protection from acute effects. These site-specific criteria are needed to provide protection to several endangered species of freshwater mussels.

y. Tidal freshwater Potomac River and tributaries that enter the tidal freshwater Potomac River from Cockpit Point (below Occoquan Bay) to the fall line at Chain Bridge. During November 1 through February 14 of each year the 30-day average concentration of total ammonia nitrogen (in mg N/L) shall not exceed, more than once every three years on the average, the following chronic ammonia criterion:

| ( | 0.0577 | + | 2.487 | ) | x 1.45(100.028(25-MAX)) |
| --- | --- | --- | --- | --- | --- |
|  | 1 + 107.688-pH |  | 1 + 10pH-7.688 |  |  |

MAX = temperature in °C or 7, whichever is greater.

The default design flow for calculating steady state waste load allocations for this chronic ammonia criterion is the 30Q10, unless statistically valid methods are employed which demonstrate compliance with the duration and return frequency of this water quality criterion.

z. A site specific dissolved copper aquatic life criterion of 16.3 μg/l for protection from acute effects and 10.5 μg/l for protection from chronic effects applies in the following area:

Little Creek to the Route 60 (Shore Drive) bridge including Little Channel, Desert Cove, Fishermans Cove and Little Creek Cove.

Hampton Roads Harbor including the waters within the boundary lines formed by I-664 (Monitor-Merrimac Bridge Tunnel) and I-64 (Hampton Roads Bridge Tunnel), Willoughby Bay and the Elizabeth River and its tidal tributaries.

This criterion reflects the acute and chronic copper aquatic life criterion for saltwater in 9 VAC 25-260-140 B X a water effect ratio. The water effect ratio was derived in accordance with 9 VAC 25-260-140 F.

aa. The following site-specific dissolved oxygen criteria apply to the tidal Mattaponi and Pamunkey Rivers and their tidal tributaries because of seasonal lower dissolved oxygen concentration due to the natural oxygen depleting processes present in the extensive surrounding tidal wetlands.  These criteria apply June 1 through September 30 to Chesapeake Bay segments MPNTF, MPNOH, PMKTF, PMKOH and are implemented in accordance with subsection D of 9 VAC 25-260-185. These criteria supersede the open water criteria listed in subsection A of 9 VAC 25-260-185.

| Designated use | Criteria Concentration/ Duration | Temporal Application |
| --- | --- | --- |
| Open Water | 30 day mean ≥ 4.0 mg/l | June 1 - September 30 |
|  | Instantaneous minimum ≥ 3.2 mg/l at temperatures <29oC Instantaneous minimum ≥ 4.3 mg/l at temperatures ≥ 29oC |  |

bb. The following site specific numerical chlorophyll a criteria apply March 1 through May 31 and July 1 through September 30 as seasonal means to the tidal James River (excludes tributaries) segments JMSTF2, JMSTF1, JMSOH, JMSMH, JMSPH and are implemented in accordance with subsection D of 9 VAC 25-260-185.

| Designated Use | Chlorophyll a µ/l | Chesapeake Bay Program Segment | Temporal Application |
| --- | --- | --- | --- |
| Open Water | 10 | JMSTF2 | March 1 - May 31 |
|  | 15 | JMSTF1 |  |
|  | 15 | JMSOH |  |
|  | 12 | JMSMH |  |
|  | 12 | JMSPH |  |
|  | 15 | JMSTF2 | July 1 - September 30 |
|  | 23 | JMSTF1 |  |
|  | 22 | JMSOH |  |
|  | 10 | JMSMH |  |
|  | 10 | JMSPH |  |

cc. For Mountain Lake in Giles County, chlorophyll a shall not exceed 6 µg/L at a depth of 6 meters and orthophosphate-P shall not exceed 8 µg/L at a depth of one meter or less.

dd. For Lake Drummond, located within the boundaries of Chesapeake and Suffolk in the Great Dismal Swamp, chlorophyll a shall not exceed 35 µg/L and total phosphorus shall not exceed 40 µg/L at a depth of one meter or less.

PART VIII.

NUTRIENT ENRICHED WATERS.

EDITOR'S NOTE: The proposed amendments to 9 VAC 25-260-350, 9 VAC 25-260-415, 9 VAC 25-260-420, 9 VAC 25-260-450, and 9 VAC 25-260-540, which appeared in 22:10 VA.R. 1497-1513 January 23, 2006, were not adopted by the board.

9 VAC 25-260-480. Chowan and Dismal Swamp (Albemarle Sound Subbasin).

Albemarle Sound Subbasin

| SEC. | CLASS | SP. STDS. | SECTION DESCRIPTION |
| --- | --- | --- | --- |
| 1 | II |  | Back Bay and its tributaries in the City of Virginia Beach to the Virginia-North Carolina state line and the Northwest River and its tidal tributaries from the Virginia-North Carolina state line to the free flowing portion, unless otherwise designated in this chapter and North Landing River and its tidal tributaries from the Virginia-North Carolina state line to the Great Bridge Lock. |
| 1a | III |  | The free flowing portions of streams in Section 1 and tributaries of Stumpy Lake. |
| 1b | III | PWS | Stumpy Lake (raw water supply for the City of Norfolk) and feeder streams to points 5 miles upstream. |
| 1c | II | PWS | Northwest River and its tributaries from the City of Chesapeake's raw water intake to points 5 miles upstream and points 5 miles downstream. |
| 2 | III |  | Intracoastal Waterway (portions not described in Section 1). |
| 3 | III | dd | Lake Drummond, including feeder ditches, and all interstate tributaries of the Dismal Swamp between Virginia and North Carolina. |

VA.R. Doc. No. R05-113; Filed August 28, 2006, 11:11 a.m.