TITLE 4. CONSERVATION AND NATURAL RESOURCES

VIRGINIA SOIL AND WATER CONSERVATION BOARD

Proposed Regulation

Title of Regulation: 4VAC50-20. Impounding Structure Regulations(amending 4VAC50-20-20 through 4VAC50-20-90, 4VAC50-20-150 through 4VAC50-20-180, 4VAC50-20-200 through 4VAC50-20-240, 4VAC50-20-260 through 4VAC50-20-320; adding 4VAC50-20-52, 4VAC50-20-54, 4VAC50-20-58, 4VAC50-20-105, 4VAC50-20-125, 4VAC50-20-155, 4VAC50-20-165, 4VAC50-20-175, 4VAC50-20-177, 4VAC50-20-330, 4VAC50-20-340, 4VAC50-20-350, 4VAC50-20-360, 4VAC50-20-370, 4VAC50-20-380, 4VAC50-20-390, 4VAC50-20-400; repealing 4VAC50-20-100, 4VAC50-20-110, 4VAC50-20-120, 4VAC50-20-130, 4VAC50-20-140, 4VAC50-20-250).

Statutory Authority: §10.1-605 of the Code of Virginia.

Public Hearing Information:

October 4, 2007 - 7 p.m. - Roanoke City Council Chambers, Noel C. Taylor Municipal Building, 215 Church Avenue Southwest, Roanoke, VA 24011

October 9, 2007 - 7 p.m. - Hampton City Hall, 22 Lincoln Street, 8th Floor, Hampton, VA 23669

October 10, 2007 - 7 p.m. - Henrico County Government Complex Board Room, 4301 East Parham Road, Richmond, VA 23228

October 11, 2007 - 7 p.m. - Augusta County Government Center, 18 Government Center Lane, Verona, VA 24482

October 16, 2007 - 7 p.m. - City of Manassas Council Chambers, 9027 Center Street, Manassas, VA 20110

Public Comments: Public comments may be submitted until 5 p.m. on October 19, 2007.

Agency Contact: David C. Dowling, Policy, Planning, and Budget Director, Department of Conservation and Recreation, 203 Governor Street, Suite 302, Richmond, VA 23219, telephone (804) 786-2291, FAX (804) 786-6141, or email david.dowling@dcr.virginia.gov.

Basis: The Virginia Dam Safety Act (§10.1-604 et seq. of the Code of Virginia) ensures public safety through the proper and safe design, construction, operation, and maintenance of impounding structures in the Commonwealth. This is accomplished through the effective administration of the Virginia Dam Safety Program (program).  Authority for the program rests with the Virginia Soil and Water Conservation Board (board) and it is administered on behalf of the board by the Department of Conservation and Recreation’s Division of Dam Safety and Floodplain Management.  The program focuses on enhancing public safety through bringing all impounding structures of regulated size under Regular Operation and Maintenance Certificates.

Pursuant to §10.1-605, the board is directed to promulgate regulations for impounding structures.

Purpose: As there have been no regulatory changes made to the impounding structure regulations since the late 1980’s except to update the definition of regulated dams to conform it with the 2001 legislative change in definition (Chapter 92 (SB1166) of the 2001 Virginia Acts of Assembly), it was determined that this body of regulations required a substantive review and potential revisions.  Since the 1980’s, public safety concerns have evolved and engineering and technology and methodologies have advanced.  These events have resulted in the need to consider amendments to the regulations.  Further with the significant revisions made to the Virginia Dam Safety Act during the 2006 legislative session (Chapter 30 (HB597) of the 2006 Virginia Acts of Assembly) it is necessary to update the regulations to reflect those revised and enhanced powers and authorities.  It has also been determined that the administration and implementation of the Dam Safety Program could be improved through regulatory updates and that the intent and procedures embodied within the regulations could be clarified for the regulated community’s and the public’s benefit.

For the purposes outlined above and most importantly for the purpose of protecting the safety and welfare of the public and their property from the impacts of a dam failure, this regulatory action amends the Virginia Soil and Water Conservation Board’s Impounding Structure Regulations to:

1. Revise the dam hazard potential classification system;

2. Specify that spillway design requirements are applicable to all state regulated dams;

3. Modify the spillway design requirements to enhance public safety and reduce subjectivity;

4. Allow for the potential reduction of the spillway design flood requirement through an incremental damage assessment for all qualified dams;

5. Establish dam break inundation zone mapping requirements;

6. Expand emergency action plan requirements for High and Significant Hazard Potential dams and emergency preparedness plan requirements for Low Hazard Potential dams;

7. Establish permit application fees for the administration of the Dam Safety Program that will create a stream of revenue sufficient to support an additional dam safety engineer;

8. Remove the forms that are incorporated by reference and move reporting standards into the regulations;

9. Create new definitions or modify current definitions;

10. Reorganize, clarify, and expand sections related to permitting procedures; and

11. Update sections related to inspections, enforcement, and unsafe conditions.

Making these key modifications to the regulations will result in a Dam Safety Program that will be better able to protect the public’s safety, treat all dam owners similarly and fairly in accordance with the regulations, increase awareness of dams and their potential impacts within local governments and their citizens, and help improve the administration of the program to the benefit of the public.  The implementation of the criteria established in this regulation should minimize dam failure and the potential significant impacts associated with such a failure.

It should also be noted that many of these impounding structures also have environmental benefits in that they serve as sediment retention basins thus improving water quality.  However, alternatively, the failure of such an impounding structure may result in significant downstream environmental damages should the sediment be released.

Substance:

Key provisions of this regulatory action include the following:

1. A revision of the dam classification system from four categories (Class I, II, III, and IV) to three hazard classifications (High, Significant, and Low). This will conform the classification categories to those used by federal agencies and many states.  Functionally, the change will primarily involve grouping Class III and Class IV dams together into the Low category.  Currently the Class IV dams do not have to have an engineer, an inspection, or an Emergency Action Plan (EAP).  It was determined that all dams should be regulated similarly for dam safety purposes.

2. A specification that the Spillway Design Flood requirements (Table 1) are applicable to all dams not just "new" (post July 1982) dams.  In addition, Table 1 is revised to:

a. Reflect the revised dam classifications.

b. Update spillway design requirements to enhance public safety and to move towards federal standards.

c. Eliminate spillway design flood ranges that may result in inconsistency in application.

d. Require that the spillway of all High hazard dams be engineered to pass the full Probable Maximum Flood.

e. Specify minimum thresholds for incremental damage assessment.  It was determined that for the purposes of public safety that all dams should be regulated in accordance with standardized spillway design requirements and evaluation procedures.

3. The creation of a new section that allows for the potential reduction of the spillway design flood requirement through an incremental damage assessment for those dams meeting the specified administrative requirements.  This would now be applicable to all eligible dams where previously it was only available to dams constructed prior to July 1982.  Additionally, it is specified that the spillway design flood shall not be reduced below the minimum threshold values as determined by Table 1. In consultation with the technical advisory committee, it was determined that the incremental damage assessment should be made available to all dam owners to see if a reduction in the required Spillway Design flood (SDF) could be considered where the breach of a dam would not significantly worsen downstream flooding.  It was determined that a minimum threshold be established below which the SDF could not be reduced to set out a baseline that adequately protects public safety.

4. The creation of a new section that sets out dam break inundation zone mapping requirements. In consultation with the TAC, it was determined that both for hazard potential classification determination for all dams and for Emergency Action Plans for High and Significant dams that a dam break inundation zone map should be required.  The map will specify the areas that might be inundated during both a sunny day failure and a probable maximum flood (PMF) failure in order to demonstrate the levels where failure of the dam does not further constitute a hazard to downstream life or property.  The areas to be impacted during a break should be the areas of focus for emergency warnings and evacuations.

5. A specification that for each Operation and Maintenance certificate (Regular or Conditional) issued, the impounding structure owner shall send a copy of the certificate to the appropriate local government(s) with planning and zoning responsibilities. As downstream development approved by a locality may result in the change in hazard potential classification of an upstream dam and for the need for the dam to upgrade its spillway design at a significant expense to the owner, this notification may result in localities making more informed zoning decisions regarding a development.

6. The development of language establishing a delayed effective date for certain dams determined to have an adequate spillway capacity prior to the effective date of these regulations but that would require modifications due to changes in the regulations.

a. It is specified that the owner shall submit to the Board an Alteration Permit Application and associated documents to address spillway capacity prior to the expiration of this Regular Operation and Maintenance Certificate or within three years of the effective date of these regulations, whichever is later.  As regular certificates are good for six years from time of issuance, this would mean that complete applications would be due no sooner than three years and no later than six years.

b. It is specified that the Alteration Permit Application shall contain a construction sequence with milestones for completing the necessary improvements within five years of Alteration Permit issuance. (NOTE: 8 to 11 years in total to come into compliance). In light of the costs associated with upgrading a dam to meet the new spillway design safety requirements and the time necessary to conduct the associated engineering studies and alteration activities, it was determined that a phased in effective date should be included in the regulations for dams that currently meet regulatory standards.

7. The creation of a new section expanding emergency action plan requirements for High and Significant Hazard Potential dams. A fundamental element of protecting against the loss of life that may occur upon the failure of an impounding structure is the development of an emergency action plan that may be successfully implemented.  The plan would be developed and periodically tested in coordination with all entities, jurisdictions, and agencies that would be affected by a dam failure or that have statutory responsibilities for warning, evacuation, and post-flood actions.

8. The creation of a new section establishing emergency preparedness plan requirements for each Low Hazard Potential dam. As low hazard dams do not pose the same risk to loss of life as higher hazard dams, it was determined that an abbreviated emergency preparedness plan should be required.  Such a plan would allow for contacts to downstream landowners that may sustain a loss of personal property should a dam fail (e.g., farmer losing livestock or machinery).

9. The creation of a series of new sections that cites the authority for the board to establish and collect application fees for the administration of the dam safety program, administrative review, certifications, and the repair and maintenance of dams and that establishes such fees. It is understood that the Commonwealth needs sufficient staff and fiscal resources to properly administer a regulatory program.  A publication by the Association of State Dam Safety Officials (Model State Dam Safety Program, Association of State Dam Safety Officials, 1998) states 10 state regulators are needed for every 250 dams.  The department currently regulates almost 600 dams and has in its inventory over 1,700 dams, a significant number of which should be regulated, with only four Regional Engineer positions and one Program Manager.  The staff workload is much higher than in other states.  The fees, which have been purposely set low to reduce constituent impacts, would generate sufficient revenue to fund approximately one engineer on an annual basis.

10. The removal of all forms currently incorporated by reference and incorporation of required elements of the forms into the regulations.  Recommended forms will still be available. This will allow for the modification and improvement of forms without going through a lengthy regulatory action.  The department will still utilize a public process to make substantial changes to the forms.

11. The provision of definitions or modifications to definitions for "Agricultural purpose," "Alteration," "Construction," "Dam break inundation zone," "Department," "Drill," "Emergency Action Plan or EAP," "Emergency Action Plan Exercise," "Emergency Preparedness Plan," "Freeboard," "Height," "Spillway," "Stage I condition," "Stage II condition," Stage III condition," "Sunny Day Dam Failure," and "Tabletop Exercise." In order to support the above-referenced amendments, the addition or alteration of definitions was necessary.

12. Reorganizes, clarifies, and expands multiple sections related to permits and repeals sections that are incorporated into the reorganized sections. In an effort to provide additional clarity to the permitting process, a number of sections related to permitting were reorganized.  It is hoped that these revised sections will provide better guidance to the regulated community as they pursue the necessary permits and seek additional information regarding the permitting processes.

13. The creation of a new section stating that dams operated primarily for agricultural purposes which are less than 25 feet in height or which create a maximum impoundment capacity smaller than 100 acre-feet are exempt from the regulations. This is to clarify the exemption contained in 4VAC50-20-30 and 4VAC50-20-50 and to set out exemption validation procedures and reporting form components.

14. Updates sections related to inspections, enforcement, and unsafe conditions to reflect changes in the Code pursuant to Chapter 30 (HB597) of the 2006 Virginia Acts of Assembly. These changes will conform the regulations to 2006 changes in the Virginia Dam Safety Act.

Issues:

The primary advantage of the proposed regulations is the enhancement of public safety.  The proposed regulations help promote the safe design, construction, alteration, maintenance, and operation of impounding structures in the Commonwealth of Virginia, and thus benefit private citizens, businesses, local governments, and the Commonwealth as a whole.  The proposed regulations also track federal standards closer in an effort to improve public safety.  The Ad Hoc Dam Safety Study Committee, which was formed at the request of the Virginia Soil and Water Conservation Board, observed in its April 30, 2005, report that "[m]any of the nation’s dams, some originally built in the 1950s and 1960s, are in need of significant maintenance and/or redesign and upgrading.  As a result of their age and unusually heavy rain events, a number of dams have failed and resulted in significant downstream damage, death or injury."  Maintaining the regulations as they currently are will significantly hamper the efforts of the board to strengthen the Dam Safety Program and to promote the safety of impounding structures in the Commonwealth.

In addition, the proposed regulations provide some environmental benefit.  Impounding structures often are constructed as retention devices for silt and other materials; ensuring their safe operation and maintenance prevents these pollutants from being released into downstream water bodies and environments.

Failure of dams or living downstream of dams that are in need of upgrades may also impact property and insurance values.  Implementation of these regulations will reduce such dam failures.

Finally, the current action is intended to increase user-friendliness of many aspects of the Dam Safety Program.  Vague and confusing references within the regulations have been clarified or removed where possible, and outdated required forms have been removed from the regulations to permit more frequent updates in order to enhance clarity and usefulness.  In addition, confusing and conflicting provisions have been amended to allow for clarity and ease of understanding.

The primary disadvantages of the proposed regulations to private citizens, local governments, and agencies of the Commonwealth are upgrading and repair costs, as all of these entity types may own impounding structures in need of rehabilitation or upgrading based on the criteria set forth by the proposed regulations.  The estimated costs of implementing dam upgrades to conform with SDF requirements in the proposed regulations is approximately $249 million.  While substantial, these costs are necessary to ensure that impounding structures are constructed, operated, and maintained in a way that adequately protects the safety of downstream homes, businesses, communities, and associated infrastructure.  Other items that may be considered disadvantages by the dam owners are the costs associated with dam break inundation zone mapping, application fees, and EAP preparation.

Department of Planning and Budget's Economic Impact Analysis: Summary of the Proposed Amendments to Regulation. The Virginia Soil and Water Conservation Board (Board) proposes several significant changes to these regulations.  Overall, the changes are designed to improve the protection of the public and their property from the impact of potential dam failures.  Proposed changes include, but are not limited to: 1) revision of the dam hazard potential classification system, 2) specification that spillway design requirements are applicable to all state regulated dams, 3) modification of the spillway design requirements to enhance public safety and reduce subjectivity, 4) allowing for the potential reduction of the spillway design flood requirement through an incremental damage assessment for all qualified dams, 5) establishing dam break inundation zone mapping requirements, 6) expanding emergency action plan requirements for High and Significant Hazard Potential dams and emergency preparedness plan requirements for Low Hazard Potential dams, 7) establishing permit application fees for the administration of the Dam Safety Program that will create a stream of revenue sufficient to support an additional dam safety engineer, 8) removing the forms that are incorporated by reference and move reporting standards into the regulations, 9) creating new definitions and modifying current definitions, 10) reorganizing, clarifying, and expanding sections related to permitting procedures, and 11) updating sections related to inspections, enforcement, and unsafe conditions.

Result of Analysis. The benefits likely exceed the costs for one or more proposed changes.  There is insufficient data to accurately compare the magnitude of the benefits versus the costs for other changes.

Estimated Economic Impact. The Virginia Dam Safety Act (§10.1-604 through §10.1-613 of the Code of Virginia) was designed to ensure public safety through requirements related to the proper and safe design, construction, operation, and maintenance of impounding structures in the Commonwealth. Section 10.1-605 of the Code of Virginia directs the Board to "promulgate regulations to ensure that impounding structures in the Commonwealth are properly and safely constructed, maintained and operated."  The Department of Conservation and Recreation (DCR) points out that "As there have been no regulatory changes made to the impounding structure regulations since the late 1980’s except to update the definition of regulated dams to conform it with a 2001 legislative change in definition [Chapter 92 (SB1166) of the 2001 Virginia Acts of Assembly], it was determined that this body of regulations required a substantive review and potential revisions."

For some of the Board’s proposed changes, the benefits clearly outweigh the costs.  For example, the Board proposes to clarify that "if an owner or the owner’s engineer has determined that circumstances are impacting the integrity of the impounding structure which could result in the imminent failure of the impounding structure, temporary repairs may be initiated prior to approval from the Board. The owner shall notify the Department within 24 hours of identifying the circumstances impacting the integrity of the impounding structure."  According to DCR, this clarification was provided in response to numerous dam owners expressing concerns that they did not feel the regulations permitted them from acting to prevent a dam failure in an emergency.  This language may very well encourage some dam owners to act more quickly to prevent dam failures.

Also, the Board proposes to require that when dam owners are issued an operation and Maintenance certificate, they send a copy to the appropriate local government(s) with planning and zoning responsibilities.  The cost of sending a copy of the certificate is minimal, while the benefits can be significant.  Downstream development approved by a locality may result in the change in hazard classification of an upstream dam and for the need for the dam to upgrade its spillway design at a significant expense to the owner.  Notification may result in localities making more informed zoning decisions regarding development.

Most of the Board’s proposed changes increase requirements related to safety, which likely reduce the probability of dam failures and the associated loss of life and property damage.  These proposed changes also increase costs for dam owners.  There is no precise estimate available to determine the reduced likelihood of loss of life due to the proposed increased requirements related to safety.  Thus, even if one were willing to place a dollar figure on the value of a human life, an accurate assessment of whether the benefits of the proposed increased requirements exceed the costs cannot be made.  Nevertheless, the following paragraphs are potentially useful to the reader in that some specifics of the proposed changes are elucidated, and fairly detailed cost estimates are presented.

Under the current regulations dams are categorized as Class I, II, III, or IV, where Class I dams are located where failure will cause probable loss of life or serious property damage to others, Class II dams are located where failure could cause possible loss of life or serious property damage to others, Class III dams are located where failure may cause minimal property damage to others, and Class IV dams are located where failure would cause no property damage to others.  The board proposes to rename these hazard categories as follows: Class I would be High, Class Two would be Significant, and Class III and Class IV would be grouped together as Low.  According to DCR, this change would conform the classification categories to those used by federal agencies and many other states.

Significant potential costs associated with the board’s proposed amendments include: A) development of a dam break inundation zone map, B) development of an emergency action plan or emergency preparedness plan, C) implementing a dam upgrade to conform with SDF requirements, D) payment of permitting fees, and E) conducting inspections.

The Board proposes to require that dam owners have a dam break inundation zone map completed by a licensed professional engineer for hazard potential class determinations.  The map would also be required for High and Significant Hazard dams as part of their Emergency Action Plan (EAP). Maps would be required to be submitted every 6 years as part of the re-certification process.  The map would be useful for planning and risk assessment since it would provide information on what areas would be affected by potential dam breaks.  According to DCR, the development of a dam break inundation zone map includes two primary elements: (1) a detailed survey with a benchmark; and (2) a hydraulic computer model run with mapping of sunny day failure, mapping of the Probable Maximum Flood (PMF) with a complete failure, and mapping of the PMF without a dam failure. DCR obtained estimates of map costs provided by engineering firms that average $16,417 per map.  DCR estimates that 465 dams would require mapping; thus the estimated total cost associated with the proposed requirement for inundation zone maps is $7,633,905.1

The Board also proposes to require the development of an EAP for High and Significant Hazard dams. EAPs are already required in the current regulations for Class I, II, and III structures. Many EAPs do not contain the dam break inundation zone map discussed above. Beyond those mapping costs estimated above, the remaining EAP preparation costs are associated with completing the plan in the specified format and in exercising the plan at the specified intervals. Although there is no requirement for the dam owner to solicit the services of an engineer to complete the plan, DCR estimates the owners of about 80% of the dams (or 464 dams out 581) will use engineers, and that engineers will charge approximately $3,125 per plan.  Total costs for plan preparation would then be approximately $1,450,000.2

Due to Board-proposed increased spillway design requirements, DCR estimates that of the 1,731 dams in the Commonwealth database, at least 166 regulated dams will require a spillway upgrade.  According to the database, there are 127 dams that are currently compliant with the regulations that may require a spillway upgrade due to the regulation changes. DCR estimates that upgrade costs for these 127 dams will total $223,397,500.  Additionally, there are 39 dams that are currently noncompliant, as they already require a spillway upgrade, but the change in the regulations will require upgrading to a higher standard.  DCR estimates that only 25% of the upgrade costs would be associated with upgrading to a higher standard.  This results in $25,556,875 total required upgrade costs for these dams.  Thus the estimated total required spillway design upgrade costs would be $248,954,375.3

The proposed regulations include the following new fees:

| Construction Permit: High or Significant Hazard Dam | $2,500 |
| --- | --- |
| Construction: Low Hazard Dam | $1,000 |
| Regular Operation and Maintenance Certificate: High Hazard | $1,500 |
| Regular Operation and Maintenance Certificate: Significant Hazard | $1,000 |
| Regular Operation and Maintenance Certificate: Low Hazard | $600 |

The proposed regulations also include other fees for Conditional Operation and Maintenance Certification and Incremental Assessment Review.  Dam owners can request an Incremental Assessment Review that may reduce required upgrades if it is deemed that the dam has lower hazard potential than it has been previously assessed.  DCR estimates that the following amounts will be paid in fees annually:

| Construction Permit | $10,500 |
| --- | --- |
| Regular Operation and Maintenance Certificate Application | $49,500 |
| Conditional Operation and Maintenance Certificate Application | $49,250 |
| Incremental Damage Analysis Review | $18,675 |
| Estimated Total | $127,925 |

The current regulations already require that Class I, Class II, and Class III dams be inspected by licensed profession engineers to ensure their structural safety; but Class IV dams are exempt.  Under the proposed regulations Low Hazard dams require an inspection by an engineer once every six years.  Since current Class IV dams will be Low Hazard dams under the proposed regulations, current Class IV dams will need to be inspected once every six years.  According to DCR there are 30 Class IV dams, and it costs on average $2,833 for inspection and report generation from engineering firms.  Thus, the proposed reclassification of Class IV dams as Low Hazard dams will result in approximately $84,990 in new costs every six years,4 or $14,165 annually.5

Businesses and Entities Affected. According to DCR, 530 private individuals and entities currently own impounding structures that are subject to the proposed regulations and that may be affected by them, at least in part. In addition, five state agencies, four public colleges and universities, 58 Virginia localities, 10 service authorities, one Watershed Improvement District, and 12 Soil and Water Conservation Districts own or maintain state regulated impounding structures subject to the requirements of the Dam Safety Act, and may be affected by provisions of the proposed regulations.  Thousands of downstream property owners will likely be affected as well.

The proposed amendments will create additional demand for the services of engineers who have the expertise to work on dams, and for contractors.  DCR is aware of approximately 60 engineers offering services to dam owners in the Commonwealth; these engineers represent 46 different engineering firms. Most of those firms are likely small businesses.  According to DCR the number of contractors is not susceptible to calculation, as contractors often vary project to project; and few specialize in dam repairs.

Localities Particularly Affected6. There are fifty-eight Virginia localities which own or maintain state-regulated impounding structures (114 dams). These localities may incur additional costs associated with the operation and maintenance of their impounding structures as a result of this proposed regulation, including costs associated with inundation mapping, emergency action plan development, engineering assessments, structural improvements, and application submittal.  According to DCR, no locality will bear a disproportionate cost per impounding structure.

Number of State Regulated Impounding Structures Owned or Maintained by Localities

| Albemarle County | 6 |  | City of Lynchburg | 3 |
| --- | --- | --- | --- | --- |
| Amherst County | 4 |  | City of Manassas | 2 |
| Augusta County | 2 |  | City of Martinsville | 2 |
| Brunswick County | 1 |  | City of Newport News | 6 |
| Buckingham County | 1 |  | City of Norfolk | 3 |
| Campbell County | 1 |  | City of Norton | 2 |
| Carroll County | 1 |  | City of Portsmouth | 4 |
| Chesterfield County | 2 |  | City of Staunton | 2 |
| Fairfax County | 8 |  | City of Virginia Beach | 1 |
| Fauquier County | 1 |  | City of Waynesboro | 1 |
| Frederick County | 1 |  | City of Williamsburg | 1 |
| Gloucester County | 1 |  | Town of Appalachia | 1 |
| Henrico County | 1 |  | Town of Big Stone Gap | 2 |
| Henry County | 1 |  | Town of Brookneal | 1 |
| James City County | 3 |  | Town of Chatham | 2 |
| Louisa County | 1 |  | Town of Coeburn | 1 |
| Patrick County | 7 |  | Town of Culpeper | 2 |
| Prince Edward County | 1 |  | Town of Drakes Branch | 1 |
| Prince William County | 2 |  | Town of Keysville | 1 |
| Roanoke County | 1 |  | Town of Luray | 2 |
| Spotsylvania County | 1 |  | Town of Pulaski | 2 |
| Stafford County | 5 |  | Town of Purcellville | 1 |
| Tazewell County | 1 |  | Town of Scottsville | 1 |
| City of Bedford | 1 |  | Town of South Boston | 1 |
| City of Clifton Forge | 1 |  | Town of Strasburg | 1 |
| City of Fairfax | 3 |  | Town of Tazewell | 1 |
| City of Fredericksburg | 2 |  | Town of Warrenton | 2 |
| City of Harrisonburg | 1 |  | Town of Wise | 1 |
| City of Lexington | 2 |  | Town of Woodstock | 1 |
|  |  |  | Total | 114 |

Additionally, there are 10 service authorities (including water authorities, sewage authorities, park authorities and airport authorities) which own or maintain state-regulated impounding structures and that may serve multiple localities (20 dams). These authorities may incur additional costs associated with the operation and maintenance of their impounding structures as a result of this proposed regulation, including costs associated with inundation mapping, emergency action plan development, engineering assessments, structural improvements, and application submittal.  According to DCR, no service authority will bear a disproportionate cost per impounding structure.

Number of State Regulated Impounding Structures Owned or Maintained by

Service Authorities

| Appomattox River Water Authority | 1 |
| --- | --- |
| Augusta County Service Authority | 1 |
| Fairfax County Park Authority | 2 |
| Louisa County Water Authority | 1 |
| Metro-Washington Airport Authority | 2 |
| Nelson County Service Authority | 1 |
| Rapidan Service Authority | 1 |
| Rivanna Water and Sewer Authority | 6 |
| Upper Occoquan Sewage Authority | 1 |
| Western Virginia Water Authority | 4 |
| Total | 20 |

Additionally, many of the local Soil and Water Conservation Districts own or maintain state-regulated impounding structures (104 dams). These Soil and Water Conservation Districts may incur additional costs associated with the operation and maintenance of their impounding structures as a result of this proposed regulation, including costs associated with inundation mapping, emergency action plan development, engineering assessments, structural improvements, and application submittal.  According to DCR, no Soil and Water Conservation District will bear a disproportionate cost per impounding structure.

Number of State Regulated Impounding Structures Owned or Maintained by

Soil and Water Conservation Districts

| Blue Ridge | 10 |
| --- | --- |
| Culpeper | 11 |
| Hanover-Caroline | 1 |
| Headwaters | 11 |
| Lord Fairfax | 2 |
| Mountain Castles | 4 |
| Peter Francisco | 17 |
| Piedmont | 14 |
| Robert E. Lee | 6 |
| Shenandoah Valley | 8 |
| Southside | 12 |
| Thomas Jefferson | 8 |
| Total | 104 |

Projected Impact on Employment. The proposed requirements for inundation maps, emergency action plans, dam upgrades, and inspections will increase demand for the services of engineers with relevant expertise.  Consequently, employment for engineers with the relevant expertise will likely increase.  Employment for their support staff may increase as well.  The required dam upgrades associated with the proposed regulations will increase demand for contractors who possess the requisite expertise. Construction employment will likely moderately increase as well.

The proposed amendments will likely have some negative impact on employment for public workers in localities. If local governments must spend multiple millions of extra dollars on dams, then there will be significant spending reductions in other areas such as education public safety, and healthcare.

Effects on the Use and Value of Private Property. The proposed requirements for inundation maps, emergency action plans, dam upgrades, and inspections will increase demand for the services of engineering firms with relevant expertise.  Consequently, the use and value of engineering firms with dam-relevant expertise will likely increase.  The required dam upgrades associated with the proposed regulations will also increase demand for contracting firms which possess the requisite expertise.  The use and value of the firms will increase as well.  Demand for construction materials associated with dam improvements will also increase.  The value of firms selling these materials may moderately increase.

Dam owners whose required expenditures on their dams increase significantly due to the proposed requirements will have fewer dollars to spend elsewhere.  For example, localities that spend millions of additional dollars on dams will likely purchase fewer supplies and services from private firms in other categories.  Also private dam owners net worth will decline somewhat with required increased expenditures on their dams.

Small Businesses: Costs and Other Effects. Some small engineering and contacting firms will benefit from the proposed regulations.

Small Businesses: Alternative Method that Minimizes Adverse Impact. There is no clear alternative that minimizes the very large costs associated with the proposed amendments while still achieving the very high level of safety sought.  Costs could potentially be significantly reduced if greater risk were deemed acceptable.

Legal Mandate. The Department of Planning and Budget (DPB) has analyzed the economic impact of this proposed regulation in accordance with §2.2-4007 H of the Administrative Process Act and Executive Order Number 36 (06).  Section 2.2-4007 H requires that such economic impact analyses include, but need not be limited to, the projected number of businesses or other entities to whom the regulation would apply, the identity of any localities and types of businesses or other entities particularly affected, the projected number of persons and employment positions to be affected, the projected costs to affected businesses or entities to implement or comply with the regulation, and the impact on the use and value of private property.  Further, if the proposed regulation has adverse effect on small businesses, §2.2-4007 H requires that such economic impact analyses include (i) an identification and estimate of the number of small businesses subject to the regulation; (ii) the projected reporting, recordkeeping, and other administrative costs required for small businesses to comply with the regulation, including the type of professional skills necessary for preparing required reports and other documents; (iii) a statement of the probable effect of the regulation on affected small businesses; and (iv) a description of any less intrusive or less costly alternative methods of achieving the purpose of the regulation.  The analysis presented above represents DPB’s best estimate of these economic impacts.

-------------------------------------

1 Calculation: 465 x $16,417 = $7,633,905

2 Calculation: 464 x $3,125 = $1,450,000

3 Calculation: $223,397,500 + $25,556,875 = $248,954,375

4 Calculation: 30 x $2,833 = $84,990

5 Calculation: $84,990 / 6 = $14,165

6 All of the information in this section was graciously provided by the Department of Conservation and Recreation.

Agency Response to Department of Planning and Budget's Economic Impact Analysis: The Department of Conservation and Recreation (DCR) has reviewed the economic impact analysis (EIA) of the Virginia Soil and Water Conservation Board’s proposed amendments to the Virginia Impounding Structure Regulations prepared by the Department of Planning and Budget (DPB) and is in concurrence with the information provided with the following qualifications:

First, DCR appreciates the recognition by DPB of the importance of these regulations in the protection of public safety.

Second, DPB noted that "one of the significant potential costs associated with the board’s proposed amendments include: …B) development of an emergency action plan or emergency preparedness plan…"  Although stated in the EIA, DCR would like to point out that emergency action plans (EAPs) for regulated dams are already an existing requirement.  Any additional costs associated with engineering expenses incurred in developing EAPs will be solely due to the dam owner choosing to enlist the services of an engineer as a matter of convenience.

Third, with regard to the development of dam break inundation zone maps, DPB stated that "DCR estimates that 465 dams would require mapping; thus the estimated total cost associated with the proposed requirement for inundation zone maps is $7,633,905."  However, DCR would like to point out that the following considerations must be taken into account when reviewing these figures:

1. A number of dam owners already have partial modeling information available to complete the mapping, which should reduce preparation costs.

2. The required maps will be good for 6 years unless circumstances change below the dam, prompting revisions to the maps.

3. Updates to the vast majority of maps will routinely be much less costly in subsequent years.  If no development has occurred, no updates will be necessary.

Fourth, DPB states that the "estimated total required spillway design upgrade costs would be $248,954,375."  However, DCR estimates that approximately 50 percent of the 166 dams that are projected to require spillway upgrades as a result of the proposed regulatory changes may pursue, for the first time, an "incremental damage assessment" that may reduce or eliminate the need to upgrade the dam’s spillway.  Under existing regulations, which have been in place since 1989, the incremental damage assessment has been available to a limited number of dam owners. This would be a significant change.  Consequently, it is likely that a significant number of dams will not be found to require a spillway upgrade, thus reducing the overall estimated cost of these proposed regulatory amendments.

Fifth, DPB states, "If local governments must spend multiple millions of extra dollars on dams, then there will be significant spending reductions in other areas such as education, public safety, and health care."  DCR respectfully takes exception to this statement.  Dam safety is a significant component to public safety and is increasingly being recognized as such across the nation.  Virginia has historically experienced a large number of storms and hurricane events, which have resulted in threats to several dams and downstream lives and property.  As pointed out in a presentation to the regulatory Technical Advisory Committee, nine of the top 15 storms in recorded U.S. history have occurred in or near Virginia as well as 3 of the top 5 most intense 12-hour storms in the United States.  The aging dam inventory in the Commonwealth, along with increased proximity of development also places more of the public in potential harm’s way unless these dams are properly structured and maintained.  DCR also notes that by virtue of localities investing in dam upgrades, they may avoid the catastrophic impacts and costs associated with a dam failure during a future storm event.  Further, DCR notes that localities may be eligible for low-interest financing from the Virginia Resources Authority to assist with repair costs, thus reducing local fiscal impacts.

Finally, DCR reiterates that the proposed amendments to Virginia’s dam safety regulations will substantially improve the Commonwealth’s means of protecting the public from dam failures, which can be devastating to dam owners and especially to downstream communities and property.  The economic impact of such failures to property can range from thousands to billions of dollars, while no price can be placed on the lives that may be lost.

Summary:

This regulatory action amends the Virginia Soil and Water Conservation Board’s Impounding Structure Regulations to protect the safety and welfare of the public and their property from the impact of dam failures.  The key elements of this proposed regulation will:

1. Revise the dam hazard potential classification system from four categories (Class I, II, III, and IV) to three hazard classifications (High, Significant, and Low);

2. Specify that spillway design requirements are applicable to all state regulated dams regardless of the date they were built;

3. Modify the spillway design requirements to enhance public safety and reduce subjectivity;

4. Allow for the reduction of the spillway design flood requirements through incremental damage assessments for all qualifying dams;

5. Establish dam break inundation zone mapping requirements to identify areas that are subject to flooding during a dam failure;

6. Expand emergency action plan requirements for High and Significant Hazard Potential dams and emergency preparedness plan requirements for Low Hazard Potential dams;

7. Establish permit application fees for the administration of the Dam Safety Program;

8. Incorporate reporting standards into the regulations;

9. Reorganize, clarify, and expand sections related to permitting procedures; and

10. Update sections related to inspections, enforcement, and unsafe conditions.

4VAC50-20-20. General provisions.

A. This chapter provides for the proper and safe design, construction, operation and maintenance of impounding structures to protect public safety. This chapter shall not be construed or interpreted to relieve the owner or operator of any impoundment or impounding structure of any legal duties, obligations or liabilities incident to ownership, design, construction, operation or maintenance.

B. Approval by the board of proposals for an impounding structure shall in no manner be construed or interpreted as approval to capture or store waters. For information concerning approval to capture or store waters, see Chapter 8 (§62.1-107) of Title 62.1 of the Code of Virginia, and other provisions of law as may be applicable.

C. In promulgating this chapter, the board recognizes that no impounding structure can ever be completely "fail-safe," because of incomplete understanding of or uncertainties associated with natural (earthquakes and floods) and manmade (sabotage) destructive forces; with material behavior and response to those forces; and with quality control during construction.

D. Any All engineering analysis analyses required by this chapter such as , including but not limited to, plans, specifications, hydrology, hydraulics and inspections shall be conducted or overseen by and bear the seal of a professional engineer licensed to practice in Virginia.

E. Design, inspection and maintenance of impounding structures shall be conducted utilizing competent, experienced, engineering judgment that takes into consideration factors including but not limited to local topography and meteorological conditions.

EF. The official forms as called for by in this chapter are available from the director department at the department’s website.

4VAC50-20-30. Definitions.

The following words and terms when used in this chapter shall have the following meanings unless the context clearly indicates otherwise:

"Acre-foot" means a unit of volume equal to 43,560 cubic feet or 325,853 gallons (equivalent to one foot of depth over one acre of area).

"Agricultural purpose" means the production of an agricultural commodity as defined in §3.1-249.27 of the Code of Virginia that requires the use of impounded waters.

"Agricultural purpose dams" means dams which are less than 25 feet in height or which create a maximum impoundment smaller than 100 acre-feet, and certified by the owner on official forms as constructed, maintained or operated primarily for agricultural purposes.

"Alteration" means changes to an impounding structure that could alter or affect its structural integrity. Alterations include, but are not limited to, changing the height or otherwise enlarging the dam, increasing normal pool or principal spillway elevation or physical dimensions, changing the elevation or physical dimensions of the emergency spillway, conducting necessary structural repairs or structural maintenance, or removing the impounding structure.

"Alteration permit" means a permit required for changes any alteration to an impounding structure that could alter or affect its structural integrity. Alterations requiring a permit include, but are not limited to: changing the height, increasing the normal pool or principal spillway elevation, changing the elevation or physical dimensions of the emergency spillway or removing the impounding structure.

"Board" means the Virginia Soil and Water Conservation Board.

"Conditional operation and maintenance certificate Operation and Maintenance Certificate" means a certificate required for impounding structures with deficiencies.

"Construction" means the construction of a new impounding structure.

"Construction permit" means a permit required for the construction of a new impounding structure.

"Dam break inundation zone" means the area downstream of a dam that would be inundated or otherwise directly affected by the failure of a dam.

"Department" means the Virginia Department of Conservation and Recreation.

"Design flood" means the calculated volume of runoff and the resulting peak discharge utilized in the evaluation, design, construction, operation and maintenance of the impounding structure.

"Design freeboard" means the vertical distance between the maximum elevation of the design flood and the top of the impounding structure.

"Director" means the Director of the Department of Conservation and Recreation or his designee.

"Drill" means a type of emergency action plan exercise that tests, develops, or maintains skills in an emergency response procedure. During a drill, participants perform an in-house exercise to verify telephone numbers and other means of communication along with the owner’s response. A drill is considered a necessary part of ongoing training.

"Emergency Action Plan or EAP" means a formal document that recognizes potential impounding structure emergency conditions and specifies preplanned actions to be followed to minimize loss of life and property damage. The EAP specifies actions the owner must take to minimize or alleviate emergency conditions at the impounding structure. It contains procedures and information to assist the owner in issuing early warning and notification messages to responsible emergency management authorities. It shall also contain dam break inundation zone maps as required to show emergency management authorities the critical areas for action in case of emergency.

"Emergency Action Plan Exercise" means an activity designed to promote emergency preparedness; test or evaluate EAPs, procedures, or facilities; train personnel in emergency management duties; and demonstrate operational capability. In response to a simulated event, exercises should consist of the performance of duties, tasks, or operations very similar to the way they would be performed in a real emergency. An exercise may include but not be limited to drills and tabletop exercises.

"Emergency Preparedness Plan" means a formal document prepared for Low Hazard dams that provides maps and procedures for notifying owners of downstream property that may be impacted by an emergency situation at an impounding structure.

"Freeboard" means the vertical distance between the maximum water surface elevation associated with the spillway design flood and the top of the impounding structure.

"Height" means the structural hydraulic height of an impounding structure. If the impounding structure spans a stream or watercourse, height means the vertical distance from the natural bed of the stream or watercourse measured at the downstream toe of the impounding structure to the top of the impounding structure. If the impounding structure does not span a stream or watercourse, height means the vertical distance from the lowest elevation of the outside downstream limit of the barrier to the top of the impounding structure.

"Impounding structure" means a man-made device structure, whether a dam across a watercourse or other structure outside a watercourse, used or to be used to retain or store waters or other materials. The term includes: (i) all dams that are 25 feet or greater in height and that create an impoundment capacity of 15 acre-feet or greater, and (ii) all dams that are six feet or greater in height and that create an impoundment capacity of 50 acre-feet or greater. The term "impounding structure" shall not include: (a) dams licensed by the State Corporation Commission that are subject to a safety inspection program; (b) dams owned or licensed by the United States government; (c) dams constructed, maintained or operated primarily for agricultural purposes which are less than 25 feet in height or which create a maximum impoundment capacity smaller than 100 acre-feet; (d) water or silt retaining dams approved pursuant to §45.1-222 or §45.1-225.1 of the Code of Virginia; or (e) obstructions in a canal used to raise or lower water.

"Impoundment" means a body of water or other materials the storage of which is caused by any impounding structure.

"Inundation zone" means an area that could be inundated as a result of impounding structure failure and that would not otherwise be inundated to that elevation.

"Life of the impounding structure" and "life of the project" mean that period of time for which the impounding structure is designed and planned to perform effectively, including the time required to remove the structure when it is no longer capable of functioning as planned and designed.

"Maximum impounding capacity" means the volume of water or other materials in acre-feet that is capable of being impounded at the top of the impounding structure.

"Normal impounding capacity" means the volume of water or other materials in acre-feet that is capable of being impounded at the elevation of the crest of the lowest ungated outlet from the impoundment.

"Operation and maintenance certificate Maintenance Certificate" means a certificate required for the operation and maintenance of all impounding structures.

"Owner" means the owner of the land on which an impounding structure is situated, the holder of an easement permitting the construction of an impounding structure and any person or entity agreeing to maintain an impounding structure. The term "owner" includes may include the Commonwealth or any of its political subdivisions, including but not limited to sanitation district commissions and authorities. Also included are , any public or private institutions, corporations, associations, firms or companies organized or existing under the laws of this Commonwealth or any other state or country, as well as any person or group of persons acting individually or as a group.

"Spillway" means a structure to provide for the controlled release of flows from the impounding structure into a downstream area.

"Stage I Condition" means a flood watch or heavy continuous rain or excessive flow of water from ice or snow melt.

"Stage II Condition" means a flood watch or emergency spillway activation or dam overtopping where a breach may be possible.

"Stage III Condition" means an emergency spillway activation or dam overtopping where imminent failure is probable.

"Sunny day dam failure" means the breaching of an impounding structure with the initial water level at the normal reservoir level, usually at the lowest ungated principal spillway elevation or the typical operating water level.

"Tabletop Exercise" means a type of emergency action plan exercise that involves a meeting of the impounding structure owner and the state and local emergency management officials in a conference room environment. The format is usually informal with minimum stress involved. The exercise begins with the description of a simulated event and proceeds with discussions by the participants to evaluate the EAP and response procedures and to resolve concerns regarding coordination and responsibilities.

"Top of the impounding structure" means the lowest point of the nonoverflow section of the impounding structure.

"Watercourse" means a natural channel having a well-defined bed and banks and in which water normally flows when it normally does flow.

4VAC50-20-40. Classes Hazard potential classifications of impounding structures.

A. Impounding structures shall be classified in one of four categories according to size and hazard potential, three hazard classifications as defined in subsection B of this section and Table 1. Size classification shall be determined either by maximum impounding capacity or height, whichever gives the larger size classification.

B. For the purpose of this chapter, hazards pertain to potential loss of human life or property damage to the property of others downstream from the impounding structure in event of failure or faulty operation of the impounding structure or appurtenant facilities. Hazard potential classifications of dams are as follows:

1. Impounding structures in the Class I hazard potential category are located where High Hazard Potential is defined where an impounding structure failure will cause probable loss of life or serious economic damage to occupied. Economic damage may occur to, but not be limited to, building(s), industrial or commercial facilities, important primary public utilities, main highway(s) or railroad(s) major public roadways, railroads, personal property, and agricultural interests.

2. Impounding structures in the Class II hazard potential category are located where Significant Hazard Potential is defined where an impounding structure failure could may cause possible the loss of life or appreciable economic damage. Economic damage may occur to, but not be limited to occupied, building(s), industrial or commercial facilities, secondary public utilities, secondary highway(s) or railroad(s) or cause interruption of use or service of relatively important public utilities public roadways, railroads, personal property, and agricultural interests.

3. Impounding structures in Class III hazard potential category are located where Low Hazard Potential is defined where an impounding structure failure may cause minimal property damage to others. No loss of life is expected would result in no expected loss of life and would cause no more than minimal economic damage. Economic damage may occur to, but not be limited to, building(s), industrial or commercial facilities, secondary public utilities, secondary public roadways, railroads, personal property and agricultural interests.

4. Impounding structures in Class IV hazard potential category are located where the failure of the impounding structure would cause no property damage to others. No loss of life is expected.

5. Such size and C. The hazard potential classifications classification and size category for the given hazard classification shall be proposed by the owner and shall be subject to approval by the director board. To support the appropriate hazard classification, dam break analysis shall be conducted by the owner’s engineer. Present and projected development of planned land-use in the dam break inundation zones downstream from the impounding structure shall be considered in determining the classification.

6.D. Impounding structures shall be subject to reclassification by the board as necessary.

4VAC50-20-50. Performance standards required for impounding structures.

A. In accordance with the definitions provided by §10.1-604 of the Code of Virginia and 4VAC50-20-30, an impounding structure shall be regulated if the dam is 25 feet or greater in height and creates a maximum impounding capacity of 15 acre-feet or greater, or the dam is six feet or greater in height and creates a maximum impounding capacity of 50 acre-feet or greater and is not otherwise exempt from regulation by the Code of Virginia. Impounding structures exempted from this chapter are those that are:

1. Licensed by the State Corporation Commission that are subject to a safety inspection program;

2. Owned or licensed by the United States government;

3. Operated primarily for agricultural purposes that are less than 25 feet in height or that create a maximum impoundment capacity smaller than 100 acre-feet;

4. Water or silt-retaining dams approved pursuant to §45.1-222 or 45.1-225.1 of the Code of Virginia; or

5. Obstructions in a canal used to raise or lower water.

Impounding structures of regulated size and not exempted shall be constructed, operated and maintained such that they perform in accordance with their design and purpose throughout the life of the project. For new impounding structures, the spillway(s) capacity shall perform at a minimum to safely pass the appropriate spillway design flood as determined in Table 1. For the purposes of utilizing Table 1, Maximum Impounding Capacity and Height shall be determined in accordance with the definitions provided in 4VAC50-20-30 and Hazard Potential Classification shall be determined in accordance with 4VAC50-20-40.

TABLE 1—Impounding Structure Regulations

| Class of Dam | Hazard Potential If Impounding Structure Fails | SIZE CLASSIFICATION | Spillway Design Flood (SDF)b |
| --- | --- | --- | --- |
|  |  | Maximum Capacity (Ac-Ft)a | Height (Ft)a |  |
| I | Probable Loss of Life; Excessive Economic Loss | Large | ≥ 50,000 | ≥ 100 | PMFc |
|  |  | Medium | ≥ 1,000 & < 50,000 | ≥ 40 & < 100 | PMF |
|  |  | Small | ≥ 50 & < 1,000 | ≥ 25 & < 40 | 1/2 PMF to PMF |
| II | Possible Loss of Life; Appreciable Economic Loss | Large | ≥ 50,000 | ≥ 100 | PMF |
|  |  | Medium | ≥ 1,000 & < 50,000 | ≥ 40 & < 100 | 1/2 PMF to PMF |
|  |  | Small | ≥ 50 & < 1,000 | ≥ 25 & < 40 | 100-YR to 1/2 PMF |
| III | No Loss of Life Expected; Minimal Economic Loss | Large | ≥ 50,000 | ≥ 100 | 1/2 PMF to PMF |
|  |  | Medium | ≥ 1,000 & < 50,000 | ≥ 40 & < 100 | 100-YR to 1/2 PMF |
|  |  | Small | ≥ 50 & < 1,000 | ≥ 25 & < 40 | 50-YRd to 100-YRe |
| IV | No Loss of Life Expected; No Economic Loss to Others | ≥ 50 (nonagricultural) ≥ 100 (agricultural) | ≥ 25 (both) | 50-YR to 100-YR |

TABLE 1

Impounding Structure Regulations

| Hazard Potential Class of Dam | SIZE CATEGORIESB | Spillway Design Flood (SDF)C | Minimum Threshold for Incremental Damage Assessment |
| --- | --- | --- | --- |
|  | Maximum Impounding Capacity (Ac-Ft) | Height (Ft) |  |  |
| High | AllB | AllB | PMFD | .50 PMF |
| Significant | Large ≥ 50,000 | ≥100 | PMFD | .50 PMF |
|  | Medium ≥ 1,000 & < 50,000 | ≥ 40 & < 100 | .75 PMF | 100-YRE |
|  | Small ≥ 15 & < 1,000 | ≥ 6 & < 40 | .50 PMF | 100-YRE |
| Low | Large ≥ 50,000 | ≥100 | .50 PMF | 100-YRE |
|  | Medium ≥ 1,000 & < 50,000 | ≥ 40 & < 100 | 100-YRE | 50-YRF |
|  | Small ≥ 15 & < 1,000 | ≥ 6 & < 40 | 100-YRE | 50-YRF |

aThe factor determining the largest size classification shall govern. B. The appropriate size category is determined by the largest size associated with the maximum impounding capacity and height of the impounding structure.

bC. The spillway design flood (SDF) represents the largest flood that need be considered in the evaluation of the performance for a given project. The impounding structure shall perform so as to safely pass the appropriate SDF. Where a range of SDF is indicated, the magnitude that most closely relates to the involved risk should be selected. The establishment in this chapter of rigid design flood criteria or standards is not intended. Safety must be evaluated in the light of peculiarities and local conditions for each impounding structure and in recognition of the many factors involved, some of which may not be precisely known. Such can only be done by competent, experienced engineering judgment, which the values in Table 1 are intended to supplement, not supplant. Reductions in the established SDF may be evaluated through the use of incremental damage assessment pursuant to 4VAC50-20-52. The SDF established for an impounding structure shall not be less than those standards established elsewhere by state law or regulations, including but not limited to the Virginia Stormwater Management Program (VSMP) Permit Regulations (4VAC50-60).

cD. PMF: Probable maximum flood This means Maximum Flood is the flood that might be expected from the most severe combination of critical meteorologic and hydrologic conditions that are reasonably possible in the region. The PMF is derived from the current probable maximum precipitation (PMP) available from the National Weather Service, NOAA. In some cases local topography or meteorological conditions will cause changes from the generalized PMP values; therefore, it is advisable to contact local, state or federal agencies to obtain the prevailing practice in specific cases. Any deviation in the application of established developmental procedures must be explained and justified by the owner’s engineer. The owner’s engineer must develop PMF hydrographs for 6-, 12-, and 24-hour durations. The hydrograph that creates the largest peak outflow is to be used to determine capacity for nonfailure and failure analysis. Present and planned land-use conditions shall be considered in determining the runoff characteristics of the drainage area.

E. 100-Yr: 100-year flood represents the flood magnitude expected to be equaled or exceeded on the average of once in 100 years. It may also be expressed as an exceedence probability with a 1.0% chance of being equaled or exceeded in any given year. Present and planned land-use conditions shall be considered in determining the runoff characteristics of the drainage area.

dF..50-Yr: 50-year flood. This means represents the flood magnitude expected to be equaled or exceeded on the average of once in 50 years. It may also be expressed as an exceedence probability with a 2.0% chance of being equaled or exceeded in any given year. Present and planned land-use conditions shall be considered in determining the runoff characteristics of the drainage area.

e 100-Yr: 100-year flood. This means the flood magnitude expected to be equaled or exceeded on the average of once in 100 years. It may also be expressed as an exceedence probability with a 1.0% chance of being equaled or exceeded in any given year.

Part II

Permit Requirements

4VAC50-20-52. Incremental damage assessment.

A. When appropriate, the spillway design flood requirement may be reduced by the board in accordance with this section.

B. Prior to qualifying for a spillway design flood reduction, certain maintenance conditions must be adequately addressed including, but not limited to, the following:

1. Operation and maintenance is determined by the director to be satisfactory and up to date;

2. The impounding structure is not in need of other alteration related to the integrity of the structure;

3. Emergency Action Plan requirements set out in 4VAC50-20-175 or Emergency Preparedness requirements set out in 4VAC50-20-177 have been satisfied;

4. Inspection report requirements have been met and are considered satisfactory by the director;

5. The applicant demonstrates in accordance with the current design procedures and references of 4VAC50-20-320 to the satisfaction of the board that the impounding structure as designed, constructed, operated and maintained does not pose an unreasonable hazard to life and property;

6. The owner satisfies all special requirements imposed by the board; and

7. Certification by the owner that these conditions will continue to be met.

C. After meeting the criteria set out in subsection B of this section, the owner’s engineer may proceed with an incremental damage analysis. Once the owner’s engineer has determined the required spillway design flood through application of Table 1, further analysis may be performed to evaluate the limiting flood condition for incremental damages. This assessment may be used to lower the spillway design flood. In no situation shall the allowable reduction be less than the level at which the incremental increase in water surface elevation downstream due to failure of a dam is no longer considered to present an unacceptable additional downstream threat. This engineering analysis will need to present water surface elevations at each structure that may be impacted downstream of the dam. Water depths greater than two feet and overbank flow velocities greater than three feet per second shall be used to define conditions for unacceptable additional downstream threat to persons or property.

D. The spillway design flood shall not be reduced below the minimum threshold values as determined by Table 1.

4VAC50-20-54. Dam break inundation zone mapping.

A. Dam break inundation zone maps shall be provided to the department to meet the requirements set out in Hazard Potential Classifications of Impounding Structures (4VAC50-20-40), Emergency Action Plan for High and Significant Potential Hazard Dams (4VAC50-20-175), and Emergency Preparedness for Low Hazard Potential Dams (4VAC50-20-177), as applicable.

B. The location of the end of the inundation mapping should be indicated where the water surface elevation of the dam break inundation zone and the water surface elevation of the spillway design flood during a nondam failure event converge to within one foot of each other. This would demonstrate a level where failure of the dam does not further constitute a hazard to downstream life or property. The inundation maps shall be supplemented with water surface profiles and cross-sections at critical areas showing the peak water surface elevation prior to failure and the peak water surface elevation after failure.

C. All inundation zone map(s), except those utilized in meeting the requirements of Emergency Preparedness for Low Hazard Potential Dams (4VAC50-20-177), shall be signed and sealed by a licensed professional engineer.

D. For determining the hazard potential classification, a minimum of the following shall be provided to the department:

1. A sunny day dam break analysis utilizing the volume retained at the normal or typical water surface elevation of the impounding structure;

2. A dam break analysis utilizing a probable maximum flood with a dam failure; and

3. A dam break analysis utilizing a probable maximum flood without a dam failure.

E. To meet the requirements of Emergency Preparedness set out in 4VAC50-20-177, all Low Hazard Potential impounding structures shall provide a simple map, acceptable to the department, demonstrating the general inundation that would result from a dam failure. Such maps do not require preparation by a professional licensed engineer, however, it is preferred that the maps be prepared by a licensed professional engineer.

F. To meet the Emergency Action Plan requirements set out in 4VAC50-20-175, all owners of High and Significant Hazard Potential impounding structures shall provide dam break inundation map(s) representing the impacts that would occur with both a sunny day dam failure and a spillway design flood dam failure.

1. The map(s) shall be developed at a scale sufficient to graphically display downstream inhabited areas and structures, roads, and other pertinent structures within the identified inundation area. In coordination with the local organization for emergency management, a list of downstream inundation zone property owners and occupants, including telephone numbers may be plotted on the map or may be provided with the map for reference during an emergency.

2. A note shall be included on each map to state: "Mapping of flooded areas and flood wave travel times are approximate. Timing and extent of actual inundation may differ from information presented on this map."

4VAC50-20-58. Local government notifications.

For each certificate issued, the impounding structure owner shall send a copy of the certificate to the appropriate local government(s) with planning and zoning responsibilities. A project description and the map(s) required under 4VAC50-20-54 showing the area that could be affected by the impounding structure breach shall be submitted with the certificate. The department will provide a standard form cover letter for forwarding the certificate copy and accompanying materials.

Part II

Permit Requirements

4VAC50-20-60. Required permits.

A. No person or entity shall construct or begin to construct an impounding structure until the board has issued a construction permit.

B. No person or entity shall alter or begin to alter an existing impounding structure in a manner which would potentially affect its structural integrity until the board has issued an alteration permit, or in the case of an emergency, authorization obtained from the director. The permit requirement may be waived if the director determines that the alteration of improvement will not substantially alter or affect the structural integrity of the impounding structure. Alteration does not mean normal operation and maintenance. If an owner or the owner’s engineer has determined that circumstances are impacting the integrity of the impounding structure that could result in the imminent failure of the impounding structure, temporary repairs may be initiated prior to approval from the board. The owner shall notify the department within 24 hours of identifying the circumstances impacting the integrity of the impounding structure. Such emergency notification shall not relieve the owner of the need to obtain an alteration permit as soon as may be practicable, nor shall the owner take action beyond that necessary to address the emergency situation.

C. When the board receives owner submits an application to the board for any permit to construct or alter an impounding structure, the director owner shall also inform the local government of any jurisdiction which or jurisdictions that might be affected by the permit application.

D. In evaluating construction and alteration permit applications the director shall use the most current design criteria and standards referenced in 4VAC50-20-320 of this chapter.

4VAC50-20-70. Construction permits.

A. Prior to preparing the complete design report for a construction permit Construction Permit, applicants are encouraged to seek approval of the project concept from the director may submit a preliminary design report to the department to determine if the project concept is acceptable to the department. For this purpose the applicant should submit The preliminary design report should contain, at a minimum, a general description of subdivisions 1 through 4  12 of subsection B of this section and subdivisions 1 and 2 of this subsection:

1. Proposed design criteria and a description of the size of the impounding structure, ground cover conditions, extent of current upstream development of within the watershed and the hydraulic, hydrological and structural features, geologic conditions and the geotechnical engineering assumptions used to determine the foundations foundation, impoundment rim stability and materials to be used.

2. Preliminary drawings of a general nature, including cross sections, plans and profiles of the impounding structure, proposed pool levels and types of spillway(s).

B. An applicant for a construction permit Construction Permit shall submit a design report on official forms. A form for the design report will be available from the department (Design Report for the Construction or Alteration of Virginia Regulated Impounding Structures). The design report shall be prepared in accordance with 4VAC50-20-240 and shall include the following information:. The design report is a required element of a complete application for a Construction Permit and shall include the following information:

1. A description of the impounding structure and appurtenances and a proposed classification conforming with this chapter. The description shall include a statement of the purposes for which the impoundment and impounding structure are to be used.

1. Project information including a description of the proposed construction, name of the impounding structure, inventory number if available, name of the reservoir, and the purpose of the reservoir.

2. The proposed hazard potential classification in conformance with Table 1 of 4VAC50-20-50.

3. Location of the impounding structure including the city or county, number of feet or miles upstream or downstream of a highway and the highway number, name of the river or the stream, and the latitude and longitude.

4. Owner’s name or representative if corporation, mailing address, residential and business telephone numbers, and other means of communication.

5. Owner’s engineer’s name, firm, professional engineer Virginia number, mailing address, and business telephone number.

6. Impounding structure data including type of material (earth, concrete, masonry or other) and the following design configurations:

a. Top of dam (elevation);

b. Downstream toe – lowest (elevation);

c. Height of dam (feet);

d. Crest length – exclusive of spillway (feet);

e. Crest width (feet);

f. Upstream slope (horizontal and vertical); and

g. Downstream slope (horizontal and vertical).

7. Reservoir data including the following:

a. Maximum capacity (acre-feet);

b. Maximum pool (elevation);

c. Maximum pool surface area (acres);

d. Normal capacity (acre-feet);

e. Normal pool (elevation);

f. Normal pool surface area (acres); and

g. Freeboard – normal pool to top of dam (feet).

8. Spillway data including the type, construction material, design configuration, and invert elevation for the low level drain, the principal spillway, and the emergency spillway.

9. Watershed data including drainage area (square miles); type and extent of watershed development; time of concentration (hours); routing procedure; spillway design flood used and state source; design inflow hydrograph volume (acre-feet), peak inflow (cfs), and rainfall duration (hours); and freeboard during passage of the spillway design flood (feet).

2.10. A description of properties located in the dam break inundation zone downstream from the site of the proposed impounding structure, including the location and number of residential structures, buildings, roads, utilities and other property that would be endangered should the impounding structure fail.

3. A statement from the governing body of the local political subdivision or other evidence confirming that body is aware of the proposal to build an impounding structure and of the land use classifications applicable to the inundation zone. 11. Evidence that the local government or governments have been notified of the proposal by the owner to build an impounding structure.

4.12. Maps showing the location of the proposed impounding structure that include: the county or city in which the proposed impounding structure would be located, the location of roads, and access to the site, and the outline of the impoundment. Existing aerial photographs or existing topographic maps may be used for this purpose.

5.13. A report of the geotechnical investigations of the foundation soils, or bedrock, or both and of the materials to be used to construct the impounding structure.

6.14. Design assumptions and analyses sufficient to indicate that the impounding structure will be stable during its construction and during the life of the impounding structure under all conditions of reservoir impoundment operations, including rapid filling, flood surcharge, seismic loadings, and rapid drawdown of the impoundment.

7.15. Evaluation of the stability of the reservoir impoundment rim area in order to safeguard against reservoir impoundment rim slides of such magnitude as to create waves capable of overtopping the impounding structure and confirmation evaluation of rim stability during seismic activity.

8.16. Design assumptions and analyses sufficient to indicate that seepage in, around, through or under the impounding structure, foundation and abutments will be reasonably and practically controlled so that internal or external forces or results thereof will not endanger the stability and integrity of the impounding structure. The design report shall also include information on graded filter design.

9.17. Calculations and assumptions relative to hydraulic and structural design of the spillway or spillways and energy dissipater or dissipaters. Spillway capacity shall conform to the criteria of Table 1 and 4VAC50-20-52.

10.18. Provisions to ensure that the impounding structure and appurtenances will be protected against unacceptable deterioration or erosion due to freezing and thawing, wind, wave action, and rain or any combination thereof.

11.19. Other pertinent design data, assumptions and analyses commensurate with the nature of the particular impounding structure and specific site conditions, including when required by the director this chapter, a plan and profile of the dam break inundation zones.

12. Erosion and sediment control plans to minimize soil erosion and sedimentation during all phases of construction, operation and maintenance. Projects shall be in compliance with local erosion and sediment control ordinances.

13.20. A description of the techniques to be used to divert stream flow during construction so as to prevent hazard to life, health and property, including a detailed plan and procedures to maintain a stable impounding structure during storm events, a drawing showing temporary diversion devices, and a description of the potential impoundment during construction. Such diversion plans shall also be in accordance with applicable environmental laws.

14.21. A plan of for project construction monitoring and quality control testing to confirm that construction materials and methods performance standards meet the design requirements set forth in the specifications.

15. A proposed schedule indicating construction sequence and time to completion.

16.22. Plans and specifications as required by 4VAC50-20-310.

17. An emergency action plan on official forms and evidence that a copy of such plan has been filed with the local organization for emergency management and the State Department of Emergency Management. The plan shall include a method of providing notification and warning to persons downstream, other affected persons or property owners and local authorities in the event of a flood hazard or the impending failure of the impounding structure.

18. A proposed impoundment and impounding structure operation and maintenance plan on official forms certified by a professional engineer. This plan shall include a safety inspection schedule and shall place particular emphasis on operating and maintaining the impounding structure in keeping with the project design, so as to maintain its structural integrity and safety during both normal and abnormal conditions which may reasonably be expected to occur during its planned life.

C. The director or the applicant may request a conference to facilitate review of the applicant's proposal.

D. The owner shall certify in writing that the operation and maintenance plan as approved by the board will be adhered to during the life of the project except in cases of unanticipated emergency requiring departure therefrom in order to mitigate hazard to life and property. At such time, the owner's engineer and the director shall be notified.

E. If the submission is not acceptable, the director shall inform the applicant within 60 days and shall explain what changes are required for an acceptable submission.

F. Within 120 days of receipt of an acceptable design report the board shall act on the application.

23. Certification by the owner’s engineer that the information provided pursuant to this subsection is true and correct in their professional judgment. Such certification shall include the engineer’s signature, printed name, Virginia number, date, and the engineer’s Virginia seal.

24. Owner’s signature certifying receipt of the information provided pursuant to this subsection.

C. A plan of construction is a required element of a complete permit application for a Construction Permit and shall include:

1. A construction sequence with milestones.

2. Elements of the work plan that should be considered include, but are not limited to, foundation and abutment treatment, stream or river diversion, excavation and material fill processes, phased fill and compaction, testing and control procedures, construction of permanent spillway and drainage devices.

3. The erosion and sediment control plan, as approved by the local government, which minimizes soil erosion and sedimentation during all phases of construction.

4. The stormwater management plan or stormwater management facility plan, as approved by the local government, if the impounding structure is a stormwater management best management practice.

D. A Temporary Emergency Action Plan is a required element of a complete application for a Construction Permit and shall include:

1. A notification list of state and local emergency response agencies;

2. Provisions for notification of potentially affected residences and structures;

3. Construction site evacuation routes; and

4. Any other special notes particular to the project.

E. Within 120 days of receipt of a complete Construction Permit Application the board shall act on the application. If the application is not acceptable, the director shall inform the applicant within 60 days of receipt and shall explain what changes are required for an acceptable application. A complete Construction Permit Application consists of the following:

1. A final design report, submitted on the department form (Design Report for the Construction or Alteration of Virginia Regulated Impounding Structures), with attachments as needed, and certified by the owner and the owner’s engineer;

2. A plan of construction that meets the requirements of subsection C of this section; and

3. A Temporary Emergency Action Plan that meets the requirements of subsection D of this section.

G.F. Prior to and during construction the owner shall notify provide the director of with any proposed changes from the approved design, plans, specifications, or operation and maintenance plan of construction. Approval shall be obtained from the director prior to the construction or installation of any changes that will affect the stability integrity or impounding capacity of the impounding structure.

H.G. The construction permit Construction Permit shall be valid for the plan of construction schedule specified in the approved design report Construction Permit Application. The construction schedule may be amended by the director for good cause at the request of the applicant.

I.H. Construction must commence within two years after the permit is issued. If construction does not commence within two years after the permit is issued, the permit shall expire, except that the applicant may petition the board for extension of the two-year period and the board may extend such period for good cause with an appropriately updated plan of construction and temporary emergency action plan.

J. The director may revoke a construction permit if any of the permit terms are violated, or if construction is conducted in a manner hazardous to downstream life or property. The director may order the owner to eliminate such hazardous conditions within a period of time limited by the order. Such corrective measures shall be at the owner's expense. The applicant may petition the board to reissue the permit with such modifications as the board determines to be necessary.

K. The owner's professional engineer shall advise the director when the impounding structure may safely impound water. The director shall acknowledge this statement within 10 days after which the impoundment may be filled under the engineer's supervision. The director's acknowledgement shall act as a temporary operation and maintenance certificate until an operation and maintenance certificate has been applied for and issued in accordance with 4VAC50-20-110.

I. The board, the director, or both may take any necessary action consistent with the Dam Safety Act (§10.1-604 et seq. of the Code of Virginia) if any terms of this section or of the permit are violated, if the activities of the owner are not in accordance with the approved plans and specifications, if construction is conducted in a manner hazardous to downstream life or property, or for other cause as described in the Act.

J. Within 90 days after completion of the construction of an impounding structure, the owner shall submit:

1. A complete set of record drawings signed and sealed by a licensed professional engineer and signed by the owner:

2. A complete Record Report (Record Report for Virginia Regulated Impounding Structures) signed and sealed by a licensed professional engineer and signed by the owner that includes:

a. Project information including the name and inventory number of the structure, name of the reservoir, and whether the report is associated with a new or old structure;

b. Location of the impounding structure including the city or county, number of feet or miles upstream or downstream of a highway and the highway number, name of the river or the stream, and the latitude and longitude;

c. Owner’s name or representative if corporation, mailing address, residential and business telephone numbers, and other means of communication;

d. Information on the design report, including who it was prepared by, the date of design report preparation, whether it was for new construction or for an alteration, and the permit issuance date;

e. Owner’s engineer’s name, firm, professional engineer Virginia number, mailing address, and business telephone number;

f. Impounding structure data including type of material (earth, concrete, masonry or other) and the following configurations:

(1) Top of dam (elevation);

(2) Downstream toe – lowest (elevation);

(3) Height of dam (feet);

(4) Crest length – exclusive of spillway (feet);

(5) Crest width (feet);

(6) Upstream slope (horizontal and vertical); and

(7) Downstream slope (horizontal and vertical).

g. Reservoir data including the following:

(1) Maximum capacity (acre-feet);

(2) Maximum pool (elevation);

(3) Maximum pool surface area (acres);

(4) Normal capacity (acre-feet);

(5) Normal pool (elevation);

(6) Normal pool surface area (acres); and

(7) Freeboard – normal pool to top of dam (feet).

h. Spillway data including the type, construction material, design configuration, and invert elevation for the low level drain, the principal spillway, and the emergency spillway; a description of the low level drain and principal spillway including dimensions, trash guard information, and orientation of intake and discharge to dam if looking downstream; and a description of the emergency spillway including dimensions and orientation to dam if looking downstream;

i. Watershed data including drainage area (square miles); type and extent of watershed development; time of concentration (hours); routing procedure; spillway design flood used and state source; design inflow hydrograph volume (acre-feet), peak inflow (cfs), and rainfall duration (hours); freeboard during passage of the spillway design flood (feet); and confirmation as to whether the impounding structure has ever been overtopped;

j. Impounding structure history including the date construction was completed, who it was designed by and the date, who it was built by and the date, who performed inspections and dates, description of repairs, and confirmation as to whether the impounding structure has ever been overtopped;

k. A narrative describing the impounding structure procedures for operation, maintenance, filling, emergency action plan implementation, and structure evaluation;

l. A narrative describing the hydraulic and hydrologic data on the spillway design flood, hydrologic records, flood experience, flood potential, reservoir regulation, and comments or recommendations regarding these attributes;

m. A narrative describing stability of the foundation and abutments, embankment materials, and a written evaluation of each;

n. A complete set of record drawings signed and sealed by a licensed professional engineer and signed by the owner;

o. Certification by the owner’s engineer that the information provided pursuant to subdivision J 2 of this section is true and correct in their professional judgment. Such certification shall include the engineer’s signature, printed name, Virginia number, date, and the engineer’s Virginia seal; and

p. Owner’s signature certifying receipt of the information provided pursuant to subdivision J 2 of this section.

3. Certification from the licensed professional engineer who has monitored construction of the impounding structure during construction that, to the best of the engineer’s judgment, knowledge and belief, the impounding structure and its appurtenances were constructed in conformance with the plans, specifications, drawings and other requirements approved by the board;

4. Operation and Maintenance Certificate Application (Operation and Maintenance Certificate Application for Virginia Regulated Impounding Structures) in accordance with 4VAC50-20-105; and

5. Emergency Action Plan or Emergency Preparedness Plan in accordance with 4VAC50-20-175 or 4VAC50-20-177.

K. Upon completion of construction, the impoundment may be filled upon board issuance of an Operation and Maintenance Certificate.

4VAC50-20-80. Alterations permits.

A. Application for a permit to alter an impounding structure in ways which would potentially affect its structural integrity shall be made on official forms. The application shall clearly describe the proposed work with appropriately detailed plans and specifications.

BA. Alterations which would potentially affect the structural integrity of an impounding structure include, but are not limited to, changing its the height or otherwise enlarging the dam, increasing the normal pool or principal spillway elevation or physical dimensions, changing the elevation or physical dimensions of the emergency spillway, conducting necessary repairs or structural maintenance, or removing the impounding structure.

C. Where feasible an application for an alteration permit shall also include plans and specifications for a device to allow for draining the impoundment if such does not exist.

D. If the submission is not acceptable, the director shall inform the applicant within 60 days and shall explain what changes are required for an acceptable submission.

E. Within 120 days of receipt of an acceptable application, the board shall act on the application.

B. An applicant for an Alteration Permit shall submit a design report. A form for the design report will be available from the department (Design Report for the Construction or Alteration of Virginia Regulated Impounding Structures). The design report shall be prepared in accordance with 4VAC50-20-240. The design report shall include, but not be limited to, the following information:

1. Project information including a description and benefits of the proposed alteration, name of the impounding structure, inventory number if available, name of the reservoir, and the purpose of the reservoir.

2. The hazard potential classification in conformance with Table 1 in 4VAC50-20-50.

3. Location of the impounding structure including the city or county, number of feet or miles upstream or downstream of a highway and the highway number, name of the river or the stream, and the latitude and longitude.

4. Owner’s name or representative if corporation, mailing address, residential and business telephone numbers, and other means of communication.

5. Owner’s engineer’s name, firm, professional engineer Virginia number, mailing address, and business telephone number.

6. Impounding structure data including type of material (earth, concrete, masonry or other) and the following configurations (note both existing and design configurations for each):

a. Top of dam (elevation);

b. Downstream toe – lowest (elevation);

c. Height of dam (feet);

d. Crest length – exclusive of spillway (feet);

e. Crest width (feet);

f. Upstream slope (horizontal and vertical); and

g. Downstream slope (horizontal and vertical).

7. Reservoir data including the following (note both existing and design configurations for each):

a. Maximum capacity (acre-feet);

b. Maximum pool (elevation);

c. Maximum pool surface area (acres);

d. Normal capacity (acre-feet);

e. Normal pool (elevation);

f. Normal pool surface area (acres); and

g. Freeboard – normal pool to top of dam (feet).

8. Spillway data including the type, construction material, design configuration, and invert elevation for the low level drain, the principal spillway, and the emergency spillway.

9. Watershed data including drainage area (square miles); type and extent of watershed development; time of concentration (hours); routing procedure; spillway design flood used and state source; design inflow hydrograph volume (acre-feet), peak inflow (cfs), and rainfall duration (hours); and freeboard during passage of the spillway design flood (feet).

10. Evidence that the local government has been notified of the alteration and repair plan.

11. Plans and specifications as required by 4VAC50-20-310. The plan view of the dam site should represent all significant structures and improvements that illustrate the location of all proposed work.

12. A report of the geotechnical investigations of the foundation soils, bedrock, or both in the areas affected by the proposed alterations and of the materials to be used to alter the impounding structure.

13. Design assumptions and analyses sufficient to indicate that the impounding structure will be stable during the alteration of the impounding structure under all conditions of reservoir operations.

14. Calculations and assumptions relative to design of the improved spillway or spillways, if applicable.

15. Provisions to ensure that the impounding structure and appurtenances during the alteration will be protected against unacceptable deterioration or erosion due to freezing and thawing, wind, wave action and rain or any combination thereof.

16. Other pertinent design data, assumptions and analyses commensurate with the nature of the particular impounding structure and specific site conditions, including when required by this chapter, a plan and profile of the dam break inundation zones.

17. If applicable, a description of the techniques to be used to divert stream flow during alteration work so as to prevent hazard to life, health and property, including a detailed plan and procedures to maintain a stable impounding structure during storm events, a drawing showing temporary diversion devices, and a description of the potential impoundment during the alteration. Such diversion plans shall be in accordance with the applicable environmental laws.

18. A plan for project construction monitoring and quality control testing to confirm that materials used in the alteration work and that performance standards meet the design requirements set forth in the specifications.

19. Certification by the owner’s engineer that the information provided pursuant to this subsection is true and correct in their professional judgment. Such certification shall include the engineer’s signature, printed name, Virginia number, date, and the engineer’s Virginia seal.

20. Owner’s signature certifying receipt of the information provided pursuant to this subsection.

C. A plan of construction is a required element of complete permit application and shall include:

1. A construction sequence with milestones.

2. Elements of the work plan that should be considered include, but are not limited to, foundation and abutment treatment, excavation and material fill processes, phased fill and compaction, testing and control procedures, construction of permanent spillway and drainage devices, if applicable.

3. The erosion and sediment control plan, as approved by the local government, which minimizes soil erosion and sedimentation during all phases of construction.

D. Within 120 days of receipt of a complete Alteration Permit Application, the board shall act on the application. If the application is not acceptable, the director shall inform the applicant within 60 days of receipt and shall explain what changes are required for an acceptable application. A complete Alteration Permit Application consists of the following:

1. A final design report with attachments as needed, and certified by the owner;

2. A plan of construction that meets the requirements of subsection C of this section;

3. Any necessary interim provisions to the current Emergency Action Plan or Emergency Preparedness Plan. Interim provisions shall be submitted to the local organization for emergency management, the Virginia Department of Emergency Management, and the department; and

4. If the owner is requesting the deregulation of an impounding structure, the application shall specify whether the impounding structure is to be removed so that the impounding structure is incapable of storing water, either temporarily or permanently; or whether the impounding structure is to be altered in such a manner that either the height or storage capacity of the impounding structure causes the impounding structure to be of less than regulated size.

E. During the alteration work, the owner shall provide the director with any proposed changes from the approved design, plans, specifications, or a plan of construction. Approval shall be obtained from the director prior to the alteration or installation of any changes that will affect the integrity or impounding capacity of the impounding structure.

F. The Alteration Permit shall be valid for the construction sequence with milestones specified in the approved Alteration Permit Application.

G. Work identified in the Alteration Permit must commence within the time frame identified in the Alteration Permit. If work does not commence within the prescribed time frame, the permit shall expire, except that the applicant may petition the board for extension of the prescribed time frame and the board may extend such period for good cause with an updated construction sequence with milestones.

H. The board, the director, or both may take any necessary action consistent with the Dam Safety Act (§10.1-604 et seq. of the Code of Virginia) if any terms of this section or of the permit are violated, if the activities of the owner are not in accordance with the approved plans and specifications, if the alteration is conducted in a manner hazardous to downstream life or property, or for other cause as described in the Act.

I. Within 90 days after completion of the alteration of an impounding structure, the owner shall submit a complete Record Report. A form for the Record Report will be available from the department (Record Report for Virginia Regulated Impounding Structures). The Record Report signed and sealed by a licensed professional engineer and signed by the owner to the department indicating the modifications made to the structural features of the impounding structure. This report is not required when the Alteration Permit has been issued for the removal of an impounding structure. The Record Report shall include the following:

a. Project information including the name and inventory number of the structure, name of the reservoir, and whether the report is associated with a new or old structure;

b. Location of the impounding structure including the city or county, number of feet or miles upstream or downstream of a highway and the highway number, name of the river or the stream, and the latitude and longitude;

c. Owner’s name or representative if corporation, mailing address, residential and business telephone numbers, and other means of communication;

d. Information on the design report, including who it was prepared by, the date of design report preparation, whether it was for new construction or for an alteration, and the permit issuance date;

e. Owner’s engineer’s name, firm, professional engineer Virginia number, mailing address, and business telephone number;

f. Impounding structure data including type of material (earth, concrete, masonry or other) and the following configurations:

(1) Top of dam (elevation);

(2) Downstream toe – lowest (elevation);

(3) Height of dam (feet);

(4) Crest length – exclusive of spillway (feet);

(5) Crest width (feet);

(6) Upstream slope (horizontal and vertical); and

(7) Downstream slope (horizontal and vertical).

g. Reservoir data including the following:

(1) Maximum capacity (acre-feet);

(2) Maximum pool (elevation);

(3) Maximum pool surface area (acres);

(4) Normal capacity (acre-feet);

(5) Normal pool (elevation);

(6) Normal pool surface area (acres); and

(7) Freeboard – normal pool to top of dam (feet).

h. Spillway data including the type, construction material, design configuration, and invert elevation for the low level drain, the principal spillway, and the emergency spillway; a description of the low level drain and principal spillway including dimensions, trash guard information, and orientation of intake and discharge to dam if looking downstream; and a description of the emergency spillway including dimensions and orientation to dam if looking downstream;

i. Watershed data including drainage area (square miles); type and extent of watershed development; time of concentration (hours); routing procedure; spillway design flood used and state source; design inflow hydrograph volume (acre-feet), peak inflow (cfs), and rainfall duration (hours); and freeboard during passage of the spillway design flood (feet);

j. Impounding structure history including the date construction was completed, who it was designed by and the date, who it was built by and the date, who performed inspections and dates, description of repairs, and confirmation as to whether the impounding structure has ever been overtopped;

k. A narrative describing the impounding structure procedures for operation, maintenance, emergency action plan implementation, and structure evaluation;

l. A narrative describing the hydraulic and hydrologic data on the spillway design flood, hydrologic records, flood experience, flood potential, reservoir regulation, and comments or recommendations regarding these attributes;

m. A narrative describing stability of the foundation and abutments, embankment materials, and a written evaluation of each;

n. A complete set of record drawings signed and sealed by a licensed professional engineer and signed by the owner;

o. Certification by the owner’s engineer that the information provided pursuant to subdivision I 2 of this section is true and correct in their professional judgment. Such certification shall include the engineer’s signature, printed name, Virginia number, date, and the engineer’s Virginia seal; and

p. Owner’s signature certifying receipt of the information provided pursuant to subdivision I 2 of this section.

J. For altered impounding structures, a certification from a licensed professional engineer who has monitored the alteration of the impounding structure that, to the best of the engineer’s judgment, knowledge, and belief, the impounding structure and its appurtenances were altered in conformance with the plans, specifications, drawings and other requirements approved by the board.

4VAC50-20-90. Transfer of permits.

A. Prior to the transfer of ownership of a permitted impounding structure the permittee shall notify the director in writing and the new owner shall file a transfer application on official forms notification with the department. A form for the transfer notification will be available from the department (Transfer of Impounding Structure Notification form Past Owner to New Owner). The new owner shall amend the existing permit application as necessary and shall certify to the director that he is aware of and will comply with all of the requirements and conditions of the permit.

B. The Transfer Notification shall include the following required information:

1. Project information including the name and inventory number of the structure, name of the reservoir, and impoundment hazard classification;

2. Location of the impounding structure including the city or county, number of feet or miles upstream or downstream of a highway and the highway number, name of the river or the stream, and the latitude and longitude;

3. Type of certificates and permits to be transferred including effective date and expiration date of all certificates and permits;

4. Past owner’s name, mailing address, and residential and business telephone numbers;

5. New owner’s name, mailing address, and residential and business telephone numbers;

6. Request to transfer certification statement signed and dated by the past owner;

7. Certification of compliance with permit or certificate with all said terms and conditions signed and dated by the new owner; and

8. Contact information updates for Emergency Action Plan or Emergency Preparedness Plan provided by the new owner. Such updates shall include the name, mailing address, and residential and business telephone numbers for the dam owner, dam operator, rainfall and staff gage observer, and alternate observer.

Part III

Certificate Requirements

4VAC50-20-100. Operation and maintenance certificates. (Repealed.)

A. A Class I Operation and Maintenance Certificate is required for a Class I Hazard potential impounding structure. The certificate shall be for a term of six years. It shall be updated based upon the filing of a new reinspection report certified by a professional engineer every two years.

B. A Class II Operation and Maintenance Certificate is required for a Class II Hazard potential impounding structure. The certificate shall be for a term of six years. It shall be updated based upon the filing of a new reinspection report certified by a professional engineer every three years.

C. A Class III Operation and Maintenance Certificate is required for a Class III Hazard potential impounding structure. The certificate shall be for a term of six years.

D. The owner of a Class I, II or III impounding structure shall provide the director an annual owner's inspection report on official forms in years when no professional reinspection is required and may be done by the owner or his representative.

E. If an Operation and Maintenance Certificate is not updated as required, the board shall take appropriate enforcement action.

F. The owner of a Class I, II or III impounding structure shall apply for the renewal of the six year operation and maintenance certificate 90 days prior to its expiration in accordance with 4VAC50-20-120 of this chapter.

G. A Class IV impounding structure will not require an operation and maintenance certificate. An inventory report is to be prepared as provided in 4VAC50-20-120 B and filed by the owner on a six-year interval, and an owners inspection report filed annually.

H. The owner of any impounding structure, regardless of its hazard classification, shall notify the board immediately of any change in either cultural features downstream from the impounding structure or of any change in the use of the area downstream that would present hazard to life or property in the event of failure.

4VAC50-20-105. Regular Operation and Maintenance Certificates.

A. A Regular Operation and Maintenance Certificate is required for an impounding structure. Such six-year certificates shall include the following based on hazard classification:

1. High Hazard Potential Regular Operation and Maintenance Certificate;

2. Significant Hazard Potential Regular Operation and Maintenance Certificate; or

3. Low Hazard Potential Regular Operation and Maintenance Certificate.

B. The owner of an impounding structure shall apply for the renewal of the six-year Regular Operation and Maintenance Certificate 90 days prior to its expiration. If a Regular Operation and Maintenance Certificate is not renewed as required, the board shall take appropriate enforcement action.

C. Any owner of an impounding structure that does not have a Regular Operation and Maintenance Certificate or any owner renewing a Regular Operation and Maintenance Certificate shall file an Operation and Maintenance Certificate Application. A form for the application will be available from the department (Operation and Maintenance Certificate Application for Virginia Regulated Impounding Structures). Such application shall be signed by the owner and signed and sealed by a licensed professional engineer. The following information shall be submitted on or with the application:

1. The application shall include the following required information:

a. The name of structure and inventory number;

b. The proposed hazard potential classification;

c. Owner’s name or representative if corporation, mailing address, residential and business telephone numbers, and other means of communication;

d. An operating plan and schedule including a narrative on the operation of control gates and spillways and the impoundment drain;

e. For earthen embankment dams, a maintenance plan and schedule for the embankment, principal spillway, emergency spillway, low-level outlet, impoundment area, downstream channel, and staff gages;

f. For concrete dams, a maintenance plan and schedule for the upstream face, downstream face, crest of dam, galleries, tunnels, abutments, spillways, gates and outlets, and staff gages;

g. An inspection schedule for operator inspection, maintenance inspection, technical safety inspection, and overtopping situations;

h. A schedule including the rainfall amounts, emergency spillway flow levels or storm event that initiates the Emergency Action or Preparedness Plan and the frequency of observations;

i. A statement as to whether or not the current hazard potential classification for the dam is appropriate and whether or not additional work is needed to make an appropriate hazard potential designation;

j. For newly constructed or recently altered impounding structures, a certification from a licensed professional engineer who has monitored the construction or alteration of the impounding structure that, to the best of the engineer’s judgment, knowledge, and belief, the impounding structure and its appurtenances were constructed or altered in conformance with the plans, specifications, drawings and other requirements approved by the board;

k. Certification by the owner’s engineer that the Operation and Maintenance Certificate Application information provided pursuant to subdivision 1 of this subsection is true and correct in their professional judgment. Such certification shall include the engineer’s signature, printed name, Virginia number, date, and the engineer’s Virginia seal; and

l. Owner’s signature certifying the Operation and Maintenance Certificate Application information provided pursuant to subdivision 1 of this subsection and that the operation and maintenance plan and schedule shall be conducted in accordance with this chapter.

2. An Inspection Report (Annual Inspection Report for Virginia Regulated Impounding Structures) in accordance with subsection E of this section;

3. An Emergency Action Plan in accordance with 4VAC50-20-175 or an Emergency Preparedness Plan in accordance with 4VAC50-20-177 and evidence that the required copies of such plan have been submitted to the local organization for emergency management and the Virginia Department of Emergency Management; and

4. Any additional analysis determined necessary by the director, the board or the owner’s engineer to address public safety concerns. Such additional analysis may include, but not be limited to, seismic stability, earthen spillway integrity, adequate freeboard allowance, stability assessment of the impoundment’s foundation, potential liquefaction of the embankment, overturning or sliding of a concrete structure and other structural stress issues.

D. If the Operation and Maintenance Certificate Application submittal is found to be not complete, the director shall inform the applicant within 30 days and shall explain what changes are required for an acceptable submission. Within 60 days of receipt of a complete application the board shall act upon the application. Upon finding that the impounding structure as currently operating is in compliance with this chapter, the board shall issue a Regular Operation and Maintenance Certificate. Should the board find that the impounding structure as currently operating is not in compliance with this chapter, the board may deny the permit application or issue a Conditional Operation and Maintenance Certificate in accordance with 4VAC50-20-150.

E. Inspections shall be performed on an impounding structure annually.

1. Inspection Reports (Annual Inspection Report for Virginia Regulated Impounding Structures) signed and sealed by a licensed professional engineer shall be submitted to the department in accordance with the following schedule:

a. For a High Hazard Potential impounding structure, every two years,

b. For a Significant Hazard Potential impounding structure, every three years,

c. For a Low Hazard Potential impounding structure, every six years.

In years when an Inspection Report signed and sealed by a licensed professional engineer is not required, an owner shall submit the Annual Inspection Report for Virginia Regulated Impounding Structures.

2. The Inspection Report shall include the following required information:

a. Project information including the name and inventory number of structure, name of the reservoir, and purpose of the reservoir;

b. City or county where the impounding structure is located;

c. Owner’s name or representative if corporation, mailing address, residential and business telephone numbers, and other means of communication;

d. Owner’s engineer’s name, firm, professional engineer Virginia number, mailing address, and business telephone number;

e. Inspection observation of the impounding structure including the following:

(1) Earthen embankment information including any embankment alterations; erosion; settlement, misalignments or cracks; seepage and seepage flow rate and location;

(2) Upstream slope information including notes on woody vegetation removed, rodent burrows discovered, and remedial work performed;

(3) Intake structure information including notes on deterioration of concrete structures, exposure of rebar reinforcement, need to repair or replace trash rack, any problems with debris in the reservoir, and whether the drawdown valve operated;

(4) Abutment contacts including notes on seepage and seepage flow rate and location;

(5) Earthen emergency spillway including notes on obstructions to flow and plans to correct, rodent burrows discovered, and deterioration in the approach or discharge channel;

(6) Concrete emergency spillway including notes on the deterioration of the concrete, exposure of rebar reinforcement, any leakage below concrete spillway, and obstructions to flow and plans to correct;

(7) Downstream slope information including notes on woody vegetation removed, rodent burrows discovered, whether seepage drains are working, and any seepage or wet areas;

(8) Outlet pipe information including notes on any water flowing outside of discharge pipe through the dam and a description of any reflection or damage to the pipe;

(9) Stilling basin information including notes on the deterioration of the concrete, exposure of rebar reinforcement, deterioration of the earthen basin slopes, repairs made, and any obstruction to flow;

(10) Gates information including notes on gate malfunctions or repairs, corrosion or damage, and whether any gates were operated and if so how often and to what extreme;

(11) Reservoir information including notes on new developments upstream of the dam, slides or erosion of lake banks, and general comments to include silt, algae, or other influence factors;

(12) Instruments information including any reading of instruments and any installation of new instruments; and

(13) General information including notes on new development in the downstream floodplain that would impact hazard classification, the maximum stormwater discharge or peak elevation during the previous year, whether general maintenance was performed and when, and actions that need to be completed before the next inspection.

f. Evaluation rating of the dam and appurtenances (excellent, good, or poor), general comments, and recommendations;

g. Certification by the owner and date of inspection; and

h. Certification and seal by the owner’s engineer and date of inspection, as applicable.

F. The owner of an impounding structure shall notify the department immediately of any change in the use of the area downstream that would impose hazard to life or property in the event of failure.

4VAC50-20-110. Operation and maintenance certificate for newly constructed impounding structures. (Repealed.)

A. Within 180 days after completion of the construction of an impounding structure, the owner shall submit:

1. A complete set of as-built drawings certified by a professional engineer and an as-built report on official forms.

2. A copy of a certificate from the professional engineer who has inspected the impounding structure during construction certifying that, to the best of his judgment, knowledge and belief, the impounding structure and its appurtenances were constructed in conformance with the plans, specifications, drawings and other requirements approved by the board.

3. A copy of the operation and maintenance plan and emergency action plan submitted with the design report including any changes required by the director.

B. If the director finds that the operation and maintenance plan or emergency action plan is deficient, he shall return it to the owner within 60 days with suggestions for revision.

C. Within 60 days of receipt of the items listed in subsection A above, if the board finds that adequate provision has been made for the safe operation and maintenance of the impounding structure, the board shall issue an operation and maintenance certificate.

4VAC50-20-120. Operation and maintenance certificates for existing impounding structures. (Repealed.)

A. Any owner of an impounding structure other than a Class IV impounding structure which has already filed an inventory report that does not have an operation and maintenance certificate or any owner renewing an operation and maintenance certificate shall file an application with the board.

B. The application for an operation and maintenance certificate shall be on official forms and shall include:

1. A reinspection report for Class I and II impounding structures. The reinspection report shall include an update of conditions of the impounding structure based on a previous safety inspection as required by the board, a previous reinspection report or an as-built report.

2. An inventory report for Class III impounding structures. The inventory report shall include:

a. The name and location of the impounding structure and the name of the owner.

b. The description and dimensions of the impounding structure, the spillways, the reservoir and the drainage area.

c. The history of the impounding structure which shall include the design, construction, repairs, inspections and whether the structure has been overtopped.

d. Observations of the condition of the impounding structure, reservoir, and upstream and downstream areas.

e. Any changes in the impounding structure, reservoir, and upstream and downstream areas.

f. Recommendations for remedial work.

3. An impoundment and impounding structure operation and maintenance plan certified by a professional engineer. This plan shall place particular emphasis on operating and maintaining the impounding structure in keeping with the project design in such manner as to maintain its structural integrity and safety during both normal and abnormal conditions which may reasonably be expected to occur during its planned life. The safety inspection report required by the board should be sufficient to serve as the basis for the operation and maintenance plan for a Class I and Class II impounding structure. For a Class III impounding structure, the operation and maintenance plan shall be based on the data provided in the inventory report.

4. An emergency action plan and evidence that a copy of such plan has been filed with the local organization for emergency management and the State Department of Emergency Management. The plan shall include a method of providing notification and warning to persons downstream, other affected persons or property owners and local authorities in the event of a flood hazard or the impending failure of the impounding structure.

C. The owner shall certify in writing that the operation and maintenance plan approved by the board will be adhered to during the life of the project except in cases of emergency requiring departure therefrom in order to mitigate hazard to life and property, at which time the owner's engineer and the director shall be notified.

D. If the director finds that the operation and maintenance plan or emergency action plan is deficient, he shall return it to the owner within 60 days with suggestions for revision.

E. Within 60 days of receipt of an acceptable application if the board finds that adequate provision has been made for the safe operation and maintenance of the impounding structure, the board shall issue an operation and maintenance certificate.

4VAC50-20-125. Delayed effective date for Spillway Design Flood requirements for impounding structures.

A. If an impounding structure has been determined to have an adequate spillway capacity prior to the effective date of these regulations and is currently operating under a Regular Operation and Maintenance Certificate, but will now require spillway modifications due to changes in these regulations, the owner shall submit to the board an Alteration Permit Application in accordance with 4VAC50-20-80 to address spillway capacity at the time of the expiration of their Regular Operation and Maintenance Certificate or within three years of the effective date of these regulations, whichever is later. The Alteration Permit Application shall contain a construction sequence with milestones for completing the necessary improvements within five years of Alteration Permit issuance. The board may approve an extension of the prescribed time frame for good cause. Should the owner be able to demonstrate that no spillway capacity change is necessary, the impounding structure may be found to be in compliance with this chapter.

B. In accordance with 4VAC50-20-105, the owner shall submit the Operation and Maintenance Certificate Application (Operation and Maintenance Certificate Application for Virginia Regulated Impounding Structures), the Emergency Action Plan or Emergency Preparedness Plan, and the Inspection Report (Annual Inspection Report for Virginia Regulated Impounding Structures) 90 days prior to the expiration of the Regular Operation and Maintenance Certificate.

C. If circumstances warrant more immediate repairs to the impounding structure, the board may direct alterations to the spillway to be completed sooner.

D. During this delay period, owners are required to address other deficiencies that may exist that are not related to the spillway design flood.

4VAC50-20-130. Existing impounding structures constructed prior to July 1, 1982. (Repealed.)

A. Many existing impoundment structures were designed and constructed prior to the enactment of the Dam Safety Act, and may not satisfy current criteria for new construction. The board may issue an operation and maintenance certificate for such structures provided that:

1. Operation and maintenance is determined by the director to be satisfactory and up to date;

2. Annual owner's inspection reports have been filed with and are considered satisfactory by the director;

3. The applicant proves in accordance with the current design procedures and references of 4VAC50-20-320 to the satisfaction of the board that the impounding structure as designed, constructed, operated and maintained does not pose an unreasonable hazard to life and property; and

4. The owner satisfies all special requirements imposed by the board.

B. When appropriate with existing impounding structures only, the spillway design flood requirement may be reduced by the board to the spillway discharge at which dam failure will not significantly increase the downstream hazard existing just prior to dam failure provided that the conditions of 4VAC50-20-130 A have been met.

4VAC50-20-140. Existing impounding structures constructed after July 1, 1982. (Repealed.)

The board may issue an operation and maintenance certificate for an impounding structure having a construction permit issued after July 1, 1982, and shall not require upgrading to meet new more stringent criteria unless the board determines that the new criteria must be applied to prevent an unreasonable hazard to life or property.

4VAC50-20-150. Conditional operation and maintenance certificate.

A. During the review of any operation Operation and maintenance application Maintenance Certificate Application (Operation and Maintenance Certificate Application for Virginia Regulated Impounding Structures) completed in accordance with 4VAC50-20-105 should the director determine that the impounding structure has nonimminent deficiencies of a nonimminent danger category, the director may recommend that the board issue a conditional operation Conditional Operation and maintenance certificate Maintenance Certificate.

B. The conditional operation Conditional Operation and maintenance certificate Maintenance Certificate for Class I, II and III High, Significant, and Low Hazard Potential impounding structures shall be for a maximum term of two years. This certificate will allow the owner to continue normal operation and maintenance of the impounding structure, and shall require that the owner correct the deficiencies on a schedule determined by the director board.

C. A conditional certificate Conditional Certificate may be renewed extended in accordance with the procedures of 4VAC50-20-120 4VAC50-20-155 provided that annual owner inspection reports Inspection Reports (Annual Inspection Report for Virginia Regulated Impounding Structures) are on file, and the board determines that the owner is proceeding with the necessary corrective actions.

D. Once the deficiencies are corrected, the board shall issue an operation a Regular Operation and maintenance certificate Maintenance Certificate based upon any required revisions to the original application the impounding structure’s meeting the requirements of 4VAC50-20-105.

4VAC50-20-155. Extension of Operation and Maintenance Certificates.

The board may extend an Operation and Maintenance Certificate for impounding structures provided that the owner submits a written request justifying an extension, the amount of time needed to comply with the requirements set out in the current Operation and Maintenance Certificate, and any required fees. The owner must have demonstrated substantial and continual progress towards meeting the requirements.

4VAC50-20-160. Additional operation and maintenance requirements.

A. The owner of an impounding structure shall not, through action or inaction, cause or allow such structure to impound water following receipt of a written report from the owner's engineer that the impounding structure will not safely impound water.

B. In accordance with §10.1-609.2 of the Code of Virginia, dam owners shall not permit the growth of trees and other woody vegetation and shall remove any such vegetation from the slopes and crest of embankments and the emergency spillway area, and within a distance of 25 feet from the toe of the embankment and abutments of the dam.

4VAC50-20-165. Agricultural Exemption.

A. Impounding structures operated primarily for agricultural purposes that are less than 25 feet in height or that create a maximum impoundment capacity smaller than 100 acre-feet are exempt from the Impounding Structure Regulations.

B. An owner covered by an agricultural exemption pursuant to §10.1-604 of the Code of Virginia and 4VAC50-20-30 may validate such exemption by submitting an Agricultural Exemption Report (Agricultural Exemption Report for Impounding Structures). The Agricultural Exemption Report shall include the following information:

1. Project information including the name and inventory number of the structure and name of the reservoir;

2. Location of the impounding structure including the city or county, number of feet or miles upstream or downstream of a highway and the highway number, name of the river or the stream, and the latitude and longitude;

3. Owner’s name or representative if corporation, mailing address, residential and business telephone numbers, and other means of communication;

4. The impounding structure height in feet and the maximum impounding capacity in acre-feet;

5. A list of the agricultural functions for which the impoundment supplies water;

6. The date of validation; and

7. The owner’s signature validating that the impoundment is operated primarily for agricultural purposes and is exempt from the regulations.

C. The Agricultural Exemption Report may be verified by the department through a possible site visit.

4VAC50-20-170. Transfer of certificates.

A. Prior to the transfer of ownership of an impounding structure the certificate holder shall notify the director in writing and the new owner shall file a transfer application on official forms notification with the department. A form for the transfer notification will be available from the department (Transfer of Impounding Structure Notification from Past Owner to New Owner). The new owner may elect to continue the current existing operation and maintenance certificate for the remaining term or he may apply for a new certificate in accordance with 4VAC50-20-120 4VAC50-20-105. If the owner elects to continue the existing certificate, he shall amend the existing certificate application as necessary and shall certify to the director that he is aware of and will comply with all of the requirements and conditions of the certificate.

B. The Transfer Notification shall include the following required information:

1. Project information including the name and inventory number of the structure, name of the reservoir, and impoundment hazard classification;

2. Location of the impounding structure including the city or county, number of feet or miles upstream or downstream of a highway and the highway number, name of the river or the stream, and the latitude and longitude;

3. Type of certificates and permits to be transferred including effective date and expiration date of all certificates and permits;

4. Past owner’s name, mailing address, and residential and business telephone numbers;

5. New owner’s name, mailing address, and residential and business telephone numbers;

6. Request to transfer certification statement signed and dated by the past owner;

7. Certification of compliance with permit or certificate with all said terms and conditions signed and dated by the new owner; and

8. Contact information updates for Emergency Action Plan or Emergency Preparedness Plan provided by the new owner. Such updates shall include the name, mailing address, and residential and business telephone numbers for the dam owner, dam operator, rainfall and staff gage observer, and alternate observer.

Part IV

Procedures

4VAC50-20-175. Emergency Action Plan (EAP) for High and Significant Hazard Potential Dams.

A. In order to protect life during potential emergency conditions at a dam, and to ensure effective, timely action is taken should a dam emergency occur, an EAP shall be required for each High and Significant Hazard Potential impounding structure. The EAP shall be coordinated with the Department of Emergency Management in accordance with §44-146.18 of the Code of Virginia. The EAP required by these regulations shall be incorporated into local and interjurisdictional emergency plans pursuant to §44-146.19 of the Code of Virginia.

B. It is the dam owner’s responsibility to develop, maintain, exercise, and implement a site-specific EAP.

C. An EAP shall be submitted every six years. The EAP shall be submitted with the owner’s submittal of their Regular Operation and Maintenance Certificate application (Operation and Maintenance Certificate Application for Virginia Regulated Impounding Structures).

D. The owner shall update the EAP immediately upon becoming aware of necessary changes to keep the EAP workable. Should a dam be reclassified, an EAP in accordance with this section shall be submitted.

E. A drill shall be conducted annually for each high or significant hazard impounding structure. To the extent practicable, the drill should include a face-to-face meeting with the local emergency management agencies responsible for any necessary evacuations to review the EAP and ensure the local emergency management agencies understand the actions required during an emergency. A table-top exercise shall be conducted once every three years. Owners shall certify to the department annually that a drill, a table-top exercise, or both has been completed, provide a critique of the exercise or exercises and any revisions or updates to the EAP or a statement that no revisions or updates are needed.

F. Dam owners shall test existing monitoring, sensing, and warning equipment at remote or unattended dams at least twice per year and maintain a record of such tests.

G. An EAP shall contain the following seven basic elements unless otherwise specified in this subsection.

1. Notification chart. A notification chart shall be included for all classes of dams that shows who is to be notified, by whom, and in what priority. The notification chart shall include contact information providing 24-hour telephone coverage for all responsible parties.

2. Emergency Detection, Evaluation, and Classification. The EAP shall include a discussion of the procedures for timely and reliable detection, evaluation, and classification of emergency situations considered to be relevant to the project setting and impounding features. Each relevant emergency situation is to be documented to provide an appropriate course of action based on the urgency of the situation. Where appropriate, situations should address dam breaks that are imminent or in progress, a situation where the potential for dam failure is rapidly developing, and a situation where the threat is slowly developing.

3. Responsibilities. The EAP shall specify responsibilities for EAP-related tasks. The EAP shall also clearly designate the responsible party for making the decision that an emergency condition no longer exists at the dam. The EAP shall include procedures and the responsible parties for notifying to the extent possible any known local occupants, owners, or lessees of downstream properties potentially impacted by the dam’s failure.

4. Preparedness. The EAP shall include a section that describes preparedness actions to be taken both before and following development of emergency conditions.

5. Dam Break Inundation Maps. The EAP shall include dam break inundation maps developed in accordance with 4VAC50-20-54.

6. Appendices. The appendices shall contain information that supports and supplements the material used in the development and maintenance of the EAP such as analyses of dam break floods; plans for training, exercising, updating, and posting the EAP; and other site-specific concerns.

7. Certification. The EAP shall include a section that is signed by all parties with assigned responsibilities in the EAP pursuant to this subdivision 3 of this subsection, where they indicate their receipt of the EAP. The preparer’s name, title, and contact information shall be printed in this section. The preparer’s signature shall also be included in the certification section. The local organization for emergency management shall provide the owner and the department with any deficiencies they may note.

H. The development of the EAP shall be coordinated with all entities, jurisdictions, and agencies that would be affected by a dam failure or that have statutory responsibilities for warning, evacuation, and postflood actions. Consultation with state and local emergency management officials at appropriate levels of management responsible for warning and evacuation of the public shall occur to ensure that there is awareness of their individual and group responsibilities. The owner shall also coordinate with the local organization for emergency management to identify properties that upon failure of the impounding structure would result in economic impacts.

I. The EAP, or any updates to an existing EAP, shall be submitted to the department, the local organization for emergency management, and the Virginia Department of Emergency Management. Two copies shall be provided to the department.

J. The following format shall be used as necessary to address the requirements of this section.

Title Page/Cover Sheet

Table of Contents

I. Certifications

II. Notification Flowchart

III. Statement of Purpose

IV. Project Description

V. Emergency Detection, Evaluation, and Classification

VI. General Responsibilities Under the EAP

A. Dam Owner Responsibilities

B. Responsibility for Notification

C. Responsibility for Evacuation

D. Responsibility for Termination and Follow-Up

E. EAP Coordinator Responsibility

VII. Preparedness

VIII. Inundation Maps

IX Appendices

A. Investigation and Analyses of Dam break Floods

B. Plans for Training, Exercising, Updating, and Posting the EAP

C. Site-Specific Concerns

4VAC50-20-177. Emergency Preparedness Plan for Low Hazard Dams.

A. Low Hazard Dams shall provide information for emergency preparedness to the department, the local organization for emergency management and the Virginia Department of Emergency Management. A form for the submission will be available from the department (Emergency Preparedness Plan for Low Hazard Virginia Regulated Impounding Structures). The information shall include, but not be limited, to the following:

1. Name of the impounding structure, inventory number, city or county, latitude, and longitude;

2. Owner’s name, mailing address, residential and business telephone numbers, and other means of communication. Contact information shall provide for 24-hour telephone contact capability;

3. Dam operator’s name, mailing address, residential and business telephone numbers, and other means of communication. Contact information shall provide for 24-hour telephone contact capability;

4. Rainfall and staff gage observer’s name, mailing address, residential and business telephone numbers, and other means of communication. Contact information shall provide for 24-hour telephone contact capability;

5. Contact information for alternate operator and alternate rainfall and staff gage observer, if applicable;

6. Contact information for the local dispatch center nearest dam including address and 24-hour telephone number;

7. City or county emergency services coordinator’s name, mailing address, residential and business telephone numbers, and other means of communication;

8. A procedure and the responsible parties for notifying to the extent possible any known local occupants, owners, or lessees of downstream properties potentially impacted by the dam’s failure;

9. A discussion of the procedures for timely and reliable detection, evaluation, and classification of emergency situations considered to be relevant to the project setting and impounding features. Each relevant emergency situation is to be documented to provide an appropriate course of action based on the urgency of the situation;

10. A simple dam break inundation map acceptable to the director, demonstrating the general inundation that would result from a dam failure. Such maps required pursuant to this section do not require preparation by a professional licensed engineer; however, maps prepared by a licensed professional engineer are preferred;

11. Identification of public roads downstream noting the highway number and distance below the dam. If roads exist, contact information for the resident Virginia Department of Transportation engineer or city or county engineer including address and 24-hour telephone numbers;

12. Amount of rainfall that will initiate a Stage II Condition in inches per six hours, inches per 12 hours, and inches per 24 hours and a Stage III Condition in inches per six hours, inches per 12 hours, and inches per 24 hours;

13. Amount of flow in the emergency spillway that will initiate a Stage II Condition in feet (depth of flow) and a Stage III Condition in feet (depth of flow);

14. Staff gage location and description; the frequency of observations by the rainfall or staff gage observer under a Stage I Condition, and Stage II Condition, and a Stage III Condition; and a clear description of an access route and means of travel during flood conditions to the dam;

15. Evacuation procedures including notification, monitoring, evacuation, and reporting processes and responsibilities;

16. Evidence that the required copies of such plan have been submitted to the local organization for emergency management and the Virginia Department of Emergency Management; and

17. Certification of the plan by the owner.

Part IV

Procedures

4VAC50-20-180. Inspections.

A. The director may make inspections during construction, alteration or operation and maintenance as deemed necessary to ensure that the impounding structure is being constructed, altered or operated and maintained in compliance with the permit or certificate issued by the board. The director shall provide the owner a copy of the findings of these inspections. This The department’s inspection does not relieve the owner from the responsibility of providing adequate inspection during construction, alteration, or operation and maintenance. During the maintenance, construction, or alteration of any dam or reservoir, the director shall require the owner to perform, at the owner’s expense, such work or tests as necessary to obtain information sufficient to enable the director to determine whether conformity with the plans and specifications approved by the certificate is being secured.

B. Periodic inspections during construction or alteration shall be conducted under the supervision direction of a licensed professional engineer who shall propose the frequency and nature of the inspections subject to approval by the director provide for full-time monitoring, review of contractor submittals, and appropriate confirmatory testing of all facets of construction affecting the safety of the impounding structure in accordance with the construction or alteration permit issued by the board.

C. Periodic Required inspections during operation and maintenance shall be conducted under the supervision of a licensed professional engineer at an interval not greater than that required to update the operation and maintenance certificate. At a minimum, an annual owner's inspection shall be conducted when a professional inspection is not required intervals designated under 4VAC50-20-105.

D. Every owner shall provide for an inspection by a licensed professional engineer after overtopping of the impounding structure or after flows cause damage to the emergency spillway. A copy of the findings of each inspection with the engineer's recommendations shall be filed with the board within a reasonable period of time not to exceed 30 days subsequent to completion of the inspection.

4VAC50-20-200. Enforcement.

Any owner refusing to obey any order of the board or the director pursuant to this chapter may be compelled to obey and comply with such provisions by injunction or other appropriate remedy obtained in a court proceeding. Such proceeding shall be instituted by the board or in the case of an emergency, by the director in the court which granted approval to the owner to impound waters or, if such approval has not been granted, the proceeding shall be instituted in any appropriate court. The provisions of this chapter may be enforced by the board, the director, or both in any manner consistent with the provisions of the Dam Safety Act (§10.1-604 et seq. of the Code of Virginia).

4VAC50-20-210. Consulting boards committee.

A. When the board needs to satisfy questions of safety regarding plans and specifications, construction, alteration, or operation and maintenance, or when requested by the owner, the board may appoint a consulting board committee to report to it with respect to those questions of the impounding structure’s safety of an impounding structure. Such a board committee shall consist of two or more consultants, none of whom have been associated with the impounding structure.

B. The costs and expenses incurred by the consulting board committee, if appointed at the request of an owner, shall be paid by the owner.

C. The costs and expenses incurred by the consulting board committee, if initiated by the board, shall be paid by the board.

4VAC50-20-220. Unsafe conditions.

A. No owner shall have the right to maintain an unsafe impounding structure which unreasonably threatens the life or property of another person. The owner of any impounding structure found to have deficiencies which could threaten life or property if uncorrected shall take the corrective actions needed to remove such deficiencies within a reasonable period of time. Designation of an impounding structure as unsafe shall be made in accordance with §10.1-607.1 of the Code of Virginia.

B. Imminent danger.

1. If an owner or the owner’s engineer has determined that circumstances are impacting the integrity of the impounding structure that could result in the imminent failure of the impounding structure, temporary repairs may be initiated prior to approval from the board. The owner shall notify the department within 24 hours of identifying the circumstances impacting the integrity of the impounding structure. Such emergency notification shall not relieve the owner of the need to obtain an alteration permit as soon as may be practicable, nor shall the owner take action beyond that necessary to address the emergency situation.

2. When the director finds that an impounding structure is unsafe and constitutes an imminent danger to life or property, he shall immediately notify the State Virginia Department of Emergency Management and confer with the owner who shall activate the Emergency Action Plan or Emergency Preparedness Plan if appropriate to do so. The owner of an impounding structure found to constitute an imminent danger to life or property shall take immediate corrective action to remove the imminent danger as required by §10.1-608 of the Code of Virginia.

C. Nonimminent danger. The owner of an impounding structure who has been issued a report by the board containing findings and recommendations, by the board, for the correction of deficiencies which that may threaten life or property if not corrected, shall undertake to implement the recommendations for correction of deficiencies according to a schedule of implementation contained in that report as required by §10.1-609 of the Code of Virginia.

4VAC50-20-230. Complaints.

A. Upon receipt of a complaint alleging that the person or property of the complainant is endangered by the construction, alteration, maintenance or operation of an impounding structure, the director shall cause an inspection of the structure, unless the data, records and inspection reports on file with the board are found adequate to determine if the complaint is valid.

B. If the director finds that an unsafe condition exists, the director shall proceed under the provisions of §§10.1-608 and 10.1-609 of the Code of Virginia to render the extant condition safe.

Part V

Design Requirements

4VAC50-20-240. Design of structures.

A. The owner shall complete all necessary investigations prior to submitting the design report (Design Report for the Construction or Alteration of Virginia Regulated Impounding Structures). The design report shall contain those components outlined in 4VAC50-20-70 for construction activities or those outlined in 4VAC50-20-80 for alteration activities. The scope and degree of precision required is a matter of engineering judgment based on the complexities of the site and the hazard potential classification of the proposed structure.

B. Surveys shall be made with sufficient accuracy to locate the proposed construction site and to define the total volume of storage in the impoundment. Locations of center lines and other horizontal and vertical controls shall be shown on a map of the site. The area downstream and upstream from the proposed impounding structure shall be investigated in order to delineate the areas and extent of potential damage in case of failure or backwater due to flooding.

C. The drainage area shall be determined. Present, projected and potential future and planned land-use conditions shall be considered in determining the runoff characteristics of the drainage area. The most severe of these conditions shall be included in the design calculations which shall be submitted as part of the design report.

D. The geotechnical engineering investigation shall consist of borings, test pits and other subsurface explorations necessary to adequately define the existing conditions. The investigations shall be performed so as to appropriately define the soil, rock and ground water conditions.

E. All construction materials shall be adequately researched and selected so as to ensure that their properties meet as constructed behavior will reasonably conform to design criteria. If on-site materials are to be utilized, they shall be located and determined to be adequate in quantity and quality.

4VAC50-20-250. Design flood. (Repealed.)

The minimum design flood to be utilized in impounding structure evaluation, design, construction, operation and maintenance shall be commensurate with the size and hazard potential of the particular impounding structure as determined in 4VAC50-20-50 and Table 1. Competent, experienced, professional engineering judgment shall be used in applying those design and evaluation procedures referenced in 4VAC50-20-320 of this chapter.

4VAC50-20-260. Emergency spillway Spillway design.

A. Every impounding structure shall have a spillway system with adequate capacity to discharge the design flood without endangering the safety of the impounding structure.

B. An emergency spillway shall be required.

CB. Vegetated earth or an unlined emergency spillway may be approved when the applicant demonstrates that it will pass the spillway design flood without jeopardizing the safety of the impounding structure. In no case shall dam owners permit the growth of trees and other woody vegetation in the emergency spillway area.

DC. Lined emergency spillways shall include design criteria calculations, plans and specifications for open channel, drop, ogee and chute suitable energy dissipators and for spillways that include crest control structures, chutes, walls, panel lining, sills, blocks, and miscellaneous details. All joints shall be reasonably water-tight and placed on a foundation capable of sustaining applied loads without undue deformation. Provision shall be made for handling leakage from the channel or under seepage and uplift pressures from the foundation which might adversely affect the structural integrity and structural stability of the impounding structure.

4VAC50-20-270. Principal spillways and outlet works.

A. It will be assumed that principal spillways and regulating outlets provided for special functions will operate to normal design discharge capabilities during the spillway design flood, provided appropriate analyses show:

1. That control gates and structures are suitably designed to operate reliably under maximum heads for durations likely to be involved and risks of blockage by debris are minimal;

2. That access roads and passages to gate regulating controls would be safely passable by operating personnel under spillway design flood conditions; and

3. That there are no other substantial reasons for concluding that outlets would not operate safely to fill full design capacity during the spillway design flood.

B. If there are reasons to doubt that any of the above basic requirements might not be adequately met under spillway design flood conditions, the "dependable" discharge capabilities of regulating outlets shall be assumed to be less than 100% of design capabilities capacities, generally as outlined in the following subsections C through G of this section.

C. Any limitations in safe operating heads, maximum velocities to be permitted through structures or approach channels, or other design limitations shall be observed in establishing "dependable" discharge rating curves to be used in routing the spillway design flood hydrograph through the reservoir.

D. If intakes to regulating outlets are likely to be exposed to dangerous significant quantities of floating drift debris, sediment depositions or ice hazards prior to or during major floods, the dependable discharge capability during the spillway design flood shall be assumed to be zero.

E. If access roads or structural passages to operating towers or controls are likely to be flooded or otherwise unusable during the spillway design flood, the dependable discharge capability of regulating outlets will be assumed to be zero for those period the periods of time during which such conditions might exist.

F. Any deficiencies in discharge performance likely to result from delays in the operation of gates before attendants could be reasonably expected to reach the control for in must be taken into account when estimating "dependable" discharge capabilities to be assumed assumptions in routing the spillway design flood through reservoir the impoundment. Reports on design studies shall indicate the allowances made for possible delays in initiating gate operations. Normally, for projects located in small basins, where critical spillway design flood inflows may occur within several hours after intense precipitation, outflows through any regulating outlets that must be opened after the flood begins shall be assumed to be zero for an appropriate period of time subsequent to the beginning of intense rainfall.

G. All gates, valves, conduits and concrete channel outlets shall be designed and constructed to prevent significant erosion or damage to the impounding structure or to the downstream outlet or channel.

4VAC50-20-280. Drain requirements.

All new impounding structures regardless of their hazard potential classification, shall include a device to permit draining of the impoundment within a reasonable period of time as determined by the owner's licensed professional engineer, subject to approval by the director.

4VAC50-20-290. Life of the impounding structure.

Components of the impounding structure, the impoundment, the outlet works, drain system and appurtenances shall be durable or replaced in keeping with the design and planned life of the impounding structure.

4VAC50-20-300. Additional design requirements.

A. Flood routings shall start at or above the elevation of the crest of the lowest ungated outlet. Freeboard determination and justification must be addressed by the owner’s engineer.

B. All elements of the impounding structure and impoundments shall conform to sound engineering practice. Safety factors, design standards and design references that are used shall be included with the design report.

C. Inspection devices may be required by the director for use by inspectors, owners or the director in conducting inspections in the interest of structural integrity during and after completion of construction and during the life of the impounding structure.

4VAC50-20-310. Plans and specifications.

The plans and specifications for a proposed impounding structure required in 4VAC50-20-70 for construction activities and in 4VAC50-20-80 for alteration activities shall consist of a detailed engineering design report that includes (Design Report for the Construction or Alteration of Virginia Regulated Impounding Structures) and engineering drawings and specifications, with the following as a minimum:

1. The name of the project; the name of the owner; classification of the impounding structure as set forth in this chapter; designated access to the project and the location with respect to highways, roads, streams and existing impounding structures and impoundments that would affect or be affected by the proposed impounding structure.

2. Cross-sections, plans, profiles, logs of test borings, laboratory and in situ test data, drawings of principal and emergency spillways, impounding structures, outlet works, drain system and appurtenances, and other additional drawings project components in sufficient detail to indicate clearly the extent and complexity of the work to be performed.

3. Contract drawings should include, but not be limited to, foundation and abutment treatment, stream or river diversion, excavation and material fill processes, phased fill and compaction and drainage devices.

4. The erosion and sediment control plan, as approved by the local government, which minimizes soil erosion and sedimentation during all phases of construction or alteration.

3. The technical provisions 5. Technical specifications, as may be required to describe the materials, performance, and methods of the construction and construction quality control for the project.

4. Special provisions, as may be required to describe technical provisions needed to ensure that the impounding structure is constructed according to the approved plans and specifications.

4VAC50-20-320. Acceptable design procedures and references.

To ensure consistency of approach, within the major engineering disciplines of hydrology, hydraulics, soils and foundations, structures, and general civil design, criteria and approaches from multiple sources shall not be mixed for developing the design of a given feature or facility without approval of the director. In all cases the owner’s engineer shall identify the source of the criteria.

The following are acceptable as design procedures and references:

1. The design procedures, manuals and criteria used by the United States Army Corps of Engineers.

2. The design procedures, manuals and criteria used by the United States Department of Agriculture, Natural Resources Conservation Service.

3. The design procedures, manuals and criteria used by the United States Department of the Interior, Bureau of Reclamation.

4. The design procedures, manuals and criteria used by the United States Department of Commerce, National Weather Service.

5. The design procedures, manuals and criteria used by the United States Federal Agency Regulatory Commission

5.6. Other design procedures, manuals and criteria that are accepted as current, sound engineering practices, as approved by the director prior to the design of the impounding structure.

4VAC50-20-330. Other applicable dam safety references.

Manuals, guidance, and criteria used by the Federal Emergency Management Agency, including the following:

1. Federal Guidelines for Dam Safety: Emergency Action Planning for Dam Owners, U.S. Department of Homeland Security, Federal Emergency Management Agency, October 1998, Reprinted January 2004; FEMA 64 or as revised.

2. Federal Guidelines for Dam Safety: Selecting and Accommodating Inflow Design Floods for Dams, U.S. Department of Homeland Security, Federal Emergency Management Agency, October 1998, Reprinted April 2004; FEMA 94 or as revised.

Part VI

Fees

4VAC50-20-340. Authority to establish fees.

Under §10.1-613.5 of the Code of Virginia, the board is authorized to establish and collect application fees for the administration of the dam safety program, administrative review, certifications, and the repair and maintenance of dams. The fees will be deposited into the Dam Safety, Flood Prevention and Protection Assistance Fund.

4VAC50-20-350. Fee submittal procedures.

A. (Upon the effective date of these regulations,) fees for all application submittals required pursuant to 4VAC50-20-370 through 4VAC50-20-390 are due prior to issuance of a certificate or permit. No application for an Operation and Maintenance Certificate or a Construction Permit will be acted upon by the board without full payment of the required fee per §10.1-613.5 of the Code of Virginia.

B. Fees shall be paid by check, draft or postal money order payable to the Treasurer of Virginia, or submitted electronically (if available), and must be in U.S. currency, except that agencies and institutions of the Commonwealth of Virginia may submit Interagency Transfers for the amount of the fee. All fees shall be sent to the following address (or submitted electronically, if available): Virginia Department of Conservation and Recreation, Dam Safety Receipts Control, P.O. Box 10150, Richmond, Virginia 23240.

C. All fee payments shall be accompanied by the following information:

1. Applicant name, address and daytime phone number.

2. The name of the dam, and the dam location.

3. The type of application or report submitted.

4. Whether the submittal is for a new permit or certificate issuance or permit or certificate reissuance.

5. The amount of fee submitted.

6. Dam identification number, if applicable.

D. No permit fees remitted to the department shall be subject to refund except as credits provided for in 4VAC50-20-390 D.

4VAC50-20-360. Fee exemptions.

Impounding structures owned by Virginia Soil and Water Conservation Districts shall be exempt from all fees associated with Part VI in accordance with §10.1-613.5 of the Code of Virginia. There will be no fee assessed for the decommissioning of an impounding structure.

4VAC50-20-370. Construction Permit application fees.

A. Any application form submitted pursuant to 4VAC50-20-70 for permitting a proposed impounding structure construction after the effective date of these regulations shall be accompanied by a payment as determined in subsection B of this section.

B. Fees shall be as follows:

1. $2,500 for High or Significant Hazard Potential impounding structures

2. $1,000 for Low Hazard Potential impounding structures

4VAC50-20-380. Regular Operation and Maintenance Certificate application fees.

A. Any application for a six-year Regular Operation and Maintenance Certificate after the effective date of these regulations, except as otherwise exempted, shall be accompanied by a payment as determined in subsection B of this section.

B. Fees for High, Significant, or Low Hazard Potential impounding structures shall be as follows:

1. $1,500 for High Hazard Potential

2. $1,000 for Significant Hazard Potential

3. $600 for Low Hazard Potential

4VAC50-20-390. Conditional Operation and Maintenance Certificate application fee.

A. Fees for a Conditional Operation and Maintenance Certificate or for the extension of a Conditional Operation and Maintenance Certificate for High or Significant Hazard Potential impounding structures shall be as follows:

1. For a 2-year Certificate: $1,000

2. For a 1.5-year Certificate: $750

3. For a 1-year Certificate: $500

4. For a 6-month Certificate: $250

B. Fees for a Conditional Operation and Maintenance Certificate or for the extension of a Conditional Operation and Maintenance Certificate for Low Hazard Potential impounding structures shall be as follows:

1. For a 2-year Certificate: $500

2. For a 1.5-year Certificate: $375

3. For a 1-year Certificate: $250

4. For a 6-month Certificate: $125

C. Fees for a Conditional Operation and Maintenance Certificate or for the extension of a Conditional Operation and Maintenance Certificate for any impounding structure that requires a modification in spillway capacity due to changes in the regulations and that is eligible for a delayed effective date pursuant to 4VAC50-20-125 shall be as follows:

1. For a 2-year Certificate: $200

2. For a 1.5-year Certificate: $150

3. For a 1-year Certificate: $100

4. For a 6-month Certificate: $50

D. The board may allow a partial credit towards the Regular Operation and Maintenance Certificate fee if the owner of the impounding structure has completed, to the director’s satisfaction, the conditions of the Conditional Certificate prior to its expiration. Credits shall only be provided to the nearest 6-month interval.

4VAC50-20-400. Incremental Damage Analysis review fees.

The fee for the review of an incremental damage analysis submitted pursuant to 4VAC50-20-52 shall be $225. Re-review of an analysis determined to be incomplete or in error upon the department’s prior review shall cost an additional $45 per subsequent submittal. Should the department determine that outside expertise to assist with the review is necessary, the applicant shall be responsible for the cost of such outside expertise. Such costs shall be agreed upon in advance by the applicant.

FORMS

Dam Owner's Annual Inspection Form, DCR 199-098 (rev. 12/01).

Operation and Maintenance Application Class I, II and III Impounding Structures, DCR 199-099 (rev. 12/01).

As-Built Report for Class I, II and III Impounding Structures, DCR 199-100 (rev. 12/01).

Design Report for the Construction/Alteration of Impounding Structures, DCR 199-101 (rev. 12/01).

Emergency Action Plan for Class I, Class II and Class III Impounding Structures, DCR 199-103 (rev. 12/01).

Inventory Report for Class III and Class IV Impounding Structures, DCR 199-104 (rev. 12/01).

Reinspection Report for Class I and II Impounding Structures, DCR 199-105 (rev. 12/01).

Agricultural Certification for Impounding Structures, DCR 199-106 (rev. 12/01).

Transfer Application for Impounding Structures, DCR 199-107 (rev. 12/01).

VA.R. Doc. No. R06-130; Filed August 1, 2007, 12:03 p.m.