TITLE 13. HOUSING

BOARD OF HOUSING AND COMMUNITY DEVELOPMENT

Final Regulation

REGISTRAR'S NOTICE: The Board of Housing and Community Development is claiming an exemption from the Administrative Act pursuant to §2.2-4006 A 13 of the Code of Virginia, which excludes regulations adopted by the Board of Housing and Community Development pursuant to §36-98.3 of the Code of Virginia provided the board (i) provides a Notice of Intended Regulatory Action in conformance with the provisions of §2.2-4007.01, (ii) publishes the proposed regulation and provides an opportunity for oral and written comments as provided in §2.2-4007.03, and (iii) conducts at least one public hearing as provided in §§2.2-4009 and 36-100 prior to the publishing of the proposed regulations.

Title of Regulation: 13VAC5-31. Virginia Amusement Device Regulations (amending 13VAC5-31-20 through 13VAC5-31-50, 13VAC5-31-200, 13VAC5-31-210, adding 13VAC5-31-75, 13VAC5-31-85, 13VAC5-31-215 through 13VAC5-31-270; repealing 13VAC5-31-70 through 13VAC5-31-170).

Statutory Authority: § 36-98.3 of the Code of Virginia .

Effective Date: May 1, 2008.

Agency Contact: Steve Calhoun, Regulatory Coordinator, Department of Housing and Community Development, 501 North Second Street, Richmond, VA 23219, telephone 804-371-7015, FAX 804-371-7090, or email steve.calhoun@dhcd.virginia.gov.

Summary:

The amendments (i) incorporate the newest editions of the nationally recognized standards into the regulations, (ii) add a new standard developed specifically for bumper boats, (iii) add minimum continuing education requirements for amusement device inspectors certified by the Board of Housing and Community Development, (iv) clarify that reporting of accidents involving serious injury or death is only necessary when the situation involves patrons of a ride, (v) clarify exemptions from the regulations to include new language for water slides used in community club swimming pools, (vi) combine the owner and operator responsibilities with the local building department responsibilities to provide a more logical arrangement of the requirements without any substantive changes, (vii) change the liability insurance requirements based on standard industry practice and standardize wording of the requirements, (viii) add a requirement that the local building department personnel verify that a private inspector being utilized to inspect amusement devices is properly certified under the board’s amusement device inspector certification program, (ix) permit small inflatable amusement devices to be set up and operated without a permit or inspection provided a valid inspection sticker is still on the device; (x) allow for rock climbing walls that have a valid certification of inspection to be moved and set up at a different location provided the certificate of inspection was issued within the past 90 days and provide that wire ropes used with a rock climbing wall must not expire during the 90-day permit timeframe, and (xi) move the bungee jumping requirements to the end of the regulation without any substantive changes.

Summary of Public Comments and Agency's Response: A summary of comments made by the public and the agency's response may be obtained from the promulgating agency or viewed at the office of the Registrar of Regulations.

13VAC5-31-20. Definitions.

A. The following words and terms when used in this chapter shall have the following meanings unless the context clearly indicates otherwise:

"Amusement device" means (i) a device or structure open to the public by which persons are conveyed or moved in an unusual manner for diversion and (ii) passenger tramways.

"Bungee cord" means the elastic rope to which the jumper is attached which lengthens and shortens to produce a bouncing action.

"Carabineer" means a shaped metal device with a gate used to connect sections of a bungee cord, jump rigging, equipment, or safety gear.

"DHCD" means the Virginia Department of Housing and Community Development.

"Gravity ride" means a ride that is installed on an inclined surface, which depends on gravity for its operation to convey a passenger from the top of the incline to the bottom, and which conveys a passenger in or on a carrier tube, bag, bathing suit, or clothes.

"Ground operator" means a person who assists the jump master to prepare a jumper for jumping.

"Harness" means an assembly to be worn by a bungee jumper to be attached to a bungee cord. It is designed to prevent the wearer from becoming detached from the bungee system.

"Jump master" means a person who has responsibility for the bungee jumper and who takes the jumper through the final stages to the actual jump.

"Jump zone" means the space bounded by the maximum designed movements of the bungee jumper.

"Jumper" means the person who departs from a height attached to a bungee system.

"Landing area" means the surface area of ground or water directly under the jump zone, the area where the lowering device moves the bungee jumper to be landed away from the jump space and the area covered by the movement of the lowering device.

"Local building department" means the agency or agencies of the governing body of any city, county or town in this Commonwealth charged with the enforcement of the USBC.

"Operating manual" means the document that contains the procedures and forms for the operation of bungee jumping equipment and activity at a site.

"Passenger tramway" means a device used to transport passengers uphill, and suspended in the air by the use of steel cables, chains or belts, or ropes, and usually supported by trestles or towers with one or more spans.

"Platform" means the equipment attached to the structure from which the bungee jumper departs.

"Private inspector" means a person performing inspections who is independent of the company, individual or organization owning, operating or having any vested interest in an amusement device being inspected.

"Ultimate tensile strength" means the greatest amount of load applied to a bungee cord prior to failure.

"USBC" means the Virginia Uniform Statewide Building Code (13VAC5-63).

B. Words and terms used in this chapter which are defined in the USBC shall have the meaning ascribed to them in that regulation unless the context clearly indicates otherwise.

C. Words and terms used in this chapter which are defined in the standards incorporated by reference in this chapter shall have the meaning ascribed to them in those standards unless the context clearly indicates otherwise.

13VAC5-31-30. Exemptions.

The following equipment or devices shall not be considered amusement devices subject to this chapter:

1. Nonmechanized playground or recreational equipment such as swing sets, sliding boards, climbing bars, jungle gyms, skateboard ramps and similar equipment where no admission fee is charged for its use or for admittance to areas where the equipment is located and three or less passenger, coin-operated ;

2. Coin-operated rides shall not be amusement devices subject to this chapter designed to accommodate three or less passengers; and

3. Water slides or similar equipment used in community association, community club or community organization swimming pools.

13VAC5-31-40. Incorporated standards.

A. The following standards are hereby incorporated by reference for use as part of this chapter:

1. American National Standards Institute (ANSI) Standard No. B77.1-1999 B77.1-2006 for the regulation of passenger tramways; and

2. American Society for Testing and Materials (ASTM) Standard Nos. F698-94 (2000) (Reapproved 2000), F747-97 F747-06, F770-93 (2000) F770-06a, F846-92 (2003) (Reapproved 2003), F853-04 F853-05, F893-04 F893-05a, F1159-03a, F1193-04 F1193-06, F1305-94 (2002) (Reapproved 2002), F1950-99, F1957-99 (Reapproved 2004), F2007-00 F2007-06, F2137-01 F2137-04, F2291-04 and F2374-04 F2291-06a, [ F2374-06 and F2374-07a ] F2376-06 [ and F2460-06 ] for the regulation of amusement devices.

The standards referenced above may be procured from:

|  | ANSI 25 W 43rd Street New York, NY 10036 | ASTM 100 Barr Harbor Dr. West Conshohocken, PA 19428-2959 |
| --- | --- | --- |

B. The provisions of this chapter govern where they are in conflict with any provisions of the standards incorporated by reference in this chapter.

C. The following requirements supplement the provisions of the ASTM standards incorporated by reference in this chapter:

1. The operator of an amusement device shall be at least 16 years of age, except when the person is under the supervision of a parent or guardian and engaged in activities determined not to be hazardous by the Commissioner of the Virginia Department of Labor and Industry;

2. The amusement device shall be attended by an operator at all times during operation except that (i) one operator is permitted to operate two or more amusement devices provided they are within the sight of the operator and operated by a common control panel or station and (ii) one operator is permitted to operate two kiddie rides with separate controls provided the distance between controls is no more than 35 feet and the controls are equipped with a positive pressure switch; and

3. The operator of an amusement device shall not be (i) under the influence of any drugs which may affect the operator's judgment or ability to assure the safety of the public or (ii) under the influence of alcohol.

D. Where an amusement device was manufactured under previous editions of the standards incorporated by reference in this chapter, the previous editions shall apply to the extent that they are different from the current standards.

[ 13VAC5-31-50. Certification of amusement device inspectors.

A. Any person, including local building department personnel, inspecting an amusement device relative to a certificate of inspection shall possess a valid certificate of competence as an amusement device inspector from the Virginia Board of Housing and Community Development.

B. Local building department personnel enforcing this chapter and private inspectors shall attend 16 hours every two years of continuing education and periodic training courses as designated and approved or required by DHCD. Additional continuing education hours shall not be required if more than one certificate is held. ]

Part II 
Owner or Operator Responsibilities Enforcement, Permits and Certificates of Inspection

13VAC5-31-70. Inspections. (Repealed.)

The owner or operator of an amusement device shall be permitted to engage a private inspector to provide the necessary inspections for obtaining a certificate of inspection for an amusement device. If a private inspector is to be used, the owner or operator shall notify the responsible local building department as soon as practical. If a private inspector is not to be used, the owner or operator shall give reasonable notice to the responsible local building department when an inspection for issuing a certificate of inspection is sought. The owner or operator may designate the specific day for the inspection to take place provided it is during the local building department's normal work week.

13VAC5-31-75. Local building department.

A. In accordance with §§36-98.3 and 36-105 of the Code of Virginia, the local building department shall be responsible for the enforcement of this chapter and may charge fees for such enforcement activity. The total amount charged for any one permit to operate an amusement device or devices or the renewal of such permit shall not exceed the following, except that when a private inspector is used, the fees shall be reduced by 50%:

1. $25 for each kiddie ride covered by the permit;

2. $35 for each circular ride or flat-ride less than 20 feet in height covered by the permit;

3. $55 for each spectacular ride covered by the permit that cannot be inspected as a circular ride or flat-ride in subdivision 2 of this subsection due to complexity or height; and

4. $150 for each coaster covered by the permit that exceeds 30 feet in height.

B. Notwithstanding the provisions of subsection A of this section, when an amusement device is constructed in whole or in part at a site for permanent operation at that site and is not intended to be disassembled and moved to another site, then the local building department may utilize permit and inspection fees established pursuant to the USBC to defray the cost of enforcement. This authorization does not apply to an amusement device that is only being reassembled, undergoing a major modification at a site or being moved to a site for operation.

C. A permit application shall be made to the local building department at least five days before the date in which the applicant intends to operate an amusement device. The application shall include the name of the owner, operator or other person assuming responsibility for the device or devices, a general description of the device or devices including any serial or identification numbers available, the location of the property on which the device or devices will be operated and the length of time of operation. The permit application shall indicate whether a private inspector will be utilized. If a private inspector is not utilized, the applicant shall give reasonable notice when an inspection is sought and may stipulate the day such inspection is requested provided it is during the normal operating hours of the local building department. In addition to the information required on the permit application, the applicant shall provide proof of liability insurance of an amount not less than $100,000 per person and $1,000,000 in the aggregate for each amusement device insuring the owner or operator against liability for injury suffered by persons riding the amusement device or by persons in, on, under or near the amusement device; or proof of equivalent financial responsibility. The local building department shall be notified of any change in the liability insurance or financial responsibility during the period covered by the permit.

D. Notwithstanding the provisions of subsection C of this section, a permit application is not required for a kiddie ride in which the passenger height is 54 inches or less, the design capacity is for 12 passengers or less and that can be assembled in two hours or less, provided the kiddie ride has an unexpired certificate of inspection issued by any local building department in this Commonwealth. In such cases, the local building department shall be notified prior to the operation of the kiddie ride and the information required on a permit application as listed in subsection C of this section shall be provided to the local building department.

E. Local building department personnel shall examine the permit application within five days and issue the permit if all requirements are met. A certificate of inspection for each amusement device shall be issued when the device has been found to comply with this chapter by a private inspector or by an inspector from the local building department. It shall be the responsibility of the local building department to verify that the private inspector possesses a valid certificate of competence as an amusement device inspector from the Virginia Board of Housing and Community Development. In addition, local building department personnel shall be responsible for assuring that the certificate of inspection is posted or affixed on or in the vicinity of the device in a location visible to the public. Permits shall indicate the length of time the device or devices will be operated at the site, clearly identify the device or devices to which it applies and the date of expiration of the permit. Permits shall not be valid for longer than one year.

F. In addition to obtaining a certificate of inspection in conjunction with a permit application, a new certificate of inspection shall also be obtained prior to the operation of an amusement device following a major modification, prior to each seasonal operation of a device and prior to resuming the operation of a device following an order from a local building department to cease operation. This requirement shall not apply to kiddie rides meeting the conditions outlined in subsection D of this section.

G. For amusement devices manufactured prior to 1978, the owner or operator shall have the information required by §§2.1 through 2.6 of ASTM F628 available at the time of inspection. In addition, the operator of any amusement device shall be responsible for obtaining all manufacturer’s notifications, service bulletins and safety alerts issued pursuant to ASTM F853 and the operator shall comply with all recommendations and requirements set out in those documents. A copy of all such documents shall be made available during an inspection.

H. In the enforcement of this chapter, local building department personnel shall have authority to conduct inspections at any time an amusement device would normally be open for operation or at any other time if permission is granted by the owner or operator, to issue an order to temporarily cease operation of an amusement device upon the determination that the device may be unsafe or may otherwise endanger the public and to accept and approve or deny requests for modifications of the rules of this chapter in accordance with the modification provisions of the USBC.

13VAC5-31-80. Owner or operator responsibilities. (Repealed.)

In addition to other applicable requirements of this chapter, the owner or operator of an amusement device or devices shall be responsible for the following:

1. Submitting a permit application to the responsible local building department at least five days before a permit to operate, or renewal of a permit to operate, is sought. The permit application shall include (i) the name of the owner, operator or other person assuming responsibility; (ii) a general description of the device or devices to be permitted; (iii) any relevant serial or identification numbers; (iv) the location of the property on which the device or devices will be operated; and (v) the length of time the device or devices will be operating at the site;

2. Submitting an application for modification of any provision of this chapter when a modification is sought due to practical difficulties involved in complying with this chapter. The application for modification shall include documentation outlining the practical difficulties and method proposed to protect the public health, safety and welfare;

3. Submitting to the responsible local building department before or with the application for a permit to operate, or renewal of a permit to operate, proof of liability insurance of an amount not less than $500,000 per occurrence or proof of equivalent financial responsibility and notifying the responsible local building department promptly of any change in the liability insurance or financial responsibility status during the period of operation to be, or which is, authorized by the permit;

4. Obtaining a permit to operate from the responsible local building department prior to operation or obtaining the renewal of a permit to operate when necessary prior to continued operation. Notwithstanding the above, a permit for a kiddie ride in which (i) the passenger height is limited to 54 inches or less; (ii) the design capacity is 12 passengers or less; and (iii) the assembly time is two hours or less need not be obtained if the device has an unexpired certificate of inspection issued by a local building department in this Commonwealth, regardless of whether the ride has been disassembled or moved to a new site. However, in such cases, the responsible local building department shall be notified prior to operation and such notification shall include the information required on a permit application as stipulated in subdivision 1 of this subsection;

5. Making available to the inspector at the time of inspection for a certificate of inspection the information listed in §§2.1 through 2.6 of ASTM F698 when an amusement device was manufactured prior to 1978;

6. The operator of an amusement device shall review promptly upon receipt all manufacturer's notifications, service bulletins and safety alerts relating to such amusement device issued pursuant to ASTM F853. The operator of the amusement device shall comply with all recommendations and requirements set out in such documents as required by ASTM F853. A copy of each such document shall be retained by the operator. Whenever such amusement device is inspected pursuant to these regulations, the operator of the amusement device shall present each such document to the inspector. It is the responsibility of the operator of an amusement device to maintain contact with the manufacturer to insure that the manufacturer knows which devices are operated by the operator and to insure that the manufacturer has the current address of the operator.

7. Obtaining a certificate of inspection from the responsible local building department (i) prior to initial operation; (ii) prior to operation following a major modification; (iii) prior to each seasonal operation; (iv) at least once a year if operated more than seasonally; and (v) prior to resuming operation following an order from the local building department to cease operation. Notwithstanding the above, a certificate of inspection for a kiddie ride in which (i) the passenger height is limited to 54 inches or less; (ii) the design capacity is 12 passengers or less; and (iii) the assembly time is two hours or less need not be obtained if the device has an unexpired certificate of inspection issued by a local building department in this Commonwealth, regardless of whether the ride has been disassembled or moved to a new site; and

8. Ceasing operation upon receipt of a temporary order to cease operation issued by the responsible local building department.

13VAC5-31-85. Accidents involving serious injury or death.

A. If an accident involving [ the ] serious injury or death [ of a patron ] occurs, the operation of an amusement device shall cease and the local building department shall be notified as soon as practicable, but in no case later than during the next working day. The operation of the device shall not resume until inspected by a private inspector or an inspector from the local building department, except where the owner or operator determines the cause was not related to malfunction or improper operation of the amusement device.

B. The owner or operator shall conduct an investigation of the accident including, at a minimum, an examination of the accident scene and interviews of any witnesses or persons involved in the accident. An accident investigation report shall be compiled which, at a minimum, shall contain a summary of the investigation and a description of the device involved, including its serial number and date of manufacture, if available. The report shall be submitted to the local building department within 24 hours of the accident except that if the local building department is closed during that period, then the report shall be submitted with four hours of the reopening of the department

C. Local building department personnel are authorized to investigate the accident and to issue an order to cease operation when warranted and to specify the conditions under which the device may resume operation. The amusement device shall be inspected prior to resuming operation either by an inspector [ form from ] the local building department or by a private inspector and found to comply with this chapter.

13VAC5-31-90. Accidents. (Repealed.)

In the event of an accident involving serious injury or death the owner or operator shall:

1. Contact the responsible local building department as soon as practical, but not later than the next work day;

2. Cease operation until the responsible local building department approves resuming operation, except that approval from the responsible local building department for resuming operation is not required if the investigation required by subdivision 3 of this section provides reasonable evidence that the serious injury or death was not related to malfunction or improper operation;

3. Conduct an investigation to include (i) an examination of the accident scene; (ii) an interview of any witnesses or persons involved in the accident; and (iii) compiling a written report. The report shall contain a summary of the investigation and a description of the device involved, including the name of the manufacturer, the serial number and the date of manufacture, if available; and

4. Submit the investigation report to the responsible local building department within 24 hours after the time of the accident except that if its office is closed during the 24-hour period, the report shall be submitted within four hours after the office reopens.

Part III 
Enforcement

13VAC5-31-100. Local building department. (Repealed.)

The local building department's official or representative shall be permitted to do the following relative to an amusement device or devices intended to be, or being, operated at a site within their jurisdiction:

1. Collect fees for a permit to operate, renewal of a permit to operate and inspections conducted by staff to issue a certificate of inspection. The total for fees associated with one permit to operate and any associated inspections or one renewal of a permit to operate and any associated inspections shall not exceed the following:

a. $25 for each kiddie ride under the permit;

b. $35 for each circular ride or flat-ride less than 20 feet in height under the permit;

c. $55 for each spectacular ride under the permit that cannot be inspected as a circular ride or flat-ride in subdivision 1 (b) of this section due to complexity or height; and

d. $150 for coasters that exceed 30 feet in height.

Notwithstanding the above, the fee for each amusement device under the permit shall be reduced by 50% when the inspection for obtaining a certificate of inspection for that device is conducted by a private inspector;

2. In addition to the above, require permits and charge fees as appropriate under the USBC for amusement devices which are being initially constructed in whole or in part at a site within the jurisdiction for intended operation at that site. This authorization does not apply to an amusement device which is only being reassembled or undergoing a major modification at a site or being moved to a site for operation;

3. Approve modifications of this chapter upon determination that the public health, safety and welfare are assured;

4. Conduct an inspection at any time when the device would normally be open for operation, or at any other time if permission is granted by the owner or operator, for compliance with this chapter; and

5. Issue an order to temporarily cease the operation of an amusement device upon determination that it may be unsafe or otherwise endanger the public. The temporary order shall remain in effect until a new certificate of inspection is issued.

13VAC5-31-110. Enforcement. (Repealed.)

The local building department's official or representative shall enforce the provisions of this chapter as provided herein and as interpreted by the State Building Code Technical Review Board (TRB).

The local building department's official or representative shall be responsible for the following relative to an amusement device or devices intended to be, or being, operated at a site within their jurisdiction:

1. Approving or rejecting any application made for a permit to operate, or renewal of a permit to operate, within five days after submittal and issuing or renewing the permit when appropriate. The permit shall be issued or renewed for the length of time the device or devices will be operating at the site, except that if the length of time exceeds one year, the permit or renewal shall expire after one year. The permit to operate or renewed permit to operate shall state (i) the estimated length of time that the device or devices will be operated at the site; (ii) the name of, or otherwise identify, the device or devices covered by the permit; and (iii) the date when the permit expires;

2. When a certificate of inspection is sought by the owner or operator, conducting an inspection to assure compliance with this chapter unless the owner or operator is providing an approved private inspector. If the owner or operator has given reasonable notice that a certificate of inspection is sought and designated a specific day for the inspection, then the inspection shall be conducted on that day;

3. Accepting a written report of inspection from an approved private inspector;

4. When in receipt of a written report of inspection from an approved private inspector or after assuring compliance with this chapter through inspection, completing a certificate of inspection distributed by DHCD and causing the certificate to be posted or affixed on or in the vicinity of the device in a location visible to the public;

5. Accepting an existing certificate of inspection for a kiddie ride in which (i) the passenger height is limited to 54 inches or less; (ii) the capacity is 12 passengers or less; and (iii) the assembly time is two hours or less, provided the existing certificate of inspection for the ride was issued by a local building department in this Commonwealth less than one year prior to the date for which a certificate of inspection is sought, regardless of whether disassembly has occurred. Notwithstanding the above, if the kiddie ride is determined to be in violation of this chapter, the existing certificate of inspection shall not be valid; and

6. Issuing an order to cease operation upon discovery or notification that an accident involving the device has caused serious injury or death, except where the owner or operator has determined that the serious injury or death was not related to malfunction or improper operation of the device. Whether or not the order to cease operation has been issued, the official or representative shall conduct an inspection, or accept an inspection report from an approved private inspector, to assure the device complies with this chapter and is safe for operation.

Part IV

Bungee Jumping

13VAC5-31-120. General requirements. (Repealed.)

A. The provisions of this part are specific to bungee jumping and are in addition to other applicable provisions of this chapter.

B. Bungee jumping operations which are open to the public shall be permitted from structures designed for use as part of the bungee jumping operation. Bungee jumping from other types of structures, cranes or derricks is not permitted for public participation.

C. Bungee jumping activities which involve double jumping, sandbagging, catapulting or stunt jumping shall not be permitted to be open for public participation.

13VAC5-31-130. Bungee cords. (Repealed.)

A. Bungee cords shall be tested by an approved testing agency or by an engineer licensed in Virginia. The following criteria shall be met:

1. Each lot of bungee cords shall have a minimum of 10%, but not less than one of the cords tested to determine the lowest ultimate tensile strength of the cords tested. A load versus elongation curve based on the test result shall be provided with each lot of bungee cords; and

2. The manufacturer shall specify the maximum number of jumps for which each cord or cord type is designed and the criteria for use of the cord.

B. Bungee cords shall be retired when the cords (i) exhibit deterioration or damage; (ii) do not react according to specifications; or (iii) have reached the maximum usage expressed in number of jumps as specified by the manufacturer. Bungee cords retired from use shall be destroyed immediately by cutting the cord into five-foot lengths.

13VAC5-31-140. Jump hardware. (Repealed.)

Jump harnesses shall be either full body-designed, which includes a waist harness worn in conjunction with a chest harness, or ankle-designed with a link to a waist harness. All jump harnesses, carabineers, cables and other hardware shall be designed and manufactured for the purpose or designed or analyzed by an engineer licensed in Virginia and shall be used and maintained in accordance with the manufacturer's or engineer's instructions.

13VAC5-31-150. Structure requirements. (Repealed.)

Structures constructed on site for bungee jumping activities shall be designed by an engineer licensed in Virginia. Structures manufactured for bungee jumping activities shall be analyzed by an engineer licensed in Virginia and assembled and supported in accordance with the manufacturer's instructions.

13VAC5-31-160. Operational and site requirements. (Repealed.)

A. Operators shall follow the criteria provided by the manufacturer for the use of bungee cords. A record of the number of jumps with each cord shall be maintained. All cords shall be inspected daily for wear, slippage, or other abnormalities unless the manufacturer specifies more frequent inspections.

B. The jump master or site manager shall be responsible for determining the appropriate use of all bungee cords in relation to the weight of the jumper and height of the platform. Bungee cords shall be attached to the structure at all times when in the connection area.

C. All harnesses shall be inspected prior to harnessing a jumper and shall be removed from service when they exhibit signs of excessive wear or damage. All carabineers shall be inspected daily and shall be removed from service when they exhibit signs of excessive wear or damage or fail to function as designed. The anchors shall be inspected daily and shall be replaced if showing signs of excessive wear.

D. A secondary retrieval system shall be provided in all operations. A locking mechanism on the line shall be used to stop and hold the jumper in place after being pulled back to the jump platform in a retrieval system. A dead man's switch or locking mechanism that will stop the lowering action shall be used in a friction lowering system.

E. The jump zone, preparation area and landing/recovery area shall be identified and maintained during bungee jumping activities. The landing/recovery area shall be accessible to emergency vehicles. Communication shall be maintained between all personnel involved with the jump.

F. An air bag, a minimum of 10 feet by 10 feet, shall be used. The air bag shall be rated for the maximum free fall height possible from the platform during operation. The air bag shall be located immediately below the jump space. The landing area shall be free of spectators and debris at all times and shall be free of any equipment or personnel when a jumper is being prepared on the jump platform and until the bungee cord is at its static extended state. A place to sit and recover shall be provided adjacent to, but outside, the landing area where the jumper shall be allowed to recover.

G. Where the jump space or landing area, or both, is over sea, lake, river, or harbor waters, the following shall apply:

1. The landing water area shall be at least nine feet deep and a minimum of 10 feet by 10 feet or have a minimum of 15 feet in diameter if circular;

2. The jump space and landing area shall be free of other vessels, floating and submerged objects and buoys. A sign of approved size which reads "Bungee Jumping! Keep Clear" shall be fixed to buoys on four sides of the landing area;

3. The landing vessel shall be readily available for the duration of the landing procedures;

4. The landing vessel shall have a landing pad size of at least five feet by five feet within and lower than the sides of the vessel;

5. A landing vessel shall be available that can be maneuvered in the range of water conditions expected and will enable staff to pick up a jumper; and

6. One person may operate the landing vessel where the vessel is positioned without the use of power. A separate person shall operate the vessel where power is required to maneuver into or hold the landing position.

H. Where the landing area is part of a swimming pool or the landing area is specifically constructed for bungee jumping, the following shall apply:

1. Rescue equipment shall be available, such as a life ring or safety pole;

2. The jump space and landing area shall be fenced to exclude the public; and

3. Only the operators of the bungee jump and jumper shall be within the jump zone and landing areas.

I. Storage shall be provided to protect equipment from physical, chemical and ultra-violet radiation damage. The storage shall be provided for any current, replacement and emergency equipment and organized for ready access and shall be secure against unauthorized entry.

13VAC5-31-170. Management and personnel responsibilities. (Repealed.)

A. All bungee jumping activities shall have a minimum of one site manager, one jump master and one ground operator to be present at all times during operation of the bungee jump.

B. The site manager is responsible for the following:

1. Controlling the entire operation;

2. Site equipment and procedures;

3. Determining whether it is safe to jump;

4. Selection of, and any training of personnel;

5. Emergency procedures; and

6. Maintaining records.

C. A jump master shall be located at each jump platform and shall have thorough knowledge of, and is responsible for, the following:

1. Overseeing the processing of jumpers, selection of the bungee cord, adjustment of the rigging, final check of jumper's preparation, and countdown for and observation of the jump;

2. Verifying that the cord is attached to the structure at all times when the jumper is in the jump area;

3. Rescue and emergency procedures; and

4. Ensuring that the number of jumps undertaken in a given period of time will allow all personnel to safely carry out their responsibilities.

D. The ground operator shall have knowledge of all equipment used and of jump procedures and shall have the following responsibilities:

1. Ensuring that the jumper is qualified to jump;

2. Assisting the jump master to prepare the jumper and attach the jumper to the harness and rigging;

3. Assisting the jumper to the recovery area; and

4. Maintaining a clear view of the landing area.

E. Each site shall have an operating manual which shall include the following:

1. Site plan, job descriptions (including procedures), inspections and maintenance requirements of equipment including rigging, hardware, bungee cords, harnesses, and lifelines; and

2. An emergency rescue plan.

F. The daily operating procedures shall be conducted in accordance with ASTM F770-93.

G. The qualification and preparation of jumpers shall include obtaining any pertinent medical information, jumper weight and a briefing of jumping procedures and safety instructions.

Part V III 
Gravity Rides

Part VI IV 
Concession Go-Karts

Part VII V 
Inflatable Amusement Devices

[ 13VAC5-31-200. General requirements.

In addition to other applicable requirements of this chapter, inflatable amusement devices shall be operated, maintained and inspected in accordance with ASTM F2374.

Notwithstanding any requirements of this chapter to the contrary, a permit to operate an inflatable amusement device that is less than 150 square feet and in which the height of the patron containment area is less than 10 feet need not be obtained if the device has an unexpired certificate of inspection issued by a local building department in this Commonwealth, regardless of whether the device has been disassembled or moved to a new site. ]

Part VIII VI 
Artificial Climbing Walls

13VAC5-31-210. General requirements.

In addition to other applicable requirements of this chapter, artificial climbing walls shall be operated, maintained and inspected in accordance with ASTM F1159.

Notwithstanding any requirements of this chapter to the contrary, an artificial climbing wall may be moved, setup and operated without obtaining a permit provided the wall has a valid certificate of inspection issued by a local building department within the prior 90 days [ and the expiration date of the wire ropes used with the device does not expire within that 90-day period ].

[ Part VII

Bumper Boats

13VAC5-31-215. General requirements.

In addition to other applicable requirements of this chapter, bumper boats shall be operated, maintained and inspected in accordance with ASTM F2460. ]

Part [ VII VIII ] 
Bungee Jumping

13VAC5-31-220. General requirements.

A. The provisions of this part are specific to bungee jumping and are in addition to other applicable provisions of this chapter.

B. Bungee jumping operations that are open to the public shall be permitted from structures designed for use as part of the bungee jumping operation. Bungee jumping from other types of structures, cranes or derricks is not permitted for public participation.

C. Bungee jumping activities that involve double jumping, sandbagging, catapulting or stunt jumping shall not be permitted to be open for public participation.

13VAC5-31-230. Bungee cords.

A. Bungee cords shall be tested by an approved testing agency or by an engineer licensed in Virginia. The following criteria shall be met:

1. Each lot of bungee cords shall have a minimum of 10%, but not less than one of the cords tested to determine the lowest ultimate tensile strength of the cords tested. A load versus elongation curve based on the test result shall be provided with each lot of bungee cords; and

2. The manufacturer shall specify the maximum number of jumps for which each cord or cord type is designed and the criteria for use of the cord.

B. Bungee cords shall be retired when the cords (i) exhibit deterioration or damage; (ii) do not react according to specifications; or (iii) have reached the maximum usage expressed in number of jumps as specified by the manufacturer. Bungee cords retired from use shall be destroyed immediately by cutting the cord into five-foot lengths.

13VAC5-31-240. Jump hardware.

Jump harnesses shall be either full body-designed, which includes a waist harness worn in conjunction with a chest harness, or ankle-designed with a link to a waist harness. All jump harnesses, carabineers, cables and other hardware shall be designed and manufactured for the purpose or designed or analyzed by an engineer licensed in Virginia and shall be used and maintained in accordance with the manufacturer's or engineer's instructions.

13VAC5-31-250. Structure requirements.

Structures constructed on site for bungee jumping activities shall be designed by an engineer licensed in Virginia. Structures manufactured for bungee jumping activities shall be analyzed by an engineer licensed in Virginia and assembled and supported in accordance with the manufacturer's instructions.

13VAC5-31-260. Operational and site requirements.

A. Operators shall follow the criteria provided by the manufacturer for the use of bungee cords. A record of the number of jumps with each cord shall be maintained. All cords shall be inspected daily for wear, slippage, or other abnormalities unless the manufacturer specifies more frequent inspections.

B. The jump master or site manager shall be responsible for determining the appropriate use of all bungee cords in relation to the weight of the jumper and height of the platform. Bungee cords shall be attached to the structure at all times when in the connection area.

C. All harnesses shall be inspected prior to harnessing a jumper and shall be removed from service when they exhibit signs of excessive wear or damage. All carabineers shall be inspected daily and shall be removed from service when they exhibit signs of excessive wear or damage or fail to function as designed. The anchors shall be inspected daily and shall be replaced if showing signs of excessive wear.

D. A secondary retrieval system shall be provided in all operations. A locking mechanism on the line shall be used to stop and hold the jumper in place after being pulled back to the jump platform in a retrieval system. A dead man's switch or locking mechanism that will stop the lowering action shall be used in a friction lowering system.

E. The jump zone, preparation area and landing/recovery area shall be identified and maintained during bungee jumping activities. The landing/recovery area shall be accessible to emergency vehicles. Communication shall be maintained between all personnel involved with the jump.

F. An air bag, a minimum of 10 feet by 10 feet, shall be used. The air bag shall be rated for the maximum free fall height possible from the platform during operation. The air bag shall be located immediately below the jump space. The landing area shall be free of spectators and debris at all times and shall be free of any equipment or personnel when a jumper is being prepared on the jump platform and until the bungee cord is at its static extended state. A place to sit and recover shall be provided adjacent to, but outside, the landing area where the jumper shall be allowed to recover.

G. Where the jump space or landing area, or both, is over sea, lake, river, or harbor waters, the following shall apply:

1. The landing water area shall be at least nine feet deep and a minimum of 10 feet by 10 feet or have a minimum of 15 feet in diameter if circular;

2. The jump space and landing area shall be free of other vessels, floating and submerged objects and buoys. A sign of approved size that reads "Bungee Jumping! Keep Clear" shall be fixed to buoys on four sides of the landing area;

3. The landing vessel shall be readily available for the duration of the landing procedures;

4. The landing vessel shall have a landing pad size of at least five feet by five feet within and lower than the sides of the vessel;

5. A landing vessel shall be available that can be maneuvered in the range of water conditions expected and will enable staff to pick up a jumper; and

6. One person may operate the landing vessel where the vessel is positioned without the use of power. A separate person shall operate the vessel where power is required to maneuver into or hold the landing position.

H. Where the landing area is part of a swimming pool or the landing area is specifically constructed for bungee jumping, the following shall apply:

1. Rescue equipment shall be available, such as a life ring or safety pole;

2. The jump space and landing area shall be fenced to exclude the public; and

3. Only the operators of the bungee jump and jumper shall be within the jump zone and landing areas.

I. Storage shall be provided to protect equipment from physical, chemical and ultra-violet radiation damage. The storage shall be provided for any current, replacement and emergency equipment and organized for ready access and shall be secure against unauthorized entry.

13VAC5-31-270. Management and personnel responsibilities.

A. All bungee jumping activities shall have a minimum of one site manager, one jump master and one ground operator to be present at all times during operation of the bungee jump.

B. The site manager is responsible for the following:

1. Controlling the entire operation;

2. Site equipment and procedures;

3. Determining whether it is safe to jump;

4. Selection of, and any training of personnel;

5. Emergency procedures; and

6. Maintaining records.

C. A jump master shall be located at each jump platform and shall have thorough knowledge of, and is responsible for, the following:

1. Overseeing the processing of jumpers, selection of the bungee cord, adjustment of the rigging, final check of jumper's preparation, and countdown for and observation of the jump;

2. Verifying that the cord is attached to the structure at all times when the jumper is in the jump area;

3. Rescue and emergency procedures; and

4. Ensuring that the number of jumps undertaken in a given period of time will allow all personnel to safely carry out their responsibilities.

D. The ground operator shall have knowledge of all equipment used and of jump procedures and shall have the following responsibilities:

1. Ensuring that the jumper is qualified to jump;

2. Assisting the jump master to prepare the jumper and attach the jumper to the harness and rigging;

3. Assisting the jumper to the recovery area; and

4. Maintaining a clear view of the landing area.

E. Each site shall have an operating manual that shall include the following:

1. Site plan, job descriptions (including procedures), inspections and maintenance requirements of equipment including rigging, hardware, bungee cords, harnesses, and lifelines; and

2. An emergency rescue plan.

F. The daily operating procedures shall be conducted in accordance with ASTM F770.

G. The qualification and preparation of jumpers shall include obtaining any pertinent medical information, jumper weight and a briefing of jumping procedures and safety instructions.

DOCUMENTS INCORPORATED BY REFERENCE.

ASTM International Standards on Amusement Rides and Devices, 7th Edition, 2004.

F 698 – 94 (Reapproved 2000), Standard Specification for Physical Information to be Provided for Amusement Rides and Devices, ASTM International, West Conshohocken, PA 19428.

F 747 – 06, Standard Terminology Relating to Amusement Rides and Devices, ASTM International, West Conshohocken, PA 19428.

F 770 – 06a, Standard Practice for Ownership and Operation of Amusement Rides and Devices, ASTM International, West Conshohocken, PA 19428.

F 846 – 92 (Reapproved 2003), Standard Guide for Testing Performance of Amusement Rides and Devices, ASTM International, West Conshohocken , PA 19428.

F 853 – 05, Standard Practice for Maintenance Procedures for Amusement Rides and Devices, ASTM International, West Conshohocken, PA 19428.

F 893 – 05a, Standard Guide for Inspection of Amusement Rides and Devices, ASTM International, West Conshohocken, PA 19428.

F 1159 – 03a, Standard Practice for Design and Manufacture of Patron Directed, Artificial Climbing Walls, Dry Slide, Coin Operated and Purposeful Water Immersion Amusement Rides and Devices and Air-Supported Structures, ASTM International, West Conshohocken, PA 19428.

F 1193 – 06, Standard Practice for Quality, Manufacture, and Construction of Amusement Rides and Devices, ASTM International, West Conshohocken , PA 19428.

F 1305 – 94 (Reapproved 2002), Standard Guide for Classification of Amusement Rides and Device Related Injuries and Illnesses, ASTM International, West Conshohocken, PA 19428.

F 1950 – 99, Standard Specification for Physical Information to be Transferred With Used Amusement Rides and Devices, ASTM International, West Conshohocken, PA 19428.

F 1957 – 99 (Reapproved 2004), Standard Test Method for Composite Foam Hardness-Durometer Hardness, ASTM International, West Conshohocken , PA 19428.

F 2007 – 06, Standard Practice for Classification, Design, Manufacture, and Operation of Concession Go-Karts and Facilities, ASTM International, West Conshohocken , PA 19428.

F 2137 – 04, Standard Practice for Measuring the Dynamic Characteristics of Amusement Rides and Devices, ASTM International, West Conshohocken , PA 19428.

F 2291 – 06a, Standard Practice for Design of Amusement Rides and Devices, ASTM International, West Conshohocken, PA 19428.

[ F 2374 – 06 F 2374 – 07a ] , Standard Practice for Design, Manufacture, Operation, and Maintenance of Inflatable Amusement Devices, ASTM International, West Conshohocken, PA 19428.

F 2376 – 06, Standard Practice for Classification, Design, Manufacture, Construction, and Operation of Water Slide Systems, ASTM International, West Conshohocken, PA 19428.

[ F 2460 – 06, Standard Practice for Special Requirements for Bumper Boats, ASTM International, West Conshohocken, PA 19428. ]

VA.R. Doc. No. R07-123; Filed February 22, 2008, 3:05 p.m.