TITLE 9. ENVIRONMENT

STATE WATER CONTROL BOARD

Final Regulation

REGISTRAR'S NOTICE: The State Water Control Board is claiming an exemption from the Administrative Process Act in accordance with §2.2-4006 A 3 of the Code of Virginia, which excludes regulations that consist only of changes in style or form or corrections of technical errors. The State Water Control Board will receive, consider and respond to petitions by any interested person at any time with respect to reconsideration or revision.

Title of Regulation: 9VAC25-120. General Virginia Pollutant Discharge Elimination System (VPDES) Permit Regulation for Discharges From Petroleum Contaminated Sites, Groundwater Remediation and Hydrostatic Tests (amending 9VAC25-120-80).

Statutory Authority: §62.1-44.15 of the Code of Virginia; §402 of the Clean Water Act; 40 CFR Parts 122, 123 and 124.

Effective Date: June 11, 2008.

Agency Contact: Burt Tuxford, Department of Environmental Quality, 629 East Main Street, P.O. Box 1105, Richmond, VA 23218, telephone 804-698-4086, FAX 804-698-4032, or email brtuxford@deq.virginia.gov.

Background: This regulation was adopted by the Water Control Board on December 4, 2007.  Subsequent to the adoption, errors were found in 9VAC25-120-80 (General Permit) in the eighth Part I A (Effluent Limitations and Monitoring Requirements) tables, and in the Part II K 1(ii) (Signatory Requirements) section.  This regulatory action corrects the errors, which are as follows:

1. Part I A, Tables 1-8 - Method Corrections: EPA updated the 40 CFR Part 136 Test Procedures rule on March 12, 2007.  They also published the "Final Update IV" to the Third Edition of the manual, "Test Methods for Evaluating Solid Waste, Physical/Chemical Methods," EPA publication SW-846, on January 3, 2008.  These updates contain new and revised analytical methods for some of the methods specified in this regulation.  To conform to the federal methods changes, all references in these tables to "40 CFR Part 136 (1996)" are changed to "40 CFR Part 136 (2007)".  All references in these tables to "EPA SW 846 (1998)" are changed to "EPA SW 846 (2008)"

2. Part I A, Tables 1-8 - Specific Method Corrections: In the Part I A Tables 1-8, wherever the following methods appear, they are changed as follows:

EPA SW 846 method 9040B changed to 9040C

EPA SW 846 method 8015B changed to 8015C

EPA SW 846 method 8270C changed to 8270D

EPA SW 846 method 7421 changed to 7010

EPA Part 136 method 239.2 changed to "200.8 or 200.9"

3. Part II K 1 (ii) - Correction:  An old version of this language was in the permit.  The language for this subsection was changed in the VPDES Permit Regulation (9VAC25-31-110 A 1) several years ago based upon EPA's changes to the 40 CFR Part 122.22 language that were published by EPA on May 15, 2000.  The correct language for this subsection is: "(ii) the manager of one or more manufacturing, production, or operating facilities, provided the manager is authorized to make management decisions that govern the operation of the regulated facility including having the explicit or implicit duty of making major capital investment recommendations, and initiating and directing other comprehensive measures to assure long-term environmental compliance with environmental laws and regulations; the manager can ensure that the necessary systems are established or actions taken to gather complete and accurate information for permit application requirements; and where authority to sign documents has been assigned or delegated to the manager in accordance with corporate procedures;".

Summary:

The amendments correct errors found in the regulation. This includes updating references to reflect newer versions of the Code of Federal Regulations with regard to test methods for evaluating solid waste, and old language that had not been updated in the permit.

9VAC25-120-80. General permit.

Any owner whose request for coverage under this general permit is accepted by the board shall comply with the requirements of the general permit and be subject to all requirements of 9VAC25-31-170 B of the VPDES permit regulation. Not all pages of Part I A of the general permit will apply to every permittee. The determination of which pages apply will be based on the type of contamination at the individual site and the nature of the waters receiving the discharge. Part I B and all pages of Part II apply to all permittees.

General Permit No.: VAG83 
Effective Date: February 26, 2008 
Expiration Date: February 25, 2013

GENERAL VPDES PERMIT FOR DISCHARGES FROM PETROLEUM CONTAMINATED SITES, GROUNDWATER REMEDIATION, AND HYDROSTATIC TESTS

AUTHORIZATION TO DISCHARGE UNDER THE VIRGINIA POLLUTANT DISCHARGE ELIMINATION SYSTEM PERMIT PROGRAM AND THE VIRGINIA STATE WATER CONTROL LAW

In compliance with the provisions of the Clean Water Act, as amended, the State Water Control Law and regulations adopted pursuant thereto, the owner is authorized to discharge to surface waters at the locations identified in the accepted registration statement within the boundaries of the Commonwealth of Virginia, except to designated public water supplies or waters specifically named in other board regulations or policies which prohibit such discharges.

The authorized discharge shall be in accordance with this cover page, Part I - Effluent Limitations and Monitoring Requirements and Part II - Conditions Applicable to All VPDES Permits, as set forth herein.

If there is any conflict between the requirements of a Department of Environmental Quality approved cleanup plan and this permit, the requirements of this permit shall govern.

Part I

A. EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS.

1. GASOLINE CONTAMINATION -- FRESHWATER RECEIVING WATERS NOT LISTED AS PUBLIC WATER SUPPLIES.

During the period beginning with the permittee's coverage under this general permit and lasting until the permit's expiration date, the permittee is authorized to discharge to freshwater receiving waterbodies from outfall serial number XXXX. Samples taken in compliance with the monitoring requirements specified below shall be taken at the following location: outfall from the final treatment unit prior to mixing with any other waters.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS | DISCHARGE LIMITATIONS | MONITORING REQUIREMENTS |
| --- | --- | --- |
|  | Instantaneous Minimum | Instantaneous Maximum | Frequency | Sample Type |
| Flow (MGD) | NA | NL | 1/Month | Estimate |
| Benzene (μg/l)1 | NA | 50.0 | 1/Month | Grab* |
| Toluene (μg/l)1 | NA | 175.0 | 1/Month | Grab |
| Ethylbenzene (μg/l)1 | NA | 320.0 | 1/Month | Grab |
| Total Xylenes (μg/l)1 | NA | 33.0 | 1/Month | Grab |
| MTBE (methyl tert-butyl ether) (μg/l)1 | NA | 1,840.0 | 1/Month | Grab |
| pH (standard units) | 6.0 | 9.0 | 1/Month | Grab |
| Total Recoverable Lead (μg/l)2 | NA | e(1.273(ln hardness)) -3.259 | 1/Month | Grab |
| Hardness (mg/l CaCO3)2 | NL | NA | 1/Month | Grab |
| Ethylene Dibromide (μg/l)2 | NA | 5.3 | 1/Month | Grab |
| 1,2 Dichloroethane (μg/l)2 | NA | 990.0 | 1/Month | Grab |
| Ethanol (μg/l)3 | NA | 4100.0 | 1/Month | Grab |

NL = No limitation, monitoring required

NA = Not applicable

1Benzene, Toluene, Ethylbenzene, Total Xylenes and MTBE shall be analyzed according to a current and appropriate EPA Wastewater Method (40 CFR Part 136, 1996) (40 CFR Part 136, 2007) or EPA SW 846 Method 8021B (1998) (1996).

2Monitoring for this parameter is required only when contamination results from leaded fuel. Lead shall be analyzed according to a current and appropriate EPA Wastewater Method (40 CFR Part 136, 1996) (40 CFR Part 136, 2007) or EPA SW 846 method 9040B Method 9040C (2004). The minimum hardness concentration that will be used to determine the lead effluent limit is 25 mg/l. 1,2 dichloroethane and EDB shall be analyzed by a current and appropriate EPA SW 846 Method or EPA Wastewater Method from 40 CFR Part 136 (1996) (2007).

3Monitoring for ethanol is only required for discharges of water contaminated by gasoline containing greater than 10% ethanol. Ethanol shall be analyzed according to EPA SW 846 Method 8015B 8015C (2007) or EPA SW 846 Method 8260B (1996). Monitoring frequency shall be 1/month in the first year of permit coverage. If the first year results demonstrate full compliance with the effluent limitations, the permittee may request that the monitoring frequency for ethanol be reduced from monthly to 1/quarter. The written request shall be sent to the appropriate regional office for review. Upon written notification from the DEQ regional office, monitoring frequency shall be reduced to 1/quarter. Should the permittee be issued a warning letter related to violation of effluent limitations, a notice of violation, or be the subject of an active enforcement action, monitoring frequency for ethanol shall revert to 1/month, upon issuance of the letter or notice or initiation of the enforcement action and remain in effect until the permit’s expiration date. Reports of quarterly monitoring shall be submitted to the DEQ regional office no later than the 10th day of April, July, October and January.

Part I

A. EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS.

2. GASOLINE CONTAMINATION -- FRESHWATER RECEIVING WATERS LISTED AS PUBLIC WATER SUPPLIES.

During the period beginning with the permittee's coverage under this general permit and lasting until the permit's expiration date, the permittee is authorized to discharge to freshwater receiving waterbodies from outfall serial number xxxx. Samples taken in compliance with the monitoring requirements specified below shall be taken at the following location: outfall from the final treatment unit prior to mixing with any other waters.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS | DISCHARGE LIMITATIONS | MONITORING REQUIREMENTS |
| --- | --- | --- |
|  | Instantaneous Minimum | Instantaneous Maximum | Frequency | Sample Type |
| Flow (MGD) | NA | NL | 2/Month4 | Estimate |
| Benzene (μg/l)1 | NA | 12.0 | 2/Month4 | Grab |
| Toluene (μg/l)1 | NA | 175.0 | 2/Month4 | Grab |
| Ethylbenzene (μg/l)1 | NA | 320.0 | 2/Month4 | Grab |
| Total Xylenes (μg/l)1 | NA | 33.0 | 2/Month4 | Grab |
| MTBE (methyl tert-butyl ether) (μg/l)1 | NA | 15.0 | 2/Month4 | Grab |
| pH (standard units) | 6.0 | 9.0 | 2/Month4 | Grab |
| Total Recoverable Lead (μg/l)2 | NA | Lower of e(1.273(ln hardness)) -3.259 or 15 | 2/Month4 | Grab |
| Hardness (mg/l CaCO3)2 | NL | NL | 2/Month4 | Grab |
| Ethylene Dibromide (μg/l)2 | NA | .169 | 2/Month4 | Grab |
| 1,2 Dichloroethane (μg/l)2 | NA | 3.8 | 2/Month4 | Grab |
| Ethanol (μg/l)3 | NA | 4100.0 | 2/Month5 | Grab |

NL = No limitation, monitoring required

NA = Not applicable

1Benzene, Toluene, Ethylbenzene, Total Xylenes and MTBE shall be analyzed according to a current and appropriate EPA Method (40 CFR Part 136, 1996) (40 CFR Part 136, 2007) or EPA SW 846 Method 8021B (1998) (1996).

2Monitoring for this parameter is required only when contamination results from leaded fuel. Lead shall be analyzed according to a current and appropriate EPA Wastewater Method (40 CFR Part 136, 1996) (40 CFR Part 136, 2007). The minimum hardness concentration that will be used to determine the lead effluent limit is 25 mg/l. EPA SW 846 Method 8011 (1992) or EPA Drinking Water Method 504.1 (1995) shall be used to analyze ethylene dibromide (EDB) in wastewaters discharged to public water supplies. 1,2 dichloroethane shall be analyzed by a current and appropriate EPA SW 846 Method or EPA Wastewater Method from 40 CFR Part 136 (1996) (2007).

3Monitoring for ethanol is only required for discharges of water contaminated by gasoline containing greater than 10% ethanol. Ethanol shall be analyzed according to EPA SW 846 Method 8015B 8015C (2007) or EPA SW 846 Method 8260B (1996).

4Monitoring frequency shall be 2/month for the first year of permit coverage. If the first year results demonstrate full compliance with the effluent limitations, the permittee may request that the monitoring frequency be reduced from 2/month to 1/month. The written request shall be sent to the appropriate regional office for review. Upon written notification from the DEQ regional office, monitoring frequency shall be reduced to 1/month. Should the permittee be issued a warning letter related to violation of effluent limitations, a notice of violation, or be the subject of an active enforcement action, monitoring frequency shall revert to 2/month, upon issuance of the letter or notice or initiation of the enforcement action and remain in effect until the permit’s expiration date.

5If the first year results demonstrate full compliance with the effluent limitations, the permittee may request that the monitoring frequency for ethanol be reduced from 2/month to 1/quarter. The written request shall be sent to the appropriate regional office for review. Upon written notification from the DEQ regional office, monitoring frequency shall be reduced to 1/quarter. Should the permittee be issued a warning letter related to violation of effluent limitations, a notice of violation, or be the subject of an active enforcement action, monitoring frequency shall revert to 2/month, upon issuance of the letter or notice or initiation of the enforcement action and remain in effect until the permit's expiration date. Reports of quarterly monitoring shall be submitted to the DEQ regional office no later than the 10th day of April, July, October, and January.

Part I

A. EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS.

3. CONTAMINATION BY PETROLEUM PRODUCTS OTHER THAN GASOLINE -- FRESHWATER RECEIVING WATERS NOT LISTED AS PUBLIC WATER SUPPLIES.

During the period beginning with the permittee's coverage under this general permit and lasting until the permit's expiration date, the permittee is authorized to discharge to freshwater receiving waterbodies from outfall serial number xxxx. Samples taken in compliance with the monitoring requirements specified below shall be taken at the following location: outfall from the final treatment unit prior to mixing with any other waters.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS | DISCHARGE LIMITATIONS | MONITORING REQUIREMENTS |
| --- | --- | --- |
|  | Instantaneous Minimum | Instantaneous Maximum | Frequency | Sample Type |
| Flow (MGD) | NA | NL | 1/Month | Estimate |
| Naphthalene (μg/l)1 | NA | 10.0 | 1/Month | Grab |
| Total Petroleum Hydrocarbons (mg/l)2 | NA | 15.0 | 1/Month | Grab |
| pH (standard units) | 6.0 | 9.0 | 1/Month | Grab |

NL = No limitation, monitoring required

NA = Not applicable

1Naphthalene shall be analyzed by a current and appropriate EPA Wastewater Method from 40 CFR Part 136 (1996) (2007) or a current and appropriate EPA SW 846 Method.

2TPH shall be analyzed using EPA SW 846 Method 8015B 8015C (2007) for diesel range organics, or by EPA SW 846 Method 8270C 8270D (2007). If method 8270C Method 8270D (2007) is used, the lab must report the total of diesel range organics and polynuclear aromatic hydrocarbons.

Part I

A. EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS.

4. CONTAMINATION BY PETROLEUM PRODUCTS OTHER THAN GASOLINE -- FRESHWATER RECEIVING WATERS LISTED AS PUBLIC WATER SUPPLIES.

During the period beginning with the permittee's coverage under this general permit and lasting until the permit's expiration date, the permittee is authorized to discharge to freshwater receiving waterbodies from outfall serial number xxxx. Samples taken in compliance with the monitoring requirements specified below shall be taken at the following location: outfall from the final treatment unit prior to mixing with any other waters.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS | DISCHARGE LIMITATIONS | MONITORING REQUIREMENTS |
| --- | --- | --- |
|  | Instantaneous Minimum | Instantaneous Maximum | Frequency | Sample Type |
| Flow (MGD) | NA | NL | 2/Month4 | Estimate |
| Naphthalene (μg/l)1 | NA | 10.0 | 2/Month4 | Grab |
| Benzene (μg/l)2 | NA | 12.0 | 2/Month4 | Grab |
| MTBE (methyl tert-butyl ether)(μg/l)2 | NA | 15.0 | 2/Month4 | Grab |
| Total Petroleum Hydrocarbons (mg/l)3 | NA | 15.0 | 2/Month4 | Grab |
| pH (standard units) | 6.0 | 9.0 | 2/Month4 | Grab |

NL = No limitation, monitoring required

NA = Not applicable

1Naphthalene shall be analyzed by a current and appropriate EPA Wastewater Method from 40 CFR Part 136 (1996) (2007) or a current and appropriate EPA SW 846 Method.

2Benzene and MTBE shall be analyzed according to a current and appropriate EPA Wastewater Method (40 CFR Part 136,1996) (40 CFR Part 136, 2007) or EPA SW 846 Method.

3TPH shall be analyzed using EPA SW 846 Method 8015B 8015C (2007) for diesel range organics, or by EPA SW 846 Method 8270C 8270D (2007). If Method 8270C 8270D is used, the lab must report the total of diesel range organics and polynuclear aromatic hydrocarbons.

4Monitoring frequency shall be 2/month for the first year of permit coverage. If the first year results demonstrate full compliance with the effluent limitations, the permittee may request that the monitoring frequency be reduced from 2/month to 1/month. The written request shall be sent to the appropriate regional office for review. Upon written notification from the DEQ regional office, monitoring frequency shall be reduced to 1/month. Should the permittee be issued a warning letter related to violation of effluent limitations, a notice of violation, or be the subject of an active enforcement action, monitoring frequency shall revert to 2/month, upon issuance of the letter or notice or initiation of the enforcement action and remain in effect until the permit’s expiration date.

Part I

A. EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS

5. DISCHARGES OF HYDROSTATIC TEST WATERS -- ALL RECEIVING WATERS

During the period beginning with the permittee's coverage under this general permit and lasting until the permit's expiration date, the permittee is authorized to discharge to receiving waterbodies from outfall serial number xxxx. Samples taken in compliance with the monitoring requirements specified below shall be taken at the following location: Outfall from the final treatment unit prior to mixing with any other waters.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS | DISCHARGE LIMITATIONS | MONITORING REQUIREMENTS |
| --- | --- | --- |
|  | Instantaneous Minimum | Instantaneous Maximum | Frequency | Sample Type |
| Flow (MGD) | NA | NL | 1/discharge | Estimate |
| pH (standard units) | 6.0 | 9.0 | 1/discharge | Grab |
| Total Petroleum Hydrocarbons (TPH, mg/l) 1 | NA | 15.0 | 1/discharge | Grab |
| Total Organic Carbon (TOC, mg/l) | NA | NL | 1/discharge | Grab |
| Total Residual Chlorine (TRC, mg/l) | NA | 0.011 | 1/discharge | Grab |
| Total Suspended Solids (TSS) | NA | NL | 1/discharge | Grab |

NL = No limitation, monitoring required

NA = Not applicable

1TPH is the sum of individual gasoline range organics and diesel range organics or TPH-GRO and TPH-DRO to be measured by EPA SW 846 Method 8015B (1996) 8015C (2007) for gasoline and diesel range organics, or by EPA SW 846 Methods 8260B (1996) and 8270C (1998) 8270D (2007). If the combination of Methods 8260B and 8270C 8270D is used, the lab must report the total of gasoline range organics, diesel range organics and polynuclear aromatic hydrocarbons.

Part I

A. EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS.

6. GASOLINE CONTAMINATION -- SALTWATER RECEIVING WATERS.

During the period beginning with the permittee's coverage under this general permit and lasting until the permit's expiration date, the permittee is authorized to discharge to saltwater receiving waterbodies from outfall serial number xxxx. Samples taken in compliance with the monitoring requirements specified below shall be taken at the following location: outfall from the final treatment unit prior to mixing with any other waters.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS | DISCHARGE LIMITATIONS | MONITORING REQUIREMENTS |
| --- | --- | --- |
|  | Instantaneous Minimum | Instantaneous Maximum | Frequency | Sample Type |
| Flow (MGD) | NA | NL | 1/Month | Estimate |
| Benzene (μg/l)1 | NA | 50.0 | 1/Month | Grab |
| Toluene (μg/l)1 | NA | 500.0 | 1/Month | Grab |
| Ethylbenzene (μg/l)1 | NA | 4.3 | 1/Month | Grab |
| Total Xylenes (μg/l)1 | NA | 74.0 | 1/Month | Grab |
| MTBE (methyl tert-butyl ether) (μg/l)1 | NA | 440.0 | 1/Month | Grab |
| pH (standard units) | 6.0 | 9.0 | 1/Month | Grab |
| Total Recoverable Lead (μg/l)2 | NA | 8.5 | 1/Month | Grab |
| Ethylene Dibromide (μg/l)2 | NA | 5.3 | 1/Month | Grab |
| 1,2 Dichloroethane (μg/l)2 | NA | 990.0 | 1/Month | Grab |
| Ethanol (μg/l)3 | NA | 4100.0 | 1/Month3 | Grab |

NL = No limitation, monitoring required

NA = Not applicable

1Benzene, Toluene, Ethylbenzene, Total Xylenes and MTBE shall be analyzed according to a current and appropriate EPA Wastewater Method 602 (40 CFR Part 136, 1996) (40 CFR Part 136, 2007) or EPA SW 846 Method 8021B (1998) (1996).

2Monitoring for this parameter is required only when contamination results from leaded fuel. Lead shall be analyzed according to a current and appropriate EPA Wastewater Method 239.2 200.8 or 200.9 (40 CFR Part 136, 1996) (40 CFR Part 136, 2007) or EPA SW 846 Method 7421 (1998) 7010 (2007). 1,2 dichloroethane and EDB (surface waters that are not public water supplies) should be analyzed by a current and appropriate EPA SW 846 Method or EPA Wastewater Method from 40 CFR Part 136 (1996) (2007).

3Monitoring for ethanol is only required for discharges of water contaminated by gasoline containing greater than 10% ethanol. Ethanol shall be analyzed according to EPA SW 846 Method 8015B 8015C (2007) or EPA SW 846 Method 8260B (1996). Monitoring frequency shall be 1/month in the first year of permit coverage. If the first year results demonstrate full compliance with the effluent limitations, the permittee may request that the monitoring frequency be reduced from monthly to 1/quarter. The written request shall be sent to the appropriate regional office for review. Upon written notification from the DEQ regional office, monitoring frequency shall be reduced to 1/quarter. Should the permittee be issued a warning letter related to violation of effluent limitations, a notice of violation, or be the subject of an active enforcement action, monitoring frequency shall revert to 1/month, upon issuance of the letter or notice or initiation of the enforcement action and remain in effect until the permit’s expiration date. Reports of quarterly monitoring shall be submitted to the DEQ regional office no later than the 10th day of April, July, October and January.

Part I

A. EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS.

7. CONTAMINATION BY PETROLEUM PRODUCTS OTHER THAN GASOLINE -- SALTWATER RECEIVING WATERS.

During the period beginning with the permittee's coverage under this general permit and lasting until the permit's expiration date, the permittee is authorized to discharge to saltwater receiving waterbodies from outfall serial number xxxx. Samples taken in compliance with the monitoring requirements specified below shall be taken at the following location: outfall from the final treatment unit prior to mixing with any other waters.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS | DISCHARGE LIMITATIONS | MONITORING REQUIREMENTS |
| --- | --- | --- |
|  | Instantaneous Minimum | Instantaneous Maximum | Frequency | Sample Type |
| Flow (MGD) | NA | NL | 1/Month | Estimate |
| Naphthalene (μg/l)1 | NA | 8.9 | 1/Month | Grab |
| Total Petroleum Hydrocarbons (mg/l)2 | NA | 15.0 | 1/Month | Grab |
| pH (standard units) | 6.0 | 9.0 | 1/Month | Grab |

NL = No limitation, monitoring required

NA = Not applicable

1Naphthalene shall be analyzed by a current and appropriate EPA Wastewater Method from 40 CFR Part 136 (1996) (2007) or a current and appropriate EPA SW 846 Method.

2TPH shall be analyzed using EPA SW 846 Method 8015B 8015C (2007) for diesel range organics or EPA SW 846 Method 8270C 8270D. If Method 8270C 8270D (2007) is used, the lab must report the total of diesel range organics and polynuclear aromatic hydrocarbons.

Part I

A. EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS.

8. CONTAMINATION BY CHLORINATED HYDROCARBON SOLVENTS -- ALL RECEIVING WATERS.

During the period beginning with the permittee's coverage under this general permit and lasting until the permit's expiration date, the permittee is authorized to discharge to receiving waterbodies from outfall serial number xxxx. Samples taken in compliance with the monitoring requirements specified below shall be taken at the following location: outfall from the final treatment unit prior to mixing with any other waters.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS | DISCHARGE LIMITATIONS | MONITORING REQUIREMENTS |
| --- | --- | --- |
|  | Instantaneous Minimum | Instantaneous Maximum | Frequency | Sample Type |
| Flow (MGD) | NA | NL | 1/Month | Estimate |
| Chloroform (CAS # 67663), (μg/l)1 | NA | 100.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| 1,1 Dichloroethane (CAS # 75343) (μg/l)1 | NA | 4.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| 1,2 Dichloroethane (CAS # 107062) (μg/l)1 | NA | 3.8 | 1/Month 2/Month if public water supply2 | Grab Grab |
| 1,1 Dichloroethylene (CAS # 75354) (μg/l)1 | NA | 7.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| cis-1,2 Dichloroethylene (CAS # 159592) (μg/l)1 | NA | 70.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| trans 1,2 Dichloroethylene (CAS # 156605) (μg/l)1 | NA | 100.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| Methylene Chloride (CAS # 75092) (μg/l)1 | NA | 5.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| Tetrachloroethylene (CAS # 127184) (μg/l)1 | NA | 5.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| 1,1,1 Trichloroethane (CAS # 71556) (μg/l)1 | NA | 112.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| 1,1,2 Trichloroethane (CAS # 79005) (μg/l)1 | NA | 5.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| Trichloroethylene (CAS # 79016) (μg/l)1 | NA | 5.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| Vinyl Chloride (CAS # 75014 ) (μg/l)1 | NA | 2.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| Carbon Tetrachloride (CAS # 56235) (μg/l)1 | NA | 2.5 | 1/Month 2/Month if public water supply2 | Grab Grab |
| 1,2 Dichlorobenzene (CAS # 95501) (μg/l)1 | NA | 15.8 | 1/Month 2/Month if public water supply2 | Grab Grab |
| Chlorobenzene (CAS # 108907) (μg/l)1 | NA | 3.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| Trichlorofluoromethane (CAS # 75694) (μg/l)1 | NA | 5.0 | 1/Month 2/Month if public water supply2 | Grab Grab |
| Chloroethane (CAS # 75003) (μg/l)1 | NA | 3.6 | 1/Month 2/Month if public water supply2 | Grab Grab |
| pH (standard units) | 6.0 | 9.0 | 1/Month 2/Month if public water supply2 | Grab Grab |

NL = No limitation, monitoring required

NA = Not applicable

1This constituent shall be analyzed by a current and appropriate gas chromatograph/mass spectroscopy method from EPA SW 846 or the EPA Wastewater Method series from 40 CFR Part 136 (1996) (2007).

2Monitoring frequency shall be 2/month for the first year of permit coverage. If the first year results demonstrate full compliance with the effluent limitations, the permittee may request that the monitoring frequency be reduced from 2/month to 1/month. The written request shall be sent to the appropriate regional office for review. Upon written notification from the DEQ regional office, monitoring frequency shall be reduced to 1/month. Should the permittee be issued a warning letter related to violation of effluent limitations, a notice of violation, or be the subject of an active enforcement action, monitoring frequency shall revert to 2/month, upon issuance of the letter or notice or initiation of the enforcement action and remain in effect until the permit’s expiration date.

Part I

B. Special conditions.

1. There shall be no discharge of floating solids or visible foam in other than trace amounts.

2. The permittee shall sample each permitted outfall each calendar month in which a discharge occurs. When no discharge occurs from an outfall during a calendar month, the discharge monitoring report for that outfall shall be submitted indicating "No Discharge."

3. O & M Manual. If the permitted discharge is through a treatment works, within 30 days of coverage under this general permit, the permittee shall develop and maintain on site, an Operations and Maintenance (O & M) Manual for the treatment works permitted herein. This manual shall detail practices and procedures which will be followed to ensure compliance with the requirements of this permit. The permittee shall operate the treatment works in accordance with the O & M Manual. The manual shall be made available to the department upon request.

4. Operation schedule. The permittee shall construct, install and begin operating the treatment works described in the registration statement prior to discharging to surface waters. The permittee shall notify the department's regional office within five days after the completion of installation and commencement of operation.

5. Materials storage. Except as expressly authorized by this permit or another permit issued by the board, no product, materials, industrial wastes, or other wastes resulting from the purchase, sale, mining, extraction, transport, preparation, or storage of raw or intermediate materials, final product, by-product or wastes, shall be handled, disposed of, or stored so as to permit a discharge of such product, materials, industrial wastes, or other wastes to state waters.

6. If the permittee discharges to surface waters through a municipal separate storm sewer system, the permittee shall, within 30 days of coverage under this general permit, notify the owner of the municipal separate storm sewer system of the existence of the discharge and provide the following information: the name and location of the facility, a contact person and telephone number; the nature of the discharge; and the number of outfalls.

7. Termination of coverage. Provided that the department agrees that the discharge covered under this general permit is no longer needed, the permittee may request termination of coverage under the general permit, for the entire facility or for specific outfalls, by submitting a request for termination of coverage. This request for termination of coverage shall be sent to the department's regional office with appropriate documentation or references to documentation already in the department's possession. Upon the permittee's receipt of the regional director's approval, coverage under this general permit will be terminated. Termination of coverage under this general permit does not relieve the permittee of responsibilities under other board regulations or directives.

Part II 
Conditions Applicable To All VPDES Permits

A. Monitoring.

1. Samples and measurements taken as required by this permit shall be representative of the monitored activity.

2. Monitoring shall be conducted according to procedures approved under 40 CFR Part 136 or alternative methods approved by the U.S. Environmental Protection Agency, unless other procedures have been specified in this permit.

3. The permittee shall periodically calibrate and perform maintenance procedures on all monitoring and analytical instrumentation at intervals that will ensure accuracy of measurements.

B. Records.

1. Records of monitoring information shall include:

a. The date, exact place, and time of sampling or measurements;

b. The individuals who performed the sampling or measurements;

c. The dates and times analyses were performed;

d. The individual or individuals who performed the analyses;

e. The analytical techniques or methods used; and

f. The results of such analyses.

2. Except for records of monitoring information required by this permit related to the permittee's sewage sludge use and disposal activities, which shall be retained for a period of at least five years, the permittee shall retain records of all monitoring information, including all calibration and maintenance records and all original strip chart recordings for continuous monitoring instrumentation; copies of all reports required by this permit; and records of all data used to complete the registration statement for this permit for a period of at least three years from the date of the sample, measurement, report or request for coverage. This period of retention shall be extended automatically during the course of any unresolved litigation regarding the regulated activity or regarding control standards applicable to the permittee, or as requested by the board.

C. Reporting monitoring results.

1. The permittee shall submit the results of the monitoring required by this permit not later than the 10th day of the month after monitoring takes place unless another reporting schedule is specified elsewhere in this permit. Monitoring results shall be submitted to the department's regional office.

2. Monitoring results shall be reported on a Discharge Monitoring Report (DMR) or on forms provided, approved or specified by the department.

3. If the permittee monitors any pollutant specifically addressed by this permit more frequently than required by this permit using test procedures approved under 40 CFR Part 136 or using other test procedures approved by the U.S. Environmental Protection Agency or using procedures specified in this permit, the results of this monitoring shall be included in the calculation and reporting of the data submitted in the DMR or reporting form specified by the department.

4. Calculations for all limitations which require averaging of measurements shall utilize an arithmetic mean unless otherwise specified in this permit.

D. Duty to provide information. The permittee shall furnish to the department, within a reasonable time, any information which the board may request to determine whether cause exists for modifying, revoking and reissuing, or terminating this permit or to determine compliance with this permit. The board may require the permittee to furnish, upon request, such plans, specifications, and other pertinent information as may be necessary to determine the effect of the wastes from his discharge on the quality of state waters or such other information as may be necessary to accomplish the purposes of the State Water Control Law. The permittee shall also furnish to the department upon request copies of records required to be kept by this permit.

E. Compliance schedule reports. Reports of compliance or noncompliance with, or any progress reports on, interim and final requirements contained in any compliance schedule of this permit shall be submitted no later than 14 days following each schedule date.

F. Unauthorized discharges. Except in compliance with this permit or another permit issued by the board, it shall be unlawful for any person to:

1. Discharge into state waters sewage, industrial wastes, other wastes, or any noxious or deleterious substances; or

2. Otherwise alter the physical, chemical or biological properties of such state waters and make them detrimental to the public health, to animal or aquatic life, to the use of such waters for domestic or industrial consumption, for recreation, or for other uses.

G. Reports of unauthorized discharges. Any permittee who discharges or causes or allows a discharge of sewage, industrial waste, other wastes or any noxious or deleterious substance into or upon state waters in violation of Part II F or who discharges or causes or allows a discharge that may reasonably be expected to enter state waters in violation of Part II F shall notify the department of the discharge immediately upon discovery of the discharge, but in no case later than 24 hours after the discovery. A written report of the unauthorized discharge shall be submitted to the department within five days of discovery of the discharge. The written report shall contain:

1. A description of the nature and location of the discharge;

2. The cause of the discharge;

3. The date on which the discharge occurred;

4. The length of time that the discharge continued;

5. The volume of the discharge;

6. If the discharge is continuing, how long it is expected to continue;

7. If the discharge is continuing, what the expected total volume of the discharge will be; and

8. Any steps planned or taken to reduce, eliminate and prevent a recurrence of the present discharge or any future discharges not authorized by this permit.

Discharges reportable to the department under the immediate reporting requirements of other regulations are exempted from this requirement.

H. Reports of unusual or extraordinary discharges. If any unusual or extraordinary discharge including a bypass or upset should occur from a treatment works and the discharge enters or could be expected to enter state waters, the permittee shall promptly notify, in no case later than 24 hours, the department by telephone after the discovery of the discharge. This notification shall provide all available details of the incident, including any adverse affects on aquatic life and the known number of fish killed. The permittee shall reduce the report to writing and shall submit the report to the department within five days of discovery of the discharge in accordance with Part II I 2. Unusual and extraordinary discharges include but are not limited to any discharge resulting from:

1. Unusual spillage of materials resulting directly or indirectly from processing operations;

2. Breakdown of processing or accessory equipment;

3. Failure or taking out of service some or all of the treatment works; and

4. Flooding or other acts of nature.

I. Reports of noncompliance. The permittee shall report any noncompliance which may adversely affect state waters or may endanger public health as follows:

1. An oral report shall be provided within 24 hours from the time the permittee becomes aware of the circumstances. The following shall be included as information which shall be reported within 24 hours under this subsection:

a. Any unanticipated bypass; and

b. Any upset which causes a discharge to surface waters.

2. A written report shall be submitted within five days and shall contain:

a. A description of the noncompliance and its cause;

b. The period of noncompliance including exact dates and times and, if the noncompliance has not been corrected, the anticipated time it is expected to continue; and

c. Steps taken or planned to reduce, eliminate, and prevent reoccurrence of the noncompliance.

The board may waive the written report on a case-by-case basis for reports of noncompliance under Part II I if the oral report has been received within 24 hours and no adverse impact on state waters has been reported.

3. The permittee shall report all instances of noncompliance not reported under Part II I 1 or 2, in writing, at the time the next monitoring reports are submitted. The reports shall contain the information listed in Part II I 2.

NOTE: The immediate (within 24 hours) reports required in Part II G, H and I may be made to the department's regional office. Reports may be made by telephone or by FAX. For reports outside normal working hours, leave a message and this shall fulfill the immediate reporting requirement. For emergencies, the Virginia Department of Emergency Services maintains a 24-hour telephone service at 1-800-468-8892.

J. Notice of planned changes.

1. The permittee shall give notice to the department as soon as possible of any planned physical alterations or additions to the permitted facility. Notice is required only when:

a. The permittee plans an alteration or addition to any building, structure, facility, or installation from which there is or may be a discharge of pollutants, the construction of which commenced:

(1) After promulgation of standards of performance under §306 of the Clean Water Act which are applicable to such source; or

(2) After proposal of standards of performance in accordance with §306 of the Clean Water Act which are applicable to such source, but only if the standards are promulgated in accordance with §306 of the Act within 120 days of their proposal;

b. The alteration or addition could significantly change the nature or increase the quantity of pollutants discharged. This notification applies to pollutants which are subject neither to effluent limitations nor to notification requirements specified elsewhere in this permit; or

c. The alteration or addition results in a significant change in the permittee's sludge use or disposal practices, and such alteration, addition, or change may justify the application of permit conditions that are different from or absent in the existing permit, including notification of additional use or disposal sites not reported during the permit application process or not reported pursuant to an approved land application plan.

2. The permittee shall give advance notice to the department of any planned changes in the permitted facility or activity which may result in noncompliance with permit requirements.

K. Signatory requirements.

1. Registration statement. All registration statements shall be signed as follows:

a. For a corporation: by a responsible corporate officer. For the purpose of this section, a responsible corporate officer means (i) a president, secretary, treasurer, or vice-president of the corporation in charge of a principal business function, or any other person who performs similar policy-making or decision-making functions for the corporation or (ii) the manager of one or more manufacturing, production, or operating facilities employing more than 250 persons or having gross annual sales or expenditures exceeding $25 million (in second-quarter 1980 dollars), if authority to sign documents has been assigned or delegated to the manager in accordance with corporate procedures the manager of one or more manufacturing, production, or operating facilities, provided the manager is authorized to make management decisions that govern the operation of the regulated facility including having the explicit or implicit duty of making major capital investment recommendations, and initiating and directing other comprehensive measures to assure long-term environmental compliance with environmental laws and regulations; the manager can ensure that the necessary systems are established or actions taken to gather complete and accurate information for permit application requirements; and where authority to sign documents has been assigned or delegated to the manager in accordance with corporate procedures;

b. For a partnership or sole proprietorship: by a general partner or the proprietor, respectively; or

c. For a municipality, state, federal, or other public agency: by either a principal executive officer or ranking elected official. For purposes of this section, a principal executive officer of a public agency includes (i) the chief executive officer of the agency or (ii) a senior executive officer having responsibility for the overall operations of a principal geographic unit of the agency.

2. Reports. All reports required by permits, and other information requested by the board shall be signed by a person described in Part II K 1, or by a duly authorized representative of that person. A person is a duly authorized representative only if:

a. The authorization is made in writing by a person described in Part II K 1;

b. The authorization specifies either an individual or a position having responsibility for the overall operation of the regulated facility or activity such as the position of plant manager, operator of a well or a well field, superintendent, position of equivalent responsibility, or an individual or position having overall responsibility for environmental matters for the company. A duly authorized representative thus may be either a named individual or any individual occupying a named position; and

c. The written authorization is submitted to the department.

3. Changes to authorization. If an authorization under Part II K 2 is no longer accurate because a different individual or position has responsibility for the overall operation of the facility, a new authorization satisfying the requirements of Part II K 2 shall be submitted to the department prior to or together with any reports or information to be signed by an authorized representative.

4. Certification. Any person signing a document under Parts II K 1 or 2 shall make the following certification:

"I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to ensure that qualified personnel properly gather and evaluate the information submitted. Based on my inquiry of the person or persons who manage the system, or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete. I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations."

L. Duty to comply. The permittee shall comply with all conditions of this permit. Any permit noncompliance constitutes a violation of the State Water Control Law and the Clean Water Act, except that noncompliance with certain provisions of this permit may constitute a violation of the State Water Control Law but not the Clean Water Act. Permit noncompliance is grounds for enforcement action; for permit termination, revocation and reissuance, or modification; or denial of a permit renewal application.

The permittee shall comply with effluent standards or prohibitions established under §307(a) of the Clean Water Act for toxic pollutants and with standards for sewage sludge use or disposal established under §405(d) of the Clean Water Act within the time provided in the regulations that establish these standards or prohibitions or standards for sewage sludge use or disposal, even if this permit has not yet been modified to incorporate the requirement.

M. Duty to reapply. If the permittee wishes to continue an activity regulated by this permit after the expiration date of this permit, the permittee shall submit a new registration statement at least 180 days before the expiration date of the existing permit, unless permission for a later date has been granted by the board. The board shall not grant permission for registration statements to be submitted later than the expiration date of the existing permit.

N. Effect of a permit. This permit does not convey any property rights in either real or personal property or any exclusive privileges, nor does it authorize any injury to private property or invasion of personal rights, or any infringement of federal, state or local law or regulations.

O. State law. Nothing in this permit shall be construed to preclude the institution of any legal action under, or relieve the permittee from any responsibilities, liabilities, or penalties established pursuant to any other state law or regulation or under authority preserved by §510 of the Clean Water Act. Except as provided in permit conditions on "bypassing" (Part II U) and "upset" (Part II V), nothing in this permit shall be construed to relieve the permittee from civil and criminal penalties for noncompliance.

P. Oil and hazardous substance liability. Nothing in this permit shall be construed to preclude the institution of any legal action or relieve the permittee from any responsibilities, liabilities, or penalties to which the permittee is or may be subject under Article 11 (§62.1-44.34:14 et seq.) of the State Water Control Law.

Q. Proper operation and maintenance. The permittee shall at all times properly operate and maintain all facilities and systems of treatment and control (and related appurtenances) which are installed or used by the permittee to achieve compliance with the conditions of this permit. Proper operation and maintenance also includes effective plant performance, adequate funding, adequate staffing, and adequate laboratory and process controls, including appropriate quality assurance procedures. This provision requires the operation of back-up or auxiliary facilities or similar systems which are installed by the permittee only when the operation is necessary to achieve compliance with the conditions of this permit.

R. Disposal of solids or sludges. Solids, sludges or other pollutants removed in the course of treatment or management of pollutants shall be disposed of in a manner so as to prevent any pollutant from such materials from entering state waters.

S. Duty to mitigate. The permittee shall take all reasonable steps to minimize or prevent any discharge or sludge use or disposal in violation of this permit which has a reasonable likelihood of adversely affecting human health or the environment.

T. Need to halt or reduce activity not a defense. It shall not be a defense for a permittee in an enforcement action that it would have been necessary to halt or reduce the permitted activity in order to maintain compliance with the conditions of this permit.

U. Bypass.

1. "Bypass" means the intentional diversion of waste streams from any portion of a treatment facility. The permittee may allow any bypass to occur which does not cause effluent limitations to be exceeded, but only if it also is for essential maintenance to assure efficient operation. These bypasses are not subject to the provisions of Part II U 2 and 3.

2. Notice.

a. Anticipated bypass. If the permittee knows in advance of the need for a bypass, prior notice shall be submitted, if possible, at least 10 days before the date of the bypass.

b. Unanticipated bypass. The permittee shall submit notice of an unanticipated bypass as required in Part II I.

3. Prohibition of bypass.

a. Bypass is prohibited, and the board may take enforcement action against a permittee for bypass, unless:

(1) Bypass was unavoidable to prevent loss of life, personal injury, or severe property damage;

(2) There were no feasible alternatives to the bypass, such as the use of auxiliary treatment facilities, retention of untreated wastes, or maintenance during normal periods of equipment downtime. This condition is not satisfied if adequate back-up equipment should have been installed in the exercise of reasonable engineering judgment to prevent a bypass which occurred during normal periods of equipment downtime or preventive maintenance; and

(3) The permittee submitted notices as required under Part II U 2.

b. The board may approve an anticipated bypass, after considering its adverse effects, if the board determines that it will meet the three conditions listed above in Part II U 3 a.

V. Upset.

1. An upset constitutes an affirmative defense to an action brought for noncompliance with technology-based permit effluent limitations if the requirements of Part II V 2 are met. A determination made during administrative review of claims that noncompliance was caused by upset and before an action for noncompliance is not a final administrative action subject to judicial review.

2. A permittee who wishes to establish the affirmative defense of upset shall demonstrate through properly signed, contemporaneous operating logs or other relevant evidence that:

a. An upset occurred and that the permittee can identify the cause or causes of the upset;

b. The permitted facility was at the time being properly operated;

c. The permittee submitted notice of the upset as required in Part II I; and

d. The permittee complied with any remedial measures required under Part II S.

3. In any enforcement proceeding, the permittee seeking to establish the occurrence of an upset has the burden of proof.

W. Inspection and entry. The permittee shall allow the director or an authorized representative, upon presentation of credentials and other documents as may be required by law, to:

1. Enter upon the permittee's premises where a regulated facility or activity is located or conducted or where records must be kept under the conditions of this permit;

2. Have access to and copy, at reasonable times, any records that must be kept under the conditions of this permit;

3. Inspect at reasonable times any facilities, equipment (including monitoring and control equipment), practices, or operations regulated or required under this permit; and

4. Sample or monitor at reasonable times, for the purposes of ensuring permit compliance or as otherwise authorized by the Clean Water Act and the State Water Control Law any substances or parameters at any location.

For purposes of this section, the time for inspection shall be deemed reasonable during regular business hours, and whenever the facility is discharging. Nothing contained herein shall make an inspection unreasonable during an emergency.

X. Permit actions. Permits may be modified, revoked and reissued, or terminated for cause. The filing of a request by the permittee for a permit modification, revocation and reissuance, or termination, or a notification of planned changes or anticipated noncompliance does not stay any permit condition.

Y. Transfer of permits.

1. Permits are not transferable to any person except after notice to the department. Except as provided in Part II Y 2, a permit may be transferred by the permittee to a new owner or operator only if the permit has been modified or revoked and reissued, or a minor modification made, to identify the new permittee and incorporate such other requirements as may be necessary under the State Water Control Law and the Clean Water Act.

2. As an alternative to transfers under Part II Y 1, this permit may be automatically transferred to a new permittee if:

a. The current permittee notifies the department at least 30 days in advance of the proposed transfer of the title to the facility or property;

b. The notice includes a written agreement between the existing and new permittees containing a specific date for transfer of permit responsibility, coverage, and liability between them; and

c. The board does not notify the existing permittee and the proposed new permittee of its intent to modify or revoke and reissue the permit. If this notice is not received, the transfer is effective on the date specified in the agreement mentioned in Part II Y 2 b.

Z. Severability. The provisions of this permit are severable, and if any provision of this permit or the application of any provision of this permit to any circumstance, is held invalid, the application of such provision to other circumstances, and the remainder of this permit, shall not be affected thereby.

NOTICE: The form used in administering the above regulation is not being published; however, the name of the form is listed below. The form is available for public inspection by contacting the agency contact for this regulation, or at the office of the Registrar of Regulations, General Assembly Building, 2nd Floor, Richmond, Virginia.

FORMS

General VPDES General Permit Registration Statement for Discharges from Petroleum Contaminated Sites, Groundwater Remediation and Hydrostatic Tests (rev. 4/03) (rev. 2/08).

DOCUMENTS INCORPORATED BY REFERENCE

|  | Method | Cite |
| --- | --- | --- |
|  | 150.1 200.7 200.8 200.9 239.2 504.1 602 610 625 1624 1625 6010B 7010 7421 8011 8015B 8015C 8021B 8100 8260B 8270C 8270D 9040B 9040C | EPA 600/4-87-020 EPA 600/R-94-111; 40 CFR 136, App D, 1996 40 CFR 136 (2007) 40 CFR 136 (2007) EPA 600/4-79-020; 40 CFR 136, App D, 1996 EPA 600/R-95-131 (1995) 40 CFR 136, 1996 40 CFR 136, 1996 40 CFR 136, 1996 40 CFR 136, 1996 40 CFR 136, 1996 EPA SW 846, Ch. 3.3, (1998) EPA SW 846 (2007) EPA SW 846, Ch. 3.3, (1998) EPA SW 846 (1992) EPA SW 846, Ch. 4.3.1, (1998) EPA SW 846 (2007) EPA SW 846, Ch. 4.3.1, (1998) (1996) EPA SW 846, Ch. 4.3.1, (1998) EPA SW 846, Ch. 4.3.2, (1998) (1996) EPA SW 846, Ch. 4.3.2, (1998) EPA SW 846 (2007) EPA SW 846, Ch. 8.2, (1998) EPA SW 846 (2004) |

VA.R. Doc. No. R08-1210; Filed April 17, 2008, 10:41 a.m.