TITLE 2. AGRICULTURE

BOARD OF AGRICULTURE AND CONSUMER SERVICES

Final Regulation

REGISTRAR'S NOTICE: The Board of Agriculture and Consumer Services is claiming an exemption from the Administrative Process Act pursuant to §2.2-4002 A 21 of the Code of Virginia when adopting, amending, or repealing regulations pursuant to §59.1-156 A (ii) of the Code of Virginia.

Title of Regulation: 2VAC5-420. Regulations for the Enforcement of the Virginia Gasoline and Motor Fuel Law (amending 2VAC5-420-30, 2VAC5-420-80).

Statutory Authority: §§59.1-153 and 59.1-156 of the Code of Virginia.

Effective Date: May 21, 2008.

Agency Contact: Robert E. Bailey, Program Manager, Department of Agriculture and Consumer Services, P.O. Box 1163, Richmond, VA 23218, telephone (804) 786-1274, FAX (804) 786-1571, TTY (800) 828-1120, or email robert.bailey@vdacs.virginia.gov.

Summary:

This regulation establishes the following mandates relating to the sales and distribution of gasoline and other motor fuels in this state: (i) specifies minimum standards for motor fuel quality; (ii) requires gasoline and other motor fuels have specific pump labeling; (iii) specifies methods of sampling and testing; (iv) requires the registration of all retail motor fuels; and (v) specifies means of compliance and methods of enforcement.

The U.S. Environmental Protection Agency’s mandated phase-in of Renewable Fuel Standard Requirements increases the amount of ethanol required to be added to gasoline distributed and sold in the United States. However, the motor fuel quality testing standards currently prescribed in this regulation are incompatible with the gasoline-ethanol blends coming to market in the Commonwealth. Thus, the following amendments are sought to:

1. Provide that the specific method for the testing of gasoline is the latest version of ASTM D 4814, "Standard Specification for Automotive Spark Ignition Engine Fuel."

2. Specify that volatility standards for gasoline-ethanol blends shall not be more restrictive that those of the EPA.

3. Allow three different options for the blending of gasoline with ethanol at concentrations up to 10% by volume.

4. Prescribe a maximum percentage by volume of undissolved water and sediment.

5. Prescribe seasonal vapor pressure requirements for the gasoline-ethanol blends.

6. Provide that the specific method for the testing of diesel fuel is the latest version of ASTM D 975, "Standard Specification of Diesel Fuel Oils."

2VAC5-420-30. Specifications for gasoline and diesel fuel.

A. Gasoline. Gasoline shall meet the requirements of the following specifications when tested in compliance with the latest version of the American Society for Testing and Materials (ASTM) ASTM International (formerly the American Society for Testing and Materials) Test Methods or other test methods specified below:

|  | Specification | Test Method ASTM |
| --- | --- | --- |
|  | 1. Distillation. | D86 |
|  | a. Percent evaporated during months of: January, February, November, and December at 50°C (122°F) Minimum | 10% |
|  | March, April, May, September, and October at 55°C (131°F) Minimum | 10% |
|  | June, July, and August at 70°C (158°F) Minimum | 10% |
|  | b. Percent evaporated during months of: January, February, November, and December at 110°C (230°F) Minimum | 50% |
|  | March, April, May, September, and October at 113°C (235°F) Minimum | 50% |
|  | June, July, and August at 121°C (250°F) Minimum | 50% |
|  | c. Percent evaporated during the months of: January, February, March, April, May, September, October, November, and December at 185°C (365°F) Minimum | 90% |
|  | June, July, and August at 190°C (374°F) Minimum | 90% |
|  | End point, maximum 225°C (437°F) |  |
|  | Residue, percent maximum | 2% |

2. a. Reid vapor pressure at 100°F, pounds per square inch (psi)

Test Method ASTM D4953 or D5191 for both oxygenated or nonoxygenated fuels.

Throughout the Commonwealth of Virginia, except for the nonattainment areas specified below during the period specified below, the Reid vapor pressure standard shall be:

|  | June 1 to September 15 | 9.0 psi. |
| --- | --- | --- |
|  | September 16 to 30 | 13.5 psi. |
|  | Maximum during months of March, April, May and October | 13.5 psi. |
|  | Maximum during months of November, December, January, and February | 15.0 psi. |

For the nonattainment areas specified in Section 3 A 2 (ii) below, the Reid vapor pressure standard shall be:

|  | Maximum during period: |  |
| --- | --- | --- |
|  | June 1 to September 15 | 7.8psi. |

b. The nonattainment areas referred to in subsection A 2 a of this section are:

(1) The Northern Virginia nonattainment area which includes the counties of Arlington, Fairfax, Loudoun, Prince William, Stafford, and includes the cities of Alexandria, Fairfax, Falls Church, Manassas, and Manassas Park.

(2) The Richmond nonattainment area which includes the counties of Charles City, Chesterfield, Hanover, Henrico, and includes the cities of Colonial Heights, Hopewell, and Richmond.

(3) The Hampton Roads nonattainment area which includes the counties of James City, York, and includes the cities of Chesapeake, Hampton, Newport News, Norfolk, Poquoson, Portsmouth, Suffolk, Virginia Beach, and Williamsburg.

The Reid vapor pressure values specified in subdivision A 2 of this section shall be increased one psi for gasoline-ethanol blends containing at least 9.0% but not more than 10% ethanol by volume.

c. Throughout the Commonwealth of Virginia, from May 1 to May 31 of each year, gasoline refiners, gasoline importers, gasoline pipeline operators, and gasoline terminal operators shall supply fuel with a maximum Reid vapor pressure standard of 9.0 psi.

|  | 3. Undissolved water and sediment, percent by volume, maximum | 0.01% VDACS Method of Test1 |
| --- | --- | --- |
|  | 4. Existent gum, 5 mg. per 100 ml., maximum | ASTM D381 |
|  | 5. The octane number shall not be more than one octane number below the octane number filed in connection with registration. | ASTM D2699 and D2700 |
|  | 6. Gasoline labeled as "unleaded," "no lead," or "lead free" shall not contain more than 0.05 grams lead per gallon and not more than 0.005 grams of phosphorus per gallon. | ASTM Lead: D3237 Phosphorus: D3231 |
|  | 1The calculation for the V.D.A.C.S. Method of Test is as follows: |
|  |  | Volume of water and/or sediment | x 100 = Water and/or Sediment |
|  |  | Total volume of sample |  |

B. Diesel fuel. Diesel fuel shall meet the requirements of the following specifications when tested in compliance with the latest version of the American Society for Testing and Materials Test Methods specified below:

|  | Specification |  | ASTM Method |
| --- | --- | --- | --- |
|  | 1. Flash point, degrees F minimum |  | D93 |
|  | (If registered and labeled as #1 Diesel) | 100°F |  |
|  | (If registered and labeled as #2 Diesel) | 125°F |  |
|  | 2. Water and sediment, percent by volume, maximum | 0.05% | D1796 |
|  | 3. Sulfur, percent by weight maximum | 0.5% | D2622 (D129 shall be the referee method) |
|  | 4. Cetane number, minimum | 40 | D613 |
|  | 5. 90 percent distillation point, degrees, F maximum | 640°F | D86 |
|  | 6. Corrosion - ASTM copper strip scale maximum | No. 3 | D130 |
|  |  |  | 3 hours at 50°C |

ASTM D 4814-07b, "Standard Specification for Automotive Spark Ignition Engine Fuel," except that volatility standards for unleaded gasoline blended with ethanol shall not be more restrictive than those adopted under the rules, regulations, and Clean Air Act waivers of the U.S. Environmental Protection Agency. Gasoline blended with ethanol at concentrations up to 10% by volume shall be blended under any of the following three options:

1. The base gasoline used in such blends shall meet the requirements of ASTM D 4814 and the ethanol shall meet the requirements of ASTM D 4806-07a, "Standard Specification for Denatured Fuel Ethanol for Blending with Gasolines for Use as Automotive Spark-Ignition Engine Fuel," with the following exceptions applicable to the gasoline-ethanol blend:

a. The distillation minimum temperature at the 50 volume percent evaporated point shall not be less than 66°C (150°F);

b. The vapor/liquid ratio specification is waived for gasoline-ethanol blends of up to 10% ethanol;

2. The blend shall meet the requirements of ASTM D 4814; or

3. The base gasoline used in such blends shall meet all the requirements of ASTM D 4814 except distillation, and the blend shall meet the distillation requirements of ASTM D 4814.

Undissolved water and sediment, percent by volume, maximum 0.01% as determined by Virginia Department of Agriculture and Consumer Services (VDACS) Method of Test. The calculation for the VDACS Method of Test is as follows:

Volume of water and/or sediment ÷ total volume of sample x 100 = Percent Water and/or Sediment.

B. Blends of gasoline and ethanol shall meet the following vapor pressure requirements:

1. During the period between June 1 and September 15 of each calendar year, blends containing 9.0% ethanol by volume and a maximum of 10% ethanol by volume shall not exceed the ASTM D 4814 vapor pressure limits by more than 1.0 psi. All other blend concentrations shall meet the ASTM D 4814 vapor pressure limits.

2. During the period between September 16 and May 31 of each calendar year, all blends of gasoline and ethanol shall not exceed the ASTM D 4814 vapor pressure standard by more than 1.0 psi.

C. Diesel fuel. Diesel fuel shall meet the requirements of ASTM D 975-08, "Standard Specification for Diesel Fuel Oils."

2VAC5-420-80. Notation for documents incorporated by reference.

Test methods published by the ASTM and incorporated by reference in this chapter are available from:

American Society for Testing and Materials 
1916 Race Street 
Philadelphia, Pennsylvania 19103
Phone: (215) 299-5585

ASTM International
100 Barr Habor Drive, P.O. Box C700
West Conshohocken, PA 19428
www.astm.org

DOCUMENTS INCORPORATED BY REFERENCE

ASTM D975-08, Standard Specification for Diesel Fuel Oils, ASTM International, West Conshohocken, PA, (www.astm.org).

ASTM Research Method D2699 ASTM D2699-07a, Standard Test Method for Research Octane Number of Spark-Ignition Engine Fuel, ASTM International, West Conshohocken, PA, (www.astm.org).

ASTM Motor Method D2700 ASTM D2700-07b, Standard Test Method for Motor Octane Number of Spark-Ignition Engine Fuel, ASTM International, West Conshohocken, PA, (www.astm.org).

ASTM D4806-07a, Standard Specification for Denatured Fuel Ethanol for Blending with Gasolines for Use as Automotive Spark-Ignition Engine Fuel, ASTM International, West Conshohocken, PA, (www.astm.org).

ASTM D4814-07b, Standard Specification for Automotive Spark-Ignition Engine Fuel, ASTM International, West Conshohocken, PA, (www.astm.org).

VA.R. Doc. No. R08-1221; Filed May 21, 2008, 11:36 a.m.