TITLE 13. HOUSING

BOARD OF HOUSING AND COMMUNITY DEVELOPMENT

Final Regulation

REGISTRAR'S NOTICE: The Board of Housing and Community Development is claiming an exclusion from the Administrative Process Act in accordance with §2.2-4006 A 4 a of the Code of Virginia, which excludes regulations that are necessary to conform to changes in Virginia statutory law where no agency discretion is involved. The Board of Housing and Community Development will receive, consider and respond to petitions by any interested person at any time with respect to reconsideration or revision.

Title of Regulation: 13VAC5-51. Virginia Statewide Fire Prevention Code (amending 13VAC5-51-81).

Statutory Authority: §27-97 of the Code of Virginia.

Effective Date: October 1, 2008.

Agency Contact: Stephen W. Calhoun, Regulatory Coordinator, Department of Housing and Community Development, The Jackson Center, 501 North 2nd Street, Richmond, VA 23219-1321, telephone (804) 371-7000, FAX (804) 371-7090, TTY (804) 371-7089, or email steve.calhoun@dhcd.virginia.gov.

Summary:

Chapter 499 of the 2008 Acts of Assembly provides that no fee may be charged for the State Fire Marshal’s Office to inspect schools. This action amends the Statewide Fire Prevention Code by removing the fee schedule previously established for the inspection of schools.

13VAC5-51-81. Section 107.0. Permits.

A. 107.1. Prior notification: The fire official may require notification prior to (i) activities involving the handling, storage or use of substances, materials or devices regulated by the SFPC; (ii) conducting processes which produce conditions hazardous to life or property; or (iii) establishing a place of assembly.

B. 107.2. Permits required: Permits may be required by the fire official as permitted under the SFPC in accordance with Table 107.2, except that the fire official shall require permits for the manufacturing, storage, handling, use, and sale of explosives. An application for a permit to manufacture, store, handle, use, or sell explosives shall only be made by an individual certified as a blaster in accordance with Section 3301.4, or by a person who has been issued a background clearance card in accordance with Section 3301.2.3.1.1.

Exception: Such permits shall not be required for the storage of explosives or blasting agents by the Virginia Department of State Police provided notification to the fire official is made annually by the Chief Arson Investigator listing all storage locations.

C. Add Table 107.2 as follows:

Table 107.2.
OPERATIONAL PERMIT REQUIREMENTS (to be filled in by local jurisdiction).

| Description | Permit required (yes or no) | Permit fee | Inspection fee |
| --- | --- | --- | --- |
| Aerosol products. An operational permit is required to manufacture, store or handle an aggregate quantity of Level 2 or Level 3 aerosol products in excess of 500 pounds (227 kg) net weight. |  |  |  |
| Amusement buildings. An operational permit is required to operate a special amusement building. |  |  |  |
| Aviation facilities. An operational permit is required to use a Group H or Group S occupancy for aircraft servicing or repair and aircraft fuel-servicing vehicles. Additional permits required by other sections of this code include, but are not limited to, hot work, hazardous materials and flammable or combustible finishes. |  |  |  |
| Carnivals and fairs. An operational permit is required to conduct a carnival or fair. |  |  |  |
| Battery systems. An operational permit is required to install stationary lead-acid battery systems having a liquid capacity of more than 50 gallons (189 L). |  |  |  |
| Cellulose nitrate film. An operational permit is required to store, handle or use cellulose nitrate film in a Group A occupancy. |  |  |  |
| Cellulose nitrate film. An operational permit is required to store, handle or use cellulose nitrate film in a Group A occupancy. |  |  |  |
| Combustible dust-producing operations. An operational permit is required to operate a grain elevator, flour starch mill, feed mill, or a plant pulverizing aluminum, coal, cocoa, magnesium, spices or sugar, or other operations producing combustible dusts as defined in Chapter 2. |  |  |  |
| Combustible fibers. An operational permit is required for the storage and handling of combustible fibers in quantities greater than 100 cubic feet (2.8 m3). Exception: An operational permit is not required for agricultural storage. |  |  |  |
| Compressed gas. An operational permit is required for the storage, use or handling at normal temperature and pressure (NTP) of compressed gases in excess of the amounts listed below. Exception: Vehicles equipped for and using compressed gas as a fuel for propelling the vehicle. |  |  |  |
| Permit Amounts for Compressed Gases |  |  |  |
| Type of Gas | Amount (cubic feet at NTP) |  |  |  |
| Corrosive | 200 |  |  |  |
| Flammable (except cryogenic fluids and liquefied petroleum gases) | 200 |  |  |  |
| Highly toxic | Any Amount |  |  |  |
| Inert and simple asphyxiant | 6,000 |  |  |  |
| Oxidizing (including oxygen) | 504 |  |  |  |
| Toxic | Any Amount |  |  |  |
| For SI: 1 cubic foot = 0.02832 m3. |  |  |  |
| Covered mall buildings. An operational permit is required for: 1. The placement of retail fixtures and displays, concession equipment, displays of highly combustible goods and similar items in the mall. 2. The display of liquid- or gas-fired equipment in the mall. 3. The use of open-flame or flame-producing equipment in the mall. |  |  |  |
| Cryogenic fluids. An operational permit is required to produce, store, transport on site, use, handle or dispense cryogenic fluids in excess of the amounts listed below. Exception: Operational permits are not required for vehicles equipped for and using cryogenic fluids as a fuel for propelling the vehicle or for refrigerating the lading. |  |  |  |
| Permit Amounts for Cryogenic Fluids |  |  |  |
| Type of Cryogenic Fluid | Inside Building (gallons) | Outside Building (gallons) |  |  |  |
| Flammable | More than 1 | 60 |  |  |  |
| Inert | 60 | 500 |  |  |  |
| Oxidizing (includes oxygen) | 10 | 50 |  |  |  |
| Physical or health hazard not indicated above | Any Amount | Any Amount |  |  |  |
| For SI: 1 gallon = 3.785 L. |  |  |  |
| Cutting and welding. An operational permit is required to conduct cutting or welding operations within the jurisdiction. |  |  |  |
| Dry cleaning plants. An operational permit is required to engage in the business of dry cleaning or to change to a more hazardous cleaning solvent used in existing dry cleaning equipment. |  |  |  |
| Exhibits and trade shows. An operational permit is required to operate exhibits and trade shows. |  |  |  |
| Explosives. An operational permit is required for the manufacture, storage, handling, sale or use of any quantity of explosive, explosive material, fireworks, or pyrotechnic special effects within the scope of Chapter 33. |  |  |  |
| Fire hydrants and valves. An operational permit is required to use or operate fire hydrants or valves intended for fire suppression purposes that are installed on water systems and accessible to a fire apparatus access road that is open to or generally used by the public. Exception: An operational permit is not required for authorized employees of the water company that supplies the system or the fire department to use or operate fire hydrants or valves. |  |  |  |
| Flammable and combustible liquids. An operational permit is required: 1. To use or operate a pipeline for the transportation within facilities of flammable or combustible liquids. This requirement shall not apply to the offsite transportation in pipelines regulated by the Department of Transportation (DOTn) (see §3501.1.2) nor does it apply to piping systems (see §3503.6). 2. To store, handle or use Class I liquids in excess of 5 gallons (19 L) in a building or in excess of 10 gallons (37.9 L) outside of a building, except that a permit is not required for the following: |  |  |  |
| 2.1. The storage or use of Class I liquids in the fuel tank of a motor vehicle, aircraft, motorboat, mobile power plant or mobile heating plant, unless such storage, in the opinion of the fire official, would cause an unsafe condition. 2.2. The storage or use of paints, oils, varnishes or similar flammable mixtures when such liquids are stored for maintenance, painting or similar purposes for a period of not more than 30 days. |  |  |  |
| 3. To store, handle or use Class II or Class IIIA liquids in excess of 25 gallons (95 L) in a building or in excess of 60 gallons (227 L) outside a building, except for fuel oil used in connection with oil-burning equipment. 4. To remove Class I or Class II liquids from an underground storage tank used for fueling motor vehicles by any means other than the approved, stationary on-site pumps normally used for dispensing purposes. 5. To operate tank vehicles, equipment, tanks, plants, terminals, wells, fuel-dispensing stations, refineries, distilleries and similar facilities where flammable and combustible liquids are produced, processed, transported, stored, dispensed or used. 6. To install, alter, remove, abandon, place temporarily out of service (for more than 90 days) or otherwise dispose of an underground, protected above-ground or above-ground flammable or combustible liquid tank. 7. To change the type of contents stored in a flammable or combustible liquid tank to a material that poses a greater hazard than that for which the tank was designed and constructed. 8. To manufacture, process, blend or refine flammable or combustible liquids. |  |  |  |
| Floor finishing. An operational permit is required for floor finishing or surfacing operations exceeding 350 square feet (33 m2) using Class I or Class II liquids. |  |  |  |
| Fruit and crop ripening. An operational permit is required to operate a fruit- or crop-ripening facility or conduct a fruit-ripening process using ethylene gas. |  |  |  |
| Fumigation and thermal insecticidal fogging. An operational permit is required to operate a business of fumigation or thermal insecticidal fogging and to maintain a room, vault or chamber in which a toxic or flammable fumigant is used. |  |  |  |
| Hazardous materials. An operational permit is required to store, transport on site, dispense, use or handle hazardous materials in excess of the amounts listed below. |  |  |  |
| Permit Amounts for Hazardous Materials |  |  |  |
| Type of Material | Amount |  |  |  |
| Combustible liquids | See flammable and combustible liquids |  |  |  |
| Corrosive materials |  |  |  |  |
| Gases Liquids Solids | See compressed gases 55 gallons 1000 pounds |  |  |  |
| Explosive materials | See explosives |  |  |  |
| Flammable materials |  |  |  |
| Gases Liquids Solids | See compressed gases See flammable and combustible liquids 100 pounds |  |  |  |
| Highly toxic materials |  |  |  |
| Gases Liquids Solids | See compressed gases Any Amount Any Amount |  |  |  |
| Oxidizing materials |  |  |  |
| Gases | See compressed gases |  |  |  |
| Liquids |  |  |  |
| Class 4 Class 3 Class 2 Class 1 | Any Amount 1 gallon 10 gallons 55 gallons |  |  |  |
| Solids |  |  |  |
| Class 4 Class 3 Class 2 Class 1 | Any Amount 10 pounds 100 pounds 500 pounds |  |  |  |
| Organic peroxides |  |  |  |
| Liquids |  |  |  |
| Class I Class II Class III Class IV Class V | Any Amount Any Amount 1 gallon 2 gallons No Permit Required |  |  |  |
| Solids |  |  |  |
| Class I Class II Class III Class IV Class V | Any Amount Any Amount 10 pounds 20 pounds No Permit Required |  |  |  |
| Pyrophoric materials |  |  |  |
| Gases Liquids Solids | See compressed gases Any Amount Any Amount |  |  |  |
| Toxic materials |  |  |  |
| Gases Liquids Solids | See compressed gases 10 gallons 100 pounds |  |  |  |
| Unstable (reactive) materials |  |  |  |
| Liquids |  |  |  |
| Class 4 Class 3 Class 2 Class 1 | Any Amount Any Amount 5 gallons 10 gallons |  |  |  |
| Solids |  |  |  |
| Class 4 Class 3 Class 2 Class 1 | Any Amount Any Amount 50 pounds 100 pounds |  |  |  |
| Water-reactive Materials |  |  |  |
| Liquids |  |  |  |
| Class 3 Class 2 Class 1 | Any Amount 5 gallons 55 gallons |  |  |  |
| Solids |  |  |  |  |
| Class 3 Class 2 Class 1 | Any Amount 50 pounds 500 pounds |  |  |  |
| For SI: 1 gallon = 3.785 L, 1 pound = 0.454 kg. |  |  |  |
| HPM facilities. An operational permit is required to store, handle or use hazardous production materials. |  |  |  |
| High piled storage. An operational permit is required to use a building or portion thereof as a high-piled storage area exceeding 500 square feet (46 m2). |  |  |  |
| Hot work operations. An operational permit is required for hot work including, but not limited to: 1. Public exhibitions and demonstrations where hot work is conducted. 2. Use of portable hot work equipment inside a structure. Exception: Work that is conducted under a construction permit. 3. Fixed-site hot work equipment such as welding booths. 4. Hot work conducted within a hazardous fire area. 5. Application of roof coverings with the use of an open-flame device. 6. When approved, the fire official shall issue a permit to carry out a Hot Work Program. This program allows approved personnel to regulate their facility's hot work operations. The approved personnel shall be trained in the fire safety aspects denoted in this chapter and shall be responsible for issuing permits requiring compliance with the requirements found in this chapter. These permits shall be issued only to their employees or hot work operations under their supervision. |  |  |  |
| Industrial ovens. An operational permit is required for operation of industrial ovens regulated by Chapter 21. |  |  |  |
| Lumber yards and woodworking plants. An operational permit is required for the storage or processing of lumber exceeding 100,000 board feet (8,333 ft3) (236 m3). |  |  |  |
| Liquid- or gas-fueled vehicles or equipment in assembly buildings. An operational permit is required to display, operate or demonstrate liquid- or gas-fueled vehicles or equipment in assembly buildings. |  |  |  |
| LP-gas. An operational permit is required for: 1. Storage and use of LP-gas. Exception: An operational permit is not required for individual containers with a 500-gallon (1893 L) water capacity or less serving occupancies in Group R-3. 2. Operation of cargo tankers that transport LP-gas. |  |  |  |
| Magnesium. An operational permit is required to melt, cast, heat treat or grind more than 10 pounds (4.54 kg) of magnesium. |  |  |  |
| Miscellaneous combustible storage. An operational permit is required to store in any building or upon any premises in excess of 2,500 cubic feet (71 m3) gross volume of combustible empty packing cases, boxes, barrels or similar containers, rubber tires, rubber, cork or similar combustible material. |  |  |  |
| Open burning. An operational permit is required for the kindling or maintaining of an open fire or a fire on any public street, alley, road, or other public or private ground. Instructions and stipulations of the permit shall be adhered to. Exception: Recreational fires. |  |  |  |
| Open flames and candles. An operational permit is required to remove paint with a torch; use a torch or open-flame device in a hazardous fire area; or to use open flames or candles in connection with assembly areas, dining areas of restaurants or drinking establishments. |  |  |  |
| Organic coatings. An operational permit is required for any organic-coating manufacturing operation producing more than 1 gallon (4 L) of an organic coating in one day. |  |  |  |
| Assembly/educational. An operational permit is required to operate a place of assembly /educational occupancy. |  |  |  |
| Private fire hydrants. An operational permit is required for the removal from service, use or operation of private fire hydrants. Exception: An operational permit is not required for private industry with trained maintenance personnel, private fire brigade or fire departments to maintain, test and use private hydrants. |  |  |  |
| Pyrotechnic special effects material. An operational permit is required for use and handling of pyrotechnic special effects material. |  |  |  |
| Pyroxylin plastics. An operational permit is required for storage or handling of more than 25 pounds (11 kg) of cellulose nitrate (pyroxylin) plastics and for the assembly or manufacture of articles involving pyroxylin plastics. |  |  |  |
| Refrigeration equipment. An operational permit is required to operate a mechanical refrigeration unit or system regulated by Chapter 6. |  |  |  |
| Repair garages and service stations. An operational permit is required for operation of repair garages and automotive, marine and fleet service stations. |  |  |  |
| Rooftop heliports. An operational permit is required for the operation of a rooftop heliport. |  |  |  |
| Spraying or dipping. An operational permit is required to conduct a spraying or dipping operation utilizing flammable or combustible liquids or the application of combustible powders regulated by Chapter 15. |  |  |  |
| Storage of scrap tires and tire byproducts. An operational permit is required to establish, conduct or maintain storage of scrap tires and tire byproducts that exceeds 2,500 cubic feet (71 m3) of total volume of scrap tires and for indoor storage of tires and tire byproducts. |  |  |  |
| Temporary membrane structures and tents. An operational permit is required to operate an air-supported temporary membrane structure or a tent. Exceptions: 1. Tents used exclusively for recreational camping purposes. 2. Tents and air-supported structures that cover an area of 900 square feet (84 m2) or less, including all connecting areas or spaces with a common means of egress or entrance and with an occupant load of 50 or less persons. |  |  |  |
| Tire-rebuilding plants. An operational permit is required for the operation and maintenance of a tire-rebuilding plant. |  |  |  |
| Waste handling. An operational permit is required for the operation of wrecking yards, junk yards and waste material-handling facilities. |  |  |  |
| Wood products. An operational permit is required to store chips, hogged material, lumber or plywood in excess of 200 cubic feet (6 m3). |  |  |  |

D. 107.3. Application for permit: Application for a permit shall be made on forms prescribed by the fire official.

E. 107.4. Issuance of permits: Before a permit is issued, the fire official shall make such inspections or tests as are necessary to assure that the use and activities for which application is made comply with the provisions of this code.

F. 107.5. Conditions of permit: A permit shall constitute permission to store or handle materials or to conduct processes in accordance with the SFPC, and shall not be construed as authority to omit or amend any of the provisions of this code. Permits shall remain in effect until revoked or for such period as specified on the permit. Permits are not transferable.

G. 107.5.1. Special conditions for the State Fire Marshal's Office: Permits issued by the State Fire Marshal's Office for the use of explosives in special operations or under emergency conditions shall be valid for one week from the date of issuance and shall not be renewable.

H. 107.6. State Fire Marshal: Permits will not be required by the State Fire Marshal except for the manufacturing, storage, handling, use, and sale of explosives in localities not enforcing the SFPC, and for the display of fireworks on state-owned property.

Exception: Such permits shall not be required for the storage of explosives or blasting agents by the Virginia Department of State Police provided notification to the State Fire Marshal is made annually by the Chief Arson Investigator listing all storage locations within areas where enforcement is provided by the State Fire Marshal's office.

I. 107.7. Annual: The enforcing agency may issue annual permits for the manufacturing, storage, handling, use, or sales of explosives to any state regulated public utility.

J. 107.8. Approved plans: Plans approved by the fire official are approved with the intent that they comply in all respects to this code. Any omissions or errors on the plans do not relieve the applicant of complying with all applicable requirements of this code.

K. 107.9. Posting: Issued permits shall be kept on the premises designated therein at all times and shall be readily available for inspection by the fire official.

L. 107.10. Suspension of permit: A permit shall become invalid if the authorized activity is not commenced within six months after issuance of the permit, or if the authorized activity is suspended or abandoned for a period of six months after the time of commencement.

M. 107.11. Revocation of permit: The fire official may revoke a permit or approval issued under the SFPC if conditions of the permit have been violated, or if the approved application, data or plans contain misrepresentation as to material fact.

N. 107.12. Local permit fees: Fees may be levied by the local governing body in order to defray the cost of enforcement and appeals under the SFPC.

O. 107.13. State explosives, blasting agents and fireworks permit fees: Fees for permits issued by the State Fire Marshal's office for the storage, use, sale or manufacture of explosives or blasting agents, and for the display of fireworks on state-owned property shall be as follows:

1. $100 per year per magazine to store explosives and blasting agents.

2. $150 per year per city or county to use explosives and blasting agents.

3. $150 per year to sell explosives and blasting agents.

4. $200 per year to manufacture explosives, blasting agents and fireworks.

5. $300 per day for fireworks, pyrotechnics or proximate audience displays conducted in any state-owned building and $150 per day for each subsequent day.

6. $200 per day for fireworks, pyrotechnics or proximate audience displays conducted out-of-doors on any state-owned property and $150 per day for each subsequent day.

7. $75 per event for the use of explosives in special operations or emergency conditions.

P. 107.14 State annual inspection permit fees. Annual fees for inspection permits issued by the State Fire Marshal's office for the inspection of buildings shall be as follows:

1. Nightclubs.

1.1. $350 for occupant load of 100 or less.

1.2. $450 for occupant load of 101 to 200.

1.3. $500 for occupant load of 201 to 300.

1.4. $500 plus $50 for each 100 occupants where occupant loads exceed 300.

2. Private schools (kindergarten through 12th grade) and private college dormitories with or without assembly areas. If containing assembly areas, such assembly areas are not included in the computation of square footage.

2.1. $150 for 3500 square feet or less.

2.2. $200 for greater than 3500 square feet up to 7000 square feet.

2.3. $250 for greater than 7000 square feet up to 10,000 square feet.

2.4. $250 plus $50 for each additional 3000 square feet where square footage exceeds 10,000.

3. Assembly areas that are part of private schools (kindergarten through 12th grade) or private college dormitories.

3.1. $50 for 10,000 square feet or less provided the assembly area is within or attached to a school or dormitory building.

3.2. $100 for greater than 10,000 square feet up to 25,000 square feet provided the assembly area is within or attached to a school or dormitory building, such as gymnasiums, auditoriums or cafeterias.

3.3. $100 for up to 25,000 square feet provided the assembly area is in a separate or separate buildings such as gymnasiums, auditoriums or cafeterias.

3.4. $150 for greater than 25,000 square feet for assembly areas within or attached to a school or dormitory building or in a separate or separate buildings such as gymnasiums, auditoriums or cafeterias.

4. Hospitals.

4.1. $300 for 1 to 50 beds.

4.2. $400 for 51 to 100 beds.

4.3. $500 for 101 to 150 beds.

4.4. $600 for 151 to 200 beds.

4.5. $600 plus $100 for each additional 100 beds where the number of beds exceeds 200.

Exception: Annual inspection permits for any building or groups of buildings on the same site may not exceed $2500.

Q. 107.15. Fee schedule: The local governing body may establish a fee schedule. The schedule shall incorporate unit rates, which may be based on square footage, cubic footage, estimated cost of inspection or other appropriate criteria.

R. 107.16. Payment of fees: A permit shall not be issued until the designated fees have been paid.

Exception: The fire official may authorize delayed payment of fees.

VA.R. Doc. No. R08-1376; Filed July 23, 2008, 12:08 p.m.