STATE WATER CONTROL BOARD

REGISTRAR'S NOTICE: The following regulations filed by the State Water Control Board are exempt from the Administrative Process Act in accordance with § 2.2-4006 A 9 of the Code of Virginia, which exempts general permits issued by the State Water Control Board pursuant to the State Water Control Law (§ 62.1-44.2 et seq.), Chapter 24 (§ 62.1-242 et seq.) of Title 62.1 and Chapter 25 (§ 62.1-254 et seq.) of Title 62.1 of the Code of Virginia if the board (i) provides a Notice of Intended Regulatory Action in conformance with the provisions of § 2.2-4007 B, (ii) following the passage of 30 days from the publication of the Notice of Intended Regulatory Action forms a technical advisory committee composed of relevant stakeholders, including potentially affected citizens groups, to assist in the development of the general permit, (iii) provides notice and receives oral and written comment as provided in § 2.2-4007 F, and (iv) conducts at least one public hearing on the proposed general permit.

Title of Regulation: 9 VAC 25-120. General Virginia Pollutant Discharge Elimination System (VPDES) Permit for Discharges From Petroleum Contaminated Sites and Hydrostatic Tests (amending 9 VAC 25-120-10, 9 VAC 25-120-20, 9 VAC 25-120-50 through 9 VAC 25-120-80; repealing 9 VAC 25-120-31).

Statutory Authority: § 62.1-44.15 of the Code of Virginia.

Effective Date: February 26, 2003.

Summary:

The amendments reissue the existing general permit, which expires on February 24, 2003. The general permit establishes limitations and monitoring requirements for point source discharges of wastewater from the clean up of sites contaminated by petroleum products and discharges of hydrostatic test waters. The general permit regulation is being reissued in order to continue to make it available after that date.

Agency Contact: Jon van Soestbergen, P.E., Environmental Manager II, Department of Environmental Quality, P.O. Box 10009, Richmond, VA 23240, telephone (804) 698-4117, FAX (804) 698-4032 or e-mail jvsoest@deq.state.va.us.

REGISTRAR'S NOTICE: The proposed regulation was adopted as published in 18:25 VA.R. 3428-3443 August 26, 2002, with the additional changes shown below. Therefore, pursuant to § 2.2-4031 A of the Code of Virginia, the text of the final regulation is not set out at length; however, the changes from the proposed regulation are printed below.

CHAPTER 120.
GENERAL VIRGINIA POLLUTANT DISCHARGE ELIMINATION SYSTEM (VPDES) PERMIT FOR DISCHARGES FROM PETROLEUM CONTAMINATED SITES AND HYDROSTATIC TESTS.

9 VAC 25-120-10. [ No change from proposed. ]

9 VAC 25-120-20. [ No change from proposed. ]

9 VAC 25-120-31. [ No change from proposed. ]

9 VAC 25-120-50. Effective date of the permit.

This general permit will become effective on February [ 24 26 ] , 1998 2003. This general permit will expire five years from the effective date. This general permit is effective as to any covered owner upon compliance with all the provisions of 9 VAC 25-120-60 and the receipt of this general permit.

9 VAC 25-120-60. [ No change from proposed. ]

9 VAC 25-120-70. [ No change from proposed. ]

9 VAC 25-120-80. General permit.

Any owner whose request for coverage under this general permit is accepted by the board shall comply with the requirements of the general permit and be subject to all requirements of 9 VAC 25-31-170 B of the VPDES permit regulation. Not all pages of Part I A of the general permit will apply to every permittee. The determination of which pages apply will be based on the type of contamination at the individual site and the nature of the waters receiving the discharge. Part I B and all pages of Part II apply to all permittees.

General Permit No.: VAG83

Effective Date: [ February 26, 2003 ]

Expiration Date: [ February 25, 2008 ]

GENERAL VPDES PERMIT FOR DISCHARGES FROM PETROLEUM CONTAMINATED SITES AND HYDROSTATIC TESTS

AUTHORIZATION TO DISCHARGE UNDER THE VIRGINIA POLLUTANT DISCHARGE ELIMINATION SYSTEM PERMIT PROGRAM AND THE VIRGINIA STATE WATER CONTROL LAW

In compliance with the provisions of the Clean Water Act, as amended, the State Water Control Law and regulations adopted pursuant thereto, the owner is authorized to discharge to surface waters at the locations identified in the accepted registration statement within the boundaries of the Commonwealth of Virginia, except to designated public water supplies or waters specifically named in other board regulations or policies which prohibit such discharges.

The authorized discharge shall be in accordance with this cover page, Part I--Effluent Limitations and Monitoring Requirements and Part II--Conditions Applicable to All VPDES Permits, as set forth herein.

If there is any conflict between the requirements of a Department of Environmental Quality approved cleanup plan and this permit, the requirements of this permit shall govern.

PART I

A. EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS.

1. GASOLINE CONTAMINATION--FRESHWATER RECEIVING WATERS.

During the period beginning with the permittee's coverage under this general permit and lasting until the permit's expiration date, the permittee is authorized to discharge to freshwater receiving waterbodies from outfall serial number XXXX. Samples taken in compliance with the monitoring requirements specified below shall be taken at the following location: outfall from the final treatment unit prior to mixing with any other waters.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS | DISCHARGE LIMITATIONS | MONITORING REQUIREMENTS |
| --- | --- | --- |
|  | Instantaneous Minimum | Instantaneous Maximum | Frequency | Sample Type |
| Flow (MGD) | NA | NL | 1/Month | Estimate |
| Benzene (µg/l) | NA | 50 | 1/Month | Grab* |
| Toluene (µg/l) | NA | 175 | 1/Month | Grab* |
| Ethylbenzene (µg/l) | NA | 320 | 1/Month | Grab* |
| Total xylenes (µg/l) | NA | 82 | 1/Month | Grab* |
| MTBE (methyl tert-butyl ether) (µg/l) | NA | NL | 1/Month | Grab* |
| pH (standard units) | 6.0 | 9.0 | 1/Month | Grab |
| Total recoverable lead* (µg/l) | NA | e(1.273(In hardness**)) -4.705 | 1/Month | Grab*** |
| Hardness (mg/l as CaCO3)* | NL | NA | 1/Month | Grab*** |

NL = No Limitation, monitoring required

NA = Not Applicable

* Benzene, Toluene, Ethylbenzene, Total Xylenes and MTBE shall be analyzed according to EPA Method 602 (40 CFR Part 136, 1996) or EPA SW 846 Method 8021B (1995 1998).

** Hardness of the effluent pH may be determined in the field using EPA Method 150.1 (EPA 600/4-87-020) or EPA SW 846 method 9040B.

*** Monitoring for this parameter is required only when contamination results from leaded fuel. Lead analysis shall be according to EPA Method 239.2 (40 CFR Part 136, 1996) or EPA SW 846 Method 7421 (1986 1998). There are no limits for hardness. The minimum hardness concentration that will be used to determine the lead effluent limit is [ 15 25 ] mg/l.

NOTICE: No further changes were made to this section; therefore, the remainder of 9 VAC 25-120-80 is not set out.

VA.R. Doc. No. R01-265; Filed January 8, 2003, 10:44 a.m.