Title of Regulation:  13 VAC 5-31. Amusement Device Regulations (amending 13 VAC 5-31-10-40, 13 VAC 5-31-10-50, 13 VAC 5-31-10-60, 13 VAC 5-31-10-90, [ 13 VAC 5-31-10-100 ]; 13 VAC 5-31-10-110 [ and 13 VAC 5-31-10-180; adding 13 VAC 5-31-190 ]).

Statutory Authority:  § 36-98.3 of the Code of Virginia.

# Effective Date:  October 1, 2003.

Agency Contact:  Stephen W. Calhoun, Regulatory Coordinator, Department of Housing and Community Development, 501 North Second Street, Richmond, VA 23219, telephone (804) 371-7015, FAX (804) 371-7090, or e-mail scalhoun@dhcd.state.va.us. Copies of the regulation may be obtained from the Department of Housing and Community Development.  There will be a $.10 charge per page for copies.

# Summary:

The amendments (i) clarify that the provisions of the Uniform Statewide Building Code shall apply to amusement devices to the extent such provisions are not superseded by the provisions of this regulation and § 36-98.3 of the Code of Virginia; (ii) update the incorporated by reference standards to the latest editions of the American National Standards Institute (ANSI) for the regulation of passenger tramways and the American Society for Testing and Materials (ASTM) for the regulation of amusement devices; (iii) regulate "go-karts" by the adoption of new referenced standards; (iv) allow appeals to the State Building Code Technical Review Board following a final determination by the local board of building code appeals; and (v) specify that the local building department's official or representative shall enforce the provisions of this regulation, including any interpretation of this regulation by the State Building Code Technical Review Board.

Summary of Public Comment and Agency Response:  A summary of comments made by the public and the agency's response may be obtained from the promulgating agency or viewed at the Office of the Registrar of Regulations.

REGISTRAR'S NOTICE: The proposed regulation was adopted as published in 19:6 VA.R. 913-916 December 2, 2002, with the changes identified below. Pursuant to § 2.2-4031 A of the Code of Virginia, the adopted regulation is not published at length; however, the sections that have changed since publication of the proposed are set out.

13 VAC 5-31-10 through 13 VAC 5-31-90. [ No change from proposed ].

# 13 VAC 5-31-100. Local building department.

The local building department's official or representative shall be permitted to do the following relative to an amusement device or devices intended to be, or being, operated at a site within their jurisdiction:

1. Collect fees for a permit to operate, renewal of a permit to operate and inspections conducted by staff to issue a certificate of inspection. The total for fees associated with one permit to operate and any associated inspections or one renewal of a permit to operate and any associated inspections shall not exceed the following:

a. $15 for each kiddie ride under the permit;

b. $25 for each circular ride or flat-ride under the permit which can be inspected from less than 20 feet above ground; and

c. $45 for each other type of amusement device under the permit.

Notwithstanding the above, the fee for each amusement device under the permit shall be reduced by 50% when the inspection for obtaining a certificate of inspection for that device is conducted by a private inspector [ , and shall not exceed a maximum of $150 for one site  ];

2. In addition to the above, require permits and charge fees as appropriate under the USBC for amusement devices which are being initially constructed in whole or in part at a site within the jurisdiction for intended operation at that site. This authorization does not apply to an amusement device which is only being reassembled or undergoing a major modification at a site or being moved to a site for operation;

3. Approve modifications of this chapter upon determination that the public health, safety and welfare are assured;

4. Conduct an inspection at any time when the device would normally be open for operation, or at any other time if permission is granted by the owner or operator, for compliance with this chapter; and

5. Issue an order to temporarily cease the operation of an amusement device upon determination that it may be unsafe or otherwise endanger the public. The temporary order shall remain in effect until a new certificate of inspection is issued.

# 13 VAC 5-31-110. [ No change from proposed. ]

[ 13 VAC 5-31-180. General requirements.

A. The provisions of this part are specific to gravity rides and are in addition to other applicable provisions of this chapter.

B. A ride using carriers shall be designed and constructed to retain the passengers in or on a carrier during the operation of the ride and retain the carrier on or within the track, slide, or chute system during the operation of the ride.

C. A ride that conveys passengers not in or on a carrier shall be designed and constructed to retain the passengers within the chute or slide during the ride.

D. At each loading or unloading area, a hard surface which is other than earth and which is reasonably level shall be provided. The surface shall be large enough to accommodate the intended quantity of passengers.

E. Where loading or unloading platforms are elevated more than 30 inches from the adjacent areas, guard rails conforming to the USBC shall be provided.

F. Passengers shall not have to step up or down more than 12 inches from the loading or unloading surface to enter or exit the ride.

G. The frequency of departure of carriers or riders from the loading areas shall be controlled by a ride operator. The minimum distance between departures shall be determined by the designer of the specific ride.

H. When a passenger has control of the speed or course of the carrier, the passenger shall have a clear sight distance along the course of the ride long enough to allow the passenger to avoid a collision with another person or carrier.

I. The unloading area of the ride shall be designed and constructed to bring riders and carriers to a safe stop without any action by the rider.

J. There shall be attendants at the loading and unloading area when the ride is in use. However, where the physical structure of the ride is such that it is not capable of accommodating an attendant at both the loading and unloading area and the entire ride is visible and under the supervision of a single attendant, attendants at both the loading and unloading areas shall not be required.

K. If the entire course of the ride is not visible to the operator, additional persons with communications equipment shall be provided or approved visual surveillance equipment shall be installed along the course of the ride which is not visible to the operator.

L. Any moving or hot parts that may be injurious to the ride operator or the public shall be effectively guarded to prevent contact.

M. Fencing or adequate clearance shall be provided that will prevent the riders from contact with persons or nearby objects.

# PART VI.

CONCESSION GO-KARTS.

# 13 VAC 5-31-190. General requirements.

Concession go-karts shall be operated, maintained and inspected in accordance with ASTM F2007-00. ]

VA.R. Doc. No. R02-171; Filed July 23, 2003, 10:08 a.m.