Title of Regulation: 13 VAC 5-51. Virginia Statewide Fire Prevention Code (amending 13 VAC 5-51-11, 13 VAC 5-51-21, 13 VAC 5-51-31, 13 VAC 5-51-41, 13 VAC 5-51-51, 13 VAC 5-51-61, 13 VAC 5-51-81, 13 VAC 5-51-91, 13 VAC 5-51-101, 13 VAC 5-51-111, 13 VAC 5-51-121, 13 VAC 5-51-130, 13 VAC 5-51-131, 13 VAC 5-51-133, 13 VAC 5-51-135, 13 VAC 5-51-136, 13 VAC 5-51-140, and 13 VAC 5-51-150; adding 13 VAC 5-51-85, 13 VAC 5-51-129, 13 VAC 5-51-132, and [ 13 VAC 5-51-155 ]; repealing 13 VAC 5-51-71, 13 VAC 5-51-160, 13 VAC 5-51-170, 13 VAC 5-51-180, 13 VAC 5-51-181, 13 VAC 5-51-182, 13 VAC 5-51-190, and 13 VAC 5-51-200).

Statutory Authority: § 27-97 of the Code of Virginia.

# Effective Date: October 1, 2003.

Agency Contact: Stephen W. Calhoun, Regulatory Coordinator, Department of Housing and Community Development, 501 North 2nd Street, Richmond, VA 23219, telephone (804) 371-7015, FAX (804) 371-7090 or e-mail scalhoun@dhcd.state.va.us. Copies of the regulation may be obtained from the Department of Housing and Community Development. There will be a $.10 charge per page for copies.

# Summary:

The major substantive amendments to this regulation (i) update the referenced model codes and standards; (ii) add that the official must notify the Department of Housing and Community Development (department) of the employment of assistants; (iii) change from three years to one and a half years the time allowed for enforcement personnel to become certified; (iv) add that officials and assistants may be held responsible for failure to discharge any duty required by law; (v) add that fire apparatus access roads be identified to the owner prior to the issuance of the building permit; (vi) amend the permit fees of the State Fire Marshal's office for the storage, use, sale or manufacture of explosives or blasting agents, and for the display of fireworks on state-owned property; (vii) add a fee for obtaining or renewing a background clearance card from the department; and (viii) amend the fee for obtaining or renewing a blaster certificate from the department.

Changes to the proposed regulation include revised enforcement provisions and coverage of additional fire-related subjects (including fireworks, fire drills and black powder).

PART I.
GENERAL REGULATIONS.

13 VAC 5-51-11. Chapter 1, Administration, Section F-101.0. Scope.

A. F-101.1. Title: These regulations shall be known as the Virginia Statewide Fire Prevention Code (SFPC), hereinafter referred to as "this code" or "SFPC." The term "chapter" means a chapter in the SFPC. The SFPC was cooperatively developed by the Virginia Fire Services Board and the Virginia Board of Housing and Community Development.

B. F-101.2. Scope: The SFPC prescribes regulations affecting or relating to maintenance of structures, processes and premises and safeguards to be complied with for the protection of life and property from the hazards of fire or explosion and for the handling, storage and use of [ fireworks, ] explosives or blasting agents, and provides for the administration and enforcement of such regulations. The SFPC requires manufacturers of explosives to register and report information concerning their manufacturing facilities and methods of operation within this Commonwealth in accordance with the SFPC. The SFPC also establishes regulations for obtaining permits for the manufacturing, storage, handling, use, or sales of explosives. Inspections under the SFPC are a governmental responsibility.

C. F-101.3. Purpose: The purposes of the SFPC are to provide for statewide standards for optional local enforcement to safeguard life and property from the hazards of fire or explosion arising from the improper maintenance of life safety and fire prevention and protection materials, devices, systems and structures, and the unsafe storage, handling, and use of substances, materials and devices, including explosives and blasting agents, wherever located.

D. F-101.4. Validity: To the extent that any provisions of the SFPC or the referenced codes or standards are not within the scope of this chapter, those provisions are considered to be invalid. When any provision of the SFPC is found to be in conflict with the USBC, OSHA, or statute, that provision of the SFPC shall become invalid.

E. F-101.5. Local regulations: Any local governing body may adopt fire prevention regulations that are more restrictive or more extensive in scope than the SFPC provided such regulations are not more restrictive than the USBC and do not affect the manner of construction or materials to be used in the erection, alteration, repair, or use of a building or structure, as provided in the USBC, including the voluntary installation of smoke alarms and regulation and inspections thereof in commercial buildings where such smoke alarms are not required under the provisions of the SFPC.

F. F-101.6. Exemption Nonresidential farm structures: Farm structures not used for residential purposes are exempt from the SFPC except when the inspection and enforcement provisions of the code are exercised by a warrant issued under the authority of §§ 27-98.2 through 27-98.5 of the Code of Virginia.

Exception: Inspections or reinspections of farm buildings, structures, property, or premises under search warrants issued pursuant to § 27-98.2 of the Code of Virginia are not exempt from the SFPC. When they are based upon a demonstration that, for the protection of life and property from the hazards of fire or explosion, the alleged unsafe storage, handling and use of substances, materials and devices, including explosives and blasting agents, are probably occurring on such premises.

# 13 VAC 5-51-21. Section F-102.0. Applicability.

A. F-102.1. General: The provisions of the SFPC shall apply to all matters affecting or relating to structures, processes and premises as set forth in Section F-101.0. The SFPC shall supersede any fire prevention regulations previously adopted by a local government or other political subdivision.

B. 102.1.1. Changes: No change shall be made in the use or occupancy of any structure that would place the structure in a different division of the same group of occupancies, unless such structure is made to comply with the requirements of this code and the USBC.

B. F- C. 102.2. Application to pre-1973 buildings and structures: Buildings and structures constructed prior to the USBC (1973) shall comply with the maintenance requirements of the SFPC to the extent that equipment, systems, devices, and safeguards which were [ required, ] provided and approved when constructed shall be maintained. Such buildings and structures, if subject to the state fire and public building regulations (Virginia Public Building Safety Regulations, VR 394-01-05) in effect prior to March 31, 1986, shall also be maintained in accordance with those regulations.

C. F- D. 102.3. Application to post-1973 buildings and structures: Buildings and structures constructed under any edition of the USBC shall comply with the maintenance requirements of the SFPC to the extent that equipment, systems, devices, and safeguards which were [ required, ] provided and approved when constructed shall be maintained.

E. 102.4. Referenced codes and standards: The codes and standards referenced in the IFC shall be those listed in Chapter 45 and considered part of the requirements of the SFPC to the prescribed extent of each such reference. Where differences occur between the provisions of this code and the referenced standards, the provisions of this code shall apply.

D. F-102.4. F. 102.5. Subsequent alteration: Subsequent alteration, enlargement, repair, or conversion of the occupancy classification of structures shall be subject to the current USBC.

E. F-102.5. G. 102.6. State structures: The SFPC shall be applicable to all state-owned structures in the manner and extent described in § 27-99 of the Code of Virginia.

F. F-102.6. H. 102.7. Relationship to USBC: Construction inspections of structures, other than state-owned structures, and the review and approval of their construction documents for enforcement of the USBC shall be the sole responsibility of the local building department.

G. F-102.7. I. 102.8. Existing structures: Upon the completion of structures [ and after the certificate of occupancy has been issued ], responsibility for fire safety protection shall pass to the local fire code official or to the State Fire Marshal, who shall also have the authority, in cooperation with any local governing body, to enforce this code [ and who shall also determine that the fire safety features approved by the building official are properly maintained ]. The State Fire Marshal shall also have authority to enforce this code in those jurisdictions in which the local governments do not enforce this code. [ The State Fire Marshal shall also have authority to enforce this code in those jurisdictions in which the local governments do not enforce this code. ]

H. F-102.8. J. 102.9. Inspections for USBC requirements: The fire code official shall require that [ The fire official shall require that ] existing structures subject to the requirements of the applicable retrofitting provisions relating to [ the ] fire protection equipment and system requirements [ for certain existing motels, hotels, hospitals, daycare facilities, dormitories, nursing homes and multi-family dwelling units mandated in Part II, Article 3 ] of the USBC subsections 3402.3, 3402.4, 3402.5, 3402.6, 3402.6.1, 3402.7, 3402.10, 3402.12, 3402.13, 3402.14 and 3402.15 comply with the provisions of those subsections, [ that do not comply with such provisions, the fire official shall notify the building official, in writing, of those structures that are in alleged violation of such provisions Section 123, comply with the provisions located therein ].

13 VAC 5-51-31. Section F-103.0. Incorporation by reference.

A. F-103.1. General: The following document is adopted and incorporated by reference to be an enforceable part of the SFPC:

The BOCA National Fire Prevention Code/1996, Tenth Edition International Fire Code/2000, hereinafter referred to as "BNFPC IFC," published by Building Officials and Code Administrators International, Inc., 4051 West Flossmoor Road, Country Club Hills, IL 60478-5795, toll free number 1-800-323-1103 the International Code Council, Inc., 5203 Leesburg Pike, Suite 708, Falls Church, VA 22041-3401, phone 703-931-4533.

B. F-103.1.1. Deletion: Delete BNFPC IFC Chapter 1.

C. F-103.2. Amendments: All requirements of the referenced codes and standards that relate to fees, permits, unsafe notices, disputes, condemnation, inspections, scope of enforcement and all other procedural, and administrative matters are deleted and replaced by the provisions of Chapter 1 of the SFPC. The purpose of this provision is to eliminate overlap, conflict and duplication by providing a single standard for administration, procedural matters and enforcement of the SFPC.

D. F-103.2.1. Other amendments: The SFPC contains provisions adopted by the Virginia Board of Housing and Community Development (BHCD), some of which delete, change or amend provisions of the BNFPC IFC and referenced standards. Where conflicts occur between such changed provisions and the unchanged provisions of the BNFPC IFC and referenced standards, the provisions changed by the BHCD shall govern.

Note: The BNFPC IFC and its referenced standards contain some areas of regulation outside of the scope of the SFPC, as established by the BHCD and under state law. Where conflicts have been readily noted, changes have been made to the BNFPC IFC and its referenced standards to bring it within the scope of authority; however, in some areas, judgment will have to be made as to whether the provisions of the BNFPC IFC and its referenced standards are fully applicable.

E. 103.3. International Fire Code. Retroactive fire protection system requirements contained in the IFC shall not be enforced unless specified by the USBC [ , including but not limited to the following IFC sections: 903, 905 and 907 ].

# 13 VAC 5-51-41. Section F-104.0. Enforcement.

A. F-104.1. Local enforcement: Any local government may enforce the SFPC following official action by such body. The official action shall (i) require compliance with the provisions of the SFPC in its entirety or with respect only to those provisions of the SFPC relating to open burning, fire lanes, fireworks, and hazardous materials and (ii) assign enforcement responsibility to the local agency or agencies of its choice. Any local governing body may establish such procedures or requirements as may be necessary for the administration and enforcement of this code. If a local governing body elects to enforce only those provisions of the SFPC relating to open burning, it may do so in all or in any designated geographic areas of its jurisdiction. The terms "enforcing agency" and "fire code official" are intended to apply to the agency or agencies to which responsibility for enforcement of the SFPC has been assigned. The terms "building code official" or "building department" are intended to apply only to the local building code official or local building department.

B. F-104.1.1. Procedures: Any local governing body shall be permitted to establish such procedures or requirements as may be necessary for the administration and enforcement of this code.

C. F- B. 104.2. State enforcement: The State Fire Marshal shall have the authority to enforce the SFPC as follows:

1. In cooperation with any local governing body;

2. In those jurisdictions in which the local governments do not enforce the SFPC [ in its entirety or enforce the SFPC with respect only to those provisions of the SFPC relating to open burning, fire lanes, fireworks, and hazardous materials ]; and

3. In all state-owned buildings and structures.

D. F- C. 104.3. State structures: Every agency, commission or institution of this Commonwealth, including all institutions of higher education, shall permit, at all reasonable hours, the fire code official reasonable access to existing structures or a structure under construction or renovation, for the purpose of performing an informational and advisory fire safety inspection. The fire code official is permitted to submit, subsequent to performing such inspection, his findings and recommendations, including a list of corrective actions necessary to ensure that such structure is reasonably safe from the hazards of fire, to the appropriate official of such agency, commission, or institution and the State Fire Marshal. Such agency, commission or institution shall notify, within 60 days of receipt of such findings and recommendations, the State Fire Marshal and the fire code official of the corrective measures taken to eliminate the hazards reported by the fire code official. The State Fire Marshal shall have the same power in the enforcement of this section as is provided for in § 27-98 of the Code of Virginia. The State Fire Marshal may enter into an agreement as is provided for in § 36-139.4 of the Code of Virginia with any local enforcement agency that enforces the SFPC to enforce this section and to take immediate enforcement action upon verification of a complaint of an imminent hazard such as a chained or blocked exit door, improper storage of flammable liquids, use of decorative materials, and overcrowding.

# 13 VAC 5-51-51. Section 105.0. Enforcing agency.

A. F-105.1. Code Fire official: Each enforcing agency shall have an executive official in charge, hereinafter referred to as the "fire code official" or "code official." [ In accordance with sanctions prescribed by the Virginia Certification Standards (13 VAC 5-21), the fire official may be held responsible for failure to discharge any duty required by law or by the SFPC. ]

[ Note: Fire officials are subject to sanctions in accordance with the Virginia Certification Standards (13 VAC 5-21). ]

B. F-105.1.1. Appointment: The fire code official shall be appointed in a manner selected by the local government having jurisdiction. After permanent appointment, the fire code official shall not be removed from office except for cause after having been afforded a full opportunity to be heard on specific and relevant charges by and before the appointing authority.

C. F-105.1.2. Notification of appointment: The appointing authority of the local governing body shall notify the DHCD within 30 days of the appointment or release of a the permanent or acting fire code official within 30 days after such appointment.

D. F-105.1.3. Qualifications: The fire code official shall have at least five years of fire-related experience as a licensed professional engineer or architect, fire inspector, contractor or superintendent of fire protection-related construction, with at least three years in responsible charge of work. Any combination of education and experience that would confer equivalent knowledge and ability shall be deemed to satisfy this requirement. The fire code official shall have general knowledge of sound engineering practice with respect to the design and construction of structures, the basic principles of fire prevention and protection, the accepted requirements for means of egress and the installation of elevators and other service equipment necessary for the health, safety and general welfare of the occupants and the public. The local governing body may establish additional qualification requirements.

E. F-105.2. Certification: The permanent or acting fire code official shall obtain certification from the BHCD in accordance with the Virginia Certification Standards (13 VAC 5-21-10 et seq.) within three years one year after permanent or acting appointment.

Exception: A fire code official appointed prior to April 1, 1994, continuously employed by the same local governing body as the fire code official shall comply with required DHCD training under the Virginia Certification Standards (13 VAC 5-21-10 et seq.).

F. F-105.2.1. Noncertified: After permanent or acting appointment, a non-BHCD certified fire code official shall complete a DHCD orientation seminar within 60 days. In addition, within 180 days, such code fire official shall attend the core program of the Virginia Building Code Academy or its equivalent in a DHCD accredited academy.

G. F-105.3. Assistant: The local governing body or its designee may appoint one or more assistants who, in the absence of the fire code official, shall have the powers and perform the duties of the fire code official. [ In accordance with sanctions prescribed by the Virginia Certification Standards (13 VAC 5-21) such assistants may be held responsible for failure to discharge any duty required by law or by the SFPC. ]

[ Note: Assistants are subject to sanctions in accordance with the Virginia Certification Standards (13 VAC 5-21). ]

H. F-105.3.1. Notification: The fire official shall notify the DHCD within 60 days of the employment [ or , ] contract [ or termination ] of all assistants for enforcement of the SFPC.

I. 105.3.2. Certification: Any person All assistants employed by or under contract to an enforcing agency for enforcing the SFPC shall be certified in the appropriate subject areas area in accordance with the Virginia Certification Standards (13 VAC 5-21-10 et seq.) within three one and one-half years after permanent or acting appointment. [ However, such assistants shall also attend and complete the applicable management, technical or DFP training as outlined in the training and certification guidance document referenced in the Virginia Certification Standards (13 VAC 5-21) within one and one-half years after initial appointment. When required by a locality to have two or more certifications, the remaining certifications shall be obtained within three years from the date of such requirement. ]

Exception: Any person assistant continuously employed by or continuously under contract to the same enforcing agency for enforcing the SFPC since before April 1, 1994, shall be exempt from the provisions of this [ subsection section ]; however, such exempt person assistant shall comply with required DHCD training under Virginia Certification Standards (13 VAC 5-21-10 et seq.).

I. F- J. 105.4. Continuing education: Code Fire officials and assistants enforcing the SFPC shall attend periodic training courses as designated by the DHCD and such other training as designated by the local governing body.

J. F- K. 105.5. Control of conflict of interest: The minimum standards of conduct for officials and employees of the enforcing agency shall be in accordance with the provisions of the State and Local Government Conflict of Interests Act, Chapter 40.1 31 (§ 2.1-639.1 2.2-3100 et seq.) of Title 2.1 2.2 of the Code of Virginia.

13 VAC 5-51-61. Section F-106.0. Duties and powers of the code fire official.

A. F-106.1. General: The fire code official shall enforce the provisions of the SFPC as provided herein and as interpreted by the State Building Code Technical Review Board (TRB) in accordance with § 36-118 of the Code of Virginia.

B. F-106.2. Delegation of duties and powers: The fire code official may delegate duties and powers subject to any limitations imposed by the local governing body. The fire code official shall be responsible that any powers and duties delegated are carried out in accordance with this code.

C. F-106.3. Inspections: The fire code official may make all of the required is authorized to conduct such inspections or may accept reports of inspections as are deemed necessary to determine the extent of compliance with the provisions of this code and to approve reports of inspection by approved agencies or individuals. All reports of such inspections [ by approved agencies or individuals ] shall be prepared and submitted in writing and for review and approval. Inspection reports shall be certified by an agency a responsible officer of such approved agency or by the responsible individual. The code fire official may is authorized to engage, subject to any limitations imposed by the local governing body, such expert opinion as deemed necessary to report upon unusual, detailed or complex technical issues that arise [ subject to the approval of the governing body in accordance with local policies ].

D. F-106.3.1. Observations: When, during an inspection, the fire code official or an authorized representative observes an apparent or actual violation of another law, ordinance or code not within the official's authority to enforce, such official shall report the findings to the official having jurisdiction in order that such official may institute the necessary measures.

E. F-106.4. Alternatives: The SFPC provisions are not intended to prevent the use of any safeguards used to protect life and property from the hazards of fire or explosion that are not specifically prescribed by the SFPC, provided that such alternative safeguards comply with the intent of the SFPC. The alternative safeguard offered shall be, for the purpose intended, at least the equivalent of that prescribed in this code in quality, strength, effectiveness, fireresistance, durability and safety.

F. F-106.5. Modifications: The fire code official may grant modifications to any provision of the SFPC upon application by the owner or the owner's agent provided the spirit and intent of the SFPC are observed and public health, welfare, and safety are assured.

G. F-106.5.1. Supporting data: The fire code official shall require that sufficient technical data be submitted to substantiate the proposed use of any alternative. If it is determined that the evidence presented is satisfactory proof of performance for the use intended, the fire code official shall approve the use of such alternative subject to the requirements of this code. The fire code official may require and consider a statement from a professional engineer, architect or other competent person as to the equivalency of the proposed modification.

H. F-106.5.2. Records Decision: The application for modification and the final decision of the fire [ code ] official shall be in writing and shall be recorded in the permanent records of the local enforcing agency.

I. F-106.5.3. Supporting data: The fire code official shall require that sufficient technical data be submitted to substantiate the proposed use of any alternative. If it is determined that the evidence presented is satisfactory proof of performance for the use intended, the fire code official shall approve the use of such alternative subject to the requirements of this code. Supporting data, when required by the fire code official to assist in the approval of all materials or assemblies not specifically provided for in this code, shall consist of duly authenticated research reports from approved sources.

J. F- I. 106.6. Notices and orders: The fire code official shall issue all necessary notices or orders to ensure compliance with the SFPC.

K. F- J. 106.7. Department records: The fire code official shall keep official records of applications received, permits and certificates issued, fees collected, reports of inspections, and notices and orders issued. Such records shall be retained in the official records or disposed of in accordance with General Schedule Number Ten available from The Library of Virginia.

# 13 VAC 5-51-71. Section F-107.0. Fees. (Repealed.)

A. F-107.1. Local: Fees may be levied by the local governing body in order to defray the cost of enforcement and appeals under the SFPC.

B. F-107.2. State: Fees for permits issued by the State Fire Marshal's office shall be as follows:

1. $50 per year per site to possess, store and dispose of explosives and blasting agents.

2. $75 per year per city or county to use explosives and blasting agents.

3. No fee for the manufacture and sale of fireworks, explosives and blasting agents.

C. F-107.2.1. Additional fees: The applicant shall pay all additional fees charged by other agencies for fingerprinting and for obtaining a national criminal history record check through the Central Criminal Records Exchange to the Federal Bureau of Investigation.

D. F-107.3. Fee schedule: The local governing body may establish a fee schedule. The schedule shall incorporate unit rates, which may be based on square footage, cubic footage, estimated cost of inspection or other appropriate criteria.

E. F-107.4. Payment of fees: A permit shall not be issued until the designated fees have been paid.

Exception: The fire code official may authorize delayed payment of fees.

# 13 VAC 5-51-81. Section F-108.0. 107.0. Permits.

A. F-108.1. 107.1. Prior notification: The fire code official may require notification prior to (i) activities involving the handling, storage or use of substances, materials or devices regulated by the SFPC; (ii) conducting processes which produce conditions hazardous to life or property; or (iii) establishing a place of assembly.

B. F-108.2. 107.2. Permits required: Permits may be required by the code fire official as permitted under the SFPC in accordance with Table F-108.2 107.2, except that the fire code official shall require permits for the manufacturing, storage, handling, use, and sale of explosives. An application for a permit to manufacture, store, handle, use, or sell explosives shall only be made by an individual certified as a blaster in accordance with Section F-3003.5 3301.4, or by a person who has been issued a background clearance card in accordance with Section F-3001.2.3.1 [ 3301.1 3301.2.3.1.1 ].

Exception: Such permits shall not be required for the storage, handling, or use of explosives or blasting agents by the Virginia Department of State Police provided notification to the fire code official is made annually by the Chief Arson Investigator listing all storage locations.

Table F-108.2
PERMIT REQUIREMENTS
(to be filled in by local jurisdiction)

| Section | Description | Permit required | Permit fee | Inspection fee |
| --- | --- | --- | --- | --- |
| F-402.3 | Candles - assembly/educational occupancies |  |  |  |
| F-403.4 | Open burning |  |  |  |
| F-404.2 | Remove paint with torch |  |  |  |
| F-601.4 | Assembly/educational occupancies |  |  |  |
| F-801.2 | Airports, heliports & helistops |  |  |  |
| F-901.2 | Flammable liquids, bowling lanes |  |  |  |
| F-1001.2 | Crop ripening & color processes |  |  |  |
| F-1101.2 | Dry cleaning |  |  |  |
| F-1201.2 | Dust explosion hazard |  |  |  |
| F-1301.2 | Flammable finishes |  |  |  |
| F-1401.2 | Fumigation - insecticidal |  |  |  |
| F-1501.2 | HPM facilities |  |  |  |
| F-1601.2 | Lumber yard - woodworking plants |  |  |  |
| F-1701.2 | Matches - bulk storage |  |  |  |

| F-1801.2 | Oil/gas wells |  |  |  |
| --- | --- | --- | --- | --- |
| F-1901.2 | Organic coatings |  |  |  |
| F-2001.2 | Tents/air-supported structures |  |  |  |
| F-2102.1 | Wrecking yard, junk yard, waste material-handling |  |  |  |
| F-2103.1 | Waste handling |  |  |  |
| F-2201.2 | Welding or cutting |  |  |  |
| F-2205.2 | Storage of welding cylinders |  |  |  |
| F-2207.1 | Calcium carbide |  |  |  |
| F-2208.1 | Acetylene generators |  |  |  |
| F-2208.7 | Acetylene cylinder storage |  |  |  |
| F-2301.2 | Hazardous materials |  |  |  |
| F-2401.2 | Aerosol products |  |  |  |
| F-2501.2 | Cellulose nitrate plastics |  |  |  |
| F-2601.2 | Combustible fibers |  |  |  |
| F-2701.2 | Compressed gases |  |  |  |
| F-2801.2 | Corrosives |  |  |  |
| F-2901.2 | Cryogenic liquids |  |  |  |
| F-3001.2 | Blasting/explosives |  |  |  |
| F-3101.2 | Fireworks |  |  |  |
| F-3201.2 | Vehicle repair shop |  |  |  |
| F-3201.2 | Flammable and combustible liquids - storage, handling, use, processing |  |  |  |
| F-3201.2 | Flammable and combustible liquids - tanks and equipment |  |  |  |
| F-3301.2 | Flammable solids |  |  |  |
| F-3401.2 | Highly toxic and toxic solids and liquids |  |  |  |
| F-3501.2 | Irritants, sensitizers and other health hazards |  |  |  |
| F-3601.2 | Liquefied petroleum gases |  |  |  |
| F-3701.2 | Organic peroxides |  |  |  |
| F-3801.2 | Liquid and solid oxidizers |  |  |  |
| F-3901.2 | Pesticides |  |  |  |
| F-4001.2 | Pyrophoric materials |  |  |  |
| F-4101.2 | Radioactive materials |  |  |  |
| F-4201.2 | Unstable (reactive) materials |  |  |  |
| F-4301.2 | Water-reactive materials |  |  |  |

Table 107.2.
OPERATIONAL PERMIT REQUIREMENTS (to be filled in by local jurisdiction).

| Description [ An operational permit may be required by the fire official: ] | Permit Required (yes or no) | Permit fee | Inspection fee |
| --- | --- | --- | --- |
| [ Aerosol products. An operational permit is required ] to manufacture, store or handle an aggregate quantity of Level 2 or Level 3 aerosol products in excess of 500 pounds (227 kg) net weight. |  |  |  |
| [ Amusement buildings. An operational permit is required ] to operate a special amusement building. |  |  |  |
| [ Aviation facilities. An operational permit is required ] to use a Group H or Group S occupancy for aircraft servicing or repair and aircraft fuel-servicing vehicles. Additional permits required by other sections of this code include, but are not limited to, hot work, hazardous materials and flammable or combustible finishes. |  |  |  |
| [ Carnivals and fairs. An operational permit is required ] to conduct a carnival or fair. |  |  |  |
| [ Battery systems. An operational permit is required ] to install stationary lead-acid battery systems having a liquid capacity of more than 50 gallons (189 L). |  |  |  |
| [ Cellulose nitrate film. An operational permit is required ] to store, handle or use cellulose nitrate film in a Group A occupancy. |  |  |  |

| [ Combustible dust-producing operations. An operational permit is required ] to operate a grain elevator, flour starch mill, feed mill, or a plant pulverizing aluminum, coal, cocoa, magnesium, spices or sugar, or other operations producing combustible dusts as defined in Chapter 2. |  |  |  |
| --- | --- | --- | --- |
| [ Combustible fibers. An operational permit is required ] for the storage and handling of combustible fibers in quantities greater than 100 cubic feet (2.8 m3). Exception: An operational permit is not required for agricultural storage. |  |  |  |
| [ Compressed gas. An operational permit is required ] for the storage, use or handling at normal temperature and pressure (NTP) of compressed gases in excess of the amounts listed below. Exception: Vehicles equipped for and using compressed gas as a fuel for propelling the vehicle. Permit Amounts for Compressed Gases Type of Gas Amount (cubic feet at NTP) Corrosive 200 Flammable (except cryogenic 200 fluids and liquefied petroleum gases) Highly toxic Any Amount Inert and simple asphyxiant 6,000 Oxidizing (including oxygen) 504 Toxic Any Amount For SI: 1 cubic foot = 0.02832 m3. |  |  |  |
| [ Covered mall buildings. An operational permit is required ] for: 1. The placement of retail fixtures and displays, concession equipment, displays of highly combustible goods and similar items in the mall. 2. The display of liquid- or gas-fired equipment in the mall. 3. The use of open-flame or flame-producing equipment in the mall. |  |  |  |
| [ Cryogenic fluids. An operational permit is required ] to produce, store, transport on site, use, handle or dispense cryogenic fluids in excess of the amounts listed below. Exception: Operational permits are not required for vehicles equipped for and using cryogenic fluids as a fuel for propelling the vehicle or for refrigerating the lading. Permit Amounts for Cryogenic Fluids Inside Building Outside Building Type of Cryogenic Fluid (gallons) (gallons) Flammable More than 1 60 Inert 60 500 Oxidizing (includes oxygen) 10 50 Physical or health hazard Any Amount Any Amount not indicated above For SI: 1 gallon = 3.785 L. |  |  |  |
| [ Cutting and welding. An operational permit is required ] to conduct cutting or welding operations within the jurisdiction. |  |  |  |
| [ Dry cleaning plants. An operational permit is required ] to engage in the business of dry cleaning or to change to a more hazardous cleaning solvent used in existing dry cleaning equipment. |  |  |  |
| [ Exhibits and trade shows. An operational permit is required ] to operate exhibits and trade shows. |  |  |  |
| [ Explosives. An operational permit is required ] for the manufacture, storage, handling, sale or use of any quantity of explosive, explosive material, fireworks, or pyrotechnic special effects within the scope of Chapter 33. |  |  |  |
| [ Fire hydrants and valves. An operational permit is required ] to use or operate fire hydrants or valves intended for fire suppression purposes that are installed on water systems and accessible to a fire apparatus access road that is open to or generally used by the public. Exception: An operational permit is not required for authorized employees of the water company that supplies the system or the fire department to use or operate fire hydrants or valves. |  |  |  |
| [ Flammable and combustible liquids. An operational permit is required: ] 1. To use or operate a pipeline for the transportation within facilities of flammable or combustible liquids. This requirement shall not apply to the offsite transportation in pipelines regulated by the Department of Transportation (DOTn) (see § 3501.1.2) nor does it apply to piping systems (see § 3503.6). 2. To store, handle or use Class I liquids in excess of 5 gallons (19 L) in a building or in excess of 10 gallons (37.9 L) outside of a building, except that a permit is not required for the following: 2.1. The storage or use of Class I liquids in the fuel tank of a motor vehicle, aircraft, motorboat, mobile power plant or mobile heating plant, unless such storage, in the opinion of the fire official, would cause an unsafe condition. 2.2. The storage or use of paints, oils, varnishes or similar flammable mixtures when such liquids are stored for maintenance, painting or similar purposes for a period of not more than 30 days. 3. To store, handle or use Class II or Class IIIA liquids in excess of 25 gallons (95 L) in a building or in excess of 60 gallons (227 L) outside a building, except for fuel oil used in connection with oil-burning equipment. 4. To remove Class I or Class II liquids from an underground storage tank used for fueling motor vehicles by any means other than the approved, stationary on-site pumps normally used for dispensing purposes. 5. To operate tank vehicles, equipment, tanks, plants, terminals, wells, fuel-dispensing stations, refineries, distilleries and similar facilities where flammable and combustible liquids are produced, processed, transported, stored, dispensed or used. 6. To install, alter, remove, abandon, place temporarily out of service (for more than 90 days) or otherwise dispose of an underground, protected above-ground or above-ground flammable or combustible liquid tank. 7. To change the type of contents stored in a flammable or combustible liquid tank to a material that poses a greater hazard than that for which the tank was designed and constructed. 8. To manufacture, process, blend or refine flammable or combustible liquids. |  |  |  |
| [ Floor finishing. An operational permit is required ] for floor finishing or surfacing operations exceeding 350 square feet (33 m2) using Class I or Class II liquids. |  |  |  |
| [ Floor finishing. An operational permit is required ] for floor finishing or surfacing operations exceeding 350 square feet (33 m2) using Class I or Class II liquids. |  |  |  |
| [ Fumigation and thermal insecticidal fogging. An operational permit is required ] to operate a business of fumigation or thermal insecticidal fogging and to maintain a room, vault or chamber in which a toxic or flammable fumigant is used. |  |  |  |
| [ Hazardous materials. An operational permit is required ] to store, transport on site, dispense, use or handle hazardous materials in excess of the amounts listed below. Permit Amounts for Hazardous Materials Type of Material Amount Combustible liquids see flammable and combustible liquids Corrosive materials Gases see [ covered mall buildings compressed gases ] Liquids 55 gallons Solids 1000 pounds Explosive materials see explosives Flammable materials Gases see [ covered mall buildings compressed gases ] Liquids see flammable and combustible liquids Solids 100 pounds Highly toxic materials Gases see [ covered mall buildings compressed gases ] Liquids Any Amount Solids Any Amount Oxidizing materials Gases see [ covered mall buildings compressed gases ] Liquids Class 4 Any Amount Class 3 1 gallon Class 2 10 gallons Class 1 55 gallons Solids Class 4 Any Amount Class 3 10 gallons Class 2 100 pounds Class 1 500 pounds Organic peroxides Liquids Class I Any Amount Class II Any Amount Class III 1 gallon Class IV 2 gallons Class V No Permit Required Solids Class I Any Amount Class II Any Amount Class III 10 pounds Class IV 20 pounds Class V No Permit Required Pyrophoric materials Gases see [ flammable and combustible liquids compressed gases ] Liquids Any Amount Solids Any Amount Toxic materials Gases see [ covered mall buildings compressed gases ] Liquids 10 gallons Solids 100 pounds Unstable (reactive) materials Liquids Class 4 Any Amount Class 3 Any Amount Class 2 5 gallons Class 1 10 gallons Solids Class 4 Any Amount Class 3 Any Amount Class 2 50 pounds Class 1 100 pounds Water-reactive Materials Liquids Class 3 Any Amount Class 2 5 gallons Class 1 55 gallons Solids Class 3 Any Amount Class 2 50 pounds Class 1 500 pounds For SI: 1 gallon = 3.785 L, 1 pound = 0.454 kg. |  |  |  |
| [ HPM facilities. An operational permit is required ] to store, handle or use hazardous production materials. |  |  |  |
| [ High piled storage. An operational permit is required ] to use a building or portion thereof as a high-piled storage area exceeding 500 square feet (46 m2). |  |  |  |
| [ Hot work operations. An operational permit is required ] for hot work including, but not limited to: 1. Public exhibitions and demonstrations where hot work is conducted. 2. Use of portable hot work equipment inside a structure. Exception: Work that is conducted under a construction permit. 3. Fixed-site hot work equipment such as welding booths. 4. Hot work conducted within a hazardous fire area. 5. Application of roof coverings with the use of an open-flame device. 6. When approved, the fire official shall issue a permit to carry out a Hot Work Program. This program allows approved personnel to regulate their facility's hot work operations. The approved personnel shall be trained in the fire safety aspects denoted in this chapter and shall be responsible for issuing permits requiring compliance with the requirements found in this chapter. These permits shall be issued only to their employees or hot work operations under their supervision. |  |  |  |
| [ Industrial ovens. An operational permit is required ] for operation of industrial ovens regulated by Chapter 21. |  |  |  |
| [ Lumber yards and woodworking plants. An operational permit is required ] for the storage or processing of lumber exceeding 100,000 board feet (8,333 ft3) (236 m3). |  |  |  |
| [ Liquid- or gas-fueled vehicles or equipment in assembly buildings. An operational permit is required ] to display, operate or demonstrate liquid- or gas-fueled vehicles or equipment in assembly buildings. |  |  |  |
| [ LP-gas. An operational permit is required ] for: 1. Storage and use of LP-gas. Exception: An operational permit is not required for individual containers with a 500-gallon (1893 L) water capacity or less serving occupancies in Group R-3. 2. Operation of cargo tankers that transport LP-gas. |  |  |  |
| [ Magnesium. An operational permit is required ] to melt, cast, heat treat or grind more than 10 pounds (4.54 kg) of magnesium. |  |  |  |
| [ Miscellaneous combustible storage. An operational permit is required ] to store in any building or upon any premises in excess of 2,500 cubic feet (71 m3) gross volume of combustible empty packing cases, boxes, barrels or similar containers, rubber tires, rubber, cork or similar combustible material. |  |  |  |
| [ Open burning. An operational permit is required ] for the kindling or maintaining of an open fire or a fire on any public street, alley, road, or other public or private ground. Instructions and stipulations of the permit shall be adhered to. Exception: Recreational fires. |  |  |  |
| [ Open flames and candles. An operational permit is required ] to remove paint with a torch; use a torch or open-flame device in a hazardous fire area; or to use open flames or candles in connection with assembly areas, dining areas of restaurants or drinking establishments. |  |  |  |
| [ Organic coatings. An operational permit is required ] for any organic-coating manufacturing operation producing more than 1 gallon (4 L) of an organic coating in one day. |  |  |  |
| [ Assembly/educational. An operational permit is required ] to operate a place of assembly [ /educational occupancy ]. |  |  |  |
| [ Private fire hydrants. An operational permit is required ] for the removal from service, use or operation of private fire hydrants. Exception: An operational permit is not required for private industry with trained maintenance personnel, private fire brigade or fire departments to maintain, test and use private hydrants. |  |  |  |
| [ Pyrotechnic special effects material. An operational permit is required ] for use and handling of pyrotechnic special effects material. |  |  |  |
| [ Pyroxylin plastics. An operational permit is required ] for storage or handling of more than 25 pounds (11 kg) of cellulose nitrate (pyroxylin) plastics and for the assembly or manufacture of articles involving pyroxylin plastics. |  |  |  |
| [ Refrigeration equipment. An operational permit is required ] to operate a mechanical refrigeration unit or system regulated by Chapter 6. |  |  |  |
| [ Repair garages and service stations. An operational permit is required ] for operation of repair garages and automotive, marine and fleet service stations. |  |  |  |
| [ Rooftop heliports. An operational permit is required ] for the operation of a rooftop heliport. |  |  |  |
| [ Spraying or dipping. An operational permit is required ] to conduct a spraying or dipping operation utilizing flammable or combustible liquids or the application of combustible powders regulated by Chapter 15. |  |  |  |
| [ Storage of scrap tires and tire byproducts. An operational permit is required ] to establish, conduct or maintain storage of scrap tires and tire byproducts that exceeds 2,500 cubic feet (71 m3) of total volume of scrap tires and for indoor storage of tires and tire byproducts. |  |  |  |
| [ Temporary membrane structures, tents and canopies. An operational permit is required ] to operate an air-supported temporary membrane structure or a tent. Exceptions: 1. Tents used exclusively for recreational camping purposes. 2. Tents and air-supported structures that cover an area of 900 square feet (84 m2) or less, including all connecting areas or spaces with a common means of egress or entrance and with an occupant load of 50 or less persons. 3. Fabric canopies and awnings open on all sides which comply with all of the following: 3.1. Individual canopies shall have a maximum size of 700 square feet (65 m2). 3.2. The aggregate area of multiple canopies placed side by side without a fire break clearance of 12 feet (3658 mm) shall not exceed 700 square feet (65 m2) total. 3.3. A minimum clearance of 12 feet (3658 mm) to structures and other tents shall be provided. |  |  |  |
| [ Tire-rebuilding plants. An operational permit is required ] for the operation and maintenance of a tire-rebuilding plant. |  |  |  |
| [ Waste handling. An operational permit is required ] for the operation of wrecking yards, junk yards and waste material-handling facilities. |  |  |  |
| [ Wood products. An operational permit is required ] to store chips, hogged material, lumber or plywood in excess of 200 cubic feet (6 m3). |  |  |  |

D. F-108.3. 107.3. Application for permit: Application for a permit shall be made on forms prescribed by the fire code official.

E. F-108.4. 107.4. Issuance of permits: Before a permit is issued, the fire code official shall make such inspections or tests as are necessary to assure that the use and activities for which application is made comply with the provisions of this code.

F. F-108.5. 107.5. Conditions of permit: A permit shall constitute permission to store or handle materials or to conduct processes in accordance with the SFPC, and shall not be construed as authority to omit or amend any of the provisions of this code. Permits shall remain in effect until

revoked or for such period as specified on the permit. Permits are not transferable.

[ G. 107.5.1. Special conditions for the State Fire Marshal's Office: Permits issued by the State Fire Marshal's Office for the use of explosives in special operations or under emergency conditions shall be valid for one week from the date of issuance and shall not be renewable. ]

[ G. H. ] F-108.6. 107.6. State Fire Marshal: Permits will not be required by the State Fire Marshal except for the manufacturing, storage, handling, use, and sale of explosives in localities not enforcing the SFPC, and for the display of fireworks on state-owned property.

Exception: Such permits shall not be required for the storage, handling, or use of explosives or blasting agents by the Virginia Department of State Police provided notification to the State Fire Marshal is made annually by the Chief Arson Investigator listing all storage locations within areas where enforcement is provided by the State Fire Marshal’s office.

[ H. I. ] F-108.7. 107.7. Annual: The enforcing agency may issue annual permits for the manufacturing, storage, handling, use, or sales of explosives to any state regulated public utility.

Exception: Such permits shall not apply to the storage, handling, or use of explosives or blasting agents pursuant to the provisions of Title 45.1 of the Code of Virginia.

[ I. J. ] F-108.8. 107.8. Approved plans: Plans approved by the fire code official are approved with the intent that they comply in all respects to this code. Any omissions or errors on the plans do not relieve the applicant of complying with all applicable requirements of this code.

[ J. K. ] F-108.9. 107.9. Posting: Issued permits shall be kept on the premises designated therein at all times and shall be readily available for inspection by the fire code official.

[ K. L. ] F-108.10. 107.10. Suspension of permit: A permit shall become invalid if the authorized activity is not commenced within six months after issuance of the permit, or if the authorized activity is suspended or abandoned for a period of six months after the time of commencement.

[ L. M. ] F-108.11. 107.11. Revocation of permit: The fire code official may revoke a permit or approval issued under the SFPC if conditions of the permit have been violated, or if the approved application, data or plans contain misrepresentation as to material fact.

[ M. N. ] 107.12. Local permit fees: Fees may be levied by the local governing body in order to defray the cost of enforcement and appeals under the SFPC.

[ N. O. ] 107.13. State permit fees: Fees for permits issued by the State Fire Marshal's office for the storage, use, sale or manufacture of explosives or blasting agents, and for the display of fireworks on state-owned property shall be as follows:

1. $100 per year per magazine to store explosives and blasting agents.

2. $150 per year per city or county to use explosives and blasting agents.

3. $150 per year to sell explosives and blasting agents.

4. $200 per year to manufacture explosives, blasting agents and fireworks.

5. $200 per event for fireworks, pyrotechnics or proximate audience displays conducted indoor of any state-owned buildings.

6. $100 per event for fireworks, pyrotechnics or proximate audience displays conducted out-of-doors on any state-owned property.

[ 7. $75 per event for the use of explosives in special operations or emergency conditions. ]

[ O. P. ] 107.14. Fee schedule: The local governing body may establish a fee schedule. The schedule shall incorporate unit rates, which may be based on square footage, cubic footage, estimated cost of inspection or other appropriate criteria.

[ P. Q. ] 107.15. Payment of fees: A permit shall not be issued until the designated fees have been paid.

Exception: The fire official may authorize delayed payment of fees.