TITLE 9. ENVIRONMENT

STATE WATER CONTROL BOARD

REGISTRAR'S NOTICE:  The State Water Control Board has claimed an exemption from the Administrative Process Act in accordance with § 2.2-4006 A 4 a of the Code of Virginia, which excludes regulations that are necessary to conform to changes in Virginia statutory law or the appropriation act where no agency discretion is involved.  The State Water Control Board will receive, consider and respond to petitions by any interested person at any time with respect to reconsideration or revision.

Title of Regulation: 9 VAC 25-31. Virginia Pollutant Discharge Elimination System (VPDES) Permit Regulation (amending 9 VAC 25-31-10, 9 VAC 25-31-100, 9 VAC 25-31-120, 9 VAC 25-31-130, 9 VAC 25-31-170, 9 VAC 25-31-200, 9 VAC 25-31-220, and 9 VAC 25-31-390; repealing 9 VAC 25-31-121

Statutory Authority: § 62.1-44.15 of the Code of Virginia; 40 CFR Parts 122, 123, 124, 403 and 503.

Effective Date: February 9, 2005, or 30 days after the U.S. Environmental Protection Agency's authorization for delegation of program authority for administering the issuance of national pollutant discharge elimination system permits for the control of stormwater discharges from MS4 and construction activities to the Virginia Soil and Water Conservation Board, whichever is the latter.

Agency Contact: Burton R. Tuxford, Department of Environmental Quality, P.O. Box 10009, Richmond, VA 23240, telephone (804) 698-4086, FAX (804) 698-4032 or e-mail brtuxford@deq.virginia.gov.

Summary:

The 2004 General Assembly adopted legislation that transfers the VPDES construction activity and municipal separate storm sewer system (MS4) storm water permitting responsibilities from the Department of Environmental Quality to the Department of Conservation and Recreation (DCR) on January 1, 2005, or as soon thereafter as EPA authorizes DCR's VPDES permitting program. The VPDES Permit Regulation has been amended to remove the construction activity and MS4 permitting requirements. Two minor typos were also corrected in the storm water section.

9 VAC 25-31-10. Definitions.

"Administrator" means the Administrator of the United States Environmental Protection Agency, or an authorized representative.

"Animal feeding operation" or "AFO" means a lot or facility (other than an aquatic animal production facility) where the following conditions are met: (i) animals (other than aquatic animals) have been, are, or will be stabled or confined and fed or maintained for a total of 45 days or more in any 12-month period, and (ii) crops, vegetation forage growth, or post-harvest residues are not sustained in the normal growing season over any portion of the lot or facility.

"Applicable standards and limitations" means all state, interstate, and federal standards and limitations to which a discharge, a sewage sludge use or disposal practice, or a related activity is subject under the Clean Water Act (CWA) (33 USC § 1251 et seq.) and the law, including effluent limitations, water quality standards, standards of performance, toxic effluent standards or prohibitions, best management practices, pretreatment standards, and standards for sewage sludge use or disposal under §§ 301, 302, 303, 304, 306, 307, 308, 403 and 405 of CWA.

"Approval authority" means the Director of the Department of Environmental Quality.

"Approved POTW Pretreatment Program" or "Program" or "POTW Pretreatment Program" means a program administered by a POTW that meets the criteria established in Part VII (9 VAC 25-31-730 et seq.) of this chapter and which has been approved by the director or by the administrator in accordance with 9 VAC 25-31-830.

"Approved program" or "approved state" means a state or interstate program which has been approved or authorized by EPA under 40 CFR Part 123 (2000).

"Aquaculture project" means a defined managed water area which uses discharges of pollutants into that designated area for the maintenance or production of harvestable freshwater, estuarine, or marine plants or animals.

"Average monthly discharge limitation" means the highest allowable average of daily discharges over a calendar month, calculated as the sum of all daily discharges measured during a calendar month divided by the number of daily discharges measured during that month.

"Average weekly discharge limitation" means the highest allowable average of daily discharges over a calendar week, calculated as the sum of all daily discharges measured during a calendar week divided by the number of daily discharges measured during that week.

"Best management practices (BMPs)" means schedules of activities, prohibitions of practices, maintenance procedures, and other management practices to prevent or reduce the pollution of surface waters. BMPs also include treatment requirements, operating procedures, and practices to control plant site run-off, spillage or leaks, sludge or waste disposal, or drainage from raw material storage.

"Board" means the Virginia State Water Control Board or State Water Control Board.

"Bypass" means the intentional diversion of waste streams from any portion of a treatment facility.

"Class I sludge management facility" means any POTW identified under Part VII (9 VAC 25-31-730 et seq.) of this chapter as being required to have an approved pretreatment program and any other treatment works treating domestic sewage classified as a Class I sludge management facility by the regional administrator, in conjunction with the director, because of the potential for its sludge use or disposal practices to adversely affect public health and the environment.

“Concentrated animal feeding operation” or “CAFO” means an AFO that is defined as a Large CAFO or as a Medium CAFO, or that is designated as a Medium CAFO or a Small CAFO. Any AFO may be designated as a CAFO by the director in accordance with the provisions of 9 VAC 25-31-130 B.

1. “Large CAFO.” An AFO is defined as a Large CAFO if it stables or confines as many or more than the numbers of animals specified in any of the following categories:

a. 700 mature dairy cows, whether milked or dry;

b. 1,000 veal calves;

c. 1,000 cattle other than mature dairy cows or veal calves. Cattle includes but is not limited to heifers, steers, bulls and cow/calf pairs;

d. 2,500 swine each weighing 55 pounds or more;

e. 10,000 swine each weighing less than 55 pounds;

f. 500 horses;

g. 10,000 sheep or lambs;

h. 55,000 turkeys;

i. 30,000 laying hens or broilers, if the AFO uses a liquid manure handling system;

j. 125,000 chickens (other than laying hens), if the AFO uses other than a liquid manure handling system;

k. 82,000 laying hens, if the AFO uses other than a liquid manure handling system;

l. 30,000 ducks, if the AFO uses other than a liquid manure handling system; or

m. 5,000 ducks if the AFO uses a liquid manure handling system.

2. “Medium CAFO.” The term Medium CAFO includes any AFO with the type and number of animals that fall within any of the ranges below that has been defined or designated as a CAFO. An AFO is defined as a Medium CAFO if:

a. The type and number of animals that it stables or confines falls within any of the following ranges:

(1) 200 to 699 mature dairy cattle, whether milked or dry;

(2) 300 to 999 veal calves;

(3) 300 to 999 cattle other than mature dairy cows or veal calves. Cattle includes but is not limited to heifers, steers, bulls and cow/calf pairs;

(4) 750 to 2,499 swine each weighing 55 pounds or more;

(5) 3,000 to 9,999 swine each weighing less than 55 pounds;

(6) 150 to 499 horses;

(7) 3,000 to 9,999 sheep or lambs;

(8) 16,500 to 29,999 laying hens or broilers, if the AFO uses a liquid manure handling system;

(9) 37,500 to 124,999 chickens (other than laying hens), if the AFO uses other than a liquid manure handling system;

(10) 25,000 to 81,999 laying hens, if the AFO uses other than a liquid manure handling system;

(11) 10,000 to 29,999 ducks, if the AFO uses other than a liquid manure handling system;

(12) 1,500 to 4,999 ducks, if the AFO uses a liquid manure handling system; and

b. Either one of the following conditions are met:

(1) Pollutants are discharged into surface waters of the state through a manmade ditch, flushing system, or other similar manmade device; or

(2) Pollutants are discharged directly into surface waters of the state that originate outside of and pass over, across, or through the facility or otherwise come into direct contact with the animals confined in the operation.

3. “Small CAFO.” An AFO that is designated as a CAFO and is not a Medium CAFO.

"Concentrated aquatic animal production facility" means a hatchery, fish farm, or other facility which meets the criteria of this definition, or which the board designates under 9 VAC 25-31-140. A hatchery, fish farm, or other facility is a concentrated aquatic animal production facility if it contains, grows, or holds aquatic animals in either of the following categories:

1. Cold water fish species or other cold water aquatic animals in ponds, raceways, or other similar structures which discharge at least 30 days per year but does not include:

a. Facilities which produce less than 9,090 harvest weight kilograms (approximately 20,000 pounds) of aquatic animals per year; and

b. Facilities which feed less than 2,272 kilograms (approximately 5,000 pounds) of food during the calendar month of maximum feeding; or

2. Warm water fish species or other warm water aquatic animals in ponds, raceways, or other similar structures which discharge at least 30 days per year, but does not include:

a. Closed ponds which discharge only during periods of excess run-off; or

b. Facilities which produce less than 45,454 harvest weight kilograms (approximately 100,000 pounds) of aquatic animals per year.

Cold water aquatic animals include, but are not limited to, the Salmonidae family of fish (e.g., trout and salmon).

Warm water aquatic animals include, but are not limited to, the Ictaluridae, Centrarchidae and Cyprinidae families of fish (e.g., respectively, catfish, sunfish and minnows).

"Contiguous zone" means the entire zone established by the United States under Article 24 of the Convention on the Territorial Sea and the Contiguous Zone (37 FR 11906).

"Continuous discharge" means a discharge which occurs without interruption throughout the operating hours of the facility, except for infrequent shutdowns for maintenance, process changes, or other similar activities.

"Co-permittee" means a permittee to a VPDES permit that is only responsible for permit conditions relating to the discharge for which it is the operator.

"CWA" means the Clean Water Act (33 USC § 1251 et seq.) (formerly referred to as the Federal Water Pollution Control Act or Federal Water Pollution Control Act Amendments of 1972) Public Law 92-500, as amended by Public Law 95-217, Public Law 95-576, Public Law 96-483, and Public Law 97-117.

"CWA and regulations" means the Clean Water Act (CWA) and applicable regulations promulgated thereunder. For the purposes of this chapter, it includes state program requirements.

"Daily discharge" means the discharge of a pollutant measured during a calendar day or any 24-hour period that reasonably represents the calendar day for purposes of sampling. For pollutants with limitations expressed in units of mass, the daily discharge is calculated as the total mass of the pollutant discharged over the day. For pollutants with limitations expressed in other units of measurement, the daily discharge is calculated as the average measurement of the pollutant over the day.

"Department" means the Virginia Department of Environmental Quality.

"Designated project area" means the portions of surface within which the permittee or permit applicant plans to confine the cultivated species, using a method or plan or operation (including, but not limited to, physical confinement) which, on the basis of reliable scientific evidence, is expected to ensure that specific individual organisms comprising an aquaculture crop will enjoy increased growth attributable to the discharge of pollutants, and be harvested within a defined geographic area.

"Direct discharge" means the discharge of a pollutant.

"Director" means the Director of the Department of Environmental Quality or an authorized representative.

"Discharge," when used without qualification, means the discharge of a pollutant.

"Discharge," when used in Part VII (9 VAC 25-31-730 et seq.) of this chapter, means "indirect discharge" as defined in this section.

"Discharge of a pollutant" means:

1. Any addition of any pollutant or combination of pollutants to surface waters from any point source; or

2. Any addition of any pollutant or combination of pollutants to the waters of the contiguous zone or the ocean from any point source other than a vessel or other floating craft which is being used as a means of transportation.

This definition includes additions of pollutants into surface waters from: surface run-off which is collected or channeled by man; discharges through pipes, sewers, or other conveyances owned by a state, municipality, or other person which do not lead to a treatment works; and discharges through pipes, sewers, or other conveyances, leading into privately owned treatment works. This term does not include an addition of pollutants by any indirect discharger.

"Discharge Monitoring Report (DMR)" means the form supplied by the department or an equivalent form developed by the permittee and approved by the board, for the reporting of self-monitoring results by permittees.

"Draft permit" means a document indicating the board's tentative decision to issue or deny, modify, revoke and reissue, terminate, or reissue a permit. A notice of intent to terminate a permit, and a notice of intent to deny a permit are types of draft permits. A denial of a request for modification, revocation and reissuance, or termination is not a draft permit. A proposed permit is not a draft permit.

"Effluent limitation" means any restriction imposed by the board on quantities, discharge rates, and concentrations of pollutants which are discharged from point sources into surface waters, the waters of the contiguous zone, or the ocean.

"Effluent limitations guidelines" means a regulation published by the administrator under § 304(b) of the CWA to adopt or revise effluent limitations.

"Environmental Protection Agency (EPA)" means the United States Environmental Protection Agency.

"Existing source" means any source which is not a new source or a new discharger.

"Facilities or equipment" means buildings, structures, process or production equipment or machinery which form a permanent part of a new source and which will be used in its operation, if these facilities or equipment are of such value as to represent a substantial commitment to construct. It excludes facilities or equipment used in connection with feasibility, engineering, and design studies regarding the new source or water pollution treatment for the new source.

"Facility or activity" means any VPDES point source or treatment works treating domestic sewage or any other facility or activity (including land or appurtenances thereto) that is subject to regulation under the VPDES program.

"General permit" means a VPDES permit authorizing a category of discharges under the CWA and the law within a geographical area.

"Hazardous substance" means any substance designated under the Code of Virginia and 40 CFR Part 116 (2000) pursuant to § 311 of the CWA.

"Illicit discharge" means any discharge to a municipal separate storm sewer that is not composed entirely of storm water except discharges pursuant to a VPDES permit (other than the VPDES permit for discharges from the municipal separate storm sewer) and discharges resulting from fire fighting activities.

"Incorporated place" means a city, town, township, or village that is incorporated under the Code of Virginia.

"Indian country" means (i) all land within the limits of any Indian reservation under the jurisdiction of the United States government, notwithstanding the issuance of any patent, and including rights-of-way running through the reservation; (ii) all dependent Indian communities with the borders of the United States whether within the originally or subsequently acquired territory thereof, and whether within or without the limits of a state; and (iii) all Indian allotments, the Indian titles to which have not been extinguished, including rights-of-way running through the same.

"Indirect discharge" means the introduction of pollutants into a POTW from any nondomestic source regulated under § 307(b), (c) or (d) of the CWA and the law.

"Indirect discharger" means a nondomestic discharger introducing pollutants to a POTW.

"Individual control strategy" means a final VPDES permit with supporting documentation showing that effluent limits are consistent with an approved wasteload allocation or other documentation that shows that applicable water quality standards will be met not later than three years after the individual control strategy is established.

"Industrial user" or "user" means a source of indirect discharge.

"Interference" means an indirect discharge which, alone or in conjunction with an indirect discharge or discharges from other sources, both: (i) inhibits or disrupts the POTW, its treatment processes or operations, or its sludge processes, use or disposal; and therefore (ii) is a cause of a violation of any requirement of the POTW's VPDES permit (including an increase in the magnitude or duration of a violation) or of the prevention of sewage sludge use or disposal in compliance with the following statutory provisions and regulations or permits issued thereunder (or more stringent state or local regulations): Section 405 of the Clean Water Act, the Solid Waste Disposal Act (SWDA) (including Title II, more commonly referred to as the Resource Conservation and Recovery Act (RCRA) (42 USC § 6901 et seq.), and including state regulations contained in any state sludge management plan prepared pursuant to Subtitle D of the SWDA) the Clean Air Act (42 USC § 701 et seq.), the Toxic Substances Control Act (15 USC § 2601 et seq.), and the Marine Protection, Research and Sanctuaries Act (33 USC § 1401 et seq.).

"Interstate agency" means an agency of two or more states established by or under an agreement or compact approved by Congress, or any other agency of two or more states having substantial powers or duties pertaining to the control of pollution as determined and approved by the administrator under the CWA and regulations.

"Land application area" means land under the control of an AFO owner or operator, that is owned, rented, or leased to which manure, litter or process wastewater from the production area may be applied.

"Large municipal separate storm sewer system" means all municipal separate storm sewers that are either:

1. Located in an incorporated place with a population of 250,000 or more as determined by the latest decennial census by the Bureau of Census (40 CFR Part 122 Appendix F (2000));

2. Located in the counties listed in 40 CFR Part 122 Appendix H (2000), except municipal separate storm sewers that are located in the incorporated places, townships or towns within such counties;

3. Owned or operated by a municipality other than those described in subdivision 1 or 2 of this definition and that are designated by the board as part of the large or medium municipal separate storm sewer system due to the interrelationship between the discharges of the designated storm sewer and the discharges from municipal separate storm sewers described under subdivision 1 or 2 of this definition. In making this determination the board may consider the following factors:

a. Physical interconnections between the municipal separate storm sewers;

b. The location of discharges from the designated municipal separate storm sewer relative to discharges from municipal separate storm sewers described in subdivision 1 of this definition;

c. The quantity and nature of pollutants discharged to surface waters;

d. The nature of the receiving waters; and

e. Other relevant factors.

4. The board may, upon petition, designate as a large municipal separate storm sewer system, municipal separate storm sewers located within the boundaries of a region defined by a storm water management regional authority based on a jurisdictional, watershed, or other appropriate basis that includes one or more of the systems described in this definition.

"Log sorting" and "log storage facilities" means facilities whose discharges result from the holding of unprocessed wood, for example, logs or roundwood with bark or after removal of bark held in self-contained bodies of water (mill ponds or log ponds) or stored on land where water is applied intentionally on the logs (wet decking).

"Major facility" means any VPDES facility or activity classified as such by the regional administrator in conjunction with the board.

"Major municipal separate storm sewer outfall (or major outfall)" means a municipal separate storm sewer outfall that discharges from a single pipe with an inside diameter of 36 inches or more or its equivalent (discharge from a single conveyance other than circular pipe which is associated with a drainage area of more than 50 acres); or for municipal separate storm sewers that receive storm water from lands zoned for industrial activity (based on comprehensive zoning plans or the equivalent), an outfall that discharges from a single pipe with an inside diameter of 12 inches or more or from its equivalent (discharge from other than a circular pipe associated with a drainage area of two acres or more).

"Manmade" means constructed by man and used for the purpose of transporting wastes.

"Manure" means manure, bedding, compost and raw materials or other materials commingled with manure or set aside for disposal.

"Maximum daily discharge limitation" means the highest allowable daily discharge.

"Medium municipal separate storm sewer system" means all municipal separate storm sewers that are either:

1. Located in an incorporated place with a population of 100,000 or more but less than 250,000, as determined by the latest decennial census by the Bureau of Census (40 CFR Part 122 Appendix G (2000));

2. Located in the counties listed in 40 CFR Part 122 Appendix I (2000), except municipal separate storm sewers that are located in the incorporated places, townships or towns within such counties;

3. Owned or operated by a municipality other than those described in subdivision 1 or 2 of this definition and that are designated by the board as part of the large or medium municipal separate storm sewer system due to the interrelationship between the discharges of the designated storm sewer and the discharges from municipal separate storm sewers described under subdivision 1 or 2 of this definition. In making this determination the board may consider the following factors:

a. Physical interconnections between the municipal separate storm sewers;

b. The location of discharges from the designated municipal separate storm sewer relative to discharges from municipal separate storm sewers described in subdivision 1 of this definition;

c. The quantity and nature of pollutants discharged to surface waters;

d. The nature of the receiving waters; or

e. Other relevant factors.

4. The board may, upon petition, designate as a medium municipal separate storm sewer system, municipal separate storm sewers located within the boundaries of a region defined by a storm water management regional authority based on a jurisdictional, watershed, or other appropriate basis that includes one or more of the systems described in subdivisions 1, 2 and 3 of this definition.

"Municipal separate storm sewer" means a conveyance or system of conveyances (including roads with drainage systems, municipal streets, catch basins, curbs, gutters, ditches, manmade channels, or storm drains):

1. Owned or operated by a state, city, town, county, district, association, or other public body (created by or pursuant to state law) having jurisdiction over disposal of sewage, industrial wastes, storm water, or other wastes, including special districts under state law such as a sewer district, flood control district or drainage district, or similar entity, or an Indian tribe or an authorized Indian tribal organization, or a designated and approved management agency under § 208 of the CWA that discharges to surface waters;

2. Designed or used for collecting or conveying storm water;

3. Which is not a combined sewer; and

4. Which is not part of a publicly owned treatment works (POTW).

"Municipal separate storm sewer system" or "MS4" means storm sewers that are defined as "large" or "medium" or "small" municipal separate storm sewer systems, or designated under 9 VAC 25-31-120 A 1.

"Municipality" means a city, town, county, district, association, or other public body created by or under state law and having jurisdiction over disposal of sewage, industrial wastes, or other wastes, or an Indian tribe or an authorized Indian tribal organization, or a designated and approved management agency under § 208 of the CWA.

"National Pollutant Discharge Elimination System (NPDES)" means the national program for issuing, modifying, revoking and reissuing, terminating, monitoring and enforcing permits, and imposing and enforcing pretreatment requirements under §§ 307, 402, 318, and 405 of the CWA. The term includes an approved program.

"National pretreatment standard," "pretreatment standard," or "standard," when used in Part VII (9 VAC 25-31-730 et seq.) of this chapter, means any regulation containing pollutant discharge limits promulgated by the EPA in accordance with § 307(b) and (c) of the CWA, which applies to industrial users. This term includes prohibitive discharge limits established pursuant to 9 VAC 25-31-770.

"New discharger" means any building, structure, facility, or installation:

1. From which there is or may be a discharge of pollutants;

2. That did not commence the discharge of pollutants at a particular site prior to August 13, 1979;

3. Which is not a new source; and

4. Which has never received a finally effective VPDES permit for discharges at that site.

This definition includes an indirect discharger which commences discharging into surface waters after August 13, 1979. It also includes any existing mobile point source (other than an offshore or coastal oil and gas exploratory drilling rig or a coastal oil and gas developmental drilling rig) such as a seafood processing rig, seafood processing vessel, or aggregate plant, that begins discharging at a site for which it does not have a permit; and any offshore or coastal mobile oil and gas exploratory drilling rig or coastal mobile oil and gas developmental drilling rig that commences the discharge of pollutants after August 13, 1979.

"New source," except when used in Part VII of this chapter, means any building, structure, facility, or installation from which there is or may be a discharge of pollutants, the construction of which commenced:

(a) After promulgation of standards of performance under § 306 of the CWA which are applicable to such source; or

(b) After proposal of standards of performance in accordance with § 306 of the CWA which are applicable to such source, but only if the standards are promulgated in accordance with § 306 of the CWA within 120 days of their proposal.

"New source," when used in Part VII of this chapter, means any building, structure, facility, or installation from which there is or may be a discharge of pollutants, the construction of which commenced after the publication of proposed pretreatment standards under § 307(c) of the CWA which will be applicable to such source if such standards are thereafter promulgated in accordance with that section, provided that:

1. a. The building, structure, facility or installation is constructed at a site at which no other source is located;

b. The building, structure, facility, or installation totally replaces the process or production equipment that causes the discharge of pollutants at an existing source; or

c. The production of wastewater generating processes of the building, structure, facility, or installation are substantially independent of an existing source at the same site. In determining whether these are substantially independent, factors such as the extent to which the new facility is integrated with the existing plant, and the extent to which the new facility is engaged in the same general type of activity as the existing source should be considered.

2. Construction on a site at which an existing source is located results in a modification rather than a new source if the construction does not create a new building, structure, facility, or installation meeting the criteria of subdivision 1 b or c of this definition but otherwise alters, replaces, or adds to existing process or production equipment.

3. Construction of a new source as defined under this subdivision has commenced if the owner or operator has:

a. Begun, or caused to begin, as part of a continuous on-site construction program:

(1) Any placement, assembly, or installation of facilities or equipment; or

(2) Significant site preparation work including clearing, excavation, or removal of existing buildings, structures, or facilities which is necessary for the placement, assembly, or installation of new source facilities or equipment; or

b. Entered into a binding contractual obligation for the purchase of facilities or equipment which are intended to be used in its operation within a reasonable time. Options to purchase or contracts which can be terminated or modified without substantial loss, and contracts for feasibility, engineering, and design studies do not constitute a contractual obligation under this subdivision.

"Outfall," when used in reference to municipal separate storm sewers, means a point source at the point where a municipal separate storm sewer discharges to surface waters and does not include open conveyances connecting two municipal separate storm sewers, or pipes, tunnels or other conveyances which connect segments of the same stream or other surface waters and are used to convey surface waters.

"Overburden" means any material of any nature, consolidated or unconsolidated, that overlies a mineral deposit, excluding topsoil or similar naturally occurring surface materials that are not disturbed by mining operations.

"Owner" means the Commonwealth or any of its political subdivisions including, but not limited to, sanitation district commissions and authorities, and any public or private institution, corporation, association, firm or company organized or existing under the laws of this or any other state or country, or any officer or agency of the United States, or any person or group of persons acting individually or as a group that owns, operates, charters, rents, or otherwise exercises control over or is responsible for any actual or potential discharge of sewage, industrial wastes, or other wastes to state waters, or any facility or operation that has the capability to alter the physical, chemical, or biological properties of state waters in contravention of § 62.1-44.5 of the Code of Virginia.

"Owner" or "operator" means the owner or operator of any facility or activity subject to regulation under the VPDES program.

"Pass through" means a discharge which exits the POTW into state waters in quantities or concentrations which, alone or in conjunction with a discharge or discharges from other sources, is a cause of a violation of any requirement of the POTW's VPDES permit (including an increase in the magnitude or duration of a violation).

"Permit" means an authorization, certificate, license, or equivalent control document issued by the board to implement the requirements of this chapter. Permit includes a VPDES general permit. Permit does not include any permit which has not yet been the subject of final agency action, such as a draft permit or a proposed permit.

"Person" means an individual, corporation, partnership, association, a governmental body, a municipal corporation, or any other legal entity.

"Point source" means any discernible, confined, and discrete conveyance including, but not limited to, any pipe, ditch, channel, tunnel, conduit, well, discrete fissure, container, rolling stock, concentrated animal feeding operation, landfill leachate collection system, vessel, or other floating craft from which pollutants are or may be discharged. This term does not include return flows from irrigated agriculture or agricultural storm water run-off.

"Pollutant" means dredged spoil, solid waste, incinerator residue, filter backwash, sewage, garbage, sewage sludge, munitions, chemical wastes, biological materials, radioactive materials (except those regulated under the Atomic Energy Act of 1954, as amended (42 USC § 2011 et seq.)), heat, wrecked or discarded equipment, rock, sand, cellar dirt and industrial, municipal, and agricultural waste discharged into water. It does not mean:

1. Sewage from vessels; or

2. Water, gas, or other material which is injected into a well to facilitate production of oil or gas, or water derived in association with oil and gas production and disposed of in a well if the well used either to facilitate production or for disposal purposes is approved by the board, and if the board determines that the injection or disposal will not result in the degradation of ground or surface water resources.

"POTW treatment plant" means that portion of the POTW which is designed to provide treatment (including recycling and reclamation) of municipal sewage and industrial waste.

"Pretreatment" means the reduction of the amount of pollutants, the elimination of pollutants, or the alteration of the nature of pollutant properties in wastewater prior to or in lieu of discharging or otherwise introducing such pollutants into a POTW. The reduction or alteration may be obtained by physical, chemical or biological processes, process changes or by other means, except as prohibited in Part VII of this chapter. Appropriate pretreatment technology includes control equipment, such as equalization tanks or facilities, for protection against surges or slug loadings that might interfere with or otherwise be incompatible with the POTW. However, where wastewater from a regulated process is mixed in an equalization facility with unregulated wastewater or with wastewater from another regulated process, the effluent from the equalization facility must meet an adjusted pretreatment limit calculated in accordance with Part VII of this chapter.

"Pretreatment requirements" means any requirements arising under Part VII of this chapter including the duty to allow or carry out inspections, entry or monitoring activities; any rules, regulations, or orders issued by the owner of a publicly owned treatment works; or any reporting requirements imposed by the owner of a publicly owned treatment works or by the regulations of the board. Pretreatment requirements do not include the requirements of a national pretreatment standard.

"Primary industry category" means any industry category listed in the NRDC settlement agreement (Natural Resources Defense Council et al. v. Train, 8 E.R.C. 2120 (D.D.C. 1976), modified 12 E.R.C. 1833 (D.D.C. 1979)); also listed in 40 CFR Part 122 Appendix A (2000).

"Privately owned treatment works (PVOTW)" means any device or system which is (i) used to treat wastes from any facility whose operator is not the operator of the treatment works and (ii) not a POTW.

"Process wastewater" means any water which, during manufacturing or processing, comes into direct contact with or results from the production or use of any raw material, intermediate product, finished product, byproduct, or waste product. Process wastewater from an AFO means water directly or indirectly used in the operation of the AFO for any of the following: spillage or overflow from animal or poultry watering systems; washing, cleaning, or flushing pens, barns, manure pits, or other AFO facilities; direct contact swimming, washing, or spray cooling of the animals; or dust control. Process wastewater from an AFO also includes any water that comes into contact with any raw materials, products, or byproducts including manure, litter, feed, milk, eggs or bedding.

“Production area” means that part of an AFO that includes the animal confinement area, the manure storage area, the raw materials storage area, and the waste containment areas. The animal confinement area includes but is not limited to open lots, housed lots, feedlots, confinement houses, stall barns, free stall barns, milkrooms, milking centers, cowyards, barnyards, medication pens, walkers, animal walkways, and stables. The manure storage area includes but is not limited to lagoons, runoff ponds, storage sheds, stockpiles, under house or pit storages, liquid impoundments, static piles, and composting piles. The raw materials storage areas includes but is not limited to feed silos, silage bunkers, and bedding materials. The waste containment area includes but is not limited to settling basins, and areas within berms and diversions that separate uncontaminated storm water. Also included in the definition of production area is any egg washing or egg processing facility, and any area used in the storage, handling, treatment, or disposal of mortalities.

"Proposed permit" means a VPDES permit prepared after the close of the public comment period (and, when applicable, any public hearing and administrative appeals) which is sent to EPA for review before final issuance. A proposed permit is not a draft permit.

"Publicly owned treatment works (POTW)" means a treatment works as defined by § 212 of the CWA, which is owned by a state or municipality (as defined by § 502(4) of the CWA). This definition includes any devices and systems used in the storage, treatment, recycling, and reclamation of municipal sewage or industrial wastes of a liquid nature. It also includes sewers, pipes, and other conveyances only if they convey wastewater to a POTW treatment plant. The term also means the municipality as defined in § 502(4) of the CWA, which has jurisdiction over the indirect discharges to and the discharges from such a treatment works.

"Recommencing discharger" means a source which recommences discharge after terminating operations.

"Regional administrator" means the Regional Administrator of Region III of the Environmental Protection Agency or the authorized representative of the regional administrator.

"Rock crushing and gravel washing facilities" means facilities which process crushed and broken stone, gravel, and riprap.

"Run-off coefficient" means the fraction of total rainfall that will appear at a conveyance as run-off.

"Schedule of compliance" means a schedule of remedial measures included in a permit, including an enforceable sequence of interim requirements (for example, actions, operations, or milestone events) leading to compliance with the law, the CWA and regulations.

"Secondary industry category" means any industry category which is not a primary industry category.

"Secretary" means the Secretary of the Army, acting through the Chief of Engineers.

"Septage" means the liquid and solid material pumped from a septic tank, cesspool, or similar domestic sewage treatment system, or a holding tank when the system is cleaned or maintained.

"Severe property damage" means substantial physical damage to property, damage to the treatment facilities which causes them to become inoperable, or substantial and permanent loss of natural resources which can reasonably be expected to occur in the absence of a bypass. Severe property damage does not mean economic loss caused by delays in production.

"Sewage from vessels" means human body wastes and the wastes from toilets and other receptacles intended to receive or retain body wastes that are discharged from vessels and regulated under § 312 of CWA.

"Sewage sludge" means any solid, semisolid, or liquid residue removed during the treatment of municipal waste water or domestic sewage. Sewage sludge includes, but is not limited to, solids removed during primary, secondary, or advanced waste water treatment, scum, domestic septage, portable toilet pumpings, type III marine sanitation device pumpings, and sewage sludge products. Sewage sludge does not include grit or screenings, or ash generated during the incineration of sewage sludge.

"Sewage sludge use" or "disposal practice" means the collection, storage, treatment, transportation, processing, monitoring, use, or disposal of sewage sludge.

"Significant industrial user," except as provided in subdivision 3 of this definition, means:

1. All industrial users subject to Categorical Pretreatment Standards under 9 VAC 25-31-780 and incorporated by reference in 9 VAC 25-31-30; and

2. Any other industrial user that: discharges an average of 25,000 gallons per day or more of process wastewater to the POTW (excluding sanitary, noncontact cooling and boiler blowdown wastewater); contributes a process wastestream which makes up 5.0% or more of the average dry weather hydraulic or organic capacity of the POTW treatment plant; or is designated as such by the Control Authority, as defined in 9 VAC 25-31-840 A, on the basis that the industrial user has a reasonable potential for adversely affecting the POTW's operation or for violating any pretreatment standard or requirement.

3. Upon a finding that an industrial user meeting the criteria in subdivision 2 of this definition has no reasonable potential for adversely affecting the POTW's operation or for violating any pretreatment standard or requirement, the control authority may at any time, on its own initiative or in response to a petition received from an industrial user or POTW, and in accordance with Part VII (9 VAC 25-31-730 et seq.) of this chapter, determine that such industrial user is not a significant industrial user.

"Significant materials" means, but is not limited to: raw materials; fuels; materials such as solvents, detergents, and plastic pellets; finished materials such as metallic products; raw materials used in food processing or production; hazardous substances designated under § 101(14) of CERCLA (42 USC § 9601(14)); any chemical the facility is required to report pursuant to§ 313 of Title III of SARA (42 USC § 11023); fertilizers; pesticides; and waste products such as ashes, slag and sludge that have the potential to be released with storm water discharges.

"Silvicultural point source" means any discernible, confined and discrete conveyance related to rock crushing, gravel washing, log sorting, or log storage facilities which are operated in connection with silvicultural activities and from which pollutants are discharged into surface waters. The term does not include nonpoint source silvicultural activities such as nursery operations, site preparation, reforestation and subsequent cultural treatment, thinning, prescribed burning, pest and fire control, harvesting operations, surface drainage, or road construction and maintenance from which there is natural run-off. However, some of these activities (such as stream crossing for roads) may involve point source discharges of dredged or fill material which may require a CWA § 404 permit.

"Site" means the land or water area where any facility or activity is physically located or conducted, including adjacent land used in connection with the facility or activity.

"Sludge-only facility" means any treatment works treating domestic sewage whose methods of sewage sludge use or disposal are subject to regulations promulgated pursuant to the law and § 405(d) of the CWA, and is required to obtain a VPDES permit.

"Small municipal separate storm sewer system" or "small MS4" means all separate storm sewers that are (i) owned or operated by the United States, a state, city, town, borough, county, parish, district, association, or other public body (created by or pursuant to state law) having jurisdiction over disposal of sewage, industrial wastes, storm water, or other wastes, including special districts under state law such as a sewer district, flood control district or drainage district, or similar entity, or an Indian tribe or an authorized Indian tribal organization, or a designated and approved management agency under § 208 of the CWA that discharges to surface waters and (ii) not defined as "large" or "medium" municipal separate storm sewer systems or designated under 9 VAC 25-31-120 A 1. This term includes systems similar to separate storm sewer systems n municipalities, such as systems at military bases, large hospital or prison complexes, and highway and other thoroughfares. The term does not include separate storm sewers in very discrete areas, such as individual buildings.

"Source" means any building, structure, facility, or installation from which there is or may be a discharge of pollutants.

"Standards for sewage sludge use or disposal" means the regulations promulgated pursuant to the law and § 405(d) of the CWA which govern minimum requirements for sludge quality, management practices, and monitoring and reporting applicable to sewage sludge or the use or disposal of sewage sludge by any person.

"State" means the Commonwealth of Virginia.

"State/EPA agreement" means an agreement between the regional administrator and the state which coordinates EPA and state activities, responsibilities and programs including those under the CWA and the law.

"State Water Control Law" or "Law" means Chapter 3.1 (§ 62.1-44.2 et seq.) of Title 62.1 of the Code of Virginia.

"Storm water" means storm water run-off, snow melt run-off, and surface run-off and drainage.

"Storm water discharge associated with industrial activity" means the discharge from any conveyance which is used for collecting and conveying storm water and which is directly related to manufacturing, processing or raw materials storage areas at an industrial plant. The term does not include discharges from facilities or activities excluded from the VPDES program. For the categories of industries identified in this definition, the term includes, but is not limited to, storm water discharges from industrial plant yards; immediate access roads and rail lines used or traveled by carriers of raw materials, manufactured products, waste material, or by-products used or created by the facility; material handling sites; refuse sites; sites used for the application or disposal of process waste waters; sites used for the storage and maintenance of material handling equipment; sites used for residual treatment, storage, or disposal; shipping and receiving areas; manufacturing buildings; storage areas (including tank farms) for raw materials, and intermediate and final products; and areas where industrial activity has taken place in the past and significant materials remain and are exposed to storm water. For the purposes of this definition, material handling activities include the storage, loading and unloading, transportation, or conveyance of any raw material, intermediate product, final product, by-product, or waste product. The term excludes areas located on plant lands separate from the plant's industrial activities, such as office buildings and accompanying parking lots as long as the drainage from the excluded areas is not mixed with storm water drained from the above described areas. Industrial facilities (including industrial facilities that are federally, state, or municipally owned or operated that meet the description of the facilities listed in subdivisions 1 through 11 of this definition) include those facilities designated under the provisions of 9 VAC 25-31-120 A 1 e. The following categories of facilities are considered to be engaging in industrial activity for purposes of this subsection:

1. Facilities subject to storm water effluent limitations guidelines, new source performance standards, or toxic pollutant effluent standards (except facilities with toxic pollutant effluent standards which are exempted under category 11);

2. Facilities classified as Standard Industrial Classifications 24 (except 2434), 26 (except 265 and 267), 28 (except 283), 29, 311, 32 (except 323), 33, 3441, 373;

3. Facilities classified as Standard Industrial Classifications 10 through 14 (mineral industry) including active or inactive mining operations (except for areas of coal mining operations no longer meeting the definition of a reclamation area under 40 CFR 434.11(1) (2000) because the performance bond issued to the facility by the appropriate SMCRA authority has been released, or except for areas of non-coal mining operations which have been released from applicable state or federal reclamation requirements after December 17, 1990) and oil and gas exploration, production, processing, or treatment operations, or transmission facilities that discharge storm water contaminated by contact with or that has come into contact with, any overburden, raw material, intermediate products, finished products, by-products, or waste products located on the site of such operations; (inactive mining operations are mining sites that are not being actively mined, but which have an identifiable owner/operator; inactive mining sites do not include sites where mining claims are being maintained prior to disturbances associated with the extraction, beneficiation, or processing of mined materials, nor sites where minimal activities are undertaken for the sole purpose of maintaining a mining claim);

4. Hazardous waste treatment, storage, or disposal facilities, including those that are operating under interim status or a permit under Subtitle C of RCRA (42 USC § 6901 et seq.);

5. Landfills, land application sites, and open dumps that receive or have received any industrial wastes (waste that is received from any of the facilities described under this subsection) including those that are subject to regulation under Subtitle D of RCRA (42 USC § 6901 et seq.);

6. Facilities involved in the recycling of materials, including metal scrapyards, battery reclaimers, salvage yards, and automobile junkyards, including but limited to those classified as Standard Industrial Classification 5015 and 5093;

7. Steam electric power generating facilities, including coal handling sites;

8. Transportation facilities classified as Standard Industrial Classifications 40, 41, 42 (except 4221-25), 43, 44, 45, and 5171 which have vehicle maintenance shops, equipment cleaning operations, or airport deicing operations. Only those portions of the facility that are either involved in vehicle maintenance (including vehicle rehabilitation, mechanical repairs, painting, fueling, and lubrication), equipment cleaning operations, airport deicing operations, or which are otherwise identified under subdivisions 1 through 7 or 9 through 11 and 10 of this definition are associated with industrial activity;

9. Treatment works treating domestic sewage or any other sewage sludge or wastewater treatment device or system, used in the storage treatment, recycling, and reclamation of municipal or domestic sewage, including land dedicated to the disposal of sewage sludge that are located within the confines of the facility, with a design flow of 1.0 mgd or more, or required to have an approved pretreatment program. Not included are farm lands, domestic gardens or lands used for sludge management where sludge is beneficially reused and which are not physically located in the confines of the facility, or areas that are in compliance with § 405 of the CWA; and

10. Construction activity including clearing, grading and excavation activities except: operations that result in the disturbance of less than five acres of total land area. Construction activity also includes the disturbance of less than five acres of total land area that is part of a larger common plan of development or sale if the larger common plan will ultimately disturb five acres or more; and

11. 10. Facilities under Standard Industrial Classifications 20, 21, 22, 23, 2434, 25, 265, 267, 27, 283, 30, 31 (except 311), 323, 34 (except 3441), 35, 36, 37 (except 373), 38, 39, and 4221-25.

"Storm water discharge associated with small construction activity" means the discharge of storm water from:

1. Construction activities including clearing, grading, and excavating that result in land disturbance of equal to or greater than one acre and less than five acres. Small construction activity also includes the disturbance of less than one acre of total land area that is part of a larger common plan of development or sale if the larger common plan will ultimately disturb equal to or greater than one and less than five acres. Small construction activity does not include routine maintenance that is performed to maintain the original line and grade, hydraulic capacity, or original purpose of the facility. The board may waive the otherwise applicable requirements in a general permit for a storm water discharge from construction activities that disturb less than five acres where storm water controls are not needed based on a "total maximum daily load" (TMDL) approved or established by EPA that addresses the pollutant(s) of concern or, for nonimpaired waters that do not require TMDLs, an equivalent analysis that determines allocations for small construction sites for the pollutant(s) of concern or that determines that such allocations are not needed to protect water quality based on consideration of existing in-stream concentrations, expected growth in pollutant contributions from all sources, and a margin of safety. For the purpose of this subdivision, the pollutant(s) of concern include sediment or a parameter that addresses sediment (such as total suspended solids, turbidity or siltation) and any other pollutant that has been identified as a cause of impairment of any water body that will receive a discharge from the construction activity. The operator must certify to the board that the construction activity will take place, and storm water discharges will occur, within the drainage area addressed by the TMDL or equivalent analysis.

2. Any other construction activity designated by the either the board or the EPA regional administrator, based on the potential for contribution to a violation of a water quality standard or for significant contribution of pollutants to surface waters.

"Submission" means: (i) a request by a POTW for approval of a pretreatment program to the regional administrator or the director; (ii) a request by POTW to the regional administrator or the director for authority to revise the discharge limits in categorical pretreatment standards to reflect POTW pollutant removals; or (iii) a request to the EPA by the director for approval of the Virginia pretreatment program.

"Surface waters" means:

1. All waters which are currently used, were used in the past, or may be susceptible to use in interstate or foreign commerce, including all waters which are subject to the ebb and flow of the tide;

2. All interstate waters, including interstate wetlands;

3. All other waters such as intrastate lakes, rivers, streams (including intermittent streams), mudflats, sandflats, wetlands, sloughs, prairie potholes, wet meadows, playa lakes, or natural ponds the use, degradation, or destruction of which would affect or could affect interstate or foreign commerce including any such waters:

a. Which are or could be used by interstate or foreign travelers for recreational or other purposes;

b. From which fish or shellfish are or could be taken and sold in interstate or foreign commerce; or

c. Which are used or could be used for industrial purposes by industries in interstate commerce.

4. All impoundments of waters otherwise defined as surface waters under this definition;

5. Tributaries of waters identified in subdivisions 1 through 4 of this definition;

6. The territorial sea; and

7. Wetlands adjacent to waters (other than waters that are themselves wetlands) identified in subdivisions 1 through 6 of this definition.

Waste treatment systems, including treatment ponds or lagoons designed to meet the requirements of the CWA and the law, are not surface waters. Surface waters do not include prior converted cropland. Notwithstanding the determination of an area's status as prior converted cropland by any other agency, for the purposes of the Clean Water Act, the final authority regarding the Clean Water Act jurisdiction remains with the EPA.

"Total dissolved solids" means the total dissolved (filterable) solids as determined by use of the method specified in 40 CFR Part 136 (2000).

"Toxic pollutant" means any pollutant listed as toxic under § 307(a)(1) of the CWA or, in the case of sludge use or disposal practices, any pollutant identified in regulations implementing § 405(d) of the CWA.

"Treatment facility" means only those mechanical power driven devices necessary for the transmission and treatment of pollutants (e.g., pump stations, unit treatment processes).

"Treatment works" means any devices and systems used for the storage, treatment, recycling or reclamation of sewage or liquid industrial waste, or other waste or necessary to recycle or reuse water, including intercepting sewers, outfall sewers, sewage collection systems, individual systems, pumping, power and other equipment and their appurtenances; extensions, improvements, remodeling, additions, or alterations thereof; and any works, including land that will be an integral part of the treatment process or is used for ultimate disposal of residues resulting from such treatment; or any other method or system used for preventing, abating, reducing, storing, treating, separating, or disposing of municipal waste or industrial waste, including waste in combined sewer water and sanitary sewer systems.

"Treatment works treating domestic sewage" means a POTW or any other sewage sludge or waste water treatment devices or systems, regardless of ownership (including federal facilities), used in the storage, treatment, recycling, and reclamation of municipal or domestic sewage, including land dedicated for the disposal of sewage sludge. This definition does not include septic tanks or similar devices. For purposes of this definition, domestic sewage includes waste and waste water from humans or household operations that are discharged to or otherwise enter a treatment works.

"TWTDS" means treatment works treating domestic sewage.

"Uncontrolled sanitary landfill" means a landfill or open dump, whether in operation or closed, that does not meet the requirements for run-on or run-off controls established pursuant to subtitle D of the Solid Waste Disposal Act (42 USC § 6901 et seq.).

"Upset," except when used in Part VII of this chapter, means an exceptional incident in which there is unintentional and temporary noncompliance with technology based permit effluent limitations because of factors beyond the reasonable control of the permittee. An upset does not include noncompliance to the extent caused by operational error, improperly designed treatment facilities, inadequate treatment facilities, lack of preventive maintenance, or careless or improper operation.

"Variance" means any mechanism or provision under § 301 or § 316 of the CWA or under 40 CFR Part 125 (2000), or in the applicable effluent limitations guidelines which allows modification to or waiver of the generally applicable effluent limitation requirements or time deadlines of the CWA. This includes provisions which allow the establishment of alternative limitations based on fundamentally different factors or on §§ 301(c), 301(g), 301(h), 301(i), or 316(a) of the CWA.

"Virginia Pollutant Discharge Elimination System (VPDES) permit" means a document issued by the board pursuant to this chapter authorizing, under prescribed conditions, the potential or actual discharge of pollutants from a point source to surface waters and the use or disposal of sewage sludge. Under the approved state program, a VPDES permit is equivalent to an NPDES permit.

"VPDES application" or "application" means the standard form or forms, including any additions, revisions or modifications to the forms, approved by the administrator and the board for applying for a VPDES permit.

"Wastewater," when used in Part VII of this chapter, means liquid and water carried industrial wastes and domestic sewage from residential dwellings, commercial buildings, industrial and manufacturing facilities and institutions, whether treated or untreated, which are contributed to the POTW.

"Wastewater works operator" means any individual employed or appointed by any owner, and who is designated by such owner to be the person in responsible charge, such as a supervisor, a shift operator, or a substitute in charge, and whose duties include testing or evaluation to control wastewater works operations. Not included in this definition are superintendents or directors of public works, city engineers, or other municipal or industrial officials whose duties do not include the actual operation or direct supervision of wastewater works.

"Water Management Division Director" means the director of the Region III Water Management Division of the Environmental Protection Agency or this person's delegated representative.

"Wetlands" means those areas that are inundated or saturated by surface or groundwater at a frequency and duration sufficient to support, and that under normal circumstances do support, a prevalence of vegetation typically adapted for life in saturated soil conditions. Wetlands generally include swamps, marshes, bogs, and similar areas.

"Whole effluent toxicity" means the aggregate toxic effect of an effluent measured directly by a toxicity test.

9 VAC 25-31-100. Application for a permit.

A. Duty to apply. Any person who discharges or proposes to discharge pollutants or who owns or operates a sludge-only facility whose sewage sludge use or disposal practice is regulated by 9 VAC 25-31-420 through 9 VAC 25-31-720 and who does not have an effective permit, except persons covered by general permits, excluded from the requirement for a permit by this chapter, or a user of a privately owned treatment works unless the board requires otherwise, shall submit a complete application to the department in accordance with this section. All concentrated animal feeding operations have a duty to seek coverage under a VPDES permit.

B. Who applies. When a facility or activity is owned by one person but is operated by another person, it is the operator's duty to obtain a permit.

C. Time to apply.

1. Any person proposing a new discharge, shall submit an application at least 180 days before the date on which the discharge is to commence, unless permission for a later date has been granted by the board. Facilities proposing a new discharge of storm water associated with industrial activity shall submit an application 180 days before that facility commences industrial activity which may result in a discharge of storm water associated with that industrial activity. Storm water discharges from construction activities included in subdivision 10 of the definition of storm water associated with industrial activity and storm water discharges associated with small construction activities shall submit applications at least 90 days before the date on which construction is to commence. Different submittal dates may be required under the terms of applicable general permits. Persons proposing a new discharge are encouraged to submit their applications well in advance of the 90 or 180 day requirements to avoid delay. New discharges composed entirely of storm water, other than those dischargers identified in 9 VAC 25-31-120 A 1, shall apply for and obtain a permit according to the application requirements in 9 VAC 25-31-120 F B.

2. All TWTDS whose sewage sludge use or disposal practices are regulated by 9 VAC 25-31-420 through 9 VAC 25-31-720 must submit permit applications according to the applicable schedule in subdivision 2 a or b of this subsection.

a. A TWTDS with a currently effective VPDES permit must submit a permit application at the time of its next VPDES permit renewal application. Such information must be submitted in accordance with subsection D of this section.

b. Any other TWTDS not addressed under subdivision 2 a of this subsection must submit the information listed in subdivisions 2 b (1) through (5) of this subsection to the department within one year after publication of a standard applicable to its sewage sludge use or disposal practice(s), using a form provided by the department. The board will determine when such TWTDS must submit a full permit application.

(1) The TWTDS's name, mailing address, location, and status as federal, state, private, public or other entity;

(2) The applicant's name, address, telephone number, and ownership status;

(3) A description of the sewage sludge use or disposal practices. Unless the sewage sludge meets the requirements of subdivision P 8 d of this section, the description must include the name and address of any facility where sewage sludge is sent for treatment or disposal and the location of any land application sites;

(4) Annual amount of sewage sludge generated, treated, used or disposed (estimated dry weight basis); and

(5) The most recent data the TWTDS may have on the quality of the sewage sludge.

c. Notwithstanding subdivision 2 a or b of this subsection, the board may require permit applications from any TWTDS at any time if the board determines that a permit is necessary to protect public health and the environment from any potential adverse effects that may occur from toxic pollutants in sewage sludge.

d. Any TWTDS that commences operations after promulgation of an applicable standard for sewage sludge use or disposal shall submit an application to the department at least 180 days prior to the date proposed for commencing operations.

D. Duty to reapply. All permittees with a currently effective permit shall submit a new application at least 180 days before the expiration date of the existing permit, unless permission for a later date has been granted by the board. The board shall not grant permission for applications to be submitted later than the expiration date of the existing permit.

E. Completeness.

1. The board shall not issue a permit before receiving a complete application for a permit except for VPDES general permits. An application for a permit is complete when the board receives an application form and any supplemental information which are completed to its satisfaction. The completeness of any application for a permit shall be judged independently of the status of any other permit application or permit for the same facility or activity.

2. No application for a VPDES permit to discharge sewage into or adjacent to state waters from a privately owned treatment works serving, or designed to serve, 50 or more residences shall be considered complete unless the applicant has provided the department with notification from the State Corporation Commission that the applicant is incorporated in the Commonwealth and is in compliance with all regulations and relevant orders of the State Corporation Commission.

3. No application for a new individual VPDES permit authorizing a new discharge of sewage, industrial wastes, or other wastes shall be considered complete unless it contains notification from the county, city, or town in which the discharge is to take place that the location and operation of the discharging facility are consistent with applicable ordinances adopted pursuant to Chapter 22 (§ 15.2-2200 et seq.) of Title 15.2 of the Code of Virginia. The county, city or town shall inform in writing the applicant and the board of the discharging facility's compliance or noncompliance not more than 30 days from receipt by the chief administrative officer, or his agent, of a request from the applicant. Should the county, city or town fail to provide such written notification within 30 days, the requirement for such notification is waived. The provisions of this subsection shall not apply to any discharge for which a valid VPDES permit had been issued prior to March 10, 2000.

4. A permit application shall not be considered complete if the board has waived application requirements under subsection J or P of this section and the EPA has disapproved the waiver application. If a waiver request has been submitted to the EPA more than 210 days prior to permit expiration and the EPA has not disapproved the waiver application 181 days prior to permit expiration, the permit application lacking the information subject to the waiver application shall be considered complete.

F. Information requirements. All applicants for VPDES permits, other than POTWs and other TWTDS, shall provide the following information to the department, using the application form provided by the department (additional information required of applicants is set forth in subsections G through K of this section).

1. The activities conducted by the applicant which require it to obtain a VPDES permit;

2. Name, mailing address, and location of the facility for which the application is submitted;

3. Up to four SIC codes which best reflect the principal products or services provided by the facility;

4. The operator's name, address, telephone number, ownership status, and status as federal, state, private, public, or other entity;

5. Whether the facility is located on Indian lands;

6. A listing of all permits or construction approvals received or applied for under any of the following programs:

a. Hazardous Waste Management program under RCRA (42 USC § 6921);

b. UIC program under SDWA (42 USC § 300h);

c. VPDES program under the CWA and the law;

d. Prevention of Significant Deterioration (PSD) program under the Clean Air Act (42 USC § 4701 et seq.);

e. Nonattainment program under the Clean Air Act (42 USC § 4701 et seq.);

f. National Emission Standards for Hazardous Pollutants (NESHAPS) preconstruction approval under the Clean Air Act (42 USC § 4701 et seq.);

g. Ocean dumping permits under the Marine Protection Research and Sanctuaries Act (33 USC § 14 et seq.);

h. Dredge or fill permits under § 404 of the CWA; and

i. Other relevant environmental permits, including state permits.

7. A topographic map (or other map if a topographic map is unavailable) extending one mile beyond the property boundaries of the source, depicting the facility and each of its intake and discharge structures; each of its hazardous waste treatment, storage, or disposal facilities; each well where fluids from the facility are injected underground; and those wells, springs, other surface water bodies, and drinking water wells listed in public records or otherwise known to the applicant in the map area; and

8. A brief description of the nature of the business.

G. Application requirements for existing manufacturing, commercial, mining, and silvicultural dischargers. Existing manufacturing, commercial mining, and silvicultural dischargers applying for VPDES permits, except for those facilities subject to the requirements of 9 VAC 25-31-100 H, shall provide the following information to the department, using application forms provided by the department.

1. The latitude and longitude of each outfall to the nearest 15 seconds and the name of the receiving water.

2. A line drawing of the water flow through the facility with a water balance, showing operations contributing wastewater to the effluent and treatment units. Similar processes, operations, or production areas may be indicated as a single unit, labeled to correspond to the more detailed identification under subdivision 3 of this subsection. The water balance must show approximate average flows at intake and discharge points and between units, including treatment units. If a water balance cannot be determined (for example, for certain mining activities), the applicant may provide instead a pictorial description of the nature and amount of any sources of water and any collection and treatment measures.

3. A narrative identification of each type of process, operation, or production area which contributes wastewater to the effluent for each outfall, including process wastewater, cooling water, and storm water run-off; the average flow which each process contributes; and a description of the treatment the wastewater receives, including the ultimate disposal of any solid or fluid wastes other than by discharge. Processes, operations, or production areas may be described in general terms (for example, dye-making reactor, distillation tower). For a privately owned treatment works, this information shall include the identity of each user of the treatment works. The average flow of point sources composed of storm water may be estimated. The basis for the rainfall event and the method of estimation must be indicated.

4. If any of the discharges described in subdivision 3 of this subsection are intermittent or seasonal, a description of the frequency, duration and flow rate of each discharge occurrence (except for storm water run-off, spillage or leaks).

5. If an effluent guideline promulgated under § 304 of the CWA applies to the applicant and is expressed in terms of production (or other measure of operation), a reasonable measure of the applicant's actual production reported in the units used in the applicable effluent guideline. The reported measure must reflect the actual production of the facility.

6. If the applicant is subject to any present requirements or compliance schedules for construction, upgrading or operation of waste treatment equipment, an identification of the abatement requirement, a description of the abatement project, and a listing of the required and projected final compliance dates.

7. a. Information on the discharge of pollutants specified in this subdivision (except information on storm water discharges which is to be provided as specified in 9 VAC 25-31-120). When quantitative data for a pollutant are required, the applicant must collect a sample of effluent and analyze it for the pollutant in accordance with analytical methods approved under 40 CFR Part 136 (2000). When no analytical method is approved the applicant may use any suitable method but must provide a description of the method. When an applicant has two or more outfalls with substantially identical effluents, the board may allow the applicant to test only one outfall and report that the quantitative data also apply to the substantially identical outfalls. The requirements in e and f of this subdivision that an applicant must provide quantitative data for certain pollutants known or believed to be present do not apply to pollutants present in a discharge solely as the result of their presence in intake water; however, an applicant must report such pollutants as present. Grab samples must be used for pH, temperature, cyanide, total phenols, residual chlorine, oil and grease, fecal coliform, and fecal streptococcus. For all other pollutants, 24-hour composite samples must be used. However, a minimum of one grab sample may be taken for effluents from holding ponds or other impoundments with a retention period greater than 24 hours. In addition, for discharges other than storm water discharges, the board may waive composite sampling for any outfall for which the applicant demonstrates that the use of an automatic sampler is infeasible and that the minimum of four grab samples will be a representative sample of the effluent being discharged.

b. For storm water discharges, all samples shall be collected from the discharge resulting from a storm event that is greater than 0.1 inch and at least 72 hours from the previously measurable (greater than 0.1 inch rainfall) storm event. Where feasible, the variance in the duration of the event and the total rainfall of the event should not exceed 50% from the average or median rainfall event in that area. For all applicants, a flow-weighted composite shall be taken for either the entire discharge or for the first three hours of the discharge. The flow-weighted composite sample for a storm water discharge may be taken with a continuous sampler or as a combination of a minimum of three sample aliquots taken in each hour of discharge for the entire discharge or for the first three hours of the discharge, with each aliquot being separated by a minimum period of 15 minutes (applicants submitting permit applications for storm water discharges under 9 VAC 25-31-120 D may collect flow-weighted composite samples using different protocols with respect to the time duration between the collection of sample aliquots, subject to the approval of the board). However, a minimum of one grab sample may be taken for storm water discharges from holding ponds or other impoundments with a retention period greater than 24 hours. For a flow-weighted composite sample, only one analysis of the composite of aliquots is required. For storm water discharge samples taken from discharges associated with industrial activities, quantitative data must be reported for the grab sample taken during the first 30 minutes (or as soon thereafter as practicable) of the discharge for all pollutants specified in 9 VAC 25-31-120 C 1. For all storm water permit applicants taking flow-weighted composites, quantitative data must be reported for all pollutants specified in 9 VAC 25-31-120 except pH, temperature, cyanide, total phenols, residual chlorine, oil and grease, fecal coliform, and fecal streptococcus. The board may allow or establish appropriate site-specific sampling procedures or requirements, including sampling locations, the season in which the sampling takes place, the minimum duration between the previous measurable storm event and the storm event sampled, the minimum or maximum level of precipitation required for an appropriate storm event, the form of precipitation sampled (snow melt or rain fall), protocols for collecting samples under 40 CFR Part 136 (2000), and additional time for submitting data on a case-by-case basis. An applicant is expected to know or have reason to believe that a pollutant is present in an effluent based on an evaluation of the expected use, production, or storage of the pollutant, or on any previous analyses for the pollutant. (For example, any pesticide manufactured by a facility may be expected to be present in contaminated storm water run-off from the facility.)

c. Every applicant must report quantitative data for every outfall for the following pollutants:

Biochemical oxygen demand (BOD5)

Chemical oxygen demand

Total organic carbon

Total suspended solids

Ammonia (as N)

Temperature (both winter and summer)

pH

d. The board may waive the reporting requirements for individual point sources or for a particular industry category for one or more of the pollutants listed in subdivision 7 c of this subsection if the applicant has demonstrated that such a waiver is appropriate because information adequate to support issuance of a permit can be obtained with less stringent requirements.

e. Each applicant with processes in one or more primary industry category (see 40 CFR Part 122 Appendix A (2000)) contributing to a discharge must report quantitative data for the following pollutants in each outfall containing process wastewater:

(1) The organic toxic pollutants in the fractions designated in Table I of 40 CFR Part 122 Appendix D (2000) for the applicant's industrial category or categories unless the applicant qualifies as a small business under subdivision 8 of this subsection. Table II of 40 CFR Part 122 Appendix D (2000) lists the organic toxic pollutants in each fraction. The fractions result from the sample preparation required by the analytical procedure which uses gas chromatography/mass spectrometry. A determination that an applicant falls within a particular industrial category for the purposes of selecting fractions for testing is not conclusive as to the applicant's inclusion in that category for any other purposes; and

(2) The pollutants listed in Table III of 40 CFR Part 122 Appendix D (2000) (the toxic metals, cyanide, and total phenols).

f. (1) Each applicant must indicate whether it knows or has reason to believe that any of the pollutants in Table IV of 40 CFR Part 122 Appendix D (2000) (certain conventional and nonconventional pollutants) is discharged from each outfall. If an applicable effluent limitations guideline either directly limits the pollutant or, by its express terms, indirectly limits the pollutant through limitations on an indicator, the applicant must report quantitative data. For every pollutant discharged which is not so limited in an effluent limitations guideline, the applicant must either report quantitative data or briefly describe the reasons the pollutant is expected to be discharged.

(2) Each applicant must indicate whether it knows or has reason to believe that any of the pollutants listed in Table II or Table III of 40 CFR Part 122 Appendix D (2000) (the toxic pollutants and total phenols) for which quantitative data are not otherwise required under subdivision 7 e of this subsection, is discharged from each outfall. For every pollutant expected to be discharged in concentrations of 10 ppb or greater the applicant must report quantitative data. For acrolein, acrylonitrile, 2,4 dinitrophenol, and 2-methyl-4,6 dinitrophenol, where any of these four pollutants are expected to be discharged in concentrations of 100 ppb or greater the applicant must report quantitative data. For every pollutant expected to be discharged in concentrations less than 10 ppb, or in the case of acrolein, acrylonitrile, 2,4 dinitrophenol, and 2-methyl-4,6 dinitrophenol, in concentrations less than 100 ppb, the applicant must either submit quantitative data or briefly describe the reasons the pollutant is expected to be discharged. An applicant qualifying as a small business under subdivision 8 of this subsection is not required to analyze for pollutants listed in Table II of 40 CFR Part 122 Appendix D (2000) (the organic toxic pollutants).

g. Each applicant must indicate whether it knows or has reason to believe that any of the pollutants in Table V of 40 CFR Part 122 Appendix D (2000) (certain hazardous substances and asbestos) are discharged from each outfall. For every pollutant expected to be discharged, the applicant must briefly describe the reasons the pollutant is expected to be discharged, and report any quantitative data it has for any pollutant.

h. Each applicant must report qualitative data, generated using a screening procedure not calibrated with analytical standards, for 2,3,7,8-tetrachlorodibenzo-p-dioxin (TCDD) if it:

(1) Uses or manufactures 2,4,5-trichlorophenoxy acetic acid (2,4,5,-T); 2-(2,4,5-trichlorophenoxy) propanoic acid (Silvex, 2,4,5,-TP); 2-(2,4,5-trichlorophenoxy) ethyl, 2,2-dichloropropionate (Erbon); O,O-dimethyl O-(2,4,5-trichlorophenyl) phosphorothioate (Ronnel); 2,4,5-trichlorophenol (TCP); or hexachlorophene (HCP); or

(2) Knows or has reason to believe that TCDD is or may be present in an effluent.

8. An applicant which qualifies as a small business under one of the following criteria is exempt from the requirements in subdivision 7 e (1) or 7 f (1) of this subsection to submit quantitative data for the pollutants listed in Table II of 40 CFR Part 122 Appendix D (2000) (the organic toxic pollutants):

a. For coal mines, a probable total annual production of less than 100,000 tons per year; or

b. For all other applicants, gross total annual sales averaging less than $100,000 per year (in second quarter 1980 dollars).

9. A listing of any toxic pollutant which the applicant currently uses or manufactures as an intermediate or final product or by-product. The board may waive or modify this requirement for any applicant if the applicant demonstrates that it would be unduly burdensome to identify each toxic pollutant and the board has adequate information to issue the permit.

10. Reserved.

11. An identification of any biological toxicity tests which the applicant knows or has reason to believe have been made within the last three years on any of the applicant's discharges or on a receiving water in relation to a discharge.

12. If a contract laboratory or consulting firm performed any of the analyses required by subdivision 7 of this subsection, the identity of each laboratory or firm and the analyses performed.

13. In addition to the information reported on the application form, applicants shall provide to the board, at its request, such other information, including pertinent plans, specifications, maps and such other relevant information as may be required, in scope and details satisfactory to the board, as the board may reasonably require to assess the discharges of the facility and to determine whether to issue a VPDES permit. The additional information may include additional quantitative data and bioassays to assess the relative toxicity of discharges to aquatic life and requirements to determine the cause of the toxicity.

H. Application requirements for manufacturing, commercial, mining and silvicultural facilities which discharge only nonprocess wastewater. Except for storm water discharges, all manufacturing, commercial, mining and silvicultural dischargers applying for VPDES permits which discharge only nonprocess wastewater not regulated by an effluent limitations guideline or new source performance standard shall provide the following information to the department using application forms provided by the department:

1. Outfall number, latitude and longitude to the nearest 15 seconds, and the name of the receiving water;

2. Date of expected commencement of discharge;

3. An identification of the general type of waste discharged, or expected to be discharged upon commencement of operations, including sanitary wastes, restaurant or cafeteria wastes, or noncontact cooling water. An identification of cooling water additives (if any) that are used or expected to be used upon commencement of operations, along with their composition if existing composition is available;

4. a. Quantitative data for the pollutants or parameters listed below, unless testing is waived by the board. The quantitative data may be data collected over the past 365 days, if they remain representative of current operations, and must include maximum daily value, average daily value, and number of measurements taken. The applicant must collect and analyze samples in accordance with 40 CFR Part 136 (2000). Grab samples must be used for pH, temperature, oil and grease, total residual chlorine, and fecal coliform. For all other pollutants, 24-hour composite samples must be used. New dischargers must include estimates for the pollutants or parameters listed below instead of actual sampling data, along with the source of each estimate. All levels must be reported or estimated as concentration and as total mass, except for flow, pH, and temperature.

(1) Biochemical oxygen demand (BOD5).

(2) Total suspended solids (TSS).

(3) Fecal coliform (if believed present or if sanitary waste is or will be discharged).

(4) Total residual chlorine (if chlorine is used).

(5) Oil and grease.

(6) Chemical oxygen demand (COD) (if noncontact cooling water is or will be discharged).

(7) Total organic carbon (TOC) (if noncontact cooling water is or will be discharged).

(8) Ammonia (as N).

(9) Discharge flow.

(10) pH.

(11) Temperature (winter and summer).

b. The board may waive the testing and reporting requirements for any of the pollutants or flow listed in subdivision 4 a of this subsection if the applicant submits a request for such a waiver before or with his application which demonstrates that information adequate to support issuance of a permit can be obtained through less stringent requirements.

c. If the applicant is a new discharger, he must submit the information required in subdivision 4 a of this subsection by providing quantitative data in accordance with that section no later than two years after commencement of discharge. However, the applicant need not submit testing results which he has already performed and reported under the discharge monitoring requirements of his VPDES permit.

d. The requirements of subdivisions 4 a and 4 c of this subsection that an applicant must provide quantitative data or estimates of certain pollutants do not apply to pollutants present in a discharge solely as a result of their presence in intake water. However, an applicant must report such pollutants as present. Net credit may be provided for the presence of pollutants in intake water if the requirements of 9 VAC 25-31-230 G are met;

5. A description of the frequency of flow and duration of any seasonal or intermittent discharge (except for storm water run-off, leaks, or spills);

6. A brief description of any treatment system used or to be used;

7. Any additional information the applicant wishes to be considered, such as influent data for the purpose of obtaining net credits pursuant to 9 VAC 25-31-230 G;

8. Signature of certifying official under 9 VAC 25-31-110; and

9. Pertinent plans, specifications, maps and such other relevant information as may be required, in scope and details satisfactory to the board.

I. Application requirements for new and existing concentrated animal feeding operations and aquatic animal production facilities. New and existing concentrated animal feeding operations and concentrated aquatic animal production facilities shall provide the following information to the department, using the application form provided by the department:

1. For concentrated animal feeding operations:

a. The name of the owner or operator;

b. The facility location and mailing address;

c. Latitude and longitude of the production area (entrance to the production area);

d. A topographic map of the geographic area in which the CAFO is located showing the specific location of the production area, in lieu of the requirements of subdivision F 7 of this section;

e. Specific information about the number and type of animals, whether in open confinement or housed under roof (beef cattle, broilers, layers, swine weighing 55 pounds or more, swine weighing less than 55 pounds, mature dairy cows, dairy heifers, veal calves, sheep and lambs, horses, ducks, turkeys, other);

f. The type of containment and storage (anaerobic lagoon, roofed storage shed, storage ponds, underfloor pits, above ground storage tanks, below ground storage tanks, concrete pad, impervious soil pad, other) and total capacity for manure, litter, and process wastewater storage (tons/gallons);

g. The total number of acres under control of the applicant available for land application of manure, litter, or process wastewater;

h. Estimated amounts of manure, litter, and process wastewater generated per year (tons/gallons); and

i. For CAFOs that must seek coverage under a permit after December 31, 2006, certification that a nutrient management plan has been completed and will be implemented upon the date of coverage.

2. For concentrated aquatic animal production facilities:

a. The maximum daily and average monthly flow from each outfall;

b. The number of ponds, raceways, and similar structures;

c. The name of the receiving water and the source of intake water;

d. For each species of aquatic animals, the total yearly and maximum harvestable weight;

e. The calendar month of maximum feeding and the total mass of food fed during that month; and

f. Pertinent plans, specifications, maps and such other relevant information as may be required, in scope and details satisfactory to the board.

J. Application requirements for new and existing POTWs and treatment works treating domestic sewage. Unless otherwise indicated, all POTWs and other dischargers designated by the board must provide to the department, at a minimum, the information in this subsection using an application form provided by the department. Permit applicants must submit all information available at the time of permit application. The information may be provided by referencing information previously submitted to the department. The board may waive any requirement of this subsection if it has access to substantially identical information. The board may also waive any requirement of this subsection that is not of material concern for a specific permit, if approved by the regional administrator. The waiver request to the regional administrator must include the board's justification for the waiver. A regional administrator's disapproval of the board's proposed waiver does not constitute final agency action but does provide notice to the board and permit applicant(s) that the EPA may object to any board-issued permit issued in the absence of the required information.

1. All applicants must provide the following information:

a. Name, mailing address, and location of the facility for which the application is submitted;

b. Name, mailing address, and telephone number of the applicant and indication as to whether the applicant is the facility's owner, operator, or both;

c. Identification of all environmental permits or construction approvals received or applied for (including dates) under any of the following programs:

(1) Hazardous Waste Management program under the Resource Conservation and Recovery Act (RCRA), Subpart C;

(2) Underground Injection Control program under the Safe Drinking Water Act (SDWA);

(3) NPDES program under the Clean Water Act (CWA);

(4) Prevention of Significant Deterioration (PSD) program under the Clean Air Act;

(5) Nonattainment program under the Clean Air Act;

(6) National Emission Standards for Hazardous Air Pollutants (NESHAPS) preconstruction approval under the Clean Air Act;

(7) Ocean dumping permits under the Marine Protection Research and Sanctuaries Act;

(8) Dredge or fill permits under § 404 of the CWA; and

(9) Other relevant environmental permits, including state permits;

d. The name and population of each municipal entity served by the facility, including unincorporated connector districts. Indicate whether each municipal entity owns or maintains the collection system and whether the collection system is separate sanitary or combined storm and sanitary, if known;

e. Information concerning whether the facility is located in Indian country and whether the facility discharges to a receiving stream that flows through Indian country;

f. The facility's design flow rate (the wastewater flow rate the plant was built to handle), annual average daily flow rate, and maximum daily flow rate for each of the previous three years;

g. Identification of type(s) of collection system(s) used by the treatment works (i.e., separate sanitary sewers or combined storm and sanitary sewers) and an estimate of the percent of sewer line that each type comprises; and

h. The following information for outfalls to surface waters and other discharge or disposal methods:

(1) For effluent discharges to surface waters, the total number and types of outfalls (e.g., treated effluent, combined sewer overflows, bypasses, constructed emergency overflows);

(2) For wastewater discharged to surface impoundments:

(a) The location of each surface impoundment;

(b) The average daily volume discharged to each surface impoundment; and

(c) Whether the discharge is continuous or intermittent;

(3) For wastewater applied to the land:

(a) The location of each land application site;

(b) The size of each land application site, in acres;

(c) The average daily volume applied to each land application site, in gallons per day; and

(d) Whether land application is continuous or intermittent;

(4) For effluent sent to another facility for treatment prior to discharge:

(a) The means by which the effluent is transported;

(b) The name, mailing address, contact person, and phone number of the organization transporting the discharge, if the transport is provided by a party other than the applicant;

(c) The name, mailing address, contact person, phone number, and VPDES permit number (if any) of the receiving facility; and

(d) The average daily flow rate from this facility into the receiving facility, in millions of gallons per day; and

(5) For wastewater disposed of in a manner not included in subdivisions 1 h (1) through (4) of this subsection (e.g., underground percolation, underground injection):

(a) A description of the disposal method, including the location and size of each disposal site, if applicable;

(b) The annual average daily volume disposed of by this method, in gallons per day; and

(c) Whether disposal through this method is continuous or intermittent;

2. All applicants with a design flow greater than or equal to 0.1 mgd must provide the following information:

a. The current average daily volume of inflow and infiltration, in gallons per day, and steps the facility is taking to minimize inflow and infiltration;

b. A topographic map (or other map if a topographic map is unavailable) extending at least one mile beyond property boundaries of the treatment plant, including all unit processes, and showing:

(1) Treatment plant area and unit processes;

(2) The major pipes or other structures through which wastewater enters the treatment plant and the pipes or other structures through which treated wastewater is discharged from the treatment plant. Include outfalls from bypass piping, if applicable;

(3) Each well where fluids from the treatment plant are injected underground;

(4) Wells, springs, and other surface water bodies listed in public records or otherwise known to the applicant within 1/4 mile of the treatment works' property boundaries;

(5) Sewage sludge management facilities (including on-site treatment, storage, and disposal sites); and

(6) Location at which waste classified as hazardous under RCRA enters the treatment plant by truck, rail, or dedicated pipe;

c. Process flow diagram or schematic.

(1) A diagram showing the processes of the treatment plant, including all bypass piping and all backup power sources or redundancy in the system. This includes a water balance showing all treatment units, including disinfection, and showing daily average flow rates at influent and discharge points, and approximate daily flow rates between treatment units; and

(2) A narrative description of the diagram; and

d. The following information regarding scheduled improvements:

(1) The outfall number of each outfall affected;

(2) A narrative description of each required improvement;

(3) Scheduled or actual dates of completion for the following:

(a) Commencement of construction;

(b) Completion of construction;

(c) Commencement of discharge; and

(d) Attainment of operational level; and

(4) A description of permits and clearances concerning other federal or state requirements;

3. Each applicant must provide the following information for each outfall, including bypass points, through which effluent is discharged, as applicable:

a. The following information about each outfall:

(1) Outfall number;

(2) State, county, and city or town in which outfall is located;

(3) Latitude and longitude, to the nearest second;

(4) Distance from shore and depth below surface;

(5) Average daily flow rate, in million gallons per day;

(6) The following information for each outfall with a seasonal or periodic discharge:

(a) Number of times per year the discharge occurs;

(b) Duration of each discharge;

(c) Flow of each discharge; and

(d) Months in which discharge occurs; and

(7) Whether the outfall is equipped with a diffuser and the type (e.g., high-rate) of diffuser used.

b. The following information, if known, for each outfall through which effluent is discharged to surface waters:

(1) Name of receiving water;

(2) Name of watershed/river/stream system and United States Soil Conservation Service 14-digit watershed code;

(3) Name of State Management/River Basin and United States Geological Survey 8-digit hydrologic cataloging unit code; and

(4) Critical flow of receiving stream and total hardness of receiving stream at critical low flow (if applicable).

c. The following information describing the treatment provided for discharges from each outfall to surface waters:

(1) The highest level of treatment (e.g., primary, equivalent to secondary, secondary, advanced, other) that is provided for the discharge for each outfall and:

(a) Design biochemical oxygen demand (BOD5 or CBOD5) removal (percent);

(b) Design suspended solids (SS) removal (percent); and, where applicable,

(c) Design phosphorus (P) removal (percent);

(d) Design nitrogen (N) removal (percent); and

(e) Any other removals that an advanced treatment system is designed to achieve.

(2) A description of the type of disinfection used, and whether the treatment plant dechlorinates (if disinfection is accomplished through chlorination).

4. Effluent monitoring for specific parameters.

a. As provided in subdivisions 4 b through j of this subsection, all applicants must submit to the department effluent monitoring information for samples taken from each outfall through which effluent is discharged to surface waters, except for CSOs. The board may allow applicants to submit sampling data for only one outfall on a case-by-case basis, where the applicant has two or more outfalls with substantially identical effluent. The board may also allow applicants to composite samples from one or more outfalls that discharge into the same mixing zone.

b. All applicants must sample and analyze for the following pollutants:

(1) Biochemical oxygen demand (BOD5 or CBOD5);

(2) Fecal coliform;

(3) Design flow rate;

(4) pH;

(5) Temperature; and

(6) Total suspended solids.

c. All applicants with a design flow greater than or equal to 0.1 mgd must sample and analyze for the following pollutants:

(1) Ammonia (as N);

(2) Chlorine (total residual, TRC);

(3) Dissolved oxygen;

(4) Nitrate/Nitrite;

(5) Kjeldahl nitrogen;

(6) Oil and grease;

(7) Phosphorus; and

(8) Total dissolved solids.

Facilities that do not use chlorine for disinfection, do not use chlorine elsewhere in the treatment process, and have no reasonable potential to discharge chlorine in their effluent may delete chlorine.

d. All POTWs with a design flow rate equal to or greater than one million gallons per day, all POTWs with approved pretreatment programs or POTWs required to develop a pretreatment program, and other POTWs, as required by the board must sample and analyze for the pollutants listed in Table 2 of 40 CFR Part 122 Appendix J (2000), and for any other pollutants for which the board or EPA have established water quality standards applicable to the receiving waters.

e. The board may require sampling for additional pollutants, as appropriate, on a case-by-case basis.

f. Applicants must provide data from a minimum of three samples taken within 4-1/2 years prior to the date of the permit application. Samples must be representative of the seasonal variation in the discharge from each outfall. Existing data may be used, if available, in lieu of sampling done solely for the purpose of this application. The board may require additional samples, as appropriate, on a case-by-case basis.

g. All existing data for pollutants specified in subdivisions 4 b through e of this subsection that is collected within 4-1/2 years of the application must be included in the pollutant data summary submitted by the applicant. If, however, the applicant samples for a specific pollutant on a monthly or more frequent basis, it is only necessary, for such pollutant, to summarize all data collected within one year of the application.

h. Applicants must collect samples of effluent and analyze such samples for pollutants in accordance with analytical methods approved under 40 CFR Part 136 (2000) unless an alternative is specified in the existing VPDES permit. Grab samples must be used for pH, temperature, cyanide, total phenols, residual chlorine, oil and grease, and fecal coliform. For all other pollutants, 24-hour composite samples must be used. For a composite sample, only one analysis of the composite of aliquots is required.

i. The effluent monitoring data provided must include at least the following information for each parameter:

(1) Maximum daily discharge, expressed as concentration or mass, based upon actual sample values;

(2) Average daily discharge for all samples, expressed as concentration or mass, and the number of samples used to obtain this value;

(3) The analytical method used; and

(4) The threshold level (i.e., method detection limit, minimum level, or other designated method endpoints) for the analytical method used.

j. Unless otherwise required by the board, metals must be reported as total recoverable.

5. Effluent monitoring for whole effluent toxicity.

a. All applicants must provide an identification of any whole effluent toxicity tests conducted during the 4-1/2 years prior to the date of the application on any of the applicant's discharges or on any receiving water near the discharge.

b. As provided in subdivisions 5 c through i of this subsection, the following applicants must submit to the department the results of valid whole effluent toxicity tests for acute or chronic toxicity for samples taken from each outfall through which effluent is discharged to surface waters, except for combined sewer overflows:

(1) All POTWs with design flow rates greater than or equal to one million gallons per day;

(2) All POTWs with approved pretreatment programs or POTWs required to develop a pretreatment program;

(3) Other POTWs, as required by the board, based on consideration of the following factors:

(a) The variability of the pollutants or pollutant parameters in the POTW effluent (based on chemical-specific information, the type of treatment plant, and types of industrial contributors);

(b) The ratio of effluent flow to receiving stream flow;

(c) Existing controls on point or nonpoint sources, including total maximum daily load calculations for the receiving stream segment and the relative contribution of the POTW;

(d) Receiving stream characteristics, including possible or known water quality impairment, and whether the POTW discharges to a coastal water, or a water designated as an outstanding natural resource water; or

(e) Other considerations (including, but not limited to, the history of toxic impacts and compliance problems at the POTW) that the board determines could cause or contribute to adverse water quality impacts.

c. Where the POTW has two or more outfalls with substantially identical effluent discharging to the same receiving stream segment, the board may allow applicants to submit whole effluent toxicity data for only one outfall on a case-by-case basis. The board may also allow applicants to composite samples from one or more outfalls that discharge into the same mixing zone.

d. Each applicant required to perform whole effluent toxicity testing pursuant to subdivision 5 b of this subsection must provide:

(1) Results of a minimum of four quarterly tests for a year, from the year preceding the permit application; or

(2) Results from four tests performed at least annually in the 4-1/2 year period prior to the application, provided the results show no appreciable toxicity using a safety factor determined by the board.

e. Applicants must conduct tests with multiple species (no less than two species, e.g., fish, invertebrate, plant) and test for acute or chronic toxicity, depending on the range of receiving water dilution. The board recommends that applicants conduct acute or chronic testing based on the following dilutions: (i) acute toxicity testing if the dilution of the effluent is greater than 100:1 at the edge of the mixing zone or (ii) chronic toxicity testing if the dilution of the effluent is less than or equal to 100:1 at the edge of the mixing zone.

f. Each applicant required to perform whole effluent toxicity testing pursuant to subdivision 5 b of this subsection must provide the number of chronic or acute whole effluent toxicity tests that have been conducted since the last permit reissuance.

g. Applicants must provide the results using the form provided by the department, or test summaries if available and comprehensive, for each whole effluent toxicity test conducted pursuant to subdivision 5 b of this subsection for which such information has not been reported previously to the department.

h. Whole effluent toxicity testing conducted pursuant to subdivision 5 b of this subsection must be conducted using methods approved under 40 CFR Part 136 (2000), as directed by the board.

i. For whole effluent toxicity data submitted to the department within 4-1/2 years prior to the date of the application, applicants must provide the dates on which the data were submitted and a summary of the results.

j. Each POTW required to perform whole effluent toxicity testing pursuant to subdivision 5 b of this subsection must provide any information on the cause of toxicity and written details of any toxicity reduction evaluation conducted, if any whole effluent toxicity test conducted within the past 4-1/2 years revealed toxicity.

6. Applicants must submit the following information about industrial discharges to the POTW:

a. Number of significant industrial users (SIUs) and categorical industrial users (CIUs) discharging to the POTW; and

b. POTWs with one or more SIUs shall provide the following information for each SIU, as defined in 9 VAC 25-31-10, that discharges to the POTW:

(1) Name and mailing address;

(2) Description of all industrial processes that affect or contribute to the SIU's discharge;

(3) Principal products and raw materials of the SIU that affect or contribute to the SIU's discharge;

(4) Average daily volume of wastewater discharged, indicating the amount attributable to process flow and nonprocess flow;

(5) Whether the SIU is subject to local limits;

(6) Whether the SIU is subject to categorical standards and, if so, under which category and subcategory; and

(7) Whether any problems at the POTW (e.g., upsets, pass through, interference) have been attributed to the SIU in the past 4-1/2 years.

c. The information required in subdivisions 6 a and b of this subsection may be waived by the board for POTWs with pretreatment programs if the applicant has submitted either of the following that contain information substantially identical to that required in subdivisions 6 a and b of this subsection:

(1) An annual report submitted within one year of the application; or

(2) A pretreatment program.

7. Discharges from hazardous waste generators and from waste cleanup or remediation sites. POTWs receiving Resource Conservation and Recovery Act (RCRA), Comprehensive Environmental Response, Compensation, and Liability Act (CERCLA), or RCRA Corrective Action wastes or wastes generated at another type of cleanup or remediation site must provide the following information:

a. If the POTW receives, or has been notified that it will receive, by truck, rail, or dedicated pipe any wastes that are regulated as RCRA hazardous wastes pursuant to 40 CFR Part 261 (2000), the applicant must report the following:

(1) The method by which the waste is received (i.e., whether by truck, rail, or dedicated pipe); and

(2) The hazardous waste number and amount received annually of each hazardous waste.

b. If the POTW receives, or has been notified that it will receive, wastewaters that originate from remedial activities, including those undertaken pursuant to CERCLA and § 3004(u) or 3008(h) of RCRA, the applicant must report the following:

(1) The identity and description of the site or facility at which the wastewater originates;

(2) The identities of the wastewater's hazardous constituents, as listed in Appendix VIII of 40 CFR Part 261 (2000), if known; and

(3) The extent of treatment, if any, the wastewater receives or will receive before entering the POTW.

c. Applicants are exempt from the requirements of subdivision 7 b of this subsection if they receive no more than 15 kilograms per month of hazardous wastes, unless the wastes are acute hazardous wastes as specified in 40 CFR 261.30(d) and 261.33(e) (2000).

8. Each applicant with combined sewer systems must provide the following information:

a. The following information regarding the combined sewer system:

(1) A map indicating the location of the following:

(a) All CSO discharge points;

(b) Sensitive use areas potentially affected by CSOs (e.g., beaches, drinking water supplies, shellfish beds, sensitive aquatic ecosystems, and outstanding national resource waters); and

(c) Waters supporting threatened and endangered species potentially affected by CSOs; and

(2) A diagram of the combined sewer collection system that includes the following information:

(a) The location of major sewer trunk lines, both combined and separate sanitary;

(b) The locations of points where separate sanitary sewers feed into the combined sewer system;

(c) In-line and off-line storage structures;

(d) The locations of flow-regulating devices; and

(e) The locations of pump stations.

b. The following information for each CSO discharge point covered by the permit application:

(1) The following information on each outfall:

(a) Outfall number;

(b) State, county, and city or town in which outfall is located;

(c) Latitude and longitude, to the nearest second;

(d) Distance from shore and depth below surface;

(e) Whether the applicant monitored any of the following in the past year for this CSO: (i) rainfall, (ii) CSO flow volume, (iii) CSO pollutant concentrations, (iv) receiving water quality, or (v) CSO frequency; and

(f) The number of storm events monitored in the past year;

(2) The following information about CSO overflows from each outfall:

(a) The number of events in the past year;

(b) The average duration per event, if available;

(c) The average volume per CSO event, if available; and

(d) The minimum rainfall that caused a CSO event, if available, in the last year;

(3) The following information about receiving waters:

(a) Name of receiving water;

(b) Name of watershed/stream system and the United States Soil Conservation Service watershed (14-digit) code, if known; and

(c) Name of State Management/River Basin and the United States Geological Survey hydrologic cataloging unit (8-digit) code, if known; and

(4) A description of any known water quality impacts on the receiving water caused by the CSO (e.g., permanent or intermittent beach closings, permanent or intermittent shellfish bed closings, fish kills, fish advisories, other recreational loss, or exceedance of any applicable state water quality standard).

9. All applicants must provide the name, mailing address, telephone number, and responsibilities of all contractors responsible for any operational or maintenance aspects of the facility.

10. All applications must be signed by a certifying official in compliance with 9 VAC 25-31-110.

11. Pertinent plans, specifications, maps and such other relevant information as may be required, in scope and details satisfactory to the board.

K. Application requirements for new sources and new discharges. New manufacturing, commercial, mining and silvicultural dischargers applying for VPDES permits (except for new discharges of facilities subject to the requirements of subsection H of this section or new discharges of storm water associated with industrial activity which are subject to the requirements of 9 VAC 25-31-120 C 1 and this subsection (except as provided by 9 VAC 25-31-120 C 1 b) shall provide the following information to the department, using the application forms provided by the department:

1. The expected outfall location in latitude and longitude to the nearest 15 seconds and the name of the receiving water;

2. The expected date of commencement of discharge;

3. a. Description of the treatment that the wastewater will receive, along with all operations contributing wastewater to the effluent, average flow contributed by each operation, and the ultimate disposal of any solid or liquid wastes not discharged;

b. A line drawing of the water flow through the facility with a water balance as described in subdivision G 2;

c. If any of the expected discharges will be intermittent or seasonal, a description of the frequency, duration and maximum daily flow rate of each discharge occurrence (except for storm water run-off, spillage, or leaks); and

4. If a new source performance standard promulgated under § 306 of the CWA or an effluent limitation guideline applies to the applicant and is expressed in terms of production (or other measure of operation), a reasonable measure of the applicant's expected actual production reported in the units used in the applicable effluent guideline or new source performance standard for each of the first three years. Alternative estimates may also be submitted if production is likely to vary;

5. The requirements in subdivisions H 4 a, b, and c of this section that an applicant must provide estimates of certain pollutants expected to be present do not apply to pollutants present in a discharge solely as a result of their presence in intake water; however, an applicant must report such pollutants as present. Net credits may be provided for the presence of pollutants in intake water if the requirements of 9 VAC 25-31-230 G are met. All levels (except for discharge flow, temperature, and pH) must be estimated as concentration and as total mass.

a. Each applicant must report estimated daily maximum, daily average, and source of information for each outfall for the following pollutants or parameters. The board may waive the reporting requirements for any of these pollutants and parameters if the applicant submits a request for such a waiver before or with his application which demonstrates that information adequate to support issuance of the permit can be obtained through less stringent reporting requirements.

(1) Biochemical oxygen demand (BOD).

(2) Chemical oxygen demand (COD).

(3) Total organic carbon (TOC).

(4) Total suspended solids (TSS).

(5) Flow.

(6) Ammonia (as N).

(7) Temperature (winter and summer).

(8) pH.

b. Each applicant must report estimated daily maximum, daily average, and source of information for each outfall for the following pollutants, if the applicant knows or has reason to believe they will be present or if they are limited by an effluent limitation guideline or new source performance standard either directly or indirectly through limitations on an indicator pollutant: all pollutants in Table IV of 40 CFR Part 122 Appendix D (2000) (certain conventional and nonconventional pollutants).

c. Each applicant must report estimated daily maximum, daily average and source of information for the following pollutants if he knows or has reason to believe that they will be present in the discharges from any outfall:

(1) The pollutants listed in Table III of 40 CFR Part 122 Appendix D (2000) (the toxic metals, in the discharge from any outfall, Total cyanide, and total phenols);

(2) The organic toxic pollutants in Table II of 40 CFR Part 122 Appendix D (2000) (except bis (chloromethyl) ether, dichlorofluoromethane and trichlorofluoromethane). This requirement is waived for applicants with expected gross sales of less than $100,000 per year for the next three years, and for coal mines with expected average production of less than 100,000 tons of coal per year.

d. The applicant is required to report that 2,3,7,8 Tetrachlorodibenzo-P-Dioxin (TCDD) may be discharged if he uses or manufactures one of the following compounds, or if he knows or has reason to believe that TCDD will or may be present in an effluent:

(1) 2,4,5-trichlorophenoxy acetic acid (2,4,5-T) (CAS #93-76-5);

(2) (2) 2-(2,4,5-trichlorophenoxy) propanoic acid (Silvex, 2,4,5-TP) (CAS #93-72-1);

(3) 2-(2,4,5-trichlorophenoxy) ethyl 2,2-dichloropropionate (Erbon) (CAS #136-25-4);

(4) 0,0-dimethyl 0-(2,4,5-trichlorophenyl) phosphorothioate (Ronnel) (CAS #299-84-3);

(5) 2,4,5-trichlorophenol (TCP) (CAS #95-95-4); or

(6) Hexachlorophene (HCP) (CAS #70-30-4);

e. Each applicant must report any pollutants listed in Table V of 40 CFR Part 122 Appendix D (2000) (certain hazardous substances) if he believes they will be present in any outfall (no quantitative estimates are required unless they are already available).

f. No later than two years after the commencement of discharge from the proposed facility, the applicant is required to submit the information required in subsection G of this section. However, the applicant need not complete those portions of subsection G of this section requiring tests which he has already performed and reported under the discharge monitoring requirements of his VPDES permit;

6. Each applicant must report the existence of any technical evaluation concerning his wastewater treatment, along with the name and location of similar plants of which he has knowledge;

7. Any optional information the permittee wishes to have considered;

8. Signature of certifying official under 9 VAC 25-31-110; and

9. Pertinent plans, specifications, maps and such other relevant information as may be required, in scope and details satisfactory to the board.

L. Variance requests by non-POTWs. A discharger which is not a publicly owned treatment works (POTW) may request a variance from otherwise applicable effluent limitations under any of the following statutory or regulatory provisions within the times specified in this subsection:

1. Fundamentally different factors.

a. A request for a variance based on the presence of fundamentally different factors from those on which the effluent limitations guideline was based shall be filed as follows:

(1) For a request from best practicable control technology currently available (BPT), by the close of the public comment period for the draft permit; or

(2) For a request from best available technology economically achievable (BAT) and/or best conventional pollutant control technology (BCT), by no later than:

(a) July 3, 1989, for a request based on an effluent limitation guideline promulgated before February 4, 1987, to the extent July 3, 1989, is not later than that provided under previously promulgated regulations; or

(b) 180 days after the date on which an effluent limitation guideline is published in the Federal Register for a request based on an effluent limitation guideline promulgated on or after February 4, 1987.

b. The request shall explain how the requirements of the applicable regulatory or statutory criteria have been met.

2. A request for a variance from the BAT requirements for CWA § 301(b)(2)(F) pollutants (commonly called nonconventional pollutants) pursuant to § 301(c) of the CWA because of the economic capability of the owner or operator, or pursuant to § 301(g) of the CWA (provided however that a § 301(g) variance may only be requested for ammonia; chlorine; color; iron; total phenols (when determined by the Administrator to be a pollutant covered by § 301(b)(2)(F) of the CWA) and any other pollutant which the administrator lists under § 301(g)(4) of the CWA) must be made as follows:

a. For those requests for a variance from an effluent limitation based upon an effluent limitation guideline by:

(1) Submitting an initial request to the regional administrator, as well as to the department, stating the name of the discharger, the permit number, the outfall number(s), the applicable effluent guideline, and whether the discharger is requesting a §§ 301(c) or 301(g) of the CWA modification, or both. This request must have been filed not later than 270 days after promulgation of an applicable effluent limitation guideline; and

(2) Submitting a completed request no later than the close of the public comment period for the draft permit demonstrating that: (i) all reasonable ascertainable issues have been raised and all reasonably available arguments and materials supporting their position have been submitted; and (ii) that the applicable requirements of 40 CFR Part 125 (2000) have been met. Notwithstanding this provision, the complete application for a request under§ 301(g) of the CWA shall be filed 180 days before EPA must make a decision (unless the Regional Division Director establishes a shorter or longer period); or

b. For those requests for a variance from effluent limitations not based on effluent limitation guidelines, the request need only comply with subdivision 2 a (2) of this subsection and need not be preceded by an initial request under subdivision 2 a (1) of this subsection.

3. A modification under § 302(b)(2) of the CWA of requirements under § 302(a) of the CWA for achieving water quality related effluent limitations may be requested no later than the close of the public comment period for the draft permit on the permit from which the modification is sought.

4. A variance for alternate effluent limitations for the thermal component of any discharge must be filed with a timely application for a permit under this section, except that if thermal effluent limitations are established on a case-by-case basis or are based on water quality standards the request for a variance may be filed by the close of the public comment period for the draft permit. A copy of the request shall be sent simultaneously to the department.

M. Variance requests by POTWs. A discharger which is a publicly owned treatment works (POTW) may request a variance from otherwise applicable effluent limitations under any of the following statutory provisions as specified in this paragraph:

1. A request for a modification under § 301(h) of the CWA of requirements of § 301(b)(1)(B) of the CWA for discharges into marine waters must be filed in accordance with the requirements of 40 CFR Part 125, Subpart G (2000).

2. A modification under § 302(b)(2) of the CWA of the requirements under § 302(a) of the CWA for achieving water quality based effluent limitations shall be requested no later than the close of the public comment period for the draft permit on the permit from which the modification is sought.

N. Expedited variance procedures and time extensions.

1. Notwithstanding the time requirements in subsections L and M of this section, the board may notify a permit applicant before a draft permit is issued that the draft permit will likely contain limitations which are eligible for variances. In the notice the board may require the applicant as a condition of consideration of any potential variance request to submit a request explaining how the requirements of 40 CFR Part 125 (2000) applicable to the variance have been met and may require its submission within a specified reasonable time after receipt of the notice. The notice may be sent before the permit application has been submitted. The draft or final permit may contain the alternative limitations which may become effective upon final grant of the variance.

2. A discharger who cannot file a timely complete request required under subdivisions L 2 a (2) or L 2 b of this section may request an extension. The extension may be granted or denied at the discretion of the board. Extensions shall be no more than six months in duration.

O. Recordkeeping. Except for information required by subdivision C 2 of this section, which shall be retained for a period of at least five years from the date the application is signed (or longer as required by Part VI (9 VAC 25-31-420 et seq.) of this chapter), applicants shall keep records of all data used to complete permit applications and any supplemental information submitted under this section for a period of at least three years from the date the application is signed.

P. Sewage sludge management. All TWTDS subject to subdivision C 2 a of this section must provide the information in this subsection to the department using an application form approved by the department. New applicants must submit all information available at the time of permit application. The information may be provided by referencing information previously submitted to the department. The board may waive any requirement of this subsection if it has access to substantially identical information. The board may also waive any requirement of this subsection that is not of material concern for a specific permit, if approved by the regional administrator. The waiver request to the regional administrator must include the board's justification for the waiver. A regional administrator's disapproval of the board's proposed waiver does not constitute final agency action, but does provide notice to the board and the permit applicant that the EPA may object to any board issued permit issued in the absence of the required information.

1. All applicants must submit the following information:

a. The name, mailing address, and location of the TWTDS for which the application is submitted;

b. Whether the facility is a Class I Sludge Management Facility;

c. The design flow rate (in million gallons per day);

d. The total population served;

e. The TWTDS's status as federal, state, private, public, or other entity;

f. The name, mailing address, and telephone number of the applicant; and

g. Indication whether the applicant is the owner, operator, or both.

2. All applicants must submit the facility's VPDES permit number, if applicable, and a listing of all other federal, state, and local permits or construction approvals received or applied for under any of the following programs:

a. Hazardous Waste Management program under the Resource Conservation and Recovery Act (RCRA);

b. UIC program under the Safe Drinking Water Act (SDWA);

c. NPDES program under the Clean Water Act (CWA);

d. Prevention of Significant Deterioration (PSD) program under the Clean Air Act;

e. Nonattainment program under the Clean Air Act;

f. National Emission Standards for Hazardous Air Pollutants (NESHAPS) preconstruction approval under the Clean Air Act;

g. Dredge or fill permits under § 404 of the CWA;

h. Other relevant environmental permits, including state or local permits.

3. All applicants must identify any generation, treatment, storage, land application, or disposal of sewage sludge that occurs in Indian country.

4. All applicants must submit a topographic map (or other map if a topographic map is unavailable) extending one mile beyond property boundaries of the facility and showing the following information:

a. All sewage sludge management facilities, including on-site treatment, storage, and disposal sites; and

b. Wells, springs, and other surface water bodies that are within 1/4 mile of the property boundaries and listed in public records or otherwise known to the applicant.

5. All applicants must submit a line drawing and/or a narrative description that identifies all sewage sludge management practices employed during the term of the permit, including all units used for collecting, dewatering, storing, or treating sewage sludge; the destination(s) of all liquids and solids leaving each such unit; and all processes used for pathogen reduction and vector attraction reduction.

6. The applicant must submit sewage sludge monitoring data for the pollutants for which limits in sewage sludge have been established in Part VI (9 VAC 25-31-420 et seq.) of this chapter for the applicant's use or disposal practices on the date of permit application with the following conditions:

a. The board may require sampling for additional pollutants, as appropriate, on a case-by-case basis.

b. Applicants must provide data from a minimum of three samples taken within 4-1/2 years prior to the date of the permit application. Samples must be representative of the sewage sludge and should be taken at least one month apart. Existing data may be used in lieu of sampling done solely for the purpose of this application.

c. Applicants must collect and analyze samples in accordance with analytical methods specified in 9 VAC 25-31-490 unless an alternative has been specified in an existing sewage sludge permit.

d. The monitoring data provided must include at least the following information for each parameter:

(1) Average monthly concentration for all samples (mg/kg dry weight), based upon actual sample values;

(2) The analytical method used; and

(3) The method detection level.

7. If the applicant is a person who prepares sewage sludge, as defined in 9 VAC 25-31-500, the applicant must provide the following information:

a. If the applicant's facility generates sewage sludge, the total dry metric tons per 365-day period generated at the facility.

b. If the applicant's facility receives sewage sludge from another facility, the following information for each facility from which sewage sludge is received:

(1) The name, mailing address, and location of the other facility;

(2) The total dry metric tons per 365-day period received from the other facility; and

(3) A description of any treatment processes occurring at the other facility, including blending activities and treatment to reduce pathogens or vector attraction characteristics.

c. If the applicant's facility changes the quality of sewage sludge through blending, treatment, or other activities, the following information:

(1) Whether the Class A pathogen reduction requirements in 9 VAC 25-31-710 A or the Class B pathogen reduction requirements in 9 VAC 25-31-710 B are met, and a description of any treatment processes used to reduce pathogens in sewage sludge;

(2) Whether any of the vector attraction reduction options of 9 VAC 25-31-720 B 1 through 8 are met, and a description of any treatment processes used to reduce vector attraction properties in sewage sludge; and

(3) A description of any other blending, treatment, or other activities that change the quality of sewage sludge.

d. If sewage sludge from the applicant's facility meets the ceiling concentrations in 9 VAC 25-31-540 B 1, the pollutant concentrations in 9 VAC 25-31-540 B 3, the Class A pathogen requirements in 9 VAC 25-31-710 A, and one of the vector attraction reduction requirements in 9 VAC 25-31-720 B 1 through 8, and if the sewage sludge is applied to the land, the applicant must provide the total dry metric tons per 365-day period of sewage sludge subject to this subsection that is applied to the land.

e. If sewage sludge from the applicant's facility is sold or given away in a bag or other container for application to the land, and the sewage sludge is not subject to subdivision 7 d of this subsection, the applicant must provide the following information:

(1) The total dry metric tons per 365-day period of sewage sludge subject to this subsection that is sold or given away in a bag or other container for application to the land; and

(2) A copy of all labels or notices that accompany the sewage sludge being sold or given away.

f. If sewage sludge from the applicant's facility is provided to another person who prepares sewage sludge, as defined in 9 VAC 25-31-500, and the sewage sludge is not subject to subdivision 7 d of this subsection, the applicant must provide the following information for each facility receiving the sewage sludge:

(1) The name and mailing address of the receiving facility;

(2) The total dry metric tons per 365-day period of sewage sludge subject to this subsection that the applicant provides to the receiving facility;

(3) A description of any treatment processes occurring at the receiving facility, including blending activities and treatment to reduce pathogens or vector attraction characteristic;

(4) A copy of the notice and necessary information that the applicant is required to provide the receiving facility under 9 VAC 25-31-530 G; and

(5) If the receiving facility places sewage sludge in bags or containers for sale or give-away to application to the land, a copy of any labels or notices that accompany the sewage sludge.

8. If sewage sludge from the applicant's facility is applied to the land in bulk form and is not subject to subdivision 7 d, e or f of this subsection, the applicant must provide the following information:

a. The total dry metric tons per 365-day period of sewage sludge subject to this subsection that is applied to the land.

b. If any land application sites are located in states other than the state where the sewage sludge is prepared, a description of how the applicant will notify the permitting authority for the state(s) where the land application sites are located.

c. The following information for each land application site that has been identified at the time of permit application:

(1) The name (if any), and location for the land application site;

(2) The site's latitude and longitude to the nearest second, and method of determination;

(3) A topographic map (or other map if a topographic map is unavailable) that shows the site's location;

(4) The name, mailing address, and telephone number of the site owner, if different from the applicant;

(5) The name, mailing address, and telephone number of the person who applies sewage sludge to the site, if different from the applicant;

(6) Whether the site is agricultural land, forest, a public contact site, or a reclamation site, as such site types are defined in 9 VAC 25-31-500;

(7) The type of vegetation grown on the site, if known, and the nitrogen requirement for this vegetation;

(8) Whether either of the vector attraction reduction options of 9 VAC 25-31-720 B 9 or 10 is met at the site, and a description of any procedures employed at the time of use to reduce vector attraction properties in sewage sludge; and

(9) Other information that describes how the site will be managed, as specified by the board.

d. The following information for each land application site that has been identified at the time of permit application, if the applicant intends to apply bulk sewage sludge subject to the cumulative pollutant loading rates in 9 VAC 25-31-540 B 2 to the site:

(1) Whether the applicant has contacted the permitting authority in the state where the bulk sewage sludge subject to 9 VAC 25-31-540 B 2 will be applied, to ascertain whether bulk sewage sludge subject to 9 VAC 25-31-540 B 2 has been applied to the site on or since July 20, 1993, and if so, the name of the permitting authority and the name and phone number of a contact person at the permitting authority;

(2) Identification of facilities other than the applicant's facility that have sent, or are sending, sewage sludge subject to the cumulative pollutant loading rates in 9 VAC 25-31-540 B 2 to the site since July 20, 1993, if, based on the inquiry in subdivision 8 d (1) of this subsection, bulk sewage sludge subject to cumulative pollutant loading rates in 9 VAC 25-31-540 B 2 has been applied to the site since July 20, 1993.

e. If not all land application sites have been identified at the time of permit application, the applicant must submit a land application plan that, at a minimum:

(1) Describes the geographical area covered by the plan;

(2) Identifies the site selection criteria;

(3) Describes how the site(s) will be managed;

(4) Provides for advance notice to the board of specific land application sites and reasonable time for the board to object prior to land application of the sewage sludge; and

(5) Provides for advance public notice of land application sites in a newspaper of general circulation in the area of the land application site.

9. If sewage sludge from the applicant's facility is placed on a surface disposal site, the applicant must provide the following information:

a. The total dry metric tons of sewage sludge from the applicant's facility that is placed on surface disposal sites per 365-day period.

b. The following information for each surface disposal site receiving sewage sludge from the applicant's facility that the applicant does not own or operate:

(1) The site name or number, contact person, mailing address, and telephone number for the surface disposal site; and

(2) The total dry metric tons from the applicant's facility per 365-day period placed on the surface disposal site.

c. The following information for each active sewage sludge unit at each surface disposal site that the applicant owns or operates:

(1) The name or number and the location of the active sewage sludge unit;

(2) The unit's latitude and longitude to the nearest second, and method of determination;

(3) If not already provided, a topographic map (or other map if a topographic map is unavailable) that shows the unit's location;

(4) The total dry metric tons placed on the active sewage sludge unit per 365-day period;

(5) The total dry metric tons placed on the active sewage sludge unit over the life of the unit;

(6) A description of any liner for the active sewage sludge unit, including whether it has a maximum permeability of 1 X 10-7cm/sec;

(7) A description of any leachate collection system for the active sewage sludge unit, including the method used for leachate disposal, and any federal, state, and local permit number(s) for leachate disposal;

(8) If the active sewage sludge unit is less than 150 meters from the property line of the surface disposal site, the actual distance from the unit boundary to the site property line;

(9) The remaining capacity (dry metric tons) for the active sewage sludge unit;

(10) The date on which the active sewage sludge unit is expected to close, if such a date has been identified;

(11) The following information for any other facility that sends sewage sludge to the active sewage sludge unit:

(a) The name, contact person, and mailing address of the facility; and

(b) Available information regarding the quality of the sewage sludge received from the facility, including any treatment at the facility to reduce pathogens or vector attraction characteristics;

(12) Whether any of the vector attraction reduction options of 9 VAC 25-31-720 B 9 through 11 is met at the active sewage sludge unit, and a description of any procedures employed at the time of disposal to reduce vector attraction properties in sewage sludge;

(13) The following information, as applicable to any groundwater monitoring occurring at the active sewage sludge unit:

(a) A description of any groundwater monitoring occurring at the active sewage sludge unit;

(b) Any available groundwater monitoring data, with a description of the well locations and approximate depth to groundwater;

(c) A copy of any groundwater monitoring plan that has been prepared for the active sewage sludge unit;

(d) A copy of any certification that has been obtained from a qualified groundwater scientist that the aquifer has not been contaminated; and

(14) If site-specific pollutant limits are being sought for the sewage sludge placed on this active sewage sludge unit, information to support such a request.

10. If sewage sludge from the applicant's facility is fired in a sewage sludge incinerator, the applicant must provide the following information:

a. The total dry metric tons of sewage sludge from the applicant's facility that is fired in sewage sludge incinerators per 365-day period.

b. The following information for each sewage sludge incinerator firing the applicant's sewage sludge that the applicant does not own or operate:

(1) The name and/or number, contact person, mailing address, and telephone number of the sewage sludge incinerator; and

(2) The total dry metric tons from the applicant's facility per 365-day period fired in the sewage sludge incinerator.

11. If sewage sludge from the applicant's facility is sent to a municipal solid waste landfill (MSWLF), the applicant must provide the following information for each MSWLF to which sewage sludge is sent:

a. The name, contact person, mailing address, location, and all applicable permit numbers of the MSWLF;

b. The total dry metric tons per 365-day period sent from this facility to the MSWLF;

c. A determination of whether the sewage sludge meets applicable requirements for disposal of sewage sludge in a MSWLF, including the results of the paint filter liquids test and any additional requirements that apply on a site-specific basis; and

d. Information, if known, indicating whether the MSWLF complies with criteria set forth in the Virginia Solid Waste Management Regulations, 9 VAC 20-80-10 et seq.

12. All applicants must provide the name, mailing address, telephone number, and responsibilities of all contractors responsible for any operational or maintenance aspects of the facility related to sewage sludge generation, treatment, use, or disposal.

13. At the request of the board, the applicant must provide any other information necessary to determine the appropriate standards for permitting under Part VI (9 VAC 25-31-420 et seq.) of this chapter, and must provide any other information necessary to assess the sewage sludge use and disposal practices, determine whether to issue a permit, or identify appropriate permit requirements; and pertinent plans, specifications, maps and such other relevant information as may be required, in scope and details satisfactory to the board.

14. All applications must be signed by a certifying official in compliance with 9 VAC 25-31-110.

Note 1: Until further notice subdivision G 7 e (1) of this section and the corresponding portions of the VPDES application Form 2C are suspended as they apply to coal mines.

Note 2: Until further notice subdivision G 7 e (1) of this section and the corresponding portions of Item V-C of the VPDES application Form 2C are suspended as they apply to:

a. Testing and reporting for all four organic fractions in the Greige Mills Subcategory of the Textile Mills industry (subpart C-Low water use processing of 40 CFR Part 410 (2000)), and testing and reporting for the pesticide fraction in all other subcategories of this industrial category.

b. Testing and reporting for the volatile, base/neutral and pesticide fractions in the Base and Precious Metals Subcategory of the Ore Mining and Dressing industry (subpart B of 40 CFR Part 440 (2000)), and testing and reporting for all four fractions in all other subcategories of this industrial category.

c. Testing and reporting for all four GC/MS fractions in the Porcelain Enameling industry.

Note 3: Until further notice subdivision G 7 e (1) of this section and the corresponding portions of Item V-C of the VPDES application Form 2C are suspended as they apply to:

a. Testing and reporting for the pesticide fraction in the Tall Oil Rosin Subcategory (subpart D) and Rosin-Based Derivatives Subcategory (subpart F) of the Gum and Wood Chemicals industry (40 CFR Part 454 (2000)), and testing and reporting for the pesticide and base-neutral fractions in all other subcategories of this industrial category.

b. Testing and reporting for the pesticide fraction in the leather tanning and finishing, paint and ink formulation, and photographic supplies industrial categories.

c. Testing and reporting for the acid, base/neutral and pesticide fractions in the petroleum refining industrial category.

d. Testing and reporting for the pesticide fraction in the Papergrade Sulfite Subcategories (subparts J and U) of the Pulp and Paper industry (40 CFR Part 430 (2000)); testing and reporting for the base/neutral and pesticide fractions in the following subcategories: Deink (subpart Q), Dissolving Kraft (subpart F), and Paperboard from Waste Paper (subpart E); testing and reporting for the volatile, base/neutral and pesticide fractions in the following subcategories: BCT Bleached Kraft (subpart H), Semi-Chemical (subparts B and C), and Nonintegrated-Fine Papers (subpart R); and testing and reporting for the acid, base/neutral, and pesticide fractions in the following subcategories: Fine Bleached Kraft (subpart I), Dissolving Sulfite Pulp (subpart K), Groundwood-Fine Papers (subpart O), Market Bleached Kraft (subpart G), Tissue from Wastepaper (subpart T), and Nonintegrated-Tissue Papers (subpart S).

e. Testing and reporting for the base/neutral fraction in the Once-Through Cooling Water, Fly Ash and Bottom Ash Transport Water process wastestreams of the Steam Electric Power Plant industrial category.

9 VAC 25-31-120. Storm water discharges.

A. Permit requirements.

1. Prior to October 1, 1994, discharges composed entirely of storm water shall not be required to obtain a VPDES permit except:

a. A discharge with respect to which a permit has been issued prior to February 4, 1987;

b. A discharge associated with industrial activity; or

c. A discharge from a large municipal separate storm sewer system;

d. A discharge from a medium municipal separate storm sewer system;  or

e. c. A discharge which either the board or the regional administrator determines to contribute to a violation of a water quality standard or is a significant contributor of pollutants to surface waters.  This designation may include a discharge from any conveyance or system of conveyances used for collecting and conveying storm water run-off or a system of discharges from municipal separate storm sewers, except for those discharges from conveyances which do not require a permit under subdivision 2 of this subsection or agricultural storm water run-off which is exempted from the definition of point source.

The board may designate discharges from municipal separate storm sewers on a system-wide or jurisdiction-wide basis.  In making this determination the board may consider the following factors:

(1) The location of the discharge with respect to surface waters;

(2) The size of the discharge;

(3) The quantity and nature of the pollutants discharged to surface waters;  and

(4) Other relevant factors.

2. The board may not require a permit for discharges of storm water run-off from mining operations or oil and gas exploration, production, processing or treatment operations, or transmission facilities, composed entirely of flows which are from conveyances or systems of conveyances (including but not limited to pipes, conduits, ditches, and channels) used for collecting and conveying precipitation run-off and which are not contaminated by contact with or that has not come into contact with, any overburden, raw material, intermediate products, finished product, by-product or waste products located on the site of such operations.

3. a. Permits must be obtained for all discharges from large and medium municipal separate storm sewer systems.

b. The board may either issue one system-wide permit covering all discharges from municipal separate storm sewers within a large or medium municipal storm sewer system or issue distinct permits for appropriate categories of discharges within a large or medium municipal separate storm sewer system including, but not limited to:  all discharges owned or operated by the same municipality;  located within the same jurisdiction;  all discharges within a system that discharge to the same watershed;  discharges within a system that are similar in nature;  or for individual discharges from municipal separate storm sewers within the system.

c. The operator of a discharge from a municipal separate storm sewer which is part of a large or medium municipal separate storm sewer system must either:

(1) Participate in a permit application (to be a permittee or a co-permittee) with one or more other operators of discharges from the large or medium municipal storm sewer system which covers all, or a portion of all, discharges from the municipal separate storm sewer system;

(2) Submit a distinct permit application which only covers discharges from the municipal separate storm sewers for which the operator is responsible;  or

(3) A regional authority may be responsible for submitting a permit application under the following guidelines:

(a) The regional authority together with co-applicants shall have authority over a storm water management program that is in existence, or shall be in existence at the time Part 1 of the application is due;

(b) The permit applicant or co-applicants shall establish their ability to make a timely submission of Part 1 and Part 2 of the municipal application;

(c) Each of the operators of municipal separate storm sewers within large or medium municipal separate storm sewer systems, that are under the purview of the designated regional authority, shall comply with the application requirements of subsection C of this section.

d. One permit application may be submitted for all or a portion of all municipal separate storm sewers within adjacent or interconnected large or medium municipal separate storm sewer systems.  The board may issue one system-wide permit covering all, or a portion of all municipal separate storm sewers in adjacent or interconnected large or medium municipal separate storm sewer systems.

e. Permits for all or a portion of all discharges from large or medium municipal separate storm sewer systems that are issued on a system-wide, jurisdiction-wide, watershed or other basis may specify different conditions relating to different discharges covered by the permit, including different management programs for different drainage areas which contribute storm water to the system.

f. Co-permittees need only comply with permit conditions relating to discharges from the municipal separate storm sewers for which they are operators.

4. 3. In addition to meeting the requirements of subsection B of this section, an operator of a storm water discharge associated with industrial activity which discharges through a large or medium municipal separate storm sewer system shall submit, to the operator of the municipal separate storm sewer system receiving the discharge no later than May 15, 1991, or 180 days prior to commencing such discharge:  the name of the facility;  a contact person and phone number;  the location of the discharge;  a description, including Standard Industrial Classification, which best reflects the principal products or services provided by each facility;  and any existing VPDES permit number.

5. The board may issue permits for municipal separate storm sewers that are designated under subdivision A 1 e of this section on a system-wide basis, jurisdiction-wide basis, watershed basis or other appropriate basis, or may issue permits for individual discharges.

6. 4. For storm water discharges associated with industrial activity from point sources which discharge through a nonmunicipal or nonpublicly owned separate storm sewer system, the board, in its discretion, may issue:  a single VPDES permit, with each discharger a co-permittee to a permit issued to the operator of the portion of the system that discharges into surface waters;  or, individual permits to each discharger of storm water associated with industrial activity through the nonmunicipal conveyance system.

a. All storm water discharges associated with industrial activity that discharge through a storm water discharge system that is not a municipal separate storm sewer must be covered by an individual permit, or a permit issued to the operator of the portion of the system that discharges to surface waters, with each discharger to the nonmunicipal conveyance a co-permittee to that permit.

b. Where there is more than one operator of a single system of such conveyances, all operators of storm water discharges associated with industrial activity must submit applications.

c. Any permit covering more than one operator shall identify the effluent limitations, or other permit conditions, if any, that apply to each operator.

7. 5. Conveyances that discharge storm water run-off combined with municipal sewage are point sources that must obtain VPDES permits in accordance with the procedures of 9 VAC 25-31-100 and are not subject to the provisions of this section.

8. 6. Whether a discharge from a municipal separate storm sewer is or is not subject to VPDES regulation under this subsection shall have no bearing on whether the owner or operator of the discharge is eligible for funding under Title II, Title III or Title VI of the CWA.

9. 7. a. On and after October 1, 1994, for discharges composed entirely of storm water, that are not required by subdivision 1 of this subsection to obtain a permit, operators shall be required to obtain a VPDES permit only if:

(1) The discharge is from a small MS4 required to be regulated pursuant to 9 VAC 25-31-121 B;

(2) The discharge is a storm water discharge associated with small construction activity as defined in 9 VAC 25-31-10;

(3) (1) The board or the EPA regional administrator determines that storm water controls are needed for the discharge based on wasteload allocations that are part of "total maximum daily loads" (TMDLs) that address the pollutant(s) of concern;  or

(4) (2) The board or the EPA regional administrator determines that the discharge, or category of discharges within a geographic area, contributes to a violation of a water quality standard or is a significant contributor of pollutants to surface waters.

b. Operators of small MS4s designated pursuant to subdivisions 9 a (1), (3), and (4) of this subsection shall seek coverage under a VPDES permit in accordance with 9 VAC 25-31-121 C through E. Operators of nonmunicipal sources designated pursuant to subdivisions 9 a (2), (3), 7 a (1) and (4) (2) of this subsection shall seek coverage under a VPDES permit in accordance with subdivision B 1 of this section.

c. Operators of storm water discharges designated pursuant to subdivisions 9 a (3) 7 a (1) and (4) (2) of this subsection shall apply to the board for a permit within 180 days of receipt of notice, unless permission for a later date is granted by the board.

B. Application requirements for storm water discharges associated with industrial activity and storm water discharges associated with small construction activity.

1. Dischargers of storm water associated with industrial activity and with small construction activity are required to apply for an individual permit or seek coverage under a promulgated storm water general permit.  Facilities that are required to obtain an individual permit, or any discharge of storm water which the board is evaluating for designation under subdivision A 1 e c of this section and is not a municipal separate storm sewer, shall submit a VPDES application in accordance with the requirements of 9 VAC 25-31-100 as modified and supplemented by the provisions of this subsection.

a. Except as provided in subdivisions 1 b through d and c of this subsection, the operator of a storm water discharge associated with industrial activity subject to this section shall provide:

(1) A site map showing topography (or indicating the outline of drainage areas served by the outfall or outfalls covered in the application if a topographic map is unavailable) of the facility including:  each of its drainage and discharge structures;  the drainage area of each storm water outfall;  paved areas and buildings within the drainage area of each storm water outfall, each past or present area used for outdoor storage or disposal of significant materials, each existing structural control measure to reduce pollutants in storm water run-off, materials loading and access areas, areas where pesticides, herbicides, soil conditioners and fertilizers are applied, each of its hazardous waste treatment, storage or disposal facilities (including each area not required to have a RCRA permit which is used for accumulating hazardous waste under 40 CFR 262.34 (2000));  each well where fluids from the facility are injected underground;  springs, and other surface water bodies which receive storm water discharges from the facility;

(2) An estimate of the area of impervious surfaces (including paved areas and building roofs) and the total area drained by each outfall (within a mile radius of the facility) and a narrative description of the following:  Significant materials that in the three years prior to the submittal of this application have been treated, stored or disposed in a manner to allow exposure to storm water;  method of treatment, storage or disposal of such materials;  materials management practices employed, in the three years prior to the submittal of this application, to minimize contact by these materials with storm water runoff;  materials loading and access areas;  the location, manner and frequency in which pesticides, herbicides, soil conditioners and fertilizers are applied;  the location and a description of existing structural and nonstructural control measures to reduce pollutants in storm water runoff;  and a description of the treatment the storm water receives, including the ultimate disposal of any solid or fluid wastes other than by discharge;

(3) A certification that all outfalls that should contain storm water discharges associated with industrial activity have been tested or evaluated for the presence of nonstorm water discharges which are not covered by a VPDES permit;  tests for such nonstorm water discharges may include smoke tests, fluorometric dye tests, analysis of accurate schematics, as well as other appropriate tests.  The certification shall include a description of the method used, the date of any testing, and the onsite drainage points that were directly observed during a test;

(4) Existing information regarding significant leaks or spills of toxic or hazardous pollutants at the facility that have taken place within the three years prior to the submittal of this application;

(5) Quantitative data based on samples collected during storm events and collected in accordance with 9 VAC 25-31-100 of this part from all outfalls containing a storm water discharge associated with industrial activity for the following parameters:

(a) Any pollutant limited in an effluent guideline to which the facility is subject;

(b) Any pollutant listed in the facility's VPDES permit for its process wastewater (if the facility is operating under an existing VPDES permit);

(c) Oil and grease, pH, BOD5, COD, TSS, total phosphorus, total Kjeldahl nitrogen, and nitrate plus nitrite nitrogen;

(d) Any information on the discharge required under 9 VAC 25-31-100 G 7 f and g;

(e) Flow measurements or estimates of the flow rate, and the total amount of discharge for the storm event or events sampled, and the method of flow measurement or estimation;  and

(f) The date and duration (in hours) of the storm event or events sampled, rainfall measurements or estimates of the storm event (in inches) which generated the sampled run-off and the duration between the storm event sampled and the end of the previous measurable (greater than 0.1 inch rainfall) storm event (in hours);

(6) Operators of a discharge which is composed entirely of storm water are exempt from the requirements of 9 VAC 25-31-100 G 2, G 3, G 4, G 5, G 7 c, G 7 d, G 7 e, and G 7 h; and

(7) Operators of new sources or new discharges which are composed in part or entirely of storm water must include estimates for the pollutants or parameters listed in subdivision 1 a (5) of this subsection instead of actual sampling data, along with the source of each estimate.  Operators of new sources or new discharges composed in part or entirely of storm water must provide quantitative data for the parameters listed in subdivision 1 a (5) of this subsection within two years after commencement of discharge, unless such data has already been reported under the monitoring requirements of the VPDES permit for the discharge.  Operators of a new source or new discharge which is composed entirely of storm water are exempt from the requirements of 9 VAC 25-31-100 K 3 b, K 3 c, and K 5.

b. The operator of an existing or new storm water discharge that is associated with construction activity solely, or is associated with small construction activity solely, is exempt from the requirements of 9 VAC 25-31-100 G and subdivision 1 a of this subsection.  Such operator shall provide a narrative description of:

(1) The location (including a map) and the nature of the construction activity;

(2) The total area of the site and the area of the site that is expected to undergo excavation during the life of the permit;

(3) Proposed measures, including best management practices, to control pollutants in storm water discharges during construction, including a brief description of applicable state and local erosion and sediment control requirements;

(4) Proposed measures to control pollutants in storm water discharges that will occur after construction operations have been completed, including a brief description of applicable state or local erosion and sediment control requirements;

(5) An estimate of the run-off coefficient of the site and the increase in impervious area after the construction addressed in the permit application is completed, the nature of fill material and existing data describing the soil or the quality of the discharge;  and

(6) The name of the receiving water.

c. b. The operator of an existing or new discharge composed entirely of storm water from an oil or gas exploration, production, processing, or treatment operation, or transmission facility is not required to submit a permit application in accordance with subdivision 1 a of this subsection, unless the facility:

(1) Has had a discharge of storm water resulting in the discharge of a reportable quantity for which notification is or was required pursuant to 40 CFR 117.21 (2000) or 40 CFR 302.6 (2000) at any time since November 16, 1987; or

(2) Has had a discharge of storm water resulting in the discharge of a reportable quantity for which notification is or was required pursuant to 40 CFR 110.6 (2000) at any time since November 16, 1987; or

(3) Contributes to a violation of a water quality standard.

d. c. The operator of an existing or new discharge composed entirely of storm water from a mining operation is not required to submit a permit application unless the discharge has come into contact with any overburden, raw material, intermediate products, finished product, byproduct or waste products located on the site of such operations.

e. d. Applicants shall provide such other information the board may reasonably require to determine whether to issue a permit and may require any facility subject to subdivision 1 b of this subsection to comply with subdivision 1 a of this subsection.

C. Application requirements for large and medium municipal separate storm sewer discharges.  The operator of a discharge from a large or medium municipal separate storm sewer or a municipal separate storm sewer that is designated by the board under subdivision A 1 e of this section, may submit a jurisdiction-wide or system-wide permit application.  Where more than one public entity owns or operates a municipal separate storm sewer within a geographic area (including adjacent or interconnected municipal separate storm sewer systems), such operators may be a coapplicant to the same application.  Permit applications for discharges from large and medium municipal storm sewers or municipal storm sewers designated under subdivision A 1 e of this section shall include;

1. Part 1 of the application shall consist of:

a. The applicants' name, address, telephone number of contact person, ownership status, and status as a state or local government entity;

b. A description of existing legal authority to control discharges to the municipal separate storm sewer system.  When existing legal authority is not sufficient to meet the criteria provided in subdivision 2 a of this subsection, the description shall list additional authorities as will be necessary to meet the criteria and shall include a schedule and commitment to seek such additional authority that will be needed to meet the criteria;

c. Source identification.

(1) A description of the historic use of ordinances, guidance or other controls which limited the discharge of nonstorm water discharges to any publicly owned treatment works serving the same area as the municipal separate storm sewer system.

(2) A USGS 7.5 minute topographic map (or equivalent topographic map with a scale between 1:10,000 and 1:24,000, if cost effective) extending one mile beyond the service boundaries of the municipal storm sewer system covered by the permit application.  The following information shall be provided:

(a) The location of known municipal storm sewer system outfalls discharging to surface waters;

(b) A description of the land use activities (e.g., divisions indicating undeveloped, residential, commercial, agricultural, and industrial uses) accompanied with estimates of population densities and projected growth for a 10-year period within the drainage area served by the separate storm sewer.  For each land use type, an estimate of an average run-off coefficient shall be provided;

(c) The location and a description of the activities of the facility of each currently operating or closed municipal landfill or other treatment, storage or disposal facility for municipal waste;

(d) The location and the permit number of any known discharge to the municipal storm sewer that has been issued a VPDES permit;

(e) The location of major structural controls for storm water discharge (retention basins, detention basins, major infiltration devices, etc.);   and

(f) The identification of publicly owned parks, recreational areas, and other open lands;

d. Discharge characterization.

(1) Monthly mean rain and snow fall estimates (or summary of weather bureau data) and the monthly average number of storm events.

(2) Existing quantitative data describing the volume and quality of discharges from the municipal storm sewer, including a description of the outfalls sampled, sampling procedures and analytical methods used.

(3) A list of water bodies that receive discharges from the municipal separate storm sewer system, including downstream segments, lakes and estuaries, where pollutants from the system discharges may accumulate and cause water degradation and a brief description of known water quality impacts.  At a minimum, the description of impacts shall include a description of whether the water bodies receiving such discharges have been:

(a) Assessed and reported in § 305(b) of the CWA reports submitted by the state, the basis for the assessment (evaluated or monitored), a summary of designated use support and attainment of law and the CWA goals (fishable and swimmable waters), and causes of nonsupport of designated uses;

(b) Listed under §§ 304(l)(1)(A)(i), 304(l)(1)(A)(ii), or 304(l)(1)(B) of the CWA that is not expected to meet water quality standards or water quality goals;

(c) Listed in State Nonpoint Source Assessments required by § 319(a) of the CWA that, without additional action to control nonpoint sources of pollution, cannot reasonably be expected to attain or maintain water quality standards due to storm sewers, construction, highway maintenance and run-off from municipal landfills and municipal sludge adding significant pollution (or contributing to a violation of water quality standards);

(d) Identified and classified according to eutrophic condition of publicly owned lakes listed in state reports required under § 314(a) of the CWA (include the following:  A description of those publicly owned lakes for which uses are known to be impaired;  a description of procedures, processes and methods to control the discharge of pollutants from municipal separate storm sewers into such lakes;  and a description of methods and procedures to restore the quality of such lakes);

(e) Areas of concern of the Great Lakes identified by the International Joint Commission;

(f) Designated estuaries under the National Estuary Program under § 320 of the CWA;

(g) Recognized by the applicant as highly valued or sensitive waters;

(h) Defined by the state or U.S. Fish and Wildlife Service's National Wetlands Inventory as wetlands;  and

(i) Found to have pollutants in bottom sediments, fish tissue or biosurvey data.

(4) Results of a field screening analysis for illicit connections and illegal dumping for either selected field screening points or major outfalls covered in the permit application.  At a minimum, a screening analysis shall include a narrative description, for either each field screening point or major outfall, of visual observations made during dry weather periods.  If any flow is observed, two grab samples shall be collected during a 24-hour period with a minimum period of four hours between samples.  For all such samples, a narrative description of the color, odor, turbidity, the presence of an oil sheen or surface scum as well as any other relevant observations regarding the potential presence of nonstorm water discharges or illegal dumping shall be provided.  In addition, a narrative description of the results of a field analysis using suitable methods to estimate pH, total chlorine, total copper, total phenol, and detergents (or surfactants) shall be provided along with a description of the flow rate.  Where the field analysis does not involve analytical methods approved under 40 CFR Part 136 (2000), the applicant shall provide a description of the method used including the name of the manufacturer of the test method along with the range and accuracy of the test.  Field screening points shall be either major outfalls or other outfall points (or any other point of access such as manholes) randomly located throughout the storm sewer system by placing a grid over a drainage system map and identifying those cells of the grid which contain a segment of the storm sewer system or major outfall.  The field screening points shall be established using the following guidelines and criteria:

(a) A grid system consisting of perpendicular north-south and east-west lines spaced  1/4 mile apart shall be overlayed on a map of the municipal storm sewer system, creating a series of cells;

(b) All cells that contain a segment of the storm sewer system shall be identified;  one field screening point shall be selected in each cell;  major outfalls may be used as field screening points;

(c) Field screening points should be located downstream of any sources of suspected illegal or illicit activity;

(d) Field screening points shall be located to the degree practicable at the farthest manhole or other accessible location downstream in the system, within each cell;  however, safety of personnel and accessibility of the location should be considered in making this determination;

(e) Hydrological conditions;  total drainage area of the site;  population density of the site;  traffic density;  age of the structures or buildings in the area;  history of the area;  and land use types;

(f) For medium municipal separate storm sewer systems, no more than 250 cells need to have identified field screening points;  in large municipal separate storm sewer systems, no more than 500 cells need to have identified field screening points;  cells established by the grid that contain no storm sewer segments will be eliminated from consideration;  if fewer than 250 cells in medium municipal sewers are created, and fewer than 500 in large systems are created by the overlay on the municipal sewer map, then all those cells which contain a segment of the sewer system shall be subject to field screening (unless access to the separate storm sewer system is impossible);  and

(g) Large or medium municipal separate storm sewer systems which are unable to utilize the procedures described in subdivisions 1 d (4) (a) through (f) of this subsection, because a sufficiently detailed map of the separate storm sewer systems is unavailable, shall field screen no more than 500 or 250 major outfalls respectively (or all major outfalls in the system, if less);  in such circumstances, the applicant shall establish a grid system consisting of north-south and east-west lines spaced 1/4 mile apart as an overlay to the boundaries of the municipal storm sewer system, thereby creating a series of cells;  the applicant will then select major outfalls in as many cells as possible until at least 500 major outfalls (large municipalities) or 250 major outfalls (medium municipalities) are selected;  a field screening analysis shall be undertaken at these major outfalls.

(5) Information and a proposed program to meet the requirements of subdivision 2 c of this subsection.  Such description shall include:  the location of outfalls or field screening points appropriate for representative data collection under subdivision 2 c (1) of this subsection, a description of why the outfall or field screening point is representative, the seasons during which sampling is intended, a description of the sampling equipment.  The proposed location of outfalls or field screening points for such sampling should reflect water quality concerns (see subdivision 1 d (3) of this subsection) to the extent practicable;

e. Management programs.

(1) A description of the existing management programs to control pollutants from the municipal separate storm sewer system.  The description shall provide information on existing structural and source controls, including operation and maintenance measures for structural controls, that are currently being implemented.  Such controls may include, but are not limited to:  Procedures to control pollution resulting from construction activities;  floodplain management controls;  wetland protection measures;  best management practices for new subdivisions;  and emergency spill response programs.  The description may address controls established under state law as well as local requirements.

(2) A description of the existing program to identify illicit connections to the municipal storm sewer system.  The description should include inspection procedures and methods for detecting and preventing illicit discharges, and describe areas where this program has been implemented;  and

f. Fiscal resources.  A description of the financial resources currently available to the municipality to complete Part 2 of the permit application.  A description of the municipality's budget for existing storm water programs, including an overview of the municipality's financial resources and budget, including overall indebtedness and assets, and sources of funds for storm water programs.

2. Part 2 of the application shall consist of:

a. A demonstration that the applicant can operate pursuant to legal authority established by statute, ordinance or series of contracts which authorizes or enables the applicant at a minimum to:

(1) Control through ordinance, permit, contract, order or similar means, the contribution of pollutants to the municipal storm sewer by storm water discharges associated with industrial activity and the quality of storm water discharged from sites of industrial activity;

(2) Prohibit through ordinance, order or similar means, illicit discharges to the municipal separate storm sewer;

(3) Control through ordinance, order or similar means the discharge to a municipal separate storm sewer of spills, dumping or disposal of materials other than storm water;

(4) Control through interagency agreements among coapplicants the contribution of pollutants from one portion of the municipal system to another portion of the municipal system;

(5) Require compliance with conditions in ordinances, permits, contracts or orders;  and

(6) Carry out all inspection, surveillance and monitoring procedures necessary to determine compliance and noncompliance with permit conditions including the prohibition on illicit discharges to the municipal separate storm sewer;

b. The location of any major outfall that discharges to surface waters that was not reported under subdivision 1 c (2) (a) of this subsection.  Provide an inventory, organized by watershed of the name and address, and a description (such as SIC codes) which best reflects the principal products or services provided by each facility which may discharge, to the municipal separate storm sewer, storm water associated with industrial activity;

c. When quantitative data for a pollutant are required under subdivision 2 c (1) (c) of this subsection, the applicant must collect a sample of effluent in accordance with 9 VAC 25-31-100 G 7 and analyze it for the pollutant in accordance with analytical methods approved under 40 CFR Part 136 (2000).  When no analytical method is approved the applicant may use any suitable method but must provide a description of the method.  The applicant must provide information characterizing the quality and quantity of discharges covered in the permit application, including:

(1) Quantitative data from representative outfalls designated by the board (based on information received in Part 1 of the application, the board shall designate between five and ten outfalls or field screening points as representative of the commercial, residential and industrial land use activities of the drainage area contributing to the system or, where there are less than five outfalls covered in the application, the board shall designate all outfalls) developed as follows:

(a) For each outfall or field screening point designated under this subsection, samples shall be collected of storm water discharges from three storm events occurring at least one month apart in accordance with the requirements at 9 VAC 25-31-100 G 7 (the board may allow exemptions to sampling three storm events when climatic conditions create good cause for such exemptions);

(b) A narrative description shall be provided of the date and duration of the storm event or events sampled, rainfall estimates of the storm event which generated the sampled discharge and the duration between the storm event sampled and the end of the previous measurable (greater than 0.1 inch rainfall) storm event;

(c) For samples collected and described under subdivisions 2 c (1) (a) and (1) (b) of this subsection, quantitative data shall be provided for:  the organic pollutants listed in Table II;  the pollutants listed in Table III (toxic metals, cyanide, and total phenols) of 40 CFR Part 122 Appendix D (2000), and for the following pollutants:

Total suspended solids (TSS)

Total dissolved solids (TDS)

COD

BOD5

Oil and grease

Fecal coliform

Fecal streptococcus

pH

Total Kjeldahl nitrogen

Nitrate plus nitrite

Dissolved phosphorus

Total ammonia plus organic nitrogen

Total phosphorus

(d) Additional limited quantitative data required by the board for determining permit conditions (the board may require that quantitative data shall be provided for additional parameters, and may establish sampling conditions such as the location, season of sample collection, form of precipitation (snow melt, rainfall) and other parameters necessary to insure representativeness);

(2) Estimates of the annual pollutant load of the cumulative discharges to surface waters from all identified municipal outfalls and the event mean concentration of the cumulative discharges to surface waters from all identified municipal outfalls during a storm event (as described under 9 VAC 25-31-100 C 7) for BOD5, COD, TSS, dissolved solids, total nitrogen, total ammonia plus organic nitrogen, total phosphorus, dissolved phosphorus, cadmium, copper, lead, and zinc.  Estimates shall be accompanied by a description of the procedures for estimating constituent loads and concentrations, including any modeling, data analysis, and calculation methods;

(3) A proposed schedule to provide estimates for each major outfall identified in either subdivision 2 b or 1 c (2) (a) of this subsection of the seasonal pollutant load and of the event mean concentration of a representative storm for any constituent detected in any sample required under subdivision 2 c (1) of this subsection;  and

(4) A proposed monitoring program for representative data collection for the term of the permit that describes the location of outfalls or field screening points to be sampled (or the location of instream stations), why the location is representative, the frequency of sampling, parameters to be sampled, and a description of sampling equipment;

d. A proposed management program which covers the duration of the permit.  It shall include a comprehensive planning process which involves public participation and where necessary intergovernmental coordination, to reduce the discharge of pollutants to the maximum extent practicable using management practices, control techniques and system, design and engineering methods, and such other provisions which are appropriate.  The program shall also include a description of staff and equipment available to implement the program.  Separate proposed programs may be submitted by each coapplicant.  Proposed programs may impose controls on a system wide basis, a watershed basis, a jurisdiction basis, or on individual outfalls.  Proposed programs will be considered by the board when developing permit conditions to reduce pollutants in discharges to the maximum extent practicable.  Proposed management programs shall describe priorities for implementing controls.  Such programs shall be based on:

(1) A description of structural and source control measures to reduce pollutants from run-off from commercial and residential areas that are discharged from the municipal storm sewer system that are to be implemented during the life of the permit, accompanied with an estimate of the expected reduction of pollutant loads and a proposed schedule for implementing such controls.  At a minimum, the description shall include:

(a) A description of maintenance activities and a maintenance schedule for structural controls to reduce pollutants (including floatables) in discharges from municipal separate storm sewers;

(b) A description of planning procedures including a comprehensive master plan to develop, implement and enforce controls to reduce the discharge of pollutants from municipal separate storm sewers which receive discharges from areas of new development and significant redevelopment.  Such plan shall address controls to reduce pollutants in discharges from municipal separate storm sewers after construction is completed.  (Controls to reduce pollutants in discharges from municipal separate storm sewers containing construction site run-off are addressed in subdivision 2 d (4) of this subsection);

(c) A description of practices for operating and maintaining public streets, roads and highways and procedures for reducing the impact on receiving waters of discharges from municipal storm sewer systems, including pollutants discharged as a result of deicing activities;

(d) A description of procedures to assure that flood management projects assess the impacts on the water quality of receiving water bodies and that existing structural flood control devices have been evaluated to determine if retrofitting the device to provide additional pollutant removal from storm water is feasible;

(e) A description of a program to monitor pollutants in run-off from operating or closed municipal landfills or other treatment, storage or disposal facilities for municipal waste, which shall identify priorities and procedures for inspections and establishing and implementing control measures for such discharges (this program can be coordinated with the program developed under subdivision 2 d (3) of this subsection);  and

(f) A description of a program to reduce to the maximum extent practicable, pollutants in discharges from municipal separate storm sewers associated with the application of pesticides, herbicides and fertilizer which will include, as appropriate, controls such as educational activities, permits, certifications and other measures for commercial applicators and distributors, and controls for application in public right-of-ways and at municipal facilities;

(2) A description of a program, including a schedule, to detect and remove (or require the discharger to the municipal separate storm sewer to obtain a separate VPDES permit for) illicit discharges and improper disposal into the storm sewer.  The proposed program shall include:

(a) A description of a program, including inspections, to implement and enforce an ordinance, orders or similar means to prevent illicit discharges to the municipal separate storm sewer system;  this program description shall address all types of illicit discharges, however the following category of nonstorm water discharges or flows shall be addressed where such discharges are identified by the municipality as sources of pollutants to surface waters:  water line flushing, landscape irrigation, diverted stream flows, rising groundwaters, uncontaminated groundwater infiltration to separate storm sewers, uncontaminated pumped groundwater, discharges from potable water sources, foundation drains, air conditioning condensation, irrigation water, springs, water from crawl space pumps, footing drains, lawn watering, individual residential car washing, flows from riparian habitats and wetlands, dechlorinated swimming pool discharges, and street wash water (program descriptions shall address discharges or flows from fire fighting only where such discharges or flows are identified as significant sources of pollutants to surface waters);

(b) A description of procedures to conduct on-going field screening activities during the life of the permit, including areas or locations that will be evaluated by such field screens;

(c) A description of procedures to be followed to investigate portions of the separate storm sewer system that, based on the results of the field screen, or other appropriate information, indicate a reasonable potential of containing illicit discharges or other sources of nonstorm water (such procedures may include:  sampling procedures for constituents such as fecal coliform, fecal streptococcus, surfactants (Methylene Blue Active Substances--MBAS), residual chlorine, fluorides and potassium;  testing with fluorometric dyes;  or conducting in storm sewer inspections where safety and other considerations allow.  Such description shall include the location of storm sewers that have been identified for such evaluation);

(d) A description of procedures to prevent, contain, and respond to spills that may discharge into the municipal separate storm sewer;

(e) A description of a program to promote, publicize, and facilitate public reporting of the presence of illicit discharges or water quality impacts associated with discharges from municipal separate storm sewers;

(f) A description of educational activities, public information activities, and other appropriate activities to facilitate the proper management and disposal of used oil and toxic materials;  and

(g) A description of controls to limit infiltration of seepage from municipal sanitary sewers to municipal separate storm sewer systems where necessary;

(3) A description of a program to monitor and control pollutants in storm water discharges to municipal systems from municipal landfills, hazardous waste treatment, disposal and recovery facilities, industrial facilities that are subject to § 313 of Title III of the Superfund Amendments and Reauthorization Act of 1986 (SARA, 42 USC § 11023), and industrial facilities that the municipal permit applicant determines are contributing a substantial pollutant loading to the municipal storm sewer system.  The program shall:

(a) Identify priorities and procedures for inspections and establishing and implementing control measures for such discharges;

(b) Describe a monitoring program for storm water discharges associated with the industrial facilities identified in subdivision 2 d (3) of this subsection, to be implemented during the term of the permit, including the submission of quantitative data on the following constituents:  any pollutants limited in effluent guidelines subcategories, where applicable;  any pollutant listed in an existing VPDES permit for a facility;  oil and grease, COD, pH, BOD5 , TSS, total phosphorus, total Kjeldahl nitrogen, nitrate plus nitrite nitrogen, and any information on discharges required under 9 VAC 25-31-100 G 7 f and g;  and

(4) A description of a program to implement and maintain structural and nonstructural best management practices to reduce pollutants in storm water run-off from construction sites to the municipal storm sewer system, which shall include:

(a) A description of procedures for site planning which incorporate consideration of potential water quality impacts;

(b) A description of requirements for nonstructural and structural best management practices;

(c) A description of procedures for identifying priorities for inspecting sites and enforcing control measures which consider the nature of the construction activity, topography, and the characteristics of soils and receiving water quality;  and

(d) A description of appropriate educational and training measures for construction site operators;

e. Estimated reductions in loadings of pollutants from discharges of municipal storm sewer constituents from municipal storm sewer systems expected as the result of the municipal storm water quality management program.  The assessment shall also identify known impacts of storm water controls on groundwater;

f. For each fiscal year to be covered by the permit, a fiscal analysis of the necessary capital and operation and maintenance expenditures necessary to accomplish the activities of the programs under subdivisions 2 c and d of this subsection.  Such analysis shall include a description of the source of funds that are proposed to meet the necessary expenditures, including legal restrictions on the use of such funds;

g. Where more than one legal entity submits an application, the application shall contain a description of the roles and responsibilities of each legal entity and procedures to ensure effective coordination;  and

h. Where requirements under subdivisions 1 d (5), 2 b, 2 c (2), and 2 d of this subsection are not practicable or are not applicable, the board may exclude any operator of a discharge from a municipal separate storm sewer which is designated under subdivision A 1 e of this section, or which is located in the counties listed in 40 CFR Part 122 Appendix H or Appendix I (2000) (except municipal separate storm sewers that are located in the incorporated places, townships or towns within such counties) from such requirements.  The board shall not exclude the operator of a discharge from a municipal separate storm sewer identified in 40 CFR Part 122 Appendix F, G, H or I (2000) from any of the permit application requirements under this subdivision except where authorized under this subsection.

D. C. Application deadlines.  Any operator of a point source required to obtain a permit under this section that does not have an effective VPDES permit authorizing discharges from its storm water outfalls shall submit an application in accordance with the following deadlines:

1. Individual applications.

a. Except as provided in subdivision 1 b of this subsection, for any storm water discharge associated with industrial activity as defined in this chapter which is not authorized by a storm water general permit, a permit application made pursuant to subsection B of this section shall be submitted to the department by October 1, 1992;

b. For any storm water discharge associated with industrial activity from a facility that is owned or operated by a municipality with a population of less than 100,000 that is not authorized by a general or individual permit, other than an airport, powerplant, or uncontrolled sanitary landfill, permit applications must be submitted to the department by March 10, 2003;

2. For any discharge from a large municipal separate storm sewer system:

a. Part 1 of the application shall be submitted to the department by November 18, 1991;

b. Based on information received in the Part 1 application the board will approve or deny a sampling plan under subdivision C 1 d (5) of this section within 90 days after receiving the Part 1 application;  and

c. Part 2 of the application shall be submitted to the department by November 16, 1992;

3. For any discharge from a medium municipal separate storm sewer system:

a. Part 1 of the application shall be submitted to the department by May 18, 1992;

b. Based on information received in the Part 1 application the board will approve or deny a sampling plan under subdivision C 1 d (5) of this section within 90 days after receiving the Part 1 application;  and

c. Part 2 of the application shall be submitted to the department by May 17, 1993;

4. 2. A permit application shall be submitted to the department within 180 days of notice, unless permission for a later date is granted by the board, for:

a. A storm water discharge which either the board or the regional administrator, determines that the discharge contributes to a violation of a water quality standard or is a significant contributor of pollutants to surface waters; or

b. A storm water discharge subject to subdivision B 1 e d of this section;

5. 3. Facilities with existing VPDES permits for storm water discharges associated with industrial activity shall maintain existing permits.  Facilities with permits for storm water discharges associated with industrial activity which expire on or after May 18, 1992, shall submit a new application in accordance with the requirements of 9 VAC 25-31-100 and 9 VAC 25-31-120 C (Form 1, Form 2F, and other applicable forms) 180 days before the expiration of such permits.

6. For any storm water discharge associated with small construction activity, see 9 VAC 25-31-100 C 1.  Discharges from these sources require permit authorization by March 10, 2003, unless designated for coverage before then.

7. For any discharge from a regulated small MS4, the permit application made under 9 VAC 25-31-121 C must be submitted to the department by:

a. March 10, 2003, if designated under 9 VAC 25-31-121 B 1, unless your MS4 serves a jurisdiction with a population under 10,000 and the board has established a phasing schedule under 40 CFR 123.35(d)(3) (2000);  or

b. Within 180 days of notice, unless the board grants a later date.

E. D. Petitions.

1. Any operator of a municipal separate storm sewer system may petition the board to require a separate VPDES permit for any discharge into the municipal separate storm sewer system.

2. 1. Any person may petition the board to require a VPDES permit for a discharge which is composed entirely of storm water which contributes to a violation of a water quality standard or is a significant contributor of pollutants to surface waters.

3. The owner or operator of a municipal separate storm sewer system may petition the board to reduce the Census estimates of the population served by such separate system to account for storm water discharged to combined sewers as defined by 40 CFR 5.2005(b)(11) (2000) that is treated in a publicly owned treatment works.  In municipalities in which combined sewers are operated, the Census estimates of population may be reduced proportional to the fraction, based on estimated lengths, of the length of combined sewers over the sum of the length of combined sewers and municipal separate storm sewers where an applicant has submitted the VPDES permit number associated with each discharge point and a map indicating areas served by combined sewers and the location of any combined sewer overflow discharge point.

4. Any person may petition the board for the designation of a large, medium or small municipal separate storm sewer system as defined by this chapter.

5. 2. The board shall make a final determination on any petition received under this section within 90 days after receiving the petition with the exception of petitions to designate a small MS4, in which case the board shall make a final determination on the petition within 180 days after its receipt.

F. E. Conditional exclusion for no exposure of industrial activities and materials to storm water.  Discharges composed entirely of storm water are not storm water discharges associated with industrial activity if there is no exposure of industrial materials and activities to rain, snow, snowmelt or run-off and the discharger satisfies the conditions in subdivisions 1 through 4 of this subsection.  No exposure means that all industrial materials and activities are protected by a storm resistant shelter to prevent exposure to rain, snow, snowmelt, and run-off.  Industrial materials or activities include, but are not limited to, material handling equipment or activities, industrial machinery, raw materials, intermediate products, by-products, final products, or waste products.  Material handling activities include the storage, loading and unloading, transportation, or conveyance of any raw material, intermediate product, final product or waste product.

1. To qualify for this exclusion, the operator of the discharge must:

a. Provide a storm resistant shelter to protect industrial materials and activities from exposure to rain, snow, snow melt, and run-off;

b. Complete and sign (according to 9 VAC 25-31-110) a certification that there are no discharges of storm water contaminated by exposure to industrial materials and activities from the entire facility, except as provided in subdivision 2 of this subsection;

c. Submit the signed certification to the department once every five years;

d. Allow the department to inspect the facility to determine compliance with the no exposure conditions;

e. Allow the department to make any no exposure inspection reports available to the public upon request; and

f. For facilities that discharge through an MS4, upon request, submit a copy of the certification of no exposure to the MS4 operator, as well as allow inspection and public reporting by the MS4 operator.

2. Storm resistant shelter is not required for:

a. Drums, barrels, tanks, and similar containers that are tightly sealed, provided those containers are not deteriorated and do not leak ("sealed" means banded or otherwise secured and without operational taps or valves);

b. Adequately maintained vehicles used in material handling;  and

c. Final products, other than products that would be mobilized in storm water discharge (e.g., rock salt).

3. a. Storm water discharges from construction activities are not eligible for this conditional exclusion.

b. a. This conditional exclusion from the requirement for a VPDES permit is available on a facility-wide basis only, not for individual outfalls.  If a facility has some discharges of storm water that would otherwise be no exposure discharges, individual permit requirements should be adjusted accordingly.

c. b. If circumstances change and industrial materials or activities become exposed to rain, snow, snow melt, or run-off, the conditions for this exclusion no longer apply.  In such cases, the discharge becomes subject to enforcement for unpermitted discharge.  Any conditionally exempt discharger who anticipates changes in circumstances should apply for and obtain permit authorization prior to the change of circumstances.

d. c. Notwithstanding the provisions of this subsection, the board retains the authority to require permit authorization (and deny this exclusion) upon making a determination that the discharge causes, has a reasonable potential to cause, or contributes to an instream excursion above an applicable water quality standard, including designated uses.

4. The no exposure certification must require requires the submission of the following information, at a minimum, to aid the board in determining if the facility qualifies for the no exposure exclusion:

a. The legal name, address and phone number of the discharger.

b. The facility name and address, the county name and the latitude and longitude where the facility is located.

c. Certification that indicates that none of the following materials or activities are, or will be in the foreseeable future, exposed to precipitation:

(1) Using, storing or cleaning industrial machinery or equipment, and areas where residuals from using, storing or cleaning industrial machinery or equipment remain and are exposed to storm water;

(2) Materials or residuals on the ground or in storm water inlets from spills/leaks;

(3) Materials or products from past industrial activity;

(4) Material handling equipment (except adequately maintained vehicles);

(5) Materials or products during loading/unloading or transporting activities;

(6) Materials or products stored outdoors (except final products intended for outside use, e.g., new cars, where exposure to storm water does not result in the discharge of pollutants);

(7) Materials contained in open, deteriorated or leaking storage drums, barrels, tanks, and similar containers;

(8) Materials or products handled/stored on roads or railways owned or maintained by the discharger;

(9) Waste material (except waste in covered, nonleaking containers, e.g., dumpsters);

(10) Application or disposal of process wastewater (unless otherwise permitted); and

(11) Particulate matter or visible deposits of residuals from roof stacks/vents not otherwise regulated, i.e., under an air quality control permit, and evident in the storm water outflow.

d. All no exposure certifications must include the following certification statement and be signed in accordance with the signatory requirements of 9 VAC 25-31-110:  "I certify under penalty of law that I have read and understand the eligibility requirements for claiming a condition of no exposure and obtaining an exclusion from VPDES storm water permitting;  and that there are no discharges of storm water contaminated by exposure to industrial activities or materials from the industrial facility identified in this document (except as allowed under 9 VAC 25-31-120 F E 2).  I understand that I am obligated to submit a no exposure certification form once every five years to the Department of Environmental Quality and, if requested, to the operator of the local MS4 into which this facility discharges (where applicable). I understand that I must allow the department, or MS4 operator where the discharge is into the local MS4, to perform inspections to confirm the condition of no exposure and to make such inspection reports publicly available upon request.  I understand that I must obtain coverage under a VPDES permit prior to any point source discharge of storm water associated with industrial activity from the facility.  I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to assure that qualified personnel properly gathered and evaluated the information submitted.  Based upon my inquiry of the person or persons who manage the system, or those persons directly involved in gathering the information, the information submitted is to the best of my knowledge and belief true, accurate and complete.  I am aware there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations."

9 VAC 25-31-121. Small municipal separate storm sewer systems. (Repealed.)

A. Objectives of the storm water regulations for small MS4s.

1. Subsections A through G of this section are written in a "readable regulation" format that includes both rule requirements and guidance that is not legally binding.  The recommended guidance is distinguished from the regulatory requirements by putting the guidance in a separate subdivision headed by the word "Note."

2. Under the statutory mandate in § 402(p)(6) of the Clean Water Act, the purpose of this portion of the storm water program is to designate additional sources that need to be regulated to protect water quality and to establish a comprehensive storm water program to regulate these sources.

3. Storm water run-off continues to harm the nation's waters.  Run-off from lands modified by human activities can harm surface water resources in several ways including by changing natural hydrologic patterns and by elevating pollutant concentrations and loadings.  Storm water run-off may contain or mobilize high levels of contaminants, such as sediment, suspended solids, nutrients, heavy metals, pathogens, toxins, oxygen-demanding substances, and floatables.

4. The board strongly encourages partnerships and the watershed approach as the management framework for efficiently, effectively, and consistently protecting and restoring aquatic ecosystems and protecting public health.

B. As an operator of a small MS4, am I regulated under the VPDES storm water program?

1. Unless you qualify for a waiver under subdivision 3 of this subsection, you are regulated if you operate a small MS4, including but not limited to systems operated by federal, state, tribal, and local governments, including the state Department of Transportation; and

a. Your small MS4 is located in an urbanized area as determined by the latest decennial census by the Bureau of the Census (If your small MS4 is not located entirely within an urbanized area, only the portion that is within the urbanized area is regulated);  or

b. You are designated by the board, including where the designation is pursuant to subdivisions E 2 c and d of this section or is based upon a petition under 9 VAC 25-31-120 E.

2. You may be the subject of a petition to the board to require a VPDES permit for your discharge of storm water.  If the board determines that you need a permit, you are required to comply with subsections C through E of this section.

3. The board may waive the requirements otherwise applicable to you if you meet the criteria of subdivision 4 or 5 of this subsection.  If you receive a waiver under this section, you may subsequently be required to seek coverage under a VPDES permit in accordance with subdivision C 1 of this section if circumstances change.  (See also subdivision E 2 of this section).

4. The board may waive permit coverage if your MS4 serves a population of less than 1,000 within the urbanized area and you meet the following criteria:

a. Your system is not contributing substantially to the pollutant loadings of a physically interconnected MS4 that is regulated by the VPDES storm water program (see subdivision E 2 d of this section);  and

b. If you discharge any pollutants that have been identified as a cause of impairment of any water body to which you discharge, storm water controls are not needed based on wasteload allocations that are part of an EPA approved or established "total maximum daily load" (TMDL) that addresses the pollutants of concern.

5. The board may waive permit coverage if your MS4 serves a population under 10,000 and you meet the following criteria:

a. The board has evaluated all surface waters, including small streams, tributaries, lakes, and ponds, that receive a discharge from your MS4;

b. For all such waters, the board has determined that storm water controls are not needed based on wasteload allocations that are part of an EPA approved or established TMDL that addresses the pollutants of concern or, if a TMDL has not been developed or approved, an equivalent analysis that determines sources and allocations for the pollutants of concern;

c. For the purpose of subdivision 5 of this subsection, the pollutants of concern include biochemical oxygen demand (BOD), sediment or a parameter that addresses sediment (such as total suspended solids, turbidity or siltation), pathogens, oil and grease, and any pollutant that has been identified as a cause of impairment of any water body that will receive a discharge from your MS4;  and

d. The board has determined that future discharges from your MS4 do not have the potential to result in exceedances of water quality standards, including impairment of designated uses, or other significant water quality impacts, including habitat and biological impacts.

C. If I am an operator of a regulated small MS4, how do I apply for a VPDES permit and when do I have to apply?

1. If you operate a regulated small MS4 under subsection B of this section, you must seek coverage under a VPDES permit issued by the board.

2. You must seek authorization to discharge under a general or individual VPDES permit, as follows:

a. If the board has issued a general permit applicable to your discharge and you are seeking coverage under the general permit, you must submit a registration statement that includes the information on your best management practices and measurable goals required by subdivision D 4 of this section.  You may file your own registration statement, or you and other municipalities or governmental entities may jointly submit a registration statement.  If you want to share responsibilities for meeting the minimum measures with other municipalities or governmental entities, you must submit a registration statement that describes which minimum measures you will implement and identify the entities that will implement the other minimum measures within the area served by your MS4. The general permit will explain any other steps necessary to obtain permit authorization.

b. (1) If you are seeking authorization to discharge under an individual permit and wish to implement a program under subsection D of this section, you must submit an application to the board that includes the information required under 9 VAC 25-31-100 F and subdivision D 4 of this section, an estimate of square mileage served by your small MS4, and any additional information that the board requests.  A storm sewer map that satisfies the requirement of subdivision D 2 c (1) of this section will satisfy the map requirement in 9 VAC 25-31-100 F 7.

(2) If you are seeking authorization to discharge under an individual permit and wish to implement a program that is different from the program under subsection D of this section, you will need to comply with the permit application requirements of 9 VAC 25-31-120 C. You must submit both parts of the application requirements in 9 VAC 25-31-120 C 1 and 2 by March 10, 2003.  You do not need to submit the information required by 9 VAC 25-31-120 C 1 b and C 2 regarding your legal authority, unless you intend for the permit writer to take such information into account when developing your other permit conditions.

(3) If allowed by the board, you and another regulated entity may jointly apply under either subdivision 2 b (1) or (2) of this subsection to be co-permittees under an individual permit.

c. If your small MS4 is in the same urbanized area as a medium or large MS4 with a VPDES storm water permit and that other MS4 is willing to have you participate in its storm water program, you and the other MS4 may jointly seek a modification of the other MS4 permit to include you as a limited co-permittee.  As a limited co-permittee, you will be responsible for compliance with the permit's conditions applicable to your jurisdiction.  If you choose this option you will need to comply with the permit application requirements of 9 VAC 25-31-120, rather than the requirements of subsection D of this section.  You do not need to comply with the specific application requirements of 9 VAC 25-31-120 C 1 c and d and 9 VAC 25-31-120 C 2 c (discharge characterization). You may satisfy the requirements in 9 VAC 25-31-120 C 1 e and 2 d (identification of a management program) by referring to the other MS4's storm water management program.

d. NOTE:  In referencing an MS4's storm water management program, you should briefly describe how the existing plan will address discharges from your small MS4 or would need to be supplemented in order to adequately address your discharges.  You should also explain your role in coordinating storm water pollutant control activities in your MS4 and detail the resources available to you to accomplish the plan.

3. If you operate a regulated small MS4:

a. Designated under subdivision B 1 a of this section, you must apply for coverage under a VPDES permit or apply for a modification of an existing VPDES permit under subdivision 2 c of this subsection by March 10, 2003, unless your MS4 serves a jurisdiction with a population under 10,000 and the board has established a schedule for phasing in permit coverage with a final deadline of March 8, 2007.

b. Designated under subdivision B 1 b of this section, you must apply for coverage under a VPDES permit or apply for a modification of an existing VPDES permit under subdivision 2 c of this subsection within 180 days of notice, unless the board grants a later date.

D. As an operator of a regulated small MS4, what will my VPDES MS4 storm water permit require?

1. Your VPDES MS4 permit will require at a minimum that you develop, implement, and enforce a storm water management program designed to reduce the discharge of pollutants from your MS4 to the maximum extent practicable (MEP), to protect water quality, and to satisfy the appropriate water quality requirements of the Clean Water Act and the State Water Control Law.  Your storm water management program must include the minimum control measures described in subdivision 2 of this subsection unless you apply for a permit under 9 VAC 25-31-120 C. For purposes of this section, narrative effluent limitations requiring implementation of best management practices (BMPs) are generally the most appropriate form of effluent limitations when designed to satisfy technology requirements (including reductions of pollutants to the maximum extent practicable) and to protect water quality.  Implementation of best management practices consistent with the provisions of the storm water management program required pursuant to this section and the provisions of the permit required pursuant to subsection C of this section constitutes compliance with the standard of reducing pollutants to the maximum extent practicable.  The board will specify a time period of up to five years from the date of permit issuance for you to develop and implement your program.

2. Minimum control measures.

a. Public education and outreach on storm water impacts.

(1) You must implement a public education program to distribute educational materials to the community or conduct equivalent outreach activities about the impacts of storm water discharges on water bodies and the steps that the public can take to reduce pollutants in storm water run-off.

(2) NOTE:  You may use storm water educational materials provided by the state, your tribe, EPA, environmental, public interest or trade organizations, or other MS4s.  The public education program should inform individuals and households about the steps they can take to reduce storm water pollution, such as ensuring proper septic system maintenance, ensuring the proper use and disposal of landscape and garden chemicals including fertilizers and pesticides, protecting and restoring riparian vegetation, and properly disposing of used motor oil or household hazardous wastes.  The board recommends that the program inform individuals and groups how to become involved in local stream and beach restoration activities as well as activities that are coordinated by youth service and conservation corps or other citizen groups.  The board recommends that the public education program be tailored, using a mix of locally appropriate strategies, to target specific audiences and communities.  Examples of strategies include:  distributing brochures or fact sheets, sponsoring speaking engagements before community groups, providing public service announcements, implementing educational programs targeted at school-age children, and conducting community-based projects such as storm drain stenciling, and watershed and beach cleanups.  In addition, the board recommends that some of the materials or outreach programs be directed toward targeted groups of commercial, industrial, and institutional entities likely to have significant storm water impacts.  For example, providing information to restaurants on the impact of grease clogging storm drains and to garages on the impact of oil discharges.  You are encouraged to tailor your outreach program to address the viewpoints and concerns of all communities, particularly minority and disadvantaged communities, as well as any special concerns relating to children.

b. Public involvement/participation.

(1) You must, at a minimum, comply with state, tribal, and local public notice requirements when implementing a public involvement/participation program.

(2) The board recommends that the public be included in developing, implementing, and reviewing your storm water management program and that the public participation process should make efforts to reach out and engage all economic and ethnic groups.  Opportunities for members of the public to participate in program development and implementation include serving as citizen representatives on a local storm water management panel, attending public hearings, working as citizen volunteers to educate other individuals about the program, assisting in program coordination with other pre-existing programs, or participating in volunteer monitoring efforts.  (Citizens should obtain approval where necessary for lawful access to monitoring sites.)

c. Illicit discharge detection and elimination.

(1) You must develop, implement and enforce a program to detect and eliminate illicit discharges (as defined in 9 VAC 25-31-10) into your small MS4.

(2) You must:

(a) Develop, if not already completed, a storm sewer system map, showing the location of all outfalls and the names and location of all surface waters that receive discharges from those outfalls;

(b) To the extent allowable under state, tribal or local law, effectively prohibit, through ordinance or other regulatory mechanism, nonstorm water discharges into your storm sewer system and implement appropriate enforcement procedures and actions;

(c) Develop and implement a plan to detect and address nonstorm water discharges, including illegal dumping, to your system;  and

(d) Inform public employees, businesses, and the general public of hazards associated with illegal discharges and improper disposal of waste.

(3) You need to address the following categories of nonstorm water discharges or flows (i.e., illicit discharges) only if you identify them as significant contributors of pollutants to your small MS4:  water line flushing, landscape irrigation, diverted stream flows, rising groundwaters, uncontaminated groundwater infiltration (as defined in 40 CFR 35.2005(20) (2000)), uncontaminated pumped groundwater, discharges from potable water sources, foundation drains, air conditioning condensation, irrigation water, springs, water from crawl space pumps, footing drains, lawn watering, individual residential car washing, flows from riparian habitats and wetlands, dechlorinated swimming pool discharges, and street wash water.  (Discharges or flows from fire-fighting activities are excluded from the effective prohibition against nonstorm water and need only be addressed where they are identified as significant sources of pollutants to surface waters.)

(4) NOTE:  The board recommends that the plan to detect and address illicit discharges include the following four components:  (i) procedures for locating priority areas likely to have illicit discharges, (ii) procedures for tracing the source of an illicit discharge, (iii) procedures for removing the source of the discharge, and (iv) procedures for program evaluation and assessment.  The board recommends visually screening outfalls during dry weather and conducting field tests of selected pollutants as part of the procedures for locating priority areas.  Illicit discharge education actions may include storm drain stenciling;  a program to promote, publicize, and facilitate public reporting of illicit connections or discharges;  and distribution of outreach materials.

d. Construction site storm water run-off control.

(1) You must develop, implement, and enforce a program to reduce pollutants in any storm water run-off to your small MS4 from construction activities that result in a land disturbance of greater than or equal to one acre.  Reduction of storm water discharges from construction activity disturbing less than one acre must be included in your program if that construction activity is part of a larger common plan of development or sale that would disturb one acre or more.  If the board waives requirements for storm water discharges associated with small construction activity in accordance with the definition in 9 VAC 25-31-10, you are not required to develop, implement, and/or enforce a program to reduce pollutant discharges from such sites.

(2) Your program must include the development and implementation of, at a minimum:

(a) An ordinance or other regulatory mechanism to require erosion and sediment controls, as well as sanctions to ensure compliance, to the extent allowable under state, tribal, or local law;

(b) Requirements for construction site operators to implement appropriate erosion and sediment control best management practices;

(c) Requirements for construction site operators to control waste such as discarded building materials, concrete truck washout, chemicals, litter, and sanitary waste at the construction site that may cause adverse impacts to water quality;

(d) Procedures for site plan review which incorporate consideration of potential water quality impacts;

(e) Procedures for receipt and consideration of information submitted by the public;  and

(f) Procedures for site inspection and enforcement of control measures.

(3) NOTE:  Examples of sanctions to ensure compliance include nonmonetary penalties, fines, bonding requirements and/or permit denials for noncompliance.  The board recommends that procedures for site plan review include the review of individual pre-construction site plans to ensure consistency with local sediment and erosion control requirements.  Procedures for site inspections and enforcement of control measures could include steps to identify priority sites for inspection and enforcement based on the nature of the construction activity, topography, and the characteristics of soils and receiving water quality.  You are encouraged to provide appropriate educational and training measures for construction site operators.  You may wish to require a storm water pollution prevention plan for construction sites within your jurisdiction that discharge into your system.  (See 9 VAC 25-31-220 R and subdivision E 2 of this section.) The board may recognize that another government entity may be responsible for implementing one or more of the minimum measures on your behalf.

e. Post-construction storm water management in new development and redevelopment.

(1) You must develop, implement, and enforce a program to address storm water run-off from new development and redevelopment projects that disturb greater than or equal to one acre, including projects less than one acre that are part of a larger common plan of development or sale, that discharge into your small MS4. Your program must ensure that controls are in place that would prevent or minimize water quality impacts.

(2) You must:

(a) Develop and implement strategies which include a combination of structural and/or nonstructural best management practices (BMPs) appropriate for your community;

(b) Use an ordinance or other regulatory mechanism to address post-construction run-off from new development and redevelopment projects to the extent allowable under state, tribal or local law;  and

(c) Ensure adequate long-term operation and maintenance of BMPs.

(3) NOTE:  If water quality impacts are considered from the beginning stages of a project, new development and potentially redevelopment provide more opportunities for water quality protection.  The board recommends that the BMPs chosen be appropriate for the local community, minimize water quality impacts, and attempt to maintain pre-development run-off conditions.  In choosing appropriate BMPs, the board encourages you to participate in locally based watershed planning efforts which attempt to involve a diverse group of stakeholders, including interested citizens.  When developing a program that is consistent with this measure's intent, the board recommends that you adopt a planning process that identifies the municipality's program goals (e.g., minimize water quality impacts resulting from post-construction run-off from new development and redevelopment), implementation strategies (e.g., adopt a combination of structural and/or nonstructural BMPs), operation and maintenance policies and procedures, and enforcement procedures.  In developing your program, you should consider assessing existing ordinances, policies, programs and studies that address storm water run-off quality.  In addition to assessing these existing documents and programs, you should provide opportunities to the public to participate in the development of the program.  Nonstructural BMPs are preventative actions that involve management and source controls such as:  (i) policies and ordinances that provide requirements and standards to direct growth to identified areas, protect sensitive areas such as wetlands and riparian areas, maintain and/or increase open space (including a dedicated funding source for open space acquisition), provide buffers along sensitive water bodies, minimize impervious surfaces, and minimize disturbance of soils and vegetation;  (ii) policies or ordinances that encourage infill development in higher density urban areas, and areas with existing infrastructure;  (iii) education programs for developers and the public about project designs that minimize water quality impacts;  and (iv) measures such as minimization of percent impervious area after development and minimization of directly connected impervious areas.  Structural BMPs include:  storage practices such as wet ponds and extended-detention outlet structures;  filtration practices such as grassed swales, sand filters and filter strips;  and infiltration practices such as infiltration basins and infiltration trenches.  The board recommends that you ensure the appropriate implementation of the structural BMPs by considering some or all of the following:  pre-construction review of BMP designs;  inspections during construction to verify BMPs are built as designed;  post-construction inspection and maintenance of BMPs;  and penalty provisions for the noncompliance with design, construction or operation and maintenance.  Storm water technologies are constantly being improved, and the board recommends that your requirements be responsive to these changes, developments or improvements in control technologies.

f. Pollution prevention/good housekeeping for municipal operations.

(1) You must develop and implement an operation and maintenance program that includes a training component and has the ultimate goal of preventing or reducing pollutant run-off from municipal operations.  Using training materials that are available from EPA, state, tribe, or other organizations, your program must include employee training to prevent and reduce storm water pollution from activities such as park and open space maintenance, fleet and building maintenance, new construction and land disturbances, and storm water system maintenance.

(2) NOTE:  The board recommends that, at a minimum, you consider the following in developing your program:  maintenance activities, maintenance schedules, and long-term inspection procedures for structural and nonstructural storm water controls to reduce floatables and other pollutants discharged from your separate storm sewers;  controls for reducing or eliminating the discharge of pollutants from streets, roads, highways, municipal parking lots, maintenance and storage yards, fleet or maintenance shops with outdoor storage areas, salt/sand storage locations and snow disposal areas operated by you, and waste transfer stations;  procedures for properly disposing of waste removed from the separate storm sewers and areas listed above (such as dredge spoil, accumulated sediments, floatables, and other debris);  and ways to ensure that new flood management projects assess the impacts on water quality and examine existing projects for incorporating additional water quality protection devices or practices.  Operation and maintenance should be an integral component of all storm water management programs.  This measure is intended to improve the efficiency of these programs and require new programs where necessary.  Properly developed and implemented operation and maintenance programs reduce the risk of water quality problems.

3. If an existing qualifying local program requires you to implement one or more of the minimum control measures of subdivision 2 of this subsection, the board may include conditions in your VPDES permit that direct you to follow that qualifying program's requirements rather than the requirements of subdivision 2 of this subsection.  A qualifying local program is a local, state or tribal municipal storm water management program that imposes, at a minimum, the relevant requirements of subdivision 2 of this subsection.

4. a. In your permit application (either a registration statement for coverage under a general permit or an individual permit application), you must identify and submit to the board the following information:

(1) The best management practices (BMPs) that you or another entity will implement for each of the storm water minimum control measures provided in subdivision 2 of this subsection;

(2) The measurable goals for each of the BMPs including, as appropriate, the months and years in which you will undertake required actions, including interim milestones and the frequency of the action;  and

(3) The person or persons responsible for implementing or coordinating your storm water management program.

b. If you obtain coverage under a general permit, you are not required to meet any measurable goals identified in your registration statement in order to demonstrate compliance with the minimum control measures in subdivisions 2 c through f of this subsection unless, prior to submitting your registration statement, EPA or the board has provided or issued a menu of BMPs that addresses each such minimum measure.  Even if no regulatory authority issues the menu of BMPs, however, you still must comply with other requirements of the general permit, including good faith implementation of BMPs designed to comply with the minimum measures.

c. NOTE:  Either EPA or the board will provide a menu of BMPs.  You may choose BMPs from the menu or select others that satisfy the minimum control measures.

5. a. You must comply with any more stringent effluent limitations in your permit, including permit requirements that modify or are in addition to the minimum control measures based on an approved total maximum daily load (TMDL) or equivalent analysis.  The board may include such more stringent limitations based on a TMDL or equivalent analysis that determines such limitations are needed to protect water quality.

b. NOTE:  The board strongly recommends that until the evaluation of the storm water program in subsection G of this section, no additional requirements beyond the minimum control measures be imposed on regulated small MS4s without the agreement of the operator of the affected small MS4, except where an approved TMDL or equivalent analysis provides adequate information to develop more specific measures to protect water quality.

6. You must comply with other applicable VPDES permit requirements, standards and conditions established in the individual or general permit developed consistent with the provisions of 9 VAC 25-31-190 through 9 VAC 25-31-250, as appropriate.

7. Evaluation and assessment.

a. You must evaluate program compliance, the appropriateness of your identified best management practices, and progress towards achieving your identified measurable goals.  The board may determine monitoring requirements for you in accordance with monitoring plans appropriate to your watershed.  Participation in a group monitoring program is encouraged.

b. You must keep records required by the VPDES permit for at least three years.  You must submit your records to the department only when specifically asked to do so.  You must make your records, including a description of your storm water management program, available to the public at reasonable times during regular business hours (see 9 VAC 25-31-80 for confidentiality provision). You may assess a reasonable charge for copying.  You may require a member of the public to provide advance notice.

c. Unless you are relying on another entity to satisfy your VPDES permit obligations under subdivision E 1 of this section, you must submit annual reports to the department for your first permit term.  For subsequent permit terms, you must submit reports in years two and four unless the department requires more frequent reports.  Your report must include:

(1) The status of compliance with permit conditions, an assessment of the appropriateness of your identified best management practices and progress towards achieving your identified measurable goals for each of the minimum control measures;

(2) Results of information collected and analyzed, including monitoring data, if any, during the reporting period;

(3) A summary of the storm water activities you plan to undertake during the next reporting cycle;

(4) A change in any identified best management practices or measurable goals for any of the minimum control measures;  and

(5) Notice that you are relying on another governmental entity to satisfy some of your permit obligations (if applicable).

E. As an operator of a regulated small MS4, may I share the responsibility to implement the minimum control measures with other entities?

1. You may rely on another entity to satisfy your VPDES permit obligations to implement a minimum control measure if:

a. The other entity, in fact, implements the control measure;

b. The particular control measure, or component thereof, is at least as stringent as the corresponding VPDES permit requirement;  and

c. The other entity agrees to implement the control measure on your behalf.  In the reports you must submit under subdivision D 7 c of this section, you must also specify that you rely on another entity to satisfy some of your permit obligations.  If you are relying on another governmental entity regulated under the VPDES permit program to satisfy all of your permit obligations, including your obligation to file periodic reports required by subdivision D 7 c of this section, you must note that fact in your registration statement, but you are not required to file the periodic reports.  You remain responsible for compliance with your permit obligations if the other entity fails to implement the control measure (or component thereof). Therefore, the board encourages you to enter into a legally binding agreement with that entity if you want to minimize any uncertainty about compliance with your permit.

2. In some cases, the board may recognize, either in your individual VPDES permit or in a VPDES general permit, that another governmental entity is responsible under a VPDES permit for implementing one or more of the minimum control measures for your small MS4. Where the board does so, you are not required to include such minimum control measure(s) in your storm water management program.  Your permit may be reopened and modified to include the requirement to implement a minimum control measure if the entity fails to implement it.

F. As an operator of a regulated small MS4, what happens if I don't comply with the application or permit requirements in subsections C through E of this section?

VPDES permits are enforceable under the Clean Water Act and the State Water Control Law.  Violators may be subject to the enforcement actions and penalties described in Clean Water Act §§ 309 (b), (c), and (g) and 505 or under §§ 62.1-44.20 through 62.1-44.32 of the Code of Virginia.  Compliance with a permit issued pursuant to § 402 of the Clean Water Act is deemed compliance, for purposes of §§ 309 and 505, with §§ 301, 302, 306, 307, and 403, except any standard imposed under § 307 for toxic pollutants injurious to human health.  If you are covered as a co-permittee under an individual permit or under a general permit by means of a joint registration statement, you remain subject to the enforcement actions and penalties for the failure to comply with the terms of the permit in your jurisdiction except as set forth in subdivision E 2 of this section.

G. Will the small MS4 storm water program regulations at subsections B through F of this section change in the future?

The board will evaluate the small MS4 regulations at subsections B through F of this section after December 10, 2012, and make any necessary revisions.  (EPA intends to conduct an enhanced research effort and compile a comprehensive evaluation of the NPDES MS4 storm water program.  The board will re-evaluate the regulations based on data from the EPA NPDES MS4 storm water program, from research on receiving water impacts from storm water, and the effectiveness of best management practices (BMPs), as well as other relevant information sources.)

9 VAC 25-31-130. Concentrated animal feeding operations.

A. Permit requirement for CAFOs.

1. Concentrated animal feeding operations are point sources that require VPDES permits for discharges or potential discharges. Once an operation is defined as a CAFO, the VPDES requirements for CAFOs apply with respect to all animals in confinement at the operation and all manure, litter and process wastewater generated by those animals or the production of those animals, regardless of the type of animal.

2. Two or more animal feeding operations under common ownership are considered, for the purposes of this chapter, to be a single animal feeding operation if they adjoin each other or if they use a common area or system for the disposal of wastes.

B. Case-by-case designations. The board may designate any animal feeding operation as a concentrated animal feeding operation upon determining that it is a significant contributor of pollution to surface waters.

1. In making this designation the board shall consider the following factors:

a. The size of the animal feeding operation and the amount of wastes reaching surface waters;

b. The location of the animal feeding operation relative to surface waters;

c. The means of conveyance of animal wastes and process wastewaters into surface waters;

d. The slope, vegetation, rainfall, and other factors affecting the likelihood or frequency of discharge of animal wastes and process wastewaters into surface waters; and

e. Other relevant factors.

2. No animal feeding operation with less than the numbers of animals set forth in the definition of Medium CAFO in this regulation shall be designated as a concentrated animal feeding operation unless:

a. Pollutants are discharged into surface waters through a manmade ditch, flushing system, or other similar manmade device; or

b. Pollutants are discharged directly into surface waters which originate outside of the facility and pass over, across, or through the facility or otherwise come into direct contact with the animals confined in the operation.

3. A permit application shall not be required from a concentrated animal feeding operation designated under this subsection until the board has conducted an on-site inspection of the operation and determined that the operation should and could be regulated under the VPDES permit program.

C. Who must seek coverage under a VPDES permit?

1. All CAFO owners or operators must apply for a permit. All CAFO owners or operators must seek coverage under a VPDES permit, except as provided in subdivision 2 of this subsection. Specifically, the CAFO owner or operator must either apply for an individual VPDES permit or apply for coverage under a VPDES general permit. If there is no VPDES general permit available to the CAFO, the CAFO owner or operator must submit an application for an individual permit to the board.

2. Exception. An owner or operator of a Large CAFO does not need to seek coverage under a VPDES permit if the owner or operator has received a notice from the board of a determination under 9 VAC 25-31-130 C 5 that the CAFO has “no potential to discharge” manure, litter or process wastewater.

3. Information to submit with permit application. A permit application for an individual permit must include the information specified in 9 VAC 25-31-100 I. A notice of intent for a general permit must include the information specified in 9 VAC 25-31-100 I and 9 VAC 25-31-170.

4. Land application discharges from a CAFO are subject to VPDES requirements. The discharge of manure, litter or process wastewater to surface waters from a CAFO as the result of the application of that manure, litter or process wastewater by the CAFO to land areas under its control is a discharge from that CAFO subject to VPDES requirements, except where it is an agricultural storm water discharge as provided in 33 USC § 1362(14). For purposes of this subdivision, where the manure, litter or process wastewater has been applied in accordance with a nutrient management plan approved by the Department of Conservation and Recreation and in accordance with site specific nutrient management practices that ensure appropriate agricultural utilization of the nutrients in the manure, litter or process wastewater, as specified in 9 VAC 25-31-200 F E, a discharge of manure, litter or process wastewater from land areas under the control of a CAFO is an agricultural storm water discharge.

5. “No potential to discharge” determinations for Large CAFOs.

a. Determination by the board. The board, upon request, may make a case-specific determination that a Large CAFO has “no potential to discharge” pollutants to surface waters. In making this determination, the board must consider the potential for discharges from both the production area and any land application areas. The board must also consider any record of prior discharges by the CAFO. In no case may the CAFO be determined to have “no potential to discharge” if it has had a discharge within the five years prior to the date of the request submitted under subdivision C 5 b of this section. For purposes of this section, the term “no potential to discharge” means that there is no potential for any CAFO manure, litter or process wastewater to be added to surface waters under any circumstance or climatic condition. A determination that there is “no potential to discharge” for purposes of this section only relates to the discharges of manure, litter and process wastewater covered by this section.

b. Information to support a “no potential to discharge” request. In requesting a determination of “no potential to discharge,” the CAFO owner or operator must submit any information that would support such a determination within the time frame provided by the board and in accordance with subdivisions 6 and 7 of this subsection. Such information must include all the information specified in 9 VAC 25-31-100 F and 9 VAC 25-31-100 I 1. The board has discretion to require additional information to supplement the request, and may also gather additional information through onsite inspection of the CAFO.

c. Process for making a “no potential to discharge” determination. Before making a final decision to grant a “no potential to discharge” determination, the board must issue a notice to the public stating that a "no potential to discharge” request has been received. This notice must be accompanied by a fact sheet that includes, when applicable: a brief description of the type of facility or activity that is the subject of the “no potential to discharge” determination; a brief summary of the factual basis, upon which the request is based, for granting the “no potential to discharge” determination; and a description of the procedures for reaching a final decision on the “no potential to discharge” determination.

The board must base the decision to grant a “no potential to discharge” determination on the administrative record, which includes all information submitted in support of a “no potential to discharge” determination and any other supporting data gathered by the board. The board must notify any CAFO seeking a “no potential to discharge” determination of its final determination within 90 days of receiving the request.

d. Deadline for requesting a “no potential to discharge” determination. The owner or operator must request a “no potential to discharge” determination by the applicable permit application date specified in subdivision C 6 of this subsection.

e. The “no potential to discharge” determination does not relieve the CAFO from the consequences of an actual discharge. Any unpermitted CAFO that discharges pollutants into surface waters is in violation of State Water Control Law even if it has received a “no potential to discharge” determination from the board. Any CAFO that has received a determination of “no potential to discharge”, but that anticipates changes in circumstances that could create the potential for a discharge, should contact the Department of Environmental Quality, and apply for and obtain permit authorization prior to the change of circumstances.

6. When a CAFO must seek coverage under a VPDES permit.

a. Operations defined as CAFOs prior to April 14, 2003. For operations that are defined as CAFOs under regulations that are in effect prior to April 14, 2003, the owner or operator must have or seek to obtain coverage under a VPDES permit as of April 14, 2003, and comply with all applicable VPDES requirements, including the duty to maintain permit coverage in accordance with subdivision 7 of this subsection.

b. Operations defined as CAFOs as of April 14, 2003, that were not defined as CAFOs prior to that date. For all CAFOs, the owner or operator of the CAFO must seek to obtain coverage under a VPDES permit by January 1, 2006.

c. Operations that become defined as CAFOs after April 14, 2003, but that are not new sources. For newly constructed AFOs and CAFOs that make changes to their operations that result in becoming defined as CAFOs for the first time, after April 14, 2003, but are not new sources, the owner or operator must seek to obtain coverage under a VPDES permit, as follows:

(1) For newly constructed operations not subject to effluent limitation guidelines, 180 days prior to the time the CAFO commences operation; or

(2) For other operations (e.g., resulting from an increase in the number of animals), as soon as possible, but no later than 90 days after becoming defined as a CAFO; except that

(3) If an operational change that makes the operation a CAFO would not have made it a CAFO prior to April 14, 2003, the operation has at least until April 14, 2006.

d. New sources. New sources must seek to obtain coverage under a permit at least 180 days prior to the time the CAFO commences operation.

e. Operations that are designated CAFOs. For operations designated as a CAFO in accordance with subsection B of this section, the owner or operator must seek to obtain coverage under a VPDES permit no later than 90 days after receiving notice of the designation.

f. “No potential to discharge.” Notwithstanding any other provision of this section, a CAFO that has received a “no potential to discharge” determination in accordance with subdivision 5 of this subsection is not required to seek coverage under a VPDES permit. If circumstances materially change at a CAFO that has received a “no potential to discharge” determination, such that the CAFO has a potential for a discharge, the CAFO has a duty to immediately notify the board and seek coverage under a VPDES permit within 30 days after the change in circumstances.

7. Duty to maintain permit coverage. No later than 180 days before the expiration of the permit, the permittee must submit an application to renew its permit, in accordance with 9 VAC 25-31-100. However, the permittee need not continue to seek continued permit coverage or reapply for a permit if:

a. The facility has ceased operation or is no longer a CAFO; and

b. The permittee has demonstrated to the satisfaction of the board that there is no remaining potential for a discharge of manure, litter or associated process wastewater that was generated while the operation was a CAFO, other than agricultural storm water from application areas.

9 VAC 25-31-170. General permits.

A. The board may issue a general permit in accordance with the following:

1. The general permit shall be written to cover one or more categories or subcategories of discharges or sludge use or disposal practices or facilities described in the permit under subdivision 2 b of this subsection, except those covered by individual permits, within a geographic area. The area should correspond to existing geographic or political boundaries, such as:

a. Designated planning areas under §§ 208 and 303 of CWA;

b. Sewer districts or sewer authorities;

c. City, county, or state political boundaries;

d. State highway systems;

e. Standard metropolitan statistical areas as defined by the Office of Management and Budget;

f. Urbanized areas as designated by the Bureau of the Census according to criteria in 30 FR 15202 (May 1, 1974); or

g. Any other appropriate division or combination of boundaries.

2. The general permit may be written to regulate one or more categories or subcategories of discharges or sludge use or disposal practices or facilities, within the area described in subdivision 1 of this subsection, where the sources within a covered subcategory of discharges are either:

a. Storm water point sources; or

b. One or more categories or subcategories of point sources other than storm water point sources, or one or more categories or subcategories of treatment works treating domestic sewage, if the sources or treatment works treating domestic sewage within each category or subcategory all:

(1) Involve the same or substantially similar types of operations;

(2) Discharge the same types of wastes or engage in the same types of sludge use or disposal practices;

(3) Require the same effluent limitations, operating conditions, or standards for sewage sludge use or disposal;

(4) Require the same or similar monitoring; and

(5) In the opinion of the board, are more appropriately controlled under a general permit than under individual permits.

3. Where sources within a specific category of dischargers are subject to water quality-based limits imposed pursuant to 9 VAC 25-31-220, the sources in that specific category or subcategory shall be subject to the same water quality-based effluent limitations.

4. The general permit must clearly identify the applicable conditions for each category or subcategory of dischargers or treatment works treating domestic sewage covered by the permit.

5. The general permit may exclude specified sources or areas from coverage.

B. Administration.

1. General permits may be issued, modified, revoked and reissued, or terminated in accordance with applicable requirements of this chapter.

2. Authorization to discharge, or authorization to engage in sludge use and disposal practices.

a. Except as provided in subdivisions 2 e and 2 f of this subsection, dischargers (or treatment works treating domestic sewage) seeking coverage under a general permit shall submit to the department a written notice of intent to be covered by the general permit. A discharger (or treatment works treating domestic sewage) who fails to submit a notice of intent in accordance with the terms of the permit is not authorized to discharge, (or in the case of a sludge disposal permit, to engage in a sludge use or disposal practice), under the terms of the general permit unless the general permit, in accordance with subdivision 2 e of this subsection, contains a provision that a notice of intent is not required or the board notifies a discharger (or treatment works treating domestic sewage) that it is covered by a general permit in accordance with subdivision 2 f of this subsection. A complete and timely notice of intent (NOI) to be covered in accordance with general permit requirements fulfills the requirements for permit applications for the purposes of this chapter.

b. The contents of the notice of intent shall be specified in the general permit and shall require the submission of information necessary for adequate program implementation, including at a minimum, the legal name and address of the owner or operator, the facility name and address, type of facility or discharges, and the receiving stream or streams. General permits for storm water discharges associated with industrial activity from inactive mining, inactive oil and gas operations, or inactive landfills occurring on federal lands where an operator cannot be identified may contain alternative notice of intent requirements. Notices of intent for coverage under a general permit for concentrated animal feeding operations must include the information specified in 9 VAC 25-31-100 I 1, including a topographic map. All notices of intent shall be signed in accordance with 9 VAC 25-31-110.

c. General permits shall specify the deadlines for submitting notices of intent to be covered and the date or dates when a discharger is authorized to discharge under the permit.

d. General permits shall specify whether a discharger (or treatment works treating domestic sewage) that has submitted a complete and timely notice of intent to be covered in accordance with the general permit and that is eligible for coverage under the permit, is authorized to discharge, (or in the case of a sludge disposal permit, to engage in a sludge use or disposal practice), in accordance with the permit either upon receipt of the notice of intent by the department, after a waiting period specified in the general permit, on a date specified in the general permit, or upon receipt of notification of inclusion by the board. Coverage may be terminated or revoked in accordance with subdivision 3 of this subsection.

e. Discharges other than discharges from publicly owned treatment works, combined sewer overflows, municipal separate storm sewer systems, primary industrial facilities, and storm water discharges associated with industrial activity, may, at the discretion of the board, be authorized to discharge under a general permit without submitting a notice of intent where the board finds that a notice of intent requirement would be inappropriate. In making such a finding, the board shall consider: the type of discharge; the expected nature of the discharge; the potential for toxic and conventional pollutants in the discharges; the expected volume of the discharges; other means of identifying discharges covered by the permit; and the estimated number of discharges to be covered by the permit. The board shall provide in the public notice of the general permit the reasons for not requiring a notice of intent.

f. The board may notify a discharger (or treatment works treating domestic sewage) that it is covered by a general permit, even if the discharger (or treatment works treating domestic sewage) has not submitted a notice of intent to be covered. A discharger (or treatment works treating domestic sewage) so notified may request an individual permit under subdivision 3 c of this subsection.

3. Requiring an individual permit.

a. The board may require any discharger authorized by a general permit to apply for and obtain an individual VPDES permit. Any interested person may request the board to take action under this subdivision. Cases where an individual VPDES permit may be required include the following:

(1) The discharger or treatment works treating domestic sewage is not in compliance with the conditions of the general VPDES permit;

(2) A change has occurred in the availability of demonstrated technology or practices for the control or abatement of pollutants applicable to the point source or treatment works treating domestic sewage;

(3) Effluent limitation guidelines are promulgated for point sources covered by the general VPDES permit;

(4) A water quality management plan containing requirements applicable to such point sources is approved;

(5) Circumstances have changed since the time of the request to be covered so that the discharger is no longer appropriately controlled under the general permit, or either a temporary or permanent reduction or elimination of the authorized discharge is necessary;

(6) Standards for sewage sludge use or disposal have been promulgated for the sludge use and disposal practice covered by the general VPDES permit; or

(7) The discharge(s) is a significant contributor of pollutants. In making this determination, the board may consider the following factors:

(a) The location of the discharge with respect to surface waters;

(b) The size of the discharge;

(c) The quantity and nature of the pollutants discharged to surface waters; and

(d) Other relevant factors;

b. Permits required on a case-by-case basis.

(1) The board may determine, on a case-by-case basis, that certain concentrated animal feeding operations, concentrated aquatic animal production facilities, storm water discharges, and certain other facilities covered by general permits that do not generally require an individual permit may be required to obtain an individual permit because of their contributions to water pollution.

(2) Whenever the board decides that an individual permit is required under this subsection, except as provided in subdivision 3 b (3) of this subsection, the board shall notify the discharger in writing of that decision and the reasons for it, and shall send an application form with the notice. The discharger must apply for a permit within 60 days of notice, unless permission for a later date is granted by the board. The question whether the designation was proper will remain open for consideration during the public comment period for the draft permit and in any subsequent public hearing.

(3) Prior to a case-by-case determination that an individual permit is required for a storm water discharge under this subsection, the board may require the discharger to submit a permit application or other information regarding the discharge under the law and § 308 of the CWA. In requiring such information, the board shall notify the discharger in writing and shall send an application form with the notice. The discharger must apply for a permit under 9 VAC 25-31-120 A 1 within 60 days of notice or under 9 VAC 25-31-120 A 9 7 within 180 days of notice, unless permission for a later date is granted by the board. The question whether the initial designation was proper will remain open for consideration during the public comment period for the draft permit and in any subsequent public hearing.

c. Any owner or operator authorized by a general permit may request to be excluded from the coverage of the general permit by applying for an individual permit. The owner or operator shall submit an application under 9 VAC 25-31-100 with reasons supporting the request. The request shall be processed under the applicable parts of this chapter. The request shall be granted by issuing of an individual permit if the reasons cited by the owner or operator are adequate to support the request.

d. When an individual VPDES permit is issued to an owner or operator otherwise subject to a general VPDES permit, the applicability of the general permit to the individual VPDES permittee is automatically terminated on the effective date of the individual permit.

e. A source excluded from a general permit solely because it already has an individual permit may request that the individual permit be revoked, and that it be covered by the general permit. Upon revocation of the individual permit, the general permit shall apply to the source.

9 VAC 25-31-200. Additional conditions applicable to specified categories of VPDES permits.

The following conditions, in addition to those set forth in 9 VAC 25-31-190, apply to all VPDES permits within the categories specified below:

A. Existing manufacturing, commercial, mining, and silvicultural dischargers. All existing manufacturing, commercial, mining, and silvicultural dischargers must notify the department as soon as they know or have reason to believe:

1. That any activity has occurred or will occur which would result in the discharge, on a routine or frequent basis, of any toxic pollutant which is not limited in the permit, if that discharge will exceed the highest of the following notification levels:

a. One hundred micrograms per liter (100 µg/l);

b. Two hundred micrograms per liter (200 µg/l) for acrolein and acrylonitrile; five hundred micrograms per liter (500 µg/l) for 2,4-dinitrophenol and for 2-methyl-4,6-dinitrophenol; and one milligram per liter (1 mg/l) for antimony;

c. Five times the maximum concentration value reported for that pollutant in the permit application; or

d. The level established by the board in accordance with 9 VAC 25-31-220 F.

2. That any activity has occurred or will occur which would result in any discharge, on a nonroutine or infrequent basis, of a toxic pollutant which is not limited in the permit, if that discharge will exceed the highest of the following notification levels:

a. Five hundred micrograms per liter (500 µg/l);

b. One milligram per liter (1 mg/l) for antimony;

c. Ten times the maximum concentration value reported for that pollutant in the permit application; or

d. The level established by the board in accordance with 9 VAC 25-31-220 F.

B. Publicly and privately owned treatment works. All POTWs and PVOTWs must provide adequate notice to the department of the following:

1. Any new introduction of pollutants into the POTW or PVOTW from an indirect discharger which would be subject to § 301 or § 306 of the CWA and the law if it were directly discharging those pollutants; and

2. Any substantial change in the volume or character of pollutants being introduced into that POTW or PVOTW by a source introducing pollutants into the POTW or PVOTW at the time of issuance of the permit.

3. For purposes of this subsection, adequate notice shall include information on (i) the quality and quantity of effluent introduced into the POTW or PVOTW, and (ii) any anticipated impact of the change on the quantity or quality of effluent to be discharged from the POTW or PVOTW.

4. When the monthly average flow influent to a POTW or PVOTW reaches 95% of the design capacity authorized by the VPDES permit for each month of any three-month period, the owner shall within 30 days notify the department in writing and within 90 days submit a plan of action for ensuring continued compliance with the terms of the permit.

a. The plan shall include the necessary steps and a prompt schedule of implementation for controlling any current problem, or any problem which could be reasonably anticipated, resulting from high influent flows.

b. Upon receipt of the owner's plan of action, the board shall notify the owner whether the plan is approved or disapproved. If the plan is disapproved, such notification shall state the reasons and specify the actions necessary to obtain approval of the plan.

c. Failure to timely submit an adequate plan shall be deemed a violation of the permit.

d. Nothing herein shall in any way impair the authority of the board to take enforcement action under §§ 62.1-44.15, 62.1-44.23, or 62.1-44.32 of the Code of Virginia.

C. Municipal separate storm sewer systems. The operator of a large or medium municipal separate storm sewer system or a municipal separate storm sewer that has been designated by the board under 9 VAC 25-31-120 A 1 e must submit an annual report by a date specified in the permit for such system. The report shall include:

1. The status of implementing the components of the storm water management program that are established as permit conditions;

2. Proposed changes to the storm water management programs that are established as permit condition. Such proposed changes shall be consistent with 9 VAC 25-31-120 C 2 d;

3. Revisions, if necessary, to the assessment of controls and the fiscal analysis reported in the permit application;

4. A summary of data, including monitoring data, that is accumulated throughout the reporting year;

5. Annual expenditures and budget for year following each annual report;

6. A summary describing the number and nature of enforcement actions, inspections, and public education programs; and

7. Identification of water quality improvements or degradation.

D. C. Wastewater works operator requirements.

1. The permittee shall employ or contract at least one wastewater works operator who holds a current wastewater license appropriate for the permitted facility. The license shall be issued in accordance with Title 54.1 of the Code of Virginia and the regulations of the Board for Waterworks and Wastewater Works Operators (18 VAC 160-20). Not withstanding the foregoing requirement, unless the discharge is determined by the board on a case-by-case basis to be a potential contributor of pollution, no licensed operator is required for wastewater treatment works:

a. That have a design hydraulic capacity equal to or less than 0.04 mgd;

b. That discharge industrial waste or other waste from coal mining operations; or

c. That do not utilize biological or physical/chemical treatment.

2. In making this case-by-case determination, the board shall consider the location of the discharge with respect to state waters, the size of the discharge, the quantity and nature of pollutants reaching state waters and the treatment methods used at the wastewater works.

3. The permittee shall notify the department in writing whenever he is not complying, or has grounds for anticipating he will not comply with the requirements of subdivision 1 of this subsection. The notification shall include a statement of reasons and a prompt schedule for achieving compliance.

E. D. Lake level contingency plans. Any VPDES permit issued for a surface water impoundment whose primary purpose is to provide cooling water to power generators shall include a lake level contingency plan to allow specific reductions in the flow required to be released when the water level above the dam drops below designated levels due to drought conditions, and such plan shall take into account and minimize any adverse effects of any release reduction requirements on downstream users. This subsection shall not apply to any such facility that addresses releases and flow requirements during drought conditions in a Virginia Water Protection Permit.

F. E. Concentrated Animal Feeding Operations (CAFOs). The activities of the CAFO shall not contravene the Water Quality Standards, as amended and adopted by the board, or any provision of the State Water Control Law. There shall be no point source discharge of manure, litter or process wastewater to surface waters of the state except in the case of a storm event greater than the 25-year, 24-hour storm, except that for swine, poultry, and veal calf operations constructed after April 14, 2003, in the case of a storm event greater than the 100-year, 24-hour storm. Agricultural storm water discharges are permitted. Domestic sewage or industrial waste shall not be managed under the Virginia Pollutant Discharge Elimination System General Permit for CAFOs (9 VAC 25-191). Any permit issued to a CAFO must include:

1. Requirements to develop and implement a nutrient management plan. At a minimum, a nutrient management plan must include best management practices and procedures necessary to implement applicable effluent limitations and standards. Permitted CAFOs must have their nutrient management plans developed and implemented by December 31, 2006. CAFOs that seek to obtain coverage under a permit after December 31, 2006, must have a nutrient management plan developed and implemented upon the date of permit coverage. The nutrient management plan must, to the extent applicable:

a. Ensure adequate storage of manure, litter, and process wastewater, including procedures to ensure proper operation and maintenance of the storage facilities;

b. Ensure proper management of mortalities (i.e., dead animals) to ensure that they are not disposed of in a liquid manure, storm water, or process wastewater storage or treatment system that is not specifically designed to treat animal mortalities;

c. Ensure that clean water is diverted, as appropriate, from the production area;

d. Prevent direct contact of confined animals with surface waters of the state;

e. Ensure that chemicals and other contaminants handled onsite are not disposed of in any manure, litter, process wastewater, or stormwater storage or treatment system unless specifically designed to treat such chemicals and other contaminants;

f. Identify appropriate site specific conservation practices to be implemented, including as appropriate buffers or equivalent practices, to control runoff of pollutants to surface waters of the state;

g. Identify protocols for appropriate testing of manure, litter, process wastewater and soil;

h. Establish protocols to land apply manure, litter or process wastewater in accordance with site specific nutrient management practices that ensure appropriate agricultural utilization of the nutrients in the manure, litter or process wastewater; and

i. Identify specific records that will be maintained to document the implementation and management of the minimum elements described above.

2. Recordkeeping requirements. The permittee must create, maintain for five years, and make available to the director upon request the following records:

a. All applicable records identified pursuant to subdivision 1 i of this subsection;

b. In addition, all CAFOs subject to EPA Effluent Guidelines for Feedlots (40 CFR Part 412) must comply with recordkeeping requirements as specified in 40 CFR 412.37(b) and (c) and 40 CFR 412.47(b) and (c);

A copy of the CAFO's site-specific nutrient management plan must be maintained on site and made available to the director upon request.

3. Requirements relating to transfer of manure or process wastewater to other persons. Prior to transferring manure, litter or process wastewater to other persons, large CAFOs must provide the recipient of the manure, litter or process wastewater with the most current nutrient analysis. The analysis provided must be consistent with the requirements of EPA Effluent Guidelines for Feedlots (40 CFR Part 412). Large CAFOs must retain for five years records of the date, recipient name and address and approximate amount of manure, litter or process wastewater transferred to another person.

4. Annual reporting requirements for CAFOs. The permittee must submit an annual report to the director. The annual report must include:

a. The number and type of animals, whether in open confinement or housed under roof (beef cattle, broilers, layers, swine weighing 55 pounds or more, swine weighing less than 55 pounds, mature dairy cows, dairy heifers, veal calves, sheep and lambs, horses, ducks, turkeys, other);

b. Estimated amount of total manure, litter and process wastewater generated by the CAFO in the previous 12 months (tons/gallons);

c. Estimated amount of total manure, litter and process wastewater transferred to other persons by the CAFO in the previous 12 months (tons/gallons);

d. Total number of acres for land application covered by the nutrient management plan developed in accordance with subdivision 1 of this subsection;

e. Total number of acres under control of the CAFO that were used for land application of manure, litter and process wastewater in the previous 12 months;

f. Summary of all manure, litter and process wastewater discharges from the production area that occurred in the previous 12 months including date, time and approximate volume; and

g. A statement indicating whether the current version of the CAFO's nutrient management plan was developed or approved by a certified nutrient management planner.

9 VAC 25-31-220. Establishing limitations, standards, and other permit conditions.

In addition to the conditions established under 9 VAC 25-31-210 A, each VPDES permit shall include conditions meeting the following requirements when applicable.

A. 1. Technology-based effluent limitations and standards based on effluent limitations and standards promulgated under § 301 of the CWA, on new source performance standards promulgated under § 306 of CWA, on case-by-case effluent limitations determined under § 402(a)(1) of CWA, or a combination of the three.  For new sources or new dischargers, these technology-based limitations and standards are subject to the provisions of 9 VAC 25-31-180 B (protection period).

2. The board may authorize a discharger subject to technology-based effluent limitations guidelines and standards in a VPDES permit to forego sampling of a pollutant found at 40 CFR Subchapter N (2000) if the discharger has demonstrated through sampling and other technical factors that the pollutant is not present in the discharge or is present only at background levels from intake water and without any increase in the pollutant due to activities of the discharger.  This waiver is good only for the term of the permit and is not available during the term of the first permit issued to a discharger.  Any request for this waiver must be submitted when applying for a reissued permit or modification of a reissued permit.  The request must demonstrate through sampling or other technical information, including information generated during an earlier permit term, that the pollutant is not present in the discharge or is present only at background levels from intake water and without any increase in the pollutant due to activities of the discharger.  Any grant of the monitoring waiver must be included in the permit as an express permit condition and the reasons supporting the grant must be documented in the permit's fact sheet or statement of basis.  This provision does not supersede certification processes and requirements already established in existing effluent limitations guidelines and standards.

B. Other effluent limitations and standards.

1. Other effluent limitations and standards under §§ 301, 302, 303, 307, 318 and 405 of the CWA. If any applicable toxic effluent standard or prohibition (including any schedule of compliance specified in such effluent standard or prohibition) is promulgated under § 307(a) of the CWA for a toxic pollutant and that standard or prohibition is more stringent than any limitation on the pollutant in the permit, the board shall institute proceedings under this chapter to modify or revoke and reissue the permit to conform to the toxic effluent standard or prohibition.

2. Standards for sewage sludge use or disposal under § 405(d) of the CWA and Part VI (9 VAC 25-31-420 et seq.) of this chapter unless those standards have been included in a permit issued under the appropriate provisions of Subtitle C of the Solid Waste Disposal Act (42 USC § 6901 et seq.), Part C of Safe Drinking Water Act (42 USC § 300f et seq.), the Marine Protection, Research, and Sanctuaries Act of 1972 (33 USC § 1401 et seq.), or the Clean Air Act (42 USC § 4701 et seq.), or in another permit issued by the Department of Environmental Quality, the Virginia Department of Health or any other appropriate state agency under another permit program approved by the administrator.  When there are no applicable standards for sewage sludge use or disposal, the permit may include requirements developed on a case-by-case basis to protect public health and the environment from any adverse effects which may occur from toxic pollutants in sewage sludge.  If any applicable standard for sewage sludge use or disposal is promulgated under § 405(d) of the CWA and that standard is more stringent than any limitation on the pollutant or practice in the permit, the board may initiate proceedings under this chapter to modify or revoke and reissue the permit to conform to the standard for sewage sludge use or disposal.

C. Reopener clause.  For any permit issued to a treatment works treating domestic sewage (including sludge-only facilities), the board shall include a reopener clause to incorporate any applicable standard for sewage sludge use or disposal promulgated under § 405(d) of the CWA. The board may promptly modify or revoke and reissue any permit containing the reopener clause required by this subdivision if the standard for sewage sludge use or disposal is more stringent than any requirements for sludge use or disposal in the permit, or controls a pollutant or practice not limited in the permit.

D. Water quality standards and state requirements.  Any requirements in addition to or more stringent than promulgated effluent limitations guidelines or standards under §§ 301, 304, 306, 307, 318 and 405 of the CWA necessary to:

1. Achieve water quality standards established under the law and § 303 of the CWA, including state narrative criteria for water quality.

a. Limitations must control all pollutants or pollutant parameters (either conventional, nonconventional, or toxic pollutants) which the board determines are or may be discharged at a level which will cause, have the reasonable potential to cause, or contribute to an excursion above any Virginia water quality standard, including Virginia narrative criteria for water quality.

b. When determining whether a discharge causes, has the reasonable potential to cause, or contributes to an in-stream excursion above a narrative or numeric criteria within a Virginia water quality standard, the board shall use procedures which account for existing controls on point and nonpoint sources of pollution, the variability of the pollutant or pollutant parameter in the effluent, the sensitivity of the species to toxicity testing (when evaluating whole effluent toxicity), and where appropriate, the dilution of the effluent in the receiving water.

c. When the board determines, using the procedures in subdivision 1 b of this subsection, that a discharge causes, has the reasonable potential to cause, or contributes to an in-stream excursion above the allowable ambient concentration of a Virginia numeric criteria within a Virginia water quality standard for an individual pollutant, the permit must contain effluent limits for that pollutant.

d. Except as provided in this subdivision, when the board determines, using the procedures in subdivision 1 b of this subsection, toxicity testing data, or other information, that a discharge causes, has the reasonable potential to cause, or contributes to an in-stream excursion above a narrative criterion within an applicable Virginia water quality standard, the permit must contain effluent limits for whole effluent toxicity.  Limits on whole effluent toxicity are not necessary where the board demonstrates in the fact sheet or statement of basis of the VPDES permit, using the procedures in subdivision 1 b of this subsection, that chemical-specific limits for the effluent are sufficient to attain and maintain applicable numeric and narrative Virginia water quality standards.

e. Where Virginia has not established a water quality criterion for a specific chemical pollutant that is present in an effluent at a concentration that causes, has the reasonable potential to cause, or contributes to an excursion above a narrative criterion within an applicable Virginia water quality standard, the board must establish effluent limits using one or more of the following options:

(1) Establish effluent limits using a calculated numeric water quality criterion for the pollutant which the board demonstrates will attain and maintain applicable narrative water quality criteria and will fully protect the designated use.  Such a criterion may be derived using a proposed Virginia criterion, or an explicit policy or regulation interpreting Virginia's narrative water quality criterion, supplemented with other relevant information which may include:  EPA's Water Quality Standards Handbook, August 1994, risk assessment data, exposure data, information about the pollutant from the Food and Drug Administration, and current EPA criteria documents;  or

(2) Establish effluent limits on a case-by-case basis, using EPA's water quality criteria, published under § 307(a) of the CWA, supplemented where necessary by other relevant information; or

(3) Establish effluent limitations on an indicator parameter for the pollutant of concern, provided:

(a) The permit identifies which pollutants are intended to be controlled by the use of the effluent limitation;

(b) The fact sheet required by 9 VAC 25-31-280 sets forth the basis for the limit, including a finding that compliance with the effluent limit on the indicator parameter will result in controls on the pollutant of concern which are sufficient to attain and maintain applicable water quality standards;

(c) The permit requires all effluent and ambient monitoring necessary to show that during the term of the permit the limit on the indicator parameter continues to attain and maintain applicable water quality standards; and

(d) The permit contains a reopener clause allowing the board to modify or revoke and reissue the permit if the limits on the indicator parameter no longer attain and maintain applicable water quality standards.

f. When developing water quality-based effluent limits under this subdivision the board shall ensure that:

(1) The level of water quality to be achieved by limits on point sources established under this subsection is derived from, and complies with all applicable water quality standards; and

(2) Effluent limits developed to protect a narrative water quality criterion, a numeric water quality criterion, or both, are consistent with the assumptions and requirements of any available wasteload allocation for the discharge prepared by Virginia and approved by EPA pursuant to 40 CFR 130.7 (2000);

2. Attain or maintain a specified water quality through water quality related effluent limits established under the law and § 302 of the CWA;

3. Conform to the conditions of a Virginia Water Protection Permit (VWPP) issued under the law and § 401 of the CWA.;

4. Conform to applicable water quality requirements under § 401(a)(2) of the CWA when the discharge affects a state other than Virginia;

5. Incorporate any more stringent limitations, treatment standards, or schedule of compliance requirements established under the law or regulations in accordance with § 301(b)(1)(C) of the CWA;

6. Ensure consistency with the requirements of a Water Quality Management plan approved by EPA under § 208(b) of the CWA;

7. Incorporate § 403(c) criteria under 40 CFR Part 125, Subpart M (2000), for ocean discharges; or

8. Incorporate alternative effluent limitations or standards where warranted by fundamentally different factors, under 40 the CFR Part 125, Subpart D (2000).

E. Technology-based controls for toxic pollutants.  Limitations established under subsections A, B, or D of this section, to control pollutants meeting the criteria listed in subdivision 1 of this subsection.  Limitations will be established in accordance with subdivision 2 of this subsection.  An explanation of the development of these limitations shall be included in the fact sheet.

1. Limitations must control all toxic pollutants which the board determines (based on information reported in a permit application or in a notification required by the permit or on other information) are or may be discharged at a level greater than the level which can be achieved by the technology-based treatment requirements appropriate to the permittee; or

2. The requirement that the limitations control the pollutants meeting the criteria of subdivision 1 of this subsection will be satisfied by:

a. Limitations on those pollutants; or

b. Limitations on other pollutants which, in the judgment of the board, will provide treatment of the pollutants under subdivision 1 of this subsection to the levels required by the law and 40 CFR Part 125, Subpart A (2000).

F. A notification level which exceeds the notification level of 9 VAC 25-31-200 A 1 a, b, or c, upon a petition from the permittee or on the board's initiative.  This new notification level may not exceed the level which can be achieved by the technology-based treatment requirements appropriate to the permittee.

G. Twenty-four-hour reporting.  Pollutants for which the permittee must report violations of maximum daily discharge limitations under 9 VAC 25-31-190 L 7 b (3) (24-hour reporting) shall be listed in the permit.  This list shall include any toxic pollutant or hazardous substance, or any pollutant specifically identified as the method to control a toxic pollutant or hazardous substance.

H. Durations for permits, as set forth in 9 VAC 25-31-240.

I. Monitoring requirements.  The following monitoring requirements:

1. Requirements concerning the proper use, maintenance, and installation, when appropriate, of monitoring equipment or methods (including biological monitoring methods when appropriate);

2. Required monitoring including type, intervals, and frequency sufficient to yield data which are representative of the monitored activity including, when appropriate, continuous monitoring;

3. Applicable reporting requirements based upon the impact of the regulated activity and as specified in 9 VAC 25-31-190 and in subdivisions 5 through 8 of this subsection.  Reporting shall be no less frequent than specified in the above regulation;

4. To assure compliance with permit limitations, requirements to monitor:

a. The mass (or other measurement specified in the permit) for each pollutant limited in the permit;

b. The volume of effluent discharged from each outfall;

c. Other measurements as appropriate including pollutants in internal waste streams; pollutants in intake water for net limitations; frequency, rate of discharge, etc., for noncontinuous discharges; pollutants subject to notification requirements; and pollutants in sewage sludge or other monitoring as specified in Part VI (9 VAC 25-31-420 et seq.) of this chapter; or as determined to be necessary on a case-by-case basis pursuant to the law and § 405(d)(4) of the CWA; and

d. According to test procedures approved under 40 CFR Part 136 (2000) for the analyses of pollutants having approved methods under that part, or alternative EPA approved methods, and according to a test procedure specified in the permit for pollutants with no approved methods;

5. Except as provided in subdivisions 7 and 8 of this subsection, requirements to report monitoring results shall be established on a case-by-case basis with a frequency dependent on the nature and effect of the discharge, but in no case less that once a year.  For sewage sludge use or disposal practices, requirements to monitor and report results shall be established on a case-by-case basis with a frequency dependent on the nature and effect of the sewage sludge use or disposal practice;  minimally this shall be as specified in Part VI of this chapter (where applicable), but in no case less than once a year;

6. Requirements to report monitoring results for storm water discharges associated with industrial activity which are subject to an effluent limitation guideline shall be established on a case-by-case basis with a frequency dependent on the nature and effect of the discharge, but in no case less than once a year;

7. Requirements to report monitoring results for storm water discharges associated with industrial activity (other than those addressed in subdivision 6 of this subsection) shall be established on a case-by-case basis with a frequency dependent on the nature and effect of the discharge.  At a minimum, a permit for such a discharge must require:

a. The discharger to conduct an annual inspection of the facility site to identify areas contributing to a storm water discharge associated with industrial activity and evaluate whether measures to reduce pollutant loading identified in a storm water pollution prevention plan are adequate and properly implemented in accordance with the terms of the permit or whether additional control measures are needed;

b. The discharger to maintain for a period of three years a record summarizing the results of the inspection and a certification that the facility is in compliance with the plan and the permit, and identifying any incidents of noncompliance;

c. Such report and certification be signed in accordance with 9 VAC 25-31-110; and

d. Permits for storm water discharges associated with industrial activity from inactive mining operations may, where annual inspections are impracticable, require certification once every three years by a Registered Professional Engineer that the facility is in compliance with the permit, or alternative requirements; and

8. Permits which do not require the submittal of monitoring result reports at least annually shall require that the permittee report all instances of noncompliance not reported under 9 VAC 25-31-190 L 1, 4, 5, 6, and 7 at least annually.

J. Pretreatment program for POTWs.  Requirements for POTWs to:

1. Identify, in terms of character and volume of pollutants, any significant indirect dischargers into the POTW subject to pretreatment standards under § 307(b) of the CWA and Part VII (9 VAC 25-31-730 et seq.) of this chapter;

2. Submit a local program when required by and in accordance with Part VII of this chapter to assure compliance with pretreatment standards to the extent applicable under § 307(b) of the CWA. The local program shall be incorporated into the permit as described in Part VII of this chapter.  The program shall require all indirect dischargers to the POTW to comply with the reporting requirements of Part VII of this chapter;

3. Provide a written technical evaluation of the need to revise local limits under Part VII of this chapter following permit issuance or reissuance; and

4. For POTWs which are sludge-only facilities, a requirement to develop a pretreatment program under Part VII of this chapter when the board determines that a pretreatment program is necessary to assure compliance with Part VI of this chapter.

K. Best management practices to control or abate the discharge of pollutants when:

1. Authorized under § 304(e) of the CWA for the control of toxic pollutants and hazardous substances from ancillary industrial activities;

2. Authorized under § 402(p) of the CWA for the control of storm water discharges;

3. Numeric effluent limitations are infeasible; or

4. The practices are reasonably necessary to achieve effluent limitations and standards or to carry out the purposes and intent of the law and the CWA.

L. Reissued permits.

1. In the case of effluent limitations established on the basis of § 402(a)(1)(B) of the CWA, a permit may not be renewed, reissued, or modified on the basis of effluent guidelines promulgated under § 304(b) of the CWA subsequent to the original issuance of such permit, to contain effluent limitations which are less stringent than the comparable effluent limitations in the previous permit.  In the case of effluent limitations established on the basis of §§ 301(b)(1)(C) or 303(d) or (e) of the CWA, a permit may not be renewed, reissued, or modified to contain effluent limitations which are less stringent than the comparable effluent limitations in the previous permit except in compliance with § 303(d)(4) of the CWA.

2. Exceptions. A permit with respect to which subdivision 1 of this subsection applies may be renewed, reissued, or modified to contain a less stringent effluent limitation applicable to a pollutant, if:

a. Material and substantial alterations or additions to the permitted facility occurred after permit issuance which justify the application of a less stringent effluent limitation;

b. (1) Information is available which was not available at the time of permit issuance (other than revised regulations, guidance, or test methods) and which would have justified the application of a less stringent effluent limitation at the time of permit issuance; or

(2) The board determines that technical mistakes or mistaken interpretations of law were made in issuing the permit under § 402(a)(1)(B) of the CWA;

c. A less stringent effluent limitation is necessary because of events over which the permittee has no control and for which there is no reasonably available remedy;

d. The permittee has received a permit modification under the law and §§ 301(c), 301(g), 301(h), 301(i), 301(k), 301(n), or 316(a) of the CWA; or

e. The permittee has installed the treatment facilities required to meet the effluent limitations in the previous permit and has properly operated and maintained the facilities but has nevertheless been unable to achieve the previous effluent limitations, in which case the limitations in the reviewed, reissued, or modified permit may reflect the level of pollutant control actually achieved (but shall not be less stringent than required by effluent guidelines in effect at the time of permit renewal, reissuance, or modification).

Subdivision 2 b of this subsection shall not apply to any revised waste load allocations or any alternative grounds for translating water quality standards into effluent limitations, except where the cumulative effect of such revised allocations results in a decrease in the amount of pollutants discharged into the concerned waters, and such revised allocations are not the result of a discharger eliminating or substantially reducing its discharge of pollutants due to complying with the requirements of the law or the CWA or for reasons otherwise unrelated to water quality.

3. In no event may a permit with respect to which subdivision 2 of this subsection applies be renewed, reissued, or modified to contain an effluent limitation which is less stringent than required by effluent guidelines in effect at the time the permit is renewed, reissued, or modified.  In no event may such a permit to discharge into waters be renewed, issued, or modified to contain a less stringent effluent limitation if the implementation of such limitation would result in a violation of a Virginia water quality standard applicable to such waters.

M. For a privately owned treatment works, any conditions expressly applicable to any user, as a limited co-permittee, that may be necessary in the permit issued to the treatment works to ensure compliance with applicable requirements under this part.  Alternatively, the board may issue separate permits to the treatment works and to its users, or may require a separate permit application from any user.  The board's decision to issue a permit with no conditions applicable to any user, to impose conditions on one or more users, to issue separate permits, or to require separate applications, and the basis for that decision, shall be stated in the fact sheet for the draft permit for the treatment works.

N. Any conditions imposed in grants made by the board to POTWs under §§ 201 and 204 of the CWA which are reasonably necessary for the achievement of effluent limitations under § 301 of the CWA and the law.

O. Requirements governing the disposal of sewage sludge from publicly owned treatment works or any other treatment works treating domestic sewage for any use regulated by Part VI of this chapter.

P. When a permit is issued to a facility that may operate at certain times as a means of transportation over water, a condition that the discharge shall comply with any applicable regulations promulgated by the secretary of the department in which the Coast Guard is operating, that establish specifications for safe transportation, handling, carriage, and storage of pollutants.

Q. Navigation. Any conditions that the Secretary of the Army considers necessary to ensure that navigation and anchorage will not be substantially impaired in accordance with 9 VAC 25-31-330.

R. Qualifying state, tribal, or local programs.

1. For storm water discharges associated with small construction activity identified in 9 VAC 25-31-10, the board may include permit conditions that incorporate qualifying state, tribal, or local erosion and sediment control program requirements by reference.  Where a qualifying state, tribal, or local program does not include one or more of the elements in this subdivision, then the board must include those elements as conditions in the permit.  A qualifying state, tribal, or local erosion and sediment control program is one that includes:

a. Requirements for construction site operators to implement appropriate erosion and sediment control best management practices;

b. Requirements for construction site operators to control waste such as discarded building materials, concrete truck washout, chemicals, litter, and sanitary waste at the construction site that may cause adverse impacts to water quality;

c. Requirements for construction site operators to develop and implement a storm water pollution prevention plan.  A storm water pollution prevention plan includes site descriptions;  descriptions of appropriate control measures;  copies of approved state, tribal or local requirements;  maintenance procedures;  inspection procedures;  and identification of nonstorm water discharges;  and

d. Requirements to submit a site plan for review that incorporates consideration of potential water quality impacts.

2. For storm water discharges from construction activity that does not meet the definition of a small construction activity, the board may include permit conditions that incorporate qualifying state, tribal, or local erosion and sediment control program requirements by reference.  A qualifying state, tribal or local erosion and sediment control program is one that includes the elements listed in subdivision 1 of this subsection and any additional requirements necessary to achieve the applicable technology-based standards of "best available technology" and "best conventional technology" based on the best professional judgment of the permit writer.

9 VAC 25-31-390. Modification or revocation and reissuance of permits.

A. Causes for modification.  The following are causes for modification but not revocation and reissuance of permits except when the permittee requests or agrees.

1. There are material and substantial alterations or additions to the permitted facility or activity (including a change or changes in the permittee's sludge use or disposal practice) which occurred after permit issuance which justify the application of permit conditions that are different or absent in the existing permit.

2. The department has received new information.  Permits may be modified during their terms for this cause only if the information was not available at the time of permit issuance (other than revised regulations, guidance, or test methods) and would have justified the application of different permit conditions at the time of issuance.  For VPDES general permits this cause includes any information indicating that cumulative effects on the environment are unacceptable.  For new source or new discharger VPDES permits this cause shall include any significant information derived from effluent testing required on the permit application after issuance of the permit.

3. The standards or regulations on which the permit was based have been changed by promulgation of amended standards or regulations or by judicial decision after the permit was issued.  Permits may be modified during their terms for this cause only as follows:

a. For promulgation of amended standards or regulations, when:

(1) The permit condition requested to be modified was based on a promulgated effluent limitation guideline, EPA approved or promulgated water quality standards, or the Secondary Treatment Regulations incorporated by reference in 9 VAC 25-31-30; and

(2) EPA has revised, withdrawn, or modified that portion of the regulation or effluent limitation guideline on which the permit condition was based, or has approved a state action with regard to a water quality standard on which the permit condition was based; and

(3) A permittee requests modification in accordance with this chapter within 90 days after Federal Register notice of the action on which the request is based;

b. For judicial decisions, a court of competent jurisdiction has remanded and stayed EPA promulgated regulations or effluent limitation guidelines, if the remand and stay concern that portion of the regulations or guidelines on which the permit condition was based and a request is filed by the permittee in accordance with this chapter within 90 days of judicial remand; or

c. For changes based upon modified state certifications of VPDES permits.

4. The board determines good cause exists for modification of a compliance schedule, such as an act of God, strike, flood, or materials shortage or other events over which the permittee has little or no control and for which there is no reasonably available remedy.  However, in no case may a VPDES compliance schedule be modified to extend beyond an applicable CWA statutory deadline.

5. When the permittee has filed a request for a variance pursuant to 9 VAC 25-31-100 L or M within the time specified in this chapter.

6. When required to incorporate an applicable CWA § 307(a) toxic effluent standard or prohibition.

7. When required by the reopener conditions in a permit which are established under 9 VAC 25-31-220 B or C or 9 VAC 25-31-800 E.

8. a. Upon request of a permittee who qualifies for effluent limitations on a net basis under 9 VAC 25-31-230 G.

b. When a discharger is no longer eligible for net limitations as provided in 9 VAC 25-31-230 G 1 b.

9. As necessary under 9 VAC 25-31-800 E for a pretreatment program.

10. Upon failure to notify another state whose waters may be affected by a discharge.

11. When the level of discharge of any pollutant which is not limited in the permit exceeds the level which can be achieved by the technology-based treatment requirements appropriate to the permittee.

12. To establish a notification level as provided in 9 VAC 25-31-220 F.

13. To modify a schedule of compliance to reflect the time lost during construction of an innovative or alternative facility, in the case of a POTW which has received a grant under § 202(a)(3) of the CWA for 100% of the costs to modify or replace facilities constructed with a grant for innovative and alternative wastewater technology under § 202(a)(2) of the CWA. In no case shall the compliance schedule be modified to extend beyond an applicable CWA statutory deadline for compliance.

14. To correct technical mistakes, such as errors in calculation, or mistaken interpretations of law made in determining permit conditions.

15. When the discharger has installed the treatment technology considered by the permit writer in setting effluent limitations imposed under the law and § 402(a)(1) of the CWA and has properly operated and maintained the facilities but nevertheless has been unable to achieve those effluent limitations.  In this case, the limitations in the modified permit may reflect the level of pollutant control actually achieved (but shall not be less stringent than required by a subsequently promulgated effluent limitations guideline).

16. When required by a permit condition to incorporate a land application plan for beneficial reuse of sewage sludge, to revise an existing land application plan, or to add a land application plan.

17. For a small MS4, to include an effluent limitation requiring implementation of a minimum control measure or measures as specified in 9 VAC 25-31-121 D 2 when:

a. The permit does not include such measures based upon the determination that another entity was responsible for implementation of the requirements;  and

b. The other entity fails to implement measures that satisfy the requirements.

B. Causes for modification or revocation and reissuance.  The following are causes to modify or, alternatively, revoke and reissue a permit:

1. Cause exists for termination under 9 VAC 25-31-410, and the board determines that modification or revocation and reissuance is appropriate; or

2. The department has received notification of a proposed transfer of the permit.  A permit also may be modified to reflect a transfer after the effective date of an automatic transfer but will not be revoked and reissued after the effective date of the transfer except upon the request of the new permittee.

VA.R. Doc. No. R05-94; Filed December 17, 2004, 2:43 p.m.