TITLE 19. PUBLIC SAFETY

DEPARTMENT OF STATE POLICE

REGISTRAR'S NOTICE:  The Department of State Police is claiming an exemption from the Administrative Process Act pursuant to § 2.2-4002 B 6 of the Code of Virginia, which exempts agency action relating to customary military, naval or police functions.

Title of Regulation: 19 VAC 30-70. Motor Vehicle Safety Inspection Rules and Regulations (amending 19 VAC 30-70-210).

Statutory Authority: § 46.2-1165 of the Code of Virginia.

Effective Date: April 15, 2005.

Agency Contact: Sergeant Robert L. Evans, 491 Southlake Boulevard, Richmond, VA 23236-3044, telephone (804) 378-3478, FAX (804) 378-3487 or e-mail robert.evans@vsp.virginia.gov.

Summary:

The amendments (i) limit the size of stickers that may be placed on a windshield in the blind spot behind the rear view mirror and (ii) provide specifications for the placement of Department of Defense decals and Commercial Vehicle Safety Alliance (CVSA) inspection decals.

19 VAC 30-70-210. Glass and glazing.

A. Motor vehicles may be inspected without windshields, side glasses, or any kind of glazing, except that any motor vehicle other than a motorcycle that was manufactured, assembled, or reconstructed after July 1, 1970, must be equipped with a windshield.  If glass or other glazing is installed, it must be inspected.  If no windshield is installed, see 19 VAC 30-70-50 C for location of the sticker.

B. INSPECT FOR AND REJECT IF:

1. Any motor vehicle manufactured or assembled after January 1, 1936, or any bus, taxicab or school bus manufactured or assembled after January 1, 1935, is not equipped throughout with safety glass, or other safety glazing material.  (This requirement includes slide-in campers used on pickups or trucks, caps, or covers used on pickup trucks, motor homes, and vans.)

2. Any safety glass or glazing used in a motor vehicle is not of an approved type and properly identified (DOT and AS-1, AS-2, or AS-3). (Replacement safety glass installed in any part of a vehicle other than the windshield need not bear a trademark or name, provided the glass consists of two or more sheets of glass separated by a glazing material, and provided the glass is cut from a piece of approved safety glass, and provided the edge of the glass can be observed.)

NOTE:  A number of 1998 and 1999 model year Ford Contour/Mystique, Econoline and Ranger vehicles were produced without the AS-1 windshield marking as required by FMVSS #205. Ford has certified that these vehicles' windshields meet all performance standards and will not be rejected.

3. Any glass at any location where glass is used is cracked or broken so that it is likely to cut or injure a person in the vehicle.

4. Windshield has any cloudiness more than three inches above the bottom, one inch inward from the outer borders, one inch down from the top, or one inch inward from the center strip.  The bottom of the windshield shall be defined as the point where the top of the dash contacts the windshield.

5. Any distortion or obstruction that interferes with a driver's vision; any alteration that has been made to a vehicle that obstructs the driver's clear view through the windshield.  This may include but is not limited to large objects hanging from the inside mirror, CB radios or tachometers on the dash, hood scoops and other ornamentation on or in front of the hood that is not transparent.

a. Any hood scoop installed on any motor vehicle manufactured for the year 1990 or earlier model year cannot exceed 2-1/4 inches high at its highest point measured from the junction of the dashboard and the windshield.

b. Any hood scoop installed on any motor vehicle manufactured for the 1991 or subsequent model year cannot exceed 1-1/8 inches high at its highest point measured from the junction of the dashboard and the windshield.

6. Windshield glass, on the driver's side, has any scratch more than 1/4 inch in width and six inches long within the area covered by the windshield wiper blade, excluding the three inches above the bottom of the windshield.  A windshield wiper that remains parked within the driver's side windshield wiper area shall be rejected.

EXCEPTION:  Do not reject safety grooves designed to clean wiper blades if the grooves do not extend upward from the bottom of the windshield more than six inches at the highest point.

7. There is a pit, chip, or star crack larger than 1-1/2 inches in diameter at any location in the windshield above the three-inch line at the bottom.

8. At any location in the windshield above the three-inch line at the bottom (as measured from the junction of the dash board and the windshield) there is more than one crack from the same point if at least one of the cracks is more than 1-1/2 inches in length.  There is any crack that weakens the windshield so that one piece may be moved in relation to the other.  (If there is more than one crack running from a star crack that extends above the three-inch line, the windshield shall be rejected.)

EXCEPTION:  Windshield repair is a viable option to windshield replacement.  A windshield that has been repaired will pass inspection unless:

a. It is likely to cut or injure a person.

b. There is any distortion that interferes with a driver's vision.

c. The windshield remains weakened so that one piece may be moved in relation to the other.

d. The integrity of the windshield has obviously been compromised by the damage or the repair.

9. Any sticker is on the windshield other than an official one required by law or permitted by the Superintendent.  Authorization is hereby granted to stickers measuring not more than three 2-1/2 inches in width and eight four inches in length to be affixed to the upper edge of the center of the windshield.  Any sticker required by law must be placed adjacent to the official inspection sticker and must not extend upward more than three inches from the bottom of the windshield, except on vehicles operating in interstate commerce under rules and regulations of ICC stickers required by law must not extend upward more than 4-1/2 inches from the bottom of the windshield placed in the blind spot behind the rear view mirror. Department of Defense decals measuring no more than three inches in width and eight inches in length may be affixed to the upper edge of the center of the windshield. At the option of the motor vehicle’s owner, the decal may be affixed at the lower left corner of the windshield so that the inside or left edge of the sticker or decal is within one inch of the extreme left edge of the windshield when looking through the windshield from inside the vehicle. When placed at this location, the bottom edge of the sticker or decal must be affixed within three inches of the bottom of the windshield. This location can only be used if the owner of the vehicle has chosen not to place any required county, town or city decal there. The normal location for any required county, town, or city decal is adjacent to the official inspection sticker and must not extend upward more than three inches from the bottom of the windshield. Commercial Vehicle Safety Alliance (CVSA) inspection decals may be placed at the bottom or sides of the windshield provided such decals do not extend more than 4-1/2 inches from the bottom of the windshield and are located outside the area swept by the windshield wipers and outside the driver’s sight line.

Fastoll Transponder devices may be affixed to the inside center of the windshield at the roof line just above the rear view mirror.  If space does not allow, then it may be affixed to the immediate right of the mirror at the roof line.

Any sticker required by the laws of any other state or the District of Columbia and displayed upon the windshield of a vehicle submitted for inspection in this state is permitted by the Superintendent, provided the vehicle is currently registered in that jurisdiction and the sticker is displayed in a manner designated by the issuing authority and has not expired.  This includes vehicles with dual registration; i.e., Virginia and the District of Columbia.

NOTE:  Volvo placed a warning sticker on the windshield of their cars equipped with side impact air bags.  In accordance with this paragraph the sticker shall be removed.  If the sticker can be removed intact then it may be placed on the left rear window in the lower front corner.  Customers should be referred to the nearest Safety Division area office for replacement if it could not be removed intact.

10. Stickers or decals used by counties, cities and towns in lieu of license plates may be placed on the windshield without further authority.  Except on privately owned yellow school buses, the sticker or decal shall be placed on the windshield adjacent to the right side of the official inspection sticker or the optional placement to the extreme lower left side of the windshield.  The top edge of the sticker or decal shall not extend upward more than three inches from the bottom of the windshield.  The left side edge adjacent to the official inspection sticker shall not be more than 1/4 inch from the right edge of the official inspection sticker when looking through the windshield from inside the vehicle.  At the option of the motor vehicle owner, the sticker or decal may be affixed at the lower left corner of the windshield so that the inside or left edge of the sticker or decal is within one inch of the extreme left edge of the windshield when looking through the windshield from inside the vehicle.  When placed at this location, the bottom edge of the sticker or decal must be affixed within three inches of the bottom of the windshield.  Any expired sticker or decal, excluding a rejection sticker that is present on the windshield at the time of inspection, shall not be issued an approval sticker unless the owner/operator "authorizes" its removal.  A rejection sticker will be issued versus an involuntary removal.  On privately owned yellow school buses, the sticker or decal shall be placed on the windshield adjacent to the left side of the official inspection sticker, and not more than 1/4 inch from the left edge of the official inspection sticker when looking through the windshield from inside the vehicle.  The top edge of the sticker shall not extend upward more than three inches from the bottom of the windshield.

11. Sunshading material attached to the windshield extends more than three inches downward from the top of the windshield, unless authorized by a medical waiver certificate.

NOTE:  Sunshading material on windshield displaying words, lettering, numbers or pictures is not approved and is not permitted.

12. Any sunscreening material is scratched, distorted, wrinkled or obscures or distorts clear vision through the glazing.

13. Front side windows have cloudiness above three inches from the bottom of the glass or other defects that affect the driver's vision or one or more cracks which permit one part of the glass to be moved in relation to another part.  Wind silencers, breezes or other ventilator adaptors are not made of clear transparent material.

EXCEPTION:  Colored or tinted ventvisors that do not exceed more than two inches from the forward door post into the driver's viewing area are permitted.

14. Glass in the left front door cannot be raised or lowered easily so a hand signal can be given.  (This does not apply to vehicles that were not designed and/or manufactured for the left front glass to be lowered, provided the vehicle is equipped with approved turn signals.) If either front door has the glass removed and material inserted in place of the glass that could obstruct the driver's vision.

EXCEPTION:  Sunscreening material is permissible if the vehicle is equipped with a mirror on each side.

15. Any sticker or other obstruction is on either front side window, rear side windows, or rear windows.  (The price label, fuel economy label and the buyer's guide required by federal statute and regulations to be affixed to new/used vehicles by the manufacturer shall normally be affixed to one of the rear side windows.) If a vehicle only has two door windows, the labels may be affixed to one of these windows.  If a vehicle does not have any door or side windows the labels may be temporarily affixed to the right side of the windshield until the vehicle is sold to the first purchaser.

NOTE:  A single sticker no larger than 20 square inches in area, if such sticker is totally contained within the lower five inches of the glass in the rear window or a single sticker or decal no larger than 10 square inches located in an area not more than three inches above the bottom and not more than eight inches from the rearmost edge of either front side window, is permissible and should not be rejected.

A single sticker issued by the Department of Transportation to identify a physically challenged driver, no larger than two inches X two inches, located not more than one inch to the rear of the front door post, or one inch to the rear of the front ventilator glass, if equipped with a ventilator glass, and no higher than one inch from the bottom of the window opening, is permitted on the front driver's side window on a vehicle specially equipped for the physically challenged.

16. Rear window is clouded or distorted so that the driver does not have a view 200 feet to the rear.

EXCEPTIONS:  The following are permissible if the vehicle is equipped with a mirror on each side:

a. There is attached to one rear window of such motor vehicle one optically grooved clear plastic right angle rear view lens, not exceeding 18 inches in diameter in the case of a circular lens or not exceeding 11 inches by 14 inches in the case of a rectangular lens, which enables the operator of the motor vehicle to view below the line of sight as viewed through the rear window.

b. There is affixed to the rear side windows, rear window or windows of such motor vehicle any sticker or stickers, regardless of size.

c. There is affixed to the rear side windows, rear window or windows of such motor vehicle a single layer of sunshading material.

d. Rear side windows, rear window or windows is clouded or distorted.

VA.R. Doc. No. R05-168; Filed April 15, 2005, 3:03 p.m.