TITLE 4. CONSERVATION AND NATURAL RESOURCES

DEPARTMENT OF MINES, MINERALS AND ENERGY

Title of Regulation:  4 VAC 25-130. Coal Surface Mining Reclamation Regulations (amending 4 VAC 25-130-816.11 and 4 VAC 25-130-816.64).

Statutory Authority:  §§ 45.1-161.3 and 45.1-230 of the Code of Virginia.

Effective Dates:  August 10, 2005, through August 9, 2006.

Agency Contact:  Stephen A. Walz, Regulatory Coordinator, Department of Mines, Minerals and Energy, 202 North Ninth Street, 8th Floor, Richmond, VA 23219-3402, telephone (804) 692-3211, FAX (804) 692-3237, or e-mail stephen.walz@dmme.virginia.gov.

Preamble:

This regulation change is being made to meet the requirements of Chapter 3 of the 2005 Acts of Assembly, which directs the Department of Mines, Minerals and Energy to promulgate regulations within 280 days of the enactment of the Act that:

1. Require coal mine permit boundary markers located on steep slopes above private dwellings or occupied buildings to be made or marked with fluorescent or reflective material; and

2. Require persons conducting blasting operations on coal mines occurring within 1,000 feet of a private dwelling or occupied building to conduct seismic monitoring of the blasting.

This regulation amendment was recommended in the accident investigation report following an August 20, 2004, accident in Wise County that resulted in fatal injuries to a three-year old boy.

This first amendment to the regulation will require coal mine operators to install and maintain permanent permit boundary markers in areas located above residences or occupied buildings that are made out of or marked with fluorescent or reflective paint.  This requirement is being put into place to ensure that persons conducting mining operations can clearly locate the boundaries of the permitted site during the night or day when they are working on slopes above residences or occupied buildings.  The goal of this change is to ensure that no danger is posed from material being released off of the permitted mine site where it can move downhill into the residences or occupied buildings.

The second amendment to the regulation will require operators of coal mines to monitor all blasts within 1,000 feet of a residence or occupied building with a seismograph.  Under current regulations, operators may use a formula, called the scaled distance equation, to determine the allowable charge weight of explosives to be detonated in any eight-millisecond period and not be required to monitor the air blast or ground vibration with a seismograph.  This amendment is being put in place to help respond to the large number of complaints from the public about the effects of blasting on coal mines.  Monitoring every blast will enable the Department of Mines, Minerals and Energy to better determine whether blasts on coal mines exceed the maximum air blast and ground vibration limits in the regulation.

4 VAC 25-130-816.11. Signs and markers.

(a) Specifications. Signs and markers required under this Part shall-

(1) Be posted, maintained, and removed by the person who conducts the surface mining activities;

(2) Be of a uniform design throughout the operation that can be easily seen and read;

(3) Be made of durable material;

(4) Be made of or marked with fluorescent or reflective paint or material if the signs are permit boundary markers on areas that are located on steep slopes above private dwellings or other occupied buildings; and

(4) (5) Conform to local ordinances and codes.

(b) Maintenance. Signs and markers shall be maintained during the conduct of all activities to which they pertain.

(c) Mine and permit identification signs.

(1) Identification signs shall be displayed at each point of access to the permit area from public roads.

(2) Signs shall show the name, business address, and telephone number of the permittee and the identification number of the current permit authorizing surface coal mining activities.

(3) Signs shall be retained and maintained until after the release of all bonds for the permit area.

(d) Perimeter markers. The perimeter of a permit area shall be clearly marked prior to the permit review conducted by the division's field enforcement personnel. The perimeter shall be clearly marked by flagging, stakes or signs. All markers shall be easily visible from adjacent markers. The approximate outer perimeter of the solid portion of any pre-existing bench shall be closely marked prior to permit review.

(e) Buffer zone markers. Buffer zones shall be marked along their boundaries, prior to permit review conducted by the division's field enforcement personnel. The boundaries shall be clearly marked by flagging, stakes or signs as required under 4 VAC 25-130-816.57. All markers of the buffer zone shall be easily visible from adjacent markers.

(f) Blasting signs. If blasting is conducted incident to surface mining activities, the person who conducts these activities shall:

(1) Conspicuously place signs reading "Blasting Area" along the edge of any blasting area that comes within 100 feet of any public road right of way, and at the point where any other road provides access to the blasting area; and

(2) At all entrances to the permit area from public roads or highways place conspicuous signs which state "Warning! Explosives In Use" which clearly list and describe the meaning of the audible blast warning and all clear signals that are in use, and which explain the marking of blasting areas and charged holes awaiting firing within the permit area.

(g) Topsoil markers. Where topsoil or other vegetation - supporting material is segregated and stockpiled as required under 4 VAC 25-130-816.22, the stockpiled material shall be clearly marked.

(h) Incremental bonding markers. When the permittee elects to increment the amount of performance bond during the term of the permit, he shall, if required by the division, identify the initial and successive incremental areas for bonding by clearly marking such areas (with markers different from the perimeter markers) prior to disturbing the incremental area(s).

4 VAC 25-130-816.64. Use of explosives; blasting schedule.

(a) General requirements.

(1) The permittee shall conduct blasting operations at times approved by the division and announced in the blasting schedule. The division may limit the area covered, timing, and sequence of blasting as listed in the schedule, if such limitations are necessary and reasonable in order to protect the public health and safety or welfare.

(2) All blasting shall be conducted during daylight hours. The division may specify more restrictive time periods for blasting.

(3) Unscheduled blasts may be conducted only where public or permittee health and safety so require and for emergency blasting actions. When a permittee conducts an unscheduled blast, the permittee, using audible signals, shall notify residents within 1/2 mile of the blasting site and document the reason for the unscheduled blast in accordance with 4 VAC 25-130-816.68(p).

(4) Seismic monitoring shall be conducted when blasting operations on coal surface mining operations are conducted within 1,000 feet of a private dwelling or other occupied building.

(b) Blasting schedule publication and distribution.

(1) The permittee shall publish the blasting schedule in a newspaper of general circulation in the locality of the blasting site at least 10 days, but not more than 30 days, before beginning a blasting program.

(2) The permittee shall distribute copies of the schedule to local governments and public utilities and to each local residence within 1/2 mile of the proposed blasting site described in the schedule.

(3) The permittee shall republish and redistribute the schedule at least every 12 months and revise and republish the schedule at least 10 days, but not more than 30 days, before blasting whenever the area covered by the schedule changes or actual time periods for blasting significantly differ from the prior announcement.

(c) Blasting schedule contents. The blasting schedule shall contain, at a minimum-

(1) Name, address, and telephone number of the permittee;

(2) Identification of the specific areas in which blasting will take place;

(3) Dates and time periods when explosives are to be detonated;

(4) Methods to be used to control access to the blasting area; and

(5) Type and patterns of audible warning and all-clear signals to be used before and after blasting.

/s/ Mark R. Warner

Governor

Date: August 5, 2005

VA.R. Doc. No. R05-283; Filed August 10, 2005, 3:01 p.m.